TS940.5

 ts-940 aaverage output power on ssb

 on the air conversations concerning

 a kenwood newsletter mod to change

 alc delay time  called for putting

 a 2.2k ohm across the top of r137

 and r104 on the control p.c.b ,

 along with a .47 mfd cap between

 pin 1 and pin 2 of connector 8 on

 the control board..

 the mod is excellent except .47 mfd

 is far too much..

 instead use a .005 to .01 mfd to 

 keep from over driving..

 electrolytic not necessary, but if

 used, make sure nagative goes to

 shield wire pin..

 from: bill k5bdz........RELAYED   BY...N0KGX...GENE