From cbfsb!att!linac!pacific.mps.ohio-state.edu!zaphod.mps.ohio-state.edu!usc!cs.utexas.edu!csc.ti.com!tilde.csc.ti.com!fstop.csc.ti.com!axis!sqa.dsg.ti.com!edh Wed Jul  8 18:17:32 EDT 1992
Article: 21685 of rec.radio.amateur.misc
Newsgroups: rec.radio.amateur.misc
Path: cbfsb!att!linac!pacific.mps.ohio-state.edu!zaphod.mps.ohio-state.edu!usc!cs.utexas.edu!csc.ti.com!tilde.csc.ti.com!fstop.csc.ti.com!axis!sqa.dsg.ti.com!edh
From: edh@sqa.dsg.ti.com (ed humphries (ASOC))
Subject: Twin Lead J-Pole Antenna
Message-ID: <1992Jul8.185323.4573@axis.dsg.ti.com>
Sender: Ed Humphries-N5RCK
Organization: Texas Instruments, Austin, Tx.
Date: Wed, 8 Jul 92 18:53:23 GMT
Lines: 101

I just read a _much_ bastardized version of an article I wrote about
a year ago and posted here. The repost had apparently been picked up
off of packet, so I cannot fault the person who reposted the tv twin-
lead j-pole plans, other than to point out that D.A.R.C. is the Dallas
Amateur Radio Club. I know many plans have been printed for this type
of antenna, but the hacked up version obviously started from my post
(as you can see when you read below). I didn't just write a cut the
wire and run article, but I researched the subject, calculated average
values for the tv twin-lead (so the builder could select the center
frequency of choice), and I give instructions on fine-tuning. I have
no problem with people sharing this information around, but those who
do so should a)attribute their source, b)avoid editing the article,
and c)especially avoid changes in meaning (i.e. using foam center tv
lead-in is not just not a good idea, it won't work and can possibly
short through the foam and damage a radio!) and _finally_ d)if someone
is going to ignore a-c, at _least_ have the decency to change the
first person references! I have e-mailed the following article to many
requesters during the past year, and have edited to improve it in
some areas. The requester here on the net (that started the thread
that contained the bastardized version) got a copy of what follows
(prefaced by a note from me) the same day the request was made.

I write the above because an aquaintance upbraided me about his
newly built j-pole not working. He had a copy of the hacked up plans
and no idea what to do to fix it. I have built _many_ of these
antennas using the plans that follow and given them to many friends
as well as using them myself. My most recent effort (the night before
field day) shows vswr at 1:1.1 at 146MHz and 1:1.2-3 at 444MHz. We
use this kind of antenna frequently for Skywarn work (since the prudent
thing is to disconnect the outdoor antenna during the storm).

--cut here and print the instructions that follow--

        The following is a description of a J-Pole antenna made from 300 ohm
        TV twin-lead. They have quite a few advantages which include improved
        performance for HTs, portability, and low cost.
 
                        |   | do not short this end.
                        |   | (when trimming for vswr, cut both sides)
                        |   |
                        |   |
                        |   |
                    3/4 |   |        Technically-speaking, this is a 1/2
                   wave |   |        wave end-fed antenna with a 1/4 wave
                        |   |        matching section.
                        |   |
                        |     1/4" gap
                        |   |         (trim for vswr _below_ gap)
                        |   | 1/4
                        |   | wave
                        |   |
    coax ctr conductor=>*   *<= coax shield
                 1 1/4"-|   |
                         -*-    solder the twin leads together at bottom
 
        For a center frequency of 146 MHz:
        1. Start with @54" of TV twin lead (flat, NOT foam core)
        2. Strip 1/2" of insulation at bottom and solder wires together.
        3. Measure 1 1/4" from soldered wires and strip insulation on both
           sides. This is the solder point for a coax feedline.
        4. Measure 16 3/4" from coax shield solder point and cut out 1/4" notch.
        5. Measure 50 1/3" from coax center conductor solder point and trim
           off twin lead at that point.
        6. Feed with a length of RG58U coax.  Tape coax at feedpoint to the
           twin lead for strength and seal coax for weather protection.
 
        To get the best possible match, in step three above simply MARK the
        "solder points" and measure from the mark for step 4 and 5. Now solder
        straight pins to your conductor and your shield. Insert the pins at
        the marked point and test for VSWR at the design frequency (146MHz).
        If necessary, probe up or down till you reach 1:1 (close as possible).
        Solder at the best points. To try this, you may want to start with
        the twin lead a little long and trim down to resonant length - note:
        you'll need to trim in a 3:1 ratio to maintain the 3/4 to 1/4 wave.
 
        It has been noted that this design can lead to rf coupling onto the
        feedline. To avoid, put ferrite beads on the coax at the feedpoint,
        or use 3-5 turns of coax (1"-2") taped together at the feedpoint.
 
        You may attach an alligator clip to the plastic on the top of
        the antenna in order to easily hang it.  Alternately, punch a
        hole near the top and use a length of fishing line to hang.
 
        This design appears on many BBSs, in club newsletters, and in books;
        the earliest reference that I know of is a Jan. 1984 D.A.R.C. antenna
        article by James Burks, KA5QYV. This antenna is relatively broad-banded
        and will be more than adequate if simply built as noted in steps above.
 
        FYI, the 1/4 wave sections for other center frequencies are:
        144 MHz =17 inches, 145 =16.88, 146 =16.75, 147 =16.65, 148 =16.54

	I usually just go ahead and solder the coax in place and trim
	down to as close to 1:1 vswr as I can get. I use the MFJ vhf
	antenna analyzer and a frequency counter then afterwards test
	with a radio and in-line swr/power meter. When done, the antenna
	should also present 1:1.2-3 vswr in the center of 444MHz band as
	well (demonstrated on my dual-band meter and Alinco DJ-580).

--
Ed Humphries                Texas Instruments, Inc. 512-250-6894
N5RCK                       Internet ed.humphries@hub.dsg.ti.com