MX4200.2
   13.  Turn the scanner on.
   14.  Locate a small gray  potentiometer  on  the  printed
        circuit  board.   The  potentiometer looks something
        like a gray plastic Phillips  screw  head.   If  the
        scanner  front  panel is facing you, the pot will be
        just behind the keyboard on the  left  side.  (Don't
        confuse  this  pot  with  the 3 pots along the right
        edge of the board.  The battery voltage  sensor  pot
        is not near any other pot.)
   15.  Slowly adjust the potentiometer to the threshhold at
        which the low battery indicator begins to flash.

   This procedure worked with great success on  an  MX-4200,
   and its battery life was increased from 2 to 7.5 hours.

   I would like to thank Rick Meyer, WB9UFL, for finding the
   potentiometer  in his MX-4000, and Ron Smithberg for let-
   ting me experiment with his MX-4200.