*****************************************************************************
Subject: Regency MX7000/MX5000 stop search function
here is a handy way to get the scanner to automatically
stop searching when it hits an active frequency and remain there until
it is re-started manually.  
With the scanner stopped on any channel using the MANUAL key, press
CLOCK SET followed by ENTER.  Now enter at least one numeric digit, but do
not press ENTER after keying in the digit(s).  Instead, press SCAN.
If you shut the scanner off, you will notice that the clock is not 
running.  The digit(s) that you entered is displayed.  Now use the
search feature as you normally would.  When it hears a signal, it will
stop and remain on that frequency.  After the signal ceases, pressing
any key that would normally give you an "error beep" (such as the ENTER
key) will restart the search from where it left off.  If you do not wish
to wait for the signal to go away before restarting the search, press
the UP key until it is gone, then press a key to produce the "error
beep."
To re-start the clock after you're through using the search-hold feature,
just use the normal clock-set method.  Incidentally, the priority feature
will not work if the clock is not running.
****************************************************************************