From lwbyppp@epix.net Mon Feb 05 21:39:11 1996
Path: news.epix.net!news.sprintlink.net!aimnet.com!news.exodus.net!uunet!in2.uu.net!news.mindspring.com!usenet
From: otterson@mindspring.com (Jeff Otterson)
Newsgroups: rec.radio.amateur.equipment
Subject: Re: yaesu ft-40 or ft-10 mods
Date: Sat, 03 Feb 1996 01:21:36 GMT
Organization: MindSpring Enterprises
Lines: 68
Message-ID: <4eueeb$cqk@brickbat.mindspring.com>
References: <4es179$q8i@sundog.tiac.net>
Reply-To: otterson@mindspring.com
NNTP-Posting-Host: otterson.mindspring.com
X-Newsreader: Forte Free Agent 1.0.82

Yaesu FT40R Expanded RF Modification.
420-480 Mhz, Transmit and Receive.

This radio is not type accepted for use outside of the amateur 
70 cm band, and transmitting with it outside of the amateur band is a
violation of U.S. Federal Law.

1) Turn the radio off and remove the battery.

2) Peel off the black NiCd information seal, (under the battery) and 
    loosen (but do not completely remove) the 2 screws on either side
    of the slot behind the keypad.

3) From the rear, carefully press on both screws to eject the keypad 
    slightly,  then remove the screws to free the keypad.

4) From the front of the radio, carefully pull the keypad up and 
    toward the top of the radio.

5) Locate and unsolder the 0 ohm chip resistor at location "M"

6) Gently but firmly press the keypad back into place on the front of 
    the radio, taking care that the gasket seals evenly around the 
    keypad with no pinching.

7) Replace the 2 screws on the back of the radio.  Do not over-tighten

    the screws, they are screwing into plastic.  Re-attach the NiCd 
    information seal.

8) Replace the battery.

9) Press and hold the knob and the light button, then press and hold 
    the power button until the radio turns on.  You may or may not 
    need to reset the radio (knob, monitor & power) then activate 
    expanded RF (knob, light & power) to make the modification
    effective.

10) Modification complete!


        __           |Ant|
       |__|          |   |
   ___|____|_________|   |  
  |    _______________    |
  |   |               |   |
  |   |               |   |
  |   |_______________|   |
  |    ===============    |
  |    ===============    |
  |    ===============    |
  |  (Pwr) ===========    |
  |  ___________________  |
  | |  Keypad Cable     | |
  | |    ||||||||       | |
  | |    [______]       | |
  | |   O          O    | |
  | |            []M    | |
  | |___________________| |
  |_______________________|


Jeff Otterson
-------------
otterson@mindspring.com
Maker and user of tools
PGP key available at http://www.mindspring.com/~otterson/pgp.htm