FT227R

OUT OF BAND MOD

1. OPEN RADIO AND LOCATE PLL CONT. UNIT.
2. REMOVE D701 AND D702. DO NOT PLACE IN A JUMPER.
3. LOCATE Q712 (MC14028B) AND BREAK THE CONNECT TO PIN 6 (BLUE WIRE)
4. CONNECT PIN 1 OF Q711 (RED WIRE) TO GROUND.
5. REASSEMBLE RADIO