FT26

YAESU FT-26
EXPANDED RF

REMOVE SCREWS HOLDING BATTERY TRACK.
REMOVE 2 SCREWS HOLDING BACK COVER.
LOCATE CONTROL BOARD AND REMOVE SOLDER ACROSS JUMPER PAD 10.
SOLDER ACROSS PADS 1, 3, 7, AND 8.
REASSEMBLE RADIO.
TURN ON RADIO AND EACH CHANNEL SHOULD BLINK.
ENTER FOLLOWING FREQS.  USE F AND UP ARROW KEYS.
CH. 1 135.000  PRESS D/MR  THIS IS LOWER RX LIMIT
CH. 2 174.000  PRESS D/MR  THIS IS UPPER RX LIMIT
CH. 3 135.000  PRESS D/MR  THIS IS LOWER TX LIMIT
CH. 4 174.000  PRESS D/MR  THIS IS UPPER TX LIMIT.
PRESS AND HOLD T AND REV. AND TURN ON.