FT530

Date: 31 Dec 92 23:11:14 EST (Thu)
From: wa2ise@kb1bd.#cnj.nj.usa.na (BOB)
Subject: FT530 ext TX/RX mod file

YAESU FT-530

Expanded Receive 110-180, 300-500 MHz
Expanded Transmit 130-180, 400-470 MHz

NOT LEGAL IN U.S.A - FOR EXPORT ONLY

o Remove Antenna and Battery.
o Remove four screws on bottom holding battery track.
o Remove the four (black) screws holding rear case.
o Slowly... open the front cover from tranceiver and lay both halves on table.
o Note positioning of white paper insulator in right half of radio and lift out
  (don't throw away)
o Carefully locate Jumper Pad 13 and remove solder.
o Re-install white paper insulator, make sure ground tab slides through the 
  paper insulator.
o Close radio back up (Careful not to pinch the ribbon cable near lithium 
  battery when closing halves).
o Re-install the four (black) screws holding rear case.
o Re-install the four (small silver) screws on bottom holding battery track to
  radio body.
o Attach Antenna and Battery.
o Turn off Radio.... Press and hold both arrow keys while turning on the Radio.
o Modification Complete.


------------------------
!                      !
!                      !
!                      !
!                      !
!           ---        !
!           ! !        !
!           ---       /
!           ---      /
!           ! !     /                         2 (!)  (!) 1
!           ---    /                          4 (!)  (!) 3
!                 /  <---  Jumpers are here   6 (!)  (!) 5
!              o /                            8 (!)  (!) 7
-----------------             Blowup --->    10 (!)  (!) 9
                                             12 (!)  (!) 11
                                             14 (!)  (!) 13
                                             16 (!)  (!) 15
-

Inside the rig, it really did not look quite like that ...    more like this:

...  12 (!)  (!) 11 
           (!) 13
      16 (!)  (!) 15

In addition to the published receive expansion, it also receives 800-950 MHz...
trunking radio, cell phone (I would *never* listen to that), 33cm ham band...

Have fun!


-------Jeff Otterson 
===============================================================
Note: I haven't tried or verified this, proceed at your own risk. 
And do not transmit outside of band!  WA2ISE