Leland (LES) Cox  AA4F
1832 E. Windwood Dr.
Mobile, AL, 36695
205 633-9079

    I have recently purchased a YAESU FT-530 HT.  It is first class
all the way.  I have been asked many questions about my new rig, and
thought I might many questions in the form of an INFO FILE!

    The FT-530 is programmable in just about any way you can imagine.
Of course it does all of the normal synthesized HT functions plus it
has built in CTCSS and DTMF functions. The HT will notify you with an
alarm when your CTCSS or tone sequence is received.  You can even
change the sound and length of the alarm!

    The built in clock has elapsed time, auto on or off at a preset time
auto off after a preset elapsed time, and can even be used as an alarm
clock.

    Frequency can be entered directly with the keyboard or selected from
two VFOs or from 42 memory channels per band.  The memory channels can be
scanned one band at a time, both bands at the same time, or both bands in
sequence. Any channel can be "skipped" during scan, but is accessible
with the dial or arrow keys. It will also scan a range between two
programmable limits. 

    Each programmed channel will have repeater split, power and CTCSS or
DTMF squelch information included.

    Two frequencies in the same band can be monitored simultaneously.

    The built in duplexer will allow you to receive on one band while
transmitting on the other band.  Setting it up as a cross band repeater 
is easy.

    The Speaker Mic with the built in display is great for using the rig
as a mobile.  The mike is about the same size as other speaker mics and
light weight.  The audio is great.  The display is the active band only,
and has the most needed function keys. One key is programmable with band
select the default.

    Other keys duplicate the U/D arrows, scan start, memory select, vfo
select, light, and power switch.  Three switches on the back will turn on
the light, turn the speaker on or off and a lock switch.  An external
speaker jack is located on the mic plug.

    The batteries are not compatible with the FT-470.  A power jack allows
5 Watt mobile operation and will charge the battery.

    I have made the modification to open up the receiver to 110-180 Mhz 
and 300-500 Mhz.  It works!!  You will need a magnifying glass and a
solder sucker.  After making this mod, Turn on the power while holding
the UP and DN arrow keys.    THIS ERASES ALL MEMORY!!!!!  I also noticed
the automatic repeater split does not work correctly.  Turn the repeater
split to manual, and this will not be problem.  The extended range is
worth the extra effort.



Yaesu FT-530



Expanded Receive only 110-180, 300-500 MHZ  (Transmit Freq. Unchanged)


- Remove Antenna and Battery.
- Remove four screws on bottom holding battery track.
- Remove the four (black) screws holding rear case.
- Slowly....open the front cover from transceiver, lay both halves on table.
- Note positioning of white paper insulator in right half of radio and lift out
    (don't throw away).
- Carefully locate JUMPER PADS 13 & 15, and REMOVE SOLDER.
- Re-install white paper insulator, make sure the ground tab slides through
    the paper insulator.
- Close radio back up (Careful not to pinch the ribbon cable near lithium 
    battery when closing case halves).
- Re-install the four (black) screws holding rear case.
- Re-install four (small silver) screws on bottom holding battery track to radio 
    body.
- Attach Antenna and Battery.
- TURN OFF RADIO...
 PRESS AND HOLD BOTH ARROW KEYS, TURN ON THE RADIO.   THIS ERASES MEMORIES!!
- Modification complete !

I have performed this modification and it does work!



                      YAESU FT-530 COMMAND REFERENCE

                           COMPILED BY LES,  AA4F

         ACTION               COMMAND SEQUENCE                ICON   RETURN

ALTERNATE SCANNING (toggle)   (F/M)   (BAND)   (UP)
ABS  AUTO BATTERY SAVER       (F/M) (SAVE) Then 1-9. 0 = OFF   "ABS"
APO  AUTO POWER OFF           (F/M) (SET) (LOW) (LOW)  to set time-out   PTT
AM RECEIVE DETECTOR           (F/M) (SET) (F/M) (VFO)                   PTT
BAND CHANGE                   (BAND)                            "->"
BAND On/Off  2nd band         (SUB)
BATTERY VOLTAGE DISP when ON  (F/M) (SET) (F/M) (BAND)  Repeat for clock           
BEEPER Enable/Disable         (F/M) (TSET) (F/M) (TSET)          "b"
BEEPER Dtmf/ Musical          (F/M) (SET) (F/M) (LOCK)      "dt" "b"  (SET)
BUSY LED Enable/Disable       (F/M) (SET) (STEP) (STEP)                 PTT
CALL CHANNEL STORAGE          [F/M] 1/2 sec (CALL)
CROSS BAND REPEAT             (RPT) while turning on.
CTCSS BELL On/Off             (PAGE) (PAGE) (PAGE)            "BELL"
CTCSS Encode/Decode           (F/M) (TONE) (TONE)          "T"  "SQ"
CTCSS FREQUENCY Display/Set   (F/M) (TSET) (DIAL)                    (TSET)
CTCSS SCANNING                (F/M) (SET) (F/M) (TSET)  1beep-on 2-off  PTT
CTCSS SCAN ACTIVATE           (F/M) (TONE) (TONE) until "T SQ" is displayed
              then            (F/M) (TSET) to display tone. [UP] to start  
DISPLAY WHEN POWER OFF        (F/M) (CLOCK) (LOCK) (LOCK)           (CLOCK)
DTMF AUTO DIAL MEMORY MODE    (F/M) (DTMF)                   "PHONE"
DTMF AUTODIAL MEM Disp/Sel    (F/M) digit  (1-10)                    (DTMF)
DTMF STORE AUTODIAL MEMORY    (F/M) 1/2 sec Mem # (F/M) (ph #)       (DTMF)
DTMF CODE SQUELCH             (F/M) (PAGE)(PAGE)(PAGE).  "PAGE" or"CODE"
DTMF CODE MEMORY              (F/M) (SET) (CODE)                        PTT
DTMF CODE MEMORY SET          (F/M) (CODE) dial                      (PAGE)
DTMF CODE TRANSMIT DELAY      (F/M) (SET) (TONE)(TONE)(TONE)            PTT
DTMF CODE PLAYBACK SPEED      (F/M) (SET) (F/M) (CLOCK)  "ds100, 150"   PTT
DTMF ROW DISABLE              (F/M) (SET) (F/M) (VOX)          "rOFF"   PTT
DTMF COLUMN DISABLE           (F/M) (SET) (F/M) (XFER)         "cOFF"   PTT
DTMF XMIT HANG TIME           (F/M) (SET) (F/M)(TONE)(TONE)(TONE)       PTT
DTMF CODE DISPLAY OPTION      (F/M) (SET) (CODE)       "opON" "opOFF"   PTT
EARPHONE AUDIO SELECT         (F/M) (SET) (PRI) (PRI)  E=ear I=int spkr PTT
ENTERING FREQUENCY            Enter digits and trailing 0's or PTT  
INTELLIGENT BAND SELECT       (F/M) (SET) (BAND)(BAND)(BAND)    "IBS"   PTT
LIGHTED DIAL ON               (F/M) (LIGHT)  Repeat to turn off.
LOCK  KEYPAD and PTT          (F/M) (LOCK) (LOCK) (LOCK)    "KL" "PL"
LOCK DIAL                     (F/M) (SET) (LOCK)                 "KL"
MEMORY MODE                   (MR)  Switch to MEMORY MODE
MEMORY MASKING                [F/M] 1/2sec (DIAL) (SKIP)
MEMORY STORING                [F/M] 1/2sec (DIAL) To select memory #  (F/M)
MEMORY STORING Sep Xmit Freq  [F/M] 1/2sec (DIAL) (FM)+PTT
MEMORY RECALL                 (MR)  (DIAL)  Memory #          ">>>>"
MEMORY TUNING                 (MR)  look for                  ">>>>"   (MR)
MHZ SELECT                    (F/M) (DIAL)
MONOBAND OPERATION            (SUB)
PAGING RINGER AUDIBLE TEST   (F/M) (SET) (DTMF)                        PTT
PAGING RINGER 0,1,3,5 RINGS   (F/M) (SET) (TSET) (TSET) (TSET)          PTT
PRIORITY CHANNEL              (F/M) (PRI)   Checks memory #1            PTT
REPEATER OFFSET               (F/M) (SET) (RPT) (DIAL)                (RPT)
REPEATER AUTO SHIFT           (F/M) (SET) (F/M) (F/M)            "A"  (RPT)
REPEATER SHIFT Up/Dn/Simplex  (F/M) (RPT) (RPT) (RPT)        "+" "-"
REPEATER REVERSE              (REV)    Reverse xmit/rec freq
RESET                         Hold (MR) and (VFO) while turning on.
SCAN START                    [UP] or [DN] Arrow    Hold 1 sec.         PTT
SCAN PROGRAMMED MEMORY        Store range in L and U memories           PTT
SCAN PAUSE MODE               (F/M) (STEP) (F/M) (F/M) (F/M)."5" "P"
SCAN MEMORY SKIP              (F/M) (SKIP)                      "->"
SPLINTER CHANNEL TUNING  1Khz (F/M) (SET) (F/M) (STEP) (STEP). ...      PTT
SUBBAND OPERATION             (F/M) (SUB OP)           "Blinking ->"
SUBBAND DISPLAY SELECTION     (F/M) (SET) (ALT) (ALT) "--- clk btry"    PTT
TIMER START                   (F/M) Hold til "1" biinks in mem box  (CLOCK)
TIMER CHECK                   (F/M) (CLOCK) (MR)                    (CLOCK)
TRANSFER L and R DISPLAY      (F/M) (XFER)
TRANSMITTER POWER L1,2,3,Hi   (F/M) (LOW) (LOW)   (Dial) when low displayed
TUNING STEP SELECTION         (F/M) (STEP) (DIAL)                    (STEP)
TRANSMIT BATTERY SAVER        (F/M) (SET) (SAVE) (SAVE)    "On" "Off"
VOX ON/HI/LO  SENSITIVITY     (F/M) (VOX) (VOX) (VOX)             "V"
VOX DELAY                     (F/M) (SET) (VOX) (VOX)".5" "1.0" "1.5"  PTT
VFO   on/a/b                  (VfO) (VFO) (VFO)               "a" "b"
1Khz MODE On/Off              (F/M) (SET) (F/M) (STEP) "1K on/ 1K off"  PTT

RINGER EVERY MIN.    on /off  (F/M) (SET) (F/M) (CODE) "crON" "crOFF"   PTT
RINGER PLAYBACK               (F/M) (SET) (CALL)                        PTT
RINGER PROGRAMMING            Store in DTMF Mem #2 for VHF and #3 for UHF
PROGRAM RINGER SELECT         (F/M) (SET) (F/M) (CALL)  "pcDT" "pc b"   PTT
RINGER  # of repeats          (F/M) (SET) (TSET) (TSET) "Pc OFF,1,3,5"  PTT

SET CLOCK               (F/M) (CLK) (F/M)     (DIAL) to set Hr
                          (DN) to select Min  (DIAL) to set.        (CLOCK)
ON  TIMER SETTING       (F/M) (CLK) (TONE)    (DIAL) to set Hr
                          (DN) to select Min  (DIAL) to set.
                          (F/M) to toggle timer ON/OFF        "ON"  (CLOCK)
OFF  TIMER SETTING      (F/M) (CLK) (TSET)    (DIAL) to set Hr
                          (DN) to select Min  (DIAL) to set.
                          (F/M) to toggle timer ON/OFF       "OFF"  (CLOCK)
TIMER ALARM SETTING     (F/M) (CLK) (LOW)     (DIAL) to set Hr
                          (DN) to select Min  (DIAL) to set.
                          (F/M) to toggle timer ON/OFF     "((.))"  (CLOCK)
ONE TOUCH TIMER         (F/M) (CLOCK)  To memorize time.
                          (F/M) (CLOCK) (MR)  To recall.            (CLOCK)
TIMER DISPLAY           (F/M) (CLOCK)                               (CLOCK)