This modification is intended for use with the Yaesu FT767GX when equipped
 with the optional 2 Meter module.

 It appears that Yaesu has the 2 Meter module default to Japanese 2M freqs
 (144.000-145.9999MHz).  After using the backup switch to reset memories on 
 the 767, the 2M module will also reset to default.

 To restore full US 2M band coverage (144.0000-147.9999MHz), follow this
 procedure:

 1) place "backup" switch on rear panel to OFF position
 2) power OFF radio
 3) hold down "2" key and power ON radio
 4) return backup switch to ON position

 Although I can't imagine that you could possibly break your radio with this
 mod, standard disclaimers for radio modifications apply.