From : G4WFQ @ GB7PET._221.GBR.EU


     Audio output from FT790R receiver's Discriminator for 9600bauds
     ---------------------------------------------------------------

Here is a very simple way of taking audio direct from the discriminator.
Connect a flying lead to pin 9 QO8 (MC3357P). (To save you having to burrow,
just solder a lead on the IC pin itself).
Drill a 1/4 hole in the case between standby and speaker sockets. Insert
phono socket here and connect the flying lead and suitable Gnd.
Thats it, job done.


    TxAudio input into FT790R Varactor diode for 9600 bauds
    -------------------------------------------------------



Here are the details to input 9600 buads into the 790.
Firstly make up the following circuit.



                470n
 Txaudio----->---] ]------------------22k----->To FC53M
            :           :       :
            :          22k     ---
            :           :      --- 10p
            :           :        :
 TxAgnd--->----------------------------------->Chassis Gnd


Notes:-

When you make up the above circuit, you must use very short leads!!!!

FC53M is a Varactor diode which is D1031 on the FT790r diagram.


73 de Dave G4WFQ @GB7PET 30th May 1990
<EOF>