FT811

OUT OF BAND MOD

1. REMOVE BAT. AND ANT.
2. REMOVE CONTROL KNOBS, SCREWS, TOP PANEL AND BODY SCREWS AND OPEN RADIO
3. REMOVE SOLDER BRIDGE FROM PAD #2
4. REMOVE SOLDER BRIDGE FROM PAD #4
4. place solder bridge on pad #3
5. reassemble radio.
6. reset cpu press and hold [mr] and [vfo] and turn on then off
             press and hold both up and down keys and turn on power
7. enter following: 4200 [vfo] 4700 [vfo] 4200 [vfo] 4700 [vfo]
8. press [f] and [7] to change channel step
covers 420-470 mhz