From lwbyppp@epix.net Wed Feb 21 16:03:35 1996
From: Mike Obermeier <ifindem@mail.calypso.com>
Newsgroups: rec.radio.scanner,alt.radio.scanner,rec.radio.amateur.misc,rec.radio.amateur.equipment,rec.radio.amateur.homebrew
Subject: Re: FT-8500 Need Mods
Date: 15 Feb 1996 04:56:45 GMT
Message-ID: <4fueef$hke@news.htp.com>
References: <4fov69$l98@news.ios.com>
To: rod@venus.hili.com

The mod is easy.  This will give you 137-174mhz and 410-470mhz Tx/Rx.

1. disconnect power and antenna (like, you would'nt of done it already.)
2. open up the case by removing the screws and gently removing the cover and 
   unpluging the speaker.
3. locate and CUT the GREEN WIRE on the CONTROL BOARD ( the vertical board beh
ind 
   the control panel.
4. reassemble the radio.
5. RESET THE MICROPROCESSOR (so much for the memory!)

   (press and hold [D/M] & [REV] & [ENT] & turn the power on (got enough finge
rs?).

   (turn off the radio).

   (press and hold [SCAN] & [HOME] & turn on the radio (extended RX mod).


Tha, Tha, Tha, That's All Folks!