copied from packet:
 Msg# T{ize #Rd  Date  Time From   MsgID        To
32972 BF   2276   0 13-Jan 1142 F1LOU  30527_ON7RC  YAESU@WW ()
 Sb: FT890 MODS

                   YAESU FT890/AT mod.  TX 1,5 to 30 MHZ.
                   ======================================
 
 - Disconnect FT890 from all connections.
 
 - Open tranceiver like explained in your "OPERATING MANUAL".
 
 - Locate on the "CONTROL UNIT" jumper point JW 3001 and close it with solder.
 
 - Close tranceiver back and reconnect power.
 
 - Push PROC, AGC-F, IPO, ATT while power ON.
 
 - Now the display shows two digits of numbers and tree of letters (i.e 13 OFF)
   Rotate main knob and set the display to "02 ON". Now press the PROC button.
 
 - Power OFF and then back ON. It's all!
 
 - Now every time you want, you can change the programation, but you will
   allways lose the memories.
 
 - Other settings than "02 ON" are of no interest. This one give you 100 w
   and automatic antenna tuning between 1,5 and 30 mhz.
 
 
    73's de Phil, F1LOU @ ON7RC.BT.BEL.EU
 =========================================================================
Note: I haven't tried or verified this, proceed at your own risk, and
do not transmit outside of legal bands!  WA2ISE