Remove the two screws from the top cover, and the two 
screws from the top rear area of the rear panel, so as to 
allow the top cover/heat sink to be slid slightly toward 
the rear.  The objective is to be able to see into the 
CNTL-1 Unit, which is the inside part of the front panel 
(not the detachable sub-panel).

2.  Locate test points TP3001 and TP3002 on the CNTL Unit.  
They are located near the top edge of the board, in the 
center from left to right.  With the transceiver still 
turned off, connect a jumper (alligator clip is ok) 
between these 2 test points.

3.  Hold in the following 4 buttons: [PROC], [ATT], [IPO], 
and [NB].  While holding them in, turn the transceiver on.  
Release the buttons.

4.  The display will indicate OFF.  
Turn the VFO dial slowly until the display reads ON.

5.  Press the [PROC] button to write the new instructions 
to EEPROM.

6.  Remove the jumper across the test points.

7.  Replace the case screws. Mod is now complete.


--