Modification FT990. I received a mail from AA6SQ about Extended transmitter
frequency range for FT990 and FT1000 - Remove top and bottom covers. Remove
top screw on each side which holds front panel to chassis. Pivot front panel
down slowly. CAUTION : if you let it go, it will flop down rapidly and
probably tear somethins loose. Behind the meter will be the CNTL unit. It has
a metal cover about 4 * 8 inches. Snap the cover off. Look to the top of the
unit. You will see JP-3. Remove the solder connection on JP-3.