I N T E G R I T Y     M A S T E R (tm)


                             Version  3.02


      An easy to use, data integrity and anti-virus program which also
       provides PC security, change control and disk error detection.



             Users Guide plus Data Integrity and Virus Guide

             ________________________________________________


                Copyright 1990 - 1996 by Wolfgang Stiller
                           All rights reserved
                           ___________________

                            Stiller Research
                           1265 Big Valley Dr.
                     Colorado Springs, CO 80919-1014
                                 U.S.A.

       Electronic mail to:

                CompuServe: 74777,3004
                Internet, Bitnet, etc.: support@stiller.com
                Uunet: uunet!support@stiller.com


   Integrity Master (tm)              -  2  -                 Version 3.02

    Fifth Edition May 1996 -- updated July 1996
    Copyright 1990-1996 Wolfgang Stiller.  All Rights reserved.

    The following paragraph does not apply where such provisions are
    inconsistent with law:

    Stiller Research provides this document "AS IS" without warranty of
    any kind, either express or implied, including, but not limited to the
    warranties of merchantability or fitness for a particular purpose.

    This document may include technical inaccuracies or typographical
    errors. We continually update and correct this document with the
    latest available information.

    Note to U.S. Government users:  Use, duplication, or disclosure by
    the U.S. Government of the computer software and documentation in
    this package shall be subject to the restricted rights applicable to
    commercial computer software as set forth in subdivision (b)(3)(ii) of
    Rights in Technical Data and Computer Software clause at 253.027-
    7013 (DFARS 53.027-7013).  The manufacturer is  Stiller Research,
    1265 Big Valley Dr., Colorado Springs, CO 80919.

    Integrity Master and Integrity Advisor are trademarks of Stiller
    Research.  Microsoft, Windows and MS/DOS are trademarks of
    Microsoft corporation.  IBM and OS/2 are trademarks of
    International Business Machines Corporation. Vines is a trademark of
    BANYAN Inc.  NetWare is a trademark of Novell Inc.  Unix is a
    trademark of AT&T. Sidekick is a trademark of Borland
    International.



   Integrity Master (tm)              -  3  -                 Version 3.02


     Use of Integrity Master (tm) (also known as IM) requires acceptance
     of the following license terms and warranty disclaimer.


     L I C E N S E    T E R M S
           
     TO USE INTEGRITY MASTER, YOU MUST AGREE TO AND UNDERSTAND THE
     FOLLOWING LICENSE TERMS AND WARRANTY DISCLAIMER, OTHERWISE DO NOT
     USE THIS PROGRAM.

     Each PC protected by Integrity Master must have its own license.
     To use Integrity Master on more than one PC, you must license extra
     copies.


     W A R R A N T Y    D I S C L A I M E R:

     INTEGRITY MASTER AND ALL ASSOCIATED PROGRAMS ARE LICENSED "AS-IS".
     STILLER RESEARCH AND WOLFGANG STILLER MAKE NO WARRANTIES, EITHER
     EXPRESSED OR IMPLIED, WITH RESPECT TO THESE PROGRAMS, THEIR
     QUALITY, PERFORMANCE, MERCHANTABILITY, OR FITNESS FOR ANY
     PARTICULAR PURPOSE. IN PARTICULAR,  INTEGRITY MASTER IS NOT
     GUARANTEED TO PREVENT OR DETECT DAMAGE TO YOUR DATA OR PROGRAMS. IN
     NO EVENT SHALL STILLER RESEARCH OR WOLFGANG STILLER BE LIABLE  FOR
     ANY CLAIMS FOR LOST PROFITS OR ANY DAMAGE, INCLUDING BUT NOT
     LIMITED TO SPECIAL, INCIDENTAL, CONSEQUENTIAL OR OTHER DAMAGE.
     SOME STATES DO NOT ALLOW THE  EXCLUSION OR LIMITATION OF INCIDENTAL
     OR CONSEQUENTIAL DAMAGES, SO THE ABOVE LIMITATION OR EXCLUSION MAY
     NOT APPLY TO YOU.

     IF YOU USE INTEGRITY MASTER (IM), YOU ASSUME EXCLUSIVE
     RESPONSIBILITY AND LIABILITY FOR ANY LOSS OR DAMAGE DIRECTLY OR
     INDIRECTLY ARISING OUT OF  THE USE OF THE PROGRAM.

     IN NO CASE SHALL STILLER RESEARCH'S OR WOLFGANG STILLER'S LIABILITY
     EXCEED THE LICENSE FEES PAID FOR THE RIGHT TO USE THE LICENSED
     SOFTWARE.

     THE LICENSE AGREEMENT AND WARRANTY DISCLAIMER SHALL BE CONSTRUED,
     INTERPRETED AND GOVERNED BY THE LAWS OF THE STATE OF COLORADO.





   Integrity Master (tm)              -  4  -                 Version 3.02



       T A B L E    O F    C O N T E N T S

       PART ONE - Integrity Master (tm) Users Guide

          License and Warranty Terms ........................  3

         CHAPTER ONE - WHY INTEGRITY MASTER
           Welcome! ..................................... 7
           Don't Read This .............................. 7
           Do Read This ................................. 7
           Why the Users Guide .......................... 8
           What Can Integrity Master Do? ................ 8
           How Does Integrity Master Do These Things?.... 9
           What Makes Integrity Master Special?.......... 9
           Requirements and Limitations ................ 10

         CHAPTER TWO - INSTALLING INTEGRITY MASTER
           Special Quick Install........................ 11
           Full Installation............................ 11
           Vital Files ................................. 12
           Screen Colors ............................... 13
           Using Integrity Master Menus................. 14

         CHAPTER THREE - RUNNING INTEGRITY MASTER
           Integrity Master Screen Contents ............ 15
           The Initialize Menu ......................... 15
           Initializing Integrity Data.................. 15
           What Is Integrity Data? ..................... 16
           The Check Menu .............................. 16
               CMOS Memory.............................. 18
           The Report File ............................. 20
           System Sectors .............................. 21
              Reloading ................................ 21
              Fixing ................................... 22
           The Commands Menu ........................... 24
              Disk Change and Directory Change ......... 24
              Quit - Exit Integrity Master ............. 24
              Uninstall - Delete Integrity Data ........ 25
           The Statistics Summary ...................... 25
           Virus Checking Procedure .................... 26
              Scanning for Viruses ..................... 27
              Quick scanning ........................... 29
              Scanning uploads ......................... 29
              Detecting Viruses ........................ 30
              Detecting Unknown (new) viruses .......... 30
              The Integrity Master virus report ........ 31
              False Alarms ............................. 32
              Destroying Viruses ....................... 33
              Data Corruption .......................... 33
           Integrity Master and Disk Problems  ......... 34
           Integrity Master for PC Security ............ 36
           Integrity Master for Change Control ......... 37
           Integrity Master for Laptop Configuration.... 37


   Integrity Master (tm)              -  5  -                 Version 3.02

           COMMAND LINE (BATCH) EXECUTION .............. 38
              Syntax ................................... 38
              Error Levels  ............................ 40
           Using IMCHECK ............................... 40
           Add-on programs.............................. 41
              RunMaybe - Conditional execution.......... 41
           Other Operating Systems ......................45
              Microsoft Windows and OS/2................ 45
              Networks ................................. 46
              Using IM on a Network .................... 46

         CHAPTER FOUR - CUSTOMIZING
           The Parameter (Options) File ................ 49
           Options Menu ................................ 50
           Options in SETUPIM .......................... 56
           Integrity Data Options ...................... 58
           Toggle CMOS Check Type ...................... 58
           Home Directory Options ...................... 58
           Updating Your Hardware Configuration ........ 59
           The Advanced Option Menu..................... 59

         CHAPTER FIVE -  ERRORS
           Solving Problems ............................ 63
           Answers to Common Questions ................. 63

     PART TWO - DATA INTEGRITY AND VIRUSES

         CHAPTER ONE - THREATS TO YOUR DATA
           Introduction - Viruses Get All The Glory .... 67
           Hardware and Power Faults ................... 68
           Finger Checks ............................... 68
           Malicious or Careless Damage................. 68
           Software Problems ........................... 69
           Software Attacks ............................ 69
               Logic Bombs ............................. 69
               Trojans ................................. 70
               Worms ................................... 70
               Viruses ................................. 70
                  General Virus Behavior................ 71
                  System Sector Viruses................. 72
                     Boot Sectors ...................... 72
                     Partition Sectors ................. 73
                  File Viruses ......................... 74
                     Macro Viruses ..................... 75
                     Polymorphic Viruses................ 79
                     Virus Toolkits .................... 80 IN PRINTED BOOK ONLY
           How Many Viruses Are There?.................. 80

         CHAPTER TWO - PROTECTION FOR YOUR PC
           Hardware Protection ......................... 83
           "Fixing" your disk .......................... 83
           Goof Protection  ............................ 83
           Intrusion Protection......................... 84
           Virus Defenses  ............................. 85
              Scanners ................................. 85
              Disinfectors ............................. 86
              Interceptors ............................. 87
              Inoculators .............................. 87
              Integrity Checkers ....................... 88
              Prevention................................ 90


   Integrity Master (tm)              -  6  -                 Version 3.02




         CHAPTER THREE - VIRUS MYTHS
           Mythical Sources ............................ 91
           Quick and Easy Cures ........................ 92
           Silly Tricks ................................ 92
           Retail Software Only? ....................... 92
           Write-Protecting Your Hard Disk ............. 93
           Safe Computing (Safe Hex?)................... 94

         CHAPTER FOUR - VIRUS REALITIES
           The ONLY Real Source of Viruses ............. 95
           Shareware Is as Safe or Safer ............... 95
           Few Virus Free Programs ..................... 95
           Write-Protecting Floppies ................... 96
           Beware the CE and the Demo! ................. 96

         CHAPTER FIVE - WHAT TO DO - SOME SUGGESTIONS
           Action is Vital - Now! ...................... 97
           Backup Policy ............................... 98
           Integrity Checking Policy ................... 98
           Run CHKDSK .................................. 99
           Determining Causes of Corruption ............ 99
           Education ................................... 99
              Signs of Software Problems ...............100
              Signs of Viruses .........................100
           Policy and Routine ..........................101
           Networks and Viruses ........................101
           Guidelines for Using Anti-virus Software.....102

         CHAPTER SIX - SAFELY USING COMPRESSION AND CACHE   IN PRINTED BOOK ONLY
           Safely Getting Maximum Benefit ..............103 IN PRINTED BOOK ONLY

         CHAPTER SEVEN- HANDLING A VIRUS ATTACK
           Report the Attack ...........................109
           Play Detective...............................109
           Clean House (Steps to Remove the Virus)......110
           Guard the House .............................110

         CHAPTER EIGHT- SPECIAL ANTI-VIRUS TECHNIQUES       IN PRINTED BOOK ONLY
           Using Common Utilities Against Viruses ......111 IN PRINTED BOOK ONLY
           Guidelines for Consultants ..................113 IN PRINTED BOOK ONLY
           Using Advanced Anti-virus Tools .............116 IN PRINTED BOOK ONLY

         CHAPTER NINE- THE LATEST INFORMATION ON VIRUSES    IN PRINTED BOOK ONLY
           Why Do People Write Viruses?.................119 IN PRINTED BOOK ONLY
           The Virus Underground .......................120 IN PRINTED BOOK ONLY
           East Block Viruses ..........................121 IN PRINTED BOOK ONLY
           How Viruses Mutate ..........................122 IN PRINTED BOOK ONLY
           Descriptions of Common Viruses ..............123 IN PRINTED BOOK ONLY

    Chapter Ten - About Stiller Research and the Author 139 IN PRINTED BOOK ONLY
           The author at work (graphic) ................140 IN PRINTED BOOK ONLY

     INDEX .............................................141 IN PRINTED BOOK




   Integrity Master (tm)              -  7  -                 Version 3.02



     PART ONE - INTEGRITY MASTER(tm) USERS GUIDE

     CHAPTER 1 - INTRODUCTION

     ____________________________________________________________________



     WELCOME!

     Welcome to the family of Integrity Master(tm) users!  Integrity
     Master (also known as IM) is the fastest, most powerful data
     integrity and anti-virus software available for any price.  I hope
     that you'll find Integrity Master an indispensable part of your PC
     tool kit.  From now on, you'll be back in control of all the data
     on your PC.


     DON'T READ THIS!

     You do not need to read the Users Guide before installing or using
     Integrity Master.  Most people should only rarely need to read the
     Users Guide.  If you're reading this to learn how to use Integrity
     Master, you're here for the wrong reason.  Just follow the
     directions on the diskette or on the cover letter.  The tutorial in
     SetupIM should tell you all you need to know to get started.  For
     additional help when using Integrity Master (IM), just press F1 and
     select the index.  The odds are, what you need to know is there.

     DO READ THIS!

     Please do read PART TWO - Data Integrity and Viruses of this book.
     It explains the threats to the integrity of your PC. It also
     explains viruses in detail so that you can understand how to fully
     protect yourself using Integrity Master. Also please do read the
     section on detecting "Unknown viruses" on page 31.

     Please do read the README.DOC file which comes with your copy of
     Integrity Master.  It contains information on anything that might
     have changed since we printed this manual.  You can read this file
     by using your favorite file viewer or the IMVIEW program included
     with Integrity Master.  The command "IMVIEW README.DOC" will let
     you browse through this file or "IMPRINT README.DOC" will print it.
     If you have any questions about IM or encounter any problems,
     please read the QUESTION.DOC file.



   Integrity Master (tm)              -  8  -                 Version 3.02


     WHY READ THE USERS GUIDE (Part One) ?

     I've written this users guide for three reasons:

     1) To provide more information on how to get the greatest benefit
       out of Integrity Master.  You'll learn how to:

       o use IM to detect totally new viruses

       o tell if file damage is likely due to a hardware problem, or
         possibly a virus or a trojan

       o use IM to protect your PC from unauthorized tampering, etc.

     2) To explain certain aspects of Integrity Master in more detail
        and in different terms than the explanation available from IM's
        internal help screens.

     3) To satisfy people who prefer to read things on paper.  If you
        prefer to read things on paper, then you're here for the right
        reason. Although, I'll bet the tutorial in SetupIM will surprise
        you.  (Give it a try!)


     What Can Integrity Master Do?

     1) Detect and remove viruses.  IM will even detect viruses that are
        not known to exist at this point.  For known viruses, IM will
        recognize them by name and describe what they do.

     2) Detect possible file corruption due to hardware or software
        problems.   This type of file damage is apparently at least 100
        times more likely than virus infection, yet it usually goes
        undetected.

     3) Supplement or replace any PC security programs you have.  IM
        will inform you if anyone changed something on your PC's disk
        while you were gone.

     4) You just compressed your disk or you restored your files from a
        backup. Are all the files really OK?   IM will tell you.

     5) You wanted to delete all your .BAK files, but you entered: "DEL
        *.BAT" by mistake.  Oops!  IM will tell you exactly which files
        you need to restore.

     6) You need a change management system to keep track of growth on
        your hard disk.  Where is all that disk space going?  IM will
        tell you.


   Integrity Master (tm)              -  9  -                 Version 3.02


     7) You're having problems with your disk drive.  Your diagnostic
        programs say all is OK . . . now.  But were some files damaged
        last night?  IM tells you!

     8) Your hard disk is having problems.  DOS will not even recognize
        it as a disk.  IM can reload your partition and boot sectors to
        "fix" your disk!


     How Does Integrity Master Do All These Things?

     1) It reads files as well as parts of the operating system on your
        disk known as system sectors.  The first time you use IM, you
        will run an "initialize" that will read your disk and calculate
        cryptographic signatures for each file and system sector.  While
        it's doing this, IM is also checking for signs of known viruses.

     2) This signature data, along with other information such as the
        file size, is encrypted and recorded in the "integrity data"
        file.  IM creates one such file for each directory on your disk.

     3) On subsequent checks, the files and system sectors are read
        again and the computed integrity data is compared with the prior
        values. This allows IM to determine if anything has changed,
        even if the time and date stamps reveal no change.

     4) IM detects changes that a virus may make to associate itself
        (companion and cluster viruses) with an existing program.

     A virus can only infect your PC by associating itself with your
     programs or system sectors.  In order to do this, a virus must
     change some existing data on your PC.  If nothing has changed, you
     can be absolutely certain that you don't have a virus.  IM can
     detect these changes if a virus tries to infect your system.

     What Makes Integrity Master Special?

     1)  Integrity Master is not just an anti-virus product but a
         complete data integrity system.  Viruses are but one threat to
         the integrity of your PC. With Integrity Master you have a
         complete solution.

     2)  Unlike other integrity checking programs, Integrity Master
         contains extensive information regarding known viruses.  If IM
         recognizes part of a known virus, it will identify the specific
         virus and provide specific steps to remove it (offering to do
         this automatically) and check for possible damage.  If it
         detects other file changes that are characteristic of a virus,
         it will alert you to that fact and provide appropriate
         instructions.

     3)  Unlike a virus scanner, Integrity Master allows you to detect
         unknown as well as known viruses.

   Integrity Master (tm)             - 10  -                 Version 3.02

     4)  Unlike anti-virus products that merely find known viruses,
         Integrity Master also detects files and sectors damaged (not
         just infected!) by viruses.

     5)  Integrity Master is fast!  We wrote it in 100% highly optimized
         assembler language.

     6)  Integrity Master utilizes easy to use menus with lots of help.
         You don't have to fully understand some of the more complex
         areas of data integrity, such as system sectors, yet you can be
         fully protected.

     7)  Integrity Master is the only anti-virus product that can check
         and report specific CMOS changes. It will also (if needed)
         reload the PC's CMOS.

     8)  IM can do ultra-fast scanning.  By running IM regularly (daily
         or every-other-day) in its "quick update" mode, you can scan a
         typical 1.2gb disk in 20 to 40 seconds and maintain a change
         history at the same time.

     9)  Integrity Master is useful with disk diagnostics.  You can run
         your normal test programs to check if your disk drive is
         working OK right now, but was it working correctly at 3 PM
         yesterday? Integrity Master will detect any disk errors which
         caused data damage earlier.


   INTEGRITY MASTER REQUIREMENTS AND LIMITATIONS:

     o  IM requires a PC with 310 thousand bytes of available memory and
        DOS 2 or later.  (At least 390 thousand bytes are needed for
        maximum speed.)

     o  Also runs under Windows 3.x, Win 95, Win NT, or OS/2.

     o  IM supports super-large disks and files.

     o  IM supports a maximum of 2621 files in a single directory.

     o  Do not use the DOS APPEND, SUBST or ASSIGN commands together
        with IM.  These can cause results that are misleading if you
        don't carefully consider the effects of these commands.  If you
        use Disk Manager or other special software loaded in the
        partition sector, be sure to read QUESTION.DOC for any special
        precautions.


   Integrity Master (tm)             - 11  -                 Version 3.02



     CHAPTER TWO - INSTALLING INTEGRITY MASTER
     ____________________________________________________________________

     Please follow the instruction on the cover letter or the diskette
     label to install Integrity Master.

     If you are a Windows user, you can use the "File Manager" or
     "Explorer" to double-click on the IMWIN.EXE file located in the
     \IM_HOME directory. This creates the Windows IM Program group and
     automatically runs SetupIM to begin the customization for your PC.
     After this completes, Click on the "2nd" icon to complete the
     install (If you need to rerun SetupIM, click on the "1st" Icon.)


     SPECIAL QUICK INSTALL PROCEDURE

     Since you may be wanting to do a quick evaluation of Integrity
     Master to see how it meets your needs, we offer a short cut install
     procedure.  In contrast, the full install procedure is intended to
     guard against unknown viruses already infecting your system or an
     attack by a sophisticated user, and is not necessary for an
     evaluation under normal circumstances.  The program SetupIM will
     offer you the quick install.  (SetupIM runs automatically during
     the install.)

     FULL INSTALLATION


     1) Follow the directions (normally by running IMsetup) in the cover
        letter to install the IM files on your hard disk and run SetupIM
        (SetupIM is started automatically by IMsetup).

     2) SetupIM will guide you from there.  SetupIM will offer you a
        full tutorial on using Integrity Master menus and give you an
        overview of how Integrity Master works.  SetupIM will then
        analyze your needs and check out your hardware configuration.
        SetupIM's Integrity Advisor(tm) component will customize IM's
        options so that it will work best to meet your needs.  The
        Integrity Advisor(tm) will also prepare a custom designed
        procedure to finish the install and a plan for day-to-day use of
        IM.  In addition to displaying this plan on your screen, the
        Integrity Advisor will write the plan to file IMPROC.TXT.  You
        can use your favorite utility to read IMPROC.TXT or you can
        enter the command:
              IMVIEW IMPROC.TXT
         to read it, or the command
              IMPRINT IMPROC.TXT
         to print the file.


   Integrity Master (tm)             - 12  -                 Version 3.02


     IMPROC.TXT contains IMCHECK check values for IM.EXE and IMCHECK.EXE
     so that you can verify that you have a good copy of these programs.

     EASY ACCESS TO INTEGRITY MASTER

     You may wish to copy *.EXE and IM.PRM into a directory on your DOS
     PATH (e.g., "\DOS") to make IM convenient to run from any location
     on your system.



     VITAL FILES

     Please check file README.DOC for a full list of files that come
     with Integrity Master and what's important about each file.  To
     read README.DOC, type: "IMVIEW README.DOC" and press ENTER.

     After you install Integrity Master, there will be only two files you
     absolutely need to use Integrity Master:

     IM.EXE  - Integrity Master itself

     IM.PRM  - The parameter file which controls how IM works
                  - This file is created by SETUPIM.EXE

     If you want to reinstall IM, or change advanced features of IM, you
     will need:

     SETUPIM.EXE The setup and install program (It creates
                    and updates IM.PRM)

     IM.DAT       Needed for initial installation of IM only.  This file
                    contains your serial number and name.

     When you install IM, SetupIM will create these files:

     IMPROC.TXT  Instructions on how to finish installation and run IM

     IM.PRM           The parameter file (all option settings are stored
                      here)


   Integrity Master (tm)             - 13  -                 Version 3.02

     SCREEN COLORS

     IM normally detects the type of video adapter you have
     automatically and uses appropriate colors for your equipment.
     There are two things that can confuse IM:

     1) Some programs change the DOS video mode from color to monochrome
        or vice-versa.  To correct this, just enter the appropriate mode
        command (e.g., "MODE CO80")

     2) Some equipment appears to have a different display than it
        really has, such as an LCD display on a laptop.  (Most modern
        laptops do a good job displaying colors directly or of mapping
        colors into shades of gray and you won't need to do any
        special.)

     If you find your display hard to read, you may want to override
     IM's choice of video mode (colors).  The best way to do this is to
     experiment by using the command line parameters to specify an
     alternate set of colors.  Try each option and choose what looks the
     most pleasing. Generally, modern Laptops will work well in color
     mode.

     Both IM and SetupIM accept these command line parameters:

     /L  - For older CGA type liquid crystal displays (e.g.,
           Toshiba 1000 laptops)
     /M  - Forces monochrome mode
     /C  - Forces color mode
     /A  - Forces automatic video detection mode (default).
     
     Example: "IM /M" will use colors appropriate for a monochrome
     display even if the display appears to be of a color display.

     Once you've found the video mode (colors) that work the best, it's
     usually easiest to use SetupIM to select that video mode and save
     it as your normal video mode.  From then on, IM will use this video
     mode without a command line parameter.


   Integrity Master (tm)             - 14  -                 Version 3.02


     USING INTEGRITY MASTER MENUS

     Integrity Master (IM) and SetupIM both employ an advanced menu
     system.  When you first install using SetupIM, it will offer you an
     extensive guided tour of how these menus work.  This is the best
     way to learn how to use the menus.  Within Integrity Master, just
     press F1 and select "Help using the menus" from the help menu for
     assistance.

     On most menus you will see one selection shown in a different color
     (or underlined) from the other selections.  The different color
     (highlight) indicates that this is the chosen line.  You can use
     the arrow (cursor) keys to select any of the items on the menu.
     Each menu line has a single capitalized letter displayed in a
     different color.  Pressing the key matching that letter will also
     select that menu item.  On many menus, an extended explanation
     automatically appears as you select any menu line.  After you have
     chosen the appropriate menu item, you must press the ENTER key
     before anything will happen.


   Integrity Master (tm)             - 15  -                 Version 3.02


     CHAPTER THREE - RUNNING INTEGRITY MASTER(TM)
     ____________________________________________________________________


     INTEGRITY MASTER SCREEN CONTENTS

     The top part of the Integrity Master screen tells you what options
     are in effect and what IM is currently doing.  The menus appear
     below this.  Be sure to go through the tutorial in SetupIM to learn
     how to use the menus.  When IM is busy checking your files, the
     report screen pops up and replaces the lower half of the screen
     including the menu area.

     The best way to get familiar with the information presented to you
     on the IM screen is by pressing the F1 (help) key and selecting the
     "Explanation of the display" entry.  This will give you a step by
     step guided tour of IM's display.


     INITIALIZING INTEGRITY DATA

     Before you can check your disk, you must initialize the integrity data
     that describes the disk.  You can use either the command line parameter (/IE) or the Initialize menu within IM.  Press "I" or alt/I (hold
     down the ALT key and press "I") to get to the Initialize menu.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÉÍÍÍÍÍÍÍÍÍÍ»ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³   Help    Options   Check   ºInitializeº    ReLoad    CoMmands  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ÉÍ¼          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ» ÄÄÄÙ
                                 º  Entire disk integrity         º
                                 º  Files on current Disk         º
                                 º  Current and Lower directories º
                                 º  Current diRectory only        º
                                 º  Boot sector                   º
                                 º  Partition sector              º
                                 º  CMOS memory                   º
                                 º  Resident Programs and memory  º
                                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     From this menu, you create (initialize) the integrity data that
     describes your files, CMOS memory, resident programs, and system
     sectors. While IM is initializing the integrity data, it will
     (unless you turned virus checking off) check for known viruses, and
     check for other indications of viruses or system problems.  For the
     system (boot and partition) sectors and CMOS, IM will save reload
     information.  This enables you to restore your system sectors
     (using the ReLoad menu) if anything should ever infect or damage
     them.  IM writes the reload data to files CMOS.SRL, BOOT.SRL, and
     PART.SRL for the CMOS memory, DOS boot sector, and partition sector
     respectively.  Be sure to read the section in Part Two, Chapter
     One, that explains why system sectors are important.


   Integrity Master (tm)             - 16  -                 Version 3.02

     When you first use IM, please select "Entire disk integrity" to
     initialize the integrity data for all files and system sectors (the
     boot or partition sectors) that exist on the current disk.  IM will
     also create the system reload files (CMOS.SRL, BOOT.SRL, and
     PART.SRL). IM will create file MEMD.SRL (MEMW.SRL if running under
     Windows or MEMO.SRL under OS/2) to contain the resident program and
     memory configuration.  Be sure to save a copy of these files on
     diskette to help you recover when your hard disk fails.  (Not all
     disks have both boot and partition sectors).


     WHAT IS INTEGRITY DATA?

     When IM checks a file, it uses each byte of the file in a
     calculation to compute cryptographic signatures for that file.  A
     change to any part of a file will result in a different signature.
     These signatures, along with other significant information such as
     file size, are what I call integrity data.  IM writes an integrity
     data file for each directory on your disk. These files can be
     stored with the files that they describe or stored on separate
     diskettes.

     When you first run SetupIM, it chooses, at random, a unique
     algorithm to compute the cryptographic signatures, and also chooses
     a unique algorithm to encrypt your integrity data files.


     WHAT ARE CRYPTOGRAPHIC SIGNATURES?

     Just as your signature uniquely identifies you, the cryptographic
     signatures serve to identify the contents of each file.  If a virus
     or a hardware problem changes a file, the signature computed for
     that file will be different, although the file size and time and
     date stamps may be the same. A change or the rearrangement of data
     in a file will result in a different signature.  When you execute
     SetupIM, it will randomly select a unique algorithm for computing
     the cryptographic signatures.



     THE CHECK MENU

     From the Check menu, you can check files or system sectors for
     changes.  Use the up and down arrow keys to select the type of
     checking you'd like to do. You may choose to check only specific
     things on your disk, such as the system sectors or individual
     files, or you can check everything on the entire disk.  IM will
     report any added,  deleted, or changed files as well as any signs
     of viruses or other known problems.  If integrity checking is on,
     IM will read the files and check for any changes.  Use the Options
     menu to control whether full integrity checking is on and the type
     of files to check.  The fourth line at the top of the screen shows
     the current status of integrity checking including the type of
     files to be checked.  If you see: "Integrity check: On", this
     indicates that full checking will be done on all files.

   Integrity Master (tm)             - 17  -                 Version 3.02

     You can reach the Check menu by pressing "C" or alt/C.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÉÍÍÍÍÍ»ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³   Help    Options   ºCheckº   Initialize    ReLoad    CoMmands  ³
     ÀÄÄÄÄÄ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼     ÈÍÍÍÍÍÍÍÍÍÍÍÍ» ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
            º  All disks                      º
            º  Entire disk integrity          º
            º  Files on current Disk          º
            º  Current and Lower directories  º
            º  Current diRectory only         º
            º  Specific file(s)               º
            º  Boot sector                    º
            º  Partition sector               º
            º  Disk for known Viruses         º
            º  CMOS memory (FULL)             º
            º  Resident Programs and memory   º
            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Entire disk integrity

       Selecting this option and pressing the ENTER key will check any
       system sectors (the boot or partition sectors) that exist on the
       current disk for changes and then check all files in all
       directories.

     Files on current Disk

       Selecting this option and pressing the ENTER key will check only
       files on the current disk.  System sectors will not be checked.

     Current and Lower directories

       Selecting this option and pressing the ENTER key will check files
       in the current directory and any files in any directories which
       are defined as descendant from the current directory.  If the
       current directory happens to be the root directory (e.g., C:\)
       then all files on that disk will be checked since all other
       directories are descendant from the root directory.  Another
       example: if you're in directory \DOS, directories such as \DOS\A,
       \DOS\UTILS or \DOS\A\B  will be checked in addition to \DOS.

     Current diRectory only

       Selecting this option and pressing the ENTER key will check only
       files in the current directory.

     Specific file(s)

       Selecting this option and pressing the ENTER key allows you to
       enter the name of a specific file to check.

     Boot sector

       Selecting this option and pressing the ENTER key will read the
       DOS boot sector and check it for any changes.  Please see the
       explanation of system sectors later in this guide.

   Integrity Master (tm)             - 18  -                 Version 3.02

     Partition sector

       Selecting this option and pressing the ENTER key will read the
       partition sector (also known as the master boot record or MBR)
       and check it for any changes.  Please see the explanation of
       system sectors later in this guide.

     Disk for known Viruses

       The option to check "Disk for known Viruses" is intended mostly
       for quick virus scans or to do checks of all files (not just
       those identified as executable files) for known viruses.  You can
       do a virus scan on just the current directory, the current
       directory and all lower subdirectories, or on the entire disk. If
       you choose the entire disk, then the appropriate system sectors
       will be checked as well as all executable files.  IM provides an
       option to scan only floppy boot sectors for viruses. I suggest
       you use this option to screen all your floppies if you should
       ever encounter a system sector virus.  IM also provides an option
       to scan all files (not just executables) for viruses. Scanning
       all types of files is useful as a double check in the event that
       IM detects an existing virus.  This is suggested since it's
       possible that you may have a program somewhere that uses a file
       with a nonstandard extension to store executable code (e.g.,
       overlays).  If you are aware of a program that uses extensions
       which IM does not recognize as executable, then you may wish to
       use the Advanced menu in SetupIM to add this extension to the
       list of extensions recognized by IM. You generally won't need the
       virus scanning option except in these special cases, since IM
       automatically checks for viruses during its normal processing.
       You can also use the /VA, /VB, /VM, /VO, /VR, or /VL command line
       parameters to perform a virus scan.

     CMOS Memory

       Integrity Master can check the CMOS memory describing the
       configuration of your PC. It can check either the "FULL", the
       "BASE" (the standard 64 byte AT CMOS portion) CMOS, or the "CORE"
       CMOS.  "CORE" is the standard setting and checks only those parts
       of CMOS that are vital to the integrity of your PC. The menu will
       display whether "FULL", "BASE", or "CORE" CMOS is being checked.
       You can use SetupIM to change this. Most modern PCs now have more
       than the standard 64 byte base CMOS memory. IM can check your
       entire CMOS.  IM ignores the "known to change" portions of your
       CMOS when checking.  CMOS is used differently by each
       manufacturer, but IM will diagnose the change to CMOS and report
       as much information as possible regarding what has changed.  For
       example, if you install a new floppy drive, you would expect the
       CMOS describing the floppy setup to change. If you see that many
       items in your CMOS have changed, then it's a good bet that your
       battery is failing or a buggy program may have trashed your
       entire CMOS.  In this case, let IM reload your CMOS for you.

   Integrity Master (tm)             - 19  -                 Version 3.02

                 CMOS is the special battery powered memory that
                 contains information on how your PC is configured.
                 If this memory is changed, your PC may be unable
                 to boot so be sure to save the CMOS.SRL file
                 on a floppy.

       Generally, XT class (and earlier) PCs don't have CMOS memory.
       There's usually a setup program (sometimes accessible only at
       boot time) that allows you to change your PC's configuration and
       thereby change the CMOS contents. If you do this, be sure to use
       the CMOS option on the Initialize menu to update IM's saved copy
       of your CMOS (in file CMOS.SRL).

       CMOS is powered by a battery so that its contents will stay
       intact when your PC is off.  You must periodically replace this
       battery. When it starts to fail, you will notice unexpected
       changes to your CMOS.  After you replace the battery, use the
       ReLoad menu to restore your original configuration.

       Most modern PCs now have more than the standard 64 byte base CMOS
       memory. IM ignores the non-critical or "known to change" portions
       of your CMOS when checking.  CMOS is used differently by each
       manufacturer, but IM will diagnose the change to CMOS

       and report as much information as possible regarding what has
       changed.  For example, if you install a new floppy drive, you
       would expect the CMOS describing the floppy setup to change. If
       you see that many items in your CMOS have changed, then it's a
       good bet that your battery is failing or a buggy program may have
       trashed your entire CMOS.  In this case, let IM reload your CMOS
       for you.

       CMOS is not implemented the same way on all PCs. Integrity Master
       follows the standard definition for the IBM PC AT which is now
       extended for modern PCs. IM supports the most common
       configurations, but it's possible that your PC may use portions
       of your CMOS memory in a different way. Don't be alarmed if an
       area of your CMOS changes (especially if you use a laptop); some
       PCs use portions of CMOS for special purposes with the result
       that there may be one area that normally changes.  The area that
       you are most likely to see changing on your PC is what IM calls
       the "OEM options' area. If IM only reports a change to only one
       area, you need not be concerned--this is normal.  If your CMOS
       supports a boot password for your PC, you will see a change to
       CMOS each time you change your password.  When this happens, it's
       best to use the Initialize menu to save a copy of the updated
       CMOS with your new password.

   Integrity Master (tm)             - 20  -                 Version 3.02

     Resident Programs and memory

       This option allows you to make sure that your resident programs
       have not changed and that no new programs (such as
       memory-resident viruses) are active on your PC. In addition to
       alerting you to potential system problems, this protects you
       against unknown memory-resident viruses without you needing to
       boot from a diskette.  It also checks to make sure your available
       memory does not show signs of a suspicious decrease. IM
       accomplishes this by examining the programs and the interrupts
       that are resident in your PC's memory.  If you install a new
       resident program or if you change device drivers (these are
       usually found in  entries in your CONFIG.SYS and AUTOEXEC.BAT
       files), IM will report a change.  The "/CM" command line switch
       allows you to invoke this option.

       It is vital that you run the "resident program check" always at
       the same point, such as immediately after boot.  If you execute
       other programs which stay resident in memory, or if you have
       programs that change their allocation of memory while you use
       your PC, you can expect IM to report these changes. If you have
       multiple boot configurations, you can use the "/MF=" command line
       option to specify a different memory configuration file for each
       situation.


     Important Reminders Before Checking:

     o Before using IM, be sure that you've run SetupIM (new install)
       and followed the directions provided for you in file IMPROC.TXT.

     o Before checking your files for the first time, run an "Entire
       disk integrity" initialize (Windows users can click on the "2nd"
       icon).

     o For protection against previously unknown viruses, be sure you
       cold boot from a write-protected floppy before checking.  (With
       version three or later you will be able to do a resident program
       check to provide similar protection.)


     THE REPORT FILE

     In addition to seeing a report of IM's findings on screen, you may
     wish to save a report on disk or on paper.  The Options menu in
     both IM and SetupIM allows you to set the type of report (if any)
     IM will create.  I recommend that you allow IM to write its
     findings to an "auto-named" disk file.  By saving these report
     files, you can discover what changed last April 1 or when you last
     changed a particular file. Each time you run IM, it will write its
     findings to the end of the report file for that day.  For example,
     on June 1, 1996, the report would be in file "0601.REP" (you can
     control the name given to these files). By saving the report files,
     you can maintain a complete change history for your PC.  If you
     ever want to find out what happened to a file, the


   Integrity Master (tm)             - 21  -                 Version 3.02

     full history will be available.  If you wish to keep more than one
     year of history on-line, try copying all the report files (COPY
     *.REP) to another disk or subdirectory.

     If you choose an "auto-named" report file, you can elect that IM
     place the file in the IM "home directory" (usually "\IM_HOME") of
     whichever disk is being checked, or you may choose to place the
     report files on a specific disk of your choice.  For normal
     installations, the report file is written to disk C.  If you
     installed IM from a version before 2.31, then your report files may
     still be written to the root directory rather than the IM "home
     directory".  (Run SetupIM if you want to start using the "home
     directory")

     You can also give the report file absolutely any name you wish.  If
     you choose a specific filename, you should include the disk and
     directory as part of the filename.  If you do not specify a disk or
     directory as part of the filename, then IM will create this file in
     the current directory at the time IM starts checking. You can also
     specify a specific report file name by using the "/RF=" command
     line parameter.

     If you elect printed output, IM will ask you to choose LPT1, 2,  or
     3. In the rare event that this does not work with your printer, you
     may also print by asking IM to write the report to a specific file
     name such as "PRN" (the printer).  If you use "PRN", you will get
     less sophisticated error handling and messages since DOS drives the
     printer rather than IM.


     SYSTEM SECTORS

     System sectors are special areas on your disk containing programs
     that are executed when you boot your computer.  These sectors are
     invisible to normal programs but are vital for correct operation of
     your PC.  They are a common target for viruses.  Please read the
     detailed description of Boot and Partition sectors in Chapter One
     of PART TWO - Data Integrity and Viruses.


     RELOADING

     You can reach the ReLoad menu by pressing "L" or alt/L from any of
     the other primary IM menus.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÉÍÍÍÍÍÍ»ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³   Help    Options   Check   Initialize    ºReLoadº    CoMmands  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ÉÍ¼      ÈÍÍÍÍÍÍÍÍÍÍÍÍ» Ù
                                               º  Boot sector        º
                                               º  Floppy boot sector º
                                               º  Partition sector   º
                                               º  Missing partition  º
                                               º  PArtition boot codeº
                                               º  CMOS memory        º
                                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     From the ReLoad menu, you may reload your CMOS memory, DOS

   Integrity Master (tm)             - 22  -                 Version 3.02

     boot sector, or  your partition sector (master boot record), in the
     event that they have become damaged or infected with a virus.  The
     "reload Missing partition" option must be used if you have a disk
     so badly damaged that DOS will not recognize that the disk exists.
     You will then be prompted to identify the disk on which to reload.
     You can identify it either by the logical disk letter (A-Z) or by
     the physical device number (0 for the first physical hard drive, 1
     for the second, and so on).

     RELOADING CMOS

     If you reload your CMOS, its contents will be reset to their state
     at the time you let IM initialize the CMOS (with the exception of
     the time and date information).  If your CMOS has a boot password,
     this will be reset also. IM must have file CMOS.SRL in the IM "home
     directory" or a root directory of one of your disks in order to
     reload the CMOS.  CMOS is not implemented the same way on all PCs.
     Some (rare) PCs can disable write to CMOS or do so in a
     non-standard way; in this case, IM may not be able to reload your
     CMOS. (Please check your motherboard manual for details on your
     CMOS.)


     REWRITING (FIXING) BOOT SECTOR CODE

     There are two options that actually reconstruct and rewrite the
     sector rather than reload from a save copy (an *.SRL file).  These
     options are "Floppy Boot Sector" and PArtition boot code."


     REWRITING (FIXING) FLOPPY BOOT SECTORS

     The "Floppy Boot Sector" option will check the disk parameters and
     replace the executable code in the boot sector with a clean selfchecking program. This option can be used to remove boot sector
     viruses from floppy diskettes when IM has no reload data. It can
     correct the disk parameters (diskette type, size, # of tracks, etc.) if
     needed.  Since viruses and disk corruption can damage or change the
     diskette parameters, Integrity Master displays the diskette type before
     rewriting the boot sector:

               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º  Your diskette appears to be of the    º
               º  type selected below. If this is OK,   º
               º  just press ENTER, otherwise select    º
               º  the correct type and press ENTER.     º
               ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
               º  180K 5.25"                            º
               º  360K 5.25"                            º
               º  1.2mb 5.25"                           º
               º  720K   3.5"                           º
               º  1.44mb 3.5"                           º
               º  2.88mb 3.5"                           º
               º  Bad or non-standard diskette type     º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


   Integrity Master (tm)             - 23  -                 Version 3.02

     IM indicates the detected diskette type by highlighting one of the
     lines above. You should verify that this is the correct type and
     hit ENTER. If this is not the correct type, you can change the
     selection and IM will correct the diskette parameters accordingly.
     If you select, "Bad or non-standard diskette type", IM will not
     change the existing diskette parameters but will rewrite the
     executable code in the boot sector.

     The most common diskette type today, is the 1.44mb 3.5 inch
     diskette. This diskette can be identified by the two square holes
     on the corners of the diskette. The next most common type, the 720K
     3.5 inch diskette has only a single hole (the hole with the
     write-protect tab).

     If booted, this boot sector will do a check on its own integrity
     and display the message:

          "This is not a bootable diskette
          Please remove and reboot."

     if the self-checks are OK.

     The command line switch: "/RF" (Reload Floppy) will invoke this
     option.

     REWRITING THE PARTITION BOOT CODE

     The ReLoad menu option titled, "Partition Boot code" (and there the
     associated command line switch: "/RE") will check the partition
     table and replace the executable code in the partition sector (AKA
     Master Boot Record) with a clean self-checking program. This can be
     used to remove boot sector viruses from your hard disk when IM has
     no reload data.  This code is compatible with DOS 2.1 or later,
     OS/2, Win 95, Win NT and other operating systems. When you boot
     from a hard disk with the new boot code you will see the message:

            Partition Sector V2 Copyright 1996 by Stiller Research

     If you don't see the above message it can indicate that the boot
     sector has been replaced.  You may have to watch carefully to see
     this message since other messages in the boot process will quickly
     overlay this message.  If the self-checks detect a problem you will
     see:

             Partition Sector is damaged or infected.
             Boot from a diskette and run a full Integrity Master check.

     These checks are intended only as an aid, not a replacement for
     normal Integrity Master checks since they will not detect infection
     by some stealth viruses.

   Integrity Master (tm)             - 24  -                 Version 3.02


     THE COMMANDS MENU

     You can reach the "CoMmands menu" by pressing "M" or alt/M from
     any of the other primary IM menus.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÉÍÍÍÍÍÍÍÍ»ÄÄÄ¿
     ³   Help    Options   Check    Initialize    ReLoad  ºCoMmandsº   ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼        ÈÍ» Ù
                               º  Temporarily Shell out to DOS       º
                               º  Quit - exit Integrity Master       º
                               º  Disk change                        º
                               º  DiRectory change                   º
                               º  Uninstall - delete integrity data  º
                               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Temporarily Shell out to DOS

       This allows you to exit IM to the DOS prompt, but leaves
       Integrity Master loaded in memory so you can quickly return by
       using the Exit command.  Shelling allows you to exit IM, and
       execute most other programs at the DOS prompt (such as copying
       files or formatting disks).

     Disk Change and DiRectory Change

       You'll mostly use this menu to change the current disk or
       directory. (You can also use the "/D" command line option to
       change to one or more other disks or use the "/P" command line
       parameter to start in a different directory)


     Quit - exit Integrity Master

       In addition to using the "Quit - exit Integrity Master" option on
       the CoMmands menu, you can use the ESCape and alt/X keys to
       terminate IM from any point.  The ESCape key allows you to
       terminate most IM menus without taking any action and return to
       the prior menu.  The only exceptions to this are menus which
       require a response one way or another.  These are usually the
       result of a detected error of some type.  If you press ESCape
       enough times, IM will ask if you really want to quit.  You must
       select "Yes" and press ENTER to exit.  The fastest way to exit
       IM, is by pressing alt/X (hold the ALTernate key down and press
       the "X" key).  This allows you to quickly exit without the final
       "Do you really want to quit?" prompt.


   Integrity Master (tm)             - 25  -                 Version 3.02

     Uninstall - delete integrity data

       If you have integrity data files in each directory of your hard
       disk, you can quickly delete these files by selecting Uninstall
       on the CoMmands menu.  If your integrity data is stored on a
       different disk than the files it describes (such as a floppy)
       then this option will have no effect.


     THE STATISTICS SUMMARY

     Whenever you finish checking files, IM will show you a summary of
     its findings.  Since the summary contains a time and date stamp,
     you can use the report file as a chronological log of all changes
     on your PC, even if you have it going to the printer.  The summary
     shows statistics for all file changes, as well as system sector and
     memory checking.  IM reports the number of times it checked a
     file's integrity data against the DOS directory information, as
     "files processed". It also reports a separate count of the number
     of files actually read and checked.  IM resets all statistics (with
     the exception of the memory check results) each time after it
     displays the summary statistics.  This means that on subsequent
     file checks, the system sectors will be indicated as "Not checked"
     even though they were indicated as checked on the prior display.
     Why is this?   IM does this because some disks are removable and
     disk X may suddenly be a different disk.  IM shows the statistics
     for any viruses, suspicious files, or system corruption (which
     includes file open and read errors) in red.

     The item "PC Config.:" displays the results of the "Resident
     programs and memory" check.


     VIRUSES - WHAT ARE THEY?

     Viruses are but one of many threats to your data.  You are far less
     likely to be hurt by a virus than by other causes of data damage
     such as software conflicts and general glitches of various types.

     Viruses are programs that attach themselves to other programs in
     such a way that when the other program is executed, the virus code
     will also execute.  The infected program usually appears to execute
     normally but the virus may be attaching itself to additional
     programs each time the infected program runs.  Many viruses are
     triggered by some event (such as a particular time or date) into an
     attack phase, resulting in anything from music to serious file
     damage.  Viruses often wait a long time before attacking; their
     goal is to spread as far as possible before revealing their
     presence.  Some viruses go resident in your PC's memory, taking
     over your PC.  This enables them to infect at will and elude
     detection attempts.

     A virus may attach itself to programs in two ways that many people
     are not aware of.  The first way is to infect the programs that are
     in the system (boot and partition) sectors of your PC.  The second
     way is by changing system information on your PC so that the virus
     code is executed before the intended program. The most obvious way



   Integrity Master (tm)             - 26  -                 Version 3.02

     to do this depends on the fact that if both a .COM and .EXE file
     have the same name, DOS will execute the .COM file instead of the
     .EXE file. Such a virus is commonly called a companion or spawning
     virus. These viruses locate .EXE files and then plant themselves as
     .COM files of the same name.  The virus (the .COM file) can
     execute, spread further, and then run the .EXE program so that
     everything appears normal. (Don't worry; IM detects all types of
     viruses!) Please read PART TWO -- Data Integrity and Viruses to
     learn more about viruses.


     VIRUS CHECKING PROCEDURE

     When you install Integrity Master using SetupIM, the Integrity Advisor will prepare a complete procedure for running IM.  If you indicated that you wanted to detect viruses, then this procedure would include the steps you need to check for viruses.  This step by step 
     procedure is customized to your own preferences, so be sure to read 
     file IMPROC.TXT first. 

     To be certain of detecting even unknown viruses, it is best to cold 
     boot from your write-protected floppy containing IM before checking 
     for viruses.  Do NOT use Ctrl/alt/del to boot, but turn your PC off
     and then on.  Some PCs have a reset button that will force a cold
     boot. (Version three of IM provides an alternative to cold booting
     by performing a resident program check that will detect
     memory-resident viruses.)

     Whenever you engage in any activity that changes or rearranges many
     files, run at least a "Quick update", so that your integrity data
     accurately reflects the status of your PC.  Use the Options menu to
     change the type of integrity checking.

     o With Integrity "CHECK ON", do a full integrity check (rather than
       a "quick update") of all files at least once a month to detect
       any unexpected changes.

     o If your work exposes you to programs that may be infected with
       viruses, do a daily full check of your disk for any unauthorized
       changes.  To save time, use the Options menu to limit checking to
       executable programs.  Check at least the current directory if you
       have executed any new or "strange" programs.

     o After installing any new software, IMMEDIATELY run IM to
       initialize the integrity data for the new files you have created.
       Be sure that you save a write-protected disk containing a copy of
       the software.  It is vital that you do this before you start to
       use the software.

     o It is worth doing some extra checking any time you copy programs
       (e.g., *.EXE or *.COM files).  When you copy programs, copy your
       integrity data also.  For example, if you are doing something


   Integrity Master (tm)             - 27  -                 Version 3.02

       like a "COPY  *.EXE   D:\DOS", then also enter a command to copy
       the integrity data to "D:\DOS".  (If you're not sure what the
       names of your integrity data files are, check your IMPROC.TXT
       file or select "Integrity data options" on the SetupIM Change
       menu.) If you simply copy all files (COPY *.*), then you won't
       have to worry; the integrity data will automatically be copied
       along with the programs.  Afterwards, run IM to check that the
       files were copied without damage or virus infection.  Naturally,
       IM will report any files that weren't copied as deleted when you
       run this check.


     SCANNING FOR VIRUSES

     To quickly do nothing but scan one or more disks for known viruses:

     o Use the CoMmands menu or the "/Dx" command line parameter to
       change to the drive you want to scan.

     o Use the Options menu to turn the report off or to set the report
       to go to the printer or your hard disk.

     o From the Check menu choose "Disk for known Viruses".  Press ENTER
       and select either "One-time scan of disk" or (if you're planning
       to check several floppies) "Check Multiple diskettes".

     o Some viruses will create a boot sector that can hang DOS or
       Windows. If your PC should freeze while checking a diskette, then
       reboot and select "Scan floppy Boot sectors" from the "Disk for
       known Viruses" menu. This will check the diskette without using
       DOS.

     o This scans the first disk.  When you see the display summarizing
       the results of the scan, insert the next diskette and press enter
       to scan that diskette or press ESCape if you're done scanning.

     You can also use the command "IM /Dx /VM" to scan multiple
     diskettes in drive x.  Use "/VO" rather than "/VM" to scan only one
     diskette.

     IM will return a DOS error level of 64 or greater if it detects a
     known virus, so you can have a batch file do automated scanning.
     We provide some batch files that do this for you and serve as
     samples for using IM in your own batch files:

     IMSCAN.BAT  This batch file allows you to scan files on an entire
          disk or specific directory on a disk and all lower
          subdirectories. For example, to scan files on disk C, type
          "IMSCAN C:" or to scan subdirectory DOS and all lower
          directories (e.g., \DOS\UTILS) type "IMSCAN \DOS". If you
          don't want to check memory each time include a "/B" (e.g.,
          "IMSCAN \DOS /B"

     IMSCAND.BAT This allows you to scan a specific subdirectory. You
          can specify just the subdirectory or both the subdirectory and
          the disk (e.g., "IMSCAND C:\PCB\UPLOADS").


   Integrity Master (tm)             - 28  -                 Version 3.02

     IMSCANM.BAT Allows you to scan multiple diskettes for known
          viruses. After each diskette, IM will prompt you to insert
          another.

     IMQ.BAT      Does a check in "Quick Update" mode of your current
          disk. This scans memory and the system sectors for known
          viruses and then checks only the files that have changed,
          providing a very fast way to check an entire disk for known
          viruses.  This also keeps your integrity data current for all
          files so that you are up-to-date in case of a problem.  If you
          want to specify a different disk to check, you must use the
          "/Dx" command line switch (e.g., "IMQ /DCF" will check both
          drive C and drive F).

     IMONCE.BAT  Uses RunMaybe to run a "Quick Update" once a day. This
          is the fastest way to make sure your disk stays clear of
          viruses.

     IMAUTO.BAT  Will create a backup copy of your AUTOEXEC.BAT file and
          then modify it to include the once-aday "Quick Update" from
          IMONCE.BAT.  This way your PC will get a daily quick check.


     To scan a disk for known viruses AND to get data integrity
     protection:

     o Use the Options menu and set the "Files to iNitialize" option to
      "Executable programs."

     o Use the Initialize menu to initialize "Entire disk integrity".

     The command line options: /VA, /VB, /VM, /VO, /VR, and /VL are
     available for scanning.  Remember that virus scanning will detect
     only viruses known at the time this program was written.  As with
     any scan program, you should have the latest version if you intend
     to rely upon scanning for serious protection.

     SCANNING DISKETTES

     If you have detected a boot sector virus on your hard disk, you
     will want to scan all your floppy diskettes for infected boot
     sectors. To do this, , select "Disk for known Viruses", (from the
     "Check" menu) then select "Scan floppy Boot sectors" or just start
     IM with the "/VB" command line option.  This will allow you to
     quickly scan diskettes (bypassing DOS) and remove any viruses
     found.  Using this option, you can scan diskettes that contain boot
     sectors that are unreadable by DOS (or which will cause DOS to
     crash.)

     QUICK SCANNING

     Integrity Master provides an ultra-fast way to effectively perform

   Integrity Master (tm)             - 29  -                 Version 3.02

     a full scan of your hard disk.  We call this "Quick scanning".
     Quick scanning is only possible on disks where you have allowed IM
     to perform an initialize to establish initial disk integrity.  Once
     you have initialized a disk, you can ask IM to check in "quick
     update" mode. This fully checks only files that show signs of
     changes or that have been added. This is not as effective as
     running Integrity Master in it's normal mode which provides full
     integrity checking, but this provides scanning as effective as that
     provided by any of the other scan programs and runs much, much
     faster. These types of checks are so fast that most users don't
     mind including a daily scan.  One way to make sure this happens
     regularly is to execute IMAUTO.  This will modify your AUTOEXEC.BAT
     so that IM runs in quick update mode once a day.  Take a look at
     the IMQ batch file  or follow these steps to do a quick scan:

     o Choose a disk on which you have run an "IM initialize" at some
       point in time.  (This initialize need not be recent.) Use the
       CoMmands menu or the "/Dx" command line parameter to change to
       the drive you want to scan.

     o Use the Options menu or the "/Q" command line parameter to place
       IM in "quick update" mode.

     o Now run a check of this disk.  If you do this frequently, you can
       check even a very large disk very quickly.  The command: "IM /Q
       /N /DCD" would very quickly scan disks C and D as well as provide
       a report of any changes.

     SCANNING UPLOADS

     You can use IM to scan uploads to your BBS. The command

               IM /VR /ND /B

     will scan the current directory or

               IM /VR /ND /B /Pxxxx

     will scan the directory (and/or disk) specified by xxxxxx.

     If your upload processor provides a filespec like "*.*" or "*.COM",
     you do not need to feed it to IM on the command line.  However, if
     it does, you can include it as the first parameter. (e.g. "IM
     @FILES@ /B /VR /ND").

     IM returns an ERRORLEVEL of 64 or greater if it finds a virus.

     SCANNING .ZIP FILES FOR VIRUSES

     We provide some utilities that automate scanning of zip compressed
     files. File scanzip.zip contains these .bat files.  You can use the
     unzip.exe program that is on the IM distribution diskette to
     extract the contents of scanzip.zip.  Read or print file

   Integrity Master (tm)             - 30  -                 Version 3.02

     READMEZ.DOC for directions on how to scan a single .zip file or a
     complete disk of .zip files.  These utilities require the use of
     program PKunzip to decompress the .zip files. READMEZ.DOC also
     explains how to process other archive types such as ARJ.

     DETECTING VIRUSES

     o Make sure that you specified that you wanted virus protection
       when you installed IM.  If you didn't, then run SetupIM and
       select "Reinstall".

     o For maximum protection make sure that you carefully followed
       SetupIM's instructions in IMPROC.TXT (created only when you do a
       full install with SetupIM).

     o If a virus is found on your PC, IM will almost always recognize
       it by name and explain how to remove it.  IM will also advise if
       viral signs are present on changes that don't match known
       viruses.

     o Whenever IM reports a change to an executable program, it's
       important to discover the cause.  Some programs modify themselves
       when you change their options; some programs change themselves
       every time they run.  Changes to executable programs are
       indicated in red on the report screen and are bracketed by "...."
       to make these changes obvious.

     o If only a single program has changed and IM does not reveal this
       to be corruption, then you probably do NOT have a virus.  If you
       have any doubt that a program change may be a virus, be very
       careful and run full checks with IM after executing this program.
       (Cold boot (power off and on) from a floppy before running IM)
       Any program changes detected at this point indicate a virus.
       Please report this (see file VIRREP.DOC for complete details on
       reporting viruses.).

     o For speed, use the Options menu to limit checking to executable
       files.


     DETECTING UNKNOWN (NEW) VIRUSES

     IM has the capability to detect infection by an unknown (new) virus as
     well as the ability to identify known viruses and their characteristics.
     If IM detects an unknown virus, it clearly can't provide the detailed
     information that it provides when it detects a known virus.  Because of
     some of the generic detection techniques used in IM, there's a good
     chance that it will identify and describe a new virus.  How is this
     possible?  This is only possible if the virus is not totally new but a
     modification of an existing virus.  In this case, IM may identify the
     "new" virus as a virus it knows about because someone created the
     new virus by simply making some changes to an existing virus.  (Most
     "new" viruses are created in exactly this way.)  IM will usually notice
     the code from the old virus still present in the new virus and identify it
     in this way.

   Integrity Master (tm)             - 31  -                 Version 3.02

     What about totally new viruses?   These are a little more work to
     identify.  In this case, IM will inform you that it has detected a
     change in a file or a system sector, but won't announce that a
     virus is present, unless it's similar to a known virus.

     How do we decide whether a virus is responsible for the detected
     change?  Consider the following factors:

     o Has IM identified virus-like symptoms with this change?  Such
       symptoms include an unusual value in the DOS time or date stamp,
       and file corruption detected (no change to the time and date
       stamp but a change to the file).

     o Are numerous unrelated executable files changed?

     If the answer to one or both of these questions is "yes" then it's
     time to do some more checking to see if it's really a virus.
     Please read the section on Virus Signs and Playing Detective in
     Part Two - Data Integrity and Viruses.  Following these procedures
     will let you determine if you have encountered a brand new virus
     (lucky you!).  If you have encountered a virus, or you are not
     sure, please contact us; see file VIRREP.DOC for details on
     reporting viruses.


     THE INTEGRITY MASTER VIRUS REPORT

     When IM detects a known virus it will optionally present at least
     one full screen of information.   The virus report screen gives you
     the following information:

     o The name of the virus.  This is usually the CARO (Computer
       Antivirus Research Organization) name or the name used by the
       UK's Virus Bulletin, but in some cases we use an abbreviated or
       more common name.  This name corresponds to an entry in file
       VTEXT.DOC.  Many viruses have been built as modifications to
       existing viruses. By identifying common (hard to change) code
       elements in the base virus, IM can identify multiple viruses by
       spotting their common characteristics.  This means for example
       that if IM reports the Jerusalem virus, it could also be the
       Anarkia, Anarkia-B or the Payday virus. Since viruses go by many
       names, alternate names for the same virus are listed in this
       table too.

     o IM lists the type of files or system sectors infected by this
       virus.

     o If the virus is known to seriously interfere with normal
       operation of your PC, this is mentioned.  We don't classify
       messages, bouncing balls, or music as serious interference. We do
       consider slowing execution of your PC or halting the system as
       serious.

     o IM will mention if the virus is known to either deliberately or
       inadvertently damage data on your disk.  Beware though, some idiot


   Integrity Master (tm)             - 32  -                 Version 3.02

       could, at any point in time, modify a previously harmless virus
       to do something destructive.  An example of this is the Cascade
       virus (letters cascade down on your screen when this virus
       activates). The first version of this virus was harmless, but
       someone created a variant that will format your disk.  In this
       case, IM makes a special check for the dangerous variant of the
       virus and warns you if it's detected.  In spite of this, please,
       NEVER assume that a virus is harmless.  If we don't mention that
       a virus is known to damage files, it means only that no one has
       reported damage from this virus. Be careful; you may have a
       variant of the virus that might very well be dangerous!

     o IM presents step-by-step removal instructions for the virus as well
       as the option of automatic removal.

     Sometimes IM presents additional screens describing necessary or
     suggested actions.  This is true if the virus is detected in
     memory. When IM first starts, it checks the memory of the PC for
     the presence of known viruses (unless you deactivate this check
     using SetupIM or the "/B" (bypass) command line parameter); if IM
     detects a virus, it will ask you to immediately cold boot your PC.
     Checking further at this point could be very dangerous since it
     might spread the virus.  If IM detects a special virus such as a
     companion or cluster virus, (see PART TWO for details) it will
     display an extra screen identifying that virus along with more
     detailed information about the virus.


     FALSE ALARMS

     If IM announces detection of a known virus, could this be a false
     alarm (not really a virus)?  If IM has checked this file before or
     if it has found more than one file infected, then you very likely
     have a REAL VIRUS!  If this is the first time that IM checked this
     file, and if it found only one file infected after checking your
     entire disk, then it's probably a false alarm (unless this file is
     COMMAND.COM or one of the programs provided with DOS).  There is
     always some risk that a legitimate program might contain code that
     matches a virus.

           IF YOU THINK YOU HAVE A FALSE ALARM, PLEASE
           NOTIFY STILLER RESEARCH.   WE WILL DETERMINE IF
           A VIRUS IS PRESENT; IF IT IS A FALSE ALARM, WE WILL,
           IF POSSIBLE, SEND A CORRECTED VERSION OF IM.

     Some anti-virus programs contain unencrypted virus fragments that
     IM may detect.  It's usually safe to assume these programs are not
     infected.  Some of these programs also leave virus fragments in
     memory that IM may then detect and announce as a memory resident
     virus.  Please do not take any chances in such a case and follow
     IM's instructions to cold boot, even though it's likely to be a
     false alarm.



   Integrity Master (tm)             - 33  -                 Version 3.02

     If you have just read an infected disk or a file, there is a chance
     that IM may detect a piece of this file in memory and announce a
     resident virus when one really isn't resident.  In such cases, it's
     best to play it safe and cold boot from a write-protected diskette.


     DESTROYING VIRUSES

     If IM detects a known virus, it will display the steps to remove
     the virus and offer to remove it automatically.

     If IM detects program or system sector changes that may be due  to
     a virus, please follow these steps:

     o Save at least one infected diskette or file and report this to
       us. This will allow us to update IM to recognize this virus and
       hopefully track down the source of the virus!  See file
       VIRREP.DOC for complete details.

     o Cold boot your PC (power off and on) from a write-protected
       floppy disk.

     o Run an "Entire disk integrity" check, noting any changed programs
       or other possible damage by the virus.

     o You can allow IM to remove the virus or follow its directions to
       remove the virus manually.  Restore infected files from the
       original program diskettes if possible.

     o Reload your system sectors if they were damaged.

     o Restore any damaged files or programs from the original diskettes
       if possible.

     o Very carefully check any floppies you've used.  If you have
       encountered a system sector virus, use the /VB command line option
       to quickly scan your floppies.

     o Run an "Entire disk integrity" check daily for a while.


     DATA CORRUPTION

     If a program changes a file by normal means, the file's time and
     date stamp will be updated to reflect this change.  On the other
     hand, if a virus or a hardware or software problem causes a file to
     be changed, there is often no change to the file's time and date
     stamps. IM calls this file corruption and raises a special alarm if
     it detects this.  If you find a corrupted file, the odds are it's
     NOT a virus.  The most likely cause of corrupted files is software
     conflicts.  The next most common cause is hardware problems.  In
     any case, if you have a corrupted file, it's essential you find
     what the cause is.  In Part Two - Data Integrity and Viruses", I
     have a chapter titled Determining the Cause of Data Corruption.


   Integrity Master (tm)             - 34  -                 Version 3.02

     Please read that chapter very carefully when you detect a corrupted
     file. The next section describes using IM when you are having
     suspected disk hardware problems.

     INTEGRITY MASTER AND DISK PROBLEMS

     It's an unfortunate fact of life that all disk drives will
     eventually fail; sometimes at the worst possible moment!  Before
     disk drives totally fail, they usually start exhibiting signs of
     problems, such as inability to reliably read and write certain
     areas on the disk. Unfortunately, these failures tend to be
     intermittent. The result may be that you have damaged files, but
     when you run your disk diagnostic software, no problems are found.
     By using IM to do periodic full checks, you can detect these
     problems when they first begin and prevent more major disk
     problems, such as total failure, from taking you by surprise.  If
     you have an MFM, RLL, or ESDI type of disk drive you probably can
     extend its life slightly by doing a low level format, or using a
     product such as Steve Gibson's SpinRite(R) that can do a
     nondestructive low level format.  The key here is to detect disk
     problems early before any serious damage is done.

     IM replaces the DOS critical error handler with its own more
     advanced routine.  If a disk error occurs, you will see a warning
     screen explaining what has happened, rather than the dreaded
     "Abort, retry, or fail" message that DOS provides.  IM may also
     present a menu offering you additional options (depending upon the
     type of error and the circumstances) such as repeating (retrying)
     the operation.

     If an error occurs while IM is checking files, it will report
     either "Read fail" or "Open fail" in place of the normal signature
     data on its report:

                      Name and    Signature     File     Update   Update
    Status: Type:     Extension:  Val1: Val2:   Size:    Date:    Time:
    ------- --------  ----------   ---- ---- ---------- -------- --------
    Added   File      NORMAL   EXE 0D83 4E93       2048 11/05/93 14:00:56
    Added   File      DISKERR  EXE Read fail     140792 11/05/93 14:01:02
    Added   File      CANTOPN  FIL Open fail        123 10/05/93 10:11:20


     In addition to "Read fail" or "Open fail" appearing in the IM
     report, additional information regarding the type of error will
     also appear and be recorded in the report file (or printout) as
     well as in the on-screen report.

     Whenever IM encounters an error reading a file, it will NOT replace
     the original integrity data with the current (in error) data. This
     means that if you have a read error on a file, and you either "fix"
     the file using some utility or restore the file from a backup, you
     can then run a check on that file and know whether or not your file
     was correctly restored.


   Integrity Master (tm)             - 35  -                 Version 3.02

     If you run IM in an environment where more than one program can
     have a file open, you may get an "Open fail" or "IO error" due to
     another program having this file open.  This can happen on networks
     (LANs), with OS/2, or with Windows. When this error occurs, you
     will see a detailed explanation along with a menu offering several
     options.  We recommend you select the option to ignore any further
     open errors; this way you will still see detailed information on
     any other problems discovered by IM.  You can avoid this error
     display and most others by using the "/NE" command line parameter
     (pause on emergencies only).


   Integrity Master (tm)             - 36  -                 Version 3.02


     INTEGRITY MASTER FOR PC SECURITY

     Although there are no 100 percent reliable techniques to prevent
     someone from making unauthorized changes to your data while you are
     away, IM does offer a reliable way of detecting these changes.

     If you specified that security was important when you first
     executed SetupIM, its Integrity Advisor will make recommendations
     on how to use IM to get the level of protection you need.  It saves
     these recommendations in file IMPROC.TXT.  By storing your
     integrity data on diskettes and keeping these diskettes in a safe
     location, you can detect any changes that occur on your PC.  This
     should provide you protection even against a user who understands
     how IM works and is technically adept.  For most situations this is
     probably overkill! (Using variably named integrity data files and
     using your own name and location for your IM.PRM file will stop all
     but the most determined intruder.)

     Keeping the integrity data on diskette may provide more protection
     than you need.  Simply keeping your parameter file (IM.PRM) on a
     diskette will provide a very high level of protection.  Since a
     user breaking into your PC will not be able to tell how the
     integrity data is computed, this user will not be able to change a
     file and then adjust the integrity data to hide the changes, even
     if they have a copy of the IM program.  This provides almost as
     much protection as keeping the integrity data on diskettes.

     You can ask SetupIM to make the names of your integrity data files
     variable (each file will have a different name) so that it is even
     more difficult for someone to attack your integrity data.

     If you keep the parameter file on the same disk with the files, you
     check, it's possible that someone could modify your files and then
     run IM to update the integrity data, in this way covering their
     tracks. This person would obviously have to have enough knowledge
     about your PC to know that you use IM.  If you'd like to keep your
     parameter file on the diskette with your files, you can still
     achieve a high degree of security by renaming IM.PRM and locating
     it in an unlikely directory.  When you invoke IM you will have to
     specify the name of the directory and the new name for the
     parameter file.  For example, the command: "IM
     D:\DOS\UTILS\BORING.DAT" will read the IM parameter information
     from file BORING.DAT in directory \DOS\UTILS on disk D.

   Integrity Master (tm)             - 37  -                 Version 3.02

     INTEGRITY MASTER FOR CHANGE CONTROL

     To use IM for change management, you really don't need to use integrity checking.  Simply running IM, in "Quick Update" mode, (which
     does not actually read files unless the DOS time/date stamp or file size
     have changed), is adequate to provide change management.  "Quick
     update" mode only requires about 10 to 20 seconds to check about
     1,000 megabytes (9000 files).  To keep a full record of what has
     changed on your PC, I recommend you use "auto-named" report files
     and that you keep all your report files.  At the end of the year, you
     may wish to copy all the old report files into a directory for that year.
     For example, on January 1, 1996:

     CD \IM_Home (or "CD \" if not using "home directories")
     MD REP96
     COPY *.REP \REP96
     DEL *.REP

     This creates a directory called "\REP96", copies all report files to that
     directory, and then deletes the old report files.

     By following this procedure you have a complete record of all
     changes on your PC.  If you want to know when a particular file
     last changed, it's easy to search through the report files for that
     filename.  If you want to know where all your disk space is going,
     you can go back and see which files were added or which files grew.

     INTEGRITY MASTER FOR LAPTOP CONFIGURATION

     If your organization lends laptop PCs to its employees or customers
     then you should consider using Integrity Master to assure that the
     laptops are correctly configured and ready for the next person to
     use. If you use IM to check the integrity of the laptop when it is
     returned you can make sure that no files are missing and any
     changed files are restored to their original form.  This way you
     know not only that the laptops are free of viruses but that all the
     installed software is ready to go the next time someone needs to
     use the laptop.  (For absolute security you can use SetupIM to
     configure IM to record the integrity data on floppy; this way there
     is no risk of the laptop user deleting the integrity data files on
     the hard disk.)


   Integrity Master (tm)             - 38  -                 Version 3.02

Command Line Execution

     Integrity Master is really designed to work by use of its menus.
     However, most functions can be automatically invoked from the
     command line to allow you to start IM from batch files.

  Syntax:
  IM Fspec /A /B /C /Cx /Dxyz /F /H /Ix /L /M /Nx /NOB /Ppath /Q /Rx /REPA
           /RF=filespec /Vx /1
  ================================================================================================
  FSpec specifies the name of the parameter file to be used.  It's best
  to specify the disk and directory path as part of the filespec. For
  example: use "IM C:\dos\NEW.PRM" rather than "IM NEW.PRM".  If you
  don't use this option, IM will search for file "IM.PRM", looking first
  in the current directory, then in the directory with the IM program
  (IM.EXE), and finally in the root directories of all available disks.
  ----------------------------------------------------------------------------------------------      "/Dxyz"  Change to disk "x", process and then change to disk "y", etc.
         If used with more than one disk, this should be used with one of the
         "/Cx" "/Ix" or "/Vx" parameters. You may also use the /Dx:y:z:" form.

    "/Ppath"  Change to directory (and optionally disk).  If you specify
          a disk here, you can't also use the "/Dxyz" parameter.  (e.g.
          "/P\dos" or "/Pc:\dos")

    "/1"   Only "1 line" virus reports. Turns off the detailed virus
           descriptions.

    "/B"   Bypass memory check.

    "/F"   Forces full integrity checking if quick update is set as the default.

    "/H"   (or /?) produces this help display.

    "/NOB" No Beep.  Disables sound.

    "/NA"  No Abort - disables the ESCape and ALT/X keys during checking

    "/N"   Nonstop: the same as setting "Halt" to "Serious problems"  on the
           Options menu.  IM will stop only on viruses or serious problems.

    "/NE"  Stop on Emergencies only.  This almost never stops.

    "/ND"  Stop on Emergencies only with no screen display (unattended exec)

    "/Q"   Forces IM to run in "Quick update" mode.

    "/REPA" Report all.  When scanning, IM lists all files scanned for viruses.
            When initializing, IM lists all files processed on the report file.

    "/MS#"  You can use the command line /MS# option (or SetupIM) to
            vary the sensitivity of IM to resident program configuration
            changes.  The sensitivity can be set from 0 to 9. 0 turns
            the check off, and 9 provides maximum sensitivity to
            changes.  /MS4 is the default (and recommended) setting. /MS9 is
            useful for for researchers and on systems where there should
            be no software changes at all.

    "/RF=filespec"  Writes the report to "filespec" (can include disk + path).
             (The form /RF:filespec is also valid)

    "/MF=XXXX.SRL"  Specifies the file used by check "Resident programs
                    and memory" command.


   Integrity Master (tm)             - 38  -                 Version 3.02
  -------------------------------------------------------------------------------
  /Cx values: do type "x" integrity check and then quit:

    "/CE"  Check Entire disk integrity.      "/CB"  Check Boot sector.
    "/CD"  Check all files on DOS disk.      "/CP"  Check Partition sector.
    "/CR"  Check files in this diRectory.    "/CF=filespec" Check this one File.
    "/CL"  Check this + Lower directories     (The form /CF:filespec is also valid
    "/CC"  Check CMOS memory
    "/CM"  Check resident programs and memory

  -------------------------------------------------------------------------------
  /Ix values: do type "x" initialize of integrity data and then quit:

    "/IE"  Init Entire disk integrity        "/IB"  Init Boot sector
    "/ID"  Init all files on DOS Disk        "/IP"  Init Partition sector
    "/IR"  Init files in this diRectory      "/IC"  Init CMOS
    "/IL"  Init files in the current directory and all lower directories

  ------------------------------------------------------------------------------
  /Vx options scan system sectors and files for signs of known viruses:

    "/VA"  Scan ALL files on a disk (not just executables).
    "/VB"  Scan only floppy disk boot sectors.  This allows rapid
           screening of floppies for boot sector viruses and access to
           (otherwise ureadable) floppies crash DOS.
    "/VM"  Virus scans of multiple diskettes - only 1 key-press needed per disk.
    "/VO"  one-time virus scan of programs on current disk.
    "/VR"  scan of programs in current directory.
    "/VL"  scan of programs in current and lower directories.
  ------------------------------------------------------------------------------
  /Rx values will rewrite or reload one of the system sectors:

    "/RP"  Reload Partition sector           "/RB"  Reload DOS Boot sector
    "/RE"  Rewrite partition Executable code "/RF"  Rewrite Floppy boot sector

  ------------------------------------------------------------------------------
  The following /Ux options control when IM updates its integrity data files:

    "/UN"  Undate integrity data NEVER.  When you run a check IM will not
           update your integrity data files (even for added or deleted files).

    "/UO"  Update off. IM will not update integrity data for changed files.

    "/UP"  IM will not update integrity data for changed programs.

    "/UA"  Update activate - update integrity data (default).

  ------------------------------------------------------------------------------
  The following may be used to override video mode selected during install:

    "/A"   Auto adjust of video mode.        "/L"   Use colors for older LCDs
    "/C"   Force use of full color mode.     "/M"   Use monochrome colors.

     Ordinarily,  you don't need ANY parameters. Just enter: "IM". IM  is
     menu driven with lots of on-line help.  The command line parameters
     are most often used for automatic unattended integrity checking.  If
     you don't have "HALT" set to "Serious problems" or "Emergencies
     only" (on the Options menu), use "/N" (or "/NE") to avoid pausing
     for input.  If you wish to have IM automatically locate your parameter
     file, DO NOT specify it on the command line.  If you specify it on the
     command line and it is not located in the current directory, then you
     must include the drive and directory of the parameter file along with
     the name.

     Examples:

      "IM /L /CE /DEF"  Uses colors appropriate for an older (CGA type)
     LCD display and checks the system sectors as well as all files on
     disk E and then changes to disk F and repeats the check there.

     "IM /IR"  Creates new integrity data for files in this diRectory.

     "IM /CF=A:\X\IO.SYS"  Checks the file IO.SYS in directory \X on
     disk A:.

     "IM D:\IO\X.PRM /CD"  Checks all files in the current disk using
     options saved in the parameter file "X.PRM" located in "D:\IO".

      "IM /RF /DA"  Writes a self-checking boot sector onto disk A:.

     We've provided some sample batch files that illustrate ways to
     automatically execute IM.  See the descriptions listed under
     "Scanning for Viruses" earlier.  Here are the steps to execute IM
     automatically in unattended (batch) mode:

     o Use the Options menu to activate the report file.  Save this
       change by selecting the first option on the Options menu, "Write
       option changes to disk." (Or use the "/RF=" command line
       parameter.)

     o Either set the halt options to "Serious problems" (on the Options
       menu) or use the "/N", "/ND" or "/NE" command line parameters.
       (e.g., "IM /ND").

   Integrity Master (tm)             - 40  -                 Version 3.02

     o Prepare the IM command line to do the type of checking that you
       want.  For example: "IM /N /DFG /CE" will run nonstop on disk G
       and check the entire disk (/CE), including system sectors.

     o You may wish to add IM to any batch file that you run regularly,
       such as a nightly backup batch file.  You can use RunMaybe with
       IM to give you control over how often IM runs.

     ERROR LEVELS

     Integrity Master returns the following DOS error levels.  You can
     check for these error levels in a batch file and execute your own
     special procedures depending upon IM's findings.  One of our beta
     testers has their PCs automatically phone their help desk if an
     error level 24 or greater is encountered.

     00   Processing complete with no changes detected
     08   Checking complete with added or deleted files detected
     12   Checking complete with changed files detected
     16   Checking complete with changed programs detected
     24   Checking complete with suspicious file changes detected
     32   Checking complete but a file or system sector showed signs of
          corruption or an I/O error.  This will be in addition to any of the
          lower valued indicators such as change to a program.  So if a
          program changed, the error level would be 16 + 32 = 48.
     64   One or more viruses were detected. Any of the lower status
          indicators will be included with this one.
     128  If a vital IM file is determined to be missing or damaged
     192  A fatal error occurred during execution, such as not enough
          memory or a disk error in internal processing.
     200  Command line error (an error in IM's "/" parameters).


     USING IMCHECK

     IMCHECK.EXE is a fast stand-alone file checker.  It will read
     whatever files you specify and compute signature data similar to
     what Integrity Master uses as part of its integrity data.

     If you print the IMPROC.TXT file created by SetupIM, you will see
     the check values that IMcheck should report for IM.EXE and IMcheck
     itself.

   Integrity Master (tm)             - 41  -                 Version 3.02

     The syntax is: IMCHECK [d:] [path] filename [/D] [/1] [/2]
     "filename" specifies the files to check.  Wild card characters
     such as * or ? may be used.
        "/D"    Display directory entries as well as files.
        "/1"    Utilize an alternate algorithm for check value one.
        "/2"    Utilize an alternate algorithm for check value two.

     Entering IMCHECK with no parameters will display an explanation of
     how to use IMcheck.

     For example: IMCHECK D:\DOS\TEST.* would check all files in
     the DOS directory on disk D: whose names begin with "TEST". (e.g.,
     TEST.COM, TEST.ABC, etc.)

     IMcheck can be very handy when you send files to others and you
     want to make sure that they got a good copy of your files.  Simply
     run IMCHECK on your files.  You will see a report like:

     IMCHECK 1.2 - Integrity Master (TM) standalone file checker.
     Copyright 1990-1991 by Wolfgang Stiller - all rights reserved.
     Checking: MYFILE.*

     File Name + Check Check    File    Update   Update
     Extension:  Val1: Val2:    Size:   Date:    Time:
     ----------   ---- ----    -------  ------   ------
     MYFILE.001   AC57 C1C4       1551 11/05/93 22:38:40
     MYFILE.DAT   2D53 B1D6       8666 11/07/93 18:57:30
     Total======> F5AA 66A7

     Record the check values and make sure the other person runs IMcheck
     to compare the check values.  The "Total=====>" values will match
     only if the files are checked in the same order.


     SPECIAL LICENSE TERMS FOR IMCHECK:

     Registered users of Integrity Master are granted permission to
     distribute copies of IMcheck to anyone who needs to verify the
     integrity of files sent by the registered user.  This other user
     may use and keep IMcheck but may not further distribute it.

     ONLY registered (licensed) IM users may distribute IMcheck.

     ADD-ON PROGRAMS

     Regisetered user receive some supplementary programs to augment the
     function of Integrity Master:

     RunMaybe  Allows you to execute IM (or any other program) on
               specific days or at specific intervals.  This enables you
               to do an automatic daily, weekly or monthly check of your
               PC.

     ASQ       ASQ analyzes and reports your PC configuration.  It
               provides both a tutorial on your PC's hardware and
               configuration as well as an excellent configuration
               analysis.  (Since ASQ is being provided to Integrity
               Master customers courtesy of Qualitas (the makers of
               386MAX(tm), it may be withdrawn or replaced without
               notice.)  To use ASQ, just type "ASQ" and hit ENTER.

   Integrity Master (tm)             - 42  -                 Version 3.02

     RunMaybe - Version 1.1

     Unlike ASQ, RunMaybe may not be shared with others.  RunMaybe
     is licensed software available only to Stiller Research customers.

     WHAT IS RUNMAYBE?

     RunMaybe is a small, fast (100% assembly language) program that
     gives you a way to execute a program, DOS command, or batch file
     on specific days.  By keeping track of when you last executed your
     program, RunMaybe makes sure that the program is executed when
     you want and also no more frequently than you desire.

     o You can choose specific days of the week, days of the month, or
       an elapsed number of days to determine whether the desired
       program will be executed.

     o RunMaybe will (if you wish) run a program at the next
       opportunity if it was not run on a designated day (with the /N
       parameter).

     HOW DO YOU USE RUNMAYBE?

     1) Decide how often (or on what days) you want to execute your
        program and formulate an appropriate RunMaybe command.  For
        example, to execute CHKDSK once a day, you would use the
        command: "RunMaybe /E CHKDSK".

     2) You place the RunMaybe command in a batch file that you execute
        at intervals, such as your AUTOEXEC.BAT file (which is executed
        every time you boot your PC).

     HOW TO INSTALL RUNMAYBE

     o  Copy RUNMAYBE.EXE to any directory on your DOS path. (Type
        "PATH" and hit ENTER to see what directories are on your path)

        or

     o  Copy the RUNMAYBE.EXE program to any convenient directory
        on your disk. If it is not in a directory on the DOS path, you will
        need to include the full path of the program to execute it. (e.g, if
        RUNMAYBE.EXE is located in D:\UTILS\IM, then your batch file
        command line would look like: "D:\UTILS\IM\RunMaybe /E
        CHKDSK" )

     How to execute multiple programs at multiple (varying) intervals:

     o If you merely want to execute several programs together at a single
       interval, simply place them all in a batch file and then execute that

   Integrity Master (tm)             - 43  -                 Version 3.02

       batch file from RunMaybe.  This can even be done in the middle of
       another batch file. (There's no need to use CALL to accomplish
       this).

     o If you want to run programs at different intervals, then RunMaybe
       will have to keep track of "last run" information for each program
       separately.  The best way to do this is to use a different "last run"
       file for each program you want to schedule.

       Let's assume you want to run program "PROG1" every second day
       and that you want to run "PROG2" on Mondays, Wednesdays, and
       Fridays. You could use the following commands:

                    "RunMaybe C:\Data\PROG1.LR /E2 PROG1"

                    "RunMaybe C:\Data\PROG2.LR /W1,3,5 PROG2"

      In each case, the first parameter ("C:\data\PROG1") specifies the
      name and directory of the file where RunMaybe will record the
      "last run" information.

      The path "C:\DATA\" can be any disk and directory you choose and
      the file names "PROG1.LR" and "PROG2.LR" can be any file names you
      choose. When RunMaybe executes for the first time, it will create
      those files.

     COMPLETE SYNTAX FOR THE RUNMAYBE COMMAND LINE:

     RunMaybe [LastRun Filespec] /E# /H /M##,##,##,.. /N /W#,#,#,... ProgName

     "LastRun FileSpec" - This is optional.  (You only need this if you
          want multiple programs to run according to different
          schedules.)  "FileSpec" specifies the name and location of the
          file where RunMaybe stores the last time and date that it was
          executed.  Be sure to specify the complete path (disk and
          directory) so RunMaybe can find this file.  If you don't
          specify this parameter, RunMaybe will create a last run file
          called "RUNMAYBE.LR" in the same directory with the
          RUNMAYBE.EXE program.  RunMaybe will search for "RUNMAYBE.LR"
          by looking first in the current directory and then in the
          directory in which the RUNMAYBE.EXE program is located.

          Use this option if you want to use RunMaybe to run different programs at different
          intervals.  You will use a different "LastRun" file to keep track of each program.

     /H or /? produce a help display

     /N   Specifies that the program should run on the next possible
          opportunity if it did not run on the designated day. This
          applies only to the /M and /W parameters.  For example, if you
          specified that a program should run very Monday but you take a
          holiday on a particular Monday, the program will be run
          whenever you return if you include the /N parameter.

     /E#   Run the program every # days. # must be from 1 to 99 days. If
          you don't specify a "#" (number of days), then it will default
          to "1" and the program will be run daily. (For example,
          "RunMaybe /E2 IM" will run IM every second day.)

     /M##,##,##... RunMaybe will run the program only on those specific
          days of any month.  You can specify a single day or a a list
          of up to 30 days. These days MUST be listed in ascending
          order. (e.g., "RunMaybe /M10,20,30 CHKDSK" will run CHKDSK on
          the 10th, 20th and 30th of any month.)

     /W#,#,#... RunMaybe will run the program only on those specific days of the week. These days
          MUST be listed in ascending order.  You can specify a single
          day of the week or a list of up to 6 days.  You specify a
          number for each day of the week:

          0 = Sunday  1 = Monday  2 = Tuesday  3=Wednesday  4 = Thursday  5 = Friday  6 = Saturday


   Integrity Master (tm)             - 44  -                 Version 3.02

          For example, " RunMaybe /M1,3,5 IM" will run IM on Monday, Wednesday and Friday.

     "ProgName" specifies the name of the DOS command, program or batch
          file you want to execute.

          You can include any parameters that the program, command or batch file needs.  You
          can safely use this command to execute batch files from within other batch files.

     DOS ERROR LEVELS

     RunMaybe returns the following DOS error levels for use in your
     batch files:

      0   Everything went well and your program was executed.  (Note,
          that RunMaybe can not actually determine if your program
          executed correctly; it simply knows that DOS reported no
          errors.)

      1   There was no need to run a program at this particular time.

      64  The system date on the PC is suspect.  The current date is
          earlier than the date that RunMaybe was last executed.

     128  A bad or unreadable last run file.  (RunMaybe aborted)

     200  A problem on the RunMaybe Command line.  (An invalid or
          missing parameter.)

     HERE ARE SOME RUNMAYBE EXAMPLES:

               RunMaybe /E IM /B /VO /DEF /N

     The above command, if placed in your AUTOEXEC.BAT file, would
     execute IM daily (/E) (but only once a day even if you boot
     multiple times). The program IM will be executed with options set
     to bypass the memory check (/B), scan the entire disk for viruses
     (/VO) and only pause on serious problems (/N).  Disks E and F will
     be checked (/DEF).  Note that the only RunMaybe parameter used in
     this example is "/E".

               RunMaybe /W1 /N IM

     This command, if placed in your AUTOEXEC.BAT file, would execute IM
     once a week on Monday.  Since the "/N" parameter was included it
     will run IM on the next chance it gets, if you don't boot your PC
     on Monday.

               RunMaybe /W1,2,3,4,5 IMBAT \DOS\NewUpl

     Here IMBAT.BAT is a batch file with these contents:

     @ECHO OFF
     IM /B /VR /DE /P%1 /ND
     IF NOT ERRORLEVEL 64 GOTO OK
     ECHO A virus was detected - please delete infected
     PAUSE
     :OK

     This will, only on weekdays (days 1 to 5 which represent Monday to
     Friday), scan the upload directory, "\DOS\NewUpl", for known

   Integrity Master (tm)             - 45  -                 Version 3.02

     viruses and display a message to delete the bad files if any are
     found. "\DOS\NewUpl" is a parameter which is passed to the IMBAT
     batch file and substituted in the IM command line (in place of  %1)
     to produce:


         IM /B /VR /DE /P\DOS\NewUpl /ND

     IM will bypass memory checking, change to disk E, change to
     directory \DOS\NewUpl\ and check it for known viruses.  The next
     line of the IMBAT batch file then checks the DOS Errorlevel. If it
     is 64 or less no virus was found.

     OTHER OPERATING SYSTEMS

     Although Integrity Master is designed to run in the DOS environment
     on Intel 80x86 family microprocessors, it is useful with other
     operating systems and processors such as OS/2, Unix, Microsoft
     Windows (this includes Win 95 and NT) and various Network (LAN)
     operating systems such as Netware and VINES.  You can even use it
     on a Macintosh with DOS emulation.  On some of these non-DOS
     systems you can't check the system sectors in the same way as under
     DOS since the underlying operating system support is different.
     Since these operating systems are multitasking, Integrity Master
     may find that it can't read certain files that are in use by the
     operating system.  This is normal and will not interfere with a
     full system check.  There's more information on this in the section
     on Integrity Master and Disk Problems.

     While it may be most convenient to do most of your checking under
     your normal operating system, I strongly suggest that you prepare a
     DOS boot check and occasionally check under native DOS.  This is
     currently the only way to give your system the most secure checking
     possible.


     MICROSOFT WINDOWS AND OS/2

     Integrity Master will run quite happily under Windows or OS/2 as a
     DOS application.  You can even run IM in the background while you
     use a different application. However, this will probably prevent it
     from checking whatever files you are currently using.

     If you are using a non-DOS file system such as the "High
     Performance File System" (HPFS) under OS/2, Integrity Master will
     be able to check only those files that DOS can access.  For OS/2
     HPFS this means that files with more than eight characters in the
     file name or more than three characters in the extension cannot be
     checked.  For example, IM could check file 12345678.ABC but not
     file 123456789.ABC.D under HPFS.


   Integrity Master (tm)             - 46  -                 Version 3.02

     When you run IM under Windows or OS/2, it may report "General
     failure" reading some files.  This is normally a hardware error but
     in this case it simply means that Microsoft Windows has certain
     files open. This prevents IM from reading these files but is no
     cause for concern.  The message returned to IM varies from one PC
     to another. On some PCs, you may see merely that certain files
     cannot be opened. When this error occurs, you will see a detailed
     explanation along with a menu offering several options.  We
     recommend you select the option to ignore any further open errors;
     this way you will still see detailed information on any other
     problems discovered by IM.  You can avoid this error display and
     most others by using the "/NE" command line parameter (pause on
     emergencies only).


     NETWORKS

     If you have a local area network (LAN), you can use Integrity
     Master on both the file server and the workstations. (Each
     workstation requires a separate license for IM; we offer very
     reasonable site license pricing.) IM can be used on a network by
     running it on the separate workstations as well as on the server.
     It can be configured in different ways.  If you place IM.EXE on a
     shared disk available to all workstations, you can have separate
     parameter (IM.PRM) files for each workstation or you could have a
     central IM.PRM in the directory with the shared IM.EXE.  Using a
     common IM.PRM file makes it easier to copy or move files and then
     immediately check to make sure the files are intact.  If the server
     does not run or emulate DOS, then you will need to check the files
     on the server from one of the DOS workstations.  PART TWO contains
     a section titled Networks and Viruses that provides some general
     procedures to make sure you keep your LAN free of viruses. It's
     particularly important that you follow the guidelines there on
     access rights and supervisor privileges. If you periodically boot
     each workstation from a write-protected floppy and do a full check
     of that PC, you can be assured of maximum protection for your LAN.

     Using IM on a Network
     The following suggestions come from users of Integrity Master on a 
     variety of different local area networks.  The details vary slightly 
     from network to network but the following procedure should allow 
     you to get benefit with minimum work.

       The benefits of this procedure are:

     1) You can run SetupIM only once to get IM installed for most
        users, yet anyone who has special needs can configure IM to work
        exactly the way they want by running SetupIM on their
        workstation.

     2) Since there's only one copy of IM.EXE and SetupIM.EXE, you can
        quickly update everyone's software by doing a single copy
        operation.


   Integrity Master (tm)             - 47  -                 Version 3.02
     3) Any files that are transferred from workstation to workstation
        can easily have their integrity verified since all workstations
        share a common integrity data encryption format.

     4) Each workstation will automatically maintain a complete change
        history in the form of the report files on that workstation.
        This facilitates centralized problem solving; if anything stops
        working on that workstation, the report files provide a complete
        change log to track down exactly what was changed, added, or
        deleted.

     SUGGESTED INSTALLATION:

     1)  Copy IM*.* and SetupIM.EXE to a directory on a server which is
         included in the DOS path of all workstations on the LAN.  It's
         best if LAN access rights do not allow the workstations to
         write to this directory.

       An alternate technique is to place a .BAT file to invoke IM on
       each workstation.  This allows IM.EXE to still be stored in a
       central location on the network. The batch file would look
       something like this:

         Q:\shared\antivir\IM /Dxyz /Q /CE %1 %2 %3

        In this case, IM.EXE and IM.PRM would be stored on the server's
        "Q:\shared\antivir" disk.  Disks x, y, and z would be the disks
        that need to be checked for this workstation. "%1 %2 %3" allows
        the workstation user to specify some additional IM command line
        parameters.

     2) Run SetupIM (new install) on a workstation that has the most
        common configuration on the LAN.  What matters here is the
        organization of the disks on the workstation.  By this I mean
        the physical partitioning of the hard drives.  If the first disk
        is usually partitioned as two logical drives, choose a PC with
        that arrangement.  An arrangement that is a superset of another
        is the best choice.  In other words, if your most common
        configuration is to have two floppy drives with the first hard
        drive partitioned as two logical drives, choose such a PC.  But
        if some of these PCs also have additional hard drives, that's
        even better. Choose one of the PCs with the extra hard drives to
        run SetupIM.

     3) Move the IM.PRM file created in step 2 to the shared directory
        where the IM.EXE file is located.  This allows all PCs that have
        a compatible configuration to execute IM and allows you to
        quickly upgrade to new versions of IM by simply copying the new
        IM.EXE file over the old one.


   Integrity Master (tm)             - 48  -                 Version 3.02

     4) If you have workstations with incompatible configurations or
        users with special needs, you can run SetupIM separately on
        those workstations (but do not place a copy of SetupIM on the
        workstation; simply execute the copy on the server).  This will
        create an IM.PRM file local to the workstation.  The user of
        that workstation will still execute the shared copy of IM.EXE
        but IM will behave according to the configuration and options
        information stored in the local copy of IM.PRM rather than the
        shared copy.  It's useful to install a batch file in a directory
        on the DOS path of the workstation to make sure that the local
        copy of IM.PRM is always used. The batch file contains this
        line:

          IM C:\LOCAL\IM.PRM %1 %2 %3 %4 %4 %5 %6

         ("C:\LOCAL\IM.PRM" could be any disk, directory or file name.)

        This procedure allows a single setup for most users, but still
        allows the flexibility to enable anyone to configure IM exactly
        the way they want.

     5) Run an Initialize "Entire disk integrity" ("IM /IE") on each
        workstation.  This will scan the entire PC for known viruses and
        also provide full integrity checking of all files.  Next ask IM
        to initialize the "CMOS memory".  (If you wish to do only
        conventional virus scanning, you can skip this step.)

     SUGGESTED USAGE:

     1) Configure each workstation so that it runs a daily check in
        "quick update" mode.  The IMQ.BAT and IMONCE.BAT files contain
        some statements that can be inserted into the AUTOEXEC.BAT file
        or elsewhere to make sure this happens. (IMAUTO will do this for
        you.)  Some people prefer to just let the user of each
        workstation run a quick update once a day (or other appropriate
        interval). IM comes with RunMaybe, a program that allows you to
        execute IM (or any other program) at any interval you choose.
        The quick update (quick scan) will catch viruses as effectively
        as conventional virus scanning but is much, much, faster and
        optionally provides a complete change log for the workstation.
        If you wish to do only conventional virus scanning, you can
        substitute a virus scan for this step ("IM /VO").

     2) Each workstation user should use IM to scan or check all new
        diskettes and especially all new software.  The batch files,
        IMSCAN, IMSCANM, and IMSCAND, will scan disks, multiple
        diskettes, or single directories respectively.

     3) A full integrity check should be run at intervals on each
        workstation.  This will make sure that the disk is thoroughly
        checked and will detect more subtle hardware or software
        problems as well as unknown viruses.  Once a week seems to be
        the most popular interval to run a full check.

   Integrity Master (tm)             - 49  -                 Version 3.02

     CHAPTER FOUR - CUSTOMIZING
     ____________________________________________________________________


     CUSTOMIZING INTEGRITY MASTER

     When you first install Integrity Master, SetupIM does an initial
     customization for you based upon your needs and preferences.
     Integrity Master offers you a myriad of different options so that
     you can set it up to work just the way you want.

     From the Integrity Master Options menu, you can control almost all
     options that regulate how IM functions.  Your option changes may be
     either temporary or permanent.  To make your changes permanent,
     select "Write option changes to disk" from the Options menu.  This
     will save your new option settings in the parameter file. These
     options will be in effect the next time you execute IM.

     In addition to initially installing IM, SetupIM allows you to
     change the less frequently used options.  The more advanced options
     (which you may never need to change) are segregated onto their own
     menu. These options include turning off virus checking, changing
     which files IM considers to be programs and deciding where IM will
     store your integrity data.  SetupIM also allows you to permanently
     change the colors that IM uses on the display.

     These options are stored in the parameter file (IM.PRM).  You may,
     if you wish, keep multiple versions of this file around to
     represent different sets of options.  You can specify a different
     name for this file on IM's command line.


     THE PARAMETER (OPTIONS) FILE

     The parameter file (IM.PRM) contains all the options that control
     how IM works.  IM and SetupIM look for this file by searching the
     following locations:

       o  the current directory,

       o  the directory where IM.EXE is located,

       o  or the root directory on any disk.

     Whenever you change any options and save the changes, the
     parameter file is rewritten.  You save the changes by using the
     option "Write option changes to disk" on IM's Options menu.


   Integrity Master (tm)             - 50  -                 Version 3.02

     THE OPTIONS MENU

     You can reach the Options menu from any primary IM menu by pressing
     the "O" or alt/O keys.   From the Options menu, you can control
     almost all options that determine how IM works.  These options
     include all normal day-to-day choices.  (There are few lesscommonly
     used options that can only be changed through SetupIM.)

     ÚÄÄÄÄÄÄÄÄÄÄÉÍÍÍÍÍÍÍ»ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³   Help   ºOptionsº   Check   Initialize    ReLoad    CoMmands  ³
     ÀÄ ÉÍÍÍÍÍÍÍ¼       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ» ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
        º Write option changes to disk             º
        º Integrity:  CHECKING ON/off=quick update º
        º Integrity Update:   Ask for prog changes º
        º Files to Check:      Executable programs º
        º Files to iNitialize: Executable programs º
        º Halt on: ALL changes, adds or deletes    º
        º Sound ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ> ON/off  º
        º Report: (file or print)--------> on/OFF  º
        º Video (screen) report ÄÄÄÄÄÄÄÄÄ> ON/off  º
        º Ignore Time/date changes ÄÄÄÄÄÄ> on/OFF  º
        º Only changes reported ÄÄÄÄÄÄÄÄÄ> on/OFF  º
        º Exclude:    OFF and exclude report OFF  º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     In addition to allowing you to set all the above options, the
     Options menu displays the current settings of these options.  The
     options that have "on/off" settings, are toggled between their "on"
     and "off" states by pressing the ENTER key.  The current setting of
     the option is displayed in capital letters, as well as in a
     distinctive color.

     Write option changes to disk

       This allows you to save any changed option settings in the
       parameter file, making your option changes effective the next
       time you execute IM. This option does not exist on the SetupIM
       version of the Options menu. (SetupIM automatically saves any
       changes unless you tell it not to.)

     Integrity:  CHECKING ON/off=quick update

       This is the most crucial item on the Options menu.  Pressing the
       ENTER key toggles IM between doing full integrity checking and
       doing only quick integrity data updating.  When you press ENTER,
       either "Checking ON" or "OFF=Quick update" will be in all capital
       letters and in a different color (on most displays).  This
       discloses whether full integrity checking is on or off.  The
       status of integrity checking is also always visible on the fourth
       line at the top of the screen.

       Quick update mode provides a very fast way to bring all your
       integrity data up-to-date and to scan your disk viruses.  IM
       reads and integrity checks only files whose size, time stamp or
       date stamp have changed.  To detect file corruption and  unknown
       (new) viruses, it's essential to regularly turn "Checking ON" to
       do full integrity checks.

   Integrity Master (tm)             - 51  -                 Version 3.02
     Integrity Update:

       IM normally updates the integrity data describing a file whenever
       the file changes (unless the file is affected by a known virus or
       a disk error).  This option allows you control when IM updates
       the integrity data describing changed files.  This option is
       handy if you expect to find some damaged files and you want to
       save the old integrity data so that you can restore the file and
       then use IM to verify that the file is back to its original
       state.  The Option menu item itself displays the current setting
       for this option.  Integrity Update can have five values:

       "On for any changes"  - this is the normal mode where the
                               integrity data will be updated
                               whenever a file changes.

       "Off for any changes" - IM will NOT overwrite the old
                               integrity data with the new when a file
                               changes.

       "Off for prog changes"- IM will NOT overwrite the old
                               integrity data with the new when an
                               executable file (a program) changes.

       "Ask for any changes" - IM will ask you if it should overwrite
                               the old integrity data with the new
                               when a file changes.

       "Ask for prog changes"- IM will ask you if it should overwrite
                               the old integrity data with the new
                               when an executable file (a program)
                               changes.

       "NEVER"               - IM will never update integrity data.
                               This includes added or deleted files.
                               (All other options affect only changed
                               files.)

       "FORCED"              - IM will always update its integrity
                               data even if it finds corrupted files or
                               read errors.

       The right-most part of the second line at the top of your screen
       will also display an indication if you have Integrity Updating
       set to anything other than "On".

   Integrity Master (tm)             - 52  -                 Version 3.02

     Files to Check:

       You can use this option to limit IM's checking to only executable
       or source programs.  Even if you are interested only in virus
       detection, I strongly recommend that you also periodically set
       this option to check all files, so that you can be alerted to the
       other (more common) causes of file damage.  The Advanced menu in
       SetupIM allows you to change which files IM considers to be
       executable or source programs.

     Files to iNitialize:

       Use this option to limit IM's initializing of integrity data to
       only executable or source programs.  Even if your primary
       interest is viruses only, I strongly recommend that you set this
       option to read all files, so that you can be alerted to the other
       (more common) causes of file damage.  The Advanced menu in
       SetupIM allows you to change which files IM considers to be
       executable or source programs.

     Halt on: ALL changes

       IM lists each new file change that it detects at the top of the
       report screen.  The other changes on the screen shift downward
       (scroll) as each new line is added at the top of the screen.  By
       setting the halt options, you control when this scrolling will
       pause and wait for you to press a key.  This prevents a change
       from scrolling off the screen without your having seen it.  The
       halt options appear on this menu:

          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º Halt on:                        º
          º All detected differences        º
          º Changed files only              º
          º Changes to Executable programs  º
          º Changes to any Program          º
          º File corruption or worse        º
          º Serious problems                º
          º Emergencies Only (not viruses)  º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

       If you halt scrolling on "All detected differences", anytime a
       line written to the report screen is about to disappear off the
       bottom of the screen, the display will pause and wait for you to
       press a key to acknowledge that you've seen all the lines on the
       display.  After you press a key, the display will not pause until
       all the lines currently on the screen have scrolled off and a new
       unseen line is about to scroll off the screen.

       If you halt scrolling on "Changed files only", the scrolling will
       pause only when a modified file is about to disappear off the
       bottom of the screen.  After you press ENTER, the display will
       not stop scrolling until a changed file is about to scroll off
       the bottom.  This changed file must not have been on the screen
       during the prior pause.


   Integrity Master (tm)             - 53  -                 Version 3.02

       If you halt scrolling on "Changes to Executable programs", the
       scrolling will pause only when a program is about to disappear
       off the bottom of the screen.  After you press ENTER, the display
       will not stop scrolling until a program that was not on the
       previous display is about to scroll off the bottom.  You can use
       the "Advanced option" menu in SetupIM to check or change what IM
       considers to be executable programs.

       If you halt scrolling on "Changes to any Program", the scrolling
       will pause only when a program (either source or executable) is
       about to disappear off the bottom of the screen.  After you press
       ENTER, the display will not stop scrolling until a program that
       was not on the previous display is about to scroll off the
       bottom. You can use the "Advanced option" menu in SetupIM to
       check or change what IM considers to be either source or
       executable programs.

       If you halt scrolling on "File corruption or worse", only signs
       of viruses, corrupted files, or possible hardware errors will
       pause the display.

       If you tell IM to halt on "Serious problems", then the display
       will pause only when it detects a virus or critical error, such
       as a hardware error.  This affects scrolling in the same way as
       using the "/N" parameter on the command line.  If you set halt to
       this option, be sure that IM is writing a report to a file or to
       the printer; otherwise, you may miss some important warnings.

       If you tell IM to halt on "Emergencies Only", then the display
       will almost never pause.  IM will continue processing even if it
       detects a known virus in a file or can't read the disk.  IM will
       only stop if it considers it dangerous to continue, or if you're
       in danger of losing important information.  This affects
       scrolling in the same way as using the "/NE" parameter on the
       command line.  The "/ND" parameter works like "/NE" but IM
       executes optimized for unattended execution with no screen
       display of file checking or summary display. If you set halt to
       "Emergencies only" (/NE or /ND), be sure that IM is writing a
       report to a file or to the printer, otherwise you may miss some
       important warnings.

       You can always halt scrolling by pressing the "P" key.

     Sound -------------------------> ON/off
       IM will provide beeps and tones to alert you that something important has happened (or that you've pressed an unsupported key).
       Pressing ENTER toggles whether or not you hear these sounds.

   Integrity Master (tm)             - 54  -                 Version 3.02

     Report: (xxxxxxxxxxxxx)--------> on/OFF

       This allows you to turn the report file off or to ask IM to write
       a report of its activities to either the printer or a disk file.
       The "xxxxxxxxx" on the option line represents the name of the
       current report file or printer.  The disk file can be
       automatically named by IM or can be any file of your choice.
       Please see "The Report File" in Chapter Three for more details on
       these options.  This option line, along with the third line from
       the top of IM's screen, display the status of the report file.

     Video (screen) report ---------> ON/off

       If you have a very slow video board (such as some old CGA
       adapters), IM will run a little faster if you turn the screen
       report off. (Be sure to turn the report file on!)

     Ignore Time/date changes ------> on/OFF

       Sometimes the DOS time or date stamp on a file will change, but
       the file itself won't change.  If you do not want to have such
       files reported as changed, set this option to "ON".

     Only changes reported ---------> on/OFF

       If you do not want reports of added or deleted files, turn this
       option "on".  If "Only changes reported" is set to "on", then you
       will see only reports of file changes; IM will not report added
       or deleted files.  IM will still update the integrity data to
       reflect the added or deleted files, but it won't report these
       files.  All other processing also continues normally, including
       the detection of companion viruses (viruses that appear only as
       added files).

     Exclude:   ON  and exclude report  OFF

       Selecting this option will pop up the Exclude menu:

          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º IM will optionally exclude selected     º
          º files or directories from checking.     º
          º                                         º
          º Please press ESCape when you are done   º
          ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
          º Exclude checking is now OFF; turn it ON º
          º Reporting is now OFF; turn it ON        º
          º Select files or directories to exclude  º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

       The Exclude menu allows you to exclude files or entire directories
       from checking, scanning, or initializing.  The bottom line of the
       Options menu along with the lines on the Exclude menu show
       whether excluding of files or directories is turned on and whether
       reporting of excluded objects is turned on.  Either may be toggled
       on or off at the press of a key.  If reporting of excluded files is
       "ON" and excluding itself is "ON", then a line will appear on the
       report every time a file or directory is bypassed from checking, 

   Integrity Master (tm)             - 55  -                 Version 3.02

       scanning, or initializing. The line will list the particular file
       or directory that was excluded. If exclude checking is "ON",
       Integrity Master will exclude the hidden directory "\SENTRY" that
       Central Point PC Tools and MSDOS use with their "Delete Sentry"
       method of undelete protection. This directory will be excluded
       during integrity checking but still be checked when using
       Integrity Master as a scanner.

       You may exclude a file by specifying the precise file name or
       using the wild card characters to specify a series of files.  You
       can also exclude all files within a directory by excluding that
       directory from checking. Either files or directories  can be
       excluded based on wild cards.  For example, you can tell IM to
       ignore any directory beginning with the characters "IM" by  using
       the wild card: "IM*".  Or you could tell IM to ignore all your
       ZIP files (all filenames ending in ".ZIP")  by using the wild
       card "*.ZIP".

       When you're entering file or directory names to exclude, you may
       use the DOS wild card characters: * and ?.  The "*" character
       matches zero or any number of characters, while "?" matches one
       and only one character.  Some examples:

       This name:    Would exclude:       But not:
        A?.*        AB.ABC, AC.D       ABC.ABC, A.DEF, AX
        ??.ABC      XY.ABC, AB.ABC    A.ABC, XYZ.ABC
        A*.A?       A.AB, ABC.AX      A.CB, A.ABC

       Note that a wild card in the form "X*" will exclude any filename
       beginning with "X" (with or without an extension) while "X.*" will
       exclude only files which have an extension.

       If a file or directory is excluded, Integrity Master will no
       longer record information for it.  If integrity data already
       exists, then  IM will remove it.  To make sure you are aware of
       this, IM will always notify you that it is updating the integrity
       data.   For this  reason, you may see changes reported in a
       directory when you otherwise wouldn't expect any.  By asking IM
       to report what is being excluded you can see exactly what is
       being affected.

       Be very careful when excluding directories.  If a directory is
       excluded, IM will not look at any of the files in that directory
       or any of the subdirectories within that directory.  This means
       you can exclude an entire series of subdirectories (and their
       associated files) by excluding a single directory.

       If you un-exclude files and directories, they will appear as
       "added" the next time you run a check.


   Integrity Master (tm)             - 56  -                 Version 3.02

     OPTIONS IN SETUPIM

     When you execute SetupIM for the first time, the Integrity
     Advisor(tm) will set your options in a way most likely to meet your
     needs and interests.  You can later go back and change any of the
     options that were set for you.  If you specify that it's not your
     first install of IM, you will see this menu:

          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º Select an option and press ENTER:    º
          º                                      º
          º Overview of IM setup and operation   º
          º Change how Integrity Master operates º
          º Repeat the install on this PC        º
          º Install IM on another PC             º
          º Quit                                 º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     From this menu, you can select "Change how Integrity Master operates" and press ENTER.  This brings you to the Change menu:

          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º Select an option and press ENTER:    º
          º                                      º
          º Screen display mode                  º
          º Integrity data options               º
          º Advanced options                     º
          º Toggle CMOS check type (now FULL)    º
          º Home directory options               º
          º Update hardware configuration        º
          º Exit  - save any changes and end     º
          º Abort - Quit and abandon any changes º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     OPTIONS AVAILABLE ONLY IN SETUPIM

     SetupIM allows you to change certain options that you would only
     want to change very rarely.  All the options on this menu are not
     available within IM itself.


SCREEN DISPLAY MODE

     This allows you to set the screen colors as explained in the Chapter
     Two section titled Screen Colors.  Unless you have problems reading
     the screen, I strongly recommend that you allow IM to continue to
     operate in automatic video mode.  This way it will choose which
     colors are best for your video equipment.


   Integrity Master (tm)             - 57  -                 Version 3.02

     INTEGRITY DATA OPTIONS

     This allows you to change how IM stores the integrity data
     describing your files and system sectors.  You can change the name,
     attributes, or the location of your integrity data files.  You can
     also use this menu selection to check what the characteristics of
     your integrity data files are.

       INTEGRITY DATA FILE ATTRIBUTES

       You can ask IM to make your integrity data files hidden,
       read-only, or both.  Unless you are used to working with
       read-only and hidden files and consider yourself fairly expert
       with DOS, we suggest  that you not set these attributes.  There
       are quite a few programs that will cause confusing results when
       they work with hidden or read-only files.  These attributes can
       easily by overridden by a knowledgeable user or program.

       INTEGRITY DATA FILE NAMES:

       You can choose the names that IM will use for the integrity data
       files.  These filenames can be either fixed or variable.  If you
       did not specify a name for your integrity data files or select
       variable names, then your integrity data is stored in files named
       "ZZ##.IM".  Each file has this same fixed name.  If you run
       SetupIM, you can choose your own name for these files or ask IM
       to use variable names.  Use the IM  CoMmands menu to remove
       (Uninstall) the old files before you run SetupIM to assign new
       names to your integrity data files.

         VARIABLE INTEGRITY DATA FILE NAMES

         To make it more difficult for rogue programs to attack your
         integrity data files, IM can use variable file names.  Both the
         file name and the extension contain some characters which will
         be different for each file. Plus, the remainder of the file
         name will be different for each installation.  When you first
         install, the Integrity Advisor usually selects variable file
         names to store your integrity data.  SetupIM will then explain
         how these file names are formed for your particular
         installation.  It will also record this in the IMPROC.TXT file
         in case you need to quickly check this later.  If you install
         on another PC, these file names will be different unless you
         use the original parameter file.  To make these files easier
         for you to find, you may choose part of both the file name and
         the extension.

         FIXED INTEGRITY DATA FILE NAMES

         If you choose fixed file names, then every integrity data file
         will have the same name.  This makes it very easy to locate
         these files.  The drawback is that this also makes it very easy
         for someone else to locate your integrity data files if you
         keep them in the same directory with the files they describe.
         A destructive program could deliberately delete these files,
         causing loss of protection.

   Integrity Master (tm)             - 58  -                 Version 3.02

       LOCATION OF INTEGRITY DATA

       As IM checks your files, it must store the integrity data that
       describes these files.  Using SetupIM you can change where IM
       stores these files.  There are two options:

       1) It can store the integrity data in the same directory along
          with the files being checked, or


       2) It can store the integrity data on a separate disk (usually a
          floppy).

       Storing the integrity data on a floppy gives you additional
       protection against a virus or a person changing a file and then
       modifying the integrity data to cover up the change.  For
       viruses, this threat is fairly remote since the virus would have
       to be written specifically to attack files created by IM.  This
       would be very difficult since these files are encrypted
       differently on each PC.   Storing the integrity data with the
       files being checked is usually easier and more flexible since the
       integrity data can be copied along with the files.  This also
       makes it easy for you to use IM to verify that you've made a good
       copy when you copy or move the files. If you want to restore an
       old copy of a file from a backup, you can restore the integrity
       data along with the file and then ask IM to check that the file
       was restored correctly.  If you move your files, it's easier to
       move the integrity data along with the files if it's stored in
       the same directory as the files.

     TOGGLE CMOS CHECK TYPE

     This option displays the current type of CMOS checking that IM will
     do (either "CORE", "FULL", or "BASE").  When you hit ENTER the
     check type will switch between "CORE", "FULL", and "BASE". Full
     checking will check all of your PC's available CMOS.  Since
     checking the full CMOS may cause too many reports of changes on
     some PCs, we offer the option of checking only the more standard
     "BASE" 64 byte CMOS or the "CORE" CMOS (the portions of the CMOS
     that are important to the integrity of your PC.)  Changing this
     option does not affect your ability to reload your full CMOS if it
     should become necessary.

     HOME DIRECTORY OPTIONS

     This allows you to specify a name and location for your home
     directory.  This is the directory where IM will store its files,
     including its "auto-named" report files and the reload files.
     (e.g., BOOT.SRL, PART.SRL, CMOS.SRL).


   Integrity Master (tm)             - 59  -                 Version 3.02

     If you have installed a version prior to 2.31, then these files are
     located in the root directory and you should use this option to
     activate use of the IM "home directory".  If you are converting
     from an earlier version, be sure to move your existing files to the
     "home directory" on each disk after you run SetupIM.


     UPDATE HARDWARE CONFIGURATION

     Please use this option whenever you change the configuration of
     disk drives on your computer, or if you use software that changes
     the assignment of DOS logical disk letters (A to Z) to your
     physical disk drives.  SetupIM will check the capabilities of each
     of your installed disk drives.  This will produce a display showing
     the drives that SetupIM recognizes.  It will also list any drives
     that do not contain DOS boot sectors and any that do not have
     partition sectors (master boot records).

     EXIT - SAVE ANY CHANGES AND END

     This updates the parameter file (IM.PRM) with any option changes
     you've selected, and exits SetupIM.

     ABORT - QUIT AND ABANDON ANY CHANGES

     This allows you to exit SetupIM without writing any of your changes.
     All option settings will be as they were before you entered SetupIM.


     THE ADVANCED OPTION MENU

     If you select this option on the SetupIM change menu, the Advanced
     option menu will appear.
          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º Select an option and press ENTER:              º
          º (Press ESCape when you're done)                º
          º                                                º
          º Specify Names of hidden system files           º
          º Define which files are Executable programs     º
          º Define which files are Source programs         º
          º Check all files for Macros is ON; turn if off  º
          º Check for virus in memory is ON; turn it off   º
          º General virus checking is ON; turn it off      º
          º Change Format for date or time                 º
          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     This menu is intended for more technically advanced users.  Most IM
     users should never need to use this menu.  When you're finished
     making changes on this menu, just press ESCape to go back to the
     previous menu.  The Advanced Option menu offers you these options:
     Specify Names of hidden system files


   Integrity Master (tm)             - 60  -                 Version 3.02

     SPECIFY NAMES OF HIDDEN SYSTEM FILES

       Selecting this option will allow you to change the names of the
       files that IM recognizes as the hidden system files.  This option
       is only needed on nonstandard PCs that don't use the standard
       Microsoft or the IBM names for the hidden system files.  The
       files SetupIM recognizes by default are: IBMBIO.COM, IBMDOS.COM,
       IO.SYS and MSDOS.SYS.  If you execute "IMCHECK *.*", in your root
       directory and you don't see two of the above files, but instead
       see two other similarly named files, you may wish to use this
       option so IM recognizes those files.  If you don't understand
       what this is all about, don't worry.  IM's ability to recognize
       your hidden system files is NOT that important.  It simply allows
       IM to provide more specific information in two warning messages.

     DEFINE WHICH FILES ARE EXECUTABLE PROGRAMS

       This option allows you to specify which file extensions (the
       letters after the "." in the file name) IM should consider to
       represent executable programs.  This is important for three
       reasons:

       1) Non-executable files are not normally checked for known viruses.

       2) IM provides special warning when executable programs change.

       3) If you use the Options menu to limit checking to executable
         programs, only these files will be checked.

       Initially, IM will consider files ending in the following
       extensions to be executable programs:

            .OV?  (where ? can be any character)     .DLL
            .BAT                                     .DRV
            .BIN                                     .EXE
            .BTM                                     .PIF
            .CMD                                     .SYS
            .COM
       Note that not all these files can actually be affected by
       viruses, but all these files in one way or another contain
       instructions that are executed by your PC.

     DEFINE WHICH FILES ARE SOURCE PROGRAMS

       This option allows you to specify which file extensions (the
       letters after the "." in the file name) IM should consider to be
       source programs.  Source programs are the programs a programmer
       would use to create executable programs.  If you are not a
       programmer then you probably don't care about this option.  This
       option is intended mostly to provide programmers with extra
       warning if something or someone is modifying their source code.

   Integrity Master (tm)             - 61  -                 Version 3.02

     CHECK ALL FILES FOR MACROS

       Some programs store sequences of commands called macros in their
       data files. These macros can be executed just like a program.  In
       some cases the macros will be automatically executed when the
       data file is opened. Viruses written in the product's macro
       language take advantage of this to attach themselves to other
       files. The Concept virus does this with respect to MS Word
       documents (actually templates disguised as documents).

       Using this option you toggle whether IM checks all files for
       macros or just those files that normally contain macros (e.g.,
       .DOC and .DOT for MS Word or .XLS for Excel.) If you use
       nonstandard extensions, you should set this option to check all
       files for the presence of macros. Checking all files, requires IM
       to open and partially read all files to determine if they contain
       macros. Beware: this will slow IM's speed considerably!

     CHECK FOR VIRUS IN MEMORY

       Selecting this option will toggle the checking of memory for known
       viruses on or off.  If you toggle memory checking on, the option
       line will be changed to read:

          Check for virus in memory is ON; turn it off.

       This indicates that memory checking is now "ON".  If you press
       ENTER at this point, you will turn it "off", and the option will
       then read:

          Check for virus in memory is OFF; turn it on.

       Having this option "ON" allows IM to detect known viruses that
       are resident in memory.  If you always cold boot from a known
       good copy of DOS on a write-protected diskette, you could safely
       turn this option off, since there would be no way for a virus to
       be resident in memory.  Since it's hard to guarantee that you
       always cold boot, please leave resident memory checking turned
       on. If you execute IM multiple times and you don't want to wait
       for the memory check to complete, you can use the"/B" (Bypass)
       command line parameter to bypass the resident memory check.


   Integrity Master (tm)             - 62  -                 Version 3.02

     GENERAL VIRUS CHECKING

       Selecting this option and pressing enter will toggle checking of files
       for known viruses on or off.  If you have absolutely no interest in
       viruses, you can speed up IM's initialize processing and its check
       processing (only when it encounters changed files) by 10 to 20
       percent.  Since this option imposes so little overhead in normal file
       checking, I suggest everyone leave it turned on.


   Integrity Master (tm)             - 63  -                 Version 3.02


     CHAPTER FIVE - ERRORS
     ____________________________________________________________________

     ERROR RECOVERY:

     IM replaces the normal DOS error recovery routines with its own
     more sophisticated routines.  If you encounter a hardware error,
     you'll generally see a message announcing what happened followed by
     a screen that will give you the option of retrying the failed
     operation, aborting (allowing whatever IM was trying to do, to
     fail), or other options depending upon the circumstances.  These
     other options may include "Shelling to DOS".  Shelling allows you
     to temporarily leave IM and execute any DOS command (such as
     formatting a disk) you wish.  You then return to IM by typing the
     EXIT command.  This returns you to the same point in IM, just as if
     you had never left.

     SOLVING PROBLEMS:

     If you encounter a problem with IM, please read file QUESTION.TXT
     (for a list of common questions and answers) and file SUPPORT.DOC
     (for the complete procedure on how to quickly get technical
     support).  File DISKHELP.TXT contains specific information on how
     to handle problems if IM won't recognize your disk drive.  You can
     use IMPRINT or IMVIEW to read any of these files. Example:  "IMVIEW
     SUPPORT.DOC"

     ANSWERS TO COMMON QUESTIONS:

     File QUESTION.TXT contains common questions and answers regarding
     IM.  You can read these by entering the command "IMVIEW
     QUESTION.TXT" at the DOS prompt or print them with the command
     "IMPRINT QUESTION.TXT".


    Integrity Master (tm)           - 64-         Data Integrity and Viruses

                                     NOTES


    Integrity Master (tm)           - 65 -        Data Integrity and Viruses


                                   PART TWO


                          Data Integrity and Viruses


                 ___________________________________________


                How do I make sure that my programs and files
                               really are safe?


                What threats are even more likely to damage my
                              data than viruses?


                      What really works against viruses?


                      What doesn't work against viruses?


                        Why are viruses so dangerous?


                            How do I kill a virus?


                 ___________________________________________



         Copyright 1990-1996, Wolfgang Stiller, All rights reserved.



    Integrity Master (tm)           - 66 -        Data Integrity and Viruses

    Integrity Master (tm)           - 67 -        Data Integrity and Viruses


     PART TWO - Data Integrity and Viruses

     CHAPTER ONE - THREATS TO YOUR DATA
     ____________________________________________________________________


     INTRODUCTION - VIRUSES GET ALL THE GLORY

     Do you have data or programs on your PC which you can't afford to
     have unexpectedly damaged?  How can you make sure that your data
     is safe?  To protect the integrity of your data, you must first
     understand the nature of the threats against it.

     The most publicized threats to your computer are software-based
     attacks often lumped together as "viruses" by the media.  Although
     viruses are often sensationalized by media coverage, they do
     present a very real menace to your data.  (See the section in this
     chapter titled How serious are viruses?.)  Even if a virus never
     attacks your PC, it is almost inevitable that system glitches will
     someday corrupt data or programs on your PC.  Considering that
     viruses are but one threat to your data and not the most likely
     threat by far, it's ironic that so many people have anti-virus
     software but so few people take steps to protect the integrity of
     their programs and data from other hazards.  Can anyone afford NOT
     to know that each and every byte on their disk is undamaged?

     So what's the explanation?  Why do so few people take steps to
     assure the integrity of the data on their PCs?  The main reason is
     that data integrity gets almost no media coverage (even in the
     trade journals), while a virus story may make the local evening
     news.  The result is that people just don't give data integrity a
     second thought.  It's all too easy to take the reliability of our
     modern PCs for granted -- and, as you'll see, all too dangerous!

     You may be reading this primarily because you're interested in
     viruses. If that's true, then, for you, the media attention to
     viruses will have had a very beneficial effect.  You are about to
     learn how to protect your PC against much more than just viruses!
     Data integrity is not a very glamorous subject, yet it's both
     crucial and fundamental to using any computer.  Without positive
     assurance of data integrity, computers cannot be depended upon to
     process any type of important data.  How would you respond if
     someone were going to change a byte of data somewhere at random on
     your disk?  You'd be pretty upset -- right?  Well, the odds are, it
     has already happened but you were not aware of it.  Perhaps the
     result was that a program quit working or CHKDSK/Scandisk found
     lost or cross-linked clusters. Or perhaps, if you're lucky, the
     damage was to some inconsequential part of your disk. Let's explore
     the different threats to your files and programs:

    Integrity Master (tm)           - 68 -        Data Integrity and Viruses

     HARDWARE AND POWER FAULTS

     These are well known but also all too common.  We all know that
     when your PC or disk gets old, it might start acting erratically
     and damage some data before it totally dies.  Unfortunately,
     hardware errors frequently damage data on even young PCs and disks.

     Your PC is busy writing data to the disk and the lights go out!
     "Arghhhh!"  Is everything OK?  Maybe so, but it's vital to know for
     sure if anything was damaged.  If your disk drive is starting to
     fail, you may start to experience occasional damage to your files.
     Regrettably, it's not a question of "if", but a question of "when"
     in regard to disk failure.  There are tools (NORTON, MACE, PCtools,
     etc) to assist in recovery from disk problems, but how do you know
     all the data is OK?  These tools do not always recover good copies
     of the original files.  It's vital to have some way to check that
     these tools really do their job correctly.

     You can have hardware problems on a perfectly healthy PC if you
     have devices installed that do not properly share interrupts.  This
     problem is getting more and more frequent as we see multiple
     adapters installed in a PC that use the same interrupt (IRQ).
     Sometimes problems are immediately obvious, other times they are
     subtle and depend upon certain events to happen at just the wrong
     time, then suddenly strange things happen!


     FINGER CHECKS (TYPOS AND "OOPS! I DIDN'T MEAN TO DO THAT.")

     These are an all too frequent cause of data corruption.  This
     commonly happens when you are intending to delete or replace one
     file but actually get another.  By using wild cards, you may
     experience a really "wild" time.  "Hmmm I thought I deleted all the
     *.BAK files . . . but they're still here . . . something was
     deleted . . . what was it? . . . or was I in the other directory?"
     Of course if you're a programmer or if you use sophisticated tools
     like Norton's sector editor (NU), then your fingers can really get
     you into trouble!


     MALICIOUS OR CARELESS DAMAGE

     Someone may accidentally or deliberately delete or change a file on
     your PC when you're not around.  If you don't keep your PC locked
     in a safe, then this is a risk.  Who knows what was changed or
     deleted?  Wouldn't it be nice to know if anything changed over the
     weekend?  Most of such damage is done unintentionally by someone
     who you probably know.  This person didn't mean to cause trouble;
     he simply didn't know what he was doing when he used your PC.
     Software Problems

     This category accounts for more damage to programs and data than
     any other.  We're talking about non-malicious software problems
     here, not viruses.  Software conflicts, by themselves, are much
     more likely threats to your PC than virus attacks.

     We run our PCs today in a complex environment.  There are many
     resident programs (TSRs such as Sidekick) running simultaneously
     with various versions of DOS, BIOS and device drivers.  All these
     programs execute at the same time, share data and are vulnerable to
     unforeseen interactions between each other.   Naturally, this means
     that there may be some subtle bugs waiting to "byte" us.  Anytime a
     program goes haywire, there's the risk it may damage information on
     disk.

     There's the further problem that not all programs do what we hope
     they will.  If you have just undeleted a file, did you really get
     all the correct clusters back in the right order?   When CHKDSK or
     Scandisk  "fixes" your disk for you, isn't it essential to know
     exactly what files it changed to do its job?  This is one more
     reason why everyone must have the capability to verify data
     integrity.


    Integrity Master (tm)           - 69 -        Data Integrity and Viruses

     DANGER WITH COMPRESSION AND CACHE

     Disk cache and compression programs (e.g. DriveSpace or Stacker)
     can cause random and unpredictable errors when reading or writing
     the disk.  This can cause random damage to your data. In chapter
     six, I offer a full explanation of how to make sure you are using
     such programs safely.


     SOFTWARE ATTACKS

     These are programs written deliberately to vandalize someone's
     computer or to use that computer in an unauthorized way.  Even
     though some viruses do not intentionally damage your data, I
     consider all viruses to be malicious software since they modify
     your programs without your permission, with occasional disastrous
     results.  There are many forms of malicious software; sometimes the
     media refers to all malicious software as viruses.  It's important
     to understand the distinction between the various types.  Let's
     examine the different types of malicious software.


     LOGIC BOMBS

     Just like a real bomb, a logic bomb will lie dormant until
     triggered by some event.  The trigger can be a specific date, the
     number of times executed, a random number, or even a specific event
     such as deletion of an employee's payroll record.  When the logic

    Integrity Master (tm)           - 70 -        Data Integrity and Viruses

     bomb is triggered, it will usually do something unpleasant. This
     can range from changing a random byte of data somewhere on your
     disk to making the entire disk unreadable.  Changing random data
     may be the most insidious attack since it generally causes
     substantial damage before anyone notices that something is wrong.
     It's vital to have some data integrity software in place so that
     such damage can be quickly detected.  Although you can detect it
     after the fact, there is unfortunately no way to prevent a well
     written logic bomb from damaging your system.  On the other hand, a
     logic bomb that uses standard DOS or BIOS requests to do its dirty
     work can be caught by most interceptor type programs (see Chapter
     Two).


     TROJANS

     These are named after the Trojan horse, which delivered soldiers
     into the city of Troy.   Likewise, a trojan program is a vehicle
     for delivering some destructive code (such as a logic bomb or a
     virus) into a computer.  The trojan program appears to be a useful
     program of some type, but when a certain event occurs, it does
     something nasty and often destructive to the system.


     WORMS

     A worm is a self-reproducing program that does not infect other
     programs as a virus will, but instead creates copies of itself,
     that create even more copies.   These are usually seen on networks
     and on multi-tasking operating systems, where the worm will create
     copies of itself that are also executed.  Each new copy will create
     more copies quickly clogging  the system.  The so-called
     ARPANET/INTERNET "virus" was actually a worm. It created copies of
     itself through the ARPA network, eventually bringing the network to
     its knees.  It did not infect other programs as a virus would, but
     simply kept creating copies of itself that would then execute and
     try to spread to other machines.


     VIRUSES

     Viruses are a subject of much confusion and a target of
     considerable misinformation even from some so-called virus experts.
     Let's define what we mean by virus:

     A virus is a program that reproduces its own code by attaching
     itself to other programs in such a way that the virus code is
     executed when the infected program is executed.

     You could probably also say that the virus must do this without the
     permission or knowledge of the user, but that's not a vital
     distinction for purposes of our discussion here.


    Integrity Master (tm)           - 71 -        Data Integrity and Viruses

     Most viruses do their "job" by placing self-replicating code in
     other programs, so that when those other programs are executed,
     even more programs are "infected" with the self-replicating code.
     This self-replicating code, when triggered by some event, may do a
     potentially harmful act to your computer.  Viruses are initially
     distributed in the form of a trojan.  In other words, the virus
     code has been planted in some useful program.  Since the virus
     infects other useful programs, absolutely any piece of executable
     code can suddenly become a trojan delivery vehicle for the virus.

     Another way of looking at viruses is to consider them to be
     programs written to create copies of themselves.  These programs
     attach these copies onto other programs (infecting those programs).
     When one of these other programs is executed, the virus code (which
     was attached to that program) executes, and links copies of itself
     to even more programs.


     GENERAL VIRUS BEHAVIOR

     Viruses come in a great many different forms, but they all
     potentially have two phases to their execution, the infection phase
     and the attack phase:

  1) When the virus executes, it will infect other programs.  What's
     often not clearly understood is precisely WHEN it will infect the
     other programs.  Some viruses infect other programs each time they
     are executed; other viruses infect only upon a certain trigger.
     This trigger could be anything; it could be a day or time, an
     external event on your PC, a counter within the virus, etc.  Modern
     viruses have become more selective about when they infect programs.
     Being selective improves the virus' chance to spread; if they
     infect too often, they will tend to be detected before they have
     enough time to spread widely. Virus writers want their programs to
     spread as far as possible before anyone notices them.  This brings
     up an important point which bears  repeating:

     It is a mistake to execute a program a few times, find nothing
     infected, and presume there are no viruses in the program. You can
     never be sure that the virus simply hasn't triggered its infection
     phase!

     Many viruses go resident in the memory of your PC in the same way
     as terminate and stay resident (TSR) programs such as Sidekick.
     This means the virus can wait for some external event before it
     infects additional programs.  The virus may silently lurk in memory
     waiting for you to insert a diskette, copy a file, or execute a
     program, before it infects any other programs.  This makes these
     viruses more difficult to analyze since it's hard to guess what
     trigger condition they use for their infection.  Resident viruses

    Integrity Master (tm)           - 72 -        Data Integrity and Viruses

     frequently corrupt the system software on the PC to hide their
     existence.  This technique is called "stealth" and I'll cover this
     in more detail shortly.

  2) The second phase is the attack phase.  Many viruses do unpleasant
     things such as deleting files or changing random data on your disk,
     simulating typos or merely slowing your PC down; some viruses do
     less harmful things such as playing music or creating messages or
     animation on your screen.  Just as the virus's infection phase can
     be triggered by some event, the attack phase also has its own
     trigger. Viruses usually delay revealing their presence by
     launching their attack only after they have had ample opportunity
     to spread.  This means that the attack may be delayed for years
     after the initial infection.  The attack phase is optional; many
     viruses simply reproduce and have no trigger for an attack phase.
     Does this mean that these are "good" viruses?  No, unfortunately
     not!  Anything that writes itself to your disk without your
     permission is stealing storage and CPU cycles.  This is made worse
     since viruses that "just infect", with no attack phase, damage the
     programs or disks they infect.  This is not an intentional act of
     the virus, but simply a result of the fact that many viruses
     contain extremely poor quality code.  One of the most common
     viruses, the STONED virus is not intentionally harmful.
     Unfortunately, this virus will write to an area on diskettes that
     may result in  file corruption.

     Now that we've examined general virus behavior, let's take a closer
     look at the two major categories of viruses and how they operate.

     SYSTEM SECTOR VIRUSES

     These are viruses that plant themselves in your system sectors.
     System sectors are special areas on your disk containing programs
     that are executed when you boot your PC.  Sectors are not files but
     simply small areas on your disk that your hardware reads in single
     chunks. Under DOS, sectors are most commonly 512 bytes in length.
     These sectors are invisible to normal programs but are vital for
     correct operation of your PC.  They are a common target for
     viruses. There are two types of system sectors found on DOS PCs:

     DOS BOOT SECTORS

     The very first sector on a disk or diskette that DOS is aware of is
     the boot sector.  From a DOS perspective, this is the first sector
     on a disk.  This sector can contain an executable program whether
     the disk is bootable or not.  Since this program is executed every
     time you power on or boot your PC, it is very vulnerable to virus
     attack. Damage to this sector can make your disk appear to be
     unreadable.

     This sector is rewritten whenever you do a "SYS" or a "FORMAT /S"
     to a disk.

    Integrity Master (tm)           - 73 -        Data Integrity and Viruses

     Warning: Even a non-bootable floppy can contain a virus in  the
     boot sector.  If you leave the floppy in your PC when you power on
     or boot, you will be infected even though the PC won't successfully
     boot from that floppy.


     PARTITION SECTORS

     On hard (fixed) disk drives, the very first sector is the partition
     sector (also known as the master boot record or partition table).
     Each physical hard disk drive has one of these sectors.  A single
     physical disk can be partitioned into one or more logical disks.
     For example, you may have a physical drive partitioned into C: and
     D: logical disks so that your single physical disk appears (to DOS)
     to be two logical disks.  The single partition sector contains the
     information that describes both logical disks. If the partition
     sector is damaged, then DOS may not even recognize that your disk
     exists.

     The partition sector also contains a program that is executed every
     time you power up or boot your PC.  This program executes and reads
     the DOS boot sector that also contains a program.  Many viruses
     plant their code in the partition sector.

     System sector viruses modify the program in either the DOS boot
     sector or the partition sector.  Since there isn't much room in the
     system sector (only 512 bytes), these viruses usually have to hide
     their code somewhere else on the disk.  These viruses sometimes
     cause problems when this spot already contains data that is then
     overwritten. Some viruses, such as the Pakistani BRAIN virus, mark
     the spot where they hide their code as bad clusters.  This is one
     reason to be alarmed if CHKDSK (or Scandisk)suddenly reports
     additional bad sectors on your disk.  These viruses usually go
     resident in memory on your PC, and infect any floppy disk that you
     access.  Simply doing a DIR on a floppy disk may cause it to be
     infected.  Some viruses will infect your diskette immediately when
     you close the drive door.  Since they are active in memory
     (resident), they can hide their presence.  If BRAIN is active on
     your PC, and you use a sector editor such as Norton's NU to look at
     the boot sector of an infected diskette, the virus will intercept
     the attempt to read the infected boot sector and return instead a
     saved image of the original boot sector.  You will see the normal
     boot sector instead of the infected version.  Viruses that do this
     are known as stealth viruses.

     In addition to infecting diskettes, some system sector viruses
     spread by also infecting files.  Viruses of this type are called
     "multipartite" (multiple part) viruses.  Since they can infect both
     files and system sectors, they have more avenues to spread and are
     more difficult to remove.

    Integrity Master (tm)           - 74 -        Data Integrity and Viruses

     FILE VIRUSES

     In terms of sheer number of viruses, these are the most common
     kind. The simplest file viruses work by locating a type of file
     that they know how to infect (usually a file name ending in ".COM"
     or ".EXE") and overwriting part of the program they are infecting.
     When this program is executed, the virus code executes and infects
     more files. These overwriting viruses do not tend to be very
     successful since the overwritten program rarely continues to
     function correctly and the virus is almost immediately discovered.
     The more sophisticated file viruses save (rather than overwrite)
     the original instructions when they insert their code into the
     program.  This allows them to execute the original program after
     the virus finishes so that everything appears normal.  Just as
     system sector viruses can remain resident in memory and use
     "stealth" techniques to hide their presence, file viruses can hide
     this way also.  If you do a directory listing, you will not see any
     increase in the length of the file and if you attempt to read the
     file, the virus will intercept the request and return your original
     uninfected program to you.  This can sometimes be used to your
     advantage.  If you have a "stealth" virus (such as 4096 or Dir-2),
     you can copy your program files (*.EXE and *.COM files) to files
     with other extensions and allow the virus to automatically
     disinfect your files!  If you "COPY *.COM  *.CON", and then cold
     boot your PC from a known good copy of DOS and "REN *.CON  *.COM",
     this will disinfect the renamed files.

     Some file viruses (such as 4096) also infect overlay files as well
     as the more usual *.COM and *.EXE files.  Overlay files have
     various extensions, but ".OVR" and ".OVL" are common examples.


     MIRACLE INFECTIONS

     Would you believe that a virus can infect your files without
     changing a single byte in the file?  Well, it's true!  There are
     two types of viruses that can do this.  The more common kind is
     called the companion or spawning type virus.  This virus infects
     your files by locating a file name ending in ".EXE".  The virus
     then creates a matching file name ending in ".COM" that contains
     the viral code. Here's what happens; let's say a companion virus is
     executing (resident) on your PC and decides it's time to infect a
     file.  It looks around and happens to find a file called "WP.EXE".
     It now creates a file called "WP.COM" containing the virus.   The
     virus usually plants this file in the current directory although it
     could place it in any directory on your DOS path.  If you type "WP"
     and press ENTER, DOS will execute "WP.COM" instead of "WP.EXE".
     The virus executes, possibly infecting more files and then loads
     and executes "WP.EXE".  The user probably won't notice anything
     wrong.  This type of virus is fortunately easy to detect by the
     presence of the extra ".COM" files.  There are some instances where
     it is normal to have both ".COM" and ".EXE" files of the same name

    Integrity Master (tm)           - 75 -        Data Integrity and Viruses
     (such as DOS 5's DOSSHELL) but this is relatively rare.  Companion
     viruses could also work by creating other file types such as .EXE
     files to match existing .BAT files. A companion virus could also
     insert matching executable files into a different directory on your
     DOS path. Since DOS searches the directories in the PATH
     sequentially, a file in an earlier directory will be executed
     before one contained in a later directory. Be sure to look very
     closely if you notice unexpected new files appearing on your disk.

     There is another type of virus known as a "cluster" virus that
     infects your files not by changing the file or planting extra files
     but by changing the DOS directory information so that directory
     entries point to the virus code instead of the actual program.
     When you type the name of the program, DOS loads and executes the
     virus code, the virus then locates the actual program and executes
     it.  Dir-2 is an example of this type of virus and is now spreading
     rapidly around the world.  I am deliberately keeping the
     description of this type of virus rather vague to avoid making it
     easier to write this type of virus.


     MACRO VIRUSES

     Many programs (e.g., most spreadsheets and word processors) provide
     what they call a "macro" capability.  In their most simple form,
     macros allow you to record key strokes and then later play them
     back. Many popular programs, such as MS Word, Excel, AmiPro, and
     Lotus 1-2-3, go far beyond keystroke recording and provide a mini
     programming language. The macros are intended to help users of
     these products to automate routine or complicated tasks but they
     can also be used to write viruses.  Since these macros can then be
     saved in data files by the program, these data files must be
     considered to be executable (at least for people who have the
     program that can execute the macros stored in these files).  These
     data files cannot execute by themselves but require the program
     (i.e, the word processor or spreadsheet) to execute them.

     Any program that supports such macros (especially if there is a way
     to automatically execute such macros without the user being aware)
     is potentially susceptible to infection by a virus written in the
     macro language used by that product.  We have currently seen a
     number of viruses that infect MS Word documents (and recently AMI
     Pro documents).

     The very first macro virus to spread in the wild was Concept (AKA
     "Prank Macro" and WordMacro.Concept). (It was discovered in August
     of 1995)   This virus is now one of the most common viruses
     world-wide based on reports from our customers.

     Concept can infect any computer that uses MS Word 6.0 (or later

    Integrity Master (tm)           - 76 -        Data Integrity and Viruses
     release).   Since there is also a version of MS Word for Apple
     Macintosh computers as well as PCs, this virus will spread to (or
     from) a Macintosh if an infected document is exchanged.  While
     Concept can spread outside the PC environment, it's important to
     recognize this is a very limited virus.  It will only spread to
     computers running MS Word.  Actually it's more limited than that;
     it will only spread to computers using English language versions of
     MS Word 6.0. It will not spread to German, French, Spanish, or
     Russian versions of MS Word.

     If you take a quick look at Concept, it seems to break the rules
     for viruses. Concept infects MS Word documents.  Simply opening an
     infected document causes the virus to infect your PC.  I mentioned
     previously that viruses infect only executable programs. It seems a
     contradiction that a virus could infect documents.  I also stated
     that to become infected by a virus, you must execute an infected
     program. Both these statements still hold true. To see how this is
     possible, let's take a close look at how Concept works.

     HOW CONCEPT WORKS:

     Concept was written using the "Macro" capability built into MS
     Word.  Actually it is somewhat of a misnomer to call this just a
     macro capability since it uses a full programming language called
     Word Basic that Microsoft provides with each copy of Word.  The
     virus was written in Word Basic.  But MS Word documents can't
     contain macros so how does the virus attach itself to documents?
     It does this by creating a "template" rather than a document.
     Templates are special files supported by MS word that are used as a
     pattern for new documents.  Templates, unlike documents can contain
     macros. Concept causes infected documents to be saved as templates
     but with the ".DOC" extension normally associated with documents.
     After this happens, the original document no longer exists as a
     document but rather as a template with a ".DOC" extension.
     Templates normally have ".DOT" extensions so the fact that the
     document has been converted to a template is not at all obvious.

     The virus consists of the macros that are stored inside of the
     template. But what causes the virus macros to be executed in the
     first place?

     AUTOMATIC MACRO VIRUS EXECUTION

     MS Word provides the capability to automatically execute a macro
     (in this case a Word Basic program) when you open a new template.
     The infected templates contain such an AutoOpen macro; this is how
     the virus code (in the form of a Word Basic macro program) is
     executed when you open an infected document.

     This makes the virus very deceptive. Few users of MS Word realize
     that every time they open what they think is a document, they could

    Integrity Master (tm)           - 77 -        Data Integrity and Viruses
     be executing a viral program.  This exposure is not unique to MS
     Word but it is also present in other environments that support
     macro languages such as MS Excel, Amir Pro, Lotus 1-2-3, and Quatro
     Pro.

     HOW CONCEPT SPREADS

     Concept creates a "FileSaveAs" macro.  This is the code that
     executes when you select "File Save As" from the MS Word File menu.
     After opening an infected document, any use of "File Save As" will
     result in the document being saved as an infected template with the
     standard ".DOC" extension normally associated with documents. Since
     documents and templates are handled almost identically by MS Word,
     the user is not aware that anything unusual has happened when
     document is converted to an infected template by the "FileSaveAs"
     macro.

     Another interesting aspect of this virus is that once you open an
     infected document, the MS Word environment itself becomes infected.
     This means that if you restart MS Word with no files open, you will
     already be infected; all files saved with "File Save As" will be
     infected templates.  The virus accomplishes this by modifying the
     "NORMAL.DOT" file.  This file contains the global macros used by MS
     Word.  Essentially this makes the virus' macros always present (and
     active) in the MS Word environment.

     IS CONCEPT REALLY A VIRUS?

     Microsoft originally called this virus "Prank Macro" and did not
     refer to it as a virus.  Does this really qualify as a virus?  Yes,
     unfortunately it does.  When you open an infected document
     (actually a template), you automatically execute the virus code.
     This code modifies the MS Word environment so that all future
     documents saved using "File Save As" will be infected templates.
     This transfers the infection from one host document to another and
     is actually spreading in the wild.

     Concept is fortunately very easy to spot.  When you open an
     infected file for the first time, you will see a box appear
     containing the number "1" and nothing else.  This apparently was
     intended by the author of the virus.  The virus does not have a
     destructive payload but it creates a macro called "Payload" that
     could easily be modified to do something destructive.  Several
     quickie removers leave the "Payload" macro in place since the
     presence of this macro will prevent reinfection by the virus.  The
     virus checks for the presence of a macro called "Payload" and will
     not infect if it sees a macro called "Payload" already there.  The
     virus also adds two other macros to the global macro pool: "AAAZA0"
     and "AAAZFS". These macros are very easy to spot and provide a
     quick way to check if you are infected.  In MS Word, simply click
     on "Tools" and then "Macros" and check if these macros are listed.
     Beyond spreading, this virus does no real damage.  The same is not
     be true for other macro based viruses.

    Integrity Master (tm)           - 78 -        Data Integrity and Viruses

     Concept is fairly easy to deal with.  Other viruses of this type
     will not be so easy.  If you don't use MS Word you may think you
     are safe but any language that supports a similar macro language is
     vulnerable to a virus of this type.  MS Excel, Lotus 1-2-3, Ami
     Pro, and Quatro Pro contain languages which would allow writing of
     viruses that could spread in these environments. It's important to
     understand that such viruses would spread only within those
     specific environments rather than universally (the way existing
     executable and boot sector viruses spread).


     PROTECTION AGAINST FUTURE MACRO VIRUSES

     There are steps you can take now to protect yourself against future
     macro viruses similar to Concept.

     1) If you click on "Options" under "Save" you can ask MS Word to
        get your approval before modifying NORMAL.DOT.  This will
        disable one of the tricks used by Concept and likely used in
        future viruses of this type.

      2) It should be obvious to you that the reason this virus works is
         that it executes without your knowledge in the "AutoOpen" macro.
         Turning this off would eliminate this type of attack and the MS
         Word documentation provides a way to do this. Just start MS Word
         with the command:

                    winword.exe /mDisableAutoMacros

         This supposedly disables all auto macros. unfortunately it
         doesn't work!  I hope Microsoft will soon fix this so we can use
         the above option to prevent automatic execution of viral macros.

      3) A technique which does work is to enter the following macro.
         Click on "Tools" and then "Macros" and create a new macro
         called "autoexec".  (This macro will automatically execute
         every time you start MS Word.)  Enter the following text as
         your macro (it's a short Word Basic program):

         SUB MAIN
            DisableAutoMacros 1
            MSGBox "Automatic Macro Execution is now OFF",-1
         END SUB

        Every time you now start up Word, it will turn off Automatic
        Macros effectively eliminating a viral attack using automatic
        execution macros.

    Integrity Master (tm)           - 79-        Data Integrity and Viruses

      4) Integrity Master as well as some other more recent anti-virus
         products will detect Concept and other more recent macro
         viruses.

     POLYMORPHIC VIRUSES

     To confound virus scanning programs, virus writers created
     polymorphic viruses.  These viruses are more difficult to detect by
     scanning because each copy of the virus looks different than the
     other copies.  Several virus authors have created tool-kits for
     other virus writers to use. The best known tool-kit is called the
     "Dark Avenger's Mutation Engine" (also known as MtE).  This allows
     someone who has a normal virus to use the mutation engine with
     their virus code.  If they use the mutation engine, each file
     infected by their virus will have what appears to be totally
     different virus code attached to it. Fortunately, the code isn't
     totally different and now anyone foolish enough to use the mutation
     engine with their virus will be creating a virus that will be
     immediately detected by most of the existing scanners.  Most of the
     viruses (such as Pogue, Dedicated, CoffeeShop, CryptLab, and
     Groove) which use the mutation engine pose little threat since they
     are all simple minded and rather buggy.  There are now several
     other tool-kits available to create polymorphic viruses such as the
     Trident Polymorphic Engine (TPE) and NED, but these have not
     resulted in significantly better viruses.  The polymorphic viruses
     that we actually see in the wild do not appear to be created using
     a polymorphic toolkit but were created from the ground up to be
     polymorphic.  Tremor, Maltese Amoeba, and Pathogen are examples of
     these viruses.  (Pathogen claims to use something called SMEG but
     we haven't seen this as a separate tool-kit.)  These viruses are
     all spreading quite widely since the scanners were late in
     detecting them. These viruses are now quite common.



    Integrity Master (tm)           - 79-        Data Integrity and Viruses
     VIRUS TOOL KITS

     Besides the polymorphic toolkits (e.g., the mutation engine), there
     are now several tool kits available to help people create viruses.

     HOW MANY PC VIRUSES ARE THERE?

     There are more PC viruses than all other types of viruses combined
     (by a large margin).  Estimates of exactly how many there are vary
     widely and the number is constantly growing.  In 1990, estimates
     ranged from 200 to 500; then in 1991 estimates ranged from 600 to
     1300 different viruses.  In late 1992, estimates were ranging from
     1000 to 2300 viruses. In late 1994 we had over 5,000 known viruses.
     Now in early 1996, we have over 8,000 different viruses in our
     collection but at least one person counts 12,000 viruses.  This
     confusion exists partly because it's difficult to agree on how to
     count viruses.  New viruses frequently arise from some idiot taking
     an existing virus that does something like put a message out on
     your screen saying: "Your PC is now stoned" and changing it to say
     something like "Donald Duck is a lie".  Is this a new virus?  Most
     "experts" say "yes."  This is a trivial change that can be done in
     less than two minutes resulting in yet another "new" virus.
     Another problem comes from viruses that try to conceal themselves
     from scanners by mutating.  In other words, every time the virus
     infects another file, it will try to use a different version of
     itself. These viruses are known as "polymorphic" viruses.  One
     example, the WHALE (a huge clumsy 10,000 byte virus) creates 33
     different versions of itself when it infects files.  At least one
     person counted this as 33 different viruses on his list.  Many of
     the large number of viruses known to exist have not been detected
     in the wild but probably exist only in someone's virus collection.
     Several authors of anti-virus products, including Mark Washburn and
     Ralph Burger, have written sophisticated viruses that are now on
     the loose, but other viruses that they created apparently exist
     only in virus collections.

     David M. Chess of IBM's High Integrity Computing Laboratory reports
     in the November 1991 Virus Bulletin that "about 30 different
     viruses and variants account for nearly all of the actual
     infections that we see in day-to-day operation."  We now find that
     about 60 different viruses account for almost all the viruses that
     actually spread in the wild.  How can there be only 60 viruses
     active when some "experts" report such high numbers?  This is
     probably because most viruses are poorly written and cannot spread
     at all or cannot spread without  betraying their presence.
     Although the actual number of viruses will probably continue to be
     hotly debated, what is clear is that the total number of viruses is
     increasing rapidly, although perhaps not quite as rapidly as the
     numbers might suggest.


    Integrity Master (tm)           - 81-        Data Integrity and Viruses

     HOW SERIOUS ARE VIRUSES?

     It's important to keep viruses in perspective.  There are many
     other threats to your programs and data that are MUCH more likely
     to harm you than viruses.  A well known anti-virus researcher once
     said that you have more to fear from a cup of coffee (which may
     spill) than from viruses.  While the growth in number of viruses
     now puts this statement into question, it's still clear that there
     are many more occurrences of data corruption from other causes than
     from viruses. So, does this mean that viruses are nothing to worry
     about? Emphatically, no!  It just means that it's foolish to spend
     much money and time on addressing the threat of viruses if you've
     done nothing about the other more likely threats to your files.
     Because viruses are deliberately written to invade and possibly
     damage your PC, they are the most difficult threat to guard
     against.  It's pretty easy to understand the threat that disk
     failure represents and what to do about it (although surprisingly
     few people even address this threat).  The threat of viruses is
     much more difficult to deal with.  There are no "cures" for the
     virus problem.  Why is this so?  We'll explore this in the next
     chapter on Protecting Your PC.


    Integrity Master (tm)           - 82-        Data Integrity and Viruses

                                 NOTES


    Integrity Master (tm)           - 83-        Data Integrity and Viruses

     CHAPTER TWO - PROTECTING YOUR PC
     ____________________________________________________________________

     HARDWARE PROTECTION

     Hardware is the foundation upon which your whole system is built.
     If you have more than one or two PC's, you probably owe it to
     yourself to buy some diagnostic programs.  If your PC is performing
     strangely or if a file is damaged, it's crucial to be able to
     determine whether hardware is the cause.  You probably don't want
     to call in a repair person each time something strange happens.
     Even if you have just one or two PCs, there are some modestly
     priced diagnostic programs that are worth having.

     One problem with diagnostic software (and hardware too, for that
     matter) is that when you run the diagnostics, everything may work
     perfectly, yet some time earlier there definitely was a problem.
     Intermittent problems like this are all too common.  Disk problems
     can be the most insidious in this respect.  When you run the
     diagnostics everything works fine.  How can you find out what's
     happening?  Run a comprehensive data integrity product (surprise)!
     This way you can find out if some data was damaged, but you don't
     have to spend days running diagnostics.  This also gives you early
     warning if your disk is just starting to have problems.

     If you haven't already, consider buying whatever you can to prevent
     your hardware from failing in the first place.  Buy surge
     protectors, keep your PC clean, and regularly clean the heads on
     your tape and diskette drives.  Be sure to protect your PC and
     keyboard from spilled coffee and similar threats.

     Your hard disk is going to fail!  It's not "if" but "when"!  It's
     absolutely vital to be able to deal with this threat.  Basic to
     dealing with this threat and most of the others is having backups.
     Please read the section in Chapter five on Backup Policy.  Your
     hard disk will most likely start performing erratically before it
     totally fails. It's essential to detect this as early as possible
     before much data gets damaged.  It will very likely NOT be obvious
     to you whether a hardware problem, software problem or a virus is
     damaging your files.  More on making this determination in the
     section in Chapter Five  titled Determining Causes of Corruption.


     "FIXING" YOUR DISK

     Damage to your files could be caused by hardware, software or who
     knows what.  When you are having the problem, your main concern is
     often not what caused it, but how to fix the damage.  This is where
     the disk utility programs offered by Gibson, Norton, Mace, and
     Central Point are often very handy.  They can sometimes take

    Integrity Master (tm)           - 84-        Data Integrity and Viruses
     unreadable data and extract some of it, or if you have logical
     damage to your disk such as cross-linked clusters, these programs
     (and DOS CHKDSK/SCANDISK) may be able to fix things for you.
     Unfortunately, things are not always fixed perfectly when these
     programs say they are.  Using a data integrity product (such as
     Integrity Master) will allow you to determine if everything really
     was put back together again.  More importantly, a data integrity
     product can be used to more accurately diagnose what is wrong to
     begin with, so you don't attempt a repair which actually makes
     things worse.

     GOOF PROTECTION

     Who has never accidentally deleted or copied onto the wrong files?
     Very few of us!  If you have a data integrity product (such as
     Integrity Master), a  utility package (Norton, Mace, PCtools, etc.)
     and current backups, you're all set.  You could probably do without
     the utilities, but it's rather convenient to be able to unerase
     files after you inadvertently delete the wrong ones (this is built
     into DOS 5 and later releases).  Of course, a backup program or an
     undelete utility won't help you if you didn't notice the incorrect
     delete when it happened and you now don't know what to restore or
     undelete.  That's why data integrity software is a vital component
     of handling this threat.


     INTRUSION PROTECTION

     This may not be an issue if you keep your PC locked in a vault when
     you're not using it, but otherwise you can never be sure that an
     intruder hasn't changed something on your PC.  Do you think I am
     exaggerating?  I am not!  The intruder may be your spouse or
     offspring.  They probably have no intention of changing anything
     but may be confused on how to use one of the programs on your PC,
     with the result that they inadvertently change the wrong file.  On
     the other hand, you may work in an environment where someone may
     want to deliberately do you harm or perhaps just "play a little
     joke" on you.

     There are programs available that modify the partition sector on
     your PC so that the hard disk is unavailable unless someone
     provides a password.  There are add-in boards that provide the same
     function. Some PCs (e.g., PS/2 PCs) come with a power-up password.
     You can lock the case to your PC to make it more difficult to open.
     You may wish to consider any of these options depending upon how
     much risk you face, but please realize that they can all be
     bypassed in less than ten minutes by a knowledgeable user.
     Surveillance cameras are regarded as a fairly good deterrent to PC
     tampering.

     While you can't totally stop someone from breaking into your PC,
     you can detect and correct the damage.  By using an integrity
     program that allows you to encrypt the integrity data or store the
     data off-line (on floppies), you can detect any illegal tampering,
     even from a technically advanced adversary.


    Integrity Master (tm)           - 85-        Data Integrity and Viruses

     VIRUS DEFENSES

     There are various methods in use to protect against viruses. What
     follows is a quick review of the viral defense mechanisms that are
     widely used today.


     SCANNERS

     Once a virus has been detected, it is possible to write programs
     that look for telltale code (signature strings) characteristic of
     the virus. The writers of the scanner then extract identifying
     strings from the virus.  The scanner uses these signature strings
     to search memory, files, and system sectors.  If the scanner finds
     a match, it announces  that it has found a virus.  This obviously
     detects only known, pre-existing, viruses.  Many so-called "virus
     writers" create "new" viruses by modifying existing viruses. This
     takes only a few minutes but creates what appears to be a new
     virus. It happens all too often that these viruses are changed
     simply to fool the scanners.

     The major advantage of scanners is that they allow you to check
     programs before they are executed.  Scanners provide the easiest
     way to check new software for old (known) viruses.  Since they have
     been aggressively marketed and since they provide what appears to
     be a simple painless solution to viruses, scanners are the most
     widely used anti-virus technique. (Integrity Master can of course
     be used as a pure scanner but we strongly suggest you allow it
     protect you fully by also utilizing its integrity checking
     capabilities.)

     Too many people seem to regard "anti-virus product" and "scanner"
     as synonymous terms.  The peril here is that if too many people
     depend solely upon scanners, newly created viruses will spread
     totally unhindered causing considerable damage before the scanners
     catch up with the viruses.  An example of this was the attack by
     the Maltese Amoeba (Irish) virus in the UK.  This virus was not
     detected prior to its destructive activation on November 1, 1991.
     Prior to its attack, it had managed to spread quite widely and none
     of the existing (mostly scanner-based) products detected this
     virus. According to the December 1991 Virus Bulletin:

     "Prior to November 2, 1991, no commercial or shareware scanner (of
     which VB has copies) detected the Maltese Amoeba virus.  Tests
     showed that not ONE of the major commercial scanners in use (the
     latest releases of Scan, Norton Anti-virus, Vi-Spy, VISCAN,
     Findvirus, Sweep, Central Point Anti-virus, et al.) detected this
     virus."

    Integrity Master (tm)           - 86-        Data Integrity and Viruses

     This incident points out the hazard of depending upon scanner
     technology or active monitor technology for virus protection.

     Another major drawback to scanners is that it's dangerous to depend
     upon an old scanner.  With the dramatic increase in the number of
     viruses appearing, it's risky to depend upon anything other than
     the most current scanner.  Even that scanner is necessarily a step
     behind the latest crop of viruses since there's a lot that has to
     happen before the scanner is ready:

     o The virus has to be detected somehow to begin with.  Since the
       existing scanners won't detect the new virus, it will have some
       time to spread before someone detects it by other means.

     o The newly discovered virus must be sent to the programmers to
       analyze and extract a suitable signature string.  This string
       must be tested for false positives on legitimate programs.

     o This string must be incorporated into the next release of the
       virus scanner.

     o The virus scanner must be distributed to the customer.

     o In the case of retail software, the software must be sent to be
       packaged, to the distributors, and then on to the retail outlets.
       Commercial retail software takes so long to get to the shelves,
       that it is almost certainly out of date.  Yet, many retail
       products depend upon their scanner for most of their
       effectiveness.


     If you depend upon a scanner, be sure to get the latest version
     directly from the author.  Also, be sure that you boot from a clean
     write-protected copy of DOS before running the scanner; there's a
     good chance that the scanner can detect a resident virus in memory,
     but if it misses the virus in memory, the scanner will wind up
     spreading the virus rather than detecting it.  Every susceptible
     program on your disk could be infected in a matter of minutes this
     way!


     DISINFECTORS

     Most vendors that sell scanners also sell a disinfector (sometimes
     it's the same program).  A disinfector has the same limitations
     that a scanner has, in that it must be current to be safe to use
     and it's always one step behind the latest crop of viruses.  The
     disinfector, however, has an even bigger disadvantage:  Many
     viruses simply cannot be removed without damaging the infected
     file.  There have also been numerous reports that files are still

    Integrity Master (tm)           - 87-        Data Integrity and Viruses
     damaged even when the program claims to have disinfected the file.
     A disinfector, like a scanner, can be a very handy tool in your
     anti-virus arsenal, but it must be used with care.  If you use a
     disinfector, be sure you have the latest version direct from the
     author and use an integrity check to verify that all files and
     system sectors are correctly restored.

     Currently, one of the oldest and most common infectors of files is
     the Jerusalem (1813) virus.  All disinfectors naturally claim to be
     able to remove this virus.  Yet the Jerusalem virus frequently
     overwrites part of the original file (due mostly to its many bugs)
     making it impossible to restore the infected program.  In spite of
     this, most (if not all) disinfectors claim to disinfect Jerusalem
     infected files.  A very dangerous situation!  I'd like to stress
     that:

       IT IS TOTALLY UNSAFE AND IRRESPONSIBLE TO DEPEND UPON
       DISINFECTORS AS A WAY TO RECOVER FROM VIRUS INFECTIONS.


     INTERCEPTORS

     Interceptors (also known as resident monitors) are particularly
     useful for deflecting logic bombs and trojans.  The interceptor
     monitors operating system requests that write to disk or do other
     things that the program considers threatening (such as installing
     itself as a resident program).  If it finds such a request, the
     interceptor generally pops up and asks you if you want to allow the
     request to continue.  There is, however, no reliable way to
     intercept direct branches into low level code or to intercept
     direct input and output instructions done by the virus itself.
     Some viruses even manage to disable the monitoring program itself.
     It is important to realize that monitoring is a risky technique.
     Some products that use this technique are so annoying to use (due
     to their frequent messages popping up) that some users consider the
     cure worse than the disease!  An interception (monitoring) product
     would be a useful adjunct to a data integrity program, as
     protection against some the more simple minded logic bombs.


     INOCULATORS

     There are two types of inoculators or so-called "immunizers." One
     modifies files or system sectors in an attempt to fool viruses into
     thinking that you are already infected.  The inoculator does this
     by making the same changes that the viruses use to identify the
     file or sector as infected.  Presumably, the virus will not infect
     anything because it thinks  everything is already infected.  This
     works only for a very small number of viruses.

     The second technique is actually an attempt to make your programs
     self-checking by attaching a small section of check code onto your

    Integrity Master (tm)           - 88-        Data Integrity and Viruses

     programs.  When your program executes, the check code first
     computes the check data and compares it with the stored data.  It
     will warn you if it finds any changes to the program. Not only can
     this be circumvented by existing stealth viruses, but the
     self-checking code and check data can be modified or disabled as
     well.   Another problem arises because some programs refuse to run
     if they have been modified in this way.  This also creates alarms
     from other anti-virus programs since the attached self-check code
     changes the original program in the same way a virus would. Some
     products use this technique to substantiate their claim to detect
     unknown viruses.


     ROM AND ENCRYPTION

     Placing executable code on a hardware write-protected device, will
     protect all those programs on that device.  Some PCs provide DOS in
     ROM (Read-only Memory). This provides some degree of protection,
     but all the other programs are still vulnerable to infection.  The
     more programs you can isolate on a write-protected device, the more
     effective this technology is. It's important to note, that
     write-protected devices such as CD-ROMs can contain infected
     programs that can infect programs on your hard disk.  In other
     words, the CD will not become infected while on your system but it
     can contain a pre-existing infection that can spread to your PC.

     Encryption is a promising technique that so far has not been
     successfully used to protect a system.  Encrypting as many of your
     files as possible makes life harder for viruses, but does not stop
     them since there is always some unencrypted code around (boot
     sector, BIOS, DOS, device drivers, etc).


     INTEGRITY CHECKERS

     Integrity check based products work by reading your entire disk and
     recording integrity data that acts as a signature for the files and
     system sectors.  A quality integrity check program is the only
     solution that can handle all the threats to your data along with
     viruses.  Integrity checkers also provide the only reliable way to
     discover what damage a virus has done.  A well-written integrity
     checker should be able to detect any virus, not just known viruses.
     So, why isn't everyone using an integrity checker?  Well, until
     recently, there hasn't been an integrity checker available without
     some significant drawbacks.  In fact, many anti-virus products now
     incorporate integrity checking techniques.  One problem with many
     products is that they don't use these techniques in a comprehensive
     way. There are still too many things not being checked. Some older
     integrity checkers were simply too slow or hard to use to be truly
     effective. A disadvantage of a bare-bones integrity checker is that
     it can't differentiate file corruption caused by a bug from
     corruption caused by a virus.  Only recently have advanced
     integrity checkers (e.g., Integrity Master) become available that
     incorporate the smarts to analyze the nature of the changes and
     recognize changes caused by a virus.  Some integrity checkers now
     use other anti-virus techniques along with integrity checking to
     improve their intelligence and ease of use.

    Integrity Master (tm)           - 89-        Data Integrity and Viruses

     If you choose an integrity checker, be sure it has all these features:

     o It's easy to use with clear, unambiguous reports and built-in help.

     o It hides complexity, so that complicated details of system file
       or system sector changes are only presented if they present
       information the user must act upon.

     o The product recognizes the various special system files on the PC
       so it can alert the user with special warnings if vital files
       have changed.

     o It's fast.  An integrity checker is of no use if it's too slow to run.

     o It recognizes known viruses, so the user doesn't have to do all
       the work to determine if a change is due to a software conflict,
       or if it's due to a virus.

     o It's important that the integrity computation be more
       sophisticated than a mere checksum.  Two sectors may get reversed
       in a file or other damage may occur that otherwise rearranges
       data in a file.  A checksum will not detect these changes.

     o It's comprehensive.  Some integrity checkers, in order to improve
       their speed, don't read each file in its entirety.  They read
       only portions of larger files.  They just spot check.  This is
       unacceptable -- it's important to know the file hasn't changed,
       not just that some of the file hasn't changed.

     o It checks and restores both boot and partition sectors.  Some programs check only files.

     o It stores the integrity data in a secure (tamper-proof) manner
       and optionally stores it on a removable medium (e.g., a
       diskette).

     (Fortunately, Integrity Master does all these things. <smile>)


    Integrity Master (tm)           - 90-        Data Integrity and Viruses

     GADGETS (Hardware protection)

     There are currently some gadgets (hardware devices) that are sold
     as virus protection.   So far, I haven't seen anything that
     provides protection beyond what is offered by software-only
     products.  Beyond putting some of the anti-virus code in read-only
     memory (ROM), I've seen little that can be accomplished by existing
     hardware.  In one product, the hardware was used to store some
     integrity data; a floppy disk can do the same thing and it's
     actually more secure.


     PREVENTION:

     Hardware techniques, such as placing all your programs in read-only
     memory (ROM), can, in theory, provide virus prevention, but nothing
     even comes close to doing this yet.  Pure software techniques can
     probably not prevent all viruses.  There are all sorts of schemes
     that make it more difficult for a virus to penetrate your system,
     but none totally eliminate the threat of a virus.  For each
     software-based technique, there is a way a virus could circumvent
     it.  Software helps a lot, but isn't absolute protection.  While
     prevention of viruses may not be possible, detection is.
     Detection, if applied carefully, can detect all viruses, no matter
     how tricky.  If viruses are detected before they spread, the most
     serious aspect of the virus threat is eliminated. If integrity
     checking (detection) is practiced widely, the threat of a virus
     spreading to millions of PCs and then years later performing a
     destructive act can be eliminated.


    Integrity Master (tm)           - 91-        Data Integrity and Viruses

     CHAPTER THREE - VIRUS MYTHS
     ____________________________________________________________________


     MYTHICAL SOURCES

     Attachment to a network or BBS

       Simply being attached to a network (such as CompuServe, or
       Internet), a bulletin board system (BBS), or even a local area
       network (LAN) will not make you susceptible to viruses.  The only
       way you can get a virus is to execute a program on your PC that
       you obtained over the network.  The mere act of downloading the
       program is harmless; it's only by downloading and then executing
       an infected program that your PC can become infected.  I hope
       it's clear that the mere act of reading electronic mail cannot
       infect your PC.

       There is one thing that can happen though.  If you have the
       device driver ANSI.SYS (or an equivalent) loaded (in your
       CONFIG.SYS file), someone could send a sequence of characters to
       your screen (ANSI sequence) that assigns a set of key strokes to
       a key on your keyboard. These keystrokes could easily be
       something harmful like "DEL *.*".  When you press the key that
       was reassigned, the command would execute just as if you had
       typed it yourself. This "practical joke" could cause some
       trouble, but it certainly can't reproduce and isn't a virus.

     From Data

       Since data is not executed, you cannot become infected from data.
       If someone sent you a data file that contained a virus, you would
       have to rename the file and then execute it to become infected!
       You can, however, become infected from a diskette that is not
       bootable and contains no (apparent) programs.  The explanation
       for this is that all diskettes have a boot sector that contains a
       program that can become infected by a boot sector virus.  If you
       leave such an infected diskette in your drive when you power up
       or boot, your PC will be infected!

     From CMOS Memory

       PC AT (80286) type computers and later models contain a small
       amount of battery backed CMOS memory to store the configuration
       and to maintain the time and date.  This memory is never
       executed, so although it could be damaged by a virus, you can
       never become infected from CMOS memory.  While no virus will
       infect your CMOS, there are several that will change or erase
       your CMOS data.

    Integrity Master (tm)           - 92-        Data Integrity and Viruses

     QUICK AND EASY CURES

     I've discussed the various approaches to the virus problem, and
     you've no doubt seen that there are no instant cures for viruses,
     yet many products make claims that they can't quite support.
     Everyone would like to just buy product X, run it, and be rid of
     viruses forever. Unfortunately there is no such easy cure.


     SILLY TRICKS

     There have been many articles and books written by various virus
     "experts" that propose doing all kinds of things to virus proof
     your PC.  Here are some of the tricks that I consider most
     widespread and most useless:

     WRITE-PROTECTING YOUR FILES

       You can use the DOS ATTRIB command to set the read-only bit on
       files. This is so easy for a virus (or any program) to bypass,
       that it simply causes far more problems than it cures.

     HIDING OR RENAMING COMMAND.COM

       COMMAND.COM is a program that executes each time you boot your
       PC.  There was an early virus that only infected COMMAND.COM, so
       the idea of hiding or renaming this file began.  Today, many
       viruses actually go out of their way to avoid infecting this
       file, since some anti-virus products single out this file and a
       few others for special scrutiny. With today's viruses, hiding
       COMMAND.COM is utterly futile.

     CHECKING TIME AND DATE STAMPS

       While it's helpful to check the time and date stamps of your
       executable files for unexpected changes, this is not a reliable
       way to catch viruses.  Many viruses are smart enough not to
       change the time and date stamps when they infect a file.  Some
       viruses even hide the change to a file's size when they infect a
       file.

     RETAIL SOFTWARE ONLY?

     Several "virus experts" have suggested that users avoid downloading
     software and avoid shareware.  There are no facts to support this
     viewpoint.  The most common viruses are boot sector viruses such as
     Stoned and Michelangelo that spread when someone boots from an
     infected diskette. To spread these viruses, a physical disk must be
     passed around and then booted.  Michelangelo spread widely because
     software distribution disks were infected with this virus.  There
     was no reported incident of this virus spreading via shareware.  It
     is, of course, wise to make sure that you download your software
     from a source that screens each program for known viruses.  You are
     actually more likely to be infected from software purchased at a
     retail outlet than from shareware.  Quite a few viruses have been

    Integrity Master (tm)           - 93-        Data Integrity and Viruses

     shipped directly from the software manufacturer in the shrink
     wrapped packages.  One major software company has on at least two
     separate occasions shipped a virus with their product.  Buying
     shrink wrapped retail software is much more dangerous than many
     people think it is, since many retailers accept returned software
     and then simply rewrap the software and sell it again.  This
     software could have easily been infected by the first user who
     tried it and then returned it.

     WRITE-PROTECTING YOUR HARD DISK

     There are several programs that claim to write-protect your hard
     disk. Since this is done in software, it can be bypassed by a
     virus.  This technique, however, will stop a few viruses and will
     protect your disk from someone inadvertently writing to it. These
     programs are generally less effective than the virus interception
     products.

     It IS possible to write-protect a disk using hardware, but this
     does not seem to be readily available.


     VIRUSES ARE THE BIG THREAT?

     As we've seen in examining the other threats to the integrity of
     your data, viruses are among the less likely threats that you face.
     Don't protect yourself against viruses and ignore the other
     threats!

    Integrity Master (tm)           - 94-        Data Integrity and Viruses

     SAFE COMPUTING (SAFE HEX?)

     You may have heard this rumor: "You don't need an anti-virus
     product, just backup your disk regularly and keep an eye on your
     programs."   Yes, it is vital to have good backups, but that is no
     longer enough.  You may also have heard that provided you don't
     share programs or download (practice "safe hex"), you have nothing
     to worry about.  This is no longer sufficient protection; every
     time you buy a software package you are exposing yourself to virus
     infection. It is not possible to be safe from viruses by secluding
     your PC!

     There are now some viruses that can do considerable damage.  The
     worst ones damage your files slowly so even your backups may be
     useless unless you detect the damage before it's too late.
     Although viruses may not be very likely to attack your system when
     compared to other threats, they do represent a very real and very
     dangerous threat -- a threat you cannot ignore or combat merely
     with good backups, seclusion, or common sense.


    Integrity Master (tm)           - 95-        Data Integrity and Viruses

     CHAPTER FOUR - VIRUS REALITIES
     ____________________________________________________________________


     THE ONLY REAL SOURCE OF VIRUSES

     You can't get a virus merely by being connected to a network or
     bulletin board system (BBS).

     There is only one way you can get a virus and that's to execute a
     program containing a virus.  Period.  End of story.  Well, almost
     the end of the story.  What some people don't know is that every
     disk and diskette has a program on it, even if it appears empty.
     This program is in the boot sector.  Most people don't think of
     boot sectors as programs or perhaps even know that boot sectors
     exist.  If you leave a data diskette in your A drive and boot your
     PC, you could be executing an infected program in the boot sector,
     thereby infecting your PC with a virus.  Make sure you NEVER boot
     from a diskette unless it's a known good copy of DOS.


     SHAREWARE IS AS SAFE OR SAFER

     There is no reason to avoid shareware.  If you want to get the
     latest anti-virus software, it's easiest to get it as shareware
     since you are buying directly from the author. Shareware does not
     have to go from the author to the publisher, then through the
     distribution chain before it even gets to sit on the shelf.  Who
     knows how long your retail package has been on that shelf?


     FEW VIRUS FREE PROGRAMS

     Unfortunately, there is no way to look at a program (unless you
     wrote the program yourself in assembly language) and positively
     declare there's no virus in it.  All you can say is that the
     program contains no known virus.  You never know what may be
     lurking inside of a program waiting for just the right trigger to
     begin infection or perhaps an attack.

     While you can't be sure of detecting a virus while it's inert
     inside a program, you definitely CAN detect it as it infects or
     attacks your files.  The changes which must be made by a virus can
     always be detected with the appropriate software.


    Integrity Master (tm)           - 96-        Data Integrity and Viruses

     OTHER CAUSES MORE LIKELY

     Viruses are not the greatest threat to your data, so let's not
     forget about the other threats too.


     WRITE-PROTECTING FLOPPIES

     While write-protecting your files and your hard disk is of
     questionable value, you definitely CAN write-protect your floppy
     disks.  Just cover the notch on the 5.25 inch diskettes, or on 3.5
     inch diskettes, slide the little tab to expose the hole.  The only
     risk here is that some diskette drives may be defective and still
     allow writing on the diskette.  If in doubt, do a test and check
     out your drive.


     BEWARE THE CE AND THE DEMO!

     According to our reports, one of the major sources for infections
     is the customer engineer (CE) or repairman.  The CEs frequently
     carry diagnostic diskettes with them when they go from PC to PC on
     service calls.  It's all too easy for these diskettes to become
     infected.  Sales people doing demos on various PCs are also very
     susceptible to getting their demo diskettes infected.

    Integrity Master (tm)           - 97-        Data Integrity and Viruses

     CHAPTER FIVE - WHAT TO DO?
     SOME SUGGESTIONS:
     ____________________________________________________________________


     ACTION IS VITAL - NOW!

     Too many people wait for a virus to attack their PC before they
     take any action.  Once a virus reveals its presence on your PC, it
     may be too late to recover damaged files.  There are many viruses
     that cannot be successfully removed due to the way the virus
     infects the program. It's absolutely vital to have protection
     before the virus strikes.

     It's vital that you protect against all threats to data integrity,
     not just viruses.  All threats to data integrity are much easier to
     deal with if they are detected as early as possible.  If you wait
     until you notice that your hard disk is losing data, you may
     already have hundreds of damaged files.


     BACKUP POLICY

     It's essential to carefully protect all your software and regularly
     backup the data on all your disks.  Do you have a single disk that
     you can afford NOT to regularly backup?  It's rare to find any PC
     that does not have some type of important data stored on it.

     SUGGESTED BACKUP POLICY:

     1) All original software (program) diskettes should immediately be
        write-protected, copied and stored in two secure, separate,
        locations after installation.  If you are using an integrity
        check program, immediately record (initialize) the integrity
        data for the new programs after installing.

     2) Determine a schedule for full backups by considering how
        frequently your data changes.  It is an excellent idea to have
        three full sets of backup tapes or diskettes and to store one
        set at another location to protect against fire, theft, or some
        other disaster.  If your data is critical, you may wish to have
        a separate cycle of backups (e.g., quarterly or yearly) that can
        be used to recover when someone damages (or deletes) a vital
        file, but the deletion isn't discovered until months later.

     3) The full backups should be coordinated with periodic incremental
        backups.  The incremental backup, which copies just the files
        that have changed, normally runs very quickly and takes just a
        minute or so.  Many people find that an incremental backup run
        at the end of each day works quite well.  This way their data is
        protected should anything happen overnight.


    Integrity Master (tm)           - 98-        Data Integrity and Viruses
     4) Make sure you use reliable backup hardware and software.
        Periodically test by restoring from a backup.  Too many people
        have discovered that their backup program couldn't recover their
        files when it was too late.  If you use an integrity check
        program you can verify that the restored files are correct.


     INTEGRITY CHECKING POLICY

     Each PC which has data that you can't afford to lose or have
     corrupted should have a schedule of regular integrity checking,
     similar to the backup schedule.  By doing once a week full
     integrity checks, you can stay one step ahead of any trouble.  By
     doing a quick update of your integrity data on a daily basis, you
     can stay aware of exactly what changes in your PC and why.  This
     way if you start to encounter a software conflict, a failing hard
     disk, or a virus, you'll be able to quickly differentiate the
     unusual changes from the usual ones.

     Whenever you install new software, immediately record the integrity
     data for those programs, so that any future infection or damage can
     be detected.

     Whenever you copy programs, check that the new programs are exact
     copies of the originals.  The easiest way to do this is to always
     copy integrity data along with the programs.  You can also use any
     integrity checker, checksum program, CRC program, cryptographic
     signature program, or even the DOS COMPARE utility to verify that
     you made good copies.  Do this check only when you know no virus is
     in control of your PC; therefore, it's best to cold boot from a
     write-protected floppy to verify your program copies are good.  A
     good scanner such as Integrity Master will verify that no known
     viruses are in memory but it's nice to have assurance that no
     unknown viruses are present.

     If you have diagnostic software, plan to run it at intervals. If
     you leave your PCs turned on at night, why not leave them running
     diagnostics?

     RUN CHKDSK OR SCANDISK

     Run CHKDSK, (or some equivalent program such as NDD or SCANDISK)
     regularly on each PC, and pay attention to the results.  If you are
     seeing problems, be sure you understand what's causing the
     problems.  If you are experiencing cross-linked or lost clusters,
     something is being damaged.  Run an integrity checker to find out
     exactly what is being damaged.  Also pay attention to the amount of
     available memory.  If this suddenly changes with no new resident
     (TSR) software installed, you may have a virus.

    Integrity Master (tm)           - 99-        Data Integrity and Viruses

     DETERMINING CAUSES OF CORRUPTION

     It's not a question of "if" but a question of "when"; all too soon
     you are going to encounter a damaged file (a file that has changed
     for unknown reasons).  How can you discover what caused the damage?

     o First gather as much information as possible.  Did you do
       anything unusual?  Did you install any new software?  Did you
       execute any programs that you don't normally use?  Have you seen
       any signs of hardware problems? (See the section following on
       signs of hardware problems).

     o Run CHKDSK or Scandisk to see if your directories and other areas
       are OK.

     o Run a full integrity check to see if anything else has changed.

     o If you suspect hardware problems as the culprit, then run any
       diagnostic programs you have.  If the diagnostics don't turn
       anything up, but you still suspect a hardware problem, then run
       your integrity check in full check mode daily for a while.  This
       should help track down exactly what's happening in your PC.

     o If you suspect software problems, run the software in question
       and then run your integrity check to see if anything is being
       corrupted. When doing this, it's very helpful to duplicate the
       original situation of the problem as closely as possible. Make
       sure the hardware is the same and that you have exactly the same
       resident programs and device drivers loaded as when the problem
       first occurred.

     o Could the problem be a virus?  If you think so, have you seen any
       of the signs of virus activity listed in the next section?  Are
       only executable files (such as files ending in .EXE, .COM, .OVR,
       .OVL .BIN, or .SYS) affected?  If so, how many?  If more than one
       or two unrelated program files have mysteriously changed, it
       could likely be a virus.  Remember that some programs (such as
       WordStar and SETVER) modify themselves as part of normal
       execution.  If the programs have changed but the DOS time and
       date stamps haven't, this is further reason to suspect either a
       serious problem or a virus.  If you are not using an advanced
       integrity checker  (such as Integrity Master) that recognizes
       known viruses, you may wish to get a virus scanner at this point
       to see if you have a known virus.  If this turns up nothing, then
       it's time to play detective - you may have discovered a brand new
       virus (lucky you!).  Please see the section in Chapter Seven on
       Playing Detective.


     EDUCATION

     One very important thing that you can do to assure the integrity of
     the data in your PCs is to educate everyone who uses a PC.  It's
     vital that they understand how to backup their files and which

    Integrity Master (tm)          -100-        Data Integrity and Viruses
     files normally change on their PC and which ones don't.  If you can
     teach them to understand the output of a thorough integrity check
     program, then you'll be able to sleep at night knowing that all is
     well with your PCs! Even lacking an integrity check program, it's
     vital that everyone be aware of what problem signs to look out for.
     This way the more dangerous threats to data integrity will not go
     unnoticed.




     SIGNS OF HARDWARE PROBLEMS

     Watch out for recurring error messages that the disk is not ready
     when you try to boot the PC.  If you periodically experience any
     type of disk-error message, or if disk accesses seem to be getting
     consistently slower, you may be experiencing the beginning of a
     serious disk problem.


     SIGNS OF SOFTWARE PROBLEMS

     These symptoms could reveal software conflicts or bugs:

     o CHKDSK or Scandisk reporting problems.

     o A file that was just processed by a program (such as a
       spreadsheet) is damaged or unreadable by the program but you can
       copy the file with no error messages.


     SIGNS OF VIRUSES

     These symptoms may betray the existence of a virus:

     o Disk activity when there should not be any activity. (Some disk
       caches cause this to happen normally.)

     o Programs taking longer to load but the disk drive appears to be
       healthy.

     o Any unexplained behavior on the PC such as music, bouncing balls,
       black areas on the screen, falling letters, weird messages, or
       unexplained slowdown of the PC.

     o Less total or free (available) memory on your PC (use CHKDSK or
       MEM).  This should change only when you add new resident programs
       or device drivers.  Note, most PCs have 655360 total bytes of
       memory but certain models (i.e., some PS/2s) reserve a thousand
       bytes of high memory.

     o Unexplained bad spots on your disk or fewer total bytes (as
       reported by CHKDSK).

     o If you find extra executable files (e.g., ".COM" files) showing
       up, you may have a companion style virus.

    Integrity Master (tm)          -101-        Data Integrity and Viruses

     RESPONSIBILITY

     If you are in a larger organization, it's crucial that someone has
     the responsibility for assuring data integrity.  The first task
     facing this person would be to assure that all important data is
     backed up and that all users are educated with respect to normal
     operation of their PC. The next step would be to start a regular
     program of integrity checking.


     POLICY AND ROUTINE

     The procedures for backing up and checking the integrity of
     critical data cannot be left to word of mouth, but should be
     clearly explained in a written set of procedures.  Data integrity
     is too important to leave to chance.  If this isn't done, guess
     what gets put on the back burner (in other words: not done), when
     people get busy? (Who isn't busy?). Some recommended procedures:

     o Never leave a floppy disk inserted in a drive longer than
       necessary. Remove all diskettes immediately.  This reduces the
       chance of
       inadvertently booting from the diskette and picking up a boot
       sector virus.

     o Check the integrity of all files after installing new software or
       copying programs.

     o If a stranger (such as a sales or repair person) runs software on
       a PC, do a full integrity check immediately afterwards.

     o Immediately write-protect and backup all diskettes containing
       software.

     o Schedule regular incremental and full backups.


     NETWORKS AND VIRUSES

     Make sure that any shared executable files allow only execute or
     read access.  Execute-only is best, but it's essential not to allow
     write access.  Most network compatible programs allow you to store
     the files they write to on separate disks from the programs
     themselves. Be sure to limit write access with access rights not
     with file attributes (Netware FLAG or FLAGDIR).  A virus can easily
     bypass file attributes, but access rights can thwart the virus's
     attempts to write to the shared disk.  The LAN administrator needs
     to have two accounts -- one privileged and one not.  For normal
     use, the LAN administrator should use the less privileged account.
     The privileged account should be used only  when the job requires
     supervisor rights.  It's critical that any user with supervisory
     rights log off as soon as possible and never execute any other
     programs, especially those on a workstation.


    Integrity Master (tm)          -102-        Data Integrity and Viruses

     Run regular integrity checks on the file server.  This is important
     on the workstations too, but is critical on the file server since
     an infected file here could quickly infect all the workstations on
     the network.

     Never access an unchecked workstation with network administrator
     (supervisor) authority!


     GUIDELINES FOR USING ANTI-VIRUS PRODUCTS

     Most modern anti-virus products use a combination of the techniques
     I just mentioned.  Unfortunately, most products still get almost
     all of their protection from their scanner component. It's vital to
     understand exactly how your product works so that you understand
     what type of protection you really have.  Here are some rules that
     will help you make sure that you get maximum protection out of
     whatever product you already have:

     o Be sure to cold boot your PC from a write-protected diskette
       before virus checking.  This provides the best protection against
       unknown resident viruses.  Most anti-virus products make this
       recommendation, but this rarely gets done because the
       recommendation is often buried in some obscure location in the
       documentation.  If your PC is infected with a virus that your
       scanner does not recognize, you could infect all the programs on
       your disk. Don't take this chance; boot from a write-protected
       diskette before you scan. (IM version three offers a resident
       program check as an alternative to cold booting.)

     o If you are using a product which depends mostly on its scanner
       component, make sure that you always have the latest version.
       Scanners are often updated every 30 to 60 days.

     o Before you execute or install any new software, check it first.
       If it comes with an install program, check again after you
       install the software; an install program will frequently change
       or decompress executable programs.  After you first execute brand
       new software do an additional check of your system to make sure
       everything is as it should be.

     o If your product contains a scanner component, consider checking
       the boot sector on all diskettes brought in from another location
       -- EVEN DATA DISKETTES!  Inevitably someone will leave one of
       these diskettes in their A drive, potentially spreading a boot
       sector virus.


    Integrity Master (tm)          -109-        Data Integrity and Viruses

      (Note: pages 103 to 108 are not included in this file.)

      CHAPTER SEVEN - HANDLING A VIRUS ATTACK
      ____________________________________________________________________


     DON'T PANIC

     Don't do anything rash if you suspect a virus attack.  Be
     skeptical, there are quite a few practical joke programs that
     behave exactly like viruses.  There's even a virus simulator that
     simulates the Ping Pong (bouncing ball), Jerusalem (black hole),
     Cascade (falling letters on the screen), Yankee doodle (music) and
     a few other viruses.  It's perfectly harmless, but it has alarmed
     many people.  Don't do anything drastic until you confirm that it
     really is a virus.


     REPORT THE ATTACK

     Report the virus attack to the police or to a virus researcher or
     anti-virus developer.  We need to stop sweeping this under the rug.
     If we can track where viruses first get started, then maybe we can
     apprehend the culprits who are writing and distributing these
     things.


     PLAY DETECTIVE

     It is very important that you track down how you got the virus.  If
     you got it from someone's software, it's vital that they be
     notified.  The sooner these viruses are detected, the less damage
     they can do.

     Suppose you have indications of a virus, but your software doesn't
     identify it as a known virus.  What do you do?  First, cold boot
     (press the red reset button or power off and back on) from a known
     good write-protected copy of DOS on a diskette.  Run a full
     integrity check. Run CHKDSK and print the results.  Now execute any
     suspect programs.  Execute them several times.  Viruses may wait
     for some trigger event to begin infection.  Run CHKDSK again to see
     if the amount of free memory has been reduced.  This is a sign of a
     virus going resident in memory.  Now cold boot again and rerun an
     integrity check.  Repeat this cycle with the various suspect
     programs.  This should track down the guilty program if you've got
     one.

     Keep in mind that if it's a virus, it will modify other programs
     and those programs should themselves further modify other programs.
     By executing the modified programs, it's possible to tell whether
     you really have a virus or you just have a buggy program that is
     accidentally writing to other programs.

    Integrity Master (tm)          -110-        Data Integrity and Viruses

     CLEAN HOUSE

     Follow these steps when removing a virus from your PCs:

     o Cold boot (Power off and on or press the reset button) from a
       known good write-protected copy of DOS.

     o Delete all infected files.

     o Reload any infected system sectors.  If you do not have a utility
       to reload the DOS boot sector, you can use the DOS "SYS" command
       after cold booting from a write-protected diskette (e.g., "SYS
       C:").

     o Rerun a full integrity check, or at least a scan if you don't
       have an integrity checker.

     o Check any floppies that may have been infected. Remember, if you
       have a system sector virus such as Stoned, Joshi or Brain, even
       empty data diskettes can be infected.  Check them all.

     o Notify any other PC users you have contact with to check their
       PCs.


     GUARD THE HOUSE

     Virus infections return in a very high number of cases.  This is
     usually because somewhere there is an infected file or diskette
     that was missed in the first cleaning.  Run your integrity checker
     or antivirus program daily, for the next month, to catch a possible
     repeat infection.


This file is a portion of the book "Defeating Viruses and Other Threats
to Data Integrity" that accompanies the registered version of Integrity
Master. All portions of this file are copyright by Stiller Research
(1990-1996) and no portion of this text may be used or quoted without
written permission from Stiller Research.