ARCDIAG

                           ARCNET DIAGNOSTIC PROGRAM
                                       
                                  USER GUIDE
                                       
                                       
                                       
                                  Version 2.2
                                       
                                       
                                       
                                 For use with
                      Novell Netware/SM/RX Type Networks
                                               
                                       










                           (c) Copyright 1986, 1989
                                      by
                              Olympic Software Co
                             2601 S. State Street
                             Ann Arbor, MI  48104
                                (313) 994-3666
                                       
                              All Rights Reserved
                                   Worldwide



INTRODUCTION

The ARCDIAG program is designed to be a service tool for network
administrator personnel for a network that uses ARCNET type
hardware (see specifications section for compliance).   The ARCDIAG
program includes two diagnostic sections that will help during
installation of an ARCNET network.  The diagnostic software can be
operated at any workstation during installation of the network or
at any time while running the Novell Network Operating System.

            NOTE: The ARCDIAG program is not intended to
            isolate Novell Software problems except in
            those cases where the physical network
            hardware is the prime cause of the problem.

The program exercises the network card by testing all of its
internal functions, RAM, RIM etc., and then displays a map of
active nodes and packet counts.  The latter also provides an
indication of any reconfiguration that might be occurring.


THE DISTRIBUTION SET

The files contained in the distribution set are:

	ARCDIAG.EXE	The executable ARCDIAG file

	ARCDIAG.DOC	This documentation file

	ARCDIAG.WP5	Documentation file in Wordperfect 5.0 format


USAGE/COPYING LICENSE 
 
The software described herein and the accompanying documentation
is copyrighted and the sole property of Olympic Software Co. 
 
The information in this document is subject to change without
notice and should not be construed as a commitment by Olympic
Software.  Olympic Software assumes no responsibility for any
errors that may appear in this document.

The software described in this document is furnished under license
and may only be used or copied in accordance with the terms of such
license.


WHAT IS SHAREWARE

Computer users and programmers have been exchanging software since
the dawn of computers. Only recently, however, has the concept
blossomed into an effort to provide low-cost alternatives to
conventional commercially marketed software.  Known as Shareware,
this concept provides a source of high quality software products
to users, and permits them the opportunity to "try before you buy".
Also, because expensive advertising and distribution costs are
avoided, the cost of Shareware tends to be significantly lower than
for a commercial product of equivalent quality and functionality.
Shareware authors hold copyrights on their programs.  Just as for
commercial software, the Shareware author's software is protected
by U.S. and international copyright law.

Shareware, unlike its commercial counterpart, may be freely copied
and passed to others.  Like commercial software, Shareware is a
"for-sale" product and Shareware authors request or require that
people who try their software and decide to use it send a
"registration fee" (approximately equivalent to purchasing the
software).  In addition to granting a license to use the product
for this registration fee, authors offer a wide variety of services
to include (depending on the program) printed documentation, disks,
advanced versions, and/or telephone support.  Some companies also
offer free updates and commissions.  But, the most important
benefit of registration is that you receive a legal license to
continue using the software. 


Some Shareware authors have formed the Association of Shareware
Professionals (ASP) dedicated to establishing recognized standards
for Shareware programs and authors.  The authors share a code of
ethics and have agreed to adhere to the ASP's standards for
software and documentation.  The ASP is also striving to help disk
dealers, the media, and the public to understand the nature and
benefits of Shareware.  Through cooperation and mutual standards,
the ASP hopes to promote Shareware as a viable alternative to
commercial software.  Not all authors belong to ASP, but as more
join, Shareware standards will be more universally followed. 

	Your Rights and Obligations
	
	License 	A limited license is granted to freely use, copy and
                  distribute the product subject to the following
                  restrictions:  

	YOU MAY NOT

		Sell and/or distribute the product for a fee, either
            alone or along with other products, without express
            written permission of the copyright holder. 

		Grant sublicense, leases, or other rights in the software
            to others. 

		Modify or remove the Copyright notice from the program,
            diskette or the documentation. 
		
		Modify the program, diskette or documentation and/or
            merge it into another program or product for any machine.
            
 

	Distribution
	    ARCDIAG is specifically authorized for distribution,
            under the SHAREWARE principle, via public electronic
            bulletin boards or by individual copying. Any
            distribution thus made must be in the form of this entire
            .ARC file, UNALTERED, including the program executable
            files, data files, and this or any other accompanying
            documentation files. NO OTHER FORM OF DISTRIBUTION,
            INCLUDING DISTRIBUTION AS PART OF A LARGER PACKAGE, NOR
            DISTRIBUTION FOR A FEE (other than a nominal copying
            charge not to exceed $10.00), IS AUTHORIZED WITHOUT
            SPECIFIC WRITTEN PERMISSION OF THE COPYRIGHT HOLDER. 
 

	Limited Warranty 
	    THE PROGRAM IS PROVIDED "AS IS" WITHOUT WARRANTY OF ANY
            KIND, EITHER EXPRESSED OR IMPLIED, INCLUDING BUT NOT
            LIMITED TO THE IMPLIED WARRANTIES OF MERCHANTABILITY AND
            FITNESS FOR A PARTICULAR PURPOSE. THE ENTIRE RISK AS TO
            QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH YOU.
            SHOULD THE PROGRAM PROVE DEFECTIVE, YOU ASSUME THE ENTIRE
            COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.
            SOME STATES DO NOT ALLOW THE EXCLUSION OF IMPLIED 
            WARRANTIES SO THE ABOVE EXCLUSION MAY NOT APPLY TO YOU.
            THIS WARRANTY GIVES YOU SPECIFIC LEGAL RIGHTS AND YOU MAY
            ALSO HAVE OTHER RIGHTS WHICH VARY FROM STATE TO STATE. 
 
	Limitation of Remedies 
	    IN NO EVENT WILL OLYMPIC SOFTWARE CO. BE LIABLE FOR ANY
            DAMAGES INCLUDING ANY LOST PROFITS, LOST SAVINGS OR OTHER
            INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF THE
            USE OR INABILITY TO USE SUCH PROGRAM EVEN IF OLYMPIC
            SOFTWARE HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH
            DAMAGES OR ANY CLAIM BY ANY OTHER PARTY. 
 
 
	Software/Shareware Dealers and Distributors 
	    Please write to the Author for permission to include this
            product in your collection PRIOR TO offering it for sale
            or distribution. Inquiries are encouraged, and will be
            responded to as quickly as possible. 
 
START UP

	The program can be run from the DOS prompt by typing:

	ARCDIAG  [-mxxxx] [-ixxxx] [-ffile descriptor] [-ttype] [-b] 

	Start Up Options: 

		-b	      Option for removing the preliminary board
                              test.

		-ffile 	      Option for specifying the location of the
                              logical name file - ARCDIAG.DAT.  40
                              characters maximum. (Unlimited version
                              only)

		-ixxxx	      Option for operating ARCDIAG at an I/O
                              address of xxxx (hex). ARCDIAG defaults
                              to 02E0 (hex).  Must use all 4 digits. 
                              (Unlimited version only).

		-mxxxx	      Option for operating ARCDIAG at a RAM
                              memory location of xxxx (hex).  ARCDIAG
                              defaults to D000 (hex).  Must use all 4
                              digits.  (Unlimited version only).

		-q	      Option allows board test only operation. 
                              Place [ARCDIAG -q] in the AUTOEXEC.BAT
                              file for automatic test of ARCNET card on
                              power up.  If an error condition is
                              detected, the nature of the error is
                              displayed and the DOS error level is set
                              to 1.  Otherwise, nothing is displayed,
                              and the DOS error level is kept at 0. 
                              (Unlimited version only).

		-ttype	      Option for selecting different network
                              interface cards.  ARCDIAG defaults to
                              standard SMC type cards with memory mapped
                              RAM and I/O mapped RIM controllers. 
                              (Unlimited version only).


      ArcDiag can be loaded and run in any file server or work
      station, providing there is a floppy drive available.  

      The ARCDIAG.EXE file may be copied onto and executed from the
      network hard disk, but keep in mind that board testing is
      disabled if the Novell Shell is loaded.

      Type ARCDIAG at the DOS prompt of the drive containing
      ARCDIAG, whereupon, if the Novell Shell is not loaded, the
      board test screen shown in Figure 1 will appear:


	Network Board Test

	PASSED: RAM test

	No Network Boot PROM found

	PASSED: Internal RIM test
	PASSED: Physical node address is: 1
	PASSED: ETS test
	PASSED: POR test



                 Figure 1 - Board Test Screen



BOARD TESTS

      Unless option [-b] is included in the startup command, the
      board test function automatically begins when entering
      [ARCDIAG] at the DOS prompt.  

	Board Types
	    ARCDIAG has been set to function on most Arcnet
            boards, with the exception of Nestar.  

	    By including [-ttype] in the command line as a start up
            option, different board types may be selected, e.g. [-
            t1], [-t2], etc.  Following is an example of the command
            line:

	     	ARCDIAG [-mxxxx] [-ffile descriptor] [-ttype]

	    [-t1] is the default and is used for most Arcnet cards
            that use memory mapped RAM and I/O mapped RIM controllers
            such as SMC, Novell, Earth, etc.  

	    [-t2] is used for memory mapped RIM controllers, such as
            Thomas Conrad, Arcmaster, etc.  When the [-t2] option is
            used, the [-I] option is disabled.  (Unlimited version
            only).

                  Note:  To select an Arcmaster card
                  that has RAM at E000 hex, enter the
                  following command line: (Unlimited
                  version only).

	          ARCDIAG -me000 -t2


      The following tests are made during the board test phase:

            NOTE:  When ARCDIAG is first executed, board
            testing is disabled if the user has already
            loaded the Novell Shell.

      RAM Test.--ARCDIAG exercises the ARCNET board's RIM RAM.  All
      2K of RAM are tested for shorted and open bits.  Also, the
      address lines are tested.  

      An error message is displayed if the RAM fails the test or if
      the DIP switch setting of the memory address set is incorrect.
      

      A PASSED message is displayed if operation is verified.

      Network Boot Prom Test.--This test indicates whether or not
      a network boot prom is installed.

      RIM Test.--The token controller IC (9026) is tested in the RIM
      test.  The network microprocessor (9026) can perform its own
      internal diagnostics.  When the test is run, approximately 95%
      of the processor's operations are exercised.  If this test
      fails, replacement of the network card is recommended if it
      is verified that the I/O address DIP switches are set
      correctly.  

      A PASSED message is displayed if operation is verified.
      
      SID Test.--During the SID test, the Controller source ID is
      located and read.  The returned value from this test is the
      station node address.  The test will fail if it is at zero. 
      If failed, make sure the address switches are set to an
      address greater than zero.  

      A PASSED message is displayed if operation is verified.

      ETS Test.--The ETS test verifies the proper location of the
      (E)xtended (T)imeout (S)etting jumper.  Newer ARCNET cards may
      not have a jumper.  Therefore, the card needs to be replaced
      if an error occurs.  

      A PASSED message is displayed if operation is verified.

      POR Test.--During this test, a power-up cycle is activated and
      verified.  The 9026 RIM processor is reset and the ARCNET card
      is placed into an operational state.

After performing all of the above tests, the program will halt for
approximately three seconds, then cycle into the Network Tests.

The Board Tests may be continued by selecting [Board] from the
Lotus-type menu at the top of screen, or by merely pressing [B]. 


NETWORK TESTS

Network tests function both in and out of the Netware shell. 
However, the file server and workstations can be tested only if
they are powered on.  

The Network Test Grid shown in Figure 2 appears after ArcDiag has
been started and the Board Tests are completed.

   Map      Count     Names    Format     Board     Print     Reset     Quit    
 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄ¿
 ³ Dec   1   2   3   4   5   6   7   8   9  10  11  12  13  14  15  ³³         ³
 ³   ÚÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄ¿³³         ³
 ³  0Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³ 15Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ Rcn/Min ³
 ³ 30Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³         ³
 ³ 45Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³ 60Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ Station ³
 ³ 75Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³         ³
 ³ 90Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³105Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ Address ³
 ³120Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³         ³
 ³135Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³150Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ Packets ³
 ³165Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³         ³
 ³180Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³195Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ Recnfgs ³
 ³210Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³         ³
 ³225Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ÄÄÄÄÄÄÄÄÄ³
 ³240Ã  ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù   ù  ´³³ ActNode ³
 ³   ÀÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÙ³³         ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÙ
         ARCDIAG V2.2  Limited    Copyright Olympic Software  1989              
                                

                 Figure 2 - Network Test Grid


Each dot on the grid represents a node.  As noted by the cursor
rapidly moving across the grid, the program polls all 255 nodes. 
When a file server or workstation is powered on, the node number
or node name will be displayed in the place of the dot.  

      Information Windows  Information from the network diagnostics
      is provided in the windows on the right side of the screen. 
      The first window contains current date and time.  Following
      is a description of the information contained in the other
      windows.


	    Rcn/Min  Indicates the number of reconfiguration per
            minute, relative to (1) the number of stations being
            powered on or off of the network, and (2) any type of
            fault condition occurring on the network.  

	    This information may be used as a gross indication of
            network fault conditions (see "Recnfgs" below).   

	    Station  If the Novell shell is running, the station
            number on which ARCDIAG is running is displayed in this
            window.  This number may be referenced to the station
            number which appears on the file server monitor.  If the
            shell is not loaded, the message "No Shell" is displayed.

	    Address  The physical address, or the dip switch setting,
            on the network interface card.

	    Packets  The number of packets that have occurred on the
            network since the last reset.  This information indicates
            relative network activity.

	    Recnfgs  Reconfiguration bursts are counted
            accumulatively and displayed in this window. 
            Reconfiguration bursts increment whenever any of the
            following occur: 

	    	1.	a workstation is powered onto the network.
	    	2.	a workstation is powered off of the network
                        (intermittent).
	    	3.	a network card is faulty.
	    	4.	the network connecting cable is faulty.

	    	  A rapidly increasing reconfiguration count indicates
                  a faulty network (refer to "Network Troubleshooting,
                  Network Tests").

	    ActNode  The number of nodes that have powered onto the
            network.  

FUNCTION SELECTION

      At the top of the Network Test screen is a "Lotus" type menu
      for selecting various functions, such as "Map," "Count,"
      "Names," etc.  To select a particular function, either move
      the cursor key to highlight the function and press [Enter],
      or merely type the first letter of the function label, e.g.
      [M] for the "Map" function.  

      Note that a "help" statement, corresponding to each function,
      appears at the bottom of the screen whenever a function is
      highlighted.  


      "Map" Function  Selection of this function displays all nodes
      on a grid, each node being indicated by a dot.  The number
      range is from 1 to 255.  The display is arranged in a matrix
      form.  Nodes are displayed 15 at a time along the horizontal. 
      Therefore, nodes 1 through 15 are displayed on the first line,
      nodes 16 through 29 on the next line, etc.  

      Stations that are powered on are indicated by a node number
      or node name, in the place of a dot.

      "Count" Function  In this mode, packets from each station are
      monitored and displayed on the grid.  Packet counts can be
      viewed as an indication of activity from each node.  Those
      nodes that transfer packets most frequently will increment the
      packet count much more rapidly.  

      Although the program is not fast enough to catch all packets,
      relative packet increases are displayed.  Therefore, the nodes
      that are assigned as fileservers should have packet counts in-
      creasing at a faster rate than workstations.

      "Names" Function  Any of the 255 nodes can be given an alpha-
      numeric designation which is useful for quick recognition of
      node locations.  (Unlimited version only).

      These logical names can be assigned to physical node numbers
      by using the "Names" function.  For example, a file server
      that might be located on node 1 may be given the logical
      designation "FS1".  

      When selecting the "Names" function, the following message
      will appear at the bottom of the screen:

	   Enter node number (1 to 255):

      At the blinking cursor, enter the number of the node to which
      you want to give a logical name, then press [Enter].  The
      following message will then appear:

     	   Enter name (3 char max):

      At the blinking cursor, enter a maximum of three characters
      and press [Enter].  You will then be asked:  

      	    Save (y/n) <return = yes>

      If your entry is correct and you want to save it to the
      ARCDIAG.DAT file on the disk, press [Enter], since "Enter" or
      "Return" is the default.  Otherwise, press [N] to ignore the
      entry.  

      The program uses the file ARCDIAG.DAT to store logical names
      for physical node numbers.  

      The ARCDIAG.DAT file can be located in either the default
      drive or when connected to a Novell network it can be located
      in the Z: (public) directory.  Optionally a command line
      argument (-f) can be used to tell ARCDIAG where to locate and
      what name to use for the logical name file (see "Start Up
      Options").


      "Format" Function  Physical node numbers can be displayed on
      the node map as either decimal or hexidecimal numbers.  The
      current mode of operation is displayed in the upper left hand
      corner of the display.  

      Pressing the [Enter] key more than once will toggle the
      display mode back and forth between decimal and hexidecimal. 
      

      "Board" Function  This function runs diagnostics on network
      interface cards.  In order for the board diagnostic test to
      operate, however, ARCDIAG cannot be running in conjunction
      with the Novell operating system. 

      When this test is initiated from the menu at the top of the
      screen, it will continue until the space bar is pressed or
      until an error is found.

      "Print" Function  If an IBM graphics compatible printer is
      available, use PrtSc to produce an exact copy of the map
      including graphic borders.  (Unlimited version only).

      If an IBM graphics compatible printer is not available, or if
      you want to label and date the node map, select the "Print"
      function on the menu, whereupon the following statement will
      appear at the bottom of the screen:

             Enter map name:

      Type a name for the map, then press [Enter].  A node map with
      time and date stamp will be sent to the printer.  All borders
      are converted to characters that can be printed on any type
      of printer.  

      The printing program does not send a form feed character at
      the end of printing allowing two maps to be printed on one 8
      1/2 by 11 inch piece of paper.
	
      "Reset" Function  Select this function to reset all counters
      to zero and reformat the grid.

      "Exit" Function  Select this function to exit the program.  


SPECIFICATIONS

      RIM RAM Base Address	D000 (hex) segment default
				configurable at runtime (Unlimited
                                version only).

      Board I/O Address       	02E0(hex) default
				configurable at runtime (Unlimited
                                version only)

      Active Nodes Displayed  	1 thru 255

      RIM RAM size		2K bytes

      Computer Compatibility	IBM PC/XT/AT or compatible Network
                                Operating Systems Novell Netware 4.61
                                and above.  Novell Advanced Netware
                                1.02 and above.

      Network Interface Cards	SMC 8 bit and Novell RX 8 bit 


NETWORK TROUBLESHOOTING

Board Tests

Symptom				Corrective Action

RAM Test Fails		      Check network card memory address DIP
                              switches for proper settings.
  
			      RAM defective, replace card.

RIM Test Fails		      Check network card I/O address DIP
                              switches for proper settings.

			      9026 RIM controller defective, replace
                              card

SID Test		      The SID address should display the node
                              address.  Note:  Do not allow two network
                              cards to have the same physical address. 

ETS Test Fails		      Newer network card does not have a jumper
                              for extended timeout.  Therefore, if this
                              test fails, the board needs to be
                              replaced.

POR Test Fails		      Before, continuing, remove the network
                              cable and try again.  If the test still
                              fails, the network card needs to be
                              replaced.  Disconnecting the cable removes
                              any type of external interference with the
                              test.



Network Tests		

Symptom			      Likely Cause

Reconfiguration 			
counter increments 
continuously		      (1) no other nodes are connected to the 
                              local network card.
			      (2) the cable network is defective from
                              the local card to the rest of the network.
			      (3) an active or passive hub port is
                              defective.


Multiple "phantom" nodes
are displayed		      (1) two nodes have been set to the same 
                              address.
			      (2) a cable connection is not making solid
                              contact.
			      (3) the memory address DIP switches are
                              set incorrectly.
			      (4) -i or -m options have been set
                              incorrectly.

When run with Novell
shell - local node is
not displayed		      Nothing is wrong with the display.  The
                              Novell shell has not passed the proper
                              physical node address to ARCDIAG.  Works
                              correctly when not running with the shell. 
                              Fixed in Novell Advanced Netware 2.0 and
                              above.


ARCDIAG shows OK, but
cannot "find fileserver"
when shell is run	      Make sure the interrupt jumper JP5
                              is used for all network cards used
                              with Advanced Netware 1.02 and above.

HOW TO REGISTER ARCDIAG
 
If you find the program useful, and continue to use it past a
30-day trial period, you are required to register it. You can
register by completing the accompanying registration form and
sending it, with a check or money order in the amount of $45.00 (if
foreign funds, at current exchange rate) to Olympic Software Co.
at the address shown on the registration form below. 
 
Registration provides the following benefits: 
 
      Elimination of the initial registration reminder screen. 

      Enabling of the following features:
		Named nodes
		Map printing
		Command Line arguments     
      	
      Full Telephone support.  

      Free major updates for a one year period, sharply discounted
      rates thereafter. 

      Inclusion on our mailing list so that you may receive new
      product announcements and notification of new Olympic Software
      products.

      You will be in compliance with federal copyright law. 

 
USER SUPPORT

Registered users are provided with automatic notification of major
updates of ARCDIAG.  Call (313) 429-7139, a call-back will normally
occur no later than the next business day. Bug fixes or
work-arounds will be mailed to the complainant, if a registered
user, and will also be uploaded to CIS (IBMSW).   Non-registered
users are welcome to call, and will be accommodated on a "time 
available" basis. Contact may, of course, always be made through
CIS EMAIL (73227, 3326). 


OTHER SHAREWARE PRODUCTS 
 
	You may wish to try these other products of Olympic Software: 

	ARCDIAG.C	Source Code for ARCDIAG		$150.00
 

 
                     ARCDIAG Registration & Comment Form 
 
 
       
Name:___________________________________________________________
       
Company:________________________________________________________

Address:________________________________________________________

City:__________________________ State:_____  ZIP _______________ 
 
Telephone:(_____) _____-_______     Date:_______________________
 
ARCDIAG Version:_____._____ 

Network Interface Card Types ___________________________________
 
Comments: 
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_________________________________________________________________
_______________________________________________________________
 
 
Payment: 
 
Quantity           Cost Each
 
________           ___$45.00___                   sub-total ____.__
 
                        (MI residents only) MI 4% Sales Tax ____.__
 
                                                      TOTAL ____.__

       Mail To:       Olympic Software Co
		      8424 Warner Rd
		      Saline, MI  48176