-------------------------------------------------------------------------
|			DAC.DOC						|
|	This document describes the process for loading the color 	|
|	registers of the video DAC and a sample code fragment.		|
-------------------------------------------------------------------------

The DAC is only enabled when an analog monitor is attached.

The VGA's Digital-to-Analog Converter (DAC) contains an internal color
lookup table to allow the user to select up to 256 colors from a palette of
262,144 possible colors.  The color look-up table is composed of 256 
18-bit color registers.  Each register is subdivided into 3 6-bit entries,
where each entry is in the range 00h..3Fh.  These three values specify the
red (R), green (G), and blue (B) intensities of the color register.  If R=G=B,
the color register's output is a shade of gray.

		-------------------------
		| 00h |  R  |  G  |  B  |
		| 01h |  R  |  G  |  B  |
		| 02h |  R  |  G  |  B  |
		| 03h |  R  |  G  |  B  |
		|  .  |  .  |  .  |  .  |
		|  .  |  .  |  .  |  .  |
		|  .  |  .  |  .  |  .  |
		| FEh |  R  |  G  |  B  |
		| FFh |  R  |  G  |  B  |
		-------------------------


For 256 color modes (IBM mode 13h, Everex Extended 256 color modes), all 256
color registers are active.  For all other modes, you can select the paging
mode and page# using IBM standard BIOS functions AX = 101Ah and AX = 1013h.
The BIOS also provides functions for reading and writing the DAC color
registers (AX = 1012h and AX = 1017h).  If you wish to program the DAC 
directly, there are several steps to follow:

	1) Wait for vertical retrace. (This is not entirely necessary, but if
	   you write to the DAC when a retrace is not active, you will get
	   snow on the screen.)
	2) Index the color register you want.
	3) Output the R, G, and B values, in order.

Note: After writing the three color values, the color register index
      will auto-increment to the next color register.  Also, you must insure
      that there is a minimum 240 nanosecond delay between the output of each
      color value.  This can easily be accomplished in assembly language by
      inserting a jmp short $+2 between each out instruction.

A vertical retrace can be detected by reading the CRTC Stat port.  This
port has address 3?Ah, where ? is D for color modes and B for monochrome
modes.  A simple means of determining which value to use is to read the
CRTC Addr port number from the BIOS data area at 0:463 (word).  This value
will be either 3B4h or 3D4h.  Bit 3 of the byte read from the CRTC Stat port
is 1 if a vertical retrace is active.  If you wish to prevent snow on the 
screen, and you have a large block of color registers to output, you may wish
to wait for the leading edge of the vertical retrace by first waiting for the
retrace bit to go to 0, then waiting for the retrace bit to go to 1.  This
will insure the maximum amount of time for outputting the block of color
registers before the retrace ends.

The DAC Addr port number is 3C7h (W) for reading the DAC, and 3C8h (RW) for
writing to the DAC.  The color values are written and read through port 3C9h 
in the order of R, then G, then B.

To read back the values in the DAC, write the starting address to port
3C7h, then read successive triples from port 3C9h.

; ************************************************************************
; ************************************************************************

mSysCrtcAddr	equ	463h		; Offset to CRTC address in BIOS data

rDacAddrW	equ	3C8h		; DAC Address port (Write mode)
rDacData	equ	3C9h		; DAC Data port

NumColors	equ	8		; Program 8 color registers
FirstReg	equ	0		; First register to program

ColorTable	db	00h,00h,00h	; Increasing intensities of gray
		db	08h,08h,08h
		db	10h,10h,10h
		db	18h,18h,18h
		db	20h,20h,20h
		db	28h,28h,28h
		db	30h,30h,30h
		db	38h,38h,38h

;	Wait for leading edge of vertical retrace first, to prevent snow

	xor	cx,cx			; Maximum delay for waiting
	mov	ds,cx
	mov	dx,ds:[mSysCrtcAddr]	; Get CRTC Addr
	add	dx,6			; Get CRTC Stat
Wait1:
	in	al,dx
	test	al,8h			; Check for retrace inactive
	jz	RetraceInactive
	loop	Wait1

;	At this point a retrace is not occurring.  Now wait for leading edge
;	of next retrace.

RetraceInactive:
	xor	cx,cx			; Maximum delay for waiting
Wait2:
	in	al,dx
	test	al,8h			; Check for retrace active
	jnz	RetraceActive
	loop	Wait2

;	A retrace should be just starting now, so set the DAC Write index

RetraceActive:
	mov	dx,rDacAddrW		; Get DAC write address
	mov	al,FirstReg		; First color register to program
	out	dx,al			; Set write index
	jmp	short $+2		; Insure sufficient delay

;	DAC index set.  Now load up the color registers

	mov	dx,rDacData		; Get DAC data address
	mov	cx,NumColors		; Number of color registers to program
	lea	si,ColorTable		; ds:si -> color table to load
	push	cs
	pop	ds

ProgramDACLoop:
	lodsb				; Get one Red color value
	out	dx,al			; Write it out
	jmp	short $+2		; Insure sufficient delay

	lodsb				; Get one Green color value
	out	dx,al			; Write it out
	jmp	short $+2		; Insure sufficient delay

	lodsb				; Get one Blue color value
	out	dx,al			; Write it out

	loop	ProgramDACLoop

;	Color registers are now loaded

; ************************************************************************
; ************************************************************************