-------------------------------------------------------------------------
|			VGABIOS.DOC					|
|	This document describes the IBM Standard VGA BIOS functions 	|
|	and their usage.						|
-------------------------------------------------------------------------

The following is a summary of the standard IBM VGA BIOS functions:

;***************************************************************

ah = 00h - Set Mode
ah = 01h - Set Cursor Type
ah = 02h - Set Cursor Position
ah = 03h - Read Cursor Position
ah = 04h - Read Light Pen Position (EGA and CGA only)
ah = 05h - Select Active Display Page
ah = 06h - Scroll Active Page Up
ah = 07h - Scroll Active Page Down
ah = 08h - Read Attribute/Character at Cursor Position
ah = 09h - Write Attribute/Character at Cursor Position (Graphics)
ah = 0Ah - Write Character at Cursor Position		(Text)
ah = 0Bh - Set Color Palette
ah = 0Ch - Write Dot
ah = 0Dh - Read Dot
ah = 0Eh - Write TTY to Active Page
ah = 0Fh - Read Video State
ah = 10h - Set Palette Registers
ah = 11h - Character Generator
ah = 12h - Alternate Select
ah = 13h - Write String
ah = 14h - reserved (PC Convertible only)
ah = 15h - reserved (PC Convertible only)
ah = 16h - reserved
ah = 17h - reserved
ah = 18h - reserved
ah = 19h - reserved
ah = 1Ah - Read/Write Display Combination Code
ah = 1Bh - Return Functionality/State Information
ah = 1Ch - Save/Restore Video State

;***************************************************************
Set Mode (ah = 00h)

Entry:	ah = 00h
	al = mode# (0..13h) => Set standard IBM mode
	   = 70h => Set Everex Extended mode 
		bl = Everex Extended mode number

	(if b7 of al is set, the video buffer is not cleared)

Exit :	None

;***************************************************************
Set Cursor Type (ah = 01h)

Entry:	ah = 01h
	ch = Starting line for cursor
	cl = Ending line for cursor

Exit :	None

;***************************************************************
Set Cursor Position (ah=02h)

Entry:	ah = 02h
	bh = Page#
	dh,dl = Row,column of cursor position

Exit :	None

;***************************************************************
Read Cursor Position (ah=03h)

Entry:	ah = 03h
	bh = Page#

Exit :	ch,cl = Current cursor type
	dh,dl = Row,column of cursor for requested page

;***************************************************************
Read Light Pen Position (ah=04h)

NOTE: Light Pen is not available on VGA adapters.

Entry:	ah = 04h

Exit :	ah = 00h => Light pen switch not activated
		bx,cx,dx are altered
	   = 01h => Light pen position successful
		bx = PEL column (0..X)
		ch = raster line (0..199) (200 line modes)
		cx = raster line (0..Y)   (new graphics modes)
		dh,dl = Row,column of character

;***************************************************************
Select Active Display Page (ah=05h)

Entry:	ah = 05h
	al = Page#

Exit :	None

;***************************************************************
Scroll Active Page Up (ah=06h)

Entry:	ah = 05h
	al = # of lines to blank at the bottom
	   = 00h to blank the entire window
	bh = Blanking attribute
	ch,cl = Row,column of upper left corner
	dh,dl = Row,column of lower right corner

Exit :	None

;***************************************************************
Scroll Active Page Down (ah=07h)

Entry:	ah = 07h
	al = # of lines to blank at the top
	   = 00h to blank the entire window
	bh = Blanking attribute
	ch,cl = Row,column of upper left corner
	dh,dl = Row,column of lower right corner

Exit :	None

;***************************************************************
Read Attribute/Character at Cursor Position (ah=08h)

Entry:	ah = 08h
	bh = Page#

Exit :	ah = Attribute of character read (Text modes only)
	al = character read

;***************************************************************
Write Attribute/Character at Cursor Position (ah=09h)

Entry:	ah = 09h
	al = Character to write
	bh = Page#
	bl = Attribute of character to write
	cx = Count of characters to write

	(For 256 color modes, bh is used as the background color)
	(For non-256 color graphics modes, if b7 of bl is set, the 
	color value is XORed)

Exit :	None

;***************************************************************
Write Character at Cursor Position (ah=0Ah)

Entry:	ah = 0Ah
	al = Character to write
	bh = Page#
	cx = Count of characters to write

Exit :	None

;***************************************************************
Set Color Palette (ah=0Bh)

Entry:	ah = 0Bh
	bh = 00h => Set background color for 320x200 graphics modes
		 => Set foreground color for 640x200 graphics modes
		 => Set border color for alphanumeric modes
		bl = (0..31)
	   = 01h => Select palette for 320x200 graphics modes
		bl = 0 => Green/red/brown
		    = 1 => Cyan/magenta/white

Exit :	None

;***************************************************************
Write Dot (ah=0Ch)

Entry:	ah = 0Ch
	al = Color value
	bh = Page#
	dx,cx = Row,column of pixel

	(In non-256 color modes, if b7 of al is set then the color is XORed)

Exit :	None

;***************************************************************
Read Dot (ah=0Dh)

Entry:	ah = 0Dh
	bh = Page#
	dx,cx = Row,column of pixel

Exit :	al = Color value

;***************************************************************
Write TTY to Active Page (ah=0Eh)

Entry:	ah = 0Eh
	al = Character to write
	bl = Foreground color (Graphics modes only)

Exit :	None

;***************************************************************
Read Video State (ah=0Fh)

Entry:	ah = 0Fh

Exit :	al = Current mode#
	ah = Columns
	bh = Active page#

	(If an Everex Extended mode is active, al will contain the base mode)

;***************************************************************
Set Palette Registers (ah=10h)

Entry:	ah = 10h
	al = 00h => Set one palette register
		bl = Palette register#
		bh = value to set
	   = 01h => Set overscan register
		bh = value to set
	   = 02h => Set all palette registers and overscan
		es:dx -> 17 byte table
	   = 03h => Toggle intensify/blinking bit
		bl = 00h => Enable intensify
		   = 01h => Enable blinking

	   = 07h => Read one palette register
		bl = Palette register#
		Exit:	bh = value read
	   = 08h => Read overscan register
		Exit:	bh = value read
	   = 09h => Read all palette registers and overscan
		es:dx -> 17 byte table

	   = 10h => Set individual color register
		bx = Color register#		(0..FFh)
		dh = Red value			(0..3Fh)
		ch = Green value		(0..3Fh)
		cl = Blue value			(0..3Fh)
	   = 12h => Set block of color registers
		bx = First color register#	(0..FFh)
		cx = Count of color registers
		es:dx -> Table of size 3*cx bytes.  Each
			triple forms a Red,Green,Blue to be
			written to one color register
	   = 13h => Select color page (not valid in 256 color modes)
		bl = 00h => Select paging mode
			bh = 00h => Select  4 blocks of 64 registers
			   = 01h => Select 16 blocks of 16 registers
		bl = 01h => Select page
			bh = Page# (00h..03h or 00h..0Fh)
	   = 15h => Read one color register
		bl = Color register#
		Exit:	dh = Red value
			ch = Green value
			cl = Blue value
	   = 17h => Read block of color registers
		bx = First color register#	(0..FFh)
		cx = Count of color registers
		es:dx -> Table of size 3*cx bytes.
		Exit:	es:dx -> Table of size 3*cx bytes.  Each triple
			forms a Red,Green,Blue value read from one color
			register.
	   = 18h => (Undocumented) Set PEL Mask
		bl = new PEL mask
		(This value is ANDed with each color value before looking
		up the color in the digital-to-analog converter (DAC))
	   = 19h => (Undocumented) Read PEL Mask
		bl = value read
	   = 1Ah => Read color page state
		Exit:	bl = paging mode
			bh = current page
	   = 1Bh => Sum a block of colors to gray shades
		bx = Starting color register#
		cx = # of color registers to convert

;***************************************************************
Character Generator (ah=11h)

Entry:	ah = 11h
	al = 00h => User alpha font load w/set mode
		bh = bytes/character
		bl = block#
		cx = count to store
		dx = character offset to start at
		es:bp -> font table of size cx*bh bytes
	al = 01h => ROM 8x14 font load w/set mode
		bl = block#
	al = 02h => ROM 8x8 font load w/set mode
		bl = block#
	al = 03h => Set block specifier
		bl - b4,b1,b0 select normal intensity font block
		bl - b5,b3,b2 select high intensity font block
	al = 04h => ROM 8x16 load w/set mode
		bl = block#

	al = 10h => User alpha font load w/o set mode
		bh = bytes/character
		bl = block#
		cx = count to store
		dx = character offset to start at
		es:bp -> font table of size cx*bh bytes
	al = 11h => ROM 8x14 font load w/o set mode
		bl = block#
	al = 12h => ROM 8x8 font load w/o set mode
		bl = block#
	al = 14h => ROM 8x16 load w/o set mode
		bl = block#

	al = 20h => Set user graphics pointer at INT 1Fh
		es:bp -> user font table
	al = 21h => Set user graphics pointer at INT 43h for user font
		es:bp -> user font table
		cx = bytes/character
		bl = Row specifier
		   = 00h => User row count
			dl = # of rows
		   = 01h => 14 rows
		   = 02h => 25 rows
		   = 03h => 43 rows
	al = 22h => Set user graphics pointer at INT 43h for ROM 8x14
		bl = Row specifier
	al = 23h => Set user graphics pointer at INT 43h for ROM 8x8
		bl = Row specifier
	al = 24h => Set user graphics pointer at INT 43h for ROM 8x16
		bl = Row specifier
	al = 30h => Return font information
		bh = font pointer requested
		Exit:	cx = bytes/character
			dl = # rows -1
			es:bp -> font requested
				bh = 00h => es:bp =  INT 1Fh font pointer
				bh = 01h => es:bp =  INT 43h font pointer
				bh = 02h => es:bp -> ROM 8x14 font
				bh = 03h => es:bp -> ROM 8x8 font (00h to 7Fh)
				bh = 04h => es:bp -> ROM 8x8 font (80h to FFh)
				bh = 05h => es:bp -> ROM 9x14 alt font
				bh = 06h => es:bp -> ROM 8x16 font
				bh = 07h => es:bp -> ROM 9x16 alt font

;***************************************************************
Alternate Select (ah = 12h)

Entry:	ah = 12h
	bl = 10h => Return EGA information
		Exit:	bh = 00h => Color mode in effect
			   = 01h => Monochrome mode in effect
			bl = Memory size (0..3)
			ch = Feature connector bits
			cl = IBM EGA switch settings
	bl = 20h => Revector print screen interrupt to EGA print screen
	bl = 30h => Select # of scan lines for next text set mode
		al = 00h => 200 scan lines (invalid for mode 7)
		   = 01h => 350 scan lines
		   = 02h => 400 scan lines
		Exit:	al = 12h if the function was supported
	bl = 31h => Enable/Disable default palette loading during set mode
		al = 00h => Enable default palette loading
		   = 01h => Disable default palette loading
		Exit:	al = 12h if the function was supported
	bl = 32h => Enable/Disable video
		al = 00h => Enable video
		   = 01h => Disable video
		Exit:	al = 12h if the function was supported
	bl = 33h => Enable/Disable gray summing
		al = 00h => Enable gray summing
		   = 01h => Disable gray summing
		Exit:	al = 12h if the function was supported
	bl = 34h => Enable/Disable cursor emulation
		al = 00h => Enable cursor emulation
		   = 01h => Disable cursor emulation
		Exit:	al = 12h if the function was supported
	bl = 36h => Video screen on/off
		al = 00h => Video screen off
		   = 01h => Video screen on
		Exit:	al = 12h if the function was supported

For IBM PS/2 computers:
	bl = 35h => Display switch
		al = 00h => Initial adapter off
			es:dx -> 128 byte save area
		al = 01h => Initial system board video on
		al = 02h => Switch off active video
			es:dx -> 128 byte save area
		al = 03h => Switch on inactive video
			es:dx -> 128 byte save area
		al = 80h => (Undocumented) Set system board video active flag
		Exit:	al = 12h if the function was supported
		
;***************************************************************
Write String (ah=13h)

Entry:	al = string format
	   = 00h => bl = attribute
		    string = ch,ch,ch,...		(cursor not moved)
	   = 01h => bl = attribute
		    string = ch,ch,ch,...		(cursor moved)
	   = 02h => string = ch,attr,ch,attr,... 	(cursor not moved)
							(text modes only)
	   = 03h => string = ch,attr,ch,attr,... 	(cursor moved)
							(text modes only)

;***************************************************************
Read/Write Display Combination Code (DCC) (ah=1Ah)

Entry:	ah = 1Ah
	al = 00h => Read DCC
		Exit:	bl = active display code
			bh = alternate display code
	al = 01h => Write DCC
		bl = active display code
		bh = alternate display code

Exit :	al = 1Ah if the function was supported

Valid display combination codes:
	00h - no display
	01h - monochrome adapter w/ monochrome display
	02h - color graphics adapter w/ color display
	03h - reserved
	04h - Enhanced graphics adapter w/ color display
	05h - Enhanced graphics adapter w/ monochrome display
	06h - Professional graphics adapter w/ color display
	07h - VGA w/ monochrome analog display
	08h - VGA w/ color analog display
	09h - reserved
	0Ah - reserved
	0Bh - MCGA w/ monochrome analog display
	0Ch - MCGA w/ color analog display
	FFh - unknown display type
	
;***************************************************************
Return Functionality/State Information (ah=1Bh)

Entry:	ah = 1Bh
	bx = Implementation type
	   = 0000h => Return functionality/state information
		es:di -> 40h byte buffer
			(di+00) (dw)->Static functionality table
			(di+04) (b) = video mode in effect
			(di+05) (w) = # of columns
			(di+07) (w) = Length of regen buffer in bytes
			(di+09) (w) = Starting address of regen buffer
			(di+0B) (w) = Cursor position for page 0
			   :
			   :
			(di+19) (w) = Cursor position for page 7
			(di+1B) (w) = Cursor type
			(di+1D) (b) = Active display page
			(di+1E) (w) = CRTC port address
			(di+20) (b) = Current setting of register (3?8)
			(di+21) (b) = Current setting of register (3?9)
			(di+22) (b) = # of rows
			(di+23) (w) = bytes/character
			(di+25) (b) = DCC of active display
			(di+26) (b) = DCC of alternate display
			(di+27) (w) = # of colors supported in current mode
			(di+29) (b) = # of pages supported in current mode
			(di+2A) (b) = # of scan lines active
					(0,1,2,3) => (200,350,400,480)
			(di+2B) (b) = Primary character block
			(di+2C) (b) = Secondary character block
			(di+2D) (b) = Miscellaneous flags
				b0 - All modes on all displays on
				b1 - Gray summing on
				b2 - Monochrome display attached
				b3 - Default palette loading disabled
				b4 - Cursor emulation enabled
				b5 - 0 => Intensity
				     1 => Blinking
				b6,b7 - reserved
			(di+2E..30) (b) - reserved
			(di+31) (b) = Video memory (0,1,2,3)=>(200,350,400,480)
			(di+32) (b) = Save pointer state flags
				b0 - 512 character set active
				b1 - Dynamic save area present
				b2 - Alpha font override active
				b3 - Graphics font override active
				b4 - Palette override active
				b5 - DCC override present
				b6,b7 - reserved
			(di+33..3F) - reserved

Static Funcionality Table format (10h bytes):
	+00 = Modes supported #1
		b0..b7 = 1 => corresponding mode (0,1,2,3,4,5,6,7) supported
	+01 = Modes supported #2
		b0..b7 = 1 => corresponding mode (8,9,A,B,C,D,E,F) supported
	+02 = Modes supported #3
		b0..b3 = 1 => corresponding mode (10,11,12,13) supported
		b4..b7 - reserved
	+03..+06 - reserved
	+07 = Scan lines supported
		b0..b2 = 1 => corresponding lines (200,350,400) supported
		in text modes
	+08 = Maximum number of active character blocks in text modes
	+09 = Total blocks available in text modes
	+0A = Miscellaneous function flags #1
		b0 - All modes on all displays function supported
		b1 - Gray summing function supported
		b2 - Character font loading function supported
		b3 - Default palette loading enable/disable supported
		b4 - Cursor emulation function supported
		b5 - EGA palette present
		b6 - Color palette present
		b7 - Color paging function supported
	+0B = Miscellaneous funcion flags #2
		b0 - Light pen supported
		b1 - Save/restore state function 1C supported
		b2 - Intensity/blinking function supported
		b3 - Display Combination Cide (DCC) supported
		b4..b7 - reserved
	+0C..+0D - reserved
	+0E = Save pointer function flags
		b0 - 512-character set supported
		b1 - Dynamic save area supported
		b2 - Alpha font override supported
		b3 - Graphics font override supported
		b4 - Palette override supported
		b5 - DCC extension supported
		b6,b7 - reserved
	+0F - reserved

;***************************************************************
Save/Restore Video State (ah=1Ch)

Entry:	ah = 1Ch
	cx = Requested states
		b0 - Video hardware
		b1 - BIOS data areas
		b2 - Color registers and state
		b3..b7 - reserved
	al = 00h => Calculate buffer size for requested statesin 64 byte blocks
		Exit:	bx = buffer size to save requested states
	al = 01h => Save requested states
		es:bx -> Buffer of sufficient size to save requested states
	al = 02h => Restore requested states
		es:bx -> Buffer containing previously saved state
		
Exit :	al = 1Ch => Function supported

;***************************************************************