TPHRT



                   Turbo Pascal High Resolution Timer Toolbox 



                                  Version 3.00



                          Shareware Evaluation Version














                                  Ryle Design

                                  P.O. Box 22

                          Mt. Pleasant, Michigan 48804

                                (517) 773-0587

                               Cserv 73047,1765


















                                 Contents



          TPHRT User Guide                                           1
             Introduction  . . . . . . . . . . . . . . . . . . . . . 1
             Functional Overview . . . . . . . . . . . . . . . . . . 2
             Theory  . . . . . . . . . . . . . . . . . . . . . . . . 3
             TPHRT Function Descriptions . . . . . . . . . . . . . . 4
             Examples  . . . . . . . . . . . . . . . . . . . . . . . 8
             Technical Support . . . . . . . . . . . . . . . . . . . 8
             Shareware . . . . . . . . . . . . . . . . . . . . . . . 8

          TPHRT Function Reference                                  11
             t_ask_delay . . . . . . . . . . . . . . . . . . . . .  11
             t_ask_timer . . . . . . . . . . . . . . . . . . . . .  11
             t_bios_ask  . . . . . . . . . . . . . . . . . . . . .  12
             t_bios_entry  . . . . . . . . . . . . . . . . . . . .  12
             t_bios_exit . . . . . . . . . . . . . . . . . . . . .  13
             t_bios_fname  . . . . . . . . . . . . . . . . . . . .  13
             t_bios_load_desc  . . . . . . . . . . . . . . . . . .  13
             t_bios_report . . . . . . . . . . . . . . . . . . . .  14
             t_bios_resume . . . . . . . . . . . . . . . . . . . .  14
             t_bios_reset  . . . . . . . . . . . . . . . . . . . .  15
             t_bios_rname  . . . . . . . . . . . . . . . . . . . .  15
             t_bios_set_file . . . . . . . . . . . . . . . . . . .  15
             t_bios_set_user . . . . . . . . . . . . . . . . . . .  16
             t_bios_start  . . . . . . . . . . . . . . . . . . . .  16
             t_bios_stop . . . . . . . . . . . . . . . . . . . . .  17
             t_bios_suspend  . . . . . . . . . . . . . . . . . . .  18
             t_calc_delay_ff . . . . . . . . . . . . . . . . . . .  18
             t_calib . . . . . . . . . . . . . . . . . . . . . . .  18
             t_cvt_time  . . . . . . . . . . . . . . . . . . . . .  19
             t_delay_calib . . . . . . . . . . . . . . . . . . . .  19
             t_diff  . . . . . . . . . . . . . . . . . . . . . . .  20
             t_do_delay  . . . . . . . . . . . . . . . . . . . . .  20
             t_do_delay_wints  . . . . . . . . . . . . . . . . . .  20
             t_entry . . . . . . . . . . . . . . . . . . . . . . .  21
             t_exit  . . . . . . . . . . . . . . . . . . . . . . .  21
             t_fname . . . . . . . . . . . . . . . . . . . . . . .  22
             t_get . . . . . . . . . . . . . . . . . . . . . . . .  22
             t_get_delay_ff  . . . . . . . . . . . . . . . . . . .  22
             t_hires_entry . . . . . . . . . . . . . . . . . . . .  23
             t_hires_exit  . . . . . . . . . . . . . . . . . . . .  23
             t_hook_int  . . . . . . . . . . . . . . . . . . . . .  23
             t_min_delay . . . . . . . . . . . . . . . . . . . . .  24
             t_name  . . . . . . . . . . . . . . . . . . . . . . .  24
             t_report  . . . . . . . . . . . . . . . . . . . . . .  24
             t_request . . . . . . . . . . . . . . . . . . . . . .  25
             t_res_delay . . . . . . . . . . . . . . . . . . . . .  25
             t_reset . . . . . . . . . . . . . . . . . . . . . . .  25



                                       i





             t_resume  . . . . . . . . . . . . . . . . . . . . . .  26
             t_rname . . . . . . . . . . . . . . . . . . . . . . .  26
             t_set_delay_ff  . . . . . . . . . . . . . . . . . . .  26
             t_setmode . . . . . . . . . . . . . . . . . . . . . .  27
             t_start . . . . . . . . . . . . . . . . . . . . . . .  27
             t_stop  . . . . . . . . . . . . . . . . . . . . . . .  28
             t_suspend . . . . . . . . . . . . . . . . . . . . . .  28
             t_unhook_int  . . . . . . . . . . . . . . . . . . . .  28

          TPHRT V3.00 Registration . . . . . . . . . . . . . . . .  30


















































                                       ii









                                TPHRT User Guide


     Introduction


     TPHRT (Turbo Pascal High Resolution  Timer) is a software library that
     provides the software developer with  reliable  timing  functions that
     work across  the entire Intel 80xxx PC compatible hardware environment
     with microsecond resolution. The TPHRT timing logic  calibrates itself
     to the host PC clock rate and processor environment at run-time,  so a
     single executable program will yield  accurate  results  regardless of
     the host microprocessor and clock speed.

     TPHRT  is  the  definitive choice for any PC application that requires
     precision timing.  Some typical TPHRT applications are:

     Source Code Timer/Profiler
     By  adding timer calls to source code  under  development,  TPHRT  can
     generate a detailed summary  of  execution  time by program subroutine
     and immediately  illustrate  the  software's  "hot  spots"  that might
     benefit from further code or algorithm optimization.  Unlike "binning"
     profilers  that display the number of "hits" in  a  range  of  program
     addresses, TPHRT provides  a  direct one to one correspondence between
     source code and elapsed time with user defined granularity.

     Hardware Performance Evaluator
     The high resolution and  self  calibration  features  of TPHRT make it
     ideal  for  insertion  in code to evaluate hardware performance.  Disk
     drives,  numeric processors and CRT controllers  can  all  have  their
     throughput measured very  accurately  with  TPHRT,  and  with numerous
     timers  at  the  users   disposal,   many   device  functions  may  be
     independently  measured  in  a single run.  The formatted timer report
     generated  by  TPHRT  makes  compilation  and  interpretation  of test
     results painless.

     Process Control
     With TPHRT, process control applications that require  precise timings
     or  precision  delays  are  easy  to  implement.    No longer will the
     application developer have to make an educated guess as to how  long a
     critical interrupt is taking to service an I/O port as TPHRT  can time
     virtually any hardware or software interrupt and provide the developer
     with  precise  accurate  timings  of  the  critical  procedure.    The
     precision delay  functions  allow  the  programmer  to  implement data
     acquisition loops with microsecond resolution.

     Timing and Scoring
     TPHRT  is the perfect "timer engine" to build  a  timing  and  scoring
     system for use in nearly any competitive event.  With  its microsecond
     resolution and self calibration features, TPHRT surpasses conventional
     sports   timing  equipment  resolution  and  allows  the   application











     developer to  package  high  resolution  timing  and  complete scoring
     functionality in a single package.

     Library Source Code Included
     Since the source code  to  the  TPHRT  linkable libraries is included,
     users needing  a particular timing function not implemented can modify
     the TPHRT functions to suit their particular requirements.


     Functional Overview


     The  functionality  of  TPHRT  can  be divided into  several  distinct
     categories of timer services:

     TPHRT Timer Logic
     These functions initialize  the  TPHRT  timing  system,  calibrate the
     timing logic, provide a low level interface to the PC timing hardware,
     and perform miscellaneous timing functions that  are  generally hidden
     from  the  user.  Some of these functions will be of interest to users
     who  need to design their own timer functions and want to build on the
     TPHRT low level timer logic.

     Generic Timer Functions
     These  functions allow the user to  control  arbitrary  event  timers.
     Functions exist to start, stop,  suspend,  resume,  name,  get elapsed
     time  and activation counts, and to  generate  detailed  reports  that
     summarize  all  timer  activity.  Timer  reports may be output to  the
     display, a disk  file,  or  to  the printer. A setmode function allows
     users to run timers  with  interrupts enabled or disabled.  The number
     of timers active concurrently is restricted  only by available memory.

     BIOS Interrupt Timer Functions
     These  functions  are  similar  to  the Generic Timer  Functions,  but
     operate only on BIOS  interrupts.   Using these functions the user may
     install  timer   logic  in  any  PC  interrupt  vector,  and  complete
     information on  that interrupt's activity can be generated.  Interrupt
     timer  reports  list  interrupt  activity  broken  down  by  interrupt
     function (contents of the AH register when the  interrupt  is invoked)
     and text  files  containing  interrupt  function  descriptions  may be
     loaded to describe each  interrupt  function  timer  in the BIOS timer
     report.    Interrupt  description  files  are  provided  for important
     software interrupts in the PC/MSDOS environment.   Multiple interrupts
     may be timed concurrently.

     Precision Delay Functions
     These functions allow the user  to  generate  delays  with microsecond
     accuracy. Functions exist to  generate  delays,  query the delay logic
     for available  delay resolution and minimum delay time possible (these
     are hardware dependent), and to  "fine tune" the delay calibration for
     one or more specific delay lengths.








                                    TPHRT  2






     Theory


     TPHRT works by directly  interfacing  with channel 0 of the 8253 timer
     chip found in all compatible PCs.  Channel 0 counts  from  65535 to 0,
     when  it  triggers  BIOS  interrupt  8 and begins counting from  65535
     again.  Interrupt 8 is the hardware timer interrupt, and it increments
     the DOS time  of  day  data  word  in  the  BIOS data area, checks for
     diskette motor activity  and  shuts  down  the  motor  if  needed, and
     finally calls BIOS interrupt 1C (hex), which is known as  the software
     timer tick.  At boot time, 1C contains an  IRET  instruction,  meaning
     there is no routine installed in  that  vector.   Since the 8253 has a
     period of 838 nanoseconds, the hardware timer tick occurs every 54.925
     milliseconds, or 18.2 times a second, which is  the  standard software
     time resolution of the PC.   The  8253  count can be read by accessing
     the appropriate IO port, and by reading the 8253 count along  with the
     low word DOS time of day count, we  can  construct  a  high resolution
     time stamp, which  is  the  base  unit  of  time  for TPHRT.  The only
     modifications we make to the PC  environment  is to change the mode of
     channel 0 to give the output count a 50 percent duty cycle, which does
     not  impact  any  other  PC  operations.    Thus  we  have  a  simple,
     unobtrusive,  highly  accurate  time  reference  with  838  nanosecond
     resolution.    Once  a highly accurate time reference is available, we
     can use it to calibrate a  simple  function that contains an inner and
     outer loop to generate precision delays.

     The accuracy of TPHRT is as  accurate  as  the 8253 timer chip and the
     ability of the software to measure the overhead in retrieving the 8253
     and DOS time of day data.  With the advent of  advanced  chips  in the
     80286 and 80386 class, the  effects  of  instruction  prefetch queues,
     pipelining, and  cache memory become significant and the same sequence
     of  instructions  may  take  different  amounts  of  time  to  execute
     depending   on   the   interaction   of  the  processor's  performance
     optimization  mechanisms.    The  end  result  is  twofold:    TPHRT's
     calibration  routines may experience inaccuracies, and software  under
     test  may  give  different timing results on different runs.  Normally
     the "jitter" introduced by these conditions  is  on the order of a few
     microseconds.

     A  major  source  of  apparent  erratic timer behavior comes from  the
     interaction of asynchronous software and hardware interrupts  that may
     occur  during a timed interval.  While  the  PC/MSDOS  environment  is
     essentially single-threaded,  there  is  enough  "background" activity
     occurring  in the form of timer and  keyboard  interrupts  that  these
     interrupts  may occur during an timed interval,  and  the  time  these
     interrupts  take  to  complete  are  naturally  counted  in the  timed
     interval.   For very short duration timing a  TPHRT  timer  mode  with
     interrupts disabled is available,  but  that  may  not be suitable for
     longer  duration  timings,  or  when  concurrent  timer   activity  is
     required.  Be aware that few results in  the  PC  environment  will be
     exactly  repeatable,  and  that some variance in the timing results is
     unavoidable.

     The high resolution  delay  function of TPHRT is particularly affected
     by  background  interrupts  and  processor   performance  optimization
     mechanisms.    The  initial delay calibration will yield delays with a
     variance of from one to three percent of the requested delay interval.



                                    TPHRT  3





     Additional functions are available to optimize  the  delay calibration
     to a specific delay interval, and using these functions can reduce the
     delay  error  to  between  zero  and  one  percent,  and thus they are
     recommended for critical applications.


     TPHRT Function Descriptions


     The following is  a  brief  synopsis  of the functions found in TPHRT.
     This chapter is meant to give  the  user  a brief overview, and is not
     meant to be a definitive reference.  It  is  essential  that  the user
     review the  complete  function  reference  in  the  Function Reference
     chapter before using any TPHRT function.  Some functions may  not work
     as they would appear at first inspection, and in order to achieve high
     performance, TPHRT has a minimum of internal error checking to prevent
     such catastrophes as NULL pointer references.

     TPHRT Timer Logic

     Initialization functions

     t_request           Requests the number of timers needed.
     t_start             Initializes the TPHRT timer logic.
     t_stop              Shuts down TPHRT and frees allocated memory.

     Internal functions

     t_get               Gets TPHRT time stamp with interrupts
                         enabled.
     t_hires_entry       Gets TPHRT time stamp with interrupts
                         disabled.  8253 count is reset.
     t_hires_exit        Gets TPHRT time stamp and restores interrupts
     t_diff              Calculates elapsed time difference between
                         two TPHRT time stamps.
     t_calib             Calibrates TPHRT timer logic, resets all
                         timers, and calls the delay calibration
                         function.
     t_bios_entry        Receives timer start request from interrupt
                         service routine.
     t_bios_exit         Receives timer stop request from interrupt
                         service routine.
     t_bios_load_desc    Loads interrupt function description file
     t_hook_int          Installs timer calls in specified interrupt
                         vector.
     t_unhook_int        Removes timer calls from specified interrupt
                         vector.
     t_delay_calib       Calibrates delay logic.

     t_request is called by the user to specify the number of timers needed
     for generic timer  operations  if  the  user  wishes  to  override the
     default  number  of  timers provided (10).    Since  each  timer  data
     structure is  allocated dynamically, the number of timers available is
     restricted by the amount of heap available and the constraints  of the
     memory model you are using. If  t_request  is used in your program, it
     must be called before t_start.




                                    TPHRT  4





     t_start allocates the appropriate  amount  of  heap  for the number of
     timers requested, initializes those  timers,  and  calibrates  the low
     level timer routines.   t_start  must always be invoked prior to using
     any other timer functions with the exception of t_request.

     t_stop deallocates all allocated heap  associated  with  generic timer
     activity and shuts down the timer logic.  t_stop must be  called prior
     to program termination, and  no  further calls to TPHRT should be made
     unless t_start is invoked first.

     The TPHRT internal functions of primary interest to the programmer are
     t_get, which is the interface to  the  8253 timer chip;  t_diff, which
     calculates  the  elapsed  time  between  two  TPHRT  time stamps;  and
     t_calib, which calibrates the  timer  and delay logic to the host run-
     time environment.

     Generic TPHRT Timer Functions

     This class of functions implement general purpose timer functionality.

     t_entry             Starts the specified timer.
     t_exit              Stops the specified timer.
     t_suspend           Suspends the specified timer.
     t_resume            Resumes the specified suspended timer.
     t_setmode           Specifies timer mode - interrupts on or off.
     t_ask_timer         Gets accumulated activations and elapsed time
                         for the specified timer
     t_cvt_time          Converts microseconds to MM:SS.xxxxxx string.
     t_reset             Resets one or all timers.
     t_report            Generates timer report
     t_name              Associates string with specified timer for
                         display in timer report.
     t_rname             Specifies title of timer report.
     t_fname             Specifies destination file for timer report.
     t_set_report        Specifies type of timer report generated.

     t_entry  and  t_exit  provide  the  mechanism  to  start  and  stop  a
     microsecond timer.  Timers are specified by number from 0 to n-1 in C,
     and  1  to  n in Pascal.  The number of  timers  available  is  10  by
     default, but the user can use  t_request  to request as many timers as
     available heap allows.  Multiple timers may be active at the same time
     if interrupts are enabled.

     t_suspend and t_resume suspend and resume a timer previously activated
     by t_entry.  Timer activation count is not  incremented  when t_resume
     is called, which is useful if you are using timer activation counts to
     track subroutine  activations in a profiling application, and for some
     reason you wish to pause  the timer during the subroutine's activation
     (perhaps before a call to another routine) and then restart it.

     t_setmode  allows  the  user to specify whether  timers  operate  with
     interrupts enabled or disabled.   With  interrupts  enabled, intervals
     greater than 54925 microseconds may  be timed, and multiple timers may
     be active concurrently.  With  interrupts  disabled,  the  timer logic
     will "roll over" after 54925 usecs,  and  only one timer may be active
     at any time.  Timing short duration events with interrupts disabled is




                                    TPHRT  5





     useful  if  background   system  interrupts  are  causing  significant
     variations in timer results.

     t_ask_timer will return to  the  user  the  activation count and total
     elapsed time in microseconds for the specified timer.  t_cvt_time will
     convert  a microsecond time count into a  printable  string  with  the
     format MM:SS.xxxxxx.  Timer activation counts and  accumulated elapsed
     time can be reset to zero by using t_reset.

     t_report generates a complete  listing  of  all  timer activity.  This
     listing can be directed to the display, a  disk  file,  or  a printer.
     t_rname allows the user to give the timer report a  descriptive title.
     t_fname overrides the default disk file name for  timer  reports going
     to disk.  t_name allows the  user  to assign a descriptive text string
     to  a  timer number - this string will be printed next  to  the  timer
     number in the timer report.    Finally,  t_set_report  determines what
     timers are listed on  the  timer report: either only those timers that
     had  been activated, or all timers,  regardless  of  their  activation
     count, up to the highest timer number activated.

     BIOS Interrupt Timer Functions

     This  class  of  functions   implement   the   BIOS   interrupt  timer
     functionality.

     t_bios_start        Installs timers in specified interrupt
                         vectors.
     t_bios_stop         Removes all timers from interrupt vectors.
     t_bios_suspend      Suspends specified interrupt timing.
     t_bios_resume       Resumes interrupt timing in the specified
                         vectors.
     t_bios_set_user     Assigns timer to user specified interrupt.
     t_bios_set_file     Assigns interrupt function description file
                         name to the user specified interrupt timer.
     t_bios_ask          Returns activations and elapsed for the
                         specified interrupt function
     t_bios_reset        Resets one or all function timers of the
                         specified interrupt vector.
     t_bios_report       Generates BIOS interrupt timer report.
     t_bios_rname        Specifies title of BIOS timer report.
     t_bios_fname        Specifies destination file for BIOS timer
                         report.

     t_bios_start  initializes  BIOS interrupt timing  for  the  interrupts
     specified.    Heap  is  allocated  for the required  data  structures,
     interrupt function description files  are  loaded  if available, and a
     new interrupt service  routine  for  each  interrupt  to  be  timed is
     inserted in  the  interrupt  vector  table.    t_bios_stop essentially
     reverses  this  process,  freeing  allocated  heap  and  restoring the
     previous interrupt service vectors.    The  BIOS timer data structures
     are separate from the generic timer structures, and thus t_request has
     no effect on BIOS interrupt timer activity.

     t_bios_suspend and  t_bios_resume allow the user to suspend and resume
     BIOS interrupt timing  of  the specified interrupt(s).  All interrupts
     to be timed must be installed by t_bios_start, but timing can  then be
     immediately suspended by t_bios_suspend until the point in the program



                                    TPHRT  6





     that the user actually wants timing  to  begin, when it can be resumed
     with t_bios_resume.

     t_bios_set_user enables the user to specify an interrupt  to  be timed
     that has not been provided for by TPHRT.  Each interrupt that is timed
     requires new interrupt  service  routine that when activated, starts a
     timer, calls the old vector, then stops the appropriate timer.   TPHRT
     provides new timer ISRs for the major device, EMS,  Mouse,  and  MSDOS
     interrupts, along with  a  spare  ISR  that  can be used for any other
     interrupt the user might want to time.   t_bios_set_user  assigns this
     spare timer ISR to the specified interrupt, allowing the user  to time
     any interrupt vector in the PC environment.   If  the  interrupt  is a
     software interrupt that has specific functions (as requested by the AH
     register when the  interrupt  is  invoked)  the  user  may  specify an
     interrupt function description  file using t_bios_set_file which loads
     a text file containing interrupt function descriptions if that file is
     in the current directory.    Interrupt  function description files are
     provided for all the software interrupts TPHRT has standard timer ISRs
     for.

     t_bios_ask   and  t_bios_reset  function  like  their  generic   timer
     counterparts and allow the user to request specific BIOS timer results
     or to reset  those results to zero.

     t_bios_report, t_bios_rname, and  t_bios_fname modify and generate the
     BIOS timer report in the same way as their generic  timer counterparts
     t_report, t_rname, and  t_fname  generate and modify the generic timer
     report.

     Be sure and carefully review the documentation for t_bios_start before
     using the BIOS interrupt timing functions.

     Delay Functions

     This class of functions  implement  the  microsecond  resolution delay
     functionality.

     t_ask_delay         Requests parameters for requested delay time.
     t_do_delay          Executes delay with interrupts disabled.
     t_do_delay_wints    Executes delay with interrupts enabled.
     t_calc_delay_ff     Optimizes delay calibration to a specified
                         delay duration.
     t_get_delay_ff      Returns delay calibration optimization.
     t_set_delay_ff      Sets current delay calibration optimization.
     t_min_delay         Returns minimum delay possible with current
                         hardware.
     t_res_delay         Returns delay resolution possible with
                         current hardware

     t_ask_delay   requests  delay  parameters  for  the  specified   delay
     interval.    These  parameters  are  stored in a user allocated  TPHRT
     defined  data structure and are passed  to  either  t_do_delay,  which
     generates  the  delay  with  interrupts disabled, or t_do_delay_wints,
     which generates the delay with interrupts enabled.

     t_calc_delay_ff,  t_set_delay_ff, and t_get_delay_ff, allows the  user
     to  have  the  TPHRT  delay  logic  "fine  tune"  its calibration to a



                                    TPHRT  7





     particular delay interval.   t_calc_delay_ff  calculates  and installs
     the  new  delay  calibration  optimization, t_set_delay_ff enables the
     user  to   install   a   previously   calculated   optimization,   and
     t_get_delay_ff retrieves the current delay optimization.

     t_min_delay returns the minimum  delay  possible  in the host run-time
     environment.  t_res_delay returns the resolution of the delay function
     in the host run-time environment.


     Examples


     While  the  accompanying  pages  spell  out the functions of TPHRT  in
     detail, as the saying goes, "a picture is worth a thousand words".  In
     keeping with that philosophy,  we  have  included several source files
     that demonstrate different  areas  of TPHRT functionality. They are as
     follows:

     DEMO             Basic  TPHRT operation.  Shows inline and  subroutine
                      timing, report generation.

     TESTBIOS         BIOS interrupt timing.

     SEEKTEST         Hard disk seek  test  benchmark.    Uses  both inline
                      timers and BIOS interrupt timing to  fully  test disk
                      seek performance.

     DELAY            Demonstration of high resolution delay functionality.

     WATCH            Full function Taylor Split stopwatch.   Shows  how to
                      activate timers with a user written interrupt service
                      routine.

     These programs are carefully commented and  provide  valuable insights
     into effective TPHRT operation.


     Technical Support


     Technical  support for licensed users of TPHRT  is  available  by  the
     following methods:

        1.  By US Mail directed to P.O. Box 22, Mt. Pleasant MI 48804.

        2.  By   Compuserve  electronic   (Easyplex)   mail   directed   to
            73047,1765.


     Shareware


     This software is distributed as "Shareware", which allows  you  to use
     the complete product  on  an  evaluation  basis  to get a feel for its
     quality, functionality, and value  to  you as a developer or end user.
     At the end of your evaluation (14 days is a  widely  accepted time for



                                    TPHRT  8





     the evaluation period) you may continue to use the software product by
     sending in a registration  fee  to  the  program author/vendor, or you
     must discontinue use of the software and are free to pass your copy on
     to another user for evaluation.   The Shareware concept allows quality
     software  to   be  distributed  at  far  less  cost  than  traditional
     commercial products, and allows the user to "try before you buy".

     TPHRT is a single language functional subset of PCHRT,  the  PC  Timer
     Toolbox distributed through traditional  commercial  channels  by Ryle
     Design.    MSCHRT  for  Microsoft  C  and  TCHRT  for Turbo C are also
     available as Shareware, and  provide  the  same  suite of functions as
     TPHRT.

     Registration of TPHRT costs $20.00,  and in return users receive units
     for  TP 5 & 5.5 (without the  shareware  messages),  complete  library
     source code, and technical  support  by  US  Mail and Compuserv Email.
     Distribution of TPHRT object  code  in  commercial applications is not
     permitted.

     Users  developing commerical applications or needing additional  timer
     functionality should purchase PCHRT, the commerical version  of TPHRT,
     which costs $49.95.  PCHRT includes all the functions of  TPHRT, along
     with three  new timer functions, five new synchronous alarm functions,
     four functions to run the timer tick interrupt at a user defined rate,
     and two utilities to  time  execution  and  profile interrupts of most
     executable programs without recompilation.  PCHRT comes with libraries
     for  Turbo  C  and MSC in small, medium, compact, and large models, as
     well  as units for Turbo Pascal V5 and V5.5.  Full library source code
     for both Pascal and C is provided, along  with  a  printed  manual and
     telephone technical support.  Distribution  of  PCHRT  object  code in
     commercial applications is permitted without royalties.

     An order form  for  these  products  appears  as the last page of this
     document.


























                                    TPHRT  9

































































                                    TPHRT  10











                            TPHRT Function Reference


     t_ask_delay


     Purpose          Fills delay parameter structure with  required values
                      for requested delay interval

     Pascal           procedure  t_ask_delay(usec  :  longint;  var   dp  :
                      tdelay_type)

     Synopsis         Parameters accepted by the delay functions are stored
                      in  a  TPHRT  defined,  user allocated data structure
                      tdelay_type.   t_ask_delay accepts the desired  delay
                      interval  in  microseconds,  and  fills   the  passed
                      tdelay_type structure with the appropriate parameters
                      to generate the requested delay.  This data structure
                      is    then    passed    to   either   t_do_delay   or
                      t_do_delay_wints,   where   the   actual   delay   is
                      generated.

     Caveat           None

     See Also         t_do_delay, t_do_delay_wints


     t_ask_timer


     Purpose          Returns activation  and  elapsed  time  count  for  a
                      specified timer

     Pascal           procedure  t_ask_timer(tnum  :   integer;   var  hits
                      :longint; var elapsed : longint)

     Synopsis         The  user may retrieve activation counts and  elapsed
                      time  (in 2microseconds)  for  the  specified  timer.
                      Timers are specified from 0 to n-1 in C and from 1 to
                      n in Pascal.  The number of timers n defaults  to 10,
                      but t_request  may  be  called  prior  to  t_start to
                      increase that number.

     Caveat           No range  checking is done.  A NULL pointer reference
                      is possible if information on a non-existant timer is
                      requested.

     See Also         t_request, t_reset






                                    TPHRT  11





     t_bios_ask


     Purpose          Returns activation count and elapsed time for  one or
                      all functions associated with a BIOS interrupt timer

     Pascal           procedure t_bios_ask(whichint : integer; whichfunc  :
                      integer; var hits : longint; var elapsed : longint)

     Synopsis         The users passes a single BIOS  timer  interrupt mask
                      (see  t_bios_start) and either an interrupt  function
                      in the range of 0 to 255 or -1, which causes  all the
                      interrupt   function  timers  to  be  summed.     The
                      accumulated number of activations and elapsed time in
                      microseconds is returned.

                      The summation of all function  timers  by  passing -1
                      feature is useful if a hardware  interrupt  that does
                      not have specific function  classes  is  being timed.
                      Interrupt functions are  specified by the contents of
                      the  AH  register,  and  since  the  AH  register may
                      contain  random, non-specific values when a  hardware
                      interrupt  is invoked, many timers for the  interrupt
                      will show some activity.   These  must  be  summed in
                      order to  determine  the  activity  of  the  hardware
                      interrupt.

     Caveat           No range  checking is done.  A NULL pointer reference
                      is possible if information is  requested  on  an non-
                      existant interrupt timer.

     See Also         t_bios_start, t_bios_reset


     t_bios_entry


     Purpose          Receives  timer  start  requests  from  an  interrupt
                      service routine

     Pascal           procedure t_bios_entry(whichint :  integer; whichfunc
                      : integer)

     Synopsis         BIOS interrupt vectors  being timed call this routine
                      to start the appropriate  timer  for  this interrupt.
                      Parameter whichfunc is the value in  the  AH register
                      when   the  interrupt  was  invoked,  which  is   the
                      interrupt function requested in a software interrupt.

     Caveat           This is  an internal TPHRT procedure and is not meant
                      to be called by the user.

     See Also         t_bios_exit







                                    TPHRT  12





     t_bios_exit


     Purpose          Receives  interrupt  timer  stop  requests   from  an
                      interrupt service routine

     Pascal           procedure t_bios_exit(whichint : integer)

     Synopsis         BIOS interrupt vectors call this routine to  stop the
                      appropriate timer for this  interrupt.    The current
                      active function timer  for this interrupt is stopped,
                      and  if  the  interrupt  was entered recursively, the
                      previous function timer is restarted.

     Caveat           This is  an internal TPHRT procedure and is not meant
                      to be called by the user.

     See Also         t_bios_entry


     t_bios_fname


     Purpose          Specifies a name for the  disk  file  created  by the
                      BIOS timer report if the disk  destination  option is
                      selected

     Pascal           procedure t_bios_fname(fname : string)

     Synopsis         By calling t_bios_report(1)  the BIOS timer report is
                      generated  and  sent  to  an  ASCII disk file.    The
                      default  name   for   this   file   is  BIOSTIME.TXT.
                      t_bios_fname  allows the user to specify a  different
                      filename,   with   complete   disk,  path,  and  file
                      specification.

     Caveat           Maximum  disk/path/filename  string   length   is  67
                      characters

     See Also         t_bios_report


     t_bios_load_desc


     Purpose          Loads   an   interrupt   description  file  into  the
                      appropriate interrupt timer data structure

     Pascal           procedure t_bios_load_desc(whichint :  integer; fname
                      : string)

     Synopsis         Each  interrupt  vector  being  timed   contains  256
                      timers,  one for each possible interrupt function  as
                      indicated  by  the  AH   register.      An  interrupt
                      description  file  contains  brief  twenty  character
                      descriptions  of  each  interrupt  function,  and  if
                      loaded, these will appear  along  with  the interrupt



                                    TPHRT  13





                      function  number in the BIOS interrupt timer  report.
                      whichint   is  a  BIOS  timer  interrupt  mask   (see
                      t_bios_start),  and  data_file  is the disk/path/file
                      descriptor.  No error is generated  if  the specified
                      file is not found.

                      See  one of the supplied interrupt description  files
                      (such as 10.INT) for the layout of these files.

                      This routine is called automatically by t_bios_start.

     Caveat           No range checking is done.  NULL pointer reference is
                      possible.

     See Also         t_bios_start, t_bios_set_file


     t_bios_report


     Purpose          Generates BIOS interrupt timer report

     Pascal           procedure t_bios_report(integer : whereto)

     Synopsis         This routine generates a  complete  timer  report for
                      all active BIOS  interrupt timers.  whereto specifies
                      the report's  destination - 0 sends the report to the
                      display, 1 to a disk file, and 2 to a printer.

     Caveat           None.

     See Also         t_bios_rname, t_bios_fname


     t_bios_resume


     Purpose          Resumes suspended BIOS interrupt timing

     Pascal           procedure t_bios_resume(biosmask : integer)

     Synopsis         This  routine  enables   previously   suspended  BIOS
                      interrupt  timing.  biosmask contains the BIOS  timer
                      bitmask (see t_bios_start)  of the interrupts to have
                      timing re-enabled.

     Caveat           No range checking is done.  NULL pointer reference is
                      possible if a interrupt is  referenced  that  was not
                      setup by t_bios_start.

     See Also         t_bios_suspend, t_bios_start









                                    TPHRT  14





     t_bios_reset


     Purpose          Resets one or  all  timers  associated  with  a timed
                      interrupt

     Pascal           procedure t_bios_reset(whichint :  integer; whichfunc
                      : integer)

     Synopsis         This function allows the  user  to  reset  either one
                      specific  or  all  function  timers associated with a
                      timed interrupt.  Specific function timers are in the
                      range of 0 to 255.  Passing -1  for  whichfunc resets
                      all  256  timers  associated  with a timed interrupt.
                      The interrupt is specified  by  whichint  which  is a
                      single BIOS interrupt timer mask (see t_bios_start).

     Caveat           No range checking is done.  NULL pointer reference is
                      possible   if  a  non-existant  interrupt  timer   is
                      specified.

     See Also         t_bios_start, t_bios_ask


     t_bios_rname


     Purpose          Specifies title for BIOS timer report

     Pascal           procedure t_bios_rname(rname : string)

     Synopsis         This function  allows the user to specify a title for
                      the  BIOS  interrupt  timer  report.    If   none  is
                      specified,  the  title  used  is Bios Interrupt Timer
                      Summary.  The title is horizontally centered.

     Caveat           Max string length is 80 characters.

     See Also         t_bios_report, t_bios_fname


     t_bios_set_file


     Purpose          Sets the interrupt  function description file for the
                      user specified interrupt timer

     Pascal           procedure t_bios_set_file(ufile : string)

     Synopsis         When a user specifies the optional interrupt  to time
                      using  t_bios_set_user, a file of interrupt  function
                      descriptions   may  also  be  specified  using   this
                      function.

     Caveat           Max file description length is 67 characters.

     See Also         t_bios_load_desc, t_bios_set_file



                                    TPHRT  15





     t_bios_set_user


     Purpose          Specifies the optional interrupt to time

     Pascal           procedure t_bios_set_user(user_int : integer)

     Synopsis         The  TPHRT  BIOS timing functionality  has  built  in
                      support for the various BIOS interrupts of interest -
                      disk, CRT, serial,  parallel, DOS, EMS, keyboard, and
                      mouse.   This function allows the user to specify any
                      other interrupt to be timed, and when t_bios_start is
                      invoked with the  USER  bit set in the timer bitmask,
                      the interrupt specified by t_bios_set_user  will have
                      timers inserted in its vector.

     Caveat           The  ISR  supplied  that  is  hooked  into  the  user
                      specified interrupt (t_new_user in the  .ASM modules)
                      does not propagate the  FLAGS  register.   If you are
                      attempting to time  a software interrupt that returns
                      meaningful information  in  the  FLAGS  register, you
                      should  modify  the  t_new_user  routine so that it's
                      last instruction is a RETF 2 instead of  IRET.   This
                      is documented in the t_new_user code.

     See Also         t_bios_start, t_bios_set_file


     t_bios_start


     Purpose          Initializes BIOS interrupt timing

     Pascal           procedure t_bios_start(biosmask : integer)

     Synopsis         This function initializes BIOS interrupt timing.  The
                      interrupts to be timed are  selected  by  passing the
                      appropriate bitmask:

                      CRT10       INT 10h Video Services

                      DISK        INT 13h Disk Services

                      COM         INT 14h Serial Port Services

                      KEYBD       INT 16h Keyboard Services

                      PRT         INT 17h Printer Services

                      DOS21       INT 21h MSDOS System Services

                      MOUSE       INT 33h Mouse Services

                      EMS         INT 67h EMS Services

                      USER        User Specified Interrupt




                                    TPHRT  16





                      As an  example, to insert timers in the DOS interrupt
                      and   the   disk   interrupt,   one    would   invoke
                      t_bios_start(DISK+DOS21).

                      Each  interrupt timed  actually  has  256  individual
                      timers,  one  for  each  possible  value  in  the  AH
                      register,  which indicates what specific function  of
                      that interrupt has been requested.    The  timer data
                      structure   is   allocated  dynamically,   and   each
                      structure requires approximately 9200 bytes, so there
                      is a limit imposed by  the memory model being used as
                      to  how  many  interrupt  timers  may  be  requested.
                      t_bios_start returns FALSE  in  C  if  the  amount of
                      memory  needed  is not available,  while  a  run-time
                      error occurs in Turbo Pascal.

                      If the USER bitmask is  to  be  used, t_bios_set_user
                      must  be  invoked  prior  to t_bios_start to indicate
                      what interrupt the USER bitmask will time.

                      Interrupt   function   description  files   for   the
                      supported interrupts are supplied, and will be loaded
                      if they are present  in  the  run-time directory.  As
                      these  will  dramatically  improve  the   information
                      presented in the BIOS  interrupt  timer  report, they
                      are  recommended.  t_bios_set_file associates a  file
                      with the USER selected interrupt.

                      If testing code with  BIOS  interrupt  timing active,
                      and the code fails prior to calling t_bios_stop, then
                      you  should immediately reboot your computer, as  the
                      interrupt vectors being timed  are  pointing  to non-
                      existant code.

     Caveat           Approximately  9200  bytes  are  required   for  each
                      interrupt to be timed.  Memory constraints can affect
                      this function.

     See Also         t_bios_stop,     t_bios_set_user,    t_bios_set_file,
                      t_bios_suspend, t_bios_resume


     t_bios_stop


     Purpose          Stops all BIOS interrupt timing

     Pascal           procedure t_bios_stop;

     Synopsis         This  function removes all timers from all  interrupt
                      vectors selected by t_bios_start and  deallocates all
                      memory associated with those timers.

     Caveat           This function must be called prior to program exit in
                      order to restore the interrupt environment.    If the
                      code under  test  fails  prior  to  t_bios_start  the




                                    TPHRT  17





                      interrupt  vectors  being  timed  will be pointing to
                      non-existant code, and a system hang is likely.

     See Also         t_bios_start, t_bios_suspend, t_bios_resume


     t_bios_suspend


     Purpose          Suspends interrupt timing selected by t_bios_start

     Pascal           procedure t_bios_suspend(biosmask : integer)

     Synopsis         BIOS  interrupt timing is initiated by  t_bios_start,
                      and terminated by t_bios_stop.   t_bios_suspend gives
                      the user the ability to selectively disable timing on
                      a particular interrupt or  interrupts  by  passing an
                      appropriate  biosmask  (see   t_bios_start).     This
                      suspended interrupt timing may  be  later  resumed by
                      invoking t_bios_resume.

     Caveat           No range checking is done.  NULL pointer reference is
                      possible   if  a  non-existant  interrupt  timer   is
                      referenced.

     See Also         t_bios_resume, t_bios_start, t_bios_stop


     t_calc_delay_ff


     Purpose          Optimizes  delay calibration  for  a  specific  delay
                      interval

     Pascal           function   t_calc_delay_ff(delay_time    :   longint;
                      ints_or_not : integer)

     Synopsis         This  function  optimizes  delay  calibration   to  a
                      specific  delay interval.  ints_or_not can be  either
                      INTS_ON,  indicating a delay with interrupts  enabled
                      should  be used for the optimization calculation,  or
                      NO_INTS_ON,   which  indicates  that  a  delay   with
                      interrupts disabled should be  used.    This function
                      sets a  global value that is used by t_ask_delay, and
                      the value is also returned,  so that it may be stored
                      for later use with the delay interval optimized.

     Caveat           None

     See Also         t_set_delay_ff, t_get_delay_ff, t_ask_delay


     t_calib


     Purpose          Calibrates the TPHRT timer and delay logic




                                    TPHRT  18





     Pascal           procedure t_calib

     Synopsis         This function calibrates the  low  level  TPHRT timer
                      and delay logic.   It  is  called  by t_start, so the
                      user  need  not  explicitly  call this routine unless
                      additional delay calibration is needed after a system
                      parameter has been  modified  during a timing run - a
                      keyboard initiated system clock  speed  change  is an
                      example.    t_calib  calls t_delay_calib to calibrate
                      the TPHRT delay logic.

     Caveat           None

     See Also         t_delay_calib


     t_cvt_time


     Purpose          Converts a microsecond count to a MM:SS.xxxxxx format
                      string

     Pascal           function t_cvt_time(usec : longint; tstring : string)
                      : string

     Synopsis         This function accepts a microsecond count and returns
                      a printable character string in a simple time format.
                      This function is useful to  the  user  who  wishes to
                      build custom timer reports.

     Caveat           Destination string length should be 13 characters.

     See Also         t_ask_timer, t_bios_ask


     t_delay_calib


     Purpose          Calibrates the TPHRT delay logic

     Pascal           procedure t_delay_calib

     Synopsis         This  function  calibrates the delay  loops  used  to
                      generate  precision  microsecond  delays.  Additional
                      calibration   is   available   from  t_calc_delay_ff.
                      t_delay_calib is called by t_calib, so the  user need
                      not call it explicitly.

     Caveat           None

     See Also         t_calib, t_calc_delay_ff









                                    TPHRT  19





     t_diff


     Purpose          Calculates  the difference  between  two  TPHRT  time
                      stamps

     Pascal           function t_diff(start, stop : TPHRT_type) : longint

     Synopsis         This function returns the difference  in microseconds
                      between two TPHRT time stamps, which are generated by
                      calls  to  t_get.   t_diff and t_get  are  low  level
                      functions  that  are  of  interest primarily to users
                      building timer functions not implemented in TPHRT.

     Caveat           Don't pass the time stamps in the wrong order.

     See Also         t_get


     t_do_delay


     Purpose          Generates   a   precision  microsecond   delay   with
                      interrupts disabled

     Pascal           procedure t_do_delay(dp : tdelay_type)

     Synopsis         This function generates a precision microsecond delay
                      with interrupts disabled.   Using  this  function for
                      delays greater than 54925 microseconds will cause the
                      PC  clock to lose time.   Delay  parameters  of  type
                      tdelay_type for  the  delay  interval  desired    are
                      generated by t_ask_delay.

                      Delay interval error will be in the range  of  one to
                      three percent if t_calc_delay_ff is not used, zero to
                      one percent if it is.

     Caveat           Interrupts are disabled during the delay period

     See Also         t_ask_delay, t_calc_delay_ff, t_do_delay_wints


     t_do_delay_wints


     Purpose          Generates   a   precision  microsecond   delay   with
                      interrupts enabled

     Pascal           procedure t_do_delay_wints(dp : tdelay_type)

     Synopsis         This function is  identical to t_do_delay except that
                      interrupts are  enabled  during  the  delay interval.
                      This  will  introduce some additional  error  in  the
                      delay produced, but is more appropriate for  longer (
                      > 54925  usec)  delays.    Delay  parameters  of type




                                    TPHRT  20





                      tdelay_type for  the  delay  interval  desired    are
                      generated by t_ask_delay.

                      Delay interval error will be in the range  of  one to
                      three percent if t_calc_delay_ff is not used, zero to
                      one percent if it is.

     Caveat           Interrupt  activity  may  cause  random errors in the
                      delay interval produced.

     See Also         t_do_delay, t_ask_delay, t_calc_delay_ff


     t_entry


     Purpose          Starts the specified general purpose timer

     Pascal           procedure t_entry(timernum : integer)

     Synopsis         This   function   starts   a  general  purpose  timer
                      counting.  Timers are specified from 0 to  n-1  in C,
                      and from 1  to  n  in  Pascal.  The default number of
                      timers  is  10,  but that can be  modified  prior  to
                      calling t_start  by  passing  the  number  of  timers
                      needed to t_request.

                      Interrupts  are  normally  enabled  during  a  timing
                      interval.    t_setmode  can   be   used   to  disable
                      interrupts during any or all timing intervals.

     Caveat           No range checking is done.    NULL  pointer reference
                      possible if non-existant timer is started.

     See Also         t_exit, t_setmode



     t_exit


     Purpose          Stops the specified general purpose timer

     Pascal           procedure t_exit(timernum : integer)

     Synopsis         This function stops a general purpose timer counting.
                      Activation count and accumulated elapsed time for the
                      specified  timer  is  updated.   Timers are specified
                      from  0 to n-1 in C, and from 1 to n in Pascal.   The
                      default  number  of  timers is 10, but  that  can  be
                      modified  prior  to calling t_start  by  passing  the
                      number of timers needed to t_request.

     Caveat           No range checking is done.    NULL  pointer reference
                      possible if non-existant timer is started.

     See Also         t_entry



                                    TPHRT  21





     t_fname


     Purpose          Changes name of timer report file

     Pascal           procedure t_fname(fname : string)

     Synopsis         t_report can send its  output  to  a disk file, which
                      has the default name TIMER.TXT.  This function allows
                      the user to assign a different disk/path/file name to
                      this file.

     Caveat           No  checking  is  done  to  determine  if   the  file
                      description is valid.  Maximum  string  length  is 67
                      characters.

     See Also         t_rname, t_report


     t_get


     Purpose          Retrieves  a   high   resolution   time   stamp  with
                      interrupts enabled

     Pascal           procedure t_get(var timestamp : TPHRT_type)

     Synopsis         This function interrogates the  8253  timer  chip and
                      the low 16  bits  of  the  DOS time of day data words
                      fills  the passed TPHRT_type data structure with  the
                      microsecond  resolution  timestamp.    This   is  the
                      fundamental unit of time for TPHRT.  The elapsed time
                      between two TPHRT_type  time stamps may be determined
                      by t_diff.

     Caveat           Interrupts are enabled when t_get returns.

     See Also         t_hires_entry, t_hires_exit


     t_get_delay_ff


     Purpose          Retrieves the current delay calibration optimization

     Pascal           function t_get_delay_ff : real

     Synopsis         t_calc_delay_ff  calculates  and  installs  a   delay
                      calibration  optimization  for   a   specified  delay
                      interval length.  Using this  additional optimization
                      can  vastly  improve  the  TPHRT  delay  accuracy  in
                      critical  applications.    t_get_delay_ff returns the
                      current  delay  calibration optimization  in  effect.
                      The default value (i.e. - no additional optimization)
                      is 1.00.

     Caveat           None



                                    TPHRT  22





     See Also         t_calc_delay_ff, t_set_delay_ff


     t_hires_entry


     Purpose          Initiates timing with interrupts disabled

     Pascal           procedure t_hires_entry(var timestamp : TPHRT_type)

     Synopsis         This   function,   like   t_get,  retrieves  a  TPHRT
                      timestamp from the timing  hardware.    Unlike t_get,
                      t_hires_entry resets the 8253 timer  chip  to  0, and
                      interrupts are disabled at exit.  This  facilitates a
                      timing mode (set by  t_setmode)  that  functions with
                      interrupts disabled.

     Caveat           Since the 8253 is reset, only one timer may be active
                      at  any  one  time.  The timer will "roll over" after
                      54925  usec,  so  this  mode  is  suitable  for short
                      duration timing  only.  This is a low level function,
                      and is not meant to be called by the user.

     See Also         t_hires_exit, t_setmode


     t_hires_exit


     Purpose          Concludes a timing interval with interrupts disabled

     Pascal           procedure t_hires_exit(var timestamp : TPHRT_type)

     Synopsis         This  is the companion function to t_hires_entry  and
                      completes a timing interval with interrupts disabled.
                      At exit interrupts are enabled.

     Caveat           See t_hires_entry.

     See Also         t_hires_entry, t_setmode


     t_hook_int


     Purpose          Installs timers in the specified interrupt vector

     Pascal           procedure t_hook_int(int_no : integer)

     Synopsis         This  function  installs  timers  in   the  specified
                      interrupt  vector  to enable precise  timing  of  the
                      interrupt activity.

     Caveat           This is a low  level  function and is not meant to be
                      called by  the user.  Users wishing to understand how
                      TPHRT interrupt timing is accomplished should inspect
                      the source code to this routine.



                                    TPHRT  23





     See Also         t_unhook_int


     t_min_delay


     Purpose          Returns   minimum   delay   possible   in    run-time
                      environment

     Pascal           function t_min_delay : longint

     Synopsis         The minimum delay interval that can  be  generated by
                      t_do_delay  or t_do_delay_wints varies with the  run-
                      time hardware environment.  This function returns the
                      minimum  delay in microseconds that can be  generated
                      in the current environment.

     Caveat           None

     See Also         t_res_delay


     t_name


     Purpose          Associates a descriptive string with a generic timer

     Pascal           procedure  t_name(timerno  :  integer;  timername   :
                      tname)

     Synopsis         This  functions  assigns   a  string  of  maximum  20
                      characters to the specified generic timer number, and
                      this string  is  then  displayed  next  to  the timer
                      number in the timer report generated by t_report.

     Caveat           Maximum string length is 20 characters.

     See Also         None


     t_report


     Purpose          Generates a report of all generic timer activity

     Pascal           procedure t_report(whereto : integer)

     Synopsis         This  function  generates   a  report  of  all  timer
                      activity that was generated using t_entry and t_exit.
                      Parameter whereto specifies the report's destination:
                      0 sends the report to the CRT display, 1 sends  it to
                      a  disk file, and 2 sends it to  the  printer.    The
                      report  may  have  a  title  (see  t_rname),  and the
                      destination  disk   file   (if   used)   defaults  to
                      TIMER.TXT, but this can modified (see t_fname).





                                    TPHRT  24





                      Timer  reports  have   two  formats,  and  these  are
                      selected by t_set_report.   The HIGHWATER report type
                      shows  the  activity  of  all timers, including those
                      with zero activation counts, up to the highest number
                      timer activated.  The NONZERO report type  only shows
                      timers with nonzero activation counts.

     Caveat           None

     See Also         t_rname, t_fname, t_set_report


     t_request


     Purpose          Request specific number of generic timers

     Pascal           procedure t_request(numtimer : integer)

     Synopsis         t_request  provides  a  mechanism  to   override  the
                      default   number  of  generic  timers  allocated   by
                      t_start.  If the user requires more (or less) than 10
                      timers,   the  number  required  may  be  passed   to
                      t_request, and t_start  will attempt to allocate this
                      number of timers.

     Caveat           Call before t_start.

     See Also         t_start


     t_res_delay


     Purpose          Retrieves delay resolution of run-time environment

     Pascal           function t_res_delay : longint

     Synopsis         In slower hardware environments, the delay resolution
                      of t_do_delay  and  t_do_delay_wints  may  be several
                      microseconds.   This  function  returns  the run-time
                      delay resolution in units of tenths of a microsecond.
                      For example, if t_res_delay returns  a  value  of 44,
                      that means the delay  functions  can  generate delays
                      starting  at   their   minimum   delay   length  (see
                      t_min_delay)   and   up    in   increments   of   4.4
                      microseconds.

     Caveat           None

     See Also         t_min_delay


     t_reset


     Purpose          Resets one or all generic timers



                                    TPHRT  25





     Pascal           procedure t_reset(timernum : integer)

     Synopsis         This  function  zeros  the accumulated activation and
                      elapsed timer counts for  a  specified  timer  in the
                      range of 0  to  n-1 in C, or 1 to n in Pascal.  If -1
                      is passed, all generic timers are reset.

     Caveat           No range checking is done.  Null pointer reference is
                      possible if a non-existant timer is specified.

     See Also         t_ask_timer


     t_resume


     Purpose          Resumes a suspended generic timer

     Pascal           procedure t_resume(tnum : integer)

     Synopsis         Functions t_suspend and t_resume  allow  the  user to
                      stop and restart an active timer without incrementing
                      its activation count.

     Caveat           No range checking is done.  NULL pointer reference is
                      possible if a non-existant timer is specified.

     See Also         t_suspend


     t_rname


     Purpose          Assigns a title to the timer report

     Pascal           procedure t_rname(report_title : string)

     Synopsis         The  generic  timer  report  generated   by  t_report
                      contains   a   horizontally   centered  title,  which
                      defaults to Timer Summary.  This function  allows the
                      user to specify an alternate title.

     Caveat           Max string length is 80 characters.

     See Also         t_report, t_fname


     t_set_delay_ff


     Purpose          Sets delay calibration optimization

     Pascal           procedure t_set_delay_ff(delay_ff : real)

     Synopsis         This function allows the  user  to  set the new delay
                      calibration  optimization  for  use  by  t_ask_delay.
                      Delay  calibration optimization  for  a  given  delay



                                    TPHRT  26





                      interval  can be automatically calculated and set  by
                      t_calc_delay_ff.  Calling t_set_delay_ff with a value
                      of  1.00  removes  any delay calibration optimization
                      that was in effect.

     Caveat           None

     See Also         t_calc_delay_ff, t_get_delay_ff, t_ask_delay


     t_setmode


     Purpose          Sets generic timing mode

     Pascal           procedure t_setmode(modetype : integer)

     Synopsis         Two modes of generic  timing  are  available: INTS_ON
                      enables generic timing  using t_entry and t_exit with
                      interrupts  enabled,  and  this  is the default mode.
                      NO_INTS_ON enables timing  with  interrupts disabled,
                      and this mode  is particularly suitable for extremely
                      short  duration  timing  that   may   be   skewed  by
                      background interrupt activity.   In  this  mode, only
                      one timer may be active at any time,  and  each timer
                      will   "roll   over"   after  54925  microseconds  of
                      continuous activation.

                      As long as only one timer is active at once,  the two
                      timer modes may be freely  mixed.  In order to change
                      modes, call t_setmode with the desired mode  prior to
                      calling the t_entry/t_exit functions.

     Caveat           NO_INTS_ON  mode  is  not  compatible  with  multiple
                      active timers or BIOS interrupt timing.

     See Also         None


     t_start


     Purpose          Initializes TPHRT timing functions

     Pascal           procedure t_start

     Synopsis         This function  initializes  the  entire  TPHRT timing
                      system, and must  be  called prior to any other TPHRT
                      functions with the  exception  of  t_request.    If a
                      different  number  of  timers  other than the default
                      number provided (10) is required, t_request should be
                      called prior to t_start to specify the number needed.
                      In C,  if t_start can allocate enough heap to fulfill
                      the timer  request,  it  will  do  so,  calibrate the
                      timing  system,  and  return  TRUE.    If  the memory
                      request  fails,  it  will  return  FALSE.    In Turbo
                      Pascal, memory allocation failure  will  result  in a



                                    TPHRT  27





                      run-time error.  Each timer requires approximately 35
                      bytes of heap.

                      The 8253 timer chip is set to mode 2.

     Caveat           None

     See Also         t_request, t_stop


     t_stop


     Purpose          Shuts down TPHRT timing logic

     Pascal           procedure t_stop

     Synopsis         This  function  deallocates  all heap associated with
                      generic timers and restores the  8253  timer  chip to
                      mode 3.  It must be called prior to program exit, and
                      no TPHRT calls (except t_request) are valid without a
                      call to t_start to reinitialize the timing system.

     Caveat           None

     See Also         t_start, t_request


     t_suspend


     Purpose          Suspends an active generic timer

     Pascal           procedure t_suspend(tnum : integer)

     Synopsis         Functions t_suspend and t_resume  allow  the  user to
                      stop and restart an active timer without incrementing
                      its activation count.

     Caveat           No range checking is done.  NULL pointer reference is
                      possible if a non-existant timer is specified.

     See Also         t_resume


     t_unhook_int


     Purpose          Removes timers from the specified interrupt vector

     Pascal           procedure t_unhook_int(int_no : integer)

     Synopsis         This  function  removes  timers  from  the  specified
                      interrupt  vector  to  disable  precise timing of the
                      interrupt activity.





                                    TPHRT  28





     Caveat           This is a low  level  function and is not meant to be
                      called by  the user.  Users wishing to understand how
                      TPHRT interrupt timing is  accomplished  may  want to
                      inspect the source code to this routine.

     See Also         t_hook_int






















































                                    TPHRT  29





                            TPHRT V3.00 Registration


     Name ______________________________ Company ______________________________

     Address __________________________________________________________________

     City/State/Zip ___________________________________________________________

     Telephone _______________________ Got TPHRT from _________________________

     Version 3 Single Language Timer Toolboxes.  Includes large & small
     model libraries (C), full library source, support by US Mail or
     Compuserve Email.  License does not permit commercial distribution
     of object code.

     Qty _____ TPHRT V3 for Turbo Pascal 5 & 5.5 @ $20.00 each ........ _______

     Qty _____ TCHRT V3 for Turbo C @ $20.00 each ..................... _______

     Qty _____ MSCHRT V3 for Microsoft C @ $20.00 each ................ _______

     Version 4 Timer  Toolbox. Supports  TC & MSC in small, medium,
     compact, and large models, Turbo Pascal 5 & 5.5.  20 additional
     functions to manage timers, profile interrupts, generate synchronous
     alarms, run the timer tick interrupt at a user specified rate.
     Two standalone utilities time execution and profile interrupts of
     most executable programs without recompilation.  Full library
     source in C & Pascal included.  Printed manual.  Support by
     telephone, US Mail or Compuserv Email.  License  permits
     commercial distribution of object code.

     Qty ______ PCHRT V4.00 @ $49.95 each ............................. _______

     Shipping in USA @ $2.00 .......................................... _______

     Shipping outside USA @ $4.00 ..................................... _______

     Subtotal ......................................................... _______

     Michigan residents add 4% ........................................ _______

     Total enclosed ................................................... _______


     Payment method:  ___Check  ___Money Order  ___VISA  ___MasterCard

     Card # ____________________________________________ Exp _________

     Signature _________________________________________

     Remit to Ryle Design, P.O. Box 22, Mt. Pleasant, MI 48804

     Credit  card  customers  may  order  by  Email  on Compuserve  to
     73047,1765,  or  by telephone at (517) 773-0587.  This is a voice
     mail system.  Leave your name and number in voice mailbox #2, and
     your call will be returned and your order taken.

     Thank you!

                                    TPHRT  30