RTCLOCK, version 1.33, by Michael Conley
         Release date: January 20, 1991

UPDATE:
        RTCLOCK version 1.33 now supports direct HEX addressing of non-
        standard COM ports, if required.  See SETUP and SERIAL SETUP
        below for details.

PURPOSE:
        RTCLOCK is intended for use on an AT class 286, 386, or 486 machine.
	It will read the real time clock and set the DOS clock from it, 
	or read the DOS clock and set the real time clock from it, or it
	will allow the user to set BOTH the real time clock and the DOS 
	clock from the keyboard.	

	If you own the Heathkit "World's Most Accurate Clock" with a
	serial interface, RTCLOCK will allow you to set BOTH your
	real time clock and your DOS clock from WWV, the short-wave
	time data service provided by the U.S. government.

OPERATION:
	Five basic commands are supported, which may be entered either
	on the command line or, if no command is specified, from a menu
	within the program.

        [R] reads the real time clock, and sets the DOS clock.

        [D] reads the DOS clock, and sets the real time clock.

        [S] sets BOTH the real time clock and the DOS clock from
	    the keyboard.
	
        [W] sets BOTH the real time clock and the DOS clock from
	    serial data transmitted by the Heathkit "World's Most 
	    Accurate Clock."  Be sure to read SETUP for additional
	    configuration required for this option.

        [V] views the time data from the Heathkit "World's Most
	    Accurate Clock" until a key is pressed.  It does NOT
	    alter either of the system clocks.  Be sure to read
	    SETUP for additional configuration required for this 
	    option.	

        [ESC] exits with no changes.
SETUP:
	Commands <R>, <D> and <S> require NO configuration.

	Commands <W> and <V> require the installation of an RS232
	serial line from the Heathkit "World's Most Accurate Clock"
	to the computer.  See the clock manual for wiring information.
	Be sure to set the DIP switch inside the clock for the AUTO
	mode, which provides CONTINUOUS output from the clock.  The
	other mode would require manipulating the DTR line to request
	clock data, and is NOT supported by the program.  Also be sure
	to select an appropriate baud rate and program the correct year
	using the DIP switches inside the clock.

	The program must be informed of the baud rate and the COM port
	in either of two ways:

	1)  You may invoke the program and provide the configuration info
	    on the command line as follows:

		RTCLOCK W COM3 2400 [enter]

	    Allowable choices here are  W or V  for the program mode,
	    COM1 thru COM4 for the data port, and 300, 600, 1200, 2400, 
	    4800, or 9600 for the baud rate.  Other choices or missing 
	    info will produce an error message.

            Default COM addresses assumed by the program are:

                        COM1  =  H3F8
                        COM2  =  H2F8
                        COM3  =  H3E8 <standards vary ... use custom
                        COM 4 =  H3E0 <addressing if these don't work
                                       for your system -- see below.

            If your data port has a non-standard address, you may specify
            the hex port address directly by substituting the following
            command structure:

                RTCLOCK W H2E0 2400 [enter]

            The program would then look for a com port at HEX address 2E0
            and attempt to read the clock from that port. 

	2)  You may create an ASCII text file (an example is included
	    in this distribution) with the port and baud rate on the
            SAME line.  Name this file RTCLOCK.CFG and place it in the
	    same directory from which the program will be run.  An 
	    example of the file contents would be:

		COM3 2400

            Note: The parameters must be on the SAME line, and it must
                  be the first line of the file.

	Please also note that, if you enter the program with NOTHING on
        the command line (i.e., menu mode) you MUST provide RTCLOCK.CFG
	in order to use the W or V options, as these cannot be entered
        from the menu.  A sample RTCLOCK.CFG is included with this
	distribution.

SERIAL SETUP:
	This release supports COM ports 1 thru 4 and functions entirely 
	without interrupts.  This allows you to avoid the common problem 
	of "interrupt sharing," where COM1 and COM3 share IRQ4, while 
        COM2 and COM4 share IRQ3.  Custom addressing is possible by
        specifying the HEX address of your com port instead of the name:
        for example:    RTCLOCK W H2E0 2400 would look for the clock on
        port 2E0 hex.

	We recommend that you set your serial I/O card for NO interrupts 
	for the port selected for use with RTCLOCK to avoid possible con-
	flicts with other serial devices.  However, the program will run
	properly even in the event that interrupts are present on the port.

CONCLUSION:
	A brief warning:  TEST the clock hookup using a communications
	program, such as Qmodem, to verify that it's hooked up and sending
	data correctly.  RTCLOCK will simply TIME OUT if there is no output
	from the clock in the W or V mode.  
	If the clock IS connected, but it cannot produce the correct time, 
	the program WILL gracefully exit with a message, so it can safely 
	be used in a batch file, provided the serial line is present.

PROBLEMS, QUESTIONS, SUGGESTIONS:
=================================
RTCLOCK is public domain.  I don't seek or accept any registration fees for 
this or any of my other public domain utility programs, including those for
Wildcat! BBS systems.  If you're interested in making a charitable contribu-
tion to express your appreciation, please read the enclosed file SHARE for
my thoughts on the subject.

I welcome suggestions, and will try to help (no guarantees) if there are
problems.  You may contact me at The Charlatan's Cabin BBS  (213) 654-7337, 
or via CompuServe (70250,220).

============================================================================