Digital Orthophoto Production FLOPPY Disk Readme File



     An orthophoto is by definition "a photographic reproduction

prepared from a perspective photograph in which the displacement

of images due to camera tilt and terrain relief have been

removed" (Manual of Photogrammetry 1966).  For the sake of

completeness the definition may be expanded to include "so that

the orthophoto has the same metric accuracy as a map and it also

has a uniform scale."

     The basic equipment used to make a digital orthophoto is a

scanning microdensitometer and a digital computer.  A scanning

microdensitometer is a precision instrument that uniformly scans

a photograph in a rectilinear fashion so that the designated area

is completely covered by adjacent picture elements (pixels) of

the desired size.  A single numerical value is assigned to each

pixel proportional to the photon flux at that point (Horton

1978).  The entire aerial photograph is digitized resulting in a

volume of data of from 20 million bytes to slightly over 80-

million bytes.  The computer required to process these large data

sets must be fast, have a large random access memory (RAM),

and have large data storage devices.

     The input data needed for generating a digital orthophoto

include:  digitized image, a digital elevation model (DEM), and

both exterior and interior image orientation parameters.  At this

time the digital orthophoto is made using many conventional

procedures.  Control for the aerial photograph is developed

by aerotriangulation methods and is transferred to the

diapositive to be scanned.  The diapositive is placed on the

microdensitometer and digitized, the digital data being written

to tape.  The data is then processed using the software developed

by the USGS.

     The software solves the exterior orientation of the

photograph by using space resection (collinearity) equations.

Next, raster fiducials are fit to the calibrated camera fiducials

using a linear conformal transformation and the transformation

parameters are saved.

     The first two profiles of the digital elevation model (DEM)

are input to form a profile pair of DEM cells.  The photo

coordinates of the cell corners in the raster system are computed

using DEM cell corner coordinates.  The DEM cell is then

subdivided into the desired resolution.  The raster coordinate

(line and sample) of each subdivision is then computed to the

nearest integer using bilinear transformation parameters.  For

each subdivision the 8-bit binary grey scale value that

corresponds to the raster coordinate is assigned to a subdivision

image coordinate.  The processing of each cell in a profile pair

and of each profile pair is accomplished sequentially.

     The result of this program is a digital orthophoto that can

be used as an image map base in a graphic display system or

written to film to form a hardcopy orthophoto.

     The digital orthophoto on this disk is the southwest quarter

of the Black Earth SW, WI quarter quadrangle.  The area covered

is approximately 1.875-minutes with a ground resolution for each

pixel of 3.75-meters.  The orthophoto is cast on North American

Datum of 1983 (NAD 83) in Universal Transverse Mercator (UTM)

zone 16.  The UTM coordinates of the northwest corner are:

     X =  275670.0 meters

     Y = 4781265.0 meters.

The radiometric resolution is 8-bits and the file contains 1,000

lines of 1,000 samples each.  There is no header i.e., header

bytes = 0.

     All instructions to display the image are explained in the

ASCII file IMDISP.DOC.  Although this program has been used by

the U.S. Geological Survey, no warranty, expressed or implied, is

made by the USGS as to accuracy and functioning of the program

and related program material nor shall the fact of distribution

constitute such warranty, and no responsibility is assumed by the

USGS in connection herewith.  Users should use care in judging

the quality of the image for specific applications.  Poor image

resolution may be due to low resolution monitors commonly found

on personal computers.