ADJRAM -- Adjustable RAM Disk
                                     
                                by Gary Cramblitt

                                   Version 4.1

        (c) Copyright 1986,1987,1988 by Gary Cramblitt.  All rights 
            reserved.  Permission is granted to copy and use this 
            software for non-commercial purposes only.  Permission is 
            granted to distribute copies of this software provided no 
            profit is obtained by doing so and that the entire package 
            is distributed.  

            NOTICE:  This program is provided on an "as is" basis 
            without warranty of any kind, expressed or implied, 
            including but not limited to the implied warranties of 
            mercantability and fitness for a particular purpose.  The 
            entire risk as to quality and performance of this program is 
            with you, the user.  Should the program prove defective, you 
            assume the entire cost of all necessary repair, servicing, 
            or correction.  In no event will the author be liable to you 
            for any damages, including any lost profits, lost savings, 
            or other incidental or consequential damages arising out of 
            the use or inability to use this program.


        This program, although copyrighted, may be freely copied and 
        used, so long as it is not used for commercial purposes.  It is 
        NOT shareware or user-supported software.  You are not expected 
        to make a donation to the author for using this program.  Enjoy 
        -- and try to do the same for others some day.  

        If you distribute copies of this software to others, you are 
        REQUIRED to distribute the ENTIRE package consisting of the 
        following files: 

                AMDISK.DVD
                ADJRAM.EXE
                ADJRAMEM.EXE
                ADJRAM.DOC
                AMDISK.ASM
                ADJRAM.C

        If you leave any of the above files out, you will be in 
        violation of copyright.  You may charge a distribution fee for 
        ADJRAM so long as the recipient is not charged more than a total 
        of $6.00 (including tax and postage) to receive ADJRAM.  If you 
        charge more than that, you are in violation of copyright.  

        
        READ THIS DOCUMENTATION
        -----------------------
        Using this program without first reading all of this document 
        can be hazardous to your data.  While the program has been 
        reasonably tested for defects, the nature of its algorithm is 
        such that under certain conditions it will fail and this could 
        in turn cause loss of valuable data.  The section on 
        Compatibility and Memory Usage and the section on Errors are 
        particularly important.  


        What Is ADJRAM?
        ---------------
        ADJRAM is a RAM disk program.  Sometimes, RAM disks are called 
        "virtual disks" like the VDISK supplied with PC-DOS.  Sometimes 
        they are called "memory disks" like MEMBRAIN.  Whatever you call 
        it, a RAM disk is a program that makes a section of the Random 
        Access Memory (RAM) of your computer look like a floppy disk 
        drive to DOS.  The advantage is that RAM is many hundreds of 
        times faster than a floppy disk -- even faster than a hard disk.  

        Why use ADJRAM, when you already have VDISK or MEMBRAIN or some 
        other RAM disk?  Because ADJRAM allows you to vary the size of 
        the RAM disk without rebooting, and without loss of existing 
        data stored in the RAM disk.  For example, you can start out 
        with 64K of your memory allocated for the RAM disk, expand it 
        later to 320K, copy a document file of 60K to the RAM disk, and 
        still later reduce the RAM disk capacity back down to 128K -- 
        without losing your document file.

        ADJRAM is ideal for those who do not have a hard disk.  It also 
        supports LOTUS/INTEL/Microsoft Expanded Memory and Reserved 
        Memory (explained later).  It does not support Extended Memory.

        Requirements
        ------------
        ADJRAM is designed to run under MS-DOS version 2 or greater.  It 
        has been tested on the following machines:

             1.  Zenith Z100 under MS-DOS version 2.21
             2.  Zenith Z171 (an IBM PC compatible) under MS-DOS version 
                 2.11
             3.  KayPro 16 also under MS-DOS 2.11
             4.  Tandy 1000 under MS-DOS 2.11
             5.  Sperry Personal Computer with 2 Mbyte JRAM 3 card under 
                 MS-DOS 3.1 
             6.  EPSON Equity I under MS-DOS 2.11 
             7.  COMPAQ DeskPro (80186) under IBM DOS 3.10
             8.  IBM PC Portable.  
             9.  Sharp PC-5000.
             10. Zenith Z160 under DOS 3.1.
             11. XEROX 6060 under MS-DOS 3.1.
             12. Epson Equity I under MS-DOS 2.11.

        It requires approximately 14K bytes of disk space.  Memory usage 
        is, of course, a function of the RAM disk's size, but it 
        requires a minimum of 50K free RAM.  


        Installation
        ------------
        Note: If you have a computer with LOTUS/INTEL/Microsoft Expanded 
              Memory and you want ADJRAM to use the Expanded Memory, 
              please read the section below entitled "Expanded Memory 
              Support" before you install ADJRAM.  

        Copy the following files to your boot disk: 

             AMDISK.DVD
             ADJRAM.EXE

        Edit your CONFIG.SYS file and place the following line in it:

             device = amdisk.dvd

        Reboot your computer.  If all goes well, you should see the 
        following message appear near the beginning of your boot 
        sequence:

             AMDISK v4.1 (c) Copyright 1986,1987,1988 by Gary Cramblitt
               -- Initialized as disk C:

        The disk drive letter will vary according to your system 
        configuration.  Remember that drive letter, since it is that 
        disk which is your RAM disk.  

        If you use any memory resident programs, such as Sidekick (a 
        trademark of Borland International), load them before attempting 
        to change the size of the RAM disk (as explained in the next 
        section).  
        
        MS-DOS 3.x users may need to add a LASTDRIVE= clause to their 
        CONFIG.SYS file.  Consult your DOS manual.

                                                        
        Using the RAM Disk
        ------------------
        The RAM disk is used just like any floppy disk drive.  You can 
        copy files to or from it, create directories on it, erase files, 
        etc.  You may NOT do the following things with the RAM disk:
        
             1.  You may not FORMAT the RAM disk.
             2.  You may not DISKCOPY from or to the RAM disk.
             3.  You may not run SYS against the RAM disk.
             4.  You may not boot from the RAM disk.
             5.  You may not use any program on the RAM disk that 
                 accesses the disk controller circuitry directly.  Some 
                 anti-copy protection programs fall into this category.
             6.  You may not use any program that depends upon IBM
                 standard disk media codes.

        Restrictions 1 through 5 are generally true of any RAM disk.  
        Restriction 6 is unique to the Adjustable RAM Disk because it 
        uses a non-standard media descriptor byte.  This shouldn't cause 
        great hardship though.  

        Also, keep in mind that anything stored in the RAM disk can 
        potentially be lost.  For example, should your power fail and 
        you don't have an Uninterruptible Power Source (UPS), then 
        everything in the RAM disk will be lost.  If you reboot (by 
        pressing CTRL-ALT-DEL for example), the contents of the RAM disk 
        are lost.  It is a good idea to periodically copy important 
        files to a more permanent medium, such as floppy disk.  


        Using ADJRAM
        ------------
        The RAM disk defaults to a size of 64K bytes when you first boot 
        the system.  The ADJRAM program is used to change this size.  
        For example, to increase the size of the RAM disk by 64K bytes, 
        enter the following command to the DOS prompt: 

             ADJRAM C: +64

        The spaces after "ADJRAM" and after "C:" are required.  The 
        drive letter (C:) will vary according to your system's 
        configuration.  Use whatever letter was displayed by AMDISK when 
        you booted the system.
        
        In case you missed it, I'll repeat:  The spaces after "ADJRAM" 
        and after the drive are required.

        When ADJRAM is run, you should see something like this displayed 
        on your screen: 

             Adjustable RAM Disk v4.1 (c) Copyright 1986,1987 by Gary Cramblitt
             Drive C:   Total Size: 64K        Free Space: 61K
                 Max Possible Size: 618K    Max Expansion: 554K
                        Final Size: 128K    Amount Change: 64K
             ADJRAM Exiting (code 0)

        The drive letter displayed will vary, as I've already explained.  

        ADJRAM always increments its size in 32K junks, called "memory 
        blocks".  The change you specify is always rounded up to the 
        next closest multiple of 32.  In the example above, two new 32K 
        memory blocks are created for the additional 64K of space.

        To see where the memory blocks are located and what their size 
        is, use the following command:

             ADJRAM C: /t

        The "/t" option tells ADJRAM to display the Memory Block Table.

        You must have sufficient free memory to allocate the additional 
        size.  ADJRAM will automatically determine the maximum size 
        possible and display it for you.  If you request too large a 
        size, ADJRAM will round down the request to the nearest 32K 
        increment.

        You can also shrink the RAM disk.  For example, the following 
        command would decrease the size of the RAM disk by 32K: 

             ADJRAM C: -32

        You must have sufficient free space in the RAM disk in order to 
        shrink it.  To find out how much free space you have in the RAM 
        disk, enter the following command:

             ADJRAM C:

        Notice how there is no size parameter.  The program will display 
        the current size and free space of the RAM disk.  If you have 
        insufficient space, you must erase enough files to get 
        sufficient space.  Then enter your ADJRAM command again.  

        You can not shrink the RAM disk to less than 64K.  (See the 
        section later entitled "Specifying an Initial Size" for a way 
        around this restriction.)

        Instead of giving the size of the RAM disk as a plus or minus 
        figure, you can specify the desired size of the RAM disk like 
        this:

             ADJRAM C: 320

        This command will set the RAM disk to 320K.  If it is currently 
        larger than 320K, it will shrink it down to 320K (provided there 
        is sufficient free space to do so).  If it is currently smaller 
        than 320K, it will expand the size to 320K by allocating new 
        memory blocks.  Remember that ADJRAM will round the figure you 
        specify to the next higher multiple of 32.  

        If you want to adjust the size of the RAM disk so that it has 
        200K of free space, enter a command like this: 

             ADJRAM C: f200

        Notice the letter "f" in front of the size.  This command will 
        expand or shrink the RAM disk so as to ensure there is about 
        200K of free space IN THE RAM DISK.  

        If you want to ensure there is AT LEAST 128K of free space in 
        the RAM disk, enter a command like this:

             ADJRAM C: m128

        Notice the letter "m" in front of the size.  This command will 
        never shrink the RAM disk, but it may expand it to make sure 
        there is a minimum of 128K of free space.  This form of the 
        command is particularly handy within batch files to make sure 
        the RAM disk is large enough to hold a file before it is copied 
        into the RAM disk.


        Online Help
        -----------
        If you can't remember the format for all these commands, fear 
        not.  Simply enter 

             ADJRAM

        and it will display a help message showing the formats described 
        above.


        Hint for Floppy Disk Systems
        ----------------------------
        If you do not have a hard disk, soon after booting your 
        computer, copy file ADJRAM.EXE to the RAM disk, for example:

             COPY A:ADJRAM.EXE C:

        You can then modify the size of the RAM disk at any time 
        thereafter without needing the boot disk.  Just put the RAM disk 
        drive letter in front of any ADJRAM commands.  For example:

             C:ADJRAM C: -32

        You can put the COPY command into your AUTOEXEC.BAT file.


        Specifying an Initial Size
        --------------------------
        By default, AMDISK sizes itself to 64K when it is initially 
        loaded at boot time.  If you wish, you can alter this initial 
        size by placing a "MINSIZE=" clause in CONFIG.SYS.  For example, 
        to set the initial size to 32K, you would put the following line 
        into CONFIG.SYS: 

             DEVICE = AMDISK.DVD MINSIZE=32

        The size may be a minimum of 15 and a maximum of 512.  Large 
        initial sizes are definitely not recommended however, because 
        you can never shrink the RAM disk to less than its initial size.  
        For example, if you put a "MINSIZE=256" into CONFIG.SYS, you can 
        never make the RAM disk any smaller than 256K.  

        ADJRAM always expands and shrinks the RAM disk in 32K 
        increments.  If you specify an initial size that is not an even 
        multiple of 32, then ADJRAM will round your sizes to some 
        strange numbers.  For example, if you specify "MINSIZE=15" in 
        CONFIG.SYS, and then give the following command: 

             ADJRAM C: 128

        ADJRAM will actually size the RAM disk to 143K (15 + 4*32).  For 
        this reason, I recommend that you always specify an even 
        multiple of 32 in your "MINSIZE=" clause.


        Expanded Memory Support
        -----------------------
        ADJRAM provides full support for LOTUS/INTEL/Microsoft Expanded 
        Memory (EMS version 3.2 compatible).  

        If you have a computer with LOTUS/INTEL/Microsoft Expanded 
        Memory and you want ADJRAM to use that memory, the installation 
        is a little different.  Instead of copying ADJRAM.EXE to your 
        boot disk, copy file ADJRAMEM.EXE and then rename it to 
        ADJRAM.EXE.
        
        Depending upon how much expanded memory you have and how large 
        you expect to make the RAM disk, you may also need to add a 
        "CLUSTER=" clause to CONFIG.SYS.  For example, if you have 8MB 
        of expanded memory (the maximum possible) your CONFIG.SYS file 
        would have the following statement:

             DEVICE = AMDISK.DVD CLUSTER=4

        The following table shows the cluster sizes you should use for 
        corresponding maximum RAM disk sizes:

             Maximum
             RAM Disk
             Size (K)         CLUSTER=
             --------         --------
              2043               1 (default)
              4083               2
              8166               4
             16332               8

        The rest of the installation is the same as for the non-expanded 
        memory version.

        If you want ADJRAM to create new memory blocks in 
        LOTUS/INTEL/Microsoft Expanded Memory, add a "/E" option, like 
        this: 

             ADJRAM C: +256 /E

        This command will expand the RAM disk by 256K.  The additional 
        256K memory block will be created within LOTUS/INTEL/Microsoft 
        Expanded Memory.  If ADJRAM ends up shrinking the RAM disk, the 
        "/E" switch is meaningless.  Remember that ADJRAM will always 
        shrink the RAM disk by freeing memory blocks in reverse of the 
        order in which they were created.  

        The version of ADJRAM that supports Expanded Memory can not be 
        used in conjunction with the version that does not support it.  
        Don't get them mixed up.  Use ADJRAMEM.EXE (renamed to 
        ADJRAM.EXE) or use ADJRAM.EXE -- but not both.
        
        Instead of allocating memory blocks in 32K increments, ADJRAM 
        allocates expanded memory blocks in 256K increments.  
        Consequently, it will shrink in 256K increments as well.  If you 
        mix conventional memory blocks with expanded memory blocks, the 
        shrinkage boundaries will vary.  Just remember that ADJRAM 
        always deallocates memory blocks in reverse of the order they 
        were created, and that it must always deallocate entire memory 
        blocks.  Playing with the combinations and using the "/t" option 
        will help you to understand what is going on.  

        One EMM handle is used for each new 256K memory block.  Hence, a 
        2MB expanded memory RAM disk will use 8 handles.  

        The Expanded Memory support in this version of ADJRAM was coded 
        based on information from the book "Advanced MS-DOS" by Ray 
        Duncan.  The code was tested on a Sperry PC with a 2 Mbyte JRAM 
        3 memory board installed (JBOOT and JPAGER loaded).  I don't own 
        a computer with Expanded Memory, so this part of the program is 
        the least tested.  Please be cautious until you've had time to 
        thoroughly check out the program -- and let me know if you 
        encounter difficulty.  


        Using Reserved Memory
        ---------------------
        Beginning with verson 4.0, ADJRAM now supports Reserved 
        Memory.  This capability should only be used by those who 
        understand 8086 addressing and have sufficient technical 
        background.  Others should skip this section entirely.  

        Support for Reserved Memory was added because many computers 
        have banks of memory not otherwise usable.  For example, in the 
        IBM Portable, banks A, C, D, and E are not normally used for 
        anything.  Some portable clones have a megabyte of memory, but 
        only 640K is usable.

        To understand what Reserved Memory is, here are a few 
        definitions: 

            1.  CONVENTIONAL Memory is directly addressable by the 8088 
                or 8086 CPU and is controlled by DOS.  On the IBM PC, it 
                is the memory from 0 to 640K.
        
            2.  RESERVED Memory is also directly addressable by the 8088 
                or 8086 CPU but it is not controlled by DOS.  On the IBM 
                PC, it would be memory from 640K to 1MB.  This memory is 
                normally reserved for use by the BIOS.  For example, the 
                memory from B0000 to BFFFF is reserved for monochrome 
                and graphics video memory.  
        
            3.  EXTENDED Memory is only found in AT class machines.  It 
                is memory above 1MB that is directly addressable by the 
                80286 (protected mode) or 80386 CPUs.  Extended Memory 
                is not currently supported by ADJRAM.  Some PC and XT 
                class machines have "extended" memory boards in them 
                that don't meet the definition of Extended Memory I've 
                given here.  Such memory must be "bank switched" or 
                "paged" into the 8088 or 8086's address area (0 to 1MB).  
                The JRAM 3 memory card is one such type of memory.  If 
                the vendor sells an Expanded Memory Manager (EMM) for 
                the board, then that memory can be used by ADJRAM.  
        
            4.  EXPANDED Memory adheres to the LOTUS/INTEL/Microsoft 
                Expanded Memory Specification (v3.2).  Note that 
                Expanded Memory is implemented through the Expanded 
                Memory Manager (EMM), and may actually reside anywhere.  
                For example, with appropriate software, it is possible 
                to convert Extended Memory into Expanded Memory.  

        Now back to Reserved Memory.  IBM reserved the memory from A0000 
        to FFFFF.  For example, they reserved memory from A0000 to AFFFF 
        for the Enhanced Graphics Adaptor (EGA).  If your computer 
        doesn't have an EGA, you may be able to use those addresses for 
        ADJRAM.  
        
        Suppose you wanted to put 64K at address A0000 to AFFFF.  To do 
        this, you would have to install a memory board with 64K 
        "jumpered" or "strapped" so that its memory resides at addresses 
        A0000 to AFFFF.  The memory must be directly addressable by the 
        CPU at addresses A0000 to AFFFF.  No "bank switching", "paging", 
        or "enabling" is allowed.  

        Now specify a command of the following form to expand into this 
        Reserved Memory:

             ADJRAM C: r:a000:64 /T

        You must use the Expanded Memory version of ADJRAM 
        (ADJRAMEM.EXE renamed to ADJRAM.EXE).  The format must be 
        exactly as shown, i.e., an "R" followed by a colon, followed by 
        a four digit hexadecimal paragraph address, followed by a colon, 
        followed by a decimal size.  (You get a paragraph address by 
        dropping the last hexadecimal digit from a 5 hex digit address).  
        Notice that this "R" option replaces the normal "size" parameter 
        in an ADJRAM command.  The maximum size permitted is 64.  The 
        hexadecimal address must be in the range A000 to FFFF and it 
        must point to valid reserved memory.

        ADJRAM doesn't do ANY error checking of this command, so use 
        with extreme caution.  The "/T" option is used so that you can 
        verify that the memory block was properly added to the Memory 
        Block Table.  In this example, a single 64K block is added 
        beginning at paragraph A000.

        You may have additional Reserved Memory, or you may wish to 
        allocate the memory in smaller blocks so that shrinkage can be 
        fine-tuned.  To do that, just specify additional ADJRAM commands 
        -- one for each new block.  For example, to divide the 64K block 
        starting at A000 into four blocks of 16K, give the following 
        commands: 

             ADJRAM C: r:a000:16
             ADJRAM C: r:a400:16
             ADJRAM C: r:a800:16
             ADJRAM c: r:AC00:16 /t

        You will normally want to specify the Reserved Memory commands 
        in your AUTOEXEC.BAT.

        If you find this capability useful, please let me know.


       
        Error Messages
        --------------
        In general, error messages are prefaced by either the phrase 
        "Error --" or the phrase "Warning --".  Warning messages are not 
        fatal.  The program will automatically adjust for them.  For 
        example, if you attempt to make the RAM disk larger than 
        available free memory, ADJRAM will automatically make it as 
        large as possible.
        
        Most errors will stop the program immediately.  However, once 
        the "Final Size" line appears, ADJRAM has begun to reorganize 
        the RAM disk.  If it gets an error during this time, it will 
        attempt to keep going; and when it does exit, the following 
        message will appear: 

             *** Sorry, RAM disk has been corrupted.  Recommend that you
                 check your files, save them if possible, and reboot.

        If this message appears, you should immediately do just what it 
        says.  If you don't need any of the data in the RAM disk, you 
        should reboot immediately.  If you do need the data, first check 
        the files to see if they are OK.  You can check ASCII text files 
        by TYPEing them.  If the files you need appear to be OK, then 
        copy them to a more permanent medium, such as floppy disk, and 
        reboot.

        Whenever ADJRAM exits, a message such as the following appears:

             ADJRAM exiting (code 0)

        The code number in parenthesis indicates the ERRORLEVEL code 
        being passed to DOS.  A code of 0 means "no error".  These codes 
        can be tested by DOS IF statements in batch commands.  More on 
        this later.
        
        There are also a large number of possible errors that MS-DOS 
        will display while you're working with the RAM disk.  Consult 
        your DOS manual.  One message I'd like to point out.  If you see 

             Bad File Allocation Table

        (or something similar) the RAM disk is probably corrupted.  
        Carefully check your files.  If they are OK, copy them to a more 
        permanent medium, such as floppy disk, then reboot.  

        Here is a list of possible error messages you might see 
        displayed by the ADJRAM.EXE program and their probable cause 
        (the numbers in parenthesis are the ERRORLEVEL codes passed to 
        DOS).  First time users will want to skip the rest of this 
        section.  Keep this .DOC file handy though, in case you need 
        help understanding an error message: 

             Error -- could not read boot sector.  Error code xx (15)

        The program could not read the boot sector (logical sector 0) of 
        the RAM disk.  An invalid drive letter was specified or the RAM 
        disk has become corrupted.  In the latter case, reboot is 
        recommended.  

             Error -- that drive is not the adjustable RAM disk or 
        invalid version of AMDISK for this version of ADJRAM (15) 

        An invalid drive letter was specified.  Use the letter that was 
        reported by AMDISK when you booted the computer.  Make sure you 
        used the correct command syntax.  A space must follow "ADJRAM".  
        It could also occur if you've mixed version 4.0 of ADJRAM with 
        an older version of AMDISK.  In this case, you need to update 
        AMDISK.DVD.

             Error -- could not free environment block.  Error code xx 
        (10)

        This error would indicate you have an incompatible version of 
        MS-DOS.  The error codes are those returned by DOS function 49H.

             Error -- Bad reserved memory parameter (1)

        You gave an "R" option but in the wrong format.  Format is
        R:hhhh:dd.  For example, a reserved memory block starting at 
        paragraph D000 and 32K long would be specified as r:d000:32
        A common error is to forget one of the colons.  Also, the 
        starting address is exactly 4 hexadecimal digits long.  Correct 
        and try again.  
        
             Error -- Unable to locate reserved memory block from
        xxxx:xxxx to xxxx:xxxx (8)

        You gave an "R" option but specified memory that ADJRAM could 
        not find.  For example, a reserved memory block starting at 
        paragraph D000 and 32K long would be specified as r:d000:32.  A 
        common error is to overlap with read-only memory or to overlap 
        with video memory.  ADJRAM tests the specified block by writing 
        a test byte at the beginning and end of the block.  If it can 
        not read the same byte back, you get this error.  Check your 
        technical documentation and try again.
        
             Error -- Invalid drive letter or RAM disk is not loaded 
        (15)

        ADJRAM reports this error if DOS returns an error code from 
        function 36H (get free disk space).  Check your drive letter and 
        command syntax.

             Warning - Insufficient free space in disk to shrink that much 
        (8)

        You do not have enough free space in the RAM disk to shrink it 
        by the requested amount.  ADJRAM will attempt to shrink the disk 
        as much as possible.  First erase some files from the RAM disk, 
        then reenter you command.  

             Warning -- Rounding your requested change of xxK to xxK

        ADJRAM is showing you how it has adjusted your expansion or 
        shrinkage request to fall within allowable boundaries.  Does not 
        alter the ERRORLEVEL code.

             Error -- could not modify memory block size.  Error code xx 
        (8)

        This error occurs when expanding the RAM disk.  The program 
        received an error code from DOS function 4AH (modify memory 
        allocation) on the first new 32K memory block to be created.  It 
        could be caused by corrupted memory allocation, possibly 
        caused by incompatibility with other memory resident programs.  
        Reboot is recommended.

              Error -- could not allocate new memory block.  Error code 
        xx (8) 

        This error is similar to the one above except that it occurs on 
        the second and subsequent new 32K memory blocks when the program 
        invokes DOS function 48H (allocate memory).  Since the program 
        supposedly made sure there was sufficient memory before 
        attempting the expansion, getting this message would indicate an 
        internal bug.

             Error -- could not allocate new memory block from EMM.  
        Error code xx (8) 

        This error is similar to the one above except that it occurs in 
        conjunction with creating new 256K memory blocks in 
        LOTUS/INTEL/Microsoft Expanded Memory.  The program will attempt 
        to keep going without expanding the disk any further.  This 
        condition is not well tested though, so to be safe, reboot is 
        recommended.  

             Error -- could not write boot sector back.  Code: xx (15)

        This is most likely an internal program error.  The program got 
        an error code from DOS interrupt 26H (write absolute disk 
        sector).  Reboot is required.  

             Error -- could not free allocated memory block #xx.  Error 
        code xx 
        
        This error occurs when shrinking the RAM disk.  The program got 
        an error code from DOS function 49H (release memory).  Could be 
        caused by an internal program bug, incompatible memory resident 
        program, or incompatible version of DOS.  The program attempts 
        to exit gracefully so that you can recover data files from the 
        RAM disk, but you should reboot as soon as possible.  

             Error -- could not free EM pages for memory block #xx.  
        Error code xx 
        
        This error occurs when shrinking the RAM disk.  The program got 
        an error condition from the LOTUS/INTEL/Microsoft Expanded 
        Memory Manager.  Could be caused by an internal program bug, 
        incompatible memory resident program, or incompatible version of 
        DOS.  The program attempts to exit gracefully so that you can 
        recover data files from the RAM disk, but you should reboot as 
        soon as possible.  

             Error -- Insufficient stack space to pack subdirectory 
        xxxxxxxx.  Too many subdirectories.  Shrink abandoned. (4)

        This error occurs when shrinking the RAM disk.  The DeSmet C 
        stack space was insufficient to handle the depth of 
        subdirectories you have on your RAM disk.  The program attempts 
        to exit gracefully without completing the shrink.  This 
        condition has not been fully tested, so caution, your files may 
        have been corrupted.  In the future, don't use so many 
        subdirectories.  

             Error -- Error while packing file xxxxxxxx

        This error occurs when shrinking the RAM disk.  It will usually 
        be displayed after the previous message.  It may also appear if 
        an internal error occurs, such as inability to read or write 
        sectors of the file.  The program attempts to exit gracefully 
        without completing the shrink.  

             Error -- Expanded Memory Manager is not avaiable.  Error 
        code: xx (15) 

        You specified the "/E" option, but the LOTUS/INTEL/Microsoft 
        Expanded Memory Manager (EMM) is not loaded.  Load the EMM and 
        try again.

             Error -- Expanded Memory Manager could not report page 
        frame.  Error code: xx (8)

        The EMM was detected by ADJRAM, but the EMM reported an error 
        when ADJRAM asked for the page frame segment address (EMM 
        function 41H).  This could be caused by a corrupted EMM, or an 
        incompatible version of the EMM (ADJRAM requires version 3.2 
        compatibility), or possibly ADJRAM encountered a "busy" 
        condition from the EMM.  Try again.  If it still fails, you'll 
        have to stick with normal memory.  

        There are two other conditions which do not display an error 
        message.  In these cases, the program simply displays the help 
        message and exits:

             1.  Invalid drive letter specified.  Must be in range A 
                 through L. (15)

             2.  Invalid size specified.  For Conventional Memory, must 
                 be in range 64 to 2016.  (1).  

        

        Using ADJRAM in Batch Files
        ---------------------------
        If an error occurs while running ADJRAM, it will return a DOS 
        error code when it exits back to DOS.  The error codes returned 
        are shown in parenthesis in the error message section above.  
        They are also displayed in the "ADJRAM exiting" message.  These 
        error codes can be used in a batch file via the DOS IF 
        command.  See your DOS manual for details.  For example, I use 
        the following batch command file to load PROCOMM into the RAM 
        disk.  Procomm's files require about 175K of space: 
        
             c:adjram c: m175
             if not error level 0 goto noram
             copy a:procomm.* c:
             c:
             rem Type PROCOMM /B
             goto xit
             noram:
             rem Not enough room in ram disk.
             xit:
               
        Some versions of MS-DOS (Z100 v2.21 for example) have a command 
        which will cause error codes to be displayed.  It is: 

              XYZZY ON


        Compatibility and Memory Usage
        ------------------------------
        The Adjustable RAM Disk falls into a class of programs known as 
        Memory Resident programs.  Sidekick is one such program.  These 
        programs are sometimes incompatible with one another.  It is 
        impossible for me to test the Adjustable RAM disk in combination 
        with every available memory resident program, so I'll apologize 
        ahead of time -- some incompatibilities are almost certain to 
        crop up.  

        Sometimes, changing the order inwhich the programs are loaded 
        makes a difference.

        Generally, you should load all of your memory resident programs 
        BEFORE you run ADJRAM.  (I know, every memory resident program 
        wants to be loaded last, but please bear with me!)  You should 
        do this to make the most efficient use of memory.  Here's why.  
        When you expand the RAM disk, ADJRAM allocates 32K memory blocks 
        using the DOS memory allocation functions.  Once that is done, 
        any subsequent memory resident programs you load will generally 
        get loaded above these new memory blocks.  When you later shrink 
        the RAM disk, ADJRAM deallocates the memory blocks.  If you have 
        loaded a memory resident program after expanding the RAM disk 
        with ADJRAM, then "holes" in the memory allocation will be 
        created when you later shrink the RAM disk.  These holes will 
        generally not be usable for transient programs until you unload 
        the memory resident program (which might not even have that 
        capability).  
        
        To help you understand what is happening, consider a system with 
        the following CONFIG.SYS file

             device = amdisk.dvd
             device = ansi.sys
        
        and the following (incorrect) AUTOEXEC.BAT:

             copy adjram.exe c:
             c:adjram c: +64
             sk

        Notice that Sidekick is incorrectly loaded AFTER expanding the 
        RAM disk.  At the completion of the boot, the following memory 
        layout exists: 

             +--------------------------------+ 640K
             |                                |
             |   Transient Program Area       |
             |                                |
             +--------------------------------+
             |           Sidekick             |
             +--------------------------------+
             |   Block #2 of RAM Disk (32K)   |
             +--------------------------------+
             |   Block #1 of RAM Disk (32K)   |
             +--------------------------------+
             |           ANSI.SYS             |
             +--------------------------------+
             |   Block #0 of RAM disk (64K)   |
             |                                |
             +--------------------------------+
             |          AMDISK.DVD            |
             +--------------------------------+
             |         BIOS and DOS           |
             +--------------------------------+ 0K

        If the user were to shrink the RAM disk now, say with the 
        following command 

             C:ADJRAM C: -32

        then the memory layout would change to this:

             +--------------------------------+ 640K
             |                                |
             |   Transient Program Area       |
             |                                |
             +--------------------------------+
             |           Sidekick             |
             +--------------------------------+
             |     32K unusable "hole"        |
             +--------------------------------+
             |   Block #1 of RAM Disk (32K)   |
             +--------------------------------+
             |           ANSI.SYS             |
             +--------------------------------+
             |   Block #0 of RAM disk (64K)   |
             |                                |
             +--------------------------------+
             |          AMDISK.DVD            |
             +--------------------------------+
             |         BIOS and DOS           |
             +--------------------------------+ 0K

        Notice how, with Sidekick where it is, the Transient Program 
        Area could not grow in size.  There is now a 32K hole of 
        unusable memory just below Sidekick.  The correct 
        AUTOEXEC.BAT

             sk
             copy adjram.exe c:
             c:adjram c: +64

        would produce the following memory layout after booting:

             +--------------------------------+ 640K
             |                                |
             |   Transient Program Area       |
             |                                |
             +--------------------------------+
             |   Block #2 of RAM Disk (32K)   |
             +--------------------------------+
             |   Block #1 of RAM Disk (32K)   |
             +--------------------------------+
             |           Sidekick             |
             +--------------------------------+
             |           ANSI.SYS             |
             +--------------------------------+
             |   Block #0 of RAM disk (64K)   |
             |                                |
             +--------------------------------+
             |          AMDISK.DVD            |
             +--------------------------------+
             |         BIOS and DOS           |
             +--------------------------------+ 0K

        Now, if the RAM disk is shrunk (up to 64K, i.e., blocks #2 and 
        #1), then the Transient Program Area will grow by that amount.  

        You generally shrink the RAM disk because you want to make more 
        memory available for other programs.  But it defeats this 
        objective to load memory resident programs after expanding the 
        RAM disk.  So...

             First load the memory resident programs, then use ADJRAM to 
             expand your RAM disk.  

        The Adjustable RAM disk doesn't "steal" interrupts from the 
        system, so expanding the RAM disk after loading programs that 
        intercept interrupts, such as Sidekick, SHOULDN't cause any 
        problems.

        If you encounter compatibility problems, please let me know at 
        the address I'll give at the end of this document.  I'd like to 
        know about them so I can fix them if possible.  Please be as 
        complete as possible when you explain the problem.  What memory 
        resident programs did you have loaded and in what order?  How 
        much memory do you have in your computer?  What computer and 
        operating system were you running?  Exactly what happened when 
        it didn't work?  I won't guarantee that I can fix the problem, 
        but I'll try.  
        
                 
        Known Compatibility Problems
        ----------------------------
        When using ADJRAM with DoubleDOS, new memory blocks are created 
        within whichever partition is active at the time you run ADJRAM.  
        If you attempt to shrink the RAM disk to gain additional room in 
        the first partition, you may find that you didn't gain any room 
        in the first partition!  Instead, the room gained was in the 
        second partition (because that's where the memory blocks were 
        created).  

        Also, DoubleDOS doesn't know about ADJRAM creating new memory 
        blocks.  This causes DoubleDOS to tell you there is more room in 
        partitions than actually exists.  Use CHKDSK to find out how big 
        your partitions really are.  In general, you should try to run 
        ADJRAM before activating DoubleDOS, to avoid this problem.

        ADJRAM is somewhat incompatible with MARK/RELEASE.  You can't 
        expand the RAM disk after you've run MARK, because when you run 
        RELEASE, AMDISK won't know that some of its memory blocks have 
        been freed.  As long as you expand before you run MARK for the 
        first time, you should be OK.  I have not tried MARK/RELEASE in 
        conjunction with ADJRAM, so there may be other problems as well.  
        The Referee, being a program similar to MARK/RELEASE, will 
        problably also have these problems.  
                 
        One user reported that Sidekick version 1.11c locked up when 
        used in conjunction with ADJRAM on his clone PC running MS-DOS 
        3.2.  The same version of Sidekick checked out OK on a Sperry 
        running MS-DOS 3.1.  I don't have easy access to a PC running 
        3.2, so if anyone can help me resolve this problem, it would be 
        appreciated.  

        Other Known Problems
        --------------------
        Some programs, such as PC-WRITE have a "shell" or "hotkey" 
        command that allows you to suspend the program, keeping it in 
        memory, and execute other DOS commands.  You may be tempted to 
        use this capability to increase or decrease the size of the RAM 
        disk in the middle of running another program.  But be careful 
        here.  Consider the following sequence of events:

             1.  You're running (the fictitious) program RAZZLDOC, 
                 editing file C:MYFILE.DOC on the RAM disk.  

             2.  You use RAZZLDOC's "shell" command to get the DOS 
                 prompt.  
        
             3.  You use ADJRAM to expand the size of disk C, the RAM 
                 disk.  

             4.  You use the DOS EXIT command to go back into RAZZLDOC.

             5.  Upon exiting RAZZLDOC, you're horrified to learn that 
                 it was unable to successfully save all your work in 
                 C:MYFILE.DOC.

        The problem here is that ADJRAM told DOS that the "media has 
        changed" on disk C.  But RAZZLDOC had a file open on disk C!  
        DOS can't properly close the file.  This sort of problem will 
        generally occur with any program that has a "shell" command but 
        fails to close all open files before executing the shell.  [One 
        user reported to me that PC-WRITE does close its files before 
        executing the shell, so it should be safe to run ADJRAM from PC-
        WRITE.]

        This kind of problem can also occur with certain memory resident 
        programs that, in effect, give you a "shell" command from within 
        any program.  POPDOS is one such program.

        Remember that whenever you expand or shrink the RAM disk, you 
        have, conceptually, removed the current "floppy disk" in the RAM 
        drive, and replaced it with another "floppy disk" that just 
        happens to have the same files as the one removed.  You wouldn't 
        change a real floppy disk in the middle of editing a Wordstar 
        file, so don't expand or shrink the RAM disk either.  

        I haven't actually tried it, but ADJRAM is likely to have 
        problems under windowing systems, like Microsoft Windows, as 
        well.  Users who try it, please let me know how it turned out.


        Future Versions of DOS
        ----------------------
        It is unlikely that ADJRAM will be compatible with future 
        versions of MS-DOS.  Starting with version 5, Microsoft plans on 
        adding multi-tasking capability.  That will require much more 
        stringent memory management.  That management is likely to 
        conflict with the way ADJRAM works.  People running version 5 
        and above are likely to own hard disks and "virtual memory" 
        machines anyway, and the need for an adjustable RAM disk will 
        disappear.


        History
        -------
        3.0   This was the first version of ADJRAM to be released.  It
              was released to the public in September 1986.
        3.1   This version fixed a bug.  3.0 did not properly pack files
              in subdirectories under certain conditions.  This lead to
              a "bad file allocation table" error.  Release October 1986.
        3.2   This version added support for the SIZE= clause in 
              CONFIG.SYS.  Not publicly released.
        4.0   This version included the following bug fixes and 
              enhancements:
                *  Full support for Expanded Memory
                *  Support for Reserved Memory
                *  Improved error reporting
                *  /T option to display Memory Block Table
                *  Max expansion and shrinkage automatically calculated.  
                   Users's request automatically rounded.
                *  "Non IBM format" message from CHKDSK fixed by making
                   FAT ID masquerade as "double-sided 9-sector".
                *  "Bad FAT" message when disk full bug fixed.
                *  CLUSTER clause added to AMDISK.DVD
                *  Volume label added to AMDISK.DVD
              Not publicly released
         4.1  This version added the following enhancements:
                * Verify that reserved memory is segment a000 or above
                * Initialize reserved memory to zeroes.
              Version 3.x and 4.x can not be mixed.


        Internals
        ---------
        This section is for anyone interested in the internal workings 
        of the Adjustable RAM Disk.  It is not necessary to know this 
        information to use the Adjustable RAM Disk, but it may be 
        helpful for resolving compatibility problems.  This section is 
        for advanced DOS programmers only.  

        AMDISK.DVD is a loadable device driver, just like VDISK or 
        ANSI.SYS.  By itself, it is a complete 64K RAM disk (assuming no 
        "MINSIZE=" clause is given in CONFIG.SYS).  A 64K "memory block" 
        is allocated immediately after the AMDISK code.  A Memory Block 
        Table is maintained in logical sector 0 (the boot sector) of the 
        RAM disk beginning at offset 1EH.  For each memory block, this 
        table contains a seven byte entry as follows: 

             1.  A byte indicating the type of memory block.  0 means 
                 the block is allocated in normal DOS memory.  1 means 
                 the block is allocated in Expanded Memory.  2 means the 
                 block is allocated in Reserved Memory.
        
             2.  A word giving the starting paragraph number of the 
                 memory block.  A paragraph of memory is simply 16 
                 bytes, so this number is just the absolute memory 
                 address shifted right by 4 bits.  All memory blocks 
                 begin on an even paragraph boundary.  This word is zero 
                 if there are no more memory blocks.  It is meaningless 
                 for Expanded Memory blocks.

             3.  A word giving the size of the memory block in 512-byte 
                 sectors.

             4.  A word giving the Expanded Memory handle for the memory 
                 block.  Zero for normal memory blocks.

        Immediately after booting, there is exactly one 64K (128 sector) 
        memory block in the Memory Block Table.  If a "MINSIZE=" clause 
        was given in CONFIG.SYS, the size will vary from 64K.  

        Note:  Don't confuse the memory blocks defined here with those 
               defined for DOS functions 48H thru 4AH.  To avoid 
               confusion -- and though not strictly accurate -- I'll 
               refer to DOS's memory blocks as "program segments".  
        
        The number of memory blocks allocated is stored in the media 
        descriptor byte at offset 15H of the boot sector.  Any time DOS 
        requests a media code from the AMDISK device driver, it returns 
        the number of memory blocks allocated.  In this way, any time 
        that the RAM Disk has been shrunk or expanded, DOS will know 
        that the "media has changed" and will rebuild its internal Disk 
        Parameter Block (DPB) tables.  This lets DOS know what the new 
        size of the RAM disk is.  

        The drive letter AMDISK.DVD uses is assigned by DOS.  AMDISK.DVD 
        gets the letter from DOS via function 19H (Get default disk 
        drive).  
        
        Upon startup of the ADJRAM program, it moves its own stack down 
        so that the program's total run size is less than 32K.  This 
        prevents corruption of future DOS memory arena blocks

        Also, DOS function 49H (release memory) is used to deallocate 
        its own environment segment.  This doesn't seem to hurt a 
        running program, and it is necessary to insure that this memory 
        can be used later when the RAM disk is shrunk.  

        At startup, the Expanded Memory version of ADJRAM tests whether 
        the Expanded Memory Manager (EMM) is loaded by opening device 
        "EMMXXXX0".  If the open fails, the EMM is not loaded.  If the 
        open succeeds, then the output status is requested from the 
        device using DOS function 44H (IOCTL).  If IOCTL reports a 
        status of 0, then coincidentally a file named "EMMXXXX0" existed 
        on the default disk, and the EMM is still not available.  If the 
        EMM is not available, ADJRAM reports an error and exits.

        Also upon startup, ADJRAM checks that the specified drive letter 
        corresponds to the AMDISK device.  The boot sector of the RAM 
        disk contains the string "AMDISK" at offset 03H.  The boot 
        sector is read using DOS interrupt 25H (absolute disk read).

        If the user has requested expansion of the RAM disk using 
        conventional memory, the program counts the number of available 
        32K memory blocks by allocating them using DOS function 48H 
        (allocate memory).  When it gets an error, it knows there are no 
        more available.  It then deallocates the blocks using DOS 
        function 49H (deallocate memory).  ADJRAM always leaves at least 
        one 32K block of free memory.  This is so that ADJRAM can be run 
        one more time in order to shrink the RAM disk.  

        If the user has requested shrinkage of the RAM disk, ADJRAM 
        examines the Memory Block Table to find out where the next 
        smaller size is.  It also uses the table to round the requested 
        shrink down to the nearest memory block boundary.

        When the ADJRAM program increases the size of the RAM disk, it 
        does so by allocating additional 32K (64 sector) memory blocks.  
        Normal memory blocks are allocated in two ways:

             1.  If it is the first memory block to be created (in this 
                 run of ADJRAM), then the memory block is allocated 
                 using DOS function 4AH (modify memory allocation).  
                 ADJRAM's own program segment is the one modified.  
                 Hence, the first memory block overwrites the ADJRAM 
                 program itself.

             2.  Additional memory blocks are allocated using DOS 
                 function 48H (allocate memory).  

        In either case, an appropriate entry is made in the Memory Block 
        Table, which is in the boot sector, for each new memory block.  
        At the end of the program, the boot sector is written back out 
        using DOS interrupt 26H (absolute disk write).  
        
        When ADJRAM exits normally, it uses DOS function 31H (terminate 
        and stay resident) to permanently allocate the new memory 
        blocks.  
        
        Expanded Memory blocks are allocated via EMM function 43H (Get 
        handle and allocate memory).
                 
        Reserved Memory blocks are not "allocated" at all.  ADJRAM 
        simply enters the starting paragraph and size into the Memory 
        Block Table.  It then zeroes the reserved memory.  That is why 
        this option is so dangerous.  

        When ADJRAM shrinks the RAM disk, it does these steps:
                 
             1.  It checks to insure there is sufficient free space in 
                 the RAM disk to do the shrink.  
             2.  The File Allocation Table (FAT) is read using DOS 
                 interrupt 25H.  The first available cluster number is 
                 determined.  
             3.  The first sector of the directory is read in using DOS 
                 interrupt 25H.
             4.  For each file, any clusters located after the first 
                 available cluster are moved down to the first available 
                 cluster.  Then the next available cluster is 
                 determined.  Clusters are moved in the RAM disk using
                 DOS interrupts 25H and 26H.  As clusters are moved, the
                 directory and FAT in memory are updated.  After all the
                 clusters of the file are packed down, and if the file
                 is a subdirectory, then the clusters of the directory
                 are read in and the file packing algorithm (steps 3 and
                 4) is recursively applied to each directory entry in
                 the file.
             5.  Step 4 is repeated for each additional directory 
                 sector.  Updated directory sectors are written back to 
                 the disk using DOS interrupt 26H.
             6.  The necessary number of memory blocks are deallocated, 
                 either using DOS function 49H (release memory) or EMM 
                 function 45H (release handle and memory).  The Memory 
                 Block Table is updated accordingly.  Blocks are 
                 deallocated in reverse of the order inwhich they are 
                 created.  
             7.  The updated FAT and boot sector are written back to the 
                 disk using DOS interrupt 26H.  
             8.  ADJRAM exits normally via DOS function 4CH (exit with 
                 return code).

        An excellent book for understanding DOS memory allocation and 
        disk structure is the "MsDOS Developer's Guide", written by the 
        Waite Group and published by SAMS.  Another excellent book, 
        which includes documentation on Expanded Memory, is "Advanced 
        MS-DOS" by Ray Duncan.
        
        In the course of developing this program, I discovered a couple 
        of interesting things about the DOS version 2 memory allocation 
        functions (48H thru 4AH).  

             1.  Transient programs are always loaded after the last 
                 allocated memory block, even if there is sufficient 
                 memory available in "holes" below the last allocated 
                 memory block.  Such holes could be created by loading a 
                 memory resident program, such as Sidekick, and then 
                 shrinking the RAM disk.

             2.  The allocate memory function (48H), on the otherhand, 
                 will use holes if they exist and if they are large 
                 enough to contain the requested block.

             3.  If a program modifies a DOS memory block (function 
                 4AH), it becomes the "owner" of that block, even if it 
                 didn't create the block in the first place.  When such 
                 a program exits, the block will be automatically 
                 deallocated by DOS unless the program exits via 
                 terminate and stay resident.   This is why ADJRAM must 
                 allocate memory blocks in fixed 32K increments.  
                 Ideally, it should allocate exactly the requested size 
                 and no more.  The DOS quirk described here prevents 
                 that though.

        The source code for the Adjustable RAM Disk is included with the 
        program.  AMDISK.DVD is coded in MASM version 1.27; ADJRAM.EXE 
        is coded in DeSmet C version 2.4.  Even though I've included the 
        source code, I would nevertheless like to act as the 
        clearinghouse for all future versions and modifications.  If you 
        make a change to the program, or fix a bug, PLEASE let me know 
        about it -- I may want to include the change in future versions.  
        
        If you modify the program, you agree to maintain my copyright.  
        You should indicate that you've modified the program by changing 
        the version number, for example "version 4.1A", or by putting 
        some other distinguishing message in the signon of the program, 
        for example "custom version by John Doe".  The rational for this 
        is simple -- I don't won't to be blamed for your bug.  

        My address, as of May 1988 is:

             GARY CRAMBLITT
             105 TENNESSEE RD
             STEVENSVILLE, MD  21666

        Please do not telephone.  I'd like to receive your letter.  
        Please note that my address is given above in order to support 
        users who encounter difficulty running ADJRAM.  I can not afford 
        to distribute copies of ADJRAM so please do not publish this 
        address.  I rely upon RBBSs and user groups to distribute 
        ADJRAM.  

                       * * * *  END OF ADJRAM.DOC * * * *