File:GET.DOC  -  Documentation for GET.EXE  -  Copyright 1991 Bob Stephan

PURPOSE: GET is a general purpose DOS BATch file enhancer.  Its purpose is 
  to make information available to the BATch file through the BATch IF 
  subcommand.  The information can come from user input or from the 
  operating system, and it is made available to the BATch file through the 
  ERRORLEVEL (Exit Code) and the GET= variable in the DOS master 
  environment. Get also has some capabilities to set some system parameters 
  and perform a few other specific actions.  Most of the items are 
  self-explanatory as seen in the help screen below.  For those which may 
  need more explanation, read on.  If you have been using an older version 
  of GET, you will probably also be interested in the information in 
  GET22NEW.DOC to help focus in on the new and improved features.

HELP SCREEN:  If you enter GET at the DOS prompt by itself, or with any 
  invalid argument such as a question mark, it will display the following 
  information:
  -------------------------------------------------------------------------
GET Version 2.2   -   Batch file enhancer   -   Copyright 1991 Bob Stephan
  Syntax:  GET command argument(s)               More Instructions: GET.DOC
Purpose             Command   Argument(s)   Environment Errorlevel  Extended
---------           -------   -----------   --(GET=)--- --(Exit)--  --[E]---
Get character(InKey)C[E] ["prompt"][chars#sec] Character ASCII dec.  No Echo
Get yes/no aNswer   N[E] ["prompt"] [seconds] Character  ASCII dec.  No Echo
Get string          S[E] ["prompt"][pattern#sec] String  Length      No Echo
Put string (Zap)    Z[E] ["string/prompt"]   String      Length      StdInput
Moving Text(GetaKey)T[E] "filespec" [chars]  Character   ASCII dec.  No Echo
Key check (IsaKey)  I[E]                     1=yes,0=no  1=yes,0=no  Get Char
Date and Time       H[E] Code 1=DoW, 2=DoM, 4=Month, etc.See GET.DOC Concat
Get DOS version     D[E]                     Major Vers. MajorMinor  MinorEnv
Keyboard BUffer     U[E] "chars" [num#num]               Length      Caps/Num
Get environment left   E[E]                  Bytes left  Bytes left  Bytes/10
Get file size (DIR=0)  F[E]  Filespec        Hex bytes   Kilobytes   Kb/10
Get disk free space    K[E] [driveletter#div] Kilobytes  Kb/10       Kb/100
Get disk capacity      Q[E] [driveletter#div] Kilobytes  Kb/10       Kb/100
Get volume label       L[E] ["label"] [drive] Label      1=yes,0=no  Match
Get memory free        M[E]                  Kilobytes   Kilobytes   Kb/10
Clear (Blank) Screen   B[E] [New attribute]  Current or last attr.   HexAttr
Check for printer(PRN) P[E]                  1=yes,0=no  1=yes,0=no  Initialize
Get/set video mode/border V[E] [New mode/color] Current or last mode VGA Border
Check coprocessor/CPU   7[E]                 1=yes,0=no  1=yes,0=no  CPU Type
Check for ANSI.SYS/Model  A[E]               1=yes,0=no  1=yes,0=no  PC Model
Get current directory   Y[E] [drive for Y]   Directory   Level/Drive Drive:A=0
Warm/Cold Boot          W[E] If argument given then 1=warm, 0=cold   ColdBoot
 See GET.DOC for additional features and BATch programming instructions.
 Surrogates:}=CR,~=Esc,Alt253=Ctrl-C,Alt255=Space.     Keys:{=Ext,Alt254=Enh.
 -----------------------------------------------------------------------------

LICENSING: VENDORS, CORPORATE, and COMMERCIAL users see licensing terms 
  below. For individuals this version of GET is free for personal use, and 
  for the use of shareware authors in distributing their products subject 
  to the conditions specified in the licensing terms below.  GET may be
  freely copied and distributed provided the files GET.DOC and 
  GET22NEW.DOC are included on the disk with it.  Contributions to support
  this development project will be gratefully accepted.

ENTERING COMMANDS: GET is used in BATch files.  When you want to use GET in 
  a BATch file, enter the word GET as the first entry on a line, followed 
  by a space and the single letter command from the above table.  If you 
  want the extended option, enter E right after the command letter with no 
  space between.  If there are arguments, enter a space and then the 
  arguments that you need or want to run the command.  On the next line 
  check the return from GET in the ERRORLEVEL and/or the GET= variable in 
  the environment which can be accessed as %GET%.  For example, to get a 
  yes or no answer you might enter the lines:

     :Ask
     GET N "Answer yes or no: "
     IF "%GET%"=="N" goto NO
     IF "%GET%"=="Y" goto YES
     Rem The next line checks to see if the user pressed Escape
     if ERRORLEVEL 126 goto END
     ECHO You must enter Y or N, or press Esc to exit.
     goto ASK
     :NO
     Rem [Do what you need to do if the user enters N]
     goto END
     :YES
     Rem [Do what you need to do if the user enters Y]
     :END The next line clears GET out of the environment.
     set GET=

  The best way to find out how GET works is to just try it.  You can try 
  it from the command line if you use SET to check the environment, but 
  to find out what is in the ErrorLevel, you must use a BATch file.  If you
  are not familiar with the DOS Environment, see the discussion of 
  ENVIRONMENT AND SHELLS later in this documentation.

SYNTAX EXPLANATIONS: 

  Command: Commands are single characters or [optionally] a character 
    immediately followed by E with no spaces between.  The E indicates the 
    Extended function above.

  Argument(s):  Arguments are zero, one, or two character strings as 
    appropriate to the command.  In some cases the first, or only, argument 
    must be enclosed in double quotes as shown on the help screen.  Each 
    character string can consist of zero or more ASCII characters.  The blank 
    or space character (ASCII 32) delimits the character strings and can only 
    be a member of one of the strings that is enclosed in double quotes.

  [] brackets indicate optional portions of commands and/or arguments. The
     command will work regardless whether these portions are included or not.
     The brackets themselves must not be included!
  "  Where double quotes ("'s) are shown, they must be included if the
     corresponding prompt or filespec argument is used.
  filespecs consist of a filename and extension as appropriate to the DOS
     file naming conventions.  They may include drive and path but no wild 
     card symbols.
  chars refers to an ASCII character string.  Blanks can only be used in 
     the strings that must be enclosed in double quotes (but see the use of
     surrogates below.)
  #  is a delimiter denoting that the characters following it are numerical 
     and have a special significance to the command.
  num, sec, and div must be entered as ASCII decimal digit characters 
     representing a number.

  Environment: this column indicates what will be found in the
     environment string GET=.  This string can be accessed from a
     BATch file with the %GET% notation. It is best to enclose %GET%
     in some additional characters in case it is empty.  For example:
     IF "%GET%" == "" will check for an empty GET variable.

  Errorlevel: this column indicates what value will be placed in the
     DOS errorlevel that can be accessed in BATch files with the
     "if errorlevel" subcommand.  Always check for ErrorLevel from 
     highest to lowest values of interest. ErrorLevel is also referred
     to as Exit Return Code.

  Extended: this column indicates the action taken if the optional
     [E]xtended command is included.  Do not include the brackets!
     In most cases E applies to the result in the Environment or the
     result in the ErrorLevel, but not to both.

  Surrogates and Extended Characters:  Some characters are awkward or 
     impossible to handle directly.  For example, BATch files generally use 
     the carriage return <CR> and space characters as delimiters instead
     of as ASCII characters that can be manipulated.  Some special symbols
     have been designated to facilitate the handling of these characters.
     Extended keys are those with no ASCII representation, such as the
     function and cursor keys.  Enhanced keys are keys on the enhanced
     keyboard which do not appear on older keyboard layouts, such as F11
     and F12. These substitutions may have different meanings depending
     on the command being used, so read the description of the command.
       Carriage Return: }=CR            Extended:       {=Ext
       Escape:          ~=Esc           Enhanced: Alt-254=Enh
       Blank:     Alt-255=Space.        Break:    Alt-253=Ctrl-C
     The Alt- characters can be entered in most text editors by holding 
     down the Alt key while spelling out the digits for the character on
     the number pad of the keyboard, but check your text editor for this
     capability.
   
GET USER INPUT:  The commands C, N, T, S, I, and Z pertain to obtaining
  keyboard input from the user.  These commands take 0, 1, or 2 arguments.  
    
  "prompt"  refers to an arbitrary character string that will be displayed
    on the screen to coach the user at to what type of input is expected.
    If a prompt is used, it must be enclosed in double quotes.
  chars -- also see char information above -- are ASCII character strings 
    which cannot include the space character, but may include surrogates. If 
    chars are given, user input will be limited to the characters in the 
    character string, or the ones indicated by the surrogates. If no chars 
    are given, any key stroke will be accepted. To indicate that a carriage 
    return, Esc, space, or Extended key is acceptable, include the surrogate 
    character listed above.  CR and Esc will return 125 and 126 in the 
    errorlevel respectively, and the surrogate character in the environment. 
    If extended keyboard characters are specified, the scan code will be in 
    the errorlevel and the corresponding ASCII byte in the environment 
    preceded by "{".  A table of keyboard scan codes will be useful.    
    Think of ASCII 255 as an upper-case Space for purposes of GET input.
  Enhanced: To indicate that enhanced characters (e.g., F11 and F12) are 
    acceptable, include the ASCII 254 character instead of {. If you use 
    ASCII 254 as the surrogate for extended keys, the BIOS function for the
    enhanced keyboard will be used.  This permits the recognition of F11 
    and F12 as well as other enhanced keyboard keys.  ASCII 254 can 
    usually be entered by using Alt-254 on the numeric keypad, but check 
    your text editor for the method it uses.  This should not be used 
    unless you are sure that all users of your batch file will be using 
    enhanced keyboards because it absolutely does not work on machines 
    with older BIOS's that do not recognize the extra enhanced keyboard 
    keys.
  Break: A surrogate of ASCII 253 will suppress Control-C and Ctrl-Break
    exception handling.  This must be the last or only character
    argument. It applies only to the S, C, or N commands, and should 
    be used with caution. Note that this surrogate has a different kind of
    meaning and function than the other surrogates.
  pattern is a special case of chars in which certain characters have 
    special meanings.  See the S command for detailed information.
  # is a delimiter that must immediately follow the chars or pattern 
    argument if it is used.  The number following # will be used to 
    establish the number of seconds to wait for the first key stroke to 
    be entered.  If timeout takes place with nothing entered, the 
    ErrorLevel will be 0, and there will be no GET variable in the 
    environment.  If no time is specified, GET will wait forever.  If a 
    wrong key is pressed the timeout is cancelled.  The #seconds must be 
    the last argument, and must contiguously follow any other character 
    argument.  Example: GET C YN#20 will wait 20 seconds for a character 
    to be entered.  If none are entered in that time, GET will exit with 
    0.  If a wrong character (not Y or N) is entered, GET will wait 
    until a correct character is entered regardless of the time.
    
  General: The C, N, and S commands read characters using a BIOS call so 
    they bypass Standard Input and most keyboard redefinition methods 
    (macros).  The argument for the C, N, or S commands can consist of 
    [chars][Alt253][#seconds] in that order, and it must be contiguous.
  Please remember that <, >, and | are DOS redirection characters and you 
    cannot use them as characters in BATch files.  4DOS also uses ^ and 
    ` as special characters so they should not be used either.
    Single keystrokes for C, N or T are acted on without pressing Enter.
    (String input, of course, will require the user to press Enter.)
    The comparison of characters is not case sensitive.  
  When checking for string matching with the MS DOS BATch IF subcommand, 
    remember that it is case sensitive. Different versions of DOS handle the 
    IF "string"=="string" somewhat differently, and there have been several 
    "bugs" reported in one version or another.  Try to test any such 
    constructs under several versions including DR DOS and 4DOS if possible.  
    In some versions the string cannot contain any spaces.  The test under 
    4DOS is not case sensitive, and it can contain spaces if the strings are 
    enclosed in double quotation marks.

  C  accepts single keystroke character input.  The keystroke will not
     be echoed to the screen if CE is used. It is often convenient to ask 
     the user to press the space bar, and the space surrogate makes it easier 
     to check for a space. (i.e., IF "%GET%"==" " does not work in all DOS 
     systems if GET contains the space character.)
  N  is a special case of C.  The yes/no aNswer will accept y, n, carriage
     return, or Esc.  The Ctrl-C surrogate and a number of seconds to wait 
     may be specified, but no other chars will be recognized.
  T  the Moving Text feature, is another special case of C.
     T requires a file with the prompt string which will be displayed moving 
     across the bottom line of the screen. Currently only standard 25 line 
     screens are supported.  The text file should be plain ASCII without any 
     control characters (No CR, LF, or any other characters below ASCII 32).  
     To be effective the prompt must be over 80 or more characters long, and 
     to ensure smooth wrap-around the first 79 characters should be repeated 
     at the end.  The maximum length for the text of the moving prompt is 
     4096 characters.  Over that it will be truncated.  T does not accept
     a waiting period argument at this time.
  S  accepts character string input terminated by a carriage return.
     SE does not echo user input to the screen.  This is useful for 
     hiding the entry of a password, for example.  Extended and enhanced
     keys will not be accepted, but break can be suppressed.  The length of
     the string entered is returned in ErrorLevel.  If the user presses Esc,
     GET will exit and leave the Esc surrogate in the Environment and 1 in
     ErrorLevel. The length of a string for the S command can be specified 
     by creating an argument of characters equal in number to the maximum
     length of the string allowed.  No argument defaults to 79 characters.  
     A beep will be sounded if the maximum length has been reached and more 
     characters are attempted.  
       The pattern in the argument specifies the acceptable characters
     for each position as follows.  Note that the upper case 
     characters T, A, and Z will cause lower case characters to be 
     converted to upper case.  Conversions to upper case also
     cause the space character to be converted to ASCII 255.  This will 
     facilitate BATch file checking with the IF subcommand. 
       tT - any typeable character,     T - a-z will be upper cased.
       aA - any alphabetic character,   A - a-z will be upper cased.
       zZ - any alphanumeric character, Z - a-z will be upper cased.
        9 - any digit 0-9.           Alt-255 - space character only.
       Any other character must match the character entered exactly.  
  I  checks to see whether a key has been pressed but it does not wait
     for a keystroke if none is in the buffer.  The IE command will
     read the key if it is present or return 0 and expunge GET from the 
     environment if no character is waiting.  Any character will be 
     accepted including extended characters, and no surrogate 
     translation is made.  The difference in the IE command from the C
     command is that IE checks DOS Standard Input so it responds
     to redirected input and Ctrl-C, but it cannot see keys that are only 
     available on the enhanced keyboard such as F11 and F12.
 Z   uses the "prompt" string as input.  It will put the "prompt" 
     string into the master environment (if it can find the master 
     environment).  GET ZE, like the old GET S, will take input from 
     Standard Input and transfer it to the GET= variable in the 
     current environment.  The input must be less than 80 characters 
     and must be terminated with a carriage return.  GET ZE will take 
     input from the keyboard (Get String), or from redirection or 
     piping.  For example, CD|GET ZE is another way to get the current 
     directory into the master environment. You can even read the first 
     line of a text file with GET ZE<filespec. If you don't want to see 
     the echo from DOS, redirect output to NUL - e.g.  CD|GET ZE>NUL or 
     GET ZE<filespec>NUL.  If you specify a prompt for ZE, it will be 
     displayed before reading standard input.  Note that only Z attempts
     to put the GET variable in the MASTER environment.  If GET is running
     under a secondary command processor, the GET variable may not be
     available to the current BATch file.  See discussion of SHELLS later.

GET DISK and FILE Information:  The commands K, Q, L, F, and Y obtain 
  information about disks and/or files.  Q, K and L will check if the drive 
  contains a formatted disk and return an ERRORLEVEL 0 if it does not.  
  This avoids the Abort, Retry, etc. error handling.  If the ERRORLEVEL is 
  0 the error code will be in %GET% as a hexadecimal value.  
     Some error values of interest are: 
      0 - Write protected diskette
      1 - Invalid drive letter
      2 - Drive not ready - no disk or door open.
      4, 6, 7, 8, & B - Disk read errors
      C - General, nonspecific error.
      F - Invalid disk change

  K disK free space in kilobytes.  The only argument is a drive letter.
    The default is the current drive.
  Q The capacity of a disk.  GET Q works just like GET K except that it 
     returns the capacity of the disk as if it were empty. Q for Quota?
  For Q and K the extended command divides the ERRORLEVEL by 100 but doesn't 
  reduce the Environment variable.  If you need a different divisor for 
  KE you can use the # notation similar to the timeout feature.  For example
  if you want the ERRORLEVEL in megabytes you can enter GET KE #1024.  This 
  will override the default division by 100 for KE.  Prior to version 2.2, 
  GET did not report accurate information on the new large hard disk 
  partitions. This is now corrected, and the # feature will be needed to 
  get ERRORLEVEL information on such large partitions.

  L  gets the Volume Label of the specified disk.  The ErrorLevel contains
     the length of the label (0-11 characters). The optional argument is
     the drive letter, defaulting to the current drive.  If the disk is not 
     labelled, the GET variable will be expunged and the ERRORLEVEL will be 
     0.  The LE command takes a trial label in the "label" argument 
     and sets the ERRORLEVEL to indicate whether the disk label
     matches.  The comparison is case sensitive and there must not be
     any trailing blanks in the "label" argument.
  F  file size in kilobytes.  The file size is reported in the Environment
     in hexadecimal and in the ErrorLevel as kilobytes.  For KE the divisor
     is 10.  This affects the ErrorLevel only.
     The file specification (filespec) is not in quotes and must not
     contain wild card characters, but may contain drive and path information.
     Directory existence.  The F command for GET Filesize can now be used to
     determine whether a named directory exists.  As usual, if the filespec
     is a directory, the ErrorLevel will be 0.  If the filespec cannot be 
     found, the GET variable will be expunged from the environment and a
     standard DOS error code will be returned in the ErrorLevel.  The 
     error codes of special interest are 2 for "File not found" and 3 for 
     "Path not found".  For example: GET F "d:\mydir\xxx" will return 
     2 if the path is found but not the file named XXX, and it will return 
     a 3 if the path D:\MYDIR is not found.  Also, GET F "d:\mydir" 
     will return 2 in either case since it is not clear whether MYDIR 
     is a file or a path.  Whenever the item specified in the filespec 
     may not exist, always check for an empty GET variable (IF "%GET%"=="")
     which indicates that an error code is in the ErrorLevel. 
  Y  gets the current directory.  It takes an optional drive letter argument
     which defaults to the current drive.  The ErrorLevel reports the 
     directory level - 0 = root directory, 1 for first subdirectory level,
     etc.  YE returns the current drive.  The drive letter is in the 
     Environment, and the drive number in the ErrorLevel - 0=A, 1=B, etc.

GET MEMORY/SYSTEM Information:  The commands B, P, V, E, M, D, 7, A, and H
  obtain information about the operating system and hardware configuration.

  B  the screen Blanker actually performs a clear screen, not a blanking.
     GET B uses your color settings unless you give it a different
     attribute to use.  It automatically adapts to any number
     of lines on the screen (e.g. EGA 43 or VGA 50).  If an attribute
     argument is given it is taken to be a 1, 2, or 3-digit decimal number
     that is converted to a two-digit hexadecimal number for the attribute.
     The extended function BE regards an argument as a 1 or 2-digit hex
     number, and the GET value in the environment is in hex.
     A table of DOS screen attributes will be useful.
  P  checks whether a printer is available and ready.  1=yes, 0=no.
     The [E] option sends the DOS BIOS initialization signal to the printer
     as it does during boot-up.  This may not work if a print buffer or
     spooler is in use unless it can be bypassed.  If your printer has an
     internal buffer this is a way to flush it.  If PE reports no 
     printer then the print-screen operation (the Print Screen or Shift 
     PrtSc key) will be disabled to prevent hanging the computer if the 
     PrtSc key is inadvertently pressed.  To enable print-screen again, 
     run GET PE with a printer attached and ready.
  V  gets and optionally sets the video mode.  A table of video modes
     will be helpful.  Don't fool around with Video mode unless you know 
     what you're doing to prevent setting a mode that is not supported by
     your monitor. VE will get/set the border color on a VGA or EGA monitor.
  E  reports the number of bytes of Environment space available.  If it
     might be over 255 use EE which divides the number of bytes by 10.
  M  reports the free memory available in kilobytes.  ME divides by 10.
  D  reports the DOS version.  The ErrorLevel will contain a number such as
     33 for DOS 3.3.  The Environment will contain the major version such 
     as 3 for DOS 3.0, 3.1, 3.3, or 3.3.  DE will report the minor version
     in the Environment such as 1 for DOS 3.1.
  7  reports whether a math coprocessor is installed.  1=yes, 0=no.
     GET 7E reports the CPU chip type - 0 for 8088/86, 2 for 80286, or
     3 for 80386 or later.
  A  reports whether ANSI.SYS is loaded.  If you are using an ANSI.SYS 
     clone, check to see if it works with yours.
     GET AE will return the ROM BIOS model byte.  At this time the 
     only documented bytes listed in "The NEW Peter Norton's 
     Programmer's Guide to the IBM PC and PS/2" (Page 64) are:
      FF(255)=PC(1981)    FE(254)=PC or PC/XT(1982)    FD(253)=PCjr(1983)
      FC(252)=PC/AT(1984-85),PC/XT Model 286(1986),PS/2 Model 50/60(1987)
      FB(251)=PC/XT(1986)      FA(250)=PS/2 Model 25(1987)/30(1986)
      F9(249)=PC Convertible   F8(248)=PS/2 Model 80(1987)
      (Example: My 80386 AT clone is an FC).
  H  The new H Date and Time command works slightly differently than 
     most of the others.  The value(s) to be gotten are determined by 
     a coded numerical argument.  The codes to be summed are:
      1 Day of the Week(default)  16 Hour
      2 Day of the Month          32 Minute
      4 Month                     64 Second
      8 Year                     128 Odd or Even
     With the HE command, you add up the codes for the values you want 
     concatenated together in the environment.  With this form of the 
     command the ErrorLevel is the length of the GET variable, but it 
     is not very meaningful or useful. The unextended H command will 
     return a single value in both the ErrorLevel and the Environment.  
     If you sum codes for H, only the lowest value in the sum will be 
     recognized and the value returned.  If 128 is added in, the 
     ErrorLevel will report only if the value is Odd(=1) or Even(=0)
     for H.  128 does nothing for HE.  Example:  GET HE 14  will
     set GET=mm-dd-yy and place 8 in the ERRORLEVEL.

PERFORM AN ACTION: The GET commands U, V, B, P, W, and Z will perform
  some system action or setting.  V, B, P, and Z have already been
  documented above and only a brief review will be given here.

  V  can set video mode or border color.
  B  can set the screen attribute.
  P  can reset the printer and turn off PrtSc.
  Z  can place a string in the master environment.
  W  will reboot the computer as if the 3-finger salute was pressed.  
     WE will reboot as if the computer was turned off then on again.  
     If any characters are present as an argument, GET will attempt to 
     determine if the preceding boot was warm or cold instead of 
     rebooting.  This does not work on all machines (it worked on my XT
     but not  on my 386).  If successful, a 1 indicates the previous boot
     was warm, 0 means it was a cold boot.
  U  will stack keys in the keyboard bUffer.  The syntax is
       GET U "chars" num#num 
     where chars are any ASCII characters you want stacked, and the "num"s
     are decimal representations of values for either ASCII codes or scan 
     codes.  Up to 4 digits can be used for either number.  E.g. to end 
     the string with a carriage return use #13. To enter a scan code 
     add it to 255.  E.g. the scan code for F1 is decimal 59 so use 
     314. The following will stack the word "help" in the buffer and 
     execute it as a command by stacking the Enter key: 
      GET U "help" #13 
     The following command will stack the F1 key: 
      GET U 314 
     NOTE: GET U will only work on AT class machines and later! 
     With GET U you can provide a default entry for a GET S string; 
     however, the DOS keyboard buffer only holds 16 characters, so it has 
     to be rather short.  Use GET U "default" followed by GET S "prompt", 
     and the default string will be entered for the user.  The user can 
     either change or accept it; but the user will have to backspace to 
     change it. 
     The UE command will let you adjust the Caps, Num, and Scroll Locks. 
     Sum the numbers for Scroll=16, Num=32, Caps=64 for the Locks you want 
     to set.  The other(s) will be cleared.  You must use GET UE #num.
        
ENVIRONMENT AND SHELLS: This is a brief, general discussion of the DOS
   Environment for those who may not be sufficiently familiar with it.

   The DOS Environment is a small area (usually) of memory that DOS 
   automatically allocates to every program that it is asked to load or 
   run.  The "master" environment is the original Environment allocated to 
   COMMAND.COM or 4DOS or whichever command processor you are using.  The 
   original size of the Environment can be set in later versions of DOS by 
   using the SHELL command in your CONFIG.SYS file.  However, the setting 
   of Environment size is not a SHELL command function, but is a command 
   processor option.  For example, the COMMAND.COM /E: switch lets you set 
   the size if you are using COMMAND.COM as your command processor.  For 
   documentation look under such topics as SHELL, COMMAND, and Configuring 
   Your System in your DOS manual.  Since most new programs make extensive 
   use of the Environment, it is important to be sure enough Environment 
   space is allocated to accommodate them all.  If you see the error 
   message "Out of Environment Space", you know that you do not have 
   enough allocated.

   You can view the contents of the Environment by issuing the DOS SET 
   command with no arguments at the DOS prompt.  You will see a sequence of 
   variable names, each followed by the "=" sign and the string value 
   assigned to the variable.  For example, COMSPEC=C:\COMMAND.COM.  You can 
   also store string information in the Environment with the SET command 
   by specifying it in the same manner as it is displayed.  For example,
   SET PATH=C:\;C:\DOS.  Do not place any spaces on either side of the "=" 
   sign unless you intend for the space to be either a part of the variable 
   name or a part of the string.  When DOS loads and runs a COM or EXE 
   program file, that program receives a copy of the Environment as it is 
   at that time, trimmed down so that only a few bytes remain free.  This 
   copy does not change unless the program that owns it changes it.

   Note that some DOS "shells" shield the master environment from programs 
   that are executed by the shell. If you find that to be the case, the 
   information will usually be available to the BATch file from the 
   environment of the secondary command processor loaded by the shell as is 
   usually necessary to run a BATch file.  Except for the Z command, GET 
   only attempts to locate the environment of the command processor that is 
   running the BATch file, so the environment information can disappear if 
   the shell or the secondary command processor is terminated.  GET 
   attempts to place the information where the BATch file can locate it 
   since that is its primary purpose.  Also, when running from a shell 
   there may be problems with "Out of environment space" since DOS does not 
   usually allocate excess environment space to child processes.  4DOS 
   provides a means to ensure that copies of the environment have 
   sufficient space available.  Check the documentation for your shell to 
   see if it can make sufficient environment space available.  You can 
   always ensure that GET has enough environment space to store its results 
   by establishing a dummy GET variable before loading any shells or other 
   programs.  The best way would be to do it in your AUTOEXEC.BAT.  Simply 
   insert the command SET GET=xxxxxxxxxxxxxxxx in your AUTOEXEC.BAT file 
   with enough x's or other characters for the maximum length input string 
   you are expecting.  

PROGRAM INFORMATION:

  GET is programmed in assembly language for MS-DOS computers. It was
  assembled with Borland's Turbo Assembler, and compressed with LZEXE. 
  If you need more BATch programming capability than is included here, I 
  suggest you look into one of the more general BATch programming 
  products such as the Shareware product, Extended Batch Language (EBL) 
  which is available through most sources of shareware.

  Some of the code for GET was adapted from the sample program named 
  WHAT.ASM included with Microsoft Macro Assembler (MASM).  The MASM 
  documentation declares that the sample programs are in the public 
  domain. For examples of GET, look at the BATch files on the MASDIR 
  disk mentioned below for the use of a similar program called SDL_GET.  
  You can do a lot in BATch programming with this utility.  

LICENSING:  Although this version of GET remains free for personal use
  for all to enjoy, if you like GET and would like to help support 
  development of inexpensive software, please send a contribution to the 
  address below.  Thank you for any support you care to provide.  If you 
  send $15 or more you will receive the following benefits:
    The latest version of GET with any new features.
    A smaller runtime version to distribute with your BATch files.
    A single user license with no royalties for use of the runtime version.
    Printed documentation giving examples and more detailed explanations.
    Free support by BBS, mail, phone, CompuServe, or Genie (see below).
    Notification of new releases and inexpensive upgrades.
  Corporate users must obtain a site license from me for in-house use.  
  If GET is to be installed on 2 machines $25, 3 machines $35, plus $5 
  for each additional machine.  None of the above licensing terms 
  includes using GET in conjunction with the distribution of a 
  commercial (retail) software product other than shareware, 
  user-supported, or public domain software. To use GET in conjunction 
  with the distribution of a retail software product you must contact 
  me to discuss terms.  Call or message me if you are interested.

  BBS SYSOPs, PC User Groups, and shareware authors and distributors are 
  hereby granted a single user license to use GET for their own purposes 
  and to freely distribute unmodified copies of this version of GET.EXE
  GET.DOC and GET22NEW.DOC together as a unit.  If an unregistered version
  of GET is used in conjunction with the distribution of a shareware or
  public domain software product, the distribution disk must include
  GET.DOC and GET22NEW.DOC.

  If you have any questions, comments, or suggestions please contact me at:
      MOBY DISK: 1021 San Carlos Road, Pebble Beach, CA 93953
  Phone: (408) 646-1899/1373.  GENIE:MOBYDISK.  COMPUSERVE:72357,2276
  BBS: The Cricket 408-373-3773           /s/ Bob Stephan   May 27, 1991

    Now for the commercial: If you like GET please try MASDIR!
  MASDIR (pronounced 'master') the MASter DIRectory System, is a general
  purpose sorted directory program with unique customization and disk label 
  printing features. If you ever use DIR, you should do yourself a
  favor and take a look at MASDIR. The main program, SDL.COM, is one of the
  best sorted directory programs anywhere. The setup program allows you to
  set the many defaults to your own specifications, including customizing
  the titles that appear in the header. In addition, you can print disk
  labels and/or sleeve inserts for 5.25" and 3.5" diskettes. This really
  saves you a lot of time when you are looking through your collection of
  diskettes for a particular file. They are all listed conveniently along
  with your own description in the title lines. You can also create disk
  file catalogs of your diskettes and directories that you can then
  annotate to describe individual files.

  Additional features include listing only subdirectories or not 
  listing them at all, listing only files created today or within a 
  specified period, reverse sorting for any of the sort options,  the 
  amount of space a group of files will occupy for different cluster 
  sizes, support for DR DOS and 4DOS, SETting defaults in the environment, 
  enter two file specifications such as *.COM *.EXE, paging up and 
  down in large directories, show only files that have not been backed 
  up, and many more.

  As of the above date, the current release of MASDIR is Version 5.4. It 
  is a shareware program that is available on bulletin boards, GENIE, 
  CompuServe, The Public (software) Library, and from other distributors 
  of public domain and shareware programs. If you cannot conveniently 
  locate a copy, I will be happy to send you one. Just contact me as 
  indicated above. Thank you for your kind attention. /Bob/