User documentation for the packet driver collection
                                   Russell Nelson
                                 Clarkson University
                                  Potsdam, NY 13676
                              nelson@clutx.clarkson.edu


          Why?

               Every PC Ethernet board is different.  The 3c501 was, for
          some time, the most popular board, and would have become the
          defacto standard but for its poor performance.  By the time 3Com
          created a board with acceptable performance, so had many others,
          and 3Com lost its lead.  FTP Software, in order to support each
          of these boards without losing its collective mind, created the
          Packet Driver Spec (PDS).


          What?

               Some boards use DMA, some use programmed I/O, and some use
          shared memory.  The PDS masks the differences between these
          boards by defining a software interface to the boards.  This
          software interface is a software interrupt in the range between
          0x60 (hex) and 0x80.


          How?

               The packet driver must be installed prior to use.  Since
          each packet driver takes only approximately 1800 bytes, this is
          best done in your autoexec.bat.  Since the Ethernet boards typi-
          cally have jumpers on board, the packet driver must be informed
          of the values of these jumpers (auto-configure is possible, but
          can disturb other boards).  The first parameter is the software
          interrupt used to communicate with the packet driver.  And again,
          because each board is different, the rest of the parameters will
          be different.

          Before installing the packet driver, you must choose a software
          interrupt number in the range between 0x60 and 0x80.  Some of
          these interrupts are used for other purposes, so your first
          choice may not work.  See Appendix A for the section of Ralf
          Brown's interrupt list between 0x60 and 0x80.

          Running a packet driver with no specifications will give a usage
          message.  The parameters for each packet driver are documented
          below.







          3Com 3C501
               usage: 3C501 packet_int_no [int_no [io_addr]]

               The 3c501 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.


          3Com 3C503

               usage: 3C503 packet_int_no [int_level(2-5) [io_addr
          [cable_type]]]

               The 3c503 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the cable type.
          The 3c503 can be attached to thick or thin Ethernet cables, and
          the selection is made in software.  The cable type parameter
          should be zero for thin, and one for thick.  The defaults are 2,
          0x300, and 0 (thin).  The 3c503 uses shared memory whose address
          is set by jumpers, but the software can ask the board what the
          address is.


          3Com 3c505

               usage: 3c505 packet_int_no [int_no [io_addr [base_addr]]]

               The 3c505 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 2 and 0x300 and 0xd000.


          3Com 3c523

               usage: 3c523 packet_int_no [int_no [io_addr [base_addr]]]

               The 3c523 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 3 and 0x300 and 0xc000.


          IBM Token Ring

               usage: ibmtoken packet_int_no [adapter_no]

               The IBM Token Ring packet driver requires one additional
          parameters -- the adapter number.  The default is zero.  See
          IBMTOKEN.DOC for more information.







          BICC Data Networks' ISOLAN 4110 ethernet

               usage: isolan packet_int_no [int_no [base_addr]]

               The BICC Isolan requires three additional parameters -- the
          hardware interrupt number and the memory base address.  The
          defaults are 2 and 0xb800h.


          3Com ne1000

               usage: ne1000 packet_int_no [int_no [io_addr]]

               The ne1000 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.


          Racal-Interlan (Formerly Interlan) NI5010

               usage: NI5010 packet_int_no [int_no [io_addr]]

               The NI5010 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.


          Racal-Interlan (Formerly Micom-Interlan) NI5210

               usage: ni5210 packet_int_no [int_no [io_addr [base_addr]]]

               The NI5210 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 2 and 0x360 and 0xd000.  Note that
          Interlan sets the default memory base to 0xa000, which is brain-
          damaged, because that area of memory is specifically reserved for
          video adapters, and in fact the EGA and VGA use it.


          Racal-Interlan (Formerly Micom-Interlan) NI9210

               usage: ni9210 packet_int_no [int_no [io_addr [base_addr]]]

               The NI9210 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 2 and 0x360 and 0xd000.


          SLIP8250

               usage: SLIP8250 packet_int_no [driver_class] [int_no]
                  [io_addr] [baud_rate] [send_buf_size] [recv_buf_size]
                  The driver_class should be SLIP, KISS, AX.25, or a
                  number.







               The SLIP8250 is not strictly an Ethernet adapter, however
          some software packages (such as KA9Q's NET) support Serial Line
          IP (SLIP).  SLIP must be specially supported because it doesn't
          use ARP and has no hardware addresses prepended to its packets.
          The PDS is not clear on this, but the packet driver does the SLIP
          encoding.
          The parameters are as follows.  The driver_class is the class
          that is returned to a client of the packet driver spec in the
          Drive_Info call.  The int_no is the hardware interrupt number,
          defaults to 3 (COM1).  The io_addr is the hardware I/O address,
          defaults to 0x3f8 (COM1).  The baud_rate defaults to 4800 baud.
          The send_buf_size and recv_buf_size default to 3000 each.


          Western Digital WD8003E,WD8003ET/A

               usage: WD8003E packet_int_no [int_level [io_addr
          [mem_base]]]

               The WD8003E driver is also for the WD8003ET/A, a
          MicroChannel Ethernet adapter.  The WD8003E requires three addi-
          tional parameters -- the hardware interrupt number, the I/O
          address, and the memory base address.  The defaults are 2 and
          0x280 and 0xc400.


          What else?

               There are also several utility programs for packet drivers:


          PKTADDR

               usage: pktaddr packet_int_no [ethernet_addr]

               If the second argument is given, the Ethernet address of
          the given packet driver is set.  The Ethernet address is printed
          out.


          PKTALL

               usage: pktall packet_int_no

               All packets are received and discarded from the given
          packet driver.  This program is of most use with PKTMODE and
          TRACE.







          PKTCHK

               usage: pktchk packet_int_no [packet_int_no]

               Test for existance of a packet driver.  Returns with
          errorlevel 0 if the specified interrupt has a packet driver.  If
          the second argument is given, all interrupts in the range are
          checked for a packet driver.  If no packet driver is found at
          all, errorlevel 1 is returned.


          PKTMODE

               usage: pktmode packet_int_no [receive_mode]

               If the second argument is given, the receive mode of the
          given packet driver is set.  A decimal number from the list of
          modes should be used.  All the possible modes are printed out.
          Unimplemented modes are marked with "xx", and the current mode is
          marked with "->".


          TERMIN

               usage: termin packet_int_no

               The specified packet driver is terminated, and its memory
          recovered.

          STAT

               usage: stat

               The statistics for all packet drivers are printed.  The
          meanings of the columns are given below.


          pktin   is the number of packets ever received by this driver.
          pktout  is the number of packets ever transmitted by this
                  driver.
          bytin   is the number of bytes ever received by this driver.
          bytout  is the number of bytes ever transmitted by this driver.
          pkdrop  Packets dropped because there was no handler for that
                  Ethernet packet type.
          errin   Dependent upon the packet driver.
          errout  Dependent upon the packet driver.



          TRACE

               usage: trace packet_int_no [buffer_size]

               Trace is very useful for debugging packet driver troubles.
          Trace lets you trace all transactions between a user program and







          the packet driver.  The transactions are stored in a memory
          buffer whose size is set with buffer_size.  The default size is
          10,000 bytes.

               When you run trace, it sets itself up and then spawns
          COMMAND.COM so that you can run a network program that uses the
          packet driver.  After you quit your network session, you issue an
          "EXIT" command.  This returns you to trace, which writes the
          transaction log to "TRACE.OUT".  The following program, DUMP,
          interprets TRACE.OUT.


          DUMP

               usage: dump

               Interprets the contents of TRACE.OUT as written by TRACE.


          Who?

          See the file support.txt for a listing of all the people who
          contributed packet drivers.







                                     Appendix A
                   Interrupt usage in the range 0x60 through 0x80



          60 -- -- reserved for user interrupt
          60 -- -- FTP Driver - PC/TCP Packet Driver Specification
          60 01 FF FTP Driver - DRIVER INFO
          60 02 -- FTP Driver - ACCESS TYPE
          60 03 -- FTP Driver - RELEASE TYPE
          60 04 -- FTP Driver - SEND PACKET
          60 05 -- FTP Driver - TERMINATE DRIVER FOR HANDLE
          60 06 -- FTP Driver - GET ADDRESS
          60 07 -- FTP Driver - RESET INTERFACE
          60 11 -- 10-NET - LOCK AND WAIT
          60 12 -- 10-NET - LOCK
          60 13 -- 10-NET - UNLOCK
          60 20 -- FTP Driver - SET RECEIVE MODE
          60 21 -- FTP Driver - GET RECEIVE MODE
          60 24 -- FTP Driver - GET STATISTICS
          61 -- -- reserved for user interrupt
          62 -- -- reserved for user interrupt
          63 -- -- reserved for user interrupt
          64 -- -- reserved for user interrupt
          65 -- -- reserved for user interrupt
          66 -- -- reserved for user interrupt
          67 -- -- LIM EMS
                   ...
          67 DE 00 Virtual Control Program Interface - INSTALLATION CHECK
                   ...
          68 01 -- APPC/PC
                   ...
          69 -- -- unused
          6A -- -- unused
          6B -- -- unused
          6C -- -- system resume vector (CONVERTIBLE)
          6C -- -- DOS 3.2 Realtime Clock update
          6D -- -- VGA - internal
          6E -- -- unused
          6F -- -- Novell NetWare - PCOX API (3270 PC terminal interface)
          6F 00 -- 10-NET - LOGIN
                   ...
          70 -- -- IRQ8 - AT/XT286/PS50+ - REAL-TIME CLOCK
          71 -- -- IRQ9 - AT/XT286/PS50+ - LAN ADAPTER 1
          72 -- -- IRQ10 - AT/XT286/PS50+ - RESERVED
          73 -- -- IRQ11 - AT/XT286/PS50+ - RESERVED
          74 -- -- IRQ12 - PS50+ - MOUSE INTERRUPT
          75 -- -- IRQ13 - AT/XT286/PS50+ - 80287 ERROR
          76 -- -- IRQ14 - AT/XT286/PS50+ - FIXED DISK
          77 -- -- IRQ15 - AT/XT286/PS50+ - RESERVED
          78 -- -- not used
          79 -- -- not used
          7A -- -- Novell NetWare - LOW-LEVEL API
          7A -- -- AutoCAD Device Interface
          7B -- -- not used







          7C -- -- not used
          7D -- -- not used
          7E -- -- not used
          7F -- -- HDILOAD.EXE - 8514/A VIDEO CONTROLLER INTERFACE
          7F -- -- HLLAPI (High-Level Language API)
          80 -- -- reserved for BASIC