File:   IBMTOKEN.DOC
       Auth:   Brian Fisher
       Date:   October 3 1989
     
       Purp:   Notes on IBMTOKEN.COM, the 'Ethernet' packet driver
               for TCP/IP and NCSA Telnet.
     
========================================================================
     
       IBMTOKEN is an Ethernet packet driver for the IBM Token Ring
       Adapter card.  The IBM Lan support program must be installed before
       you use IBMTOKEN.
     
       CONFIG.SYS - to install the LAN Support program:
     
       device=C:\PCLAN\DXMA0MOD.SYS
       device=C:\PCLAN\DXMC0MOD.SYS
       device=C:\PCLAN\DXMT0MOD.SYS
     
       AUTOEXEC.BAT - to install IBMTOKEN and define NCSA config file:
     
       IBMTOKEN 0x61   0
       SET CONFIGTEL=C:\CONFIG.TEL
     
     
       CONFIG.TEL
     
       myip=xx.yy.zz.qq                # put your IP address here
       netmask=255.255.255.0           # use your network mask here
       hardware=packet                 # tell NCSA to use the packet driver
                                       # interface
       address=0                       # class for packet driver
       ioaddr=0x61                     # vector given to IBMTOKEN
     
       mtu=1500                        # max IBMTOKEN can transmit
       maxseg=1500                     # max IBMTOKEN can receive
       rwin=536                        # max if NCSA can't do IP fragments
     
     
       IBMTOKEN:
     
       IBMTOKEN <vector> <adapter>
     
       where    vector is the interrupt assigned to the packet driver
                interface
     
                adapter is 0 for the first adapter card, and 1 if the
                second adapter card is to be used.
     
     
     
       When IBMTOKEN installs, the following occurs:
     
               1)   DIR.INITIALIZE is called to initialize the adapter.
               2)   DIR.OPEN.ADAPTER is called to set up buffers for
                    IBMTOKEN.
               3)   RECEIVE is called to set up the receive service
                    routines.
               4)   DIR.STATUS is called to determine the address of the
                    adapter.
     
               If any of these calls fails, the installation is aborted.
     
               IBMTOKEN may not install properly if the token ring adapter
               has been in use by another program, and to closed properly.
               If this is the case, reboot and run IBMTOKEN.
     
     
       OPERATION:
     
       IBMTOKEN translates 'Ethernet' packet driver calls to 802.2 LLC
       format packets for transmission.  Currently it supports IP and
       ARP transmissions.  RARP and BOOTP probably won't work.
     
       IP packets are sent 'as is'.  ARP packets require a minor modification
       before they are sent.  The hwr address space value must be changed from
       1h to 6h.  On receive, the driver changes 6h back to 1h.  The size (60
       is min for Ether) must be set to 28 or some token hosts won't accept
       the transmission.
     
       Receive packets smaller than 60 bytes are rounded up so the upper
       level will accept them.
     
       Token Ring source routing.  When the upper level call back routine
       accepts a packet, its RIF is recorded in a table interal to IBMTOKEN.
       When IBMTOKEN sees the destination address requires a RIF, the
       info is pulled from the table and added to the MAC header for transmit.
     
       IBMTOKEN can handle a maximum of 32 source route entries.  One
       default entry is present for the 'broadcast' address.  The first
       source route received for an address is assumed to be the shortest.
       Subsequent source routes from the same host are ignored.