-------------------------[ WI.LIB ]----------for DOS---------------------------
                      WI.LIB - Wilkes Index Library
                    Copyright (c) 1989 by Roger Wilkes
           Member: Association of Shareware Professionals (ASP)
                  Cost of this Software $40; Gov./Ed. $30
                        Wilkes Software, inc.
                        Memphis, TN 38134
                    or Register on BBS at (901)377-5608
-------------------------------------------------------------------------------

    There are a total of six (6) function calls available with this library.
1) IX_add        - to add keys to an index file
2) IX_del        - to delete keys from an index file
3) IX_find_first - to find the first key which meets comparison criteria
4) IX_find_last  - to find the last key which meets comparison criteria
5) IX_find_next  - to find the next key
6) IX_find_prev  - to find the previous key

-------------------------------------------------------------------------------

    You must insure that "WI.LIB" is available to the linker at link time.
WI.LIB is to be linked with Microsoft large (-AL) and huge (-AH) memory
models.

    Place WI.LIB in your LIB directory and place INDEX.H in your INCLUDE
directory.

    The maximum char array key length is 127.  All data types other than this
one can use the "data_type" defines (see INDEX.H).  The character array
data type is formed by anding the length and 0x80.

-------------------------------------------------------------------------------

1) Adding a new key to the index file:
   Indexing/Reindexing a file:

    int IX_add (long            file_pos,
                char            *key_addr,
                unsigned char   data_type,
                int             file_handle);

    file_pos      - is the piece of data which will accompany the key.  This
                    information will be returned to you when you use the
                    IX_find_xxxxx function calls.  If you are working with
                    fixed length records this can be a record length.  If you
                    use this field to contain a record number, you will have
                    to do multiplications to get it to a byte position within
                    the file you are indexing.  You may simply use this field
                    to contain the byte position of the record being indexed.
    key_addr      - contains the address of either
                    1) the key data
                    2) a KEY_STRUCT (see INDEX.H) structure containing up to
                       10 key parts.  The order of importance of the key
                       fields is from lowest index to highest (i.e.
                       KEY_COMPONENT.key[0] to KEY_COMPONENT.key[9]).
    data_type     - specifies that the "key_value" above is either key data
                    or a KEY_STRUCT structure (see INDEX.H).  If data_type
                    designates key data, the length (in bytes) is also known.

    RETURNS:    One of the function returns shown in INDEX.H
                    OK          where no errors were detected
                    IX_IO_ERR
                    IX_ERR
                    INV_PARAM
                    INV_NUM_KEYS

    EXAMPLE:    if we have a file with the following record layout which we
                wish to index on the last_name

-------------------------------------------------------------------------------
    /* using the Microsoft "C" Optimizing compiler */
#include <index.h>      /* after placing in include dir */
#include <fcntl.h>
#include <sys\types.h>
#include <sys\stat.h>
#include <io.h>
#include <stdlib.h>
#include <stdio.h>

#define TRUE        1
#define FALSE       0

int nad_file;
int index_file;

int num_bytes;
int err;
long file_pos = 0L;

struct {
    char        first_name [15];
    char        last_name [15];
    char        addr [30];
    char        city [20];
    char        state [2];
    char        zip [9];
} name_and_addr;

main ()
{
    if ((nad_file = open ("nameaddr.fil", O_CREAT | O_BINARY | O_RDWR,
                          S_IREAD | S_IWRITE)) == -1)
    {
       /* do something about the error */
    }
    if ((index_file = open ("nameaddr.inx", O_CREAT | O_BINARY | O_RDWR,
                           S_IREAD | S_IWRITE)) == -1)
    {
      /* do something about the error */
    }
    while (TRUE)
    {
        num_bytes = read (nad_file, (char *)&name_and_addr,
                          sizeof(name_and_addr));
        if (num_bytes == 0)     /* end of file */
            break;
        if (num_bytes != sizeof(name_and_addr))
        {
           /* take care of short read */
        }
        err = IX_add (file_pos, name_and_addr.last_name,
                      sizeof(name_and_addr.last_name)+0x80, index_file);
                   /* 0x80 is simply the high order bit
                      of the data_type.  For all other data
                      types you can use the #define names
                      (see INDEX.H) */
        switch (err)
        {
            case OK:
                printf ("NAME: %15.15s indexed\n",
                        name_and_addr.last_name);
                break;
            case IX_IO_ERR:
                printf ("IO Error on \"nameaddr.inx\" file\n");
                break;
            case IX_ERR:
                printf ("Index File is corrupted\n");
                break;
            case INV_PARAM:
                printf ("Function Call Parameters don't match\n");
                printf (" information already in \"nameaddr.inx\"\n");
                break;
            case INV_NUM_KEYS:
                printf ("The number of key fields does not match\n");
                printf (" information already in \"nameaddr.inx\"\n");
                break;
            default: break;
        }
        if (err)
            break;
        file_pos += sizeof(name_and_addr);
    }
}
-------------------------------------------------------------------------------

2) Deleting an index entry from an index file:

    int IX_del (char            *key_addr,
                long            file_pos,
                unsigned char   data_type,
                int             file_handle);

    key_addr      - contains the address of either
                    1) the key data
                    2) a KEY_STRUCT (see INDEX.H) structure containing up to
                       10 key parts.  The order of importance of the key
                       fields is from lowest index to highest (i.e.
                       KEY_COMPONENT.key[0] to KEY_COMPONENT.key[9]).
    file_pos      - is the piece of data which will accompany the key.  This
                    information will be returned to you when you use the
                    IX_find_xxxxx function calls.  If you are working with
                    fixed length records this can be a record length.  If you
                    use this field to contain a record number, you will have
                    to do multiplications to get it to a byte position within
                    the file you are indexing.  You may simply use this field
                    to contain the byte position of the record being indexed.
                    The file position field is required in the delete to
                    differentiate between duplicate keys and must be the same
                    as used during IX_add.
    data_type     - specifies that the "key_value" above is either key data
                    or a KEY_STRUCT structure (see INDEX.H).  If data_type
                    designates key data, the length (in bytes) is also known.

    RETURNS:    One of the function returns shown in INDEX.H
                    OK          where no errors were detected
                    IX_IO_ERR
                    IX_ERR
                    INV_PARAM
                    INV_NUM_KEYS

    EXAMPLE:    if we have a file with the following record layout which we
                wish to delete all indexes from.  NOTE: we could accomplish
                the same thing, in this case, by deleting the file; except
                here, the file size will not change (i.e. not be clean).

-------------------------------------------------------------------------------
    /* using the Microsoft "C" Optimizing compiler */
#include <index.h>      /* after placing in include dir */
#include <fcntl.h>
#include <sys\types.h>
#include <sys\stat.h>
#include <io.h>
#include <stdlib.h>
#include <stdio.h>

#define TRUE        1
#define FALSE       0

int nad_file;
int index_file;

int num_bytes;
int err;
long file_pos = 0L;

struct {
    char        first_name [15];
    char        last_name [15];
    char        addr [30];
    char        city [20];
    char        state [2];
    char        zip [9];
} name_and_addr;

main ()
{
    if ((nad_file = open ("nameaddr.fil", O_CREAT | O_BINARY | O_RDWR,
                          S_IREAD | S_IWRITE)) == -1)
    {
       /* do something about the error */
    }
    if ((index_file = open ("nameaddr.inx", O_CREAT | O_BINARY | O_RDWR,
                            S_IREAD | S_IWRITE)) == -1)
    {
      /* do something about the error */
    }
    while (TRUE)
    {
        num_bytes = read (nad_file, (char *)&name_and_addr,
                          sizeof(name_and_addr));
        if (num_bytes == 0)     /* end of file */
            break;
        if (num_bytes != sizeof(name_and_addr))
        {
            /* take care of short read */
        }
        err = IX_del (name_and_addr.last_name, file_pos,
                      sizeof(name_and_addr.last_name)+0x80, index_file);
                   /* 0x80 is simply the high order bit
                      of the data_type.  For all other data
                      types you can use the #define names
                      (see INDEX.H) */
        switch (err)
        {
        case OK:
            printf ("NAME: %15.15s index Deleted\n",
                    name_and_addr.last_name);
            break;
        case IX_IO_ERR:
            printf ("IO Error on \"nameaddr.inx\" file\n");
            break;
        case IX_ERR:
            printf ("Index File is corrupted\n");
            break;
        case INV_PARAM:
            printf ("Function Call Parameters don't match\n");
            printf (" information already in \"nameaddr.inx\"\n");
            break;
        case INV_NUM_KEYS:
            printf ("The number of key fields does not match\n");
            printf (" information already in \"nameaddr.inx\"\n");
            break;
        default: break;
        }
        if (err)
            break;
        file_pos += sizeof(name_and_addr);
    }
}
-------------------------------------------------------------------------------

3) Finding indexed keys in an index file:

    int IX_find_first (FIND_IX          *fix,
                       char             *key_addr,
                       int              find_condition,
                       int              file_handle,
                       unsigned char    data_type);

    int IX_find_last  (FIND_IX          *fix,
                       char             *key_addr,
                       int              find_condition,
                       int              file_handle,
                       unsigned char    data_type);

    int IX_next       (FIND_IX          *fix);

    int IX_prev       (FIND_IX          *fix);

    fix           - is the address of the FIND_IX structure
                    typedef struct
                    {
                        long            data_rec;   /* returned file pos */
                        long            recno[3];   /* used internally */
                        int             ix[3];      /* used internally */
                        unsigned char   data_type;  /* used internally */
                        unsigned char   find_type;  /* used internally */
                        VALUE           *val        /* used internally */
                        int             fn;         /* used internally */
                    } FIND_IX;
                    the data_rec field contains the file position of the
                    indexed file, in order to locate the proper record.
    key_addr      - contains the address of either
                    1) the key data
                    2) a KEY_STRUCT (see INDEX.H) structure containing up to
                       10 key parts.  The order of importance of the key
                       fields is from lowest index to highest (i.e.
                       KEY_COMPONENT.key[0] to KEY_COMPONENT.key[9]).
                    You must insure that the value this address points to
                    does not change between IX_find_first/IX_find_last
                    calls and IX_find_next/IX_find_prev calls.
    find_condition- is one of the file conditions listed in INDEX.H
                    1) FIND_EQL
                    2) FIND_GTR
                    3) FIND_LSS
                    4) FIND_NEQ
                    5) FIND_GEQ
                    6) FIND_LEQ
    file_handle   - is the file number of the open file in which the indexes
                    will be found.
    data_type     - specifies that the "key_value" above is either key data
                    or a KEY_STRUCT structure (see INDEX.H).  If data_type
                    designates key data, the length (in bytes) is also known.

    EXAMPLE:    if we have a file with the following record layout which we
                wish find and print all records where the last name is
                greater than or equal to "Marty" - remember that upper and
                lower case are different:

-------------------------------------------------------------------------------
    /* using the Microsoft "C" Optimizing compiler */
#include <index.h>      /* after placing in include dir */
#include <fcntl.h>
#include <sys\types.h>
#include <sys\stat.h>
#include <io.h>
#include <stdlib.h>
#include <stdio.h>

#define TRUE        1
#define FALSE       0

int nad_file;
int index_file;

int num_bytes;
int err;
long file_pos = 0L;
FIND_IX fix;
char *compare_field = "Marty          ";

struct {
    char        first_name [15];
    char        last_name [15];
    char        addr [30];
    char        city [20];
    char        state [2];
    char        zip [9];
} name_and_addr;

main ()
{
    if ((nad_file = open ("nameaddr.fil", O_RDONLY | O_BINARY)) == -1)
    {
       /* do something about the error */
    }
    if ((index_file = open ("nameaddr.inx", O_RDONLY | O_BINARY)) == -1)
    {
       /* do something about the error */
    }

    err = IX_find_first (&fix, compare_field,
                         FIND_GEQ, index_file,
                         sizeof(name_and_addr.last_name)+0x80);
    while (TRUE)
    {
        switch (err)
        {
        case OK:
            lseek (nad_file, fix.data_rec, SEEK_SET);
            num_bytes = read (nad_file, (char *)&name_and_addr,
                              sizeof(name_and_addr));
            if (num_bytes != sizeof(name_and_addr))
            {
                /* take care of short read */
            }
            printf ("NAME: %15.15s %15.15s | CITY/ST: %20.20s %2.2s\n",
                    name_and_addr. first_name,
                    name_and_addr. last_name,
                    name_and_addr. city,
                    name_and_addr. state);
            break;
        case IX_IO_ERR:
            printf ("IO Error on \"nameaddr.inx\" file\n");
            break;
        case IX_ERR:
            printf ("Index File is corrupted\n");
            break;
        case NOT_FOUND:
            printf ("No Matching Keys Found\n");
            break;
        case NO_MORE:
            printf ("No More Matching Keys Found\n");
            break;
        case INV_PARAM:
            printf ("Function Call Parameters don't match\n");
            printf (" information already in \"nameaddr.inx\"\n");
            break;
        case INV_NUM_KEYS:
            printf ("The number of key fields does not match\n");
            printf (" information already in \"nameaddr.inx\"\n");
            break;
        default: break;
        }
        if (err)
            break;
        err = IX_find_next (&fix);
    }
}
-------------------------------------------------------------------------------

4) Data Types:

    #define             "C"
    -------             ---
    ftCHAR              char
    ftUCHAR             unsigned char
    ftSCHAR             signed char
    ftUNS_INT           unsigned int
    ftINT               int
    ftULONG             unsigned long
    ftLONG              long
    ftFLOAT             float
    ftDOUBLE            double
    ftH_BCD_1 - 10      -------         1 to 10 char BCD field with
                                        sign at front of field
    ftT_BCD_1 - 10      -------         1 to 10 char BCD field with
                                        sign at end of field
    ftSTRUCT            -------         multi field key where the
                                        location of the fields is
                                        specified in the KEY_STRUCT
                                        structure (see INDEX.H)
-------------------------------------------------------------------------------

5) KEY_STRUCT structure for multi-field keys:

    typedef struct
    {
        unsigned char       num_keys;
        struct
        {
            unsigned char   data_type;      /* data_type for this field */
            VALUE           *val;           /* addr of this key field */
        } key [10];
    } KEY_STRUCT;

    If we wish to take the following record layout and index it on
last_name and first_name (in that order):

    struct {
        char        first_name [15];
        char        last_name [15];
        char        addr [30];
        char        city [20];
        char        state [2];
        char        zip [9];
    } name_and_addr;

with

    KEY_STRUCT      keys;

the keys would populated as follows:

    keys. num_keys = 2;
    keys. key [0]. data_type = sizeof(name_and_addr.last_name) | 0x80;
    keys. key [0]. val = (VALUE *)name_and_addr.last_name;
    keys. key [1]. data_type = sizeof(name_and_addr.first_name) | 0x80;
    keys. key [1]. val = (VALUE *)name_and_addr.first_name;

the key_addr parameter for the function calls would be "(char *)&keys"
and the data_type parameter to the function calls would be ftSTRUCT.

NOTE: that the maximum number of key fields is 10.  This should be enough
    for any reasonable purpose.  If you require more you can stack the
    keys in some instances (char arrays back to back can be considered
    a single field as long as the cumulative sizes are < 128 characters).
-------------------------------------------------------------------------------






            LICENSE
            -------

    Wilkes INDEX, version 1.0, is being distributed under the "shareware" or
user supported concept.  This software is NOT free software.  The use or
reproduction of this software outside of the limits specified in this license
agreement is prohibited.

    Non-registered users are granted a limited license to use this software
for a period not to exceed thirty days.  During this period they should test
and evaluate the software to determine if it will meet their needs. The use of
this software beyond this limited time period requires registration.
Non-registered users are not allowed to distribute this software without the
express written permission of Wilkes Software inc.  The only exceptions to this
distribution restriction are SYSOPS of electronic bulletin boards and
distributors of public domain and user supported software.  SYSOPS and
software distributors must abide by the copying restrictions specified below.

    Registered users are granted the right to use Wilkes INDEX on only
one computer at any time.  Site licensing agreements are available for
businesses, corporations, and government agencies.  Registered users are also
granted the right to copy and distribute Wilkes INDEX subject to the
following conditions.

    Wilkes INDEX must be copied in its original unmodified form.

    All of the files must be included in the copy.

    Wilkes INDEX may not be distributed in conjunction with any other
    product without the express written consent of Wilkes Software inc.





                WARRANTY
                --------

    Wilkes Software makes no warranty of any kind, express or implied,
including without limitation, any warranties of merchantability and or fitness
for a particular purpose.  Wilkes Software shall not be liable for any
damages, whether direct, indirect, special or consequential arising from a
failure of this software to operate in the manner desired by the user.
Wilkes Software shall not be liable for any damage to data or property which
may be caused directly or indirectly by use of the program.

    IN NO EVENT WILL Wilkes Software BE LIABLE TO YOU FOR ANY DAMAGES,
INCLUDING ANY LOST PROFITS, LOST SAVINGS OR OTHER INCIDENTAL OR CONSEQUENTIAL
DAMAGES ARISING OUT OF YOUR USE OR INABILITY TO USE THE PROGRAM, OR FOR ANY
CLAIM BY ANY OTHER PARTY.






            REGISTRATION FEES
            -----------------

The registration fee for Wilkes INDEX, version 1.0, is only $40.00, with
quantity discount for 10 or more copies: $25.00/copy.

Government and Education registration fee is only $30.00, with quantity
discount for 10 or more copies: $20.00/copy.

You may fill out and return the registration page below or register on-line
at (901)377-5608.

Future updates of the site license copy are provided as follows. The first
update is free.   All others $15.00.

Prices are for a titled master copy and cover all charges including shipping.
Licensees will be informed when updates become available and given the option
to update at will.  There is NO penalty for skipping updates.






    If you should require assistance in the use of the Wilkes INDEX, you
may call the WSI BBS at (901)377-5608.

    If you like this software please let me know.  If you have enhancements
you would like to see in this software, please let me know those also.  If you
have complaints about the way the Wilkes INDEX functions I would even like to
hear those.

    The following is a registration form.  In addition to the licensing use,
I will also use this information to correlate requests for additional
functionality and for Wilkes Software mailing list purpose (only by Wilkes
Software).  When Wilkes Software offers other software into the shareware
system in the future, information will be sent to registered users of the
Wilkes INDEX.  If you register a non-current version I will send the
current version to you.




to: Wilkes Software, inc.
    5231 Longwood Drive
    Memphis, TN  38134


    Name (first) ____________________  (last) ____________________

    Title    ___________________________________

    Company  ___________________________________

    Address  ___________________________________

             ___________________________________

    City     _________________________  State  ___  Zip code _______

    Where software obtained: ________________________________________

    Version of Wilkes INDEX for Microsoft C: 1.0

    System: ____________________

    DOS Version: _____

    Phone: (____) ____ - _____

    If Gov./Ed. please specify: _____________________________________

COST:

    $40/copy; 10+ copies $25/copy
    Gov./Ed. $30/copy; 10+ copies $20/copy

    Tennessee Residents: sales tax is 7.75%

    # copies _________ x your price: ____________ + TN sales tax __________

        = Total _________________

METHOD OF PAYMENT:

    VISA/MASTERCARD/CHECK: __________

    V/MC account #: ___________________________  Expiration Date: _________

    Signature: __________________________________________________