/*
	HEADER:		CUG113;
	TITLE:		1802 Cross-Assembler (BDS C Version);
	FILENAME:	A15.DOC;
	VERSION:	1.2;
	DATE:		07/22/1985;

	DESCRIPTION:	"This program lets you use your CP/M-80-based computer
			to assemble code for the RCA 1802, 1804, 1805, 1805A,
			1806, AND 1806A microprocessors.  The program is
			written in BDS C for the best possible performance on
			8-bit machines.  All assembler features are supported
			except relocation, linkage, listing control, and
			macros.";

	KEYWORDS:	Software Development, Assemblers, Cross-Assemblers,
			RCA, CDP1802, CDP1805A;

	SEE-ALSO:	CUG149, 1805A Cross-Assembler (Portable);

	SYSTEM:		CP/M-80;
	COMPILERS:	BDS C;

	WARNINGS:	"This package is specifically tailored to CP/M-80
			machines and the rather non-standard, but high-
			performance BDS C compiler.  For other environments,
			use the portable version of this package on CUG149.";

	AUTHORS:	William C. Colley III;
*/











	                 1805A/1802 Cross-assembler


                             Version 1.2


         Copyright (c) 1980, 82, 83, 85 William C. Colley III



                      The Manual Such As It Is.


1805A Cross-assembler User Manual                              Page  1


Table of Contents

1.0       Format of Cross-assembler Commands........................ 2

     1.1  Command Strings........................................... 2
     1.2  Options................................................... 2
     1.3  Examples.................................................. 2

2.0       Format of Cross-assembler Source Files.................... 4

     2.1  Statements................................................ 4
     2.2  Symbols................................................... 5
     2.3  Numeric Constants......................................... 5
     2.4  Strings................................................... 6

3.0       Expression Evaluation..................................... 7

4.0       1805A Instructions........................................ 8

     4.1  No Argument Group......................................... 8
     4.2  Register Group............................................ 8
     4.3  8-bit Immediate Group..................................... 8
     4.4  Short Branch Group........................................ 9
     4.5  Long Branch Group......................................... 9
     4.6  Input/Output Group........................................ 9
     4.7  2-Argument Group.......................................... 9

5.0       Pseudo-operations.........................................10

     5.1  BLK.......................................................10
     5.2  BYTE......................................................10
     5.3  Conditional Assembly......................................10
     5.4  CPU.......................................................11
     5.5  END.......................................................11
     5.6  EQU.......................................................12
     5.7  LOAD......................................................12
     5.8  ORG.......................................................12
     5.9  PAGE......................................................13
     5.10 SET.......................................................13
     5.11 TEXT......................................................13
     5.12 WORD......................................................13

6.0  Error Messages.................................................14

7.0  Assembler Abort Conditions.....................................16

8.0  Compiling the Assembler........................................17

9.0  Final Comments.................................................18


1805A Cross-assembler User Manual                              Page  2


1.0  Format of Cross-assembler Commands

1.1  Command Strings

     To run the 1805A cross-assembler, type the following command
line:

          A>a15 filename options

          filename: The name of the source input file is filename.rca,
                    the list can go to filename.prn, and the hex file
                    can go to filename.hex.  If any type is appended
                    to the filename, it is ignored.

          options:  See next section.


1.2  Options

     The source file comes from the currently logged disk drive unless
     it is redirected by putting the string "sd" in the options field.
     "s" specifies the source file and "d" is a device code from the
     following list:

          a, b, c, d     disk drives
          -              the currently logged-in disk drive

     Lines of input containing errors will always be output to the
     console device.  If the full listing is desired, it must be
     called for by putting the string "ld" in the options field.  "l"
     specifies the list file and "d" is a device code as per the
     source file or one of the following:

          x              console device
          y              list device

     The hex file will not be output unless called for with the string
     "hd" with device codes as per the list file.

     Options must be run together into a single string with no
     embedded blanks.


1.3  Examples

     A>a15 barf               source -- a:barf.rca
                              list   -- none
                              hex    -- none

     A>a15 barf sblxha        source -- b:barf.rca
                              list   -- con:
                              hex    -- a:barf.hex


1805A Cross-assembler User Manual                              Page  3


     A>a15 barf ly            source -- a:barf.rca
                              list   -- lst:
                              hex    -- none

     A>b:a15 barf sbh-        source -- b:barf.rca
                              list   -- none
                              hex    -- a:barf.hex

     B>a:a15 barf h-          source -- b:barf.rca
                              list   -- none
                              hex    -- b:barf.rca


1805A Cross-assembler User Manual                              Page  4


2.0  Format of Cross-assembler Source Files

     Lines of source input are terminated with CR/LF pairs.
     Internally, the character before the LF is discarded, so if the
     CR is missing, the last character of the line will be eaten up.
     The internal line buffer will hold a 120-character line.  This
     may be changed by altering the "#define LINLEN 120" statement in
     a15.h and recompiling the cross-assembler.  Excess characters in
     the line are thrown out.

     Lower case letters are converted to upper case in as few places
     as possible.  They are:

          1)  In opcodes,

          2)  In checking for keywords such as NOT, and

          3)  In command strings.

     This means that "not", "NOT", "Not", etc. are all possible
     spellings of the logical inversion operator.  This also means
     that "foo" and "FOO" are different symbols.  Watch this if you
     start encountering U errors of symbols that you "know" you
     defined.


2.1  Statements

     Source files input to the cross-assembler consist of statements
     of the form:

          [label]   [opcode   [arguments]]   [;comments]

     Labels are recognized by their beginning in column 1.  If it
     doesn't begin there, it is assumed to be an opcode.  Labels are
     assigned the current program counter value unless the line's
     opcode is "EQU" or "SET".

     Opcodes may be either 1805A machine instruction mnemonics or
     pseudo-ops (i.e. assembler directives).

     The arguments following the opcode will vary with the opcode. In
     the case of opcodes such as "NOP", they may be absent entirely.

     Lines terminate with either a CR/LF pair or a semicolon that is
     not embedded in a quoted string.  Anything after a semicolon is
     ignored by the assembler, but will appear in the listing.  Note
     that a semicolon in column 1 will make the entire line a comment.


1805A Cross-assembler User Manual                              Page  5


2.2  Symbols

     Symbols may be of any length, but only the first 8 characters are
     significant.  This may be changed by changing the "#define SYMLEN
     8" statement in a15.h and recompiling the assembler.  Note that
     this increases the storage required by the symbol table as each
     entry in the symbol table sits on SYMLEN+2 bytes of storage.  The
     following characters are legal in a symbol:

          A-Z  a-z  !    #    $    %    &    .    :    ?    @    [
                    \    ]    ^    _    `    {    |    }

     Note that symbols may not begin with 0-9 as this would make it
     impossible to tell numbers from symbols.

     A special symbol $ is always equal to the address of the first
     byte of code generated by a given line.


2.3  Numeric Constants

     The default base for numeric constants is decimal.  Putting a
     trailing H, D, Q, O, or B onto the number will override the
     default base.  The base designators may be in either lower or
     upper case and are as follows:

          H    Hexidecimal    (Note that for A-F, lower case is
                              converted to upper case.)
          D    Decimal

          O Q  Octal          (Either O or Q will do.)

          B    Binary

     Numbers are 16-bit unsigned quantities.  Overflows from the upper
     byte are ignored with no error flagged.  For example:

          0fedcbh        evaluates to edcb hex
          000111000b     evaluates to 0039 hex
          035Q           evaluates to 001d hex
          128            evaluates to 0080 hex
          1feh           evaluates to 01fe hex

     Numbers are recognized by their first character of 0-9, so make
     sure that hex numbers have a zero padded onto the front if
     needed.

     A character constant is a string composed of zero, one, or two
     ASCII characters delimited by either single or double quotes (''
     or "").  Note that single quotes only balance single quotes and


1805A Cross-assembler User Manual                              Page  6


     double quotes only balance double quotes.  Thus, a character
     constant of 22 hex can be specified by '"'.  For example:

          "ab"           evaluates to 6162 hex
          ""             evaluates to 0000 hex
          "'"            evaluates to 0022 hex
          'A'            evaluates to 0041 hex

     Note that in the two-byte character constant, the left-hand
     character will appear in the upper-order byte and the right-hand
     character will appear in the lower-order byte.


2.4  Strings

     Strings are formed in the same way as character constants except
     that they may be of any length up to and including 255
     characters.  The first character will be placed in the
     lowest-order memory byte.  A line-feed character may not be
     embedded in a string as it will yield a quote imbalance error.
     Note that strings are only valid in the argument field of a
     "TEXT" pseudo-op.


1805A Cross-assembler User Manual                              Page  7


3.0  Expression Evaluation

     The following operators are allowed in expressions.  The
     operators are listed in order of precedence.

          Unary +   Unary -

          *    /    MOD  SHL  SHR

          +    -

          >    >=   <    <=   <>   =    (These can also be written as
                                        GT, GE, LT, LE, NE, and EQ.)

          NOT                           (1's complement)

          AND

          OR   XOR

          LOW  HIGH

     Parentheses are used to change the order of precedence.  During
     evaluation of an expression, as soon as a new operator is
     encountered that has precedence less than or equal to the last
     operator encountered, all operations up to the new operator are
     performed.  That is, subexpressions involving operators of higher
     precedence are computed first.

     All operators except +, -, *, /, =, <>, >=, <=, >, and < must be
     separated from their operands by at least one space or tab.

     The operation "HIGH mumble" is equivalent to "mumble SHR 8" and
     the operation "LOW mumble" is equivalent to "mumble AND 0ffh".

     The relational operators (GE, EQ, etc.) evaluate to 0ffffh if the
     relationship is true, 0 if it is false.

     Expressions are terminated by commas, semicolons, or CR/LF pairs.


1805A Cross-assembler User Manual                              Page  8


4.0  1805A Instructions

     The instructions of the 1805A microprocessor fall into several
     catagories.  Most require one or more arguments, though some
     permit none.  Blanks may be used freely throughout the argument
     field (except within symbols or operators such as NOT and <=) to
     enhance the readability of the source code.  The basic syntax is
     as follows:

          [label]   SEX       expression          ;comments.


4.1  No Argument Group

     This group contains the following opcodes:

          ADC       ADD       AND       CID       CIE       DADC
          DADD      DIS       DSM       DSMB      DTC       ETQ
          GEC       IDL       IRX       LDC       LDX       LSDF
          LSIE      LSKP      LSNF      LSNQ      LSNZ      LSQ
          LSZ       MARK      NOP       OR        REQ       RET
          RSHL      RSHR      SAV       SCM1      SCM2      SD
          SDB       SEQ       SHL       SHLC      SHR       SHRC
          SKP       SM        SMB       SPM1      SPM2      STM
          STPC      STXD      XID       XIE       XOR

     These opcodes permit no arguments.


4.2  Register Group

     This group contains the following opcodes:

          DEC       GHI       GLO       INC       LDA       LDN
          PHI       PLO       RLXA      RNX       RSXD      SEP
          SEX       SRET      STR

     This group requires one argument in the range 0-15.  The labels
     R0, R1, ..., R9, RA, RB, ..., RF are predefined by the assembler
     for specifying registers in these instructions.  If the argument
     is out of range, a register (R) error is flagged.

     Note that a LDN R0 instruction will draw a register (R) error as
     its opcode is used for the IDL instruction.


4.3  8-bit Immediate Group

     This group contains the following opcodes:

          ADCI      ADDI      ANI       DACI      DADI      DSBI
          DSMI      LDI       ORI       SDBI      SDI       SMBI
          SMI       XRI


1805A Cross-assembler User Manual                              Page  9


     This group requires one argument between -128 and 255.  If the
     argument is out of range, a value (V) error is flagged.


4.4  Short Branch Group

     This group contains the following opcodes:

          B1        B2        B3        B4        BCI       BDF
          BGE       BL        BM        BN1       BN2       BN3
          BN4       BNF       BNQ       BNZ       BPZ       BQ
          BR        BZ        BXI       NBR

     This group requires one argument whose high-order byte is equal
     to the high-order byte of $+1 ($+2 for BCI and BXI).  If the
     high-order bytes do not match, a branch (B) error is flagged.


4.5  Long Branch Group

     This group contains the following opcodes:

          LBDF      LBNF      LBNQ      LBNZ      LBQ       LBR
          LBZ       NLBR

     This group requires one argument having any value.


4.6  Input/Output Group

     This group contains the following opcodes:

          INP       OUT

     This group requires one argument in the range 1-7.  If the
     argument is out of range, a value (V) error is flagged.


4.7  2-Argument Group

     This group contains the following opcodes:

          DBNZ      RLDI      SCAL

     This group requires two arguments. The first argument is in the
     range 0-15 as per the register group.  The second argument can
     have any value.


1805A Cross-assembler User Manual                              Page 10


5.0  Pseudo-operations

5.1  BLK

     This statement is used to reserve a block of memory for working
     storage, etc.  It requires one argument that gives the number of
     bytes of storage to reserve.  The syntax is as follows:

          [label]   BLK       expression


5.2  BYTE

     This statement is used to place bytes in memory.  Each byte is
     defined by an expression.  Multiple bytes can be defined by
     expressions separated by commas.  If an expression evaluates to a
     quantity outside the range -128 to 255, a value (V) error is
     flagged.  The syntax follows:

          [label]   BYTE      [expr[,expr[,...]]]


5.3  Conditional Assembly

     Blocks of code can be assembled or not assembled based on the
     value of some expression.  The basic syntax is as follows:

                    IF        expression

                    (lines of code)

                    ENDI

     If the expression evaluates to 0, the code will not be assembled.
     The source lines will be transferred to the listing, but no hex
     output will be generated.  It is recommended that a value of
     0ffffh be used for a true value since it turns into a false value
     under bitwise inversion.

     In addition, the ELSE directive is supported as follows:

                    IF        expression

                    (lines of code)

                    ELSE

                    (more lines of code)

                    ENDI


1805A Cross-assembler User Manual                              Page 11


     This is equivalent to:

                    IF        expression

                    (lines of code)

                    ENDI
                    IF        NOT expression

                    (more lines of code)

                    ENDI

     Note that labels are not permitted on conditional assembly
     directives.  Also, note that an END statement can fail to be
     recognized if it is in a conditional assembly block with a false
     expression.

     A phasing (P) error will be flagged if there are any forward
     references in the expression.


5.4  CPU

     This statement is used to tell the assembler whether to assemble
     code for the 1802 CPU or for the 1805A CPU.  The syntax is as
     follows:

          [label]   CPU       expression

     If the expression evaluates to 1802 (decimal), the 1805A
     extensions to the 1802 instruction set are disallowed.  If the
     expression evaluates to 1805 (decimal), the 1805A extensions are
     allowed.  Any other value results in a value (V) error and the
     statement has no effect.  The default condition is "CPU 1802",
     though the default can be changed by changing the "#define DEFEXT
     FALSE" statement in a15.h and recompiling the assembler.


5.5  END

     When this statement is encountered, the assembler decides that
     the end of the source file has been reached.  If this statement
     is missing or in a conditional assembly block that is not being
     assembled, the assembler will encounter end-of-file on the source
     file.  In this case, the assembler will attach an END statement
     and will flag a * error.  The syntax is as follows:

          [label]   END


1805A Cross-assembler User Manual                              Page 12


     If any IF statement is not closed with an ENDI at this point, an
     if (I) error will be flagged.

     This statement permits no arguments.


5.6  EQU

     This statement is used to assign a permanent value to a symbol.
     This value may not be subsequently changed by a SET, another EQU,
     or by writing the symbol in column 1 as a label.  The syntax is
     as follows:

          label     EQU       expression

     A phasing (P) error will result if any forward references are
     encountered in the evaluation of the expression.


5.7  LOAD

     This statement is used to load a 16-bit immediate value into a
     register of the 1802 which has no RLDI instruction.  It is, in
     effect, a built-in macro.  The syntax is as follows:

          [label]   LOAD      reg, data

     The following sequence of instructions is placed into the code:

          [label]   LDI       HIGH data
                    PHI       reg
                    LDI       LOW data
                    PLO       reg

     Note that execution of this macro blows up the D register.


5.8  ORG

     This statement is used to load a value into the assembly program
     counter.  The value is obtained from the expression.  If the
     expression contains any forward references, a phasing (P) error
     will result.  If a label is present, it will be EQUed to the new
     program counter value.  The syntax is:

          [label]   ORG       expression


1805A Cross-assembler User Manual                              Page 13


5.9  PAGE

     This statement is used to set the assembly program counter to the
     beginning of the next 256-byte page.  If the program counter is
     already at the beginning of a page, the statement has no effect.
     It permits no arguments, and it handles a label in the same way
     as an ORG statement does.  The syntax is as follows:

          [label]   PAGE


5.10 SET

     This statement is used to assign a temporary value to a symbol.
     The symbol may not be redefined by an EQU or by writing it in
     column 1 as a label, but it may be redefined by another SET
     statement.  The value for the symbol is obtained from the
     expression.  If it contains forward references, a phasing (P)
     error will result.  The syntax is:

          label     SET       expression


5.11 TEXT

     This statement is used to place strings in memory.  Its
     arguments may only be strings.  Multiple strings may be placed
     in memory if the strings are separated by commas.  The syntax is
     as follows:

          [label]   TEXT      [string[,string[,...]]]


5.12 WORD

     This statement is used to place words in memory.  Each word is
     defined by an expression.  Multiple words may be defined by
     expressions separated by commas.  Words are placed in memory with
     the high-order byte in the low-order memory location and the
     low-order byte in the high-order memory location.  The syntax is
     as follows:

          [label]   WORD      [expr[,expr[,...]]]


1805A Cross-assembler User Manual                              Page 14


6.0  Error Messages

     Error messages are flagged with a single letter in column 1 of
     the offending line in the listing.  The meaning of each letter
     follows:

          B    Short branch was not to a location on the current page.
               Note that the branch must go to the same page as $+1
               ($+2 for BCI and BXI) is on.  Thus short branch
               instructions at location 0xxffh (and 0xxfeh for BCI and
               BXI) act strangely.  Don't ask me, I didn't invent the
               instruction set!

          D    Digit too large for the base encountered.  In
               particular, watch for 8 or 9 in an octal number and a-f
               in a decimal number.

          E    Expression ill-formed.

          I    If stack imbalance.  Look for ELSE or ENDI without an
               IF or an IF still open at the end of the file.

          L    Invalid label.  Label may contain invalid characters or
               be equal to a reserved word like NOT.  Label may be
               present on a conditional assembly directive.

          M    Label multiply defined.  Label defined more than once
               and all definitions are not SET statements.

          O    Invalid opcode.  Look for misspellings, missing
               semicolons, or opcodes in column 1.

          P    Phasing error.  Look for expressions in ORG, EQU, SET
               or IF directives that contain forward references.  If
               none exist, something weird is going on as a label that
               was defined in pass 1 mysteriously vanished in pass 2.

          R    Register specification argument out of range (0-15) or
               LDN R0 instruction.

          S    Syntax error.  Check your syntax against my samples.

          T    Too many arguments on this line.  WORD directives may
               only define 127 words, while TEXT and BYTE directives
               may only define 255 bytes.  On other statements, you
               put superfluous arguments on the line.

          U    Undefined symbol encountered during expression
               evaluation.


1805A Cross-assembler User Manual                              Page 15


          V    Value out of range.  In particular, BYTE expressions
               and 8-bit immediate values must evaluate to -128 to
               255, I/O port numbers must evaluate to 1 to 7, and CPU
               types must evaluate to 1802 or 1805.

          *    This statement generated by the assembler.  Right now,
               this only happens if you drop an END statement or
               remove it through conditional assembly.

          "    Quote imbalance error.  Bear in mind that ' will not
               terminate a string started with " and vice-versa.

          (    Parenthesis imbalance error.  Count them!


1805A Cross-assembler User Manual                              Page 16


7.0  Assembler Abort Conditions

     Under certain circumstances, this assembler will just give up and
     quit in middle of an assembly.  If you don't get the error count
     diagnostic on the console, read your screen for sure!  The
     following messages occur:

          1)   Can't open source.

               The source file does not exist on the specified disk
               drive.

          2)   Can't open list.
               Can't open hex.

               No directory entries left on the disk drive in
               question.

          3)   Illegal command line.
               No file info supplied

               Bone up on command lines.

          4)   If stack overflow.

               IF directives may only be nested 16 deep.  Rebuild your
               source code to reduce your nesting depth, or change the
               "#define IFDEPTH 16" statement in a15.h and recompile
               the assembler.

          5)   Disk write error.

               Out of disk or directory space on the list or hex file.

          6)   Error closing file.

               You shouldn't get this one.

          7)   Symbol Table Overflow.

               Your source program defines too many symbols.  The
               current limit is 500.  If you have more memory than I
               do, you can change the "#define SYMBOLS 500" line in
               a15.h and recompile the assembler.  Otherwise, you must
               work on your source code.


1805A Cross-assembler User Manual                              Page 17


8.0  Compiling the Assembler

     To compile the assembler as it stands, you will need the
     following software tools:

          1)   40K+ of RAM

          2)   BDS C Compiler Version 1.4x with its CMAC.LIB macro
               library or Version 1.5x with its CASM utility.

          3)   Digital Research's MAC Macro-assembler and the CP/M
               LOAD utility (for BDS C 1.4x) or the CP/M ASM and DDT
               utilities (for BDS C 1.5x).

     To get a15tbl1.crl and a15tbl2.crl up from scratch, you do the
     following.  I assume that everything lives on drive A.

               BDS C 1.4x                         BDS C 1.5x

          A>mac a15tbl1 $szpz                A>cmac a15tbl1
          A>mac a15tbl2 $szpz                A>cmac a15tbl2
          A>load a15tbl1                     A>asm a15tbl1.aaz
          A>load a15tbl2                     A>asm a15tbl2.aaz
          A>ren a15tbl1.crl=a15tbl1.com      A>ddt a15tbl1.hex
          A>ren a15tbl2.crl=a15tbl2.com      -g0
                                             A>save 6 a15tbl1.crl
                                             A>ddt a15tbl2.hex
                                             -g0
                                             A>save 4 a15tbl2.crl

     You should now have a15tbl1.crl and a15tbl2.crl on drive A. Erase
     the artifacts a15tbl1.hex and a15tbl2.hex (also a15tbl1.asm and
     a15tbl2.asm if you're using BDS C 1.5x) if you want to.

     Now you are ready to compile the rest of the beast like this:

          A>cc a15.c -e4600
          A>cc a15asmln -e4600
          A>cc a15eval -e4600
          A>cc a15get -e4600
          A>cc a15put -e4600
          A>cc a15symb -e4600

     Now you can link it all together like this (all on one line):

          A>clink a15 a15asmln a15eval a15get a15put
                    a15symb a15tbl1 a15tbl2

     And, as if by magic, you've got a15.com on drive A.  Note that if
     you have more than 40K of RAM, you may want to increase your
     symbol table size.  Symbols are 10 bytes each, so plan
     accordingly.


1805A Cross-assembler User Manual                              Page 18


9.0  Final Comments

     Happy hacking!  If you have questions or note any bugs, I'd
     appreciate a shout at (216)288-1122 x469 days or at (216)775-3680
     evenings.  The questions will point out weaknesses in the manual,
     and the bugs need to be stamped upon unmercifully.

                                                  WCC3
                                              20-JUN-1985
 A>cc a15asmln -e4