#if 0Luminance.docThis file documents Luminance.c.HISTORY:3/11/92 dgp added prototypes to supplement the explanations of the routines.3/24/94	dgp added LToE, LToEOrdered, and EToL.10/17/94 dgp updated, in response to queries by Lan Zhang.INTRODUCTION:The purpose of these subroutines is accurate control of contrast of visual stimuli for vision experiments. These subroutines set up the Color Lookup Table (CLUT) of a video framestore on the Mac II (e.g. the Apple Mac II Color Video Card) to properly drive a monochrome monitor (e.g. the Apple High Resolution Monochrome Monitor) via an Institute for Sensory Research (ISR) Video Attenuator. The ISR Video Attenuator consists of resistive dividers which attenuate the three color signal from the video framestore by different amounts and combine them to produce one monochrome signal.The video attenuator and the theory behind the algorithms described here arethe topic of a paper:D.G. Pelli and L. Zhang (1991) Accurate control of contrast on microcomputer displays. Vision Research, 31:1337-1360.Achieving the goal of accurate control of contrast required solving five problems:1. The luminance of the monitor is nonlinearly related to the input voltagewhich depends linearly on the triplet loaded into the CLUT. This is solved byallowing the user to provide a polynomial (I recommend 4th order) describing thenonlinear relationship between luminance and nominal voltage. (For computationalreasons, you must also supply a quadratic fit.) The subroutines LToV and VToLuse this polynomial to convert back and forth.2. Affordable framestores for microcomputers have 8 bit Digital to AnalogConverters (DACs), which can only represent 256 different luminances. This isnot enough precision to produce threshold-contrast patterns, which are importantfor vision experiments. This is solved by the ISR Video Attenuator whichcombines the outputs of the three DACs ("red", "green", and "blue") with variousattenuations to yield one monochrome signal which can represent low contrasts(by varying an attenuated DAC) and high contrasts (by varying an unattenuatedDAC).3. DACs are only accurate to ± a least significant bit (LSB). The Brooktree DACsused by Apple and RasterOps are specified to have a ±1 LSB "integratedlinearity" error, which means that the voltage produced by any number willdeviate from a line connecting the 0 and 255 points by at most 1 LSB, which isdefined as 1/255 times the voltage difference between 0 and 255. I assume aslightly stronger restriction will hold, that the difference between any twosettings will be in error by at most one LSB. So it is important to allow theuser to specify what range of luminances will be used to present a particularstimulus and to fix the coarsest DACs (i.e. those with the least attenuation inthe ISR Video Attenuator) and only vary the fine DACs to produce the specifiedluminances. The range setting is done by SetLuminanceRange() which is calledautomatically by SetLuminance() and SetLuminances().4. Apple's software environment for graphics, QuickDraw, isn't designed forvision experiments. The facilities for creating images are fine, but the controlof the CLUTs provided by the Palette and Color Managers is unsatisfactory forvision research because a lot happens behind your back. In particular thePalette Manager likes to maintain a consistent color environment across theentire desktop, which includes all your screens. Well, in vision experiments wegenerally want to treat each screen as a totally separate device, unaffected bywhat we do to the other screens. This is solved by the routine GDSetEntries()which makes a low-level call to the video driver to change the CLUT directlywithout QuickDraw's knowledge. (This will work with any video card that workswith the Mac II.) The routine LoadLuminances(), which is used below, is just aconvenient glue routine for calling GDSetEntries().5. Apple specifies that the video driver should silently implement gammacorrection to attempt to correct for the display's nonlinear relation betweenluminance and input voltage. We don't want this because this hidden gammacorrection loses precision and interferes with the operation of the ISR VideoAttenuator, which will seem to operate NONlinearly if this gamma correctiontakes place unbeknownst to us. This is solved by the routine GDLinearGamma()which makes a low-level call to the video driver and loads a linear gamma table,i.e. no correction.SUMMARY:double EToL(LuminanceRecord *LP,int entry);Returns the luminance associated with the particular entry.int LToE(LuminanceRecord *LP,double L,int firstEntry,int lastEntry);Returns the index of the table entry in specified range with luminance closest to L.int LtoEOrdered(LuminanceRecord *LP,double L,int firstEntry,int lastEntry);Returns the index of the table entry in specified range with luminance closest to L.Runs fast by assuming an ordered table from firstEntry to lastEntry, either increasing or decreasing.double SetLuminance(GDHandle device,LuminanceRecord *LP	,int entry,double luminance	,double lowLuminance,double highLuminance)Set one entry in the ColorSpec table (and the CLUT if device is not NULL) toa specified luminance. It's ok for lowLuminance to be greater than highLuminance.SetLuminance() sets a single entry to the specified luminance. You must alsoindicate the luminance range that you are working over, to allow optimal choiceof which dacs to fix, etc., to yield minimum error in relative luminance. SetLuminances() does its work by making a call to SetLuminance() for each entry.SetLuminance takes 1 ms to set up the range (by calling SetLuminanceRange), whichit only has to do once. Repeated calls to SetLuminance with the same range willnot cause re-computation of the range. Once the range is set, SetLuminance takesabout 0.1 ms. If SetLuminance is too slow for a real-time application you can tellit to just compute, but not load the new ColorSpec table (just supply NULL in placeof device), and you can then quickly load your ColorSpec table into the CLUTlater by calling LoadLuminances().double SetLuminancesAndRange(GDHandle device,LuminanceRecord *LP	,int firstEntry,int lastEntry	,double firstLuminance,double lastLuminance	,double lowLuminance,double highLuminance)/*Set a series of entries in the ColorSpec table (and the CLUT if device is not NULL)to a linear sequence of luminances. Uses last two arguments to set the luminance range of interest.*/double SetLuminances(GDHandle device,LuminanceRecord *LP	,int firstEntry,int lastEntry	,double firstLuminance,double lastLuminance)/*Set a series of entries in the ColorSpec table (and the CLUT if device is not NULL)to a linear sequence of luminances. Assume this is the entire luminance range of interest.*/SetLuminances() and SetLuminancesAndRange() both produce a linear relationshipbetween CLUT entry and luminance over the range firstLuminance to lastLuminance,with minimum error relative to any luminance in the range lowLuminance tohighLuminance. (We don't care about a small error in mean luminance.)(SetLuminances, which doesn't have these arguments, uses firstLuminance andlastLuminance to set this range.) The three DACs are linear, and the videoattenuator will combine them linearly yielding a voltage V at the display input.This allows you to compute your image (e.g. a sinewave grating) and loaded tothe frame store as a full scale linear function, i.e. with values ranging0..255.  Linearization of the display and setting of contrast to whatever youwant are both accomplished by one call to SetLuminances(). The contrast can bechanged by calling SetLuminances() again, now with a larger or smaller luminancerange. If SetLuminances is too slow for a real-time application (itscomputations take about 8-30 ms to compute a whole 256-entry CLUT) you can tellit to just compute, but not load the new ColorSpec table (just supply NULL inplace of device), and you can then quickly load your ColorSpec table intothe CLUT later by calling LoadLuminances().double GetLuminance(GDHandle device,LuminanceRecord *LP,int entry)/*If device is not NULL then examines one entry in the actual CLUT, otherwiseexamines the ColorSpec table contained in *LP, and in either case returns theluminance that will be produced. Supplying an illegal entry value results in areturned value of -INF.*/GetLuminance() returns the luminance of a single entry. If device is not NULL thenGetLuminance will make a low-level call to the video driver to determine what is in thatCLUT entry in the actual hardware, and will return the luminance that is expectedto result given the channel gains and luminance nonlinearity described in yourLuminanceRecord. If device is NULL then GetLuminancereturns the luminance corresponding to the entry in the ColorSpec table in yourLuminanceRecord.void IncrementLuminance(GDHandle device,LuminanceRecord *LP,int entry)/*Make smallest possible increase of the luminance of one entry in the ColorSpec table.This is a way to figure out what is the lowest contrast that you can produce.*/void LoadLuminances(GDHandle device, LuminanceRecord *LP,	int firstEntry, int lastEntry)/*This just calls GDSetEntries() to load your ColorSpec table into the CLUT ofyour screen device. It is here simply to provide a cosmetic match to thecall to SetLuminances(), for which loading the CLUT is optional.Note: if you prefer, instead of LP you may send just the address of a ColorSpec table, cast to (LuminanceRecord *), since a LuminanceRecord begins with a ColorSpec table.Does nothing if device==NULL or the device has no driver.*/double GetV(GDHandle device,LuminanceRecord *LP,int entry);double VToL(LuminanceRecord *LP,double V);double LToV(LuminanceRecord *LP,double L);double LToL(LuminanceRecord *LP,double L);Most users will never have any reason to use these routines. They are usefulprimarily in error analysis of the Luminance.c package.EXAMPLES:double tolerance,luminance,meanLuminance,c;int firstEntry,lastEntry,entry;/* load CLUT with linear luminance range, immediately */tolerance=SetLuminances(device,&LR,0,255,(1.-c)*meanLuminance,(1+c)*meanLuminance);/* load ColorSpec table with linear luminance range, then load CLUT */tolerance=SetLuminances(NULL,&LR,0,255,(1.-c)*meanLuminance,(1+c)*meanLuminance);LoadLuminances(device,&LR,firstEntry,lastEntry);/* load ColorSpec table with sinusoidal luminance range, then load CLUT */for(entry=0;entry<256;entry++) {	luminance = meanLuminance*(1.0+c*sin(2.0*3.14159265*entry/256.));	tolerance=SetLuminance(NULL,&LR,entry,luminance,(1.-c)*meanLuminance,(1+c)*meanLuminance);}LoadLuminances(device,&LR,firstEntry,lastEntry);/* Examine an entry in the ColorSpec table or CLUT */luminance=GetLuminance(device,&LR,entry);	/* in CLUT */luminance=GetLuminance(NULL,&LR,entry);		/* in ColorSpec table */NOTES:The argument firstEntry must not exceed lastEntry. They may be equal.The returned value, tolerance, is an estimate of the largest possible error inthe luminance DIFFERENCES, taking into account the precision, accuracy (assumedto be ±1 least significant bit), and range of the DACs. (Note the returnedtolerance tells you about errors in the luminance DIFFERENCES on the display.The error in ABSOLUTE luminance of the display is expected to be at most ±1 stepof all the DACs, i.e. one part in 255 of full scale.)There are no restrictions at all on firstLuminance and lastLuminance. It isreasonable to request an impossibly large luminance range, e.g. from a negativeluminance up to twice the maximum luminance. SetLuminances will produce theclosest possible approximation. The luminance of each entry will be clipped tofit in the range of possible luminances. Thus you will obtain the requestedcontrast for pixel values that aren't clipped. You can detect the clipping bythe fact that the returned tolerance will be very large.A common mistake in C programming is to use a pointer that supposedly points toa structure, without ever allocating said structure. Consider theLuminanceRecord. The following declaration and call will be accepted by thecompiler, but will usually have disastrous consequences:	LuminanceRecord *LP;	SetLuminances(...,LP,...);		/* Bad! */The problem is that you never allocated a LuminanceRecord, only a pointer. WhenSetLuminances starts storing information in what it thinks is a LuminanceRecord itwill actually be writing over a random part of memory. What you should do is:	LuminanceRecord LR;	SetLuminances(...,&LR,...);		/* Good */Or you can do this:	LuminanceRecord LR,*LP;	LP=&LR;	SetLuminances(...,LP,...);		/* Good */This second technique is a better habit, since if you want to put some of your code intoa subroutine, you'll be passing the pointer, not the structure itself, so you might as wellget used to using the pointer.Before using SetLuminance or SetLuminances you must initialize your LuminanceRecord. You should do that by reading in,	LuminanceRecord LR;	ReadLuminanceRecord("LuminanceRecord2.h",&LR,0);or #including a file with all the parameters describing your monitor. 	LuminanceRecord LR;	#include "LuminanceRecord2.h"Here's an example of the contents of a LuminanceRecord1.h file, as produced by theprogram CalibrateLuminance. You must use CalibrateLuminance to calibrateyour own framestore, ISR Video Attenuator, and display. 	LR.screen=1;	/* device=GetScreenDevice(LR.screen); */	/* Caution: the screen number used here and in GetScreen Device is NOT the same as */	/* displayed by the Monitors cdev in the Control Panel. Sorry. The most obvious difference */	/* is that GetScreenDevice always assigns 0 to the main screen, the one with the menu bar. */	LR.date="3:09 PM Friday, October 16, 1992";	LR.id="5111767";	LR.name="signal";	LR.notes="manoj, lights off, photometer 1 inch from screen";	LR.dpi=76.0;	/* pixels per inch */	LR.Hz=66.67;	/* frames per second */	LR.units="cd/m^2";	/* coefficients of polynomial fit */	LR.coefficients=9;	/* # of coefficients in polynomial fit */	/* L(V)=p[0]+p[1]*V+p[2]*V*V+ . . . ±polynomialError */	LR.p[0]=1.28201e-14;	LR.p[1]=8.25776e-13;	LR.p[2]=5.00064e-11;	LR.p[3]=2.51138e-09;	LR.p[4]=7.98055e-08;	LR.p[5]=-2.04184e-09;	LR.p[6]=1.79181e-11;	LR.p[7]=-6.3791e-14;	LR.p[8]=8.10888e-17;	LR.polynomialError=  0.2263;	/* RMS error of fit */	/* coefficients of quadratic fit */	/* L(V)=q[0]+q[1]*V+q[2]*V*V±quadraticError */	LR.q[0]=4.86285;	LR.q[1]=-0.201266;	LR.q[2]=0.00125998;	LR.quadraticError=  2.5493;	/* RMS error of fit */	/* coefficients of power law fit */	/* L(V)=power[0]+Rectify(power[1]+power[2]*V)^power[3]±powerError */	/* where Rectify(x)=x if x³0, and Rectify(x)=0 otherwise */	/* Pelli & Zhang (1991) Eqs.9&10 use symbols v=V/255, alpha=power[0], beta=power[1], kappa=power[2]*255, gamma=power[3] */	LR.power[0]=-0.0615421;	LR.power[1]=-3.38554;	LR.power[2]=0.0305017;	LR.power[3]=2.48866;	LR.powerError=  0.2616;	/* RMS error of fit */	/* coefficients of power law fit, with fixed exponent */	/* L(V)=fixedPower[0]+Rectify(fixedPower[1]+fixedPower[2]*V)^fixedPower[3]±fixedPowerError */	LR.fixedPower[0]=-0.764058;	LR.fixedPower[1]=-2.96785;	LR.fixedPower[2]=0.0310164;	LR.fixedPower[3]=  2.28;	LR.fixedPowerError=  1.1986;	/* RMS error of fit */	LR.r=0.0282406;	LR.g=0.149883;	LR.b=0.821877;	LR.gainAccuracy=-0.0337905;	LR.gm=3.85543;	/* The monitor's contrast gain. */	LR.VMin=  0;	/* minimum value that can be loaded into DAC */	LR.VMax=255;	/* maximum value that can be loaded into DAC */	LR.LMin=   -0.06;	/* luminance at VMin */	LR.LMax=   39.70;	/* luminance at VMax */	LR.LBackground=   9.731;	/* background luminance during calibration */	LR.VBackground=193;	/* background number used during calibration */	LR.rangeSet=0;	/* indicate that range parameters have yet to be set */	LR.L.exists=0;	/* indicate that luminance table has yet to be initialized */Note that these parameters describe fits of three functions to the gamma function.You may omit any or all of these fits, but should document it by setting thecorresponding error terms to infinity (=1.0/0.0). If you omit all of them thenyou must supply a table describing the gamma function, e.g.	LR.L._VMin=DoubleToFix(0.);	/* if possible, restrict to just the monotonic range */	LR.L._VMax=DoubleToFix(255.);	/* if possible, restrict to just the monotonic range */	LR.L._dV=(LR.L._VMax-LR.L._VMin)/(LUMINANCES_IN_TABLE-1);	LR.L.latestIndex=-1;			/* invalid latestIndex, so hunt will start from scratch */	LR.L.exists=luminanceSet;		/* mark table as valid */	LR.L._Lu[0]=DoubleToFix(0.57);	LR.L._Lu[1]=DoubleToFix(0.57);	...	LR.L._Lu[LUMINANCES_IN_TABLE-1]=DoubleToFix(101.13);"LUMINANCES_IN_TABLE" is currently defined to be 128 in Luminance.h. Normally this table is synthesized at run time, from one of the formulaic descriptions,but you may prefer to supply it directly, possibly using the raw measurements,and not bother with any fitting. The formulas are not used if the table is supplied.To fill in the numbers above, you have to do two calibrations. (This is what theCalibrateLuminance program does.)0. Before starting, call GDLinearGamma(). (Note that GDOpenWindow automatically calls GDLinearGamma for you.) All calibrations should be donewith the ISR Video Attenuator in place.1. Measure the luminance versus "voltage" nonlinearity of your monitor.I use a separate program "CalibrateLuminance" to measure the screen luminance at valuesof V from 0 to 255. For this calibration you load equal values into Red, Green, and Bluelookup tables. I use quadratic, polynomial, and power law fits. See Pelli & Zhang (1991).You must set LR.LMin and LR.LMax to the luminances at LR.VMin and LR.VMax.The following program fragment allows you to measure the screen luminance as a functionof nominal voltage.#include "VideoToolbox.h"#include "Luminance.h"void main(void){	LuminanceRecord LR;	int V,i,done;	double a;	GDHandle oldDevice,device;	CWindowPtr cWindow,oldCWindow;	char string[32];		#include "LuminanceRecord1.h"	GetGWorld(&oldCWindow,&oldDevice);	LR.screen=1;	device=GetScreenDevice(LR.screen);	/* screen 1 */	cWindow=GDOpenWindow(device);		/* Open a full-screen window with explicit colors */	SetGWorld(cWindow,device);	PmBackColor(1);						/* pick a color table entry */	EraseRect(&cWindow->portRect);		/* fill whole window with that color */	SetGWorld(oldCWindow,oldDevice);	LR.L._VMin=DoubleToFix(0.);			/* if possible, restrict to just the strictly monotonic range */	LR.L._VMax=DoubleToFix(255.);	done=0;	for(i=0;i<LUMINANCES_IN_TABLE;i++){		LR.L._dV=ceil(FixToDouble(LR.L._VMax-LR.L._VMin)/(LUMINANCES_IN_TABLE-1));		V=FixToLong(i*LR.L._dV);		if(V>=FixToLong(LR.L._VMax)){			V=FixToLong(LR.L._VMax);			done=1;		}		LR.table[1].rgb.red		=V<<8;	/* Set color table entry 1. */		LR.table[1].rgb.green	=V<<8;		LR.table[1].rgb.blue	=V<<8;		LoadLuminances(device,&LR,1,1);	/* Copy color table entry 1 to CLUT */		printf("%3d Please measure screen luminance now, in %s, and type in:",V,LR.units);		gets(string);		sscanf(string,"%lf",&a);		printf("%6.2g %s\n",a,LR.units);		LR.L._Lu[i]=DoubleToFix(a);		if(done)break;		if(LR.L._Lu[i]<=LR.L._Lu[0]){	/* restrict to just the strictly monotonic range */			LR.L._VMin=LongToFix(V);			LR.L._Lu[0]=LR.L._Lu[i];			i=0;		}	}	LR.L.latestIndex=-1;			/* invalid latestIndex, so hunt will start from scratch */	LR.L.exists=luminanceSet;		/* mark table as valid */}2. Measure the gains of the three inputs of your ISR Video Attenuator. You coulddo this by using an oscilloscope to measuring the voltage at the input to the monitor.Instead, I measure the resulting luminance and use LToV() to infer the voltage.Vary one DAC while holding the other two fixed at 255 and measure the luminances. Use the function LToV() to convert back to a "voltage" and compute the gain of thevarying DAC. Note that the three DACs on your framestore will generally have gains thatmatch to only ±5%. This calibration is measuring the overall gain of each of the threepathways, including your DACs and the ISR Video Attenuator.	LIMITATIONS:It is imperative that you call GDLinearGamma() at some time before usingSetLuminances. SetLuminances ASSUMES that no gamma correction takes place. Youonly need to call GDLinearGamma once. It will stay that way until the next timeyou restart your computer. Incidentally, GDOpenWindow() calls GDLinearGamma foryou.The luminance calibration data that you supply to SetLuminances must also havebeen collected with no gamma correction, i.e. AFTER calling GDLinearGamma.The reason that gamma correction is not allowed is that it would result in anonlinear transformation of the three channels BEFORE they are combined in theVideo Attenuator.The measurement of the gains of the three pathways must be made using YOURframestore. The gains of your three DACs will in general be different from eachother, and different from framestore to framestore. Brooktree guarantees thematching of the gains of the three DACs on their chip to only ±5%.The luminance record may include either a table of luminance calibrations. If itis not supplied then it will be synthesized from the parameters of thepolynomial or power law fit. If the power, polynomial, or quadratic fitparameters are not supplied then the appropriate LR.powerError,LR.polynomialError, or LR.quadraticError field should be set to infinity(=0.0/1.0).			The whole package is at present restricted to grayscale.There is no provision for linearizing a color monitor. In particular it isassumed that the the DACs are linearly combined BEFORE the display nonlinearity.Linearizing luminance on a color display would need to allow for three differentnonlinear transformations.EXPLANATION OF THE CODE:Physically your framestore transforms each CLUT entry number to a voltage thatwill be linearly related to the number. The three output voltages will becombined by the ISR Video Attenuator to produce a single voltage which drivesthe video monitor. Finally, the display nonlinearly transforms V to produce aluminance L. My convention for "measuring" the "voltage" V at the input of themonitor is that V=0 when all three DACs are set to zero and V=255 when all threeDACs are set to 255. (This will be linearly related to volts measured, with avoltmeter, at the output of the Video Attenuator.) The virtue of the attenuatoris that it allows us to produce nonintegral values of V.There are two givens:1. DACs are inaccurate. A good DAC may be specified to be merely monotonic. Forpurposes of computing the returned tolerance value, I follow the Brooktree DACspecification of ±1 LSB error in integrated linearity and assume that the errorin any luminance difference is at most ±1 LSB.2. We want to minimize the error in representing the waveform, but are notparticularly worried about the exact value of the mean luminance. Thus, if wehave DACs with different gains we may fix the coarse DACs to set the meanluminance and vary the fine DACs to produce the linear range of luminancesrequested.Here's the strategy. We want to cover the range L0 to Ln with the smallestpossible error in L-L0.Steps 1 to 5 happen in SetLuminanceRange:1. Sort the DACs by gain g, where gain is defined as the change in V whena single DAC is increased from 0 to 255, so g0+g1+g2=1. Let the gains be g0>g1>g2. 2. Transform the luminance range to a nominal voltage range lowV and highV.3. Decide which DACs should be variable and which should be fixed,so as the minimize the tolerance in the luminance increments.4. Temporarily set the variable DACs to their midpoints. Now set the fixed DACs tomost accurately represent the midpoint of the nominal voltage range, (lowV+highV)/2.5. If necessary, compute a small luminance offset LShift to bring the requested range lowV to highV into the range attainable by the variable DACs. (This is necessarybecause the centering in step 4 may not be precise enough.)Step 6 happens in _SetLuminance:6. Set the variable DACs in the ColorSpec entry so as to most accurately representL+LShift.SetLuminances(), SetLuminancesAndRange(), and SetLuminance() all call _SetLuminance().#endif