TOUGH LITTLE CABIN


                   Construction Plans in ASCII and .PCX Files





                Designed, Illustrated and Written by Dan Jincks





                           Copyright Dan Jincks 1990

                                Box 155A, HCR 77
                              Annapolis, MO 63620

                          SHAREWARE - SEE NOTICE BELOW






































     *1





                               TABLE OF CONTENTS


     SHAREWARE NOTICE

     PREFACE

     ABOUT THE DRAWINGS

     OVERVIEW

     BEFORE YOU START

     WINDOWS, DOORS AND OTHER OPENINGS

     FLOOR FRAME CONSTRUCTION

     SUB-FLOOR INSTALLATION

     WALL AND ROOF FRAMING

     ROOF PLYWOOD INSTALLATION

     ROOFING INSTALLATION

     EXTERIOR WALL PLYWOOD INSTALLATION

     INTERIOR FLOOR INSTALLATION

     UTILITY PANEL INSERT - WOOD STOVE

     INTERIOR PANELING INSTALLATION

     INTERIOR CEILING INSTALLATION

     FINISHING TOUCHES
























     *2




                                 ILLUSTRATIONS


     FLOOR PLAN   (FLPLAN?.PCX)

     DEVICE OPENINGS   (OPENING?.PCX)

     FLOOR FRAME   (FLOORF?.PCX)

     INSTALLATION OF SUB-FLOOR PLYWOOD   (SFLOOR?.PCX)

     FRONT WALL FRAMING   (FWALLF?.PCX)

     REAR WALL FRAMING   (RWALL?.PCX)

     END WALLS FRAMING   (EWALL?.PCX)

     ROOF BEAM INSTALLATION   (ROOFA?.PCX)

     ROOF FRAMING   (ROOFB?.PCX)

     ROOF PLYWOOD AND ROOFING INSTALLATION   (ROOFC?.PCX)

     EXTERIOR WALLS PLYWOOD INSTALLATION   (OUTPLY?.PCX)

     FLOOR PLYWOOD INSTALLATION   (FLOORP?.PCX)

     UTILITY PANEL INSERT FOR A WOOD STOVE FLUE   (UPANEL?.PCX)

     INTERIOR PANELING INSTALLATION   (INPLY?.PCX)































     *3




     **********************************************************************


                                SHAREWARE NOTICE


     All materials in this plan package are copyrighted by the author.
     This means that it is illegal to make copies of these plans and
     distribute them for your profit.  You may freely distribute these
     plans so long as they are complete and unaltered, and no fees are
     charged for them, except copying costs - not to exceed $5.  All files
     must remain together whether they are computer files, or are printed
     out.  If these plans are used in an actual construction of a
     structure, the user must register and pay a small fee of $15 to the
     author.  THESE PLANS ARE COPYRIGHTED SHAREWARE - NOT PUBLIC DOMAIN.

     If the plans are to be used for construction, register before
     beginning.  Registered users will be notified of any corrections or
     recommended alterations that may have come to light since the plans
     were originated.  Other plans related to this Cabin may also be
     available.  Registered users will receive notice of their
     availability.  Registered users may also order sets of Laser Printed
     hard copy (super sharp 3300 X 2550 page resolution from vector
     drawings and formatted typeset text); or vector drawings in Generic
     CADD, or DXF format on 5 1/4" HD floppy disk.  Up to two printed copy
     sets and one drawing set on disk are available with each $15
     registration.  For printed copy add $5 per set.  For drawings on disk,
     add $5 and specify DXF or Generic CADD format.


     TLCABIN BASIC REGISTRATION -- $15

     TLCABIN PRINTED COPY ----- ADD $5  Each Set (Up to 2 per registration)

     TLCABIN DRAWINGS ON DISK - ADD $5  (Specify .DXF or Generic CADD .DWG)
                              ____________

     TOTAL --------------------              PRINTED COPY ____
                                             .DXF on DISK ____
                                             Generic .DWG ____

     Name _________________________________________________________________

     Company ______________________________________________________________

     Address ______________________________________________________________

     City __________________________State_______ Zip ______________________


     Make payment by check or money order in U.S. Currency to:

                               DAN JINCKS
                               BOX 155A, HCR 77
                               ANNAPOLIS, MO 63620

     **********************************************************************




     *4




                                    PREFACE


     The Tough Little Cabin was originally designed as an earthquake
     emergency shelter.  It has an integrated structure specifically
     intended to withstand earthquake shock - even if your home doesn't.
     There is plenty about that in the text below.  What is interesting
     about the design, is that it costs about the same as most weaker
     structures the same size.  And probably less then one with a fixed
     concrete foundation.  Since it is not tied down and is a reasonable
     size, it can be transported.  You can move it after construction or
     take it with you if you move.

     There is a host of possible uses for small buildings.  It really
     doesn't matter if you need it for an emergency shelter or not.  If you
     are thinking about needing a small out building you should consider
     these plans.  The design came from the actual construction project by
     an experienced designer.  They are not just hypothetical untested
     plans from a pipe dream drawing board.  It WILL work as described,
     since it is described by how it worked out.  If you haven't done any
     full scale construction, this is an excellent project to get your feet
     wet.  These plans are complete and easy to follow - even for a novice.

     Of the many possible uses, some might be: A storage shed, a camping
     cabin, a kids playhouse, a gardening shed, an animal breeding shelter,
     a spare room, a workshop, a construction site store room, a remote on
     site office, a hunting shack, a hobby room (the author is using his as
     a photography darkroom), and of course an earthquake emergency
     shelter.  Some of the following text is aimed primarily at the
     emergency shelter usage, so just skim through those parts if you don't
     need such a thing.

     It's a strong long lasting design no matter what your specific needs
     may be.  The materials costs should be between $500 and $1000.  The
     actual cost will depend on factors like your shopping skills and the
     local costs in your area.  If you decide to use deluxe finishing
     inside or out, the costs will of course go up.  Detailed bill of
     material listings are provided to allow you to work up an accurate
     cost estimation before you make a commitment to the construction.  A
     tool list is also provided.





















     *5




                               ABOUT THE DRAWINGS


     The drawings provided in this plan package are in the most universal
     format and resolution believed reasonable by the author.  They are 640
     X 350 2 color EGA .PCX files.  Each drawing was divided into 4 parts
     so that a readable drawing could be assembled after they are printed
     out.  It was a compromise, but it was believed the most acceptable for
     the largest majority of IBM computer users.  Files in the .PCX format
     can be viewed and printed by many paint programs, and 640 X 350
     resolution is available to most 1990 users.  (actually it is 640 X 348
     for possible Hercules compatibility).  A Shareware program called
     Compushow or CSHOW can be acquired and used to view and print these
     files.  A special viewing script for Compushow is included.  Place
     this plan set in a directory called C:\CABIN and from your Compushow
     directory give the command CSHOWS C:\CABIN\CABIN.SCR and a demo of all
     of the drawings will be displayed.  If nothing screens up, Compushow
     may not be configured properly for you.  Read the literature with
     Compushow.  CSHOW can also print the drawings out for you if you load
     a printer driver.  Again read the Compushow literature.

     There are 14 drawings in a total of 70 .PCX files.  See the table of
     contents above, to see which files are for which illustration.  There
     are 5 files for each drawing.  The file name of each ends with a
     number.  0 is the unreadable overall view, and 1 - 4 are the readable
     1/4 divisions of that drawing.  To get readable copy, you must print
     out 1 - 4 and piece them together.  This is something of an
     inconvenience for sure, but it is the best that can be provided in a
     reasonably universal manner to all.  These .PCX files are a bit crude,
     but the dimensions were touched up to be clearly readable.  They were
     converted from vector files intended for 300 dpi laser printed pages,
     so slight offsets and rough looking text did happen.  As stated above,
     sharp printed copy and vector based drawings are available to
     registered users.



























     *6




                                    OVERVIEW


     This cabin is a tough free standing structure that has many potential
     uses.  It can be used as a storage shed, workshop, kids club house,
     spare room, or camping cabin.  The basic structure was designed to be
     strong enough to withstand and survive the rigors of transport as well
     as strong shocks associated with earthquakes.  In addition to the
     variety of everyday uses for this utility building, it can be relied
     upon to serve as an emergency shelter in the event of a seismic
     disaster (major earthquake).

     Its construction requires only basic carpentry using readily available
     standard building materials and standard carpentry tools.  Most of the
     construction techniques are fairly standard and all steps are
     thoroughly documented.  A few steps may seem a little unusual to
     someone that has done some standard framing construction.  This
     structure is designed to withstand and absorb shock without damage, so
     these slightly different methods should be tolerated and followed as
     given in the instructions.  If you insist on deviating from the plans,
     be sure you are adding to the integrity and not creating stress
     failure shortcuts.

     Every effort was made to keep the material costs down while keeping
     the strength to the maximum.  It is designed to have a very long
     service life requiring little to no maintenance.  Of course it will
     only be as good as the materials and craftsmanship that go into its
     construction.  Using low grade materials or being careless in doing
     the construction could reduce both strength and longevity.  Don't take
     shortcuts that are hard to live with later.

     If this cabin is to serve as an emergency earthquake shelter, certain
     things need to be understood:

     1.  LOCATION.  It is very difficult to assess all of the nasty things
     that can be caused by an earthquake but some possibilities can be
     anticipated.  The whole world will literally be tossed around, so
     things that are standing now may not be afterwards.  Locate the cabin
     well clear of other buildings and trees.  Don't locate it on or near
     the top or bottom of a steep grade.  Don't locate it in a flood plain
     since water may back up or surge.  Uncontrolled fires can happen after
     a quake, so don't locate it near a building, propane tank or brushy
     wooded area.  Keep it well clear of overhead power lines as well.
     Just imagine that everything that can fall or burn will do so, and you
     can assess your location needs from there.

     Even if you don't have a good location on your property, there is
     still hope.  Since the cabin is transportable, you may be able to
     "park" it on some neighboring property.  A location may be able to be
     rented for little or nothing.  Be sure that you confirm this before
     making the building and expecting something that may not be available.
     Be sure that this alternate location is within walking distance of
     your home since roads may not be passable.








     *7






     2.  NON-EMERGENCY USES.  It is very tempting to stuff a utility
     building with stray household items.  There is nothing wrong with
     using it for storage as long as you realize the possible consequences.
     What if you need it as an emergency shelter in the dark of night in
     sub-zero weather?  Are you willing to risk the time and effort
     required to unload it?  You or a family member may be injured and need
     immediate shelter.  Large, heavy unsecured items stored within the
     cabin could do considerable damage as they get tossed around inside of
     it during a quake.

     Highly flammable materials such as gasoline or Coleman fuel should
     NEVER be stored inside or near the cabin.  Even fairly safe
     non-flashing liquids like kerosene are best left outside if practical.
     Otherwise pack them securely in a sealed plastic container within
     another sealed plastic container.  Propane is another very hazardous
     item - leave it outside and turned off.  In addition to the flammable
     liquids themselves, devices that contain them should be emptied of all
     fuel before storage within the cabin.  This would include lawn mowers,
     chain saws, Coleman appliances, etc..  This may seem strict, but in a
     winter emergency situation you will need a heat source that
     doubtlessly will come from a flame.  If fuel is spilled in the cabin
     during the quake, you would not be able to have a flame in the cabin
     without risking a fire or explosion!

     3.  SECURITY.  One very real possibility in a quake is that you and
     your family may need to vacate your house instantly without any
     warning or preparation.  The cabin will become an emergency shelter -
     but not if YOU cannot get into it!  You will likely store things in
     the cabin that you don't want to have "walk off" so they will need to
     be locked up.  If you get separated from the key, you have a problem
     right in the middle of the emergency.  Think ahead about this.

     The solution will depend on how much security that is required.  In an
     area where things don't "walk off" you may leave the door unlocked and
     just lock supplies in a cabinet with a combination lock.  If you are
     in a security problem area you will need to lock the door.  You could
     use a combination lock on a hasp.  If you do use a key lock, stash a
     few keys outside somewhere well away from any building.  Don't forget
     ice and snow can make some places a bad choice.  It might also be wise
     to hide a pry bar just in case the door should jam from the shock.  If
     your cabin is to be used as the kids club house or spare room etc.,
     keep your emergency supplies locked in cabinets so they don't get
     tampered with.

     4.  EMERGENCY SUPPLIES.  To be an effective emergency earthquake
     shelter, you will need to keep a stock of emergency supplies in it at
     ALL times.  This means that no matter what other uses you have for the
     cabin, it will always be an emergency supply storage building to some
     extent.  The surest way to accomplish this, is to have permanent
     cabinets that are only used as supply storage.  Anchor the cabinets
     securely to the structure of the cabin and pack them as if a moving
     man might drop them off of his truck.  Be sure first aid, lighting,
     and blankets are immediately accessible.  However that you use the
     cabin on a regular basis, be sure that you don't block immediate
     access to your first order emergency supplies.




     *8




     Other supplies of less immediate importance, such as food, could be in
     cabinets that might be temporarily blocked by other activities.  In
     the winter months, be sure that spare winter clothes are quickly
     accessible as well.  In the fall, check the operation of your
     emergency heating source and be sure that it is reasonably accessible.
     Also be sure that you have at least a 2 week supply of fuel.  A 2
     month supply is best.  Spare parts for heat and lighting equipment are
     advised as well.

     A good way to anticipate your emergency supply inventory is to imagine
     planning for a 2 month camping experience.  You will be dropped off
     buck naked in the middle of winter with no chance of getting any
     supplies - except what you have in this cabin.  No utilities -
     electric, water, sewer, etc.  will be available on this camping trip.
     It's just you and your well stocked cabin for 2 whole months!  Stock
     it well and with great care.

     As you can see from the above considerations, there are a lot of
     things that go into planning an effective emergency earthquake
     shelter.  The careful construction and proper usage of this cabin can
     go a long way towards protecting you and your family from suffering or
     perishing in the event of a major earthquake disaster.  It cannot be
     guaranteed that you, or the cabin will withstand all of the
     unpredictable effects, but proper preparation may be the difference.

     In addition to the basic instructions for constructing this cabin,
     there are extra suggestions and safety options.  There are many
     excellent illustrations to guide the construction and it is tempting
     to just build from the pictures, but please read the text that
     accompanies them.  Every step in these instructions were performed by
     the author to build an actual cabin.  The author is using this cabin
     as his own earthquake emergency shelter in the New Madrid Fault
     region, and is depending on it to work - just as you will.




























     *9




                                   DISCLAIMER


     The construction of this cabin is completely at your own risk.  While
     the author has made every attempt to provide you with a reasonably
     safe structure using reasonably safe methods, the risks involved in
     the construction and usage of the cabin are not within his control and
     are strictly your own.  If this is not satisfactory - do not attempt
     the construction.  If you do attempt the construction, it will mean
     that you have accepted the condition that all risks taken, are
     strictly your own.  In plain English - This means that if you injure
     yourself while building the cabin or it does not perform the way that
     you expected it to, you cannot blame the author, and if you don't like
     this arrangement, you should not construct this cabin.

     If you find that something is missing, a dimension for instance, and
     you are a registered user.  you can write to the address below.  A
     reply will be given as quickly as possible.  Be sure to be specific in
     your letter about the nature of the problem.  Address the letter to:


                                   DAN JINCKS
                               TLCABIN QUESTIONS
                                BOX 155A, HCR 77
                               ANNAPOLIS, MO 63620




































     *10




                                BEFORE YOU START

     The cabin can be put to many different uses when not being utilized
     for an earthquake emergency shelter.  That was the primary design
     criteria for the plans you are now holding.  The first illustration
     (floor plan) shows how the interior space was planned to be utilized
     by the author.  The locations of windows, door, utility panel and
     vents are based on this particular usage of interior space.

     You may have an entirely different idea of how you wish to use your
     interior floor space.  The locations and numbers of windows, the size
     and location of the door and the need for and size of the utility
     panel could be adjusted for your own requirements.  If you decide that
     you might want to change things around, now is the time to do so -
     before you start construction.

     Any modification of the original plans will need to be reflected in
     each step of the construction and the illustrations that follow will
     not be entirely correct for you.  Here are some basic do's and don't
     to consider:

     1.  Keep the floor to front/rear wall to roof beam connections intact
     at spacings averaging 24 inches, with the exception of 1 break in the
     front wall structure for a door.  (see the roof beam and front wall
     frame illustrations)

     2.  Do not put a door in an end wall or exceed the openings
     illustrated for the end walls.

     3.  Put windows in the front or rear walls between the wall beams,
     with not more then 1 on the front and 2 on the rear.  Do not break a
     wall beam to install a window.

     4.  Fewer and/or smaller windows create a stronger structure than
     putting more or bigger windows in.  Eliminating any window illustrated
     will be cheaper, warmer in the winter and increase the structure
     strength.  Of course windows are good in the summer and let in more
     daylight.

     5.  The utility panel is optional.  It is intended to serve 3
     purposes:

     A.  It can be used to create a safe means of venting a wood stove.

     B.  The panel is removable so that the wood stove vent could be
     installed in a home window to allow the use of wood heat if power is
     down and your chimney is damaged.

     C.  Other devices may be installed later into the utility opening -
     Such as a window air conditioner for a summer workshop or kids room.

     If you decide to modify the plan beyond eliminating a window, be sure
     to thoroughly study all illustrations so that you realize the
     consequences of your changes.  Always try to add structure rather than
     take away from it.  For instance if you go with a 4 foot wide utility
     door and a lot of large windows (within the limits of the above
     guidelines) increase the thickness of your exterior plywood to 1/2"
     instead of 3/8" to regain some of the lost structure.  The Device
     Openings illustration shows the maximum recommended size openings.


     *11




                       WINDOWS, DOORS AND OTHER OPENINGS


     The cabin, as illustrated, has openings for 4 windows, 1 door, 2
     overhead vents, and 1 removable utility panel.  The openings shown are
     for standard size pre-manufactured devices that were available at the
     time, and in the area, that the original cabin was constructed.  The
     door opening is for a pre-hung 32" exterior door.  The windows chosen
     were single glazed aluminum frame type that were inexpensive.  The
     vents were inexpensive open/close louver vents made of aluminum and
     intended to replace an 8" X 16" concrete block.

     The actual devices that you can acquire, at a price that you like, may
     be somewhat different in size.  The device openings illustration shows
     the sizes worked with and the maximum opening sizes recommended.  It
     may seem early in the project to choose windows and doors, but it is
     not.  It is recommended that you resolve your size needs now and
     actually purchase the devices before you start.  This recommendation
     is because of inaccuracies and availability problems encountered by
     the author.

     On the original cabin: The front window size had to be altered because
     an "available" window size turned out not to be available after all.
     The vents turned out to be a different size then were quoted.
     Construction progress was stopped because a window was late in
     shipping.  The only available doors were not what was desired and the
     door ended up being constructed from a door blank and taking up the
     better part of a day to install.  There was a great deal of
     frustration and time wasted that could have been avoided if they had
     been acquired first.

     A special note about the door.  Pre-hung exterior doors are all
     intended to open inward.  This is standard and normal.  An inwardly
     opening door takes up a fair amount of precious floor space which may
     not be desirable in this application (hence the special door on the
     original cabin).  An inwardly opening door might also be a hazard,
     since if it stuck shut from an earthquake after-shock it would be more
     difficult to force if you are inside.  Pre-hung doors also had a
     tighter fit then was desired, and appeared that they could jam too
     easily.

     Hanging a door properly from a blank is an art best left to the
     experienced.  If you want an outwardly opening door with a 1/4" gap to
     resist jamming, it will need to be a custom installation.  Either get
     someone with door experience to help you, or hire a carpenter for at
     least the door work.

     The main purpose of the utility panel is to provide safe passage for
     venting a wood stove.  The utility panel opening (if you want one)
     should have a height and width smaller then a window in your house.
     That way, it and the wood stove, could be used in your house, until
     normal utilities are restored.  Even if you now heat your house with
     wood, a masonry chimney is likely to be destroyed by an earthquake,
     and you will need a safe temporary alternate vent passage.  (see the
     utility panel illustration)

     The vents provide cooler conditions in the summer and a source of
     smoke exit and fresh air if a wood stove acts up.  They are highly
     recommended.


     *12





     Windows are an interesting problem.  You cannot do without them, but
     they are a source of potential trouble.  They are glass and can break
     in an earthquake.  Just broken windows in your house, from a winter
     quake, could force you to require immediate shelter.  If your shelter
     windows break as well, it won't do you much good.  You could replace
     the glass in your shelter windows with unbreakable plastic
     (polycarbonate or Lexan is best).  You could also leave the glass
     windows as they are and make plastic panels that fit the inside of the
     frames behind the aluminum windows and only install them in the
     winter.  The vents can provide fresh air.  That way as long as the
     glass and plastic are both intact, you get double glazed windows and
     only need to buy inexpensive single glazed windows.  If the glass
     breaks, you are still covered and broken glass will not invade the
     cabin either.  Don't make the plastic panels difficult to remove from
     the inside, so windows can still be a emergency exit if the door
     should jam.

     Since the various styles and brands of doors, windows, and vents are
     all different, these instructions will not give details about their
     installation.  Follow the instructions that accompany them.  Get them
     first - and adjust the openings to their true requirements before you
     start.






































     *13


             RECOMMENDED BASIC TOOL LIST FOR THE CABIN CONSTRUCTION


   7 1/4" ELECTRIC CIRCULAR SAW (SKILL TYPE) WITH A CARBIDE COMBINATION BLADE

   3/8" ELECTRIC DRILL (VARIABLE SPEED REVERSIBLE RECOMMENDED)

   SPECIAL DRILL BITS - 1/4" AND 3/8" EXTENDED LENGTH

   SCREW DRIVER TIP HOLDER FOR THE DRILL WITH A PHILLIPS TIP FOR THE DRYWALL
   SCREWS

   SABER SAW WITH FINE METAL CUTTING AND WOOD BLADES

   ROUTER WITH A 3/8" - 1/2" SQUARE BOTTOM BIT

   24" FRAMING SQUARE

   12" COMBINATION SQUARE

   15 FOOT OR LONGER TAPE MEASURE

   SOCKET WRENCH WITH 1/2" AND 9/16" SOCKETS

   ADJUSTABLE WRENCH OR 9/16" BOX END WRENCH

   CLAW HAMMER

   HEAVY HAMMER

   CHALK LINE

   PRY BAR

   2 SAW HORSES

   LONG STRAIGHT EDGE ( 6 - 8 FOOT)

   LEAD PENCILS

   FINE LINE FELT TIP MARKER

   CORD(S) FOR THE ELECTRIC TOOLS

   SMALL SAW - KEY HOLE TYPE

   CAULKING GUN

   METAL SNIPS

   PHILLIPS SCREW DRIVER

   WOOD CHISEL

   UTILITY RAZOR KNIFE

   STAPLE GUN

   2 - 5 INCH OR LARGER "C" CLAMPS

   6 FOOT STEP LADDER


     *14




                            FLOOR FRAME CONSTRUCTION

     Materials required:

     2 - 16' 4 X 6 TREATED PINE (MUST BE STRAIGHT)

     7 - 10' 4 X 4 TREATED PINE (MUST BE STRAIGHT)

     11 - 8' 2 X 4 PINE

     #16 COMMON NAILS (20 LBS.  FOR THE ENTIRE PROJECT)

     CARPENTER'S WOOD GLUE

     18 - 3/8 X 5 1/2" LAG BOLTS

     18 - 3/8" FLAT WASHERS

     MASKING TAPE



     General Instructions - The floor frame is the foundation for the
     cabin.  Therefore, it's quality and strength is of high importance to
     the remaining construction.  Use only straight high quality lumber for
     the beams.  Double check measurements, sizes and squareness as you
     work.  Follow the instructions carefully step by step.

     STEP 1.  Have your materials on hand.

     STEP 2.  Cut the 2 - 4 X 6 X 16' skid beams to length and cut the
     wedges from the ends.  This will require marking and cutting from both
     sides to cut through the 3 1/2" thickness with a 7 1/4" diameter saw.
     Keep the wedges for later use.

     STEP 3.  Cut the 7 - 4 X 4 X 10' floor beams to length.  Measure and
     draw lines on them marking the locations where the skids will be under
     them.

     STEP 4.  Cut 28 - 2 X 4 pieces about 6" long (from scrap if
     available).  Be sure one end is cut square and mark it.

     STEP 5.  Measure and draw lines marking the locations of the floor
     beams on the tops of the skids.  Then nail down the 2 X 4 pieces on
     each side of the floor beam positions.

     STEP 6.  Place the skids on a flat surface if possible, or use the
     wedges to help level them.  Place the floor beams on the skids and get
     them all aligned properly.  Use a framing square to square up
     everything.  Starting at the corners, toe a nail through the 2 X 4
     pieces into the sides of the floor beams to hold them in position -
     keep checking the squareness and positions as you work.









     *15




     STEP 7.  Double check squareness and position of the beams.  Wrap
     masking tape around your extended 1/4" drill bit marking a depth of 5
     1/2" and drill that depth through the floor beams into the skids where
     they cross.  Wrap masking tape around your extended 3/8" drill bit
     marking a depth of 3 1/2" and drill that depth into the previous
     holes.  Using a router with a 3/8" to 1/2" square bottom bit, route a
     recess around the holes in the floor beams 1/2" deep and large enough
     to clear a 3/8" flat washer.  Install 3/8" X 5 1/2" lag bolts with
     washers into each hole and tighten securely.  Remove the 4 blocks
     outside of the end 4 X 4 floor beams, but leave the remaining 24
     blocks in place.

     STEP 8.  Cut the 32 - 2 X 4 intermediate members for the floor beams

     STEP 9.  Mark the positions of the intermediate members on the floor
     beams and nail them into place.  The connections to the 4 X 4 beams
     will need to be toed as illustrated.  When installing the outer
     intermediate members that are 3 1/2" from the end of the beams, use a
     piece of 2 X 4 as a reference to insure proper spacings for the wall
     beams that will be installed there later.  Be sure the tops of all
     pieces and beams are even.

     STEP 10.  Glue and nail the 2 end 8' X 2 X 4s into place using
     waterproof carpenter's glue.  Be sure the tops are even with the tops
     of the 4 X 4s.

     This completes the construction of the floor framing.


































     *16




                             SUB-FLOOR INSTALLATION


     Materials Required: 3 - 4' X 8' SHEETS OF 3/8" C/D EXTERIOR PLYWOOD

     2 - 8' 2 X 4 PINE (CAN BE REUSED LATER)

     2 TUBES OF LIQUID NAILS ADHESIVE OR EQUIVALENT

     #6 GALVANIZED BOX NAILS (7 LBS FOR THE ENTIRE PROJECT)

     1 5/8" DRYWALL SCREWS (5 LBS FOR THE ENTIRE PROJECT)

     2 - 3/8 X 3 1/2" LAG BOLTS

     2 - 3/8 FLAT WASHERS


     General Instructions - The sub-floor is both structural and a barrier
     for the underside of the cabin.  The fit does not need to be tight and
     you might even want to drill 3/8" drain holes in each compartment for
     condensation relief.  To conserve materials, a gap will remain near
     the skid beams.  The tricky part of this operation is to get under the
     frame.  A method is suggested below.

     STEP 1.  Have your materials on hand.

     STEP 2.  If practical, drag the floor frame to the final location of
     the cabin for the remainder of the construction.  If you must move it
     later, be sure to build it in a place that a truck can get access to
     tow or haul it later.  Use a rope or chain to assist dragging it.

     STEP 3.  To install the sub-floor, the floor frame must either be
     turned over or propped up.  Be sure that at least 2 persons assist in
     this operation, since it is heavy!  To prop it up, you will need to
     temporarily install a couple of 2 X 4s as supports.  Drill 3/8" holes
     near the ends then drill 1/4" tap holes in the end floor beams of the
     frame and bolt them together with the 3/8 X 3 1/2" lag bolts.  Do this
     on each end of one side.  Leave the bolts slightly loose so the 2 X 4s
     can pivot.  Drive stakes (#1) into the ground on the side opposite of
     the 2 X 4s.  Lift the side of the frame (using 2 or more people) until
     the frame is propped up.  While 1 person steadies the frame, have the
     other person drive a stake behind the base of the 2 X 4s and a nail,
     near the lag bolt, through the 2 x 4, into the frame -leaving the
     heads out a bit, so that you can pull them later.  Study the
     illustration before attempting this.

     STEP 4.  Measure the actual panel size for the center panels and cut
     the sheets of plywood as shown in the illustration.  Then verify their
     fit.

     STEP 5.  Apply the Liquid Nails adhesive to the frame - one plywood
     section at a time and nail it into place, spacing the nails about one
     foot apart.  Then go back and install a 1 5/8" drywall screw between
     each nail driven.  Do this one panel at a time, for the 3 center
     panels and the three upper panels.  Again, you can expect a slight gap
     around the edges of the panels.




     *17




     STEP 6.  Cautiously, remove stakes #2 and the set nails from the 2 X
     4s and then gradually lower the frame back to the ground.  Caution!!
     Be sure this is done by 2 or more people it is heavy!

     STEP 7.  Remove the props from the frame and install them on the
     opposite side of the frame and repeat step 3 to prop up the opposite
     side of the frame.

     STEP 8.  Install the 3 remaining panels as described in step 5.

     STEP 9.  Lower the frame and remove the props from the frame.

     STEP 10.  Use wedges under the corners of the skids to flatten the
     frame before doing the remaining construction.  The flatness can be
     tested by stretching string across the frame from diagonally opposite
     corners.  When the frame is adjusted flat, the string will just touch
     at both of the ends and the center.  Double check the flatness by
     "eyeballing" the top of the floor beams from a number of angles.  You
     may wish to try to level it as well, but it is not critical to do so.
     Flatness of the frame and squareness of future construction is all
     that is required.

     This completes the installation of the sub-floor and preparation of
     the floor frame for future construction.  Take care not to step on the
     sub-floor plywood or you could break it loose.




































     *18




                             WALL AND ROOF FRAMING


     Materials Required:

     2 - 12' 2 X 4 PINE

     7 - 10' 2 X 4 PINE

     65 - 8' 2 X 4 PINE

     #16 COMMON NAILS (20 LBS.  FOR THE ENTIRE PROJECT)

     13 - 3/8 X 5 1/2" MACHINE BOLTS

     14 - 3/8 X 3 1/2" MACHINE BOLTS

     27 - 3/8 NUTS

     54 - 3/8 FLAT WASHERS

     20 - 1/4 X 3 1/2" LAG BOLTS

     20 - 1/4 FLAT WASHERS

     CARPENTER'S WOOD GLUE



     General Instructions - There are 2 different methods of doing the
     remaining framing construction.  Method #1 is probably faster, but
     requires 2 people to raise the walls.  Method #2 is probably best if
     only one person is doing the construction work.  Both methods will
     give equally good results as long as careful attention is given to
     dimensions, positions and squareness at each step of the construction.
     First review both methods, and choose the one that suits you best.  5
     pages of illustrations are provided to guide the construction of the
     framing.  Study them carefully before beginning, and refer to them
     often.  They are: Front Wall Frame, Rear Wall Frame, End Wall Frames,
     Roof Beam Installation and Roof Framing.





















     *19




                       WALL AND ROOF FRAMING - METHOD #1


     Procedure Summary - The front and rear wall framing is assembled as
     units on a horizontal flat surface and then erected and attached to
     the floor frame.  The roof beams are then attached between the front
     and rear wall beams.  The end walls are then constructed as units on a
     horizontal flat surface and installed between the front and rear
     walls, and the floor frame.  The roof framing is completed in place on
     the structure.  Finally the end wall additions are installed.

     STEP 1.  Have your materials on hand.

     STEP 2.  Locate a large enough flat surface to construct the front
     wall framing.  You can build the frames on top of the floor frame if
     you place 3 sheets of plywood on top of it.  It is not recommended to
     fully install the interior floor yet, but you could temporarily attach
     the 3 sheets of plywood that you will be using for that purpose.  Put
     the good side down until you do the actual installation later.  They
     could be cut to size (see the interior floor illustration) but it
     would be best to do that after installing the end walls and verify
     their actual sizes.  If rain threatens, be sure to cover them.

     STEP 3.  List out and pre-cut all of the 2 X 4 boards needed for the
     front wall framing.  Measure, cut accurately and write the lengths on
     each piece as you cut them.

     STEP 4.  Lay the main wall beams in approximate positions.  Number
     them and measure and mark the positions of to horizontal intermediate
     members that go between them.

     STEP 5.  Nail together the main wall beams and the horizontal
     intermediate members as shown, except for the upper 2 boards of the
     door header.

     STEP 6.  Assemble the remaining parts of the wall frame.  The boards
     that are doubled up on the sides of the door opening should be both
     glued and nailed as they are installed.  Be sure the door, window and
     vent opening sizes are correct before installing their surrounding
     members.

     STEP 7.  Assemble and install the upper portion of the door header as
     illustrated.  Be sure the orientation is correct and use glue as well
     as nails.  Use "C" clamps to hold it in place as you nail it.

     STEP 8.  Make preparations to erect the wall.  2 persons are required.
     Have 2 - 5" "C" clamps, a framing square and 3 extra 8' 2 X 4s (to use
     as supports) ready near the floor frame.  See the illustration on the
     rear wall frame drawing.  The assembled frame may be wobbly,
     especially if you must carry it to the floor frame.  Temporarily
     nailing some boards across the top and front will stabilize it.  (But
     not below the bottom intermediate members) If you have put plywood on
     the floor frame for a working surface, you will need to remove it to
     erect the front and rear walls.  You may wish to set the front wall
     frame aside, and construct the rear wall frame before removing the
     plywood.





     *20




     STEP 9.  Erect the front wall frame and position it onto the floor
     frame.  The lower intermediate members will rest on the floor frame.
     While one person steadies the wall, the other should install the
     supports.  Nail the support to the floor frame and clamp to the wall
     until the squareness is adjusted, then nail the support to the wall as
     well.  Do the ends and then add a support near the center.

     STEP 10.  Adjust the bottom of each wall beam to properly match its
     adjoining floor beam and drive 1 nail to hold the position.  Recheck
     and adjust the squareness.  Finish nailing the wall beams to the floor
     beams.  Then drill through them and install the bolts as illustrated.
     The heads of the outer 2 bolts will need to be recessed with a router.
     Leave the supports in place until the end walls are installed later.

     STEP 11.  Construct the Rear Wall frame following steps 3, 4, 5 and 6
     above, as they apply to the rear wall.

     STEP 12.  Erect and attach the rear wall frame following steps 8, 9
     and 10 above.  Be sure that it is installed with the right to left
     orientation being correct.  See the illustration - it is from the
     outside.

     STEP 13.  Cut the 7 roof beams to size.

     STEP 14.  Starting on one end, install the roof beams one at a time.
     Use "C" clamps to get the position and squareness (of the walls)
     adjusted, then nail the roof beam to the wall beams.  See the roof
     beam installation illustration.  Use the front wall as your squareness
     reference and adjust the back wall to be parallel to it.  Removing the
     rear wall supports may be required as you work.  After all beams are
     in place, drill through them and install the bolts as shown.

     STEP 15.  Measure the exact opening size at the top and bottom of the
     opening for the right end wall frame.  Note the adjusted dimensions
     for the boards used to create the outer wall frame.  (A tight fit is
     required for the inserted end wall frames.)

     STEP 16.  List out and pre-cut all of the 2 X 4 boards needed for the
     right end wall framing.  Measure, cut accurately and write the lengths
     on each piece as you cut them.

     STEP 17.  On a flat horizontal working surface (as described in step
     #2), nail together the 4 boards that form the outer frame.  Then
     install a recessed 1/4 X 3 1/2" lag bolt and washer into each corner.

     STEP 18.  Assemble the remaining parts of the wall frame.  Be sure
     that the window opening size is correct before installing the
     surrounding members.

     STEP 19.  Erect and install the end wall frame between the front and
     rear walls.  You will need to remove any remaining wall supports to do
     this.  If it is a good tight fit, as it should be, you may need to do
     some pounding to install it.  The outer face of the end wall should be
     exactly even with the ends of the front and rear walls.  Nail it into
     place and then install the 6 - 1/4 X 3 1/2" lag bolts and washers as
     illustrated.





     *21





     STEP 20.  Assemble the Left Wall frame following steps 15, 16, 17 and
     18 above.

     STEP 21.  Erect and install the left end wall as in step 19.  Be sure
     that the right to left orientation is correct.  The lag bolt within
     the utility opening will need to be recessed.

     STEP 22.  Measure the tops and bottoms of the front and rear walls to
     be sure that the tops are not spread.  If they are, you will need to
     compress them until they match.  This can be done by starting at one
     end and striking the wall beams, each in turn, with a heavy hammer to
     work the gaps out of the intermediate members.  A slight spread will
     do no real harm, but this is your last chance to correct this and you
     will be fighting any out of squareness later.

     STEP 23.  Measure, and cut to size, the 3 sheets of 1/2" A/C plywood
     to be used for the interior floor.  (See the floor plywood
     illustration) Lay them in place, good side down, so that you have
     something to put a ladder on.  Don't install them yet, and cover them
     if rain threatens before the roof and wall plywood is done.

     STEP 24.  Finish out the roof framing beginning with the 2 front and
     rear end boards and then installing the intermediate members, and
     finally the end pieces as shown in the illustration.  The end pieces
     are basically fillers, so they do not need to be exactly full length.
     It might be a good idea to check the measurements of the opening sizes
     for the intermediate members before cutting them.

     STEP 25.  Install the end wall additions as illustrated.  Each board
     length will need to be measured to be a tight fit.  The fit should be
     tight but not heavily forced.  The outside faces of these boards
     should match the outside face of their end wall.

     This concludes the wall and roof framing.


























     *22




                       WALL AND ROOF FRAMING - METHOD #2


     Procedure Summary - Each set of Front and Rear wall beams, and the
     Roof beam between them, are installed individually to the floor frame.
     Then the 2 long end boards for the roof beams are installed to set the
     proper spacings between the beams.  The intermediate members in the
     front and rear walls are installed.  The end walls are constructed on
     a flat horizontal surface and then installed between the front and
     rear walls, and floor frame.  The roof framing is completed on the
     structure.  Finally the end wall additions are installed.

     STEP 1.  Have your materials on hand.

     STEP 2.  Cut to size the 6 front wall and 7 rear wall main vertical
     beams, and the 7 roof beams.  Refer to the illustrations for Front
     Wall Frame, Rear Wall Frame and Roof Beams.

     STEP 3.  One at a time, install all 13 of the main wall beams to the
     floor frame.  Use a 5" or larger "C" clamp to position and square up
     each one, and nail them into place.  Then drill through them and
     install the bolts as illustrated.  Be careful that they are installed
     on the correct sides of the floor beams.

     STEP 4.  Cut to size and install the framing boards and header for the
     door opening area of the front wall.  Install supports as shown in the
     roof beam illustration for this operation and any other steps that
     they are helpful.  Glue as well as nail the doubled up boards beside
     the door opening and the header boards.  Be sure of the correct
     opening size for you door before doing this.

     STEP 5.  Starting on one end, install the roof beams one at a time.
     Use "C" clamps to get the position and squareness (of the walls)
     adjusted.  Then nail the roof beam to the wall beams.  See the roof
     beam illustration.  Use the front wall as your squareness reference
     and adjust the back wall to be parallel to it.  Removing the rear wall
     supports may be required as you work.  After all beams are in place,
     drill through them and install the bolts as shown.

     STEP 6.  Cut to size the 2 front and rear end boards for the roof
     beams.  Measure and mark the proper positions of the roof beams on
     each board.  Then carefully nail them to the roof beams at the marked
     locations.  Refer to the Roof Framing drawing.  This will set the
     upper spacing of the wall beams so be as accurate as possible.

     STEP 7.  Measure and mark the locations of the intermediate members
     for the front and rear walls.

     STEP 8.  Cut to length and install all of the remaining intermediate
     members and framing boards for the front and rear walls.  Be sure the
     vent and window opening sizes are correct for your devices.

     STEP 9.  Beginning with step #15 in WALL AND ROOF FRAMING - METHOD #1,
     complete the framing of the walls and roof by those instructions.







     *23




                           ROOF PLYWOOD INSTALLATION


     Materials Required:

     4 - 4' X 8' SHEETS OF 3/8" C/D EXTERIOR PLYWOOD

     3 TUBES OF LIQUID NAILS ADHESIVE OR EQUIVALENT

     1 5/8" DRYWALL SCREWS (5 LBS.  FOR THE ENTIRE PROJECT)

     #6 GALVANIZED BOX NAILS (7 LBS.  FOR THE ENTIRE PROJECT)

     100 SQ.  FT.  - 15 LB.  TAR PAPER

     1 BOX 3/8" STAPLES



     General Instructions - The roof plywood is the first structure
     rigidity locking step.  The overall squareness of the walls will be
     set by this installation, so take your time and get everything as
     square as possible before you start.  Recheck the flatness of the
     floor first, and then square the walls.  Use support braces to force
     the walls square if needed.

     STEP 1.  Have your materials on hand.

     STEP 2.  Check and correct the flatness of the floor frame.  Check and
     correct the squareness of the walls.

     STEP 3.  Place panel #1 into position and temporarily hold in place
     with a few nails.  Don't drive them all the way down.

     STEP 4.  Measure the widths of panels #2 and #3.  Cut and temporarily
     hold in place with a few nails.  Adjust all three large panels as
     required to get a good square fit.  If all 3 sides along the edges of
     the roof frame don't seem to square up right, recheck and correct your
     wall squareness as much as possible.  If squareness cannot be
     completely achieved, try getting at least 2 corners on one side
     square.

     STEP 5.  Measure, cut and tack into place the remaining 3 panels.

     STEP 6.  Get all 6 panels adjusted to your satisfaction.  One at time,
     remove a panel, apply Liquid Nails or similar to the roof framing and
     nail the panel down at about 12" intervals.  Then go back and install
     drywall screws between the nails.  Be sure to screw down to every
     portion of the roof frame under each panel.

     STEP 7.  After all panels are installed, staple down 15 lb.  tar paper
     over the plywood as soon as possible.  Start from the back edge and
     lap 4 to six inches.  Overhang the paper about 4 to six inches on all
     four sides and tack it to the sides so that the wind won't lift it.







     *24




                              ROOFING INSTALLATION


     Materials Required:

     6 - 10' PANELS OF GALVANIZED CORRUGATED STEEL (1 1/4" RIB SPACING)

     2 LBS.  OF 1" DRYWALL SCREWS OR ? LBS.  OF SPECIAL NAILS

     1 TUBE OF CLEAR OR SILVER SILICONE CAULKING


     General Instructions - The preferred material for the cabin is
     corrugated galvanized steel panels.  They are lighter then shingles
     and require no maintenance for a great many years.  The main
     preference for steel is for fire safety.  Even if a piece of burning
     wood was on top of the roof, no serious damage would likely happen.
     The same cannot be said for asphalt shingles.  The size of the roof
     was designed to allow quick and easy installation of readily available
     10' panels.  If you would rather use a different type of roofing, try
     to use a metal material.  Steel is the best.  Some people think steel
     gets hotter and makes the building hotter.  This is not true.  It may
     FEEL hotter to the touch, but it actually releases heat much faster
     then shingles do, so less heat passes into the structure.  Light
     colors or metallic finishes also reflect heat better then dark
     finishes.

     STEP 1.  Have your materials on hand.  Do this on a day with little or
     no wind and wear heavy gloves while handling the sheets.

     STEP 2.  Position your first panel according to the illustration and
     hold it down with 2 - 1" drywall screws.  Drive the screws into raised
     ribs, not the valleys.

     STEP 3.  Position and screw (with 2 screws each) the rest of the
     panels as described in the illustration.

     STEP 4.  Once you are satisfied with the locations of the sheets,
     fasten them down with 5 rows front to back and 4 fasteners per sheet
     per row.  The standard fastener for these panels are nails with
     washers or lead caps but they may not work very well, driven into
     plywood.  The original cabin roofing was installed with 1" drywall
     screws.  Then each head was sealed over with silicone rubber caulking.
     Which ever fastener that is used, be sure that they are driven only
     into the raised ribs, not the valleys.

     This completes the roof installation.














     *25




                       EXTERIOR WALL PLYWOOD INSTALLATION


     Materials Required:

     10 - 4' X 8' SHEETS OF PLYWOOD (SEE INSTRUCTIONS FOR THICKNESS AND
     TYPE)

     1 5/8" DRYWALL SCREWS (5 LBS FOR THE ENTIRE PROJECT)

     #6 GALVANIZED BOX NAILS (7 LBS.  FOR THE ENTIRE PROJECT)

     6 TUBES OF LIQUID NAILS ADHESIVE OR EQUIVALENT

     DOOR, WINDOWS, AND VENTS

     EXTERIOR FINISH - SEE THE INSTRUCTIONS

     15 SQ.  FT.  OF 3 1/2" INSULATION


     General Instructions - Before buying your plywood, some considerations
     should be reviewed.  First, how will you be finishing the cabin
     exterior?  Second, are you putting in windows and a door larger then
     the plans show?  The basic recommended plywood thickness is 3/8".  If
     your openings are enlarged, the plywood should thickness should be
     increased to 1/2" instead of 3/8".  The price difference is usually
     not that great, and the strength increases considerably.  Your choice
     of exterior finish ranges from painted plywood to expensive elegant
     siding.  There is even treated plywood that requires no finish.  If
     you intend to install siding, basic C/D exterior sheathing grade
     plywood is all that is needed.  If you intend to just paint the
     plywood, A/C exterior grade plywood would be best.  A/C plywood may
     cost almost twice as much as C/D, and by the time you include the cost
     of the paint, it makes siding worth looking into.

     The original cabin was sided with the same galvanized steel panel
     recommended for the roof.  It is tough, long lasting, fire resistant,
     available, inexpensive and matched a nearby building.  An appearance
     that blends in with the location is a definite consideration.  Siding
     costs a fair chunk of the building cost and takes some time and
     patience to install correctly.  A time and dollar stretching
     compromise might be to paint C/D plywood for now, and when extra time
     and/or money become available, install the siding.  Any way that you
     decide to handle it, plan to put some sort of finish on immediately,
     to weather proof it.

     Installing the exterior wall plywood is what really sets the rigidity
     of the structure.  Be extra sure that the walls are square to the
     floor, and it is not leaning.  Recheck the flatness of the floor first
     and then square up the walls by installing temporary supports as
     required.  Since you will be starting with the front and rear walls,
     try placing the supports on the ends if you can.  Don't put any
     plywood on until you are absolutely satisfied with the squareness.

     STEP 1.  Have your materials on hand.





     *26




     STEP 2.  Be sure that the floor is flat and the walls are square.
     Adjust with temporary supports as needed.  Install insulation in the
     lower and end cavities that cannot be accessed from the interior after
     the exterior plywood is installed.

     STEP 3.  Beginning on the back wall; measure, cut and place check the
     first panel.  (see the Wall Plywood Installation illustration.)  The
     panel should overhang the end, equal to the thickness of your plywood.
     When you are satisfied with the fit, take it down and apply Liquid
     Nails or equal to the wall frame that it contacts.  Nail it into place
     at about 12" intervals.  Then go back and drive 1 5/8" drywall screws
     between the nail placements.  Be sure screws are driven into every
     frame member behind the panel.

     STEP 4.  Cut the over all size of the second panel and tack it into
     place with a few partially set nails.  Trace the outline of the window
     opening from behind.  Take it down and cut the window opening except
     about an inch in each corner, so that the panel is stable to handle.
     Apply the adhesive to the wall framing.  Nail and screw it into place.
     Use a keyhole type saw and finish cutting the window opening when it
     is convenient to do so.

     STEP 5.  Measure and cut panel #3 being sure it overhangs the end
     equal to the thickness of your plywood.  Glue, nail and screw it into
     place.

     STEP 6.  Install the plywood on the front wall in the same manner as
     above.  Remember that it overhangs the ends as well.  Note that panels
     #2 and #3 have a staggered step around the window opening and that
     panel #3 could be pieced to conserve material.

     STEP 7.  Install plywood on the ends in a similar manner as above.
     Note that panel #1 on both ends will not quite extend to full height
     in the upper front corners, and that a notch for the skid beams is
     required for panels #1 and #2 on both ends.

     STEP 8.  Install insulation in the cavities under the eves.

     STEP 9.  Measure, cut, glue, nail and screw plywood panels under the
     eves.

     STEP 10.  Optionally install trim strips on the front and rear roof
     end faces, and under the roofing edges on the sides.

     STEP 11.  Either caulk and paint the plywood, or staple up 15 lb.  tar
     paper if using siding.

     STEP 12.  Install windows, door and vents.

     STEP 13.  Install any desired exterior electrical outlets, generator
     input, electrical inputs, etc..

     STEP 14.  Install siding if that is the plan.

     STEP 15.  Temporarily cover the Utility Panel opening until in is
     completed and installed.

     This completes the exterior of your cabin.  (Take a well deserved
     break and admire your work.)


     *27




                          INTERIOR FLOOR INSTALLATION


     Materials Required:

     3 - 4' X 8' SHEETS OF 1/2" (OR THICKER) A/C EXTERIOR PLYWOOD

     1 5/8" DRYWALL SCREWS (5 LBS.  FOR THE ENTIRE PROJECT)

     2 TUBES OF LIQUID NAILS ADHESIVE OR EQUIVALENT

     100 SQ.  FT.  3 1/2" INSULATION

     1 QT.  OIL BASED FLOOR PAINT

     General Instructions - Your floor consists of 3 sheets of plywood.
     The type used should be A/C exterior grade.  The thickness should be
     1/2" minimum, and thicker if you intend to put it to heavy use.  Flake
     or particle board is not recommended because of formaldehyde release,
     moisture expansion and less structural strength per pound.  Insulation
     should be installed in the floor cavities.  Since the use of glue is
     recommended, don't lap the backing of the insulation over the floor
     frame.  Drilling drain holes into the bottom of each cavity for
     condensation relief is a good plan, but that will allow insect
     invasion into the sub-floor area.  The original cabin floor cavities
     were heavily dusted with Diatomaceous Earth powder (fossil powder)
     before the insulation was installed.  This material is like broken
     glass and razor blades to insects, and will eventually kill any that
     contact it.  It has an indefinite residual, and is harmless to humans.
     It can be found at organic garden supply stores and possibly feed
     stores.  (it is used to kill intestinal parasites in livestock.)

     STEP 1.  Have your materials on hand.  Check that there are no high
     spots from the intermediate members.  If there are, use a wood chisel
     to remove them.

     STEP 2.  Drill drain holes through the sub-floor plywood and treat the
     cavities with insecticide if desired.

     STEP 3.  Install insulation into the floor cavities.  Don't lap the
     backing over the floor frame.

     STEP 4.  Place panel #1 (a full size sheet) and center it.  An equal
     gap of about 3/8" to the front and rear, and equal distance from both
     end walls.  Tack it into place with a couple of drywall screws.  (see
     the illustration)

     STEP 5.  Measure, cut and place panels #2 and #3 so there is about a
     1/4" gap by the end walls.

     STEP 6.  One at a time, remove a panel and apply Liquid Nails or equal
     to the floor frame, replace and screw down with 1 5/8" drywall screws.
     Place a screw about every 9" and be sure to screw to every member of
     the floor frame.  If the edge gaps are not covered by the wall
     paneling later, you can caulk or install trim strips.  (The gaps act
     like expansion joints for shrinkage and motion displacement to help
     prevent floor buckling)

     STEP 7.  Paint the floor with 2 coats of good oil based floor paint
     and let dry.

     *28




     This completes the basic floor installation.  A floor covering of your
     choice can also be placed over it.  Carpet is not recommended.  If a
     wood stove will be used, take care in your choice of floor covering
     within 3' of it in any direction.  It may be best to install floor
     covering after any permanent cabinets or fixtures are installed.
























































     *29




                       UTILITY PANEL INSERT - WOOD STOVE


     Materials Required:

     2 - 8' 2 X 4 PINE

     1 - 4' X 8' SHEET OF 3/8" C/D PLYWOOD

     1 - 3' X 8' SHEET 26 GA.  GALVANIZED SHEET STEEL

     1 - DOUBLE FLANGE COLLAR WALL PASS-THROUGH FOR A WOOD STOVE FLUE

     1 - 100 CT BOX #8 X 1/2" SHEET METAL SCREWS - PHILLIPS HEAD

     CARPENTER'S WOOD GLUE

     SILICONE RUBBER CAULKING



     General Instructions - A wood burning heat source is a valuable item
     for camping or an emergency shelter.  It is also a potentially
     dangerous device as well.  If not throttled back properly the stove
     and flue pipe can literally get red hot.  If either is in near contact
     with an ignitable item, it will start a fire.  Passing a flue pipe
     through a wall requires special precautions to insure safety.
     Commercially produced devices are available to do this, but they need
     some help.  The small double flanged collars for about $10 are
     marginal at best.  (insurance companies won't approve them) A utility
     panel insert can be built that will prevent excess heat build up
     around the flue exit.  It is used in conjunction with the flange
     collar for more positive safety.  (although it has not been rated by
     insurance companies) Wood stove operation and safety is something of
     an art.  If you don't have experience, find someone that does, to help
     you get started.  One serious mistake could burn the place down.

     The principal behind the flue panel is simple.  Keep the flammable
     materials away and allow air to circulate to keep heat from building
     up.  Two hollow cavities with convection venting are created buy the
     panel.  The first is all metal and the second is metal covered wood.
     This is in addition to the commercial flange collar device.  A triple
     safety factor.  Be warm, but be safe.  That is also the reason that
     the floor plan has the door located well away from the wood stove.

     STEP 1.  Have you materials on hand.  Refer to the illustration.

     STEP 2.  Construct a 2 X 4 frame that fits the utility panel opening.
     This can be done right in the opening for good accuracy.

     STEP 3.  Glue and screw pieces of 3/8" paneling to both the front and
     back of the frame.  Use carpenter's wood glue (non flammable type) and
     let dry.

     STEP 4.  Cut openings in the plywood as illustrated.  Note the drawing
     is showing both the inside and outside surface in each step.  The
     convection openings are only on the inside.




     *30




     STEP 5.  Cut pieces of sheet metal to cover the entire face for each
     side and set aside for later.

     STEP 6.  Cut pieces of sheet metal and install them to form a tunnel
     through the 18" square holes.  26 Ga.  steel can be hand formed and
     then pounded down with a hammer.  Install with nails because you will
     not want screw heads sticking up later.  Also try to overlap them in
     the tunnel corners and screw them together.  Seal the corners air
     tight with silicone rubber caulking.

     STEP 7.  Cut the openings in the steel face panel, for the interior,
     with a saber saw.  Drill a hole in the center of each marked cut-out
     to insert the saw blade and then cut an "X" diagonally from corner to
     corner.  Then you can fold the metal back and avoid sharp edges at the
     openings.  The center circle needs to be the size for your
     manufactured flange device.  The cut edges of the circle will be
     rough, but covered later by the flange.

     STEP 8.  Screw the interior face plate to the insert and don't spare
     the screws.  Then turn it over and caulk around the face panel and
     tunnel inside.

     STEP 9.  Temporarily install the exterior steel panel with a couple
     screws and turn the assembly over.  Insert the flange collar and use
     it as a guide to mark the circle for the other flange tube opening.
     Note that the flange tube openings are different sizes since one
     slides into the other.

     STEP 10.  Remove the exterior face panel and cut the circle out for
     the flange tube.  Check the fit of the flanges.

     STEP 11.  Place a bead of silicone caulk around the tunnel opening on
     the exterior insert face and replace the exterior metal panel and
     screw them together - not sparing the screws.

     STEP 12.  Install the flange collars from both sides.

     STEP 13.  Install the completed insert assembly into the panel opening
     with the convection vents inward.  To hold the insert in the wall, lag
     bolt pieces of bracket metal to both the insert and inside (and/or
     outside) wall face of the cabin.  You can now pass a flue pipe safely
     through the wall.

     This completes the utility panel insert for a wood stove.  Again, have
     an experienced wood stove user inspect your setup and show you the
     proper safe operation of your stove.  Don't be a burned beginner!!















     *31




                         INTERIOR PANELING INSTALLATION


     Materials Required:

     10 - 4' X 8' SHEETS OF PLYWOOD PANELING

     3 LBS 1" DRYWALL OR PANELING SCREWS

     5 TUBES OF LIQUID NAILS ADHESIVE OR EQUAL (SEE INSTRUCTIONS)


     General Instructions - Before doing the interior paneling, install any
     electrical wiring desired and the insulation.  The paneling should be
     made out of plywood and be 1/4" thick minimum.  It could be anything
     from painted 3/8" plywood to fancy 1/4" interior wood grain paneling.
     The interior paneling does add to the building structure, so attach it
     well.  Installing the insulation and using glue for the paneling
     installation conflict with each other.  The facing paper of the
     insulation is usually stapled to the framing just where the glue is
     applied.  A compromise might be to limit the facing on the framing and
     apply glue to only some areas of the framing.  Use of glue is not
     essential but highly recommended.  In any case, install the paneling
     with screws rather then nails.  Screws are a much more positive
     attachment means than nails.

     STEP 1.  Install any electrical wiring that is desired.

     STEP 2.  Install insulation in all of the wall frame cavities.

     STEP 3.  Beginning with the rear wall, cut the full width overall
     panel for the center.  Do not extend the panel into the gap between
     the floor plywood and the wall frame.  Open the window and remove the
     screen so that you can reach through it from the outside.  Tack the
     panel into place with a couple of screws and mark as much of the
     window as you can from behind it.  Take the panel down and finish
     marking the window opening and cut it out except about 1" in the
     corners.  That way the panel will remain stable until it is installed.

     STEP 4.  Install the center panel with screws at no less then 12"
     intervals.  Be sure to screw to every member of the wall framing.
     Glue is recommended as well, especially around the window.  Finish
     cutting out the window opening with a keyhole type saw.

     STEP 5.  Measure, cut and install the outer 2 panels for the back
     wall.  Be sure that the vertical cut edges are on the outside wall
     corners, not adjacent to the first panel.

     STEP 6.  Panel the front wall in the same manner as described above.
     You will need a helper to mark the door opening from the outside while
     you place the panel from the inside.  The vents will need to be
     measured and marked.  The vent openings could be marked and cut out
     undersize and then finish cut after the panels are installed, to get
     an exact opening fit.







     *32




     STEP 7.  Measure, cut and install the paneling for the end walls as
     shown in the illustration.  Since both panels on each end wall are
     full width, install them from the center edges out.  Any gap in the
     corners can be covered with trim strips.

     STEP 8.  Install trim strips or caulk around the floor edges and wall
     corners.  Do not do anything to the tops along the roof.

     This completes the interior wall paneling installation.




















































     *33




                         INTERIOR CEILING INSTALLATION


     Materials Required:

     3 - 4' X 8' SHEETS OF PLYWOOD PANELING 1/8" THICK

     1 LB.  - 1" DRYWALL OR PANELING SCREWS

     2 - 12' TRIM STRIPS (SEE INSTRUCTIONS)

     General Instructions - The material for the roof paneling should be
     thin and light 1/8" thick plywood paneling.  Install any electrical
     wiring and the insulation first.  The panels can be 3 large sheets or
     strips the width of each set of roof beams.  The advantage of strips
     is that it allows their removal to anchor beams to the roof beams to
     build cabinet structures later.  For this reason, using glue is NOT
     recommended, at least not until after all interior structures are
     completed.

     STEP 1.  Install any electrical wiring desired.

     STEP 2.  Install insulation into the ceiling cavities.

     STEP 3.  The ceiling panels will be sized and positioned just like the
     floor panels.  See the flooring illustration and instructions.
     Measure the ceiling length.  It will be longer then the 8' sheets.
     Divide the amount over 8' equally on both ends.  Using screws, install
     the full size center panel.

     STEP 4.  Measure, cut and install the 2 outer panels.

     STEP 5.  Install trim boards along the front and rear walls.  The trim
     boards should be wide enough to cover the gaps left by the ends of the
     roof panels.  Use hefty size screws to install them.

     STEP 6.  Install trim strips or caulk the edges along the ceiling and
     end walls.

     STEP 7.  Optionally install trim strips over the 2 seams between the
     sheets for added assurance that the panels will stay up.  If you are
     installing strips instead of full panels, trim strips can be used to
     cover all of the seams.

     This completes the installation of the interior ceiling.
















     *34




                               FINISHING TOUCHES


     The basic exterior and interior structure is now completed, but many
     details still need to be completed.  The details will be finished in a
     different manner by each proud owner of their cabin to match their own
     personal needs.  Below is a list of items to consider.

     VENT DOORS.  The vents are probably not very air tight when they are
     closed.  A hinged interior door with a closure catch and a foam
     compression gasket around the edges would create a positive seal.

     SAFETY PANELS FOR THE WINDOWS.  Winter panels made of rigid clear
     plastic sheeting could be made for each window to reduce heat loss in
     the winter.  The best plastic is polycarbonate (Lexan) because it is
     unbreakable and will not distort from normal heat exposure.  The
     panels should be installed into the window frame from the inside.
     Make at least 1 of them easy to remove, without tools, so that the
     window can be opened if needed.

     WINDOW COVERS.  Interior covers for each window made of gasketed wood
     panels hinged to the wall above the window.  The covers would provide
     extra security as well as better insulation on really cold nights.
     They can be held open by a catch on the ceiling, or closed and
     retained by a catch on the wall.  If a window is broken, it is a
     simple matter of closing that cover until repairs are possible.  This
     cover would be used on the window above the beds if the optional bunk
     bed were employed.  (see floor plan).

     STORAGE CABINETS AND COUNTER TOPS.  The cabin furnishings will
     certainly include some storage cabinets.  These could be manufactured
     ones or self-constructed ones.  Regardless of the type they should be
     securely anchored to the cabin structure.  Vertical beams could be
     installed from the floor to the roof beams for supports.  At the very
     least, they should be bolted to the walls and floor.  Refer to the
     framing illustrations to locate the main beams in the walls and bolt
     directly to them.

     BEDDING.  Refer to the floor plan illustration for the bedding
     suggestions.  3 twin mattresses could be stacked and employed as
     needed.  One pulled out on the floor beside and one above as a bunk.
     The bunk option will require creating a support structure.  An under
     mattress plywood structure board can be stored against the wall behind
     the mattresses when not being used.  Then placed onto the support
     structure when needed for the bunk.  The support structure would need
     to be anchored from floor to ceiling at the end away from the wall.
     The addition of a panel to the support structure would form a wall to
     create a closet or small toilet privacy area.  Of course any toilet
     would be a port-a-potty type, since there is no plumbing.  Notice the
     convenient location of one of the vents just above this possible
     toilet area.  Store plenty of blankets for the beds.










     *35




     HEATING.  Any cabin or emergency shelter would require a heat source.
     There are a number of possibilities, but any type of heater used must
     require no external utility source to function (electricity or piped
     in gas).  All portable heaters are dangerous to some degree.  Whether
     it is wood, kerosene, or propane; they all consume oxygen and could
     release deadly carbon monoxide.  A vent should be open at all times
     during their operation.  Exposure of a flammable item to high heat
     could start a fire, so be careful about the installation.  Keep a fire
     extinguisher on the wall.  Anchor the heater and accessories very
     securely.  Never refuel with a flammable liquid inside of the
     structure and store the extra fuel outside away from the building.
     Have your setup inspected by someone that is experienced with your
     type of heater - before you use it.  Then test it, before you actually
     need to rely on it.

     LIGHTING.  A portable lighting source is needed for the cabin.
     Battery operated lights are great for occasional hand use, but a long
     term lighting method will be needed.  Kerosene lamps are probably the
     safest and most reliable.  Coleman fuel type lights require the use of
     a very explosive fuel and need new mantles if banged around.  The also
     give off some radiation that is not safe for long term day to day
     usage, and they are noisy as well.  Whatever the light source, anchor
     them securely and have spare parts for anything that can break or wear
     out.  The safety rules are the same as for the heaters.

     PROVISIONS.  Everyone has different requirements for provisions.
     Food, water, and clothing are universal.  Store these items carefully
     and in sufficient quantity.  Store water in containers that can
     withstand the expansion of freezing.  A method of treating
     questionable water should be kept as well.  Purification chemicals,
     micro filters, or a distilling device are some possibilities.

     Food can be in the form of dry grain products and/or canned goods.
     The canned food should be in the ribbed steel cans that can withstand
     freezing.  Never eat from a can that remains bulged after thawing or
     you risk deadly botulism poisoning.  Grain foods should be stored in
     sealed rigid containers and inspected occasionally for insect or
     rodent invasion.

     Store extra clothing.  It can be some that you don't use anymore, that
     is out of style or a bit worn.  Extra shoes and winter clothes are a
     must.

     The cabin is a great place to store all of your camping gear when you
     are not using it.  The gear will contain most of the items that are
     needed in an emergency shelter.  Be sure that the Coleman fuel stays
     out and any appliances are emptied.

     The cabin is also a great place to store your tools, especially the
     hand operated ones.  They could be real handy in an emergency
     situation.  Especially store hammer, nails, hand saws, pry bars and
     similar items.

     Store first aid items on top for quick access.

     Be sure heavy items are stored low and pack everything securely.


                                      END


     *36