CT470.DK Help File

  Loading in the file CT470.DK will setup Band-in-a-Box for the Casio CT470
keyboard in Multi-Timbral Mode (Mode B).In Mode B the CT470 can receive 4
different instruments at a time(with 12 note polyphony amongst them). Being 
that Band-in-a-Box has some 5 instrument styles, the CT470 will be unable to 
play Guitar and String parts from such styles.The polyphony of each channel
refers to the amount of notes that channel will be able to receive in total.
In Mode B, the polyphony of each channel is; Channel 1 = 6 notes, Channel 2 
= 4 notes, Channel 3 = 2 notes, and Channel 4 = 4 notes. If any notes get 
'cutoff' during a Band-in-a-Box session, the polyphony of each channel 
could give some problems.

The CT470.DK file will setup:
1. Drum #'s for the Casio CT470.
2. General Midi Patch Map (assigned to factory settings of the C470).
3. Startup Patches and Channels in the Midi Settings Window.

To setup your CT470 do the following:

- Ensure that ACCOMP VOLUME is turned UP

- Set the dial used to turn the CT470 on to MIDI (for Multi Voice Mode)

- Press the ORCHESTRATION buttons:Chord1,Chord2,Obligato,and Auto Harmonize

- These four buttons correspond to MIDI channels 1-4

- Midi Channel 1 will be dedicated to Piano,2 to Melody,3 to Bass and 4 to
  Drums
- Press the Auto Harmonize button to ensure that the SELECT button shows
  the bottom red  light is on so it will be setup to play DRUMS.
  Please note: DO NOT SEND PATCH CHANGES ON THE DRUMS FROM BAND-IN-A-BOX! 
Doing so will result in a pitched instrument receiving what are intended to 
be DRUMS.Also make sure that in the Midi Settings window in Band-in-a-Box
that Output Sync/Start info is 'N' for NO or else you'll hear your CT470's
Multi-Accompaniment System start to go.
 
  Ensure that the MIDI OUT of your computer is going to the MIDI IN of your
synth and vice versa. Now load CT470.DK under the MIDI pulldown menu 
(Load Alternate Drum/Midi Set).That should be all that need be done to allow
Band-in-a-Box to "talk" with your CT470. If by any chance we haven't covered
everything on your particular synth, please consult your owners manual.
 
                                                Have Fun!