TEKN1000.DK Help File

Loading the file TEKN1000.DK will set up Band-in-a-Box for 
the Technics KN1000 PCM Keyboard.  It will setup:

1.  Drum #’s for the Technics KN1000.
2.  Patch Map (assigned to factory settings of the Technics 
KN1000).
3.  Startup Patches and Channels in the MIDI Settings Window.

In order to set up the Technics KN1000, there are only two 
deviations
from the original factory presets. First, if you have changed many 
of
the MIDI settings of the instrument and you wish to retrieve them 
later,
it is recommended to save the existing layout to diskette or with a
sysex dump to a sequencer or librarian, or to copy down the
particular settings you have made. Then set the KN1000 MIDI 
inputs
to the factory settings by pressing:

   MEMORY & CONTROL, then CTRL1, then MIDI, and "YES" 
I am sure.
   Press MEMORY & CONTROL again to reset the display.

Now two changes to these settings must be made:

(1) Realtime Start/Stop messages must be disabled so that the 
KN1000
doesn't start its own built-in drum machine every time you start a
Band-in-a-Box song. Do this by pressing:

   MEMORY & CONTROL, then MIDI2, then the accomp 2 
button to change
   Realtime Cmd <EN> to show Realtime Cmd <DIS>.
   Press MEMORY & CONTROL again to reset the display.

(2) The program change selection must be changed from 
"NORM" (which
can select only 40 sounds from the sound pad, and the sound 
variation
depends on the variation you last selected for each sound) to 
"TECH"
which allows MIDI patches for nearly all the sounds built into the
KN1000. To do this, press:

   MEMORY & CONTROL, then MIDI2, then the PAGE ^ to 
display page 2,
   and finally the poly-1 button to change P.CHG<NORM> to 
P.CHG<TECH>.
   Press MEMORY & CONTROL again to reset the display.

Have Fun!