TG33.DK Help File

  Loading in the file TG33.DK will setup Band-in-a-Box for the Yamaha
TG33 multi-timbral synthesizer module.

It will setup:
1. Drum #'s for the Yamaha TG33 module.
2. General Midi Patch Map (assigned to factory settings of the TG33).
3. Startup Patches and Channels in the Midi Settings Window.

To setup your TG33 do the following:

- Press the  MULTI button so the TG33 can receive on more than one Midi
  channel at once ( commonly reffered to as "Multi-Timbral" mode )
- Next go to UTILITY and cursor through until you come across MIDI
- You should see PROG CHANGE = ON/OFF ; set to ON so Band-in-a-Box can
  change the sounds of your synth according to the Styles and Songs
- Keeping 8 Midi Channels open for Band-in-a-Box is required within a Multi
  patch (each location can be assigned an instrument and Midi channel )
- We reccomend using one Multi patch as your Band-in-a-Box working Patch

 Configure a Band-in-a-Box patch for the TG33 as follows:

INST                        BANK                        MIDI CHANNEL
----                        ----                        ------------
Bass                         P2                              3    
Piano                        P2                              2  
Drums                        P1                             10
Guitar                       P2                              7
Strings                      P2                              6
Melody                       P2                              4
Thru                         P2                              5  

  Use the Bank/Multi Channel buttons to select Midi channels for the 
various instruments. You'll be using the Factory Preset sounds; P2 for Piano,
Bass,Guitar,Strings,Melody and Thru instruments and P1 for Drums. Use the 
cursor to change between I,P1 and P2 (Flashing square over top of the current
selection). 
  Once the parameters of your Multi patch have been setup, save the Multi
as "BandBox" by pressing the page> button SIX times to get to the page of 
available characters for the patch name. To store the Multi patch: Press 
[Store/Copy] key from the Multi Play mode and select a memory location (1-16)
using the bank multi channel keys. Press +1 . Select 'Yes'. "Are U Sure?" 
comes up; select 'YES'. The Multi Patch is now stored in the TG33's memory.

  Please note: DO NOT SEND PATCH CHANGES ON THE DRUMS FROM BAND-IN-A-BOX! 
Doing so will result in a pitched instrument receiving what are intended to 
be DRUMS.
 
  Ensure that the MIDI OUT of your computer is going to the MIDI IN of your
synth and vice versa. Now load TG33.DK under the MIDI pulldown menu
(Load Alternate Drum/Midi Set).That should be all that need be done to allow
Band-in-a-Box to "talk" with your TG33. If by any chance we haven't covered 
everything on your particular synth, please consult your owners manual.
 
                                                Have Fun!