GUS MIDI Player, version 0.02 Alpha - INTERNAL USE ONLY - 11-Nov-93

History:

0.02 - Added MIDI channel mask CL option, detailed below
     - Fixed drum channel not drumming in 0.01
     - Erc: returned in decimal instead of hex to match codes below
     - Display more voice status info

0.01 - Yeah, well, what can I say (having fun, though)


Okay, so after four months I have something for you! The toolkit will be
made available able to on the BBS in the Ruckus developer's conference
as soon as we get some basic testing done. This program contains the
generic MIDI parser and the static LIB version of the GUS support code.
The dynamic DLX version will be tested at a later (same code, just
a couple of small load/management modules, in addition).

Back to this program. Here's what you need:

 1. 286 or higher CPU - the GUS support code was written using
    a few 286 instructions that made a world of difference.
    Only high-end cards will have 286+ code. The AdLibs, OPL2s,
    will run just fine with an 8088. 1MB of GRAM probably is
    a good idea. All patches are loaded in native form (16-bit,
    full sample).

 2. These environment variables must be set:

    ULTRASND=260,7,7,11,11
    rem ULTRADIR=F:\SND\_GUS (not used by Ruckus)
    PATDIR=F:\SND\_GUS\MIDI
    rem DLXDIR=F:\PRG\ASM\R2\_DLX (not needed now)

    In other words, set the ULTRASND= eVar to something that
    works for your system. The above is my setting. the PATDIR=
    eVar is the location of the GUS patch files (patch file
    version 1.10). The old patch files may not work. Anyway,
    everyone should have their GUS 2.06 disks by now. The new
    patches are on these disks (5.5MB worth!). BTW, this should work:

         SET PATDIR=%ULTRADIR%\MIDI

    You'll probably need the ULTRADIR= for other GUS software.
    The DLXDIR= is for locating the dynamic link modules. You'll
    know all about these later.

 3. That's it. To use the program, GMP002.EXE, you have these
    command-line options:

        C>gmp001 pathname.ext /Vnn /Cnnn?

        pathname.ext can be any valid DOS pathname to a valid
        MIDI file. GMP002.EXE is setup to play over MIDI channels
        0 to 9, with the percussion on 9 (1-10 for 1-based folk).
        This is just to simplify running Windows CANYON.MID file,
        which is a dual-sequenced MIDI file. Ruckus can deal with
        it, but the interface is not setup yet (i.e., for the
        control program -- itself only about 120 lines of assembly).
        The default patch is 0, acpiano.pat. Ruckus allows for
        remapping patchnames, patch numbers, banks, and so on, but
        again, the interface isn't set up (hey, though it's small,
        there's four months of work in here). Enough on this for now.

        The /Vnn is for the number of voices to use. The default is
        32 (1-based). You can use any value from 14 to 32. The number
        at the top-middle during play is the number of voices "stolen".
        The less voices, the more likely this will zoom right along.
        The numbers at the top-left are the current MIDI tick-toc, in
        hex and decimal. As for the table, that's for you to guess
        at for now.

        The /Cnnn? is to override the default channels selected. You
        can enter either a hex, binary, or if you can figure it out,
        decimal number here. Hex values must be followed with an "h",
        and binary either a "b" or "y". E.g.:

                /C3FFh  channels 0-9
                /C3F0h  channels 4-9
                /C111b  channels 0-2
                /C1111111b       0-6
                /C1000011111y    0-4,9
                /C01000011111b   0-4,9
                /FFFFh           0-15 (all)
                /-1              may also work as 0-15, maybe not

        At startup the current channel map is shown, just to make sure.

        Pressing Esc at any time exits. The on-board timer is used
        so your system time won't be affected if there are any
        system hangs, etc. The PC timer can also be used, but again,
        no interface set up.

        If there's a problem, the program should tell you the error code
        in deciaml format. The error codes are at the end of the docs.
        Those < 150 or so should be DOS error codes. Higher are Ruckus.
        Just make a note of any problems you have. If you get a lock up,
        try running GMP002.EXE from DEBUG. There's still much debug code
        in there and INT 3 breakpoints around weak areas. If you get a
        break at an INT 3, let me know the address of the break and also
        the MIDI file you used, voices, etc. Had enough talk? Go for it.

    4.  You can contact me through the BBS, preferably in the developer's
        conference, or through my Fido point (Cornel Huth @ 1:387/800.8),
        or via Internet (chuth@lonestar.utsa.edu). As for other cards,
        the SB16 (CSP), PAS-16, Arai-based cards, and a refinement of
        the previous cards supported will also be in the toolkit. I'll
        keep a steady flow of alphas/betas in the conference's download
        area. Just keep me posted on any problems.

    5.  One more thing. GMP002.EXE uses a default program/patch load just
        in case. I've got it set to load patch 0, or ACPIANO.PAT. Yeah, I
        could also post the list of filenames<->patches, but you can
        figure out that (tip: the 2.06 manual has lots of errors). There's
        still some loose ends, and I've got to do some more work on the
        volume mapping (kind of scratchy at times -- maybe that's also
        somewhat related to the loose ends..., anyway).

<Error List:Prelim>

;temporary RM errors
ERR_MIDI_DEVICE         EQU -1

ERR_ILLEGAL_CMD EQU 200
ERR_MIDI_INIT   EQU 210
ERR_MIDI_FORMAT EQU 211
ERR_MIDI_TRACKS EQU 212
ERR_MIDI_TIMING EQU 213
ERR_MIDI_HEADER EQU 214
ERR_MIDI_CHNUM  EQU 215
ERR_NODEVICE    EQU 220
ERR_NOTINGEAR   EQU 223
ERR_INGEAR      EQU 224
ERR_UNKFILE     EQU 225
ERR_NOCHANNEL   EQU 226
ERR_NOXMM       EQU 227
ERR_BADMODE     EQU 228
ERR_INVFMT      EQU 229



ERR_NOT_ENOUGH_MEMORY   EQU 8   ;a DOS error
ERR_UNXEOF      EQU -3          ;unexpected end of file
ERR_DISKFULL    EQU -2          ;disk full

ERR_INVALID_TASK EQU 254        ;most likely just an internal error

ERR_BADPATH     EQU 242         ;path+patchname+ext > MAX_PATHSIZE
ERR_BADENVVAR   EQU 241
ERR_NOMATCH     EQU 240


ERR_PATCHZERO   EQU 235         ;patch number is not allocated/no patch data
ERR_PATCHINUSE  EQU 234         ;patch number is in use (gfPatchAlloc)
ERR_NOCACHE     EQU 233         ;no cache available for patch caching
ERR_BADPATCH    EQU 232         ;patch format not handled
ERR_UNKPATCH    EQU 231             
ERR_BADPATCHNO  EQU 230         ;MIDI patch/drum number out-of-range
    
ERR_VOICERUNNING EQU 224        ;voice is running (cannot unassign; stop first)
ERR_VOICENA     EQU 223         ;voice is not available
ERR_NOVOICE     EQU 222         ;voice is not valid
ERR_INVADDR     EQU 221         ;SetVoiceParm begin/loopstart/loopend invalid
ERR_NODEVICE    EQU 220

ERR_DMA_TIMEOUT EQU 212
ERR_DMA_BADCMD  EQU 211
ERR_DMA_BUSY    EQU 210

ERR_NOMEMORY    EQU 199         ;no/not enough memory from ss$Malloc for MCB
ERR_NOHANDLES   EQU 198         ;no handles left from ss$Malloc for MCB
ERR_MEMCORRUPT  EQU 197         ;memory corrupt from ss$Malloc for MCB
ERR_BADHANDLE   EQU 196         ;handle not valid from ss$Free for MCB/xms$ too

ERR_NOXMSMGR    EQU 189         ;xms$Init called but no XMS manager installed
ERR_XMS16MB     EQU 188         ;XMS allocation crossed 16MB (no-go for ISA DMA)
      

;GF-specific error codes found in gf@error

EGF_INTERNAL    EQU (1 SHL 8)+1                 ;internal coding error                                  
EGF_UNKPATCH    EQU (ERR_BADPATCH SHL 8)+10     ;patch doesn't start w/ GF...
EGF_INSTR_GT1   EQU (ERR_BADPATCH SHL 8)+11     ;more than 1 instrument in patch
EGF_LAYER_GT1   EQU (ERR_BADPATCH SHL 8)+12     ;more than 1 layer in patch
EGF_DATASIZE    EQU (ERR_NOMEMORY SHL 8)+13     ;patch datasize not even-32
EGF_NOMEMORY    EQU (ERR_NOMEMORY SHL 8)+14     ;not enough GRAM for patch
EGF_NOPATCH     EQU (ERR_BADPATCHNO SHL 8)+15   ;patch is not loaded
EGF_VOICEINUSE  EQU (ERR_VOICENA SHL 8) + 16    ;VIB.running<>0 for patch assign        
EGF_NOFREEVOICE EQU (ERR_VOICENA SHL 8) + 17    ;no free voices (patch assign)
EGF_NOMEMVIB    EQU (ERR_NOMEMORY SHL 8)+30     ;DOS mem for VIBs in gfReset

<EOF>