USING I/O MAP OVERLAY FILES IN 22DISK

                         September, 1993

                           Sydex, Inc.
                          P.O Box 5700
                        Eugene, OR  97405

This  document describes using the IOMAP facility in 22DISK.   If 
you are interested in using this facility, you should be familiar 
with 8086 assembly code and have the necessary programming  tools 
to develop a simple DOS .COM-type program.

The  I/O mapping facility allows the programmer to  simulate  the 
activity  of devices seen by the emulated 8-bit  processor.   For 
example, if a CP/M program accesses a serial port, it is possible 
to  write  an  I/O mapping overlay to  simulate  the  8-bit  port 
activity of the serial port.  I/O mapping is supported only  with 
the  software-emulated  processor  modes, not with  the  NEC  V20 
processor hardware emulation.

An IOMAP overlay is nothing more than a simple DOS .COM-type file 
with  a  special header and a file name extension  of  .IOM.   To 
incorporate the overlay into the pre-loader generated by  GENCOM, 
the IOMAP= keyword is used with the name of the overlay file.

The skeleton of an IOMAP overlay is given in the file IOSKEL.ASM.  
Note that the overlay must be coded as a self-relocating program.
The  DS register points to the TPA of the emulated program.   Any 
memory needed by the IOMAP overlay must be explicitly reserved by 
declaring it as initialized data.

The  IOMAP overlay is assumed to have an offset of 0 in the  code 
segment.

For more information on using this facility, please contact Sydex.