CLEANING AND RESPOOLING INSTRUCTIONS
                            Rev 8/93

Now that you realize the necessity of your backups, it's time to
talk about the care and cleaning of your tape backup system. 
Periodic cleaning of the end-of-tape sensor and read/write head
will help to keep your tape drive operating at its peak.  These two
procedures are the only routine maintenance you need to perform.

CLEANING THE END OF TAPE SENSOR and READ/WRITE HEAD
When to Clean 
1.   After every 8 hours of tape operation, approximately 20
     backups or restores.
2.   Or, when dust accumulates.
3.   Or, if a tape comes unspooled.  The end of tape is detected by
     light projected through a series of holes towards the end of
     the tape.  Dust, dirt or smoke blocking this light can cause
     the tape to unspool, or wind to one side of the cartridge. 
     Although the tape can look as if it is damaged beyond repair,
     most tapes can be respooled and often the data will still be
     intact.  Follow the instructions to respool your tape.
4.   Or, when errors occur.  Residue buildup on the read/write head
     can cause the message:  Caution - excessive read errors. Clean
     read/write head -or- Replace tape cartridge to display.

Supplies You Will Need
1.   Aerosol can of compressed air - purchased at an office supply
     or computer store.  CAUTION:  Do not use shop air or air from
     an oil-lubricated compressor.
2.   Sponge-tipped swabs
3.   90% isopropyl alcohol.   CAUTION:  Do not use cotton swabs as
     they may leave behind fibers that can amage the read/write
     head.  Do not use rubbing alcohol or any abrasive to clean the
     head or apply a lubricant to any part of the drive.
                     
To Clean the End-of-Tape Sensor and Read/Write Head
1.   Turn off the computer.
2.   Hold open the tape drive door.
3.   Note the location of the sensor and read/write head.  They are
     approximately 2 inches back from the door.
4.   Use the can of compressed air to blow the dust away from the
     two areas.
                              or
     Dip a sponge-tipped swab in 90% isopropyl alcohol and rub the
     swab back and forth over the sensor and read/write head in the
     direction of tape motion several times until it is shiny.
5.   Let the read/write head dry completely before using the tape
     drive.


                   RESPOOLING A TAPE CARTRIDGE

Your investment in tapes for your backup system is appreciated!  To
retrieve tapes that have come unspooled, follow the outlined
procedure that follows.  PLEASE READ THOROUGHLY BEFORE ATTEMPTING
THIS PROCEDURE!

1.   Remove the two or three screws from the cartridge base plate.
2.   Place the cartridge on a flat surface in a clean area.  While
     firmly holding the metal base plate with one hand, carefully
     remove the cover.  It may be helpful to hold the door of the
     tape down as it remains with the base plate.
3.   Locate and carefully free the loose end of the tape.  Wind all
     but approximately 3-4 inches of tape on the full spool.
4.   Thread the tape through its designated tape path using a fully 
     assembled cartridge as a model.  The tape must be routed
     around the tape guides, in the front of the tape capstan, and
     in front of the guide pin next to the drive capstan.  Be
     certain that hands are clean.  CAUTION:  DO NOT allow any of
     the cartridge components to lose their position as they can be
     difficult to reposition properly.
5.   Moisten the backside of the tape with freon or water and
     attach to the empty tape hub.  Turn the capstan a couple of
     turns counter-clockwise until the tape is secure on the empty
     tape hub.  Make sure the tape clings to the tape hub rather
     than traveling toward the tape capstan.
     On some tapes it may be necessary to hold a finger on the top
     of the tape hub to prevent the tape from riding up on the hub.
6.   Hold one tape hub securely and turn the other slightly to
     remove the slack in the tape.
7.   Use a pointed object, such as a pen, to turn the belt capstan
     counter-clockwise and watch for a set of two holes in the
     tape.  NOTE:  Some tapes may unspool at the end of the tape
     rather than the beginning, making it necessary to turn the
     belt capstan in a clockwise direction.  The first set of holes
     should be about 12 inches (about 8 turns of the capstan) into
     the tape.
     Another 12 inches should reveal a second set of two holes and,
     finally, a single hole should appear approximately 36 inches
     (23 turns of the capstan) from the end of the tape.  The tape
     is wound sufficiently when this single hole becomes visible.
8.   Make sure that the mirror is pushed all the way down on its
     mounting posts then carefully replace the cover on the base
     plate.  Insert the screws in the base plate to complete the
     assembly.

To get a diagram showing the parts listed in the above
instructions, please call our QICFAX service and request document
#2020.