The PC Assembler Tutor                                        114
             ______________________

             We can consolidate all this information into the following list:

                 All the following addressing modes can be used with or
                 without a constant:

                 variable_name  (+constant)
                 [bx]     (+constant)
                 [si]     (+constant)
                 [di]     (+constant)
                 [bp]     (+constant)
                 [bx+si]  (+constant)
                 [bx+di]  (+constant)
                 [bp+si]  (+constant)
                 [bp+di]  (+constant)

                 This is a complete list.

             Thus, you can access a variable by name or with one of the eight
             pointer combinations. There are no other possibilities.


             One thing that may confuse you about an addressing statement is
             all the plusses and minuses. As an example:

                 mov  cx, -45+27[bx+22]+[-195+di]+23-44

             the total address is:

                 -45+27[bx+22]+[-195+di]+23-44

             When the 8086 performs this instruction, it will ADD (1) BX (2)
             DI and (3) a single constant. That single constant can be a
             positive or a negative number; the 8086 will ADD all three
             elements. The '+' in front of  'di' is for convenience of the
             assembler only;  [-195-di] is illegal and the assembler will
             generate an error. If you actually want the negative of what is
             in one of the registers, you must negate it before calling the
             addressing instruction:

                 neg  di
                 mov  cx, -45+27[bx+22]+[-195+di]+23-44

             once again, the only allowable forms are +[di], [di] or [+di].
             Either -[di] or [-di] will generate an assembler error. 


             If you ever see a technical description of the addressing modes,
             you will find a list of 24 different machine codes. The reason
             for this is that:

                      [bx]
                      [bx] + byte constant
                      [bx] + word constant

             are three different machine codes. Here is a listing of the same
             machine instruction with the three different styles:






             Chapter 11 - Addressing Modes                                 115
             _____________________________


                 MACHINE CODE             ASSEMBLER INSTRUCTION

                  03 04                     add   ax, [si] 
                  03 44 1B                  add   ax, [si+27] 
                  03 44 E5                  add   ax, [si-27] 
                  03 84 5BA7                add   ax, [si+23463] 
                  03 84 A459                add   ax, [si-23463] 


             (27d = 1Bh , 23463d = 5BA7h). The first byte of code (03) is the
             add (word) instruction. The second byte is the addressing code,
             and the third and fourth bytes (if any) are the constant (in
             hex). Addressing code 04 is:  (ax, [si]). Addressing code 44 is: 
             (ax, [si] + byte constant). Addressing code 84 is:  (ax, [si] +
             word constant). The fact that there are three different machine
             codes is of concern to the assembler, not to you. It is the
             assembler's job to make the machine code as efficient as
             possible. It is your job to write quality, robust code.


             SEGMENT OVERRIDES

             So far, we haven't talked about segment registers. You will
             remember from the last chapter that the 8086 assumes that a named
             variable is in the DS segment:

                 mov  ax, variable1

             If it isn't, the Microsoft assembler puts the correct segment
             override in the machine code. The segment overrides are:

                 SEGMENT OVERRIDE         MACHINE CODE (hex)
                      CS                       2E
                      DS                       3E
                      ES                       26
                      SS                       36

             As an example:

                 MACHINE CODE        ASSEMBLER  INSTRUCTIONS

                 2E: 03 06 0000 R      add   ax, variable3 
                 26: 2B 1E 0000 R      sub   bx, variable2 
                 31 36 0000 R          xor   variable1, si ; no override
                 36: 21 3E 00C8 R      and   variable4, di 

             when the different variables were in segments with different
             ASSUME statements. If you don't remember this, you should reread
             the section on overrides in the last chapter. Remember, the colon
             is in the listing only to tell you that we have a segment
             override. The colon is not in the machine code.










             The PC Assembler Tutor                                        116
             ______________________

             What about pointers? The natural segment for anything with [bp]
             is SS, the stack segment.{1}  Everything else has DS as its
             natural segment. The natural segments are:

                 (1) DS

                      variable + (constant)
                      [bx] + (constant)
                      [si] + (constant)
                      [di] + (constant)
                      [bx+si] + (constant)
                      [bx+di] + (constant)


                 (2) SS

                      [bp] + (constant)
                      [bp+si] + (constant)
                      [bp+di] + (constant)

             where the constant is always optional. Can you use segment
             overrides? Yes, in all cases.{2}  Here is some assembler code
             along with the machine code which was generated.


                 MACHINE CODE             ASSEMBLER INSTRUCTIONS
                                      
                  26: 03 07                 add   ax, es:[bx] 
                  2E: 01 05                 add   cs:[di], ax 
                  36: 2B 44 11              sub   ax, ss:[si+17] 
                  2E: 29 46 00              sub   cs:[bp], ax 
                  3E: 33 03                 xor   ax, ds:[bp+di] 
                  26: 31 02                 xor   es:[bp+si], ax 
                  26: 89 43 16              mov   es:[bp+di+22], ax 
              
              
                  03 04                     add   ax, [si] 
                  03 44 1B                  add   ax, [si+27] 
                  03 84 A459                add   ax, [si-23463] 
                  26: 03 04                 add   ax, es:[si] 
                  26: 03 44 1B              add   ax, es:[si+27] 
                  26: 03 84 A459            add   ax, es:[si-23463] 


             (17d = 11h, 22d = 16h, 27d = 1Bh, -23463d = 0A459h). The first
             number (which is followed by a colon) is the segment override
             that the assembler has inserted in the machine code. Remember,
             the colon is in the listing to inform you that an override is
             ____________________

                1 We will see why when we look at subroutines. BP is called
             the base pointer [bp] and is used in a special way.

                2 There are some special instructions for two independent
             pointers which we will cover at the end of the book. These allow
             segment overrides but force the override to refer to the first
             pointer.





             Chapter 11 - Addressing Modes                                 117
             _____________________________

             involved; it is not in the machine code itself.
                                       
             Unfortunately, when you use pointers you must put the override
             into the assembler instructions yourself. The assembler has no
             way of knowing that you want an override. This can cause some
             truly gigantic errors (if you reference a pointer seven times and
             forget the override once, the 8086 will access the wrong segment
             that one time), and those errors are extremely difficult to
             detect.

             As you can see from above, you put the override in the
             instructions by writing the appropriate segment (CS, DS, ES or
             SS) followed by a colon. As always, it is your responsibility to
             make sure that the segment register holds the address of the
             appropriate segment before using an override. 


             We have talked about two different types of constants in the
             chapter, a constant which is part of the address:

                 mov  ax, [bx+17]
                 add  [si+2190], dx
                 and  [di-8179], cx

             and a constant which is a number to used for an arithmetical or
             logical operation:

                 add  ax, 17
                 sub  dl, 45
                 add  dx, 22187

             They are both part of the machine instruction, and are
             unchangeable (true constants). This machine code is going to be
             difficult to read, so just look for (1) the constant DATA and (2)
             the constant in the ADDRESS. All constants in the assembler
             instructions are in hex so that they look the same as in the
             listing of the machine code. Here's a listing of different
             combinations.


             1. Pointer + constant as an address:

                 MACHINE CODE             ASSEMBLER INSTRUCTIONS
                  01 44 1B                  add   [si+1Bh], ax 
                  29 85 0A04                sub   [di+0A04h], ax 
                  30 5C 1F                  xor   [si+1Fh], bl 
                  20 9E 1FAB                and   [bp+1FABh], bl 
              
             2. Arithmetic instruction with a constant:

                 MACHINE CODE             ASSEMBLER INSTRUCTIONS
                  05 1065                   add   ax, 1065h 
                  2D 6771                   sub   ax, 6771h 
                  80 F3 37                  xor   bl, 37h 
                  80 E3 82                  and   bl, 82h 
              
             3. Pointer + constant as an address; arithmetic with a constant





             The PC Assembler Tutor                                        118
             ______________________


                 MACHINE CODE             ASSEMBLER INSTRUCTIONS
                  81 44 1B 1065             add   [si+1Bh], 1065h 
                  81 AD 0A04 6771           sub   [di+0A04h], 6771h 
                  80 74 1F 37               xor   [si+1Fh], BYTE PTR 37h 
                  80 A6 1FAB 82             and   [bp+1FABh], BYTE PTR 82h 
              

             You will notice that the ADD instruction (as well as the other
             instructions) changes machine code depending on the complete
             format of the instruction (byte or word? to a register or from a
             register? what addressing mode? is AX one of the registers?).
             That's part of the 8086 machine language encoding, and it makes
             the 8086 machine code extremely difficult to decipher without a
             table listing all the options.


             OFFSET AND SEG

             There are two special instructions that the assembler has -
             offset and seg. For any variable or label, offset gives the
             offset from the beginning of the segment, and seg gives the
             segment address. If you write:

                 mov  ax, offset variable1

             the assembler will calculate the offset of variable1 and put it
             in the machine code. It also signals the linker and loader; if
             the linker should change the offset during linking, it will also
             adjust this number. If you write:

                 mov  dx, seg variable1

             The assembler will signal to the linker and the loader that you
             want the address of the segment that variable1 is in. The linker
             and loader will put it in the machine code at that spot. You
             don't need to know the name of the segment. The linker takes care
             of that. We will use the seg operator later. 


             LEA

             LEA (load effective address) is a completely different animal. It
             allows you to use any addressing mode to put an address in a
             register. One of the addressing modes covered before was for the
             following code:

                           xor  dx, 45+[di+23][bx+15]-94

             The 8086 added DI, BX and the constant to calculate the address.
             It then XOR'ed the variable at that address with DX. If you
             write:

                           lea  dx, 45+[di+23][bx+15]-94

             the 8086 will add DI, BX and the constant to calculate the
             address. It will then put the ADDRESS in DX. LEA can use any





             Chapter 11 - Addressing Modes                                 119
             _____________________________

             addressing mode to calculate an address. The machine code looks
             almost the same:

                 MACHINE CODE                  ASSEMBLER INSTRUCTIONS

                  33 51 F5                  xor dx, 45+[di+23][bx+15]-94 
                  8D 51 F5                  lea dx, 45+[di+23][bx+15]-94 

             The first byte of the machine code is the instruction and the
             second and third byte are the addressing mode.

             You almost never need LEA. It is slower than:

                 mov  dx, offset variable1

             However, when the addressing gets complicated (perhaps 1% of the
             time), it's nice to have. Remember, it will calculate ANY 8086
             addressing mode.

             Let's run a program so we can see what actually happens with LEA

             ;lea.asm
             ; + + + + + + + + + + + + + + + START DATA BELOW THIS LINE 
             variable1 dw ? 
             ; + + + + + + + + + + + + + + + END DATA ABOVE THIS LINE 

             ; + + + + START CODE BELOW THIS LINE 
                    ; reg style 
                    mov   si_byte, 1   ; signed 
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   bp, 0  ; clear unused registers  
                    mov   di, 0 
                 
                   ;lea and mov show the two ways to address variable1
                    lea   ax, variable1  ; effective address 
                    mov   bx, offset variable1  ; offset 
                    call  show_regs_and_wait 
              
             lea_loop: 
                    mov   si, 0  ; clear registers 
                    mov   dx, 0 
                    mov   cx, 0 
                    mov   bx, 0 
                    mov   ax, 0 
                    call  show_regs 
              
                    call  get_unsigned ; unsigned for bx 
                    mov   bx, ax 
                    mov   ax, 0   ; blank ax 
                    call  show_regs 
              
                    call  get_signed ; signed for si 
                    mov   si, ax 
              
                    mov   ax, 0   ; blank ax 





             The PC Assembler Tutor                                        120
             ______________________

                    lea   cx, [bx+si]+100      ; addresses to cx and dx
                    lea   dx, [si+bx-100]
                    call  show_regs_and_wait 
              
                    jmp   lea_loop 
              ; + + + + END CODE ABOVE THIS LINE 

             The first part of the program shows that LEA and MOV give the
             same offset address. Then we enter the loop. It gets an unsigned
             number, puts it in BX, gets a signed number, puts it in SI, then
             uses LEA to calculate [bx+si+100] and [bx+si-100]. The plus and
             minus 100 is simply to show you a difference of 200 in the two
             results. BX and SI could also have contained (1) both signed
             numbers or (2) both unsigned numbers. It doesn't make any
             difference. This program has a signed and an unsigned number for
             variety. Of special interest to you shold be when [bx+si] is
             within 100 of 65536 (or 0). One of the results will be > 0 while
             the other result will be < 65536  The address value wraps around
             from 65535 -> 0. Note that with minor alteration, this program
             can be used to look at ANY addressing mode that uses pointers.  

             You should make two executable files for this. First:

                 link  lea+asmhelp

             and the second:

                 link asmhelp+lea

             Give them different names and run them. Note the offset values
             for:

                 lea  ax, variable1
                 mov  bx, offset variable1

             With lea+asmhelp you should have an offset of 8 for variable1
             since there are 8 bytes in the array (ax_byte, bx_byte, etc.).
             This array appears before variable1 in the data segment. When you
             link it the other way (asmhelp+lea), all the data for asmhelp.obj
             is in front of your data and the offset should be something
             completely different for variable1.





















             Chapter 11 - Addressing Modes                                 121
             _____________________________

                                        SUMMARY

             These are the natural (default) segments of all addressing modes:

                 (1) DS

                      variable + (constant)
                      [bx] + (constant)
                      [si] + (constant)
                      [di] + (constant)
                      [bx+si] + (constant)
                      [bx+di] + (constant)


                 (2) SS

                      [bp] + (constant)
                      [bp+si] + (constant)
                      [bp+di] + (constant)

             Where the constant is optional. Segment overrides may be used.
             The segment overrides are:

                 SEGMENT OVERRIDE         MACHINE CODE (hex)
                      CS:                      2E
                      DS:                      3E
                      ES:                      26
                      SS:                      36


             OFFSET

             The reserved word 'offset' tells the assembler to calculate the
             offset of the variable from the beginning of the segment.

                      mov  ax, offset variable2


             SEG

             The reserved word 'seg' tells the assembler, linker and loader to
             get the segment address of the segment that the variable is in.

                      mov  ax, seg variable2

             LEA

             LEA calculates an address using any of the 8086 addressing modes,
             then puts the address in a register.

                      lea  cx, [bp+di+27]