122


                          CHAPTER 12 - MULTIPLE WORD ARITHMETIC I


             Let's review the LOOP instruction. We often want to repeat an
             action a specific number of times. In a FOR loop, we write:

                 FOR I = 1, 10

             That means we want to repeat the code that follows ten times. The
             8086 has an instruction for this, called the loop instruction. It
             looks like this:

                 mov  cx, 10
             label17:
                 ...
                 (a bunch of code)
                 ...
                 loop label17

             The count MUST be in the CX register. This is the only register
             you can use for this. When the machine sees the loop instruction,
             it decrements the CX register by one, LEAVING ALL FLAGS ALONE,
             and if the result is not zero, it loops back to the label. If the
             result is zero, it falls through the loop. One problem we might
             have with this instruction is if you enter it with CX = 0, it is
             going to loop 65,536 times. Intel provided a second instruction
             to avoid this - JCXZ (jump if CX is zero). You put it right
             before the loop for insurance.

                 jcxz label19
             label17:
                 ...
                 (a bunch of code)
                 ...
                 loop label17
             label19:

             Obviously, in our first example this instruction is not necessary
             because we set CX to 10 just before entering the loop.



             If you have seen the list of 8086 instructions, you will have
             noticed lots of strange looking add and subtract instructions.
             Why are they there? In this chapter we will look at ADC and SBB.
             The others will come in later chapters. 

             How do engineers decide what a reasonable size for a number is?
             When they started making 8 bit machines (the maximum unsigned
             number is 255) did they go out on the streets and take a poll to
             find out if 255 was the maximum number that people used?  No,
             they didn't even think about what people needed. It was a
             question of what the technology would allow at that time.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 12 - Multiple Word Arithmetic I                       123
             _______________________________________

             Similarly, at the time the 8086 was engineered, 16 bits was
             pushing the limits of the technology. But 65,535 doesn't really
             cut the mustard. If those are 65,535 pennies, that isn't even
             your yearly food bill, let alone the cost of housing.

             The 8086 instructions give us the option of making integers of
             whatever size we want. Because it is done in software, it is
             slower, but if we are doing thousands or tens of thousands of
             additions instead of hundreds of thousands or millions, it won't
             be a great inconvenience.{1} 

             ASMHELP.OBJ is set up to input 2 word (4 byte) and 4 word (8
             byte) numbers so those are what we are going to use. 4 byte
             numbers are up to +/- 2 billion and 8 byte numbers are up to
             9X10exp18. Those should be large enough. 

             The first instruction is ADC, add with carry. When you add by
             hand, you add everything in the right column, then carry to the
             next column left, repeating this over and over. We don't need to
             do it column by column, but it is necessary to do it word by
             word. In the data section we need:

             variable1  dq  ?
             variable2  dq  ?

             and the code for a 4 word (8 byte) addition is the following:

                 lea  si, variable1
                 lea  di, variable2
                 mov  ax, [di]                 ; first addition
                 add  [si], ax
                 pushf                    ; save the flags
                 mov  cx, 3 
                 add  si, 2               ; go to next higher word
                 add  di, 2

             long_add_loop:               ; next three additions
                 mov  ax, [di]
                 popf                     ; restore the flags
                 adc  [si], ax
                 pushf                    ; save the new flags
                 add  di, 2
                 add  si, 2
                 loop long_add_loop

                 popf                     ; pop the flags off the stack


             ADC is the same as ADD, but it looks at the carry flag - if the
             carry flag is 1, it adds 1 to the result; if the carry flag is
             zero, it does nothing to the result. This works for both signed
             and unsigned numbers. If you don't believe it, you should go back
             ____________________

                1 As a benchmark, it took a moderately slow PC 6.5 seconds to
             do 100,000 eight byte additions. The same PC can do over a
             million two byte additions in 6 seconds.





             The PC Assembler Tutor                                        124
             ______________________

             to the introductory chapter with the base 10 machine and look at
             long additions.

             Notice PUSHF and POPF. These are special instructions called push
             flags and pop flags. Rather than pushing an arithmetic register
             on the stack, pushf pushes the register containing the flags.
             Popf pops them back into the flags register. This is necessary
             because ADC looks at the carry flag and the ADD instructions in
             the loop:

                 add  di,2
                 add  si,2

             might change the carry flag. The last POPF after the loop is to
             get it off the stack (anything we put on the stack we need to
             take off the stack).

             The first addition is a normal addition, the last three take the
             carry into account. We are moving the pointers a word at a time.
             Because the 8086 doesn't allow both operands to be in memory, we
             need to move one into a register. After the addition is
             performed, the result is in memory. We can discard what is in the
             register. 

             Notice that the first half of the code looks almost the same as
             the code inside the loop. If we could only use ADC instead of
             ADD, we could put the first addition inside the loop. It is
             possible to do this. There is another instruction, CLC, which
             clears the carry flag. Recall that if the carry flag is 0, ADC
             does nothing different from ADD. Therefore, we can have:

                 lea  si, variable1
                 lea  di, variable2
                 mov  cx, 4               ; 4 additions in loop
                 clc                      ; set cf to zero
                 pushf                    ; save the flags

             long_add_loop:
                 mov  ax, [di]            ; word to a register
                 popf                     ; restore the flags
                 adc  [si], ax            ; register + memory
                 pushf                    ; save the flags
                 add  di, 2
                 add  si, 2
                 loop long_add_loop

                 popf                     ; pop the flags off the stack

             It's the same code. The number of loops was increased from 3 to
             4, and the carry flag was cleared to insure that the first
             addition would have nothing extra added. Here is the basic
             program.

             ; - - - - - PUT DATA BELOW THIS LINE
             variable1  dq  ?
             variable2  dq  ?
             ; - - - - - PUT DATA ABOVE THIS LINE





             Chapter 12 - Multiple Word Arithmetic I                       125
             _______________________________________


             ; - - - - - PUT CODE BELOW THIS LINE

                 call  show_regs

             outer_loop:
                 lea  ax, variable1            ; get the variables
                 call get_signed_8byte
                 call print_signed_8byte
                 lea  ax, variable2
                 call get_signed_8byte
                 call print_signed_8byte

                 lea  si, variable1            ; set the pointers
                 lea  di, variable2
                 mov  cx, 4                    ; loop 4 times (4 words)
                 clc                           ; clear the cf
                 pushf                         ; save the flags

             long_add_loop:
                 mov  ax, [di]            ; word to a register
                 popf                     ; restore the flags
                 adc  [si], ax            ; register + memory
                 pushf                    ; save the flags
                 add  di, 2
                 add  si, 2
                 loop long_add_loop

                 popf                     ; restore the flags

                 lea  ax, variable1
                 call print_signed_8byte

                 jmp  outer_loop

             ; - - - - - PUT CODE ABOVE THIS LINE

             The calls to get_signed_8byte are followed by print_signed_8byte.
             This is so you can see what you have actually typed in. It will
             be neat and with commas, so it will be much easier to read.
             Everything else is the same as before.

             As an aside, let's talk about commas. Though we can get along
             without commas if we have a 4 digit number, There is no reason to
             do without them when using larger numbers. I find printer output
             that has 15 digit floating point numbers without commas not only
             hard to read but also silly. It's not that the computer is
             incapable of putting in commas, it's that the prople who wrote
             the programs couldn't be bothered with doing 2 hours of work to
             save the users lots and lots of aggrivation. Therefore, for all
             large number input (that is, larger than 1 word)  you can use
             commas. They don't even have to be in the right place, the
             computer ignores them. All the following are the same number:

                 723469746
                 723,4,69746
                 72,3,46974,6





             The PC Assembler Tutor                                        126
             ______________________

                 7,2,3,4,6,9,7,4,6
                 723,469,746

             The program strips all commas out of the line and then looks at
             the input. All large output has the commas in the right spot. In
             order to enlist you in the crusade to stamp out unreadable input
             and output, the summary at the end of this chapter has the C code
             necessary for stripping commas. This is my contribution to world
             culture.

             If you have played with the signed addition program, all we need
             to do to make it unsigned is to change all the get_signed_8byte
             calls to get_unsigned_8byte calls. Change the print calls to
             unsigned also. Run the program.

             Now, let's try subtraction. How much code do we have to alter to
             make it a subtraction program? The answer is - one word. Just
             change the ADC (add with carry) to SBB (subtract with borrow).
             SBB learns from the CF flag whether the last subtraction had to
             borrow, and tells the next subtraction via the CF flag whether it
             has had to borrow. Change it, and try it out. (Yes, really do it,
             don't just pretend that you are going to do it). 

             Why does this program work with exactly 8 bytes? Because we tell
             the loop via CX that it is 4 words long. If we put 2 in CX, the
             loop will think that the number is 2 words (4 bytes) long, and if
             we put 17 in CX, the loop will think that the number is 17 words
             (34 bytes) long. In fact, this little snippet of code can do
             either signed or unsigned addition or subtraction of any number
             of words simply by altering one number and one word of code. 

             The code as it stands has only one shortfall. Remember from our
             earlier subtraction that we might want to have an INTO (interrupt
             on overflow) instruction after signed addition and subtraction.
             It needs to be after the last addition (or subtraction). All we
             need to do is put it after the POPF just below the loop. At this
             point the flags show the condition right after the last addition
             or subtraction:

                 loop long_add_loop

                 popf                ; pop the flags off the stack
                 into                ; interrupt if overflow is set


















             Chapter 12 - Multiple Word Arithmetic I                       127
             _______________________________________

                                       SUMMARY


             ADC (add with carry) is used for multiple word arithmetic. It
             adds two numbers along with plus the value in CF, the carry flag
             (1 if the flag is set and 0 if the flag is cleared). CLC (clear
             the carry flag) should be used to clear CF before the first
             addition. After the addition, the flags register should be pushed
             in order to store CF unless it is certain that CF will not be
             effected by the rest of the loop.

                 popf
                 adc  [di], ax
                 pushf



             SBB (subtract with borrow) is used for multiple word arithmetic.
             It subtracts one number from the other and subtracts the value in
             CF to account for any borrows from the right. CLC (clear the
             carry flag) should be used to clear CF before the first
             subtraction. After the subtraction, the flags register should be
             pushed in order to store CF unless it is certain that CF will not
             be effected by the rest of the loop.

                 popf
                 sbb  [di], ax
                 pushf

             These operations have the typical 5 possibilities:

                 1) register, register
                 2) register, memory
                 3) memory, register
                 4) memory, constant
                 5) register, constant



             You may manually control the value in CF with STC and CLC. STC
             (set the carry flag) sets the value to 1, while CLC (clear the
             carry flag) sets the value to 0. These are used for initial
             settings of multiple word operations.


             In order to store the values in the flags register you use PUSHF
             (push the flags) until you need them again. At that time you can
             get them back with POPF (pop the flags).














             The PC Assembler Tutor                                        128
             ______________________

                             STRIPPING COMMAS IN C

             In order to get rid of commas, you need some discipline in what
             kind of data entry you have. Specifically, you can't enter large
             numbers on the same line as text strings because text strings are
             likely to have commas that should be kept. This is hardly a major
             restriction. You can have as many numbers as you want on the same
             line since in C you must have whitespace between pieces of data.

             We will take all commas out of the line. You can retrofit most
             old programs with almost no change. 

             The only time that you need this capability is if you are getting
             something from the keyboard, and what you probably have in the
             program is:

                 scanf ( "format string", variables );

             The method is (1) import a text string as a single string, (2)
             strip the commas, and (3) use sscanf instead of scanf.

                 char buffer[80] ;

                 fgets (buffer, 80, stdin) ;
                 strip_commas (buffer);
                 sscanf (buffer, "format string", variables) ;

             Both "format string" and the variables remain unchanged when you
             switch from scanf to sscanf. You might want to check for EOF with
             fgets.

             Heres the program:

             strip_commas (buffer)
             char   *buffer ;
             {
                 char *ptr1, *ptr2 ;

                 ptr1 = ptr2 = buffer ;
                 while (1)
                 {
                      if ( *ptr2 == ',')  /* skip commas */
                      {
                           ptr2++ ;
                           continue ;
                      }
                      /*move, increment, and check for 0 */
                      if (!(*ptr1++ = *ptr2++))   /* this is '=', not '==' */
                           break ;
                 }
                 return ;
             }