170

                   CHAPTER 16 - LONG SIGNED MULTIPLICATION AND DIVISION


             Now that you have some subroutines under your belt, it is time to
             get back to multiple word arithmetic. This was put on the back
             burner because we needed to negate long numbers and it is more
             efficient to do that as a subroutine. First, let's negate a long
             number and then put the parts together.

             To negate a number you complement it, then add 1. It looks like
             this:

                 NUMBER_LENGTH  EQU 4

                 variable1 dq   ?

                      mov  si, offset variable1
                      mov  cx, NUMBER_LENGTH
                 not_loop:
                      not  WORD PTR [si]
                      add  si, 2
                      loop not_loop

                      mov  si, offset variable1
                      mov  cx, NUMBER_LENGTH
                      stc                      ; set carry flag
                 add_loop:
                      adc  WORD PTR [si], 0
                      inc  si
                      inc  si
                      loop add_loop

             This is straightforward. First negate, then add 1. The first add
             will add 1 because the carry flag is set. If there is a carry
             out, it will be taken care of in the next word with ADC (we add
             nothing but the carry). We can make this more compact and
             efficient with:

                      mov  si, offset variable1
                      mov  cx, NUMBER_LENGTH
                      stc                      ; set carry flag
                 negate_loop:
                      not  WORD PTR [si]
                      adc  WORD PTR [si], 0
                      inc  si
                      inc  si
                      loop negate_loop

             Neither NOT nor INC effect CF, the carry flag, so the correct CF
             value will be propagated through the whole long number. 


             When we do negation during our multiplication, the multiplicand
             will be a 4 word negation while the result will be a 5 word

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 16 - Multiple Word Arithmetic III                     171
             _________________________________________

             negation, so we will pass the length as a parameter. The call in
             C would look like this:

                 negate_it ( &number, length ) ; {1}

             On entry, the stack will look like this:

                           length    bp + 6
                           address   bp + 4
                           old IP    bp + 2
                 bp   ->   old BP    bp + 0

             Here is the entire subroutine:

             ; - - - - - START SUBROUTINES BELOW THIS LINE
             negate_it proc near

                 NUMBER_LENGTH  EQU [bp+6]
                 NUMBER_ADDRESS EQU [bp+4]

                 push bp
                 mov  bp, sp
                 PUSHREGS cx, si


                 mov  si, NUMBER_ADDRESS
                 mov  cx, NUMBER_LENGTH
                 stc                      ; set carry flag
             negate_loop:
                 not  WORD PTR [si]
                 adc  WORD PTR [si], 0
                 inc  si
                 inc  si
                 loop negate_loop

                 POPREGS cx, si
                 pop  bp
                 ret                 ; calling routine adjusts stack

             negate_it endp

             ; - - - - - END SUBROUTINES ABOVE THIS LINE

             Well, so far we have the negation routine and the unsigned
             multiplication and division routines. What else is necessary?
             Only the main program, and here it is for multiplication:

             ; - - - - - START DATA BELOW THIS LINE
             multiplicand       dq   ?
             multiplier         dw   ?
             result             dt   ?
             result_sign_flag   db   ?
             ; - - - - - END DATA ABOVE THIS LINE

             ____________________

                1. For you non-C people, the '&' stands for the address.





             The PC Assembler Tutor                                        172
             ______________________

             ; - - - - - START CODE BELOW THIS LINE
             outer_loop:
                 mov  result_sign_flag, 0      ; assume positive
                 mov  ax, offset multiplicand
                 call get_signed_8byte

                 test WORD PTR multiplicand + 6, 8000h   ; is it negative ?
                 jz   get_next_number

                 mov  ax,4                     ; negate 4 word number
                 push ax
                 mov  ax, offset multiplicand
                 push ax
                 call negate_it
                 add  sp, 4                    ; clear 2 pushes off stack
                 not  result_sign_flag         ; reverse sign of result

             get_next_number:
                 call get_signed               ; get signed multiplier
                 mov  multiplier, ax
                 test ax, 8000h                ; is it negative
                 jz   do_the_multiplication

                 neg  multiplier               ; negate
                 not  result_sign_flag         ; reverse sign of result

             do_the_multiplication:
                 mov  ax, offset result
                 push ax
                 mov  ax, multiplier      ; the number, not the address
                 push ax
                 mov  ax, offset multiplicand
                 push ax
                 call multiply_it
                 add  sp, 6                    ; clear 3 pushes off stack

                 ; is the result negative?
                 test result_sign_flag, 0FFh   ; 1111 1111 mask
                 jz   print_it

                 mov  ax, 5                    ; 5 word result
                 push ax
                 mov  ax, offset result
                 push ax
                 call negate_it
                 add  sp, 4                    ; clear 2 pushes off stack

             print_it:
                 mov  ax, WORD PTR result + 8  ; top two bytes
                 call print_hex
                 mov  ax, offset result        ; the rest of result
                 call print_signed_8byte

                 jmp  outer_loop
             ; - - - - - END CODE ABOVE THIS LINE

             The driver routine gets an 8 byte signed number. If the number is





             Chapter 16 - Multiple Word Arithmetic III                     173
             _________________________________________

             negative it negates the number (to make it positive) and switches
             the sign of the result_sign_flag. The sign flag will either be
             00h for positive or FFh for negative. It then gets a two byte
             signed number. If it is negative, the routine negates it and
             switches the sign flag. At this point both numbers are positive,
             so it calls the unsigned multiplication routine. At the end, it
             checks the result_sign_flag to see if the result should be
             positive or negative. If it should be negative, the routine calls
             negate_it one more time. Finally, the routine prints the number.
             The hex portion will be 0000 for positive or FFFF for negative
             unless the value is larger than an 8 byte signed number can hold,
             at which point the value of the 8 byte signed number will be
             incorrect.

             Here's the unsigned multiplication routine which has been turned
             into a subroutine:

             ; - - - - - 
             multiply_it proc near

                 RESULT_ADDRESS           EQU  [bp+8]
                 MULTIPLIER_VALUE         EQU  [bp+6]
                 MULTIPLICAND_ADDRESS     EQU  [bp+4]

                 push bp
                 mov  bp, sp
                 PUSHREGS  ax, bx, cx, dx, si, di

                 mov  si, MULTIPLICAND_ADDRESS ; load pointers
                 mov  bx, RESULT_ADDRESS

                 mov  cx, 4          ; number of words
                 sub  di,di          ; clear di 

             mult_loop:
                 mov  ax, [si]       ; multiplicand to ax
                 mul  WORD PTR  MULTIPLIER_VALUE
                 add  ax, di         ; add high word from last multiplication
                 jnc  store_result
                 inc  dx
             store_result:
                 mov  [bx], ax       ; store 1 word of result.
                 mov  di, dx         ; save high word for next multiplication
                 add  si, 2          ; increment pointers
                 add  bx, 2
                 loop mult_loop

                 mov  [bx], di       ; move last word of result

                 POPREGS   ax, bx, cx, dx, si, di
                 pop  bp
                 ret                 ; calling routine adjusts stack

             multiply_it endp
             ; - - - - - - - - - - - 

             Draw a picture of the stack to verify that the EQU values are





             The PC Assembler Tutor                                        174
             ______________________

             correct. The multiplication and the negation subroutines go in
             the subroutine section of SUBTEMP1.ASM. The driver routine is the
             main routine. If you don't remember how this multiplication
             routine works, go back to the chapter on unsigned multiple word
             multiplication since the code is the same.



             DIVISION

             Division is the same situation. We need a driver routine, but the
             division itself will be the unsigned division. In division, the
             remainder is the same sign as the dividend, and the sign of the
             quotient is (dividend_sign XOR divisor_sign). If both signs are
             the same, the quotient is positive; if the signs are different
             the quotient is negative. Here's the driver routine:

             ; - - - - - START DATA BELOW THIS LINE 
             dividend                dq  ? 
             divisor                 dw  ? 
             quotient                dq  ? 
             remainder               dw  ? 
             quotient_sign_flag      db  ? 
             remainder_sign_flag     db  ? 
             ; - - - - - END DATA ABOVE THIS LINE 

             ; - - - - - START CODE BELOW THIS LINE 
             outer_loop: 
                    mov   quotient_sign_flag, 0            ; assume positive
                    mov   remainder_sign_flag, 0 

                    mov   ax, offset dividend 
                    call  get_signed_8byte 
                    test  WORD PTR (dividend + 6), 8000h   ; is it negative?
                    jz    get_next_number 
              
                    mov   ax,4                      ; negate 4 word number 
                    push  ax 
                    mov   ax, offset dividend 
                    push  ax 
                    call  negate_it 
                    add   sp, 4                     ; adjust stack 
                    not   quotient_sign_flag        ; switch sign of quotient
                    mov   remainder_sign_flag, 0FFh ; remainder is negative 
              
             get_next_number: 
                    call  get_signed 
                    mov   divisor, ax 
                    test  ax, 8000h                 ; is it negative 
                    jz    do_the_division 
              
                    neg   divisor 
                    not   quotient_sign_flag       ; switch sign of quotient
              
             do_the_division: 
                    mov   ax, offset remainder 
                    push  ax 





             Chapter 16 - Multiple Word Arithmetic III                     175
             _________________________________________

                    mov   ax, offset quotient 
                    push  ax 
                    mov   ax, divisor        ; the number, not the address
                    push  ax 
                    mov   ax, offset dividend    
                    push  ax 
                    call  divide_it 
                    add   sp, 8                    ; clear 4 pushes off stack
              
                    ; are the remainder and quotient negative? 
                    test  remainder_sign_flag, 0FFh 
                    jz    test_the_quotient 
                    neg   remainder 
              
             test_the_quotient: 
                    test  quotient_sign_flag, 0FFh      ; 1111 1111 mask 
                    jz    print_it 
                    
                    mov   ax, 4                         ; 4 word result 
                    push  ax 
                    mov   ax, offset quotient 
                    push  ax 
                    call  negate_it 
                    add   sp, 4                   ; clear 2 pushes off stack
              
             print_it: 
                    mov   ax, offset quotient 
                    call  print_signed_8byte 
                    mov   ax, remainder 
                    call  print_signed 
              
                    jmp  outer_loop 
             ; - - - - - END CODE ABOVE THIS LINE 

             We get the dividend and check the sign. If it is negative, we (1)
             negate the number, (2) switch the sign of the quotient, and (3)
             set the remainder sign flag to negative. We get the divisor,
             check for negative; if it is negative we negate it and switch the
             sign of the quotient. We now have two unsigned numbers and do
             unsigned division. After division, both the quotient and
             remainder are adjusted for sign.

             The division routine is the same as the unsigned routine before
             except it is now a subroutine:

             ; - - - - - - - - ENTER SUBROUTINE BELOW THIS LINE 
             divide_it proc near 
              
                    REMAINDER_ADDRESS         EQU  [bp+10] 
                    QUOTIENT_ADDRESS          EQU  [bp+8] 
                    DIVISOR_VALUE             EQU  [bp+6] 
                    DIVIDEND_ADDRESS          EQU  [bp+4] 
              
                    push  bp 
                    mov   bp, sp 
                    PUSHREGS  ax, bx, cx, dx, si, di 
              





             The PC Assembler Tutor                                        176
             ______________________

              
                    mov   si, DIVIDEND_ADDRESS  
                    mov   bx, QUOTIENT_ADDRESS 
                    add   si, 6                 ; start at the top word
                    add   bx, 6 
                    mov   di, WORD PTR  DIVISOR_VALUE 
                    mov   cx, 4                    ; number of words 
                    sub   dx, dx          ; clear dx for first division 
              
             division_loop: 
                    mov   ax, [si]        ; dividend word to ax 
                    div   di  
                    mov   [bx], ax        ; word of result to quotient 
                    sub   si, 2           ; decrement the pointers 
                    sub   bx, 2 
                    loop  division_loop 
              
                    mov   bx, REMAINDER_ADDRESS    ; store remainder
                    mov   [bx], dx 
              
                    POPREGS  ax, bx, cx, dx, si, di 
                    pop   bp 
                    ret                ; calling routine adjusts the stack 
              
             divide_it  endp 
              
             ; - - - - - - - - ENTER SUBROUTINE ABOVE THIS LINE 

             Draw a picture of the stack to verify that the EQU statements are
             correct for a NEAR routine. The division and negation subroutines
             go in the SUBROUTINES section of SUBTEMP1.ASM. The driver is the
             main program. If you don't remember how this division works, go
             back to the division chapter and look it over. Try out a few
             numbers to make sure that it is working the way it should.


             DATA INTEGRITY

             One thing that may have been annoying some of you is that when
             the programs sent us numbers for multiplication and division we
             sometimes negated them, effectively changing the data in memory,
             but never changed them back when we were done. In an operational
             subroutine, you would have to do it differently. The logic would
             be:

                 NUMBER NEGATIVE?    no   everything's o.k.

                      yes

                      make copy
                      negate
                      reset pointer

             If the number is positive we won't change it. If the number is
             negative, we make a copy, negate the copy and use the copy for
             the operation.