177

                                CHAPTER 17 - INTERRUPTS


             Your word processor will work on a Compaq, an IBM, an AST or any
             other type of PC compatible computer. Every time it wants to read
             a file from disk or write to a printer, it calls a DOS or BIOS
             function that takes care of it.{1}  Yet every computer has its
             own versions of these subroutines, and they not only are
             different, they are in different places in memory. How does the
             word processor know where to find them? It uses interrupts.{2}

             An interrupt is a glorified subprogram call. The first 1024 bytes
             of your computer's memory (that's from 0000:0000 to 0000:03FF)
             contain the addresses of all the DOS and BIOS interrupts. Which
             address contains the address of which subprogram was decided by
             the triumverate of Intel/IBM/Microsoft. We have two different
             sets of addresses here, so let's keep them straight. Starting at
             memory address 0000 there are 4 byte addresses called interrupt
             vectors. There is a different vector at 0000d, at 0004d, at
             0008d, at 0012d at 0016d etc.; there are 256 of them in all. Each
             of these 256 places can hold the address of a subprogram
             somewhere in memory (although not all of them are used). 

             When you call an interrupt, the 8086 goes to the appropriate
             place in low memory (from 0000 to 3FFh) and finds the address of
             the subprogram that you want, loads it into CS and IP, and goes
             to that subprogram. When that subprogram is done, it goes back to
             the next instruction in your program after the interrupt. 

             How did those addresses get into the first 1024 bytes? The
             computer put them there when you started it up. It is one of the
             first things that the computer did when you turned it on. These
             subprograms do EVERYTHING, and you can't run the computer without
             them. 

             If you want to scroll the screen, you put the appropriate
             information in the 8086 registers and use:

                 int 10h             ; decimal 16 {3}

             The 8086 goes to the interrupt 16 address (4*16 = 64), gets the
             address of the program that contains the video subprograms, and
             ____________________

                1. BIOS stands for basic input/output services.

                2. If you haven't gotten it yet, it's time to get either "DOS
             Programmer's Reference" or "The Peter Norton Programmer's Guide
             to the IBM PC." I'm serious. They contain the information you
             need to make use of this chapter.

                3. It is normal to use hex numbers for the interrupts, so if
             you read about an interrupt make sure you know if the numbers are
             hex or decimal.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                        178
             ______________________

             goes to it. If you want to write to the printer, you put the
             appropriate information in the 8086 registers and call:

                 int 21h             ; decimal 33

             The 8086 goes to address 132 (4*33 = 132), gets the address of
             the DOS program, puts it in CS and IP, and starts it. If you want
             to get input from the keyboard, you put the appropriate
             information in the 8086 registers and call:

                 int  21h            ; decimal 33

             That's right, it is the same program as the one that does the
             printer. The 8086 goes to 132 (4*33), gets the program address,
             and goes to it. 

             The lowest interrupt is int 0 (address = 4*0 = 0000). The highest
             interrupt is int 255 (address = 4*255 = 1020). 

             This is an intelligent way to handle the situation. As long as
             everyone agrees which interrupt contains the address of which
             subprogram, our programs will work on any PC compatible. This is
             one of the things that is meant by PC compatible. 

             On my computer, here is a section of these addresses starting
             with int 1Eh (30d). High memory is at the top, low memory is at
             the bottom.

                 INT #           DATA       LOCATION

                                0724h cs       146
                   36           04A8h ip       144
                             cs 0724h          142
                   35        ip 01BDh          140
                                0724h cs       138
                   34           01B0h ip       136
                             cs 019Fh          134
                   33        ip 05EBh          132
                                019Fh cs       130
                   32           05E7h ip       128
                             cs 0000h          126
                   31        ip 0000h          124
                                0070h cs       122
                   30           0EB8h ip       120

             If we call int 30d, the 8086 goes to 120 (4*30), puts 0EB8h into
             the IP, and puts 0070h (from the next higher location) into CS.
             The next instruction it does will be 0070:0EB8. If we call int
             35d, the 8086 goes to 140 (4*35), puts 01BDh in IP, puts 0724h
             (from the next higher location) in CS. The next instruction the
             8086 does will be 0724:01BD. If we call int 33d, the 8086 goes to
             132 (4*33), and puts 05EBh in IP, 019Fh  (from the next higher
             location) in CS. The next instruction executed will be
             019F:05EBh. The 0000:0000 for int 31d indicates that there is no
             int 31d (address 0000:0000 contains data, [the vectors for int
             0], not a program). Make sure that you understand how this is
             working before you go on.





             Chapter 17 - Interrupts                                       179
             _______________________


             On the PC, information for the interrupts is always passed
             through registers, not on the stack. Each interrupt type has a
             specific register for each piece of information it needs. We will
             do a couple to see how they work.


             DISPLAYING A CHARACTER

             We can print a character at a time on the monitor, so we'll input
             a string, and then print out each character of the string
             individually. We will stop the printout when we see the 0 at the
             end of the string.

             ; - - - - - - - - - - START DATA BELOW THIS LINE
             buffer  db  80 dup (?)
             ; - - - - - - - - - - START DATA BELOW THIS LINE
             ; - - - - - - - - - - START CODE BELOW THIS LINE
                 call show_regs
             outer_loop:
                 mov  ax, offset buffer
                 call get_string

                 mov  si, offset buffer
             inner_loop:
                 mov  al, [si]
                 cmp  al, 0
                 je   next_string
                 mov  ah, 14              ; ah contains function number
                 mov  bh, 0               ; where in memory
                 int  10h                 ; 33d
                 inc  si
                 jmp  inner_loop

             next_string:
                 call get_continue
                 jmp  outer_loop

             ; - - - - - - - - - - START CODE BELOW THIS LINE

             The program is simple. It gets a string, then checks each
             character for 0 (end of string), before shipping it off to the
             screen. I'll explain AH in a second. There are several places
             this character can be displayed{4}, so use show_regs to force the
             video screen to a certain place in memory, then put BH = 0 to
             tell the interrupt that the screen memory is in that place.
             Finally, with all the information in place, we do the interrupt.
             You will not print a carriage return, only the data, so we use
             get_continue to give us a carriage return. It's a little sloppy,
             but much easier. 

             We have lots and lots of subprograms for the disks, printer,
             screen, etc. There are only 255 interrupts, so it was decided at
             the beginning to make most of the interrupts groups of programs
             ____________________

                4. Cf. one of those two books.





             The PC Assembler Tutor                                        180
             ______________________

             instead of a single program. Int 10h (16d) contains about two
             dozed different video subprograms. Each program is distinguished
             by a specific number in AH. For int 10h (16d):

                 ah = 2h        Get cursor position
                 ah = 6h        Scroll window up
                 ah = Eh        (14d) Write character to screen

             For int 21h (33d):

                 ah = 1h        Keyboard input
                 ah = 5h        Printer output
                 ah = 17h       Rename a file
                 ah = 2Ch       Get the time

             As you can see, int 21h is a potpourri of subprograms. We'll do
             the same program as above, but with printer output. Everything is
             the same except that the inner loop should be changed to look
             like this:

             ; - - - - - 
                 mov  si, offset buffer
             inner_loop:
                 mov  dl, [si]
                 cmp  dl, 0
                 je   next_string
                 mov  ah, 5               ; ah contains function number
                 int  21h                 ; 33d
                 inc  si
                 jmp  inner_loop

             ; - - - - -

             There is practically no change. We use DL instead of AL, have
             "int 21h" instead of "int 10h", and change the function number in
             AH to 5. Also, BH is not needed.

             Leave your printer off at the beginning to see what happens. Turn
             your printer on and enter a string of 10 or 20 letters. Probably
             nothing happened. Enter another 20 or 30 letters. Nothing again.
             Try 50 letters this time. This time it should work. Lots of
             printers won't print anything unless (1) they get a carriage
             return (which you haven't sent) or (2) they have a backlog of
             more than 80 characters. If you ever use the printer interrupt,
             you'll have to remember that.

             These interrupts which are in your program are called software
             interrupts. They are your interface with the peripheral devices
             on your machine, doing everything from disk i/o to handling
             memory allocation. They do all your housekeeping for you.{5}  If
             you are going to work at this level then you should buy one of
             those two books. They contain all the software interrupts (and
             there are about a hundred of them), tell how they work and which
             registers to set for each interrupt. If you don't have access to
             ____________________

                5. But they don't do Windows.





             Chapter 17 - Interrupts                                       181
             _______________________

             these interrupts it's like having your arms cut off - you're
             unable to do any i/o at all.


             HARDWARE INTERRUPTS

             The interrupts that we write in our programs aren't the only
             interrupts there are. The hardware uses interrupts to take
             temporary control of the computer. On a Macintosh, if you insert
             a disk, the program stops and the operating system reads in the
             disk directory. A modem that is in use will request time for
             doing i/o. Also, if the 8086 detects a zero divide, it will
             trigger a special interrupt. You have met int 4 already. It is
             the INTO instruction, which will trigger an interrupt if the
             overflow flag is set. 

             Your interrupts are in specific places in your code, but these
             machine interrupts can happen at any time. There are two lines
             (wires) into the 8086. One is for serious problems that need to
             be taken care of NOW, and it has non-maskable interrupts. The
             other line is for interrupts that need to be taken care of in a
             timely fashion, and they are maskable interrupts. 

             A non-maskable interrupt (NMI) is when the hardware detects that
             it is in deep doo doo. It sends a signal on the NMI line that
             says "Hey! I need an interrupt." The 8086 finishes the
             instruction it is processing and then IMMEDIATELY gives over
             control. The NMI uses the same 1024 bytes in low memory for
             interrupt vectors, but has its own interrupt numbers. Normally
             this is for very serious errors, so the interrupt program may
             decide to abort your program and return to the operating system;
             if it makes sense to, it will return to your program where your
             program left off.

             A maskable interrupt is when a piece of hardware has some work to
             do. It sends a signal to the 8086 (on the INTR line), and the
             8086 takes care of it when it is ready.

             When the 8086 is ready depends on you. In the flags register is
             the IEF, the interrupt enable flag. It should always be set to 1
             unless you are doing something critical. Basically, the only
             things that are critical are interrupts themselves and context
             switches. Context switches are done by the operating system in
             multitasking environments, so they don't concern you, and you are
             not writing interrupts, so they don't concern you. Therefore,
             always keep the IEF set. Just for your information, you set the
             IEF with:

                 sti  ; set interrupt flag (interrupts enabled)

             and clear it with:

                 cli  ; clear interrupt flag (interrupts disabled)

             Why do interrupt programs clear the interrupt flag? Because you
             could have interrupts interrupting other interrupts and wind up
             with scads of half finished interrupts lying around. This way,





             The PC Assembler Tutor                                        182
             ______________________

             one interrupt finishes before another can take over. 


             Suppose you are in the middle of the following two instructions
             when an interrupt hits:

                 cmp  al, 7
                 jne  some_label

             If the hardware interrupt takes over after the CMP instruction
             but before the JNE instruction, the correctness of the result
             will depend on the zero flag staying the same. Can you trust it?
             The answer is yes. The first three things an interrupt request
             does (in the microcode) are:

                 push flags     ; push the flags
                 push old CS    ; push the code segment
                 push old IP    ; push the instruction pointer

             On return, it pops the flags back in place, so they are exactly
             the same as just before the interrupt. You will notice that there
             are 3 things on the stack instead of the usual 2 in a far call.
             Therefore, there is a special RET instruction called IRET (return
             from interrupt) which pops not only IP and CS, but the flags as
             well. You can only use this instruction in an interrupt because
             it assumes that the flags register is right after CS on the
             stack.


             DEBUGGING

             Finally, if you have a debugger installed, the debugger uses two
             interrupts, int 1 and int 3. You code int 3 into the program by
             placing:

                 int

             in the program with no number.{6}  The interrupt will call the
             debugger. The reason for this int with no number is that
             afterwards, you can replace it with NOP, since they are both 1
             byte instructions. Int 3 is a 2 byte instruction (they are coded
             differently, even though they wind up at the same place).

             Int 1 is the trap instruction. In the flags register is the trap
             flag (TF). If TF is set, the 8086 will interrupt after the next
             instruction. That way, the debugger can single step through
             sections of code. You put Int 3 to set a breakpoint and then set
             TF to single step from there. 

             The only way to set TF from your own program is:

             ____________________

                6. Though the Microsoft assembler considers this an error. You
             must code it as:

                 int  3





             Chapter 17 - Interrupts                                       183
             _______________________

                 pushf
                 pop  ax
                 or   ax, 0100h
                 push ax
                 popf

             but you should let the debugger do it.

             Just so you can get a feel for how the debugger system works,
             there is a pseudo-debugger called PSEUDDBG.COM in \XTRAFILE. It
             is not a debugger. It does nothing but tell you whether you have
             generated a breakpoint interrupt (int 3) or a single_step
             interrupt (int 1). It is memory resident. That means that once
             you have loaded it, it will stay in memory until you shut the
             machine off or reset the machine. You load it by executing:

                 >pseuddbg

             It will tell you that it has been loaded and then sit there
             waiting for interrupts. When you generate a breakpoint interrupt,
             PSEUDDBG will allow you to set the trap flag or just continue.
             When you generate a single step interrupt, PSEUDDBG will allow
             you to clear TF or to continue single stepping. All you need to
             try it out is a simple program:

             ; - - - - - ENTER CODE BELOW THIS LINE
             outer_loop:
                 call get_continue

                 mov  cx, 4
                 int  3
             inner_loop:
                 mov  ax, 5
                 add  ax, 3
                 add  ax, 7
                 add  ax, 10
                 loop inner_loop

                 loop outer_loop
             ; - - - - - FINISH CODE ABOVE THIS LINE

             Each time you start the outer loop, it will generate a breakpoint
             interrupt. At this point you can set TF to single step or
             continue. If you single step, watch IP. It will be changing,
             cycling through the loop till it gets to get_continue. If you
             start trapping through get_continue, things will get strange
             because get_continue stores the flags. This means that after you
             quit trapping, get_continue will POP some flags that have TF set
             and it will start trapping again. If this happens, just continue
             hitting 0 until you get out of the single step mode. 

             If you like this method of single stepping through code, there is
             a memory resident version of ASMHELP called HELPMEM.COM which
             contains show_regs and allows single stepping. It can be used in
             conjunction with ASMHELP.OBJ. For details consult APP1.DOC in the
             appendix.






             The PC Assembler Tutor                                        184
             ______________________

                                          SUMMARY

             Software interrupts send the 8086 to the first 1024 bytes of
             memory where it finds the address of the DOS or BIOS subprogram
             that you want to go to. The correspondence between the interrupt
             number and the location of the address is:

                 address location = 4 * interrupt number

             The address is stored in the next 4 bytes; first IP, then CS.



             The first 5 interrupts are:

                 int 0     divide by zero
                 int 1     trap flag induced single stepping for the debugger
                 int 2     non_maskable_interrupt (NMI)
                 int 3     1 byte interrupt for the debugger
                 int 4     interrupt on overflow


             There are two types of hardware interrupts. NMI (non maskable
             interrupt) interrupts are for serious problems that need to be
             taken care of IMMEDIATELY. They have priority and take over right
             after the current instruction is finished.

             Maskable interrupts are hardware interrupts that should be taken
             care of in a timely fashion. If IEF (the interrupt enable flag)
             is set the maskable interrupts will go through. If IEF is
             cleared, the maskable interrupts must wait until it is set again.
             Set the IEF with:

                 sti  ; set interrupt flag

             and clear it with:

                 cli  ; clear interrupt flag

             The IEF should always stay set unless there is a specific reason
             for not allowing interrupts to happen.


             If you are writing an interrupt routine, then instead of RET you
             use IRET (return from interrupt) which not only pops off IP and
             CS, but pops the flags register as well.