24

                                  CHAPTER 4 - SHOW_REGS


             We got started using the program show_regs in the last chapter,
             but we have already run into problems. The hex number doesn't
             look the same once we put it in the register - that's because
             what we are seeing in the arithmetic registers is an unsigned
             number. Also, when we moved a byte from AL to CH, it was clear
             that something had moved, but it wasn't clear what the number
             was. There are two problems here:

                 (1) We want to use data in hex, binary, ascii, unsigned and
                 signed format depending on what we are doing in the program.

                 (2) Some of the registers can be used as half registers, so
                 we want a whole register when we need it and a half register
                 when we need it.

             Nooooooo problem. There are eight registers whose formats we want
             to be able to change: AX, BX, CX, DX, SI, DI, BP and SP. We need
             to give each one a code to tell it what to display. The code is
             the following:

                 signed number       1
                 unsigned number     2
                 binary number       3
                 hex number          4
                 ascii               5

             Also, we need to know whether AX, BX, CX and DX are half or full
             registers. The code for that is:

                 half register       128       (80 hex)
                 full register       0

             We will need to do two things - set up the codes, then tell
             show_regs about the code. We'll begin by setting up the codes.

             First let's start with SI, DI, BP and SP. They must be full
             registers, so the half register information is irrelevant.{1}  In
             the data section is a set of data starting ax_byte, bx_byte ...
             sp_byte. That is where you need to put the code. Don't change the
             order of these variables. Just put the correct formatting code in
             the appropriate byte. 

                 mov  si_byte, 3

             will display SI as a binary number. 

             ____________________

                1 show_regs is very forgiving. It only recognizes half
             registers where appropriate, and if you screw up on the format
             code, it just makes it an unsigned number.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 4 - SHOW_REGS                                          25
             _____________________

                 mov  bp_byte, 4

             will display BP as a hex number.

                 mov  di_byte, 1

             will display DI as a signed number.

             That's pretty easy. If you are using AX, BX, CX, or DX as a full
             register, they are exactly the same.

                 mov  dx_byte, 5     ; full register, character format
                 mov  ax_byte, 2     ; full register, unsigned format
                 mov  bx_byte, 3     ; full register, binary

             If we use half registers we need to pass more information.
             show_regs needs to know that it is half registers, not full
             registers; it also needs to know what the left format is and what
             the right format is. This is easier than it sounds but will take
             a little getting used to. The right nibble (half byte) gets the
             right format and the left nibble (half byte) gets the left
             format. Then you add 128 to the total. This works easily in hex.
             13h means that the left half register is (1 = signed) and the
             right register is (3 = binary). Then we add (128 = 80h) for a
             total of 93h. Here are some more examples. Remember, 8 + 1 = 9, 8
             + 2 = A, 8 + 3 = B, 8 + 4 = C, 8 + 5 = D

                 C4h       ; 80h + 44h  left and right are hex
                 A5h       ; 80h + 25h  left is unsigned, right is ascii
                 B1h       ; 80h + 31h  left is binary, right is signed
                 D2h       ; 80h + 52h  left is ascii, right is unsigned
                 94h       ; 80h + 14h  left is signed, right is hex

             There is a summary at the end of the chapter giving all the
             commands and codes for show_regs. It is important to take some
             time here and learn to make the registers look the way we want,
             because later on we have machine instructions for signed numbers,
             for ascii characters, for binary numbers, and you need to see
             what the registers look like in the appropriate formats.
             Spending a little time right now will save you a lot of time
             later on.

             If you don't like using hex numbers you can use decimal numbers:

                 code = type_of_register + left code + right code

             where full register = 0, half register = 128d and:

                 NUMBER FORMAT        LEFT CODE     RIGHT CODE

                 signed                   16d            1d
                 unsigned                 32d            2d
                 binary                   48d            3d
                 hex                      64d            4d
                 ascii                    80d            5d

             Therefore, left binary, right hex = 128 + 48 + 4 = 180d. Some





             The PC Assembler Tutor                                         26
             ______________________

             more examples:

                 left ascii, right signed = 128 + 80 + 1 = 209d
                 left signed, right binary = 128 + 16 + 3 = 147d
                 left hex, right unsigned = 128 + 64 + 2 = 192d

             We can put in the code the same way as before.

                 mov  ax_byte, 192d
                 mov  dx_byte, 147d
                 mov  cx_byte, 0D2h
                 mov  bx_byte, 94h

             We now have the codes in out program, but show_regs doesn't know
             about them. In order to give the information to show_regs, we
             call set_reg_style. set_reg_style makes a copy of your
             information for use by show_regs. The next time that you call
             show_regs, it will use the new register formats. There is a small
             problem, however. The information we have is eight bytes long,
             and ax is only two bytes long. How do we pass the information?
             The answer is: we don't pass the information. Instead, we pass
             the address of the information. If you look in the data segment
             of temp2.asm, you will see that ax_byte is the first byte of this
             data. We pass the address of ax_byte (the first byte) and
             set_reg_style knows that that address plus the following 7
             addresses have the information that it needs. There is a special
             machine instruction for putting an address in a register - it is
             LEA or load effective address. It looks like this:

                 lea  ax, ax_byte

             This instruction says: put the address of ax_byte in the AX
             register. Combined with the call, we have:

                 lea  ax, ax_byte
                 call set_reg_style


             Before we start writing programs with set_reg_style, we will run
             a pre-existing program called SETREGS.EXE. Its pathname is
             \ASMHELP\SETREGS.EXE. It puts the same (pseudo) random number in
             all arithmetic registers except SP, then requests a formatting
             code for each register. After cycling through all the registers,
             it asks you to press ENTER. It then puts a new random number in
             the registers and starts the cycle again. The hex codes are
             displayed on the screen before each request. As usual, use
             Control-C to exit the program.

             Here is what the screen might look like after the first cycle.
             The prseudo random number 2571 will be the same, but your
             formatting might be different:











             Chapter 4 - SHOW_REGS                                          27
             _____________________

             *********************** SCREEN SHOT ***************************
                 AX +02571                             SI +02571
                 BH  00001010      BL  0B **           DI  02571
                 CX  0A 0B **                          BP  0000101000001011
                 DH  0A **         DL  0B **           SP  00C4H

                 CS  0AA4H   DS  0A42H   ES  0A25H   SS  0A35H   IP  0115H

                 OF   DF  IEF   TF   SF   ZF   AF   PF   CF
                  x    +    x         +              O    x      COUNT  00009
             ----------------------------------------------------------------
             hex = C0h or 4h;   ascii = D0h or 5h
             Enter a code for sp.
             Enter a one byte hex number  4
             Press ENTER to continue

             *****************************************************************

             The formats I have used are:
                 AX   full register  (signed)
                 BX   half registers (binary, ascii)
                 CX   full register  (ascii)
                 DX   half registers (ascii, ascii)
                 SI   full register  (signed)
                 DI   full register  (unsigned)
                 BP   full register  (binary)
                 SP   full register  (hex) 

             Cycle through the registers a couple of times. If you make them
             binary, they get longer, if you make them hex or ascii they get
             shorter; a sign appears if they are signed, and you can change
             from full to half registers for AX, BX, CX and DX.

             You will always be able to tell what kind of number show_regs is
             printing because (1) a signed number always has a + or - in front
             of it, (2) a hex number always has an h after it, (3) a binary
             number is 8 digits long for a half register or 16 digits long for
             a full register, and (4) an ascii has an asterisk after it. Just
             as with print_num, if the ascii character has one of the values
             0-32, 127 or 255, it will print a hex number and show a double
             asterisk '**' to signal the event. (5) If none of the above is
             true, then it is an unsigned decimal number.

             If you have a feel for what's happening, it is time to take a
             mini-test. This is an untimed test, so just make sure that it is
             correct. I'll give you a particular style, and you figure out the
             code for that style. The answers are at the bottom of the page.
             You don't have to memorize the codes. You should be using the
             summary at the end of the chapter for this quiz.

                 1.   full register, binary
                 2.   half register, left ascii, right hex
                 3.   half register, left signed, right unsigned
                 4.   full register, ascii
                 5.   half register, left binary, right ascii
                 6.   half register, left hex, right signed
                 7.   half register, left unsigned, right binary





             The PC Assembler Tutor                                         28
             ______________________

                 8.   full register, hex
                 9.   full register, signed
                 10.  half register, left signed, right binary.

             If you feel comfortable with what's going on and are able to do
             set the registers with the help of the summary, we are ready to
             move on. 

             Here are the answers.{2}





























             ____________________

                2 Here are the answers, both in hex and decimal.

                   PROBLEM      HEX       DECIMAL

                      1.         3h         3d
                      2.        D4h       212d
                      3.        92h       146d
                      4.         5h         5d
                      5.        B5h       181d
                      6.        C1h       193d
                      7.        A3h       163d
                      8.         4h         4d
                      9.         1h         1d
                      10.       93h       147d

             These things are slow to calculate. It took me about a minute per
             problem to do both the hex and binary.





             Chapter 4 - SHOW_REGS                                          29
             _____________________


                                          SUMMARY

             The registers may be displayed in signed, unsigned, binary, hex,
             and ascii formats.  The basic codes for this are:

                 signed    1
                 unsigned  2
                 binary    3
                 hex       4
                 ascii     5

             In addition you need to add the register type. They are:

                 full register  0
                 half register  128d or 80h


             For the left half register, we have:

                 FORMAT            LEFT HEX     LEFT DECIMAL

                 signed               10h           16d
                 unsigned             20h           32d
                 binary               30h           48d
                 hex                  40h           64d
                 ascii                50h           80d


             Since the left code is of interest only when the half register
             type is being used, we simply add 80h and come up with:

                 FORMAT            LEFT CODE    RIGHT CODE

                 signed                90h          1h
                 unsigned              A0h          2h
                 binary                B0h          3h
                 hex                   C0h          4h
                 ascii                 D0h          5h


             Or we add 128d and have:

                 FORMAT            LEFT CODE    RIGHT CODE

                 signed              144d           1d
                 unsigned            160d           2d
                 binary              176d           3d
                 hex                 192d           4d
                 ascii               208d           5d


             SETTING THE FORMATS

             Formats are set by calling set_reg_style. The address of ax_byte
             must be in AX. The standard assembler instructions for this are:






             The PC Assembler Tutor                                         30
             ______________________

                 lea  ax, ax_byte
                 call set_reg_style

             set_reg_style makes a copy of your format data. It changes
             nothing on the screen. The next time that you call show_regs, it
             will use the new formatting data.

             The correct order for the data in the data segment is:

             ax_byte, bx_byte, cx_byte, dx_byte, si_byte, di_byte, bp_byte,
             sp_byte. They are, of course, all byte sized data.