47

                                   CHAPTER 7 - LOGIC


             There are a number of operations which work on individual bits of
             a byte or word. Before we start working on them, it is necessary
             for you to learn the Intel method of numbering bits. Intel starts
             with the low order bit, which is #0, and numbers to the left. If
             you look at a byte:

                 7 6 5 4 3 2 1 0

             that will be the ordering. If you look at a word:

                 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

             that is the ordering. The overwhelming advantage of this is that
             if you extend a number, the numbering system stays the same. That
             means that if you take the number 45 :

                 7 6 5 4 3 2 1 0
                 0 0 1 0 1 1 0 1  (45d)

             and sign extend it:

                 15 14 13 12 11 10  9  8  7  6  5  4  3  2  1  0
                  0  0  0  0  0  0  0  0  0  0  1  0  1  1  0  1 

             each of the bits keeps its previous numbering. The same is true
             for negative numbers. Here's -73:

                 7 6 5 4 3 2 1 0
                 1 0 1 1 0 1 1 1 (-73d)

                 15 14 13 12 11 10  9  8  7  6  5  4  3  2  1  0
                  1  1  1  1  1  1  1  1  1  0  1  1  0  1  1  1  (-73d)

             In addition, the bit-position number denotes the power of 2 that
             it represents. Bit 7 = 2 ** 7 = 128, bit 5 = 2 ** 5 = 32, 
             bit 0 = 2 ** 0 = 1. {1}.

             Whenever a bit is mentioned by number, e.g. bit 5, this is what
             is being talked about.


             AND

             We will use AND as the prototype. There are five different ways
             you can AND two numbers:


             ____________________

                1 I'm using the Fortran convention for showing exponents. That
             is, 2 ** 7 is 2 to the 7th, 3 ** 19 is 3 to the 19th. 

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                         48
             ______________________

                 1.   AND two register
                 2.   AND a register with a variable
                 3    AND a variable with a register
                 4.   AND a register with a constant
                 5.   AND a variable with a constant

             That is:

                 variable1 db   ?
                 variable2 dw   ?

                 and  cl, dh
                 and  al, variable1
                 and  variable2, si
                 and  dl, 0C2h
                 and  variable1, 01001011b

             You will notice that this time the constants are expressed in hex
             and binary. These are the only two reasonable alternatives. These
             instructions work bit by bit, and hex and binary are the only two
             ways of displaying a number bitwise (bit by bit). Of course, with
             hex you must still convert a hex digit into four binary digits.

             The table of bitwise actions for AND is:

                 1    1    ->   1
                 1    0    ->   0
                 0    1    ->   0
                 0    0    ->   0

             That is, a bit in the result will be set if and only if that bit
             is set in both the source and the destination. What is this used
             for? Several things. First, if you AND a register with itself,
             you can check for zero.

                 and  cx, cx

             If any bit is set, then there will be a bit set in the result and
             the zero flag will be cleared. If no bit is set, there will be no
             bit set in the result, and the zero flag will be set. No bit will
             be altered, and CX will be unchanged. This is the standard way of
             checking for zero. You can't AND a variable that way:

                 and  variable1, variable1

             is an illegal instruction. But you can AND it with a constant
             with all the bits set:

                 and  variable1, 11111111b

             If the bit is set in variable1, then it will be set in the
             result. If it is not set in variable1, then it won't be set in
             the result. This also sets the zero flag without changing the
             variable.

             AND is also used in masks, which will be covered at the end of
             the chapter.





             Chapter 7 - Logic                                              49
             _________________


             Finally, there is a variant of AND called TEST. TEST does exactly
             the same thing as AND but throws away the results when it is
             done. It does not change the destination. This means that it can
             check for specific things without altering the data. It has the
             same possibilities as AND:

                 variable1 db   ?
                 variable2 dw   ?

                 test cl, dh
                 test al, variable1
                 test variable2, si
                 test dl, 0C2h
                 test variable1, 01001011b

             will set the flags exactly the same as the similar AND
             instructions but will not change the destination. We need a
             concrete example, and for that we'll turn to your video card. In
             text mode, your screen is 80 X 25. That is 2000 cells. Each cell
             has a character byte and an attribute byte. The character byte
             has the actual ascii number of the character. The attribute byte
             says what color the character is, what color the background is,
             whether the character is high or low intensity and whether it
             blinks. An attribute byte looks like this:

                 7 6 5 4 3 2 1 0
                 X R G B I R G B

             Bits 0,1 and 2 are the foreground (character) color. 0 is blue, 1
             is green, and 2 is red. Bits 4, 5, and 6 are the background
             color. 4 is blue, 5 is green, and 6 is red. Bit 3 is high
             intensity, and bit 7 is blinking. If the bit is set (1) that
             particular component is activated, if the bit is cleared (0),
             that component is deactivated. 

             The first thing to notice is how much memory we have saved by
             putting all this information together. It would have been
             possible to use a byte for each one of these characteristics, but
             that would have required 8 X 2000 bytes = 16000 bytes. If you add
             the 2000 bytes for the characters themselves, that would be 18000
             bytes. As it is, we get away with 4000 bytes, a savings of over
             75%. Since there are four different screens (pages) on a color
             card, that is 18000 X 4 = 72000 bytes compared to 4000 X 4 =
             16000. That is a huge savings.

             We don't have the tools to access these bytes yet, but let's
             pretend that we have moved an attribute byte into dl. We can find
             out if any particular bit is set. TEST dl with a specific bit
             pattern. If the zero flag is cleared, the result is not zero so
             the bit was on. If the zero flag is set, the result is zero so
             that bit was off


                 test dl, 10000000b       ; is it blinking?
                 test dl, 00010000b       ; is there blue in the background?
                 test dl, 00000100b       ; is there red in the foreground?





             The PC Assembler Tutor                                         50
             ______________________


             If we look at the zero flag, this will tell us if that component
             is on. It won't tell us if the background is blue, because maybe
             the green or the red is on too. Remember, test alters neither the
             source nor the destination. Its purpose is to set the flags, and
             the results go into the Great Bit Bucket in the Sky.


             OR

             The table for OR is:

                 1    1    ->   1
                 1    0    ->   1
                 0    1    ->   1
                 0    0    ->   0

             If either the source or the destination bit is set, then the
             result bit is set. If both are zero then the result is zero.
             OR is used to turn on a specific bit.

                 or   dl, 10000000b  ; turn on blinking
                 or   dl, 00000001b  ; turn on blue foreground

             After this operation, those bits will be on whether or not they
             were on before. It changes none of the bits where there is a 0.
             They stay the same as before.


             XOR

             The table for XOR is:

                 1    1    ->   0
                 1    0    ->   1
                 0    1    ->   1
                 0    0    ->   0

             That is, if both are on or if both are off, then the result is
             zero. If only one bit is on, then the result is 1. This is used
             to toggle a bit off and on.

                 xor  dl, 10000000b  ; toggle blinking
                 xor  dl, 00000001b  ; toggle blue foreground

             Where there is a 1, it will reverse the setting. Where there is a
             0, the setting will stay the same. This leads to one of the
             favorite pieces of code for programmers.

                 xor  ax, ax

             zeros the ax register. There are three ways to zero the ax
             register:

                 mov  ax, 0
                 sub  ax, ax
                 xor  ax, ax





             Chapter 7 - Logic                                              51
             _________________


             The first one is very clear, but slightly slower. For the second
             one, if you subtract a number from itself, you always get zero.
             This is slightly faster and fairly clear.{2}  For the third one,
             any bit that is 1 will become 0, and and bit that is 0 will stay
             0. It zeros the register as a side effect of the XOR instruction.
             You'll never guess which one many programmers prefer. That's
             right, XOR. Many programmers prefer the third because it helps
             make the code more obsure and unreadable. That gives a certain
             aura of technical complexity to the code.



             NEG and NOT

             NOT is a logical operation and NEG is an arithmetical operation.
             We'll do both here so you can see the difference. NOT toggles the
             value of each individual bit:

                 1    ->   0
                 0    ->   1

             NEG negates the value of the register or variable (a signed
             operation). NEG performs (0 - number) so:

                 neg  ax
                 neg  variable1

             are equivalent to (0 - AX) and (0 - variable1) respectively. NEG
             sets the flags in the same way as (0 - number).

             ; negvsnot.asm
             ; compares the operations NEG and NOT
             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
                    mov   ax_byte, 1          ; signed 
                    mov   bx_byte, 1          ; signed 
                    mov   cx_byte, 1          ; signed 
                    mov   si_byte, 3          ; binary 
                    mov   di_byte, 3          ; binary 
                    mov   bp_byte, 3          ; binary 
                    mov   dx, 0               ; not used, so clear
                    lea   ax, ax_byte 
                    call  set_reg_style 
                    call  show_regs 
              
             outer_loop: 
                    call  get_signed          ; get number 
                    mov   bx, ax              ; move it to all registers 
                    mov   cx, ax 
                    mov   si, ax 
                    mov   di, ax 
                    mov   bp, ax 
              
                    not   bx                  ; NOT the second row down 
             ____________________

                2 This is one of the first instructions in the template files.





             The PC Assembler Tutor                                         52
             ______________________

                    not   di 
                    neg   cx                  ; NEG the third row down 
                    neg   bp 
              
                    call  show_regs 
                    jmp   outer_loop 
              
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 


             This is set up so the left registers are signed and the right
             registers are binary. The top registers retain the original
             value, the second registers down will do NOT and the third
             registers down will do NEG.

             Put a number in. On the right side, you will see that NOT (in DI)
             reverses the bit pattern, while on the left, NEG (in CX) negates
             the number. Do a few more. This is always true. But they seem to
             be related. In fact, BX will always be 1 too negative. Why?
             Remember that in the introduction on numbers, when we changed
             signs, we had:

                 negative of number = one's complement + 1

             but the one's complement is exactly NEG. It switches the value of
             each bit. To get the values in the third row (CX and BP), simply
             add 1 to the values in the second row (BX and DI). Remember, NOT
             is a logical operation, NEG is an arithmetic operation.


             MASKS

             To explain masks, we'll need some data, and we'll use the
             attribute byte for the monitor. Here it is again:

                 7 6 5 4 3 2 1 0
                 X R G B I R G B

             Bits 0,1 and 2 are the foreground (character) color. 0 is blue, 1
             is green, and 2 is red. Bits 4, 5, and 6 are the background
             color. 4 is blue, 5 is green, and 6 is red. Bit 3 is high
             intensity, and bit 7 is blinking.

             What we want to do is turn certain bits on and off without
             affecting other bits. What if we want to make the background
             black without changing anything else? We use and AND mask.

                 and  video_byte, 10001111b

             Bits 0, 1, 2, 3 and 7 will remain unchanged, while bits 4, 5 and
             6 will be zeroed. This will make the background black. What if we
             wanted to make the background blue? This is a two step process.
             First we make the background black, then set the blue background
             bit. This involves first the AND mask, then an OR mask.

                 and  video_byte, 10001111b
                 or   video_byte, 00010000b





             Chapter 7 - Logic                                              53
             _________________


             The first instruction shuts off certain bits without changing
             others. The second turns on certain bits without effecting
             others. The binary constant that we are using is called a mask.
             You may write this constant as a binary or a hex number. You
             should never write it as a signed or unsigned number (unless you
             are one of those people who just adores making code unreadable).

             If you want to turn off certain bits in a piece of data, use an
             AND mask. The bits that you want left alone should be set to 1,
             the bits that you want zeroed should be set to 0. Then AND the
             mask with the data.

             If you want to turn on certain bits in a piece of data, use an OR
             mask. The bits that you want left alone should be set to 0. The
             bits that you want turned on should be set to 1. Then OR the mask
             with the data.

             Go back to AND and OR to make sure you believe that this is what
             will happen. 










































             The PC Assembler Tutor                                         54
             ______________________

                                       SUMMARY


             For AND, TEST, OR, and XOR you can have the following
             combinations:

                 1.   two register
                 2.   a register with a variable
                 3    a variable with a register
                 4.   a register with a constant
                 5.   a variable with a constant


             AND is a bitwise logical operation.

                 1    1    ->   1
                 1    0    ->   0
                 0    1    ->   0
                 0    0    ->   0

             TEST does the same thing as AND except that the result is
             discarded. It is used for setting the flags without altering the
             data.

             OR is a bitwise logical operation.

                 1    1    ->   1
                 1    0    ->   1
                 0    1    ->   1
                 0    0    ->   0

             XOR is a bitwise logical operation.

                 1    1    ->   0
                 1    0    ->   1
                 0    1    ->   1
                 0    0    ->   0



             You can use NOT and NEG with either a register or a variable in
             memory.

             NOT is a bitwise logical operation

                 0    ->   1
                 1    ->   0

             NEG is an arithmetic operation. NUMBER -> - NUMBER. It gives the
             negative of a signed number.


             MASKS

                 If you want to turn off certain bits of a piece of data, use
                 an AND mask. The bits that you want left alone should be set
                 to 1, the bits that you want zeroed should be set to 0. Then





             Chapter 7 - Logic                                              55
             _________________

                 AND the mask with the data.

                 If you want to turn on certain bits of a piece of data, use
                 an OR mask. The bits that you want left alone should be set
                 to 0. The bits that you want turned on should be set to 1.
                 Then OR the mask with the data.