INT 05H - PRINT_SCREEN
        This logic eill be invoked by interrupt 05H to print the screen.
        The cursor position at the time this routine is invoked will be saved
        and restored upon completion. The routine is intended to run with 
        interrupts enabled. If a subsequent Print Screen Key is depressed 
        while this routine is printing it will be ignored. The base printers
        status is checked for not busy and not out of paper. An initial
        status error will abend the print request. 
        Address 0050:0000 contains the status of the print screen:

        50:00   = 0     Print Screen has not been called or upon return
                         from a call. this indicates a successful operation.
                = 1     Print Screen is in progress - Ignore the request.
                = 255   Error encountered during printing.

PDL:

        Save all registers
        IF STATUS_BYTE (50:00) is in progress (= 01)
        THEN 
            jump to EXIT: (ignore this key progress)
        ELSE
            get currnt page, number of rows, and number of columns on screen
            get printer status from INT 17h
            IF printer stataus is Busy or Out_of_Paper
            THEN
                set STATUS_BYTE to error status (= 0FFh),
                jump to EXIT:
            ELSE 
                print the screen
                IF printer stataus is error during process
                THEN
                    set STATUS_BYTE to error status (= 0FFh),
                    jump to EXIT:
                ELSE
                    set STATUS_BYTE to no error status (= 00h)
                ENDIF
            ENDIF
        ENDIF

        EXIT:
        restore all registers
        return