INT 08H (IRQ 0) - TIMER_INT hardwre interrupt
        This routine handles the Timer Interrupt from channel 0 of the 8254
        Timer chip. Input frequency is 1.19318 MHZ and the divisor is 65536.
        Resulting in approximately 18.2 Interrupts every second.

        The Interrupt Handler maintains a Count (40:6C) of Interrupts since
        Power On Time, which may be used to establish Time Of Day.
        The Interrupt Handler also decreases the Motor Control Count (40:40)
        of the diskette, and when it expires, will Turn Off the diskette
        motor(s), and Reset the Motor Running Flags.
        The Interrupt Handler will also invoke a user routine through
        Interrupt 1Ch at every Time Tick. The user must code a routine and 
        place the correct address in the vcetor table.

PDL:
        Save the registers
        decrease the TIMER_COUNT (TIMER_HIGH,TIMER_LOW - 40:6E,40:6C)
        IF Timer Count equals 24 hours (TIMER_HIGH,TIMER_LOW) = (018h,0B0h) 
        THEN
            Set the TIMER_COUNT to zero,
            Set the TIMER_OVERFLOW (40:70) to one 
                ( Timer has counted past 24 hours)
        ENDIF
        decrease MOTOR_COUNT (40:40)
        IF MOTOR_COUNT equals to zero
        THEN
           Turn off motor running bits (bit 3,2,1,0 of 40:3F = 0,0,0,0)
           Turn off the motor (Output the C0h to PORT 3F2h)
        ENDIF
        Call the user interrupt routine (INT 1CH)
        Send EOI to 8259 Interrupt Controller
        Restore the registers
        return