INT 70H (IRQ 8) - ALARM INTERRUPT HANDLER (RTC) hardware interrupt
        This Routine handles the Periodic and Alarm Interrupts from the CMOS
        TIMER. Input Frequency is 1.024 KHZ or approximately 1024 interrupts
        every second for the Periodic Interrupt. For the Alarm Function,
        the interrupt will occur at the designated time.

        Interrupts are Enabled when the EVENT or ALARM Function is Activated.
        For the EVENT INTERRUPT, the Handler will decrease the WAIT COUNTER
        and when it expires will SET the designated Location to 80H. For the
        ALARM INTERRUPT, the user must provide a routine to intercept the 
        correct address from the VECTOR TABLE invoked by INTERRUPT 4AH
        prior to SETTING the REAL TIMER CLOCK ALARM (INT 1AH, AH = 06H)

PDL:
        Save the registers
        RESTART:
        Read the PIE and AIE bits from the index 0Bh of COMS (bit 5,4)
        IF PIE and AIE is not Enabled (= 0,0)
        THEN
            jump EXIT:
        ELSE
            Read the PF and AF bits from the index 0Ch of CMOS (bit 5,4)
            IF PIE is Enabled (=1) and Periodic Interrupt is occured (PF=1)
            THEN 
                Decrease the User Wait Count (0,976) (High, Low - 40:9E,40:9C)
                IF User Wait Count < 0 
                THEN
                    Turn Off Periodic Interrupt Enable
                    Set the Wait Active Flag Off (40:A0 = 0)
                    Set User Wait Complete Flag ON (= 80H)
                    (Offset Address to User Wait Complete Flag - 40:98,
                    Segment Address to User Wait Complete Flag - 40:9A)
                ENDIF
            ENDIF     
            IF AIE is Enabled (=1) and Alarm Interrupt is occured (AF=1)
            THEN
            Enable NMI from the CMOS
            Call the User interrupt routine (INT 4AH)
            jump RESTART:
            ENDIF
        ENDIF     

        EXIT:
        Enable NMI from the CMOS
        Send EOI to 8259 Interrupt Controller
        restore the registers
        return