ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                        º                                 º
                        º  ßßÛßßßßßßßßßßßßßßßßßßßßß       º
                        º    Û ÛßÛ ÛßÛ Û   ÛßÛ ÛßÛ ßÛßßß  º
                        º    Û Û     Û Û Û Û     Û  Û     º
                        º    Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û     º
                        º    Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û     º
                        º    Û                            º
                        º    Û                            º
                        º           Version 2.50          º
                        ÈÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍ¼
                            º                         º
                            º     Paul E. Traufler    º
                            º     111 Emerald Drive   º
                            º     Harvest, Al 35749   º
                            º     (205) 726-5511      º
                            º                         º
                            ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
 
                             Satellite Tracking Program
 
                                  1 October, 1990
 
 
 
 
 
 
 
 
 
 
 
 
  
                                      TRAKSAT
                                  (C)opyright 1990
                                 By Paul E. Traufler
                                 All Rights Reserved
 
 
 
 
 
 
 
 
 


 
 
 
 
 
 
 
      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                                  º
      º             TRAKSAT is free for NON-COMMERCIAL use only.         º
      º                                                                  º
      ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
      º                                                                  º
      º  If you find TRAKSAT useful and would like to use it in a        º
      º  commercial operation please call or write for more information. º
      º                                                                  º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»                         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                          º                         º
                          º   Paul E. Traufler      º
                          º   111 Emerald Drive     º
                          º   Harvest, Al.  35749   º
                          º   205-726-5511 (work)   º
                          º   205-830-8450 (home)   º
                          º                         º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
 
         ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
         ****************************************************************
 
         TRAKSAT and its companion files is being distributed as
         shareware. You are encouraged to share this software with others
         provided that it is distributed complete with documentation and
         in unmodified form and that no fee or other consideration is
         charged or accepted.
 
         ****************************************************************
         ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
 
 
         TRAKSAT makes no warranty of any kind, either express or implied,
         including but not limited to implied warranties of
         merchantability and fitness for a particular purpose, with
         respect to this software and accompanying documentation.
 
         Paul E. Traufler, author of TRAKSAT, SHALL NOT BE LIABLE FOR ANY
         DAMAGES (INCLUDING DAMAGES FOR LOSS OF BUSINESS PROFITS, BUSINESS
         INTERRUPTION, LOSS OF BUSINESS INFORMATION) ARISING OUT OF THE
         USE OF OR INABILITY TO USE TRAKSAT.
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  2


 
 
 
                              TABLE OF CONTENTS
         -----------------------------------------------------------
 
 
         INTRODUCTION ...........................................  4
         THEORY OF SATELLITE MOTION .............................  5
         HARDWARE REQUIRED TO RUN THE PROGRAM ...................  6
         RUNNING THE PROGRAM ....................................  7
         CHANGING SATELLITE DATA FILES (MAIN MENU FILE OPTIONS)..  9
         READ SATELLITE DATA (MAIN MENU FILE OPTION) ............ 10
         USER DEFINED STAR DATA (MAIN MENU FILE OPTION) ......... 12
         TRACKING STATIONS (MAIN MENU FILE OPTION) .............. 13
         SYSTEM DATE/TIME (MAIN MENU SYSTEM OPTION) ............. 15
         REAL-TIME MODE (MAIN MENU TIME OPTION) ................. 16
         DELTA-TIME MODE (MAIN MENU TIME OPTION) ................ 16
         OUTPUT MODES  .......................................... 18
         ANALYTICAL SOLUTION (MAIN MENU OUTPUT OPTION) .......... 19
         USER DEFINED/ALL SATELLITES ............................ 21
         GROUND TRACKS (MAIN MENU OUTPUT OPTION) ................ 24
         SUN TERMINATOR ......................................... 24
         STAR BACKGROUND (MAIN MENU OUTPUT OPTION) .............. 27
         ORTHROGRAPHIC VIEW (MAIN MENU OUTPUT OPTION) ........... 31
         TABULAR MODES (MAIN MENU OUTPUT OPTION) ................ 32
         VISIBILITY (MAIN MENU VISIBILITY OPTION) ............... 35
         MULTI-TRACK MODE (MAIN MENU OPTION EIGHT) .............. 36
         MULTI-TRACK TABULAR OUTPUT MODE ........................ 38
         QUITTING THE PROGRAM  .................................. 39
         USER DEFINED SATELLITE PLOTTING COLOR .................. 39
         NORAD/NASA 2-LINE SATELLITE DATA ....................... 40
         WHAT ARE THE MEAN CLASSICAL ELEMENTS ................... 42
         MODELS FOR PROPAGATION OF NORAD ELEMENT SETS ........... 47
         THE PROPAGATION MODELS ................................. 47
         COMPATIBILITY WITH NORAD ELEMENT SETS .................. 48
         PROGRAM LIMITATIONS AND ASSUMPTIONS .................... 49
         ACCURACY OF TRAKSAT .................................... 51
         A BRIEF EDITORIAL ...................................... 53
         SPECIAL THANKS ......................................... 54
         QUESTIONS AND COMMENTS ................................. 55
         FUTURE UPGRADES ........................................ 57
         OBTAINING NORAD SATELLITE DATA SETS .................... 58
         FILES REQUIRED FOR TRAKSAT ............................. 59
         BIBLIOGRAPHY ........................................... 60
 
 
                        Trademarks used in this document
         -----------------------------------------------------------------
 
         IBM,PS/2 PC DOS are registered trademarks of International Business
         Machines Corporation.
 
         Microsoft MS, MS-DOS, QuickC, are registered trademarks of
         Microsoft Corporation.
 
         Epson FX,LQ, is a registered trademarks of Epson American Inc..
 
         Hercules is a registered trademark of Hercules Computer Technology.
 
 
     TRAKSAT  Satellite Tracking Program                           Page  3


 
 
 
                 INTRODUCTION
 
 
          Ever since college I have been interested in satellites and
         tracking methods. I have often looked up into the night sky and
         thought, "I know satellites are up there but can I predict when
         and where to look to see one".
 
         I have several small programs to calculate different satellite
         related quantities but there was not one program available to do
         all the things I felt a satellite tracking program should do.
 
         After several years of working in the aerospace field, I decided
         that I could take on such a programing task.
 
         I started it all with a program called STS, it was geared towards
         tracking the space shuttle, but used the same basic orbital
         calculations.
 
         STS, version .95, is available on several BBS around the country,
         see the references at the end of this document.
 
         For a first attempt at such a satellite tracking program I was
         some-what pleased with the results. But I felt there is room for
         improvement and that is where TRAKSAT steps in.
 
         TRAKSAT is a general purpose satellite tracking program, by that
         I mean any satellite that has a NORAD, NASA 2-Line element set
         can be used. There are some limitations in the program along with
         some assumptions, the reader is directed to the section on limits
         and assumptions for further study.
 
         The solution to the satellite motion which is used by TRAKSAT is
         completely analytic and therefore requires no numerical
         integration. This makes the program fast, even faster when a
         coprocessor is used, since the solutions can be evaluated at
         arbitrarily large, or small, time intervals.
 
         The purpose of this program is to provide the user with a means
         of propagating NORAD element sets in time to obtain tracking
         information of the space object.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  4


 
 
 
 
                 THEORY OF SATELLITE MOTION
 
 
 
                 A complete development of the theory required to predict
         the position of an artificial satellite about the earth is not
         presented here because this is not proper place for it. Such a
         development would require a volume in itself and would be more
         of a distraction than an aid to the potential user. Only enough
         of the concepts required for a general understanding plus the
         final results are given. References to detailed works from which
         these results are derived are provided for the more than
         casually interested reader.
 
         At the end of the TRAKSAT operating instructions is a brief
         overview of the fundamentals used in this program and is included
         to help the reader understand the motion of an artificial
         satellite about the earth.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  5


 
 
 
                 HARDWARE REQUIRED TO RUN THE PROGRAM
 
 
         In order to run the program the user will need the following
         hardware;
                       IBM or compatible PC,XT,AT,PS/2,386, 640K Ram
                       (450K FREE RAM IS REQUIRED), Floppy or Hard Disk,
                       Text mode display (25x80), Hercules, CGA, EGA,
                       or VGA graphics (used for plotting only),
                       Math coprocessor is NOT required for TRAKSAT,
                       (IF A COPROCESSOR IS PRESENT IT WILL BE USED *),
                       Epson FX-80 printer or compatible (for graphic print
                       out only), PC DOS or MS DOS version 2.1 or above.
 
         * It should be noted that a coprocessor will be 3 to 4 times
         faster than the emulator version. If the user plans on using the
         real-time tracking mode, a coprocessor will "smooth out" the time
         steps to such a small delta as to appear instantaneously. At any
         rate the real-time mode runs as fast as the host computer can
         calculate the data and update the screen.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The user will not be able to run TRAKSAT on a 360K floppy drive,
         The size of the executable and the earth map data plus a
         satellite data file will simply not fit on the 360K floppy disk.
 
         The best solution to the problem would be run TRAKSAT from a hard
         disk! The prices of hard disks have come down to a point where
         practically all computers have them. If the user needs a "good
         reason" to buy a hard disk, perhaps TRAKSAT can convince them to
         do so.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         To print out the document, TRAKSAT.DOC use the DOS copy command.
         The syntax to use would be "COPY TRAKSAT.DOC PRN", without the
         quotation marks.
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  6


 
 
 
                  RUNNING THE PROGRAM
 
 
         To start TRAKSAT you type "TRAKSAT", without the quotation marks,
         at the DOS prompt. The opening screen will appear and display the
         version number of the program. The earth data file will be loaded
         into memory while displaying the opening screen also. This may
         slow down the loading time on some slower XT type machines.
 
         After the opening screens are displayed the main menu will be
         displayed next. From the main menu the user can control the
         program. The main menu will display the current status of the
         program, i.e., current satellite, output mode, tracking station,
         etc.. The Status Box will always display the current information
         that is loaded in memory. This will help the user to identify the
         modes of operation available in TRAKSAT.
 
         The main menu is the core of the program, i.e. from this menu the
         user can setup satellite data, tracking station data, and output
         selections.
 
         Here is an main menu example;
 
 
        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³               ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
        ³               ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
        ³               ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
        ³               ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
        ³               ³   Û      Version 2.50         ³              ³
        ³               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
        ³                                                              ³
        ³    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
        ³    ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
        ³    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
        ³                                                              ³
        ³                                                              ³
        ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CURRENT STATUS BOX ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
        ³ ³ Tracking Station = Huntsville, AL                         ³³
        ³ ³ Latitiude (deg)  = 34.7317 Longitude  (deg) = -86.5967    ³³
        ³ ³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³³
        ³ ³ Current Satellite   =               File: NASA748.TXT     ³³
        ³ ³ Current Output Mode = Ground Track            : Single    ³³
        ³ ³ Current Time Mode   = Real     Visibility =   LOS         ³³
        ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
         From the Current Status Box the user can see that no satellite is
         currently loaded but the tracking station is Huntsville, Al and
         the default satellite data file is NASA748.TXT. The output mode
         will be Ground Track using the Real time mode and LOS visibility.
 
         If the user selects the Output option from the main menu the
         other options available in TRAKSAT will be displayed. If the user
         selects a different output mode the Current Status Box will
         display that output mode.

     TRAKSAT  Satellite Tracking Program                           Page  7


         A full explaination of the options is included in this document
         but for the most part the user can figure out most of the
         options with out additional help.
 
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         Error messages are displayed for 3 SECONDS, then depending on
         what the error was, program control will return to the user to
         correct the problem.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         All of the menu selections can be changed by either the arrow
         keys, mouse movement, or the first letter of the menu choice.
         (The left mouse button will select the hi-lighted menu option.)
 
         The mouse driver version used in the testing of TRAKSAT was
         Microsoft 6.01. Several other versions and other mice have been
         used with no problems also. (The mouse is disabled during any
         graphics ouput.)
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  8


 
 
                 Main Menu FILE Options
 
 
         The file options from the main menu will allow the user to change
         tracking stations, satellites, and load user defined star data.
         Below is an example of the File options.
 
 
        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³               ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
        ³               ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
        ³               ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
        ³               ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
        ³               ³   Û      Version 2.50         ³              ³
        ³               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
        ³                                                              ³
        ³                                                              ³
        ³    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
        ³    ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
        ³    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
        ³            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                       ³
        ³            ³ Change Satellite File   ³                       ³
        ³            ³ Load Satellite Elements ³                       ³
        ³ ÚÄÄÄÄÄÄÄÄÄÄ³ Read User Star Database ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
        ³ ³ Tracking ³ New Tracking Station    ³                      ³³
        ³ ³ LatitiudeÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  (deg) = -86.5967    ³³
        ³ ³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³³
        ³ ³ Current Satellite   =               File: NASA748.TXT     ³³
        ³ ³ Current Output Mode = Ground Track            : Single    ³³
        ³ ³ Current Time Mode   = Real     Visibility =   LOS         ³³
        ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
                 Change Satellite File
 
         For example; if the user would like to change the name of the
         satellite data file the hi-lighted bar would be placed on the
         Change Satellite File option. (The user could have pressed the C
         key and moved the hi-lighted choice directly to the choice.) To
         select this option press the return (or Enter) key or the left
         mouse button.
 
         The program will display the old satellite data file and prompt
         the user for the new file name. The displayed file name can be
         edited using the arrow keys, or mouse to obtain the desired file.
         After editing the file name the user will press return and the
         program will look for the file. A message will be displayed if
         the file is found and an error message will be displayed if the
         file is not found.
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page  9


 
         The screen will appear simular to;
 
   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   ³                    ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³                    ³
   ³                    ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³                    ³
   ³                    ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³                    ³
   ³                    ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³                    ³
   ³                    ³   Û      Version 2.50         ³                    ³
   ³                    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                    ³
   ³                                                                         ³
   ³         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿       ³
   ³         ³   File  System  Time  Output  Visibility  Run  Quit   ³       ³
   ³         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ       ³
   ³ÚÄÄ< Satellite Filename >ÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                             ³
   ³³ Currently: [NASA748.TXT ] ³ellite File   ³                             ³
   ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙlite Elements ³                             ³
   ³      ÚÄÄÄÄÄÄÄÄÄÄ³ Read User Star Database ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿      ³
   ³      ³ Tracking ³ New Tracking Station    ³                      ³      ³
   ³      ³ LatitiudeÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  (deg) = -86.5967    ³      ³
   ³      ³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³      ³
   ³      ³ Current Satellite   =               File: NASA748.TXT     ³      ³
   ³      ³ Current Output Mode = Ground TrÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
   ³      ³ Current Time Mode   = Real     ³ Satellite data file was found. ³³
   ³      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÀÄ´ Press any key to continue ÃÄÄÙ³
   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
 
                 Load Satellite Elements
 
         To load a particular satellite into memory the user will select
         the Load Satellite Elements option. The current satellite name
         will be displayed for the user to change as required. If a blank
         search string is entered the program will display all of the
         satellites in the data file one at a time until one is accepted
         or the end of file is reached. The Status Box will always display
         the current satellite in memory. (If the satellite name display
         is blank that means no satellite has been loaded.) A maximum
         length of 12 characters is allowed in the search string
 
         This program uses the NASA, or NORAD 2-line satellite element
         data file format to read data into the program, (in this text the
         use of NORAD refers to NASA 2-Line or NORAD satellite element
         data sets). For a full explanation of the NASA 2-line satellite
         element data sets see section; NASA 2-Line Satellite Data.
 
         To help the new user a NORAD satellite date file is included with
         TRAKSAT, see section; Satellite Data Sets.
 
         The search method used by the program will locate the first
         occurrence of what was typed in for a search string when compared
         to the satellite names, i.e. typing in "mi" could locate the
         satellite named "Mir". The search is NOT upper/lower case
         sensitive. If a match is found the full name is displayed and the
         user is asked to accept this data or read for the next occurrence.
 
         If the user does not know ANY satellite names they can enter a
         carriage return, (Return or Enter), and ALL of the satellite names
     TRAKSAT  Satellite Tracking Program                           Page 10


         will be displayed one at a time.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
          TRAKSAT is limited to the first 2000 satellites in any data file.
         If the user has more than 2000 satellites in a data file they will
         need to remove, using a text editor, satellite data sets as to
         include the desired data set in the 2000 limit. This may not prove
         to be a limitation for most users as most satellite data sets have
         less than 150 satellite data ssts.
 
         If no match is found a error message is displayed and the user
         will try another match.
 
 
                 Reading User Defined Stars
 
         TRAKSAT has the data for 58 stars in memory at all times however
         the user can read a properly formatted star data base into memory
         also. To load a User Defined Star Data Base the user will select
         the File option from the main menu and then move the hi-lighted
         bar to the option; Read User Star Database. The program will
         first ask the user for a file name of the star data base and then
         look for the file. If the file is located the program will read
         in the FIRST 1500 stars into memory. The program will then return
         to the main menu.
 
         The user will have the responsibility to check the user defined
         star data for duplicates of the TRAKSAT internal star data. (See
         the section on PROGRAM LIMITATIONS AND ASSUMPTIONS for a list of
         the internal stars used in TRAKSAT.)
 
         See the section on USER DEFINED STAR DATA for the format of the
         star files.
 
         ONCE THE USER DEFINED STAR DATA IS LOADED THE PROGRAM WILL USE
         THE STAR DATA FOR ALL STAR BACKGROUND PLOTS.
 
         *****************************************************************
         ** REMEMBER TO USE EPOCH J2000 FOR ANY USER DEFINED STAR DATA. **
         *****************************************************************
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 11


 
         The screen will be simular to;
 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³          ÚÄ< Star Database Filename >ÄÄ¿                    ³
         ³          ³  Currently: [STARS.DAT   ]  ³                    ³
         ³          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                    ³
         ³ÚÄÄÄÄÄÄÄÄÄÄ³ Read User Star Database ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking ³ New Tracking Station    ³                      ³³
         ³³ LatitiudeÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  (deg) = -86.5967    ³³
         ³³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³³
         ³³ Current SatÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ile: NASA748.TXT     ³³
         ³³ Current Out³ Reading User Star Data ³         : Single    ³³
         ³³ Current TimÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙlity =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
                 TRACKING STATIONS
 
         The last file option, New Tracking Station, will only need to be
         run once, unless a different tracking station is used, by the
         user. The program defaults to using Huntsville, Al. as the
         tracking station, if the user does not want to use the default
         option they can select a city from the city data file. The city
         data file has over 720 of the larger U.S. cities latitude and
         longitudes in it.
 
         The tracking station search works very much like the satellite
         name search. The user is asked for a search string and the first
         occurrence is displayed, then the next one and so on, until no
         more matches are found.
 
         If the user accepts a match some additional data is asked for by
         the program. The altitude above mean sea level in meters and
         hours from Greenwich are required for the tracking station. (Some
         examples of the hours from Greenwich; EDT = -4, CDT = -5,
         CST = -6). If the altitude of the tracking station are not known
         the user can enter zero with out to much loss in accuracy.
 
         If the user can not find a match to the city data then they will
         need to use a text editor to add the city data in the file
         TRAKSAT.CTY or use the closest city in the file.
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 12


         Below is an example screen for Huntsville, Al..
 
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³                ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³               ³
       ³                ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³               ³
       ³                ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³               ³
       ³                ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³               ³
       ³                ³   Û      Version 2.50         ³               ³
       ³                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ               ³
       ³                                                                ³
       ³                                                                ³
       ³     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
       ³     ³   File  System  Time  Output  Visibility  Run  Quit   ³  ³
       ³     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
       ³ÚÄÄ< Tracking Station >ÄÄ¿ÚÄ< Tracking Station Found In File >Ä¿³
       ³³ [Huntsville, AL      ] ³³ Name: [HUNTSVILLE, AL       ]      ³³
       ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
       ³  ÚÄÄÄÄÄÄÄÄÄÄ³ Read User Star Database ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
       ³  ³ Tracking ³ New Tracking Station    ³                      ³ ³
       ³  ³ LatitiudeÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  (deg) = -86.5967    ³ ³
       ³  ³ Altitiude (m)    = 228.60  UTC Offset ÚÄ< Keep Reading? >Ä¿ ³
       ³  ³ Current Satellite   = MIR           Fi³ Yes               ³ ³
       ³  ³ Current Output Mode = Ground Track    ³ No                ³ ³
       ³  ³ Current Time Mode   = Real     VisibilÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
       ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
         If the user accepts this city the program will ask for some
         additional information about the tracking station. The screen
         will appear simular to;
 
 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³                                                             ³
         ³                                                             ³
         ³                                                             ³
         ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CURRENT STATUS BOX ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking Station = Huntsville, AL                         ³³
         ³³ LatitiudÚÄÄ< Tracking Station >ÄÄ¿de  (deg) = -86.5967    ³³
         ³³ Altitiud³ Altitude (m)  [228.6]  ³set (hrs) = -5.         ³³
         ³³ Current ³ Hours From UTC [    ]  ³  File: NASA748.TXT     ³³
         ³³ Current ³ ie, CDT = -5, CST = -6 ³            : Single    ³³
         ³³ Current ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙibility =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
     TRAKSAT  Satellite Tracking Program                           Page 13


                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         If the tracking station changes from the default values the file
         TRAKSAT.DEF will hold the last saved tracking station data. While
         running the program if a new tracking station is selected the
         user will be asked if the old tracking station data should be
         overwritten or not.
 
         If the user saves the current data then the next time TRAKSAT is
         run that new data will be the default else the old TRAKSAT.DEF
         will be used.
 
         A text editor can be used to change the TRAKSAT.DEF data also,
         the user will need to use some caution with this method. The TWO
         EXCEPTIONS are the multi-track options, see the section on its
         recommended use (MAIN MENU OPTION EIGHT) and the user defined
         area, see section; Analytical Solution.
 
         After the tracking station has been chosen the main menu will
         appear waiting for the next user choice.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 14


 
                 Main Menu System Options
 
         The System options can change the system date, time, or both.
         This may prove useful for the user to set the internal DOS clock
         from within TRAKSAT.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         THE SYSTEM HARDWARE CLOCK MAY BE RESET ALSO WITH SOME VERSIONS OF
         MS-DOS OR PC-DOS. Use some caution with this option. Refer to
         your DOS manuals to use the time and date functions.
 
         The System options screen will appear simular to;
 
 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                       ³
         ³                ³ Set System Date    ³                       ³
         ³                ³ Set System Time    ³                       ³
         ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ³ Set Both Date/Time ³  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking StatiÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                      ³³
         ³³ Latitiude (deg)  = 34.7317 Longitude  (deg) = -86.5867    ³³
         ³³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³³
         ³³ Current Satellite   = MIR           File: NASA748.TXT     ³³
         ³³ Current Output Mode = Ground Track            : Single    ³³
         ³³ Current Time Mode   = Real     Visibility =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 15


 
                 Main Menu Time Mode Options
 
         TRAKSAT can propagate satellites in real-time or "delta-time"
         modes. (The delta-time mode is starting at some particular date
         and time using a user defined time increment until a ending
         time is reached.)
 
         To change time modes in TRAKSAT the user can select Time from the
         main menu. The two time mode options will be displayed. If the
         real-time mode is chosen the Current Status Box will display
         Real-Time.
 
         The real-time mode will update the screen as fast as the hardware
         will allow. For an XT class machine with no coprocessor, the
         update time may be 1 to 2 seconds. An AT class computer with a
         coprocessor can whip along at about 0.4 seconds per update. The
         powerful and fast 386 coprocessor equipped machine can sing along
         at 0.1 seconds per update. The average user will not require this
         great of detail but it is included for the advanced user.
 
         If the user would like to track a satellite from say todays date
         to some future date, the delta time mode is the choice to use.
         The basic idea is track from some starting date to some stopping
         date. If the user selects the Delta-Time mode some additional
         information will be required. The starting date and time along
         with the length of the simulation. The time step will also need
         to be entered. The program will display "defaults" that can be
         accepted by the user or edited to suit the users needs.
 
         It is noted that the maximum length, that is from the starting
         date to some future time, of the simulation is 99 days 99 hours
         99 minutes 99 seconds.
 
         An approach most people use with the Delta-Time mode is to pick a
         2-3 minute time step and check the output for any passes near the
         tracking station for that day. Then return back to the Delta-Time
         mode and use a smaller time step to obtain a better estimate of
         the satellite visibility. Another method is to use the analytical
         solution option, see the section on Analytical Solution for more
         information.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The time is read from the system clock, and as such is only as
         accurate as the setting of this clock. The software date and time
         can be set before running TRAKSAT, OR the system date and time
         can be set within TRAKSAT. The System option from the main menu
         will allow the user to change the system date, time or both.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         THE SYSTEM HARDWARE CLOCK MAY BE RESET ALSO IF THE USER HAS MS-
     TRAKSAT  Satellite Tracking Program                           Page 16


         DOS VERSION 3.3 AND ABOVE. Use some caution with this option.
         Refer to your DOS manuals to use the time and date functions.
 
 
         A brief note about tracking satellites.
 
         The accuracy of the data is the most important part of the
         prediction process. NORAD does track some 8000+ objects in orbit
         around the earth, and maintains a data base of the objects. The
         earth modeling and perturbations are the most important factors
         in satellite tracking. This program uses the NORAD element sets
         mainly because they are available and have reasonably good
         accuracy.
 
         If the user would like to "see" a satellite in the night sky the
         precision of 1 or 2 seconds is not important, several minutes may
         not even be that important. This is not to say that the average
         person can not locate the satellite, it is going to pass over
         some site sooner or later, its the time of the passing that is of
         importance.
 
         It could be said that if you tell me where to look for the
         satellite and tell me about when I should be looking for it the
         chances are it will be spotted. The sky is a big place and it
         would be almost impossible to locate a satellite without any help
         from programs such as TRAKSAT.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 17


 
                 Main Menu Output Options
 
         The main menu Output options will control the output modes
         available in TRAKSAT. The output modes available will be
         Analytical Solution, Ground Track, Orthrographic, Tabular, and
         Star Background. (Assuming a single satellite tracking mode is
         desired. The Multi-Track will only have a Ground Track or Tabular
         output option.) If the user selects the Output from the main menu
         the following screen will appear. The user will select either the
         single track mode or the multi-track modes.
 
 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                   ³
         ³                      ³ Single Satellite ³                   ³
         ³                      ³ Multi-Satellites ³                   ³
         ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking Station = HUNTSVILLE, AL                         ³³
         ³³ Latitiude (deg)  = 34.7317 Longitude  (deg) = -86.5867    ³³
         ³³ Altitiude (m)    = 228.60  UTC Offset (hrs) = -5.         ³³
         ³³ Current Satellite   = MIR           File: NASA748.TXT     ³³
         ³³ Current Output Mode = Ground Track            : Single    ³³
         ³³ Current Time Mode   = Delta    Visibility =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
         If the user selects the single satellite option the output will
         be the next choice for the user.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 18


 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³                        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿              ³
         ³                        ³ Analytical Solution ³              ³
         ³                        ³ Ground Tracks       ³              ³
         ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ CUR³ Orthrographic View  ³ÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking Station = HUN³ Tabular Output      ³             ³³
         ³³ Latitiude (deg)  = 34.³ Star Background     ³ -86.5867    ³³
         ³³ Altitiude (m)    = 228ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ -5.         ³³
         ³³ Current Satellite   = MIR           File: NASA748.TXT     ³³
         ³³ Current Output Mode = Ground Track            : Single    ³³
         ³³ Current Time Mode   = Delta    Visibility =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
                 Main Menu Output Analytical Solution Options
 
         TRAKSAT version 2.00 and above has included a very powerful
         option, Analytical Rise & Set. Many people have asked "why use
         this analytical approach ?". Three reasons come to mind speed,
         speed, and speed! The analytical approach used is a closed form
         solution to the problem of determining when a satellite can be
         seen (either LOS or Optical) by a ground tracking station. In
         effect, this problem usually involves the calculation of the
         rise-and-set time (UTC) of a given satellite from a specific
         ground tracking station.
 
         In the past, it has been the custom to solve the problem by
         letting the satellite run through its ephemeris, and checking at
         each instant to see whether the elevation angle of the satellite
         was greater than some minimum value. However, by attacking the
         problem from a different point of view, that is, with the
         eccentric anomaly taken to be the independent variable, it is
         possible to obtain a closed-form solution to the satellite
         visibility problem. Specifically, the closed-form solution is a
         single transcendental equation in the eccentric anomalies
         corresponding to a rise-and-set time for a given orbital pass of
         a satellite. It is more difficult to solve the controlling
         equation than the standard Keplerian equation. However, the
         method offers the advantage that the controlling equation is
         solved only once per orbit period as contrasted with the hundreds
         of times the Keplerian equation must be solved with the standard
         step-by-step technique.
 
         "How much faster is the analytical solution ?" Several
         "benchmarks" were run using the same satellite data sets and
         starting times to determine the speed of each method. If the user
     TRAKSAT  Satellite Tracking Program                           Page 19


         selects the Delta Time Mode and then the Analytical Solution the
         speed difference will be obvious.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The analytical solution methods will use 10 DEGREES AS THE
         MINIMUM ELEVATION ANGLE that the viewer can "see". In practice
         that "assumption" is very well founded. The minimum is NOT user
         selectable in this case.
 
         On the machine used for testing (coprocessor installed) the
         analytical solution runs about 4 seconds per satellite per 24
         hours of simulation time vs. the 120 seconds per 24 hours in the
         delta time mode. (This was on a 386/16 with a 287 coprocessor.)
         (A 386/33 computer with a 387 can crank out 160 satellites per
         minute!!!!)
 
         Use the analytical solution for "rough" estimates and the delta
         time mode for the detailed analysis. The term "rough" implies
         that the analytical solution is not as accurate as the Delta Time
         mode, and in fact that is true. The error (Delta Time mode vs.
         Analytical Solution) is usually LESS then 1 minute for predicted
         rise or set times. (Remember that the analytical solution will
         display results for a satellite elevation ABOVE 10 degrees.) The
         error is the price to pay for the speed advantage.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The analytical solution DOES INCLUDE THE DRAG EFFECTS in the
         calculations, (as of TRAKSAT version 2.30). By including the
         drag effects in the solution a long term prediction can be done
         without a great loss of accuracy.
 
         It has proved helpful for several TRAKSAT users to predict
         several weeks into the future any visible passes and make a note
         of the dates. As the date approaches and newer elements become
         available the user can "improve" the viewing times to finally
         obtain a accurate prediction of the satellites. Using this
         approach the user can mark "special" days when a particular
         satellite should be seen.
 
         The analytical solution will save the user from "looking" for
         satellites that will not be seen, or unfavorable passes.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         If the user selects the analytical solution AND the OPTICAL
         visibility test then only satellites with a mean motion of
         greater than 2.5 revs per day will be calculated. That is any
         satellite that is "near geosync" will not be calculated. This
         approach was necessary due to some of the limits of the
         analytical solution. This should NOT be of to great importance to
         most users as seeing ANY near geosync satellites is VERY
     TRAKSAT  Satellite Tracking Program                           Page 20


         DIFFICULT. The line of sight (LOS) method will still work for the
         near geosync satellites. If the user needs to "see" a near
         geosync satellite than the delta time mode will be required.
 
                 ALL/USER DEFINED SATELLITES
 
         The user has the choice with the analytical solution options to
         select all of the satellites in the data file or some user
         defined satellites. The default will be to read ALL of the
         satellites for these options. The user can define his or her
         "favorite" satellites, up to 25 satellites can be included. The
         user will need to use a word processor to edit the TRAKSAT.DEF
         file and add the satellites names to it. The word processor used
         will need to save the file in PLAIN ASCII format, i.e., NO
         SPECIAL CONTROL CHARACTERS EXCEPT THE END OF FILE MARKER. The
         edlin or PC-Write word processors will do the job nicely for the
         user. An example of the TRAKSAT.DEF file with user defined
         satellites is included below;
 
         column number
 
         123456789012
 
          2447836.50000000 Color = 14 Printer Pins = 9
          HUNTSVILLE, AL         34.7317000  273.4033000    228.60 -5
          NASA678.TXT
             Multi-Track Satellite Names
          Satellite # 1: MIR
          Satellite # 2: SALYUT 7
          Satellite # 3: IRAS
          Satellite # 4: SEASAT 1
          Satellite # 5: EGP
          Satellite # 6: NOAA 9
             User Defined Satellite Names
          IRAS
          SALYUT 7
          COSMOS 1686
          COSMOS 1766
          MIR
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         Remember to start the user defined satellite name in column 2.
         The next 12 characters make up the satellite name, upper or lower
         case makes no difference. If a user defined satellite is NOT
         located in the satellite data file a warning message will be
         displayed. The user defined satellites can be ANY of the
         satellites included in the data file, however, 25 satellites is
         the maximum number allowed. If the user has more than 25
         satellites then select the All Satellite Data Sets option.
 
         That is enough "horn blowing" let us look at an example.
 
         Below is and example output from the analytical solution using
         the screen output option. The visibility method in this example
         was LOS (line of sight) while the starting date was 4-20-1990 @ 0
         UTC hours. The end time was 24 hours.
     TRAKSAT  Satellite Tracking Program                           Page 21


         The "header" at the top of the display will show some vital
         information to the user. The tracking station name and satellite
         data file name along with the visibility method will be displayed
         to remind the user of the current settings.
 
                               (SCREEN OUTPUT OPTION)
 
                    TRAKSAT Version 2.00   Analytical Solution
 Tracking Station: HUNTSVILLE, AL       File: NASA678.TXT   Visibility: LOS
 Satellite    UTC     TIME     LOCAL   TIME      AZIMUTH  MAX   MIN    DURATION
              DATE    HR:MN:SC DATE    HR:MN:SC           ELE   RANGE  HR:MN:SC
 Alouette 1   20Apr90 01:08:32 19Apr90 20:08:32  N  TO SE 25    1905   00:10:32
              20Apr90 02:54:12 19Apr90 21:54:12  NW TO S  43    1387   00:12:12
 Cosmos 398   20Apr90 01:19:02 19Apr90 20:19:02  NW TO E  33    1970   00:16:02
              20Apr90 03:34:48 19Apr90 22:34:48  NW TO SE 74    2069   00:26:48
              20Apr90 05:54:02 20Apr90 00:54:02  W  TO S  21    4272   00:23:02
              20Apr90 20:54:16 20Apr90 15:54:16  NW TO N  10    1100   00:01:16
              21Apr90 01:27:19 20Apr90 20:27:19  NW TO E  39    1879   00:18:19
 Starlette    20Apr90 02:27:41 19Apr90 21:27:41  NW TO E  35    1582   00:13:41
 
 
 
 
                                      Working ...
                                   Press Esc to Quit
 
 
         If the Optical method was selected the header message will
         display so.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The user can NOT stop/start the screen as in the other modes,
         i.e., pressing Esc will STOP the display and terminate the
         analytical solution. This method was chosen to avoid
         inadvertently waiting for the screen to update while in a pause
         mode. The screen update can be slow on a Optical visibility test
         and a NON-coprocessor equipped machine. (There may not be any
         satellites optical visible at all!)
 
         If a file output was selected the header placed in the file has
         the same information as the screen header. Below is an example of
         the analytical solution file output. (The same times as above
         were used but this example used the optical visibility test.)
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 22


 
         Below is the screen or file output option menu.
 
         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»          º
         º           º              TRAKSAT               º          º
         º           ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹          º
         º           º       ANALYTICAL RISE & SET        º          º
         º           ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹          º
         º           º                                    º          º
         º           º      (F) Output To File            º          º
         º           º      (S) Output To Screen          º          º
         º           º          LOS Visibility            º          º
         º           º       Enter Option (F,S) [F]       º          º
         º           º                                    º          º
         º           º                                    º          º
         º           º                                    º          º
         º           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼          º
         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The default is to write output to the file TRAKSAT.OUT. This is
         NOT user selectable, ANY OLD FILES WITH THIS NAME WILL BE
         OVERWRITTEN.
 
                                (FILE OUTPUT OPTION)
                               TRAKSAT  Version 2.00
 
                                Analytical Solution
 
                         Tracking Station: HUNTSVILLE, AL
                              [ Optical Visibility ]
 
 
  Satellite    UTC     TIME     LOCAL   TIME      AZIMUTH  MAX  MIN    DURATION
               DATE    HR:MN:SC DATE    HR:MN:SC           ELE  RANGE  HR:MN:SC
 
 
  Alouette 1   20Apr90 02:54:12 19Apr90 21:54:12  NW TO S   43   1387  00:12:12
  Cosmos 398   20Apr90 01:19:02 19Apr90 20:19:02  NW TO E   33   1970  00:16:02
               20Apr90 03:34:48 19Apr90 22:34:48  NW TO SE  74   2069  00:26:48
               21Apr90 01:27:19 20Apr90 20:27:19  NW TO E   39   1879  00:18:19
  Starlette    20Apr90 02:27:41 19Apr90 21:27:41  NW TO E   35   1582  00:13:41
               20Apr90 02:30:13 19Apr90 21:30:13  NW TO E   55   1241  00:13:13
  LAGEOS       20Apr90 04:57:34 19Apr90 23:57:34  NE TO W   47   6830  00:51:34
               20Apr90 08:22:09 20Apr90 03:22:09  NE TO NW  27   8006  00:40:09
               21Apr90 03:34:44 20Apr90 22:34:44  NE TO SW  70   6108  00:56:44
  GPS-0001     20Apr90 02:33:52 19Apr90 21:33:52  W  TO SE  65  20491  06:47:52
  GPS-0002     20Apr90 05:05:15 20Apr90 00:05:15  NW TO NW  13  24419  01:15:15
  GPS-0005     21Apr90 02:37:23 20Apr90 21:37:23  W  TO SE  65  20533  06:47:23
  GPS-0006     20Apr90 00:16:22 19Apr90 19:16:22  NW TO SW  57  20854  04:27:22
  SME          21Apr90 02:15:21 20Apr90 21:15:21  S  TO NW  29    812  00:05:21
  Salyut 7     20Apr90 09:56:11 20Apr90 04:56:11  SW TO NE  71    413  00:06:11
  Cosmos 1383  20Apr90 02:53:40 19Apr90 21:53:40  N  TO S   50   1293  00:12:40
  IRAS         20Apr90 01:52:33 19Apr90 20:52:33  S  TO SW  23   1793  00:08:33
 
     TRAKSAT  Satellite Tracking Program                           Page 23


         The screen below will be displayed when the file output mode is
         selected and the simulation is over. This case took 423 seconds
         to complete 112 satellite predictions for 24 hours.
 
                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ» º
                  º  º              TRAKSAT               º º
                  º  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹ º
                  º  º       ANALYTICAL RISE & SET        º º
                  º  ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹ º
                  º  º                                    º º
                  º  º      (F) Output To File            º º
                  º  º      (S) Output To Screen          º º
                  º  º          LOS Visibility            º º
                  º  º       Enter Option (F,S) [F]       º º
                  º  º       Input File: NASA678.TXT      º º
                  º  º       Record# 112   of  112        º º
                  º  º       Total Time: 423   Sec        º º
                  º  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
 
 
 
 
 
                 Output Ground Track Options
 
         If the ground track option is entered the program proceeds to
         draw a Mercator projection map of the world. The upper left
         corner is at latitude 90 degrees and longitude -180 degrees,
         while the lower right corner is latitude -90 degrees and
         longitude 180 degrees. The grid spacing is 30 degrees for both
         the latitude and the longitude. A "+" will be plotted for the
         tracking station coordinates, the coordinates from TRAKSAT.DEF or
         the currently loaded data.
 
         The plotting process may take a minute or two on a slow XT type
         computer, something under 2 seconds on the particular computer I
         use.
 
         The user will be asked about displaying the sun terminator. The
         sun terminator is not dependent on the satellite but rather the
         tracking station. The terminator is plotted based on a zero sun
         elevation angle. (That is to say the terminator is the line where
         the sun is "just" below the local horizon.) The terminator is
         accurate to about 10-15 minutes of actual. The effects of the
         local horizon and atmospheric refraction can "shift" the
         terminator a few minutes anyway so great accuracy may not be
         achieved. The sun is plotted as an "+" in the center of the
         terminator. This will tell the user on what side of the
         terminator the tracking station is on. (Daylight or darkness.)
 
         The sun terminator will be "REFRESHED" EVERY 4 MINUTES IN EITHER
         THE REAL OR DELTA TIME MODES. The refresh may take several
         seconds on the slower machines. (About 20 seconds.)
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
     TRAKSAT  Satellite Tracking Program                           Page 24


         THE SUN TERMINATOR PLOTTING PROCESS MAY TAKE A MINUTE OR SO ON A
         SLOW XT TYPE COMPUTER, something under 1/3 second on the
         particular computer I use.
 
         The ground track plot is the only option that will display the
         sun terminator.
 
         The file EARTH.DAT contains the world map data, some 8200 vectors
         in all. This file is compressed to save space and reduce the
         reading time. (TRAKSAT version 2.10 and up has improved the
         compression ratio (45%), older versions of the program can NOT be
         used with this new data file, nor can TRAKSAT use the older data
         file.)
 
         If the EARTH.DAT file is not found an error message will be
         displayed and the program will return to the main menu again.
 
         After the world map is displayed the simulation begins. The
         starting position for the satellite is marked as a yellow filled
         (if that is the user defined color) circle, this was added to
         help locate the starting position. The screen will plot the
         orbital ground trace of the chosen satellite along with other
         valuable data. The top line will have the UTC date and time,
         while the second line will have the local date and time
         displayed. The lower lines will have the tracking data displayed.
 
         An example of the output screen would be;
 
      -----------------------Ý   TRAKSAT Version 1.80  Þ--------------------
     |                                                                      |
     |   UTC   21:37:26.1  Date 12/26/1989  Satellite Name:   MIR           |
     |   Local 15:37:26.1  Date 12/26/1989  Tracking Station: HUNTSVILLE,AL |
     |                                                                      |
     |        (The version number may be different in this display.)        |
     |              (no world map drawn in this example)                    |
     |                                                                      |
     |  Lat     45.1635ø  Azimuth    309.1281ø  Range   7115.4 Km Ph 129.00 |
     |  Long  -175.3926ø  Elevation  -30.1331ø  Rev # 22120 NOT Visible     |
     |                                                                      |
      -----------------------------------------------------------------------
         The Lat and Long are the satellite latitude and longitude. The
         Azimuth and Elevation are as seen from the tracking station,
         while the Range is the distance from the satellite to the
         tracking station.
 
         The azimuth is always between 0 and 360 degrees with north being
         0, east 90 south 180 and so on. The elevation will be always be
         between -90 and +90 degrees. If the elevation is less than zero
         the satellite is below the horizon as seen from the tracking
         station.
 
         The Rev # is based on the input data starting revolution number
         plus the number of revs per day times the days past the epoch
         date, i.e. the formula;
 
           rev = rev_epoch + (mean motion(rev/day) * (epoch date - date).
 
         The epoch refers to the NORAD satellite data set, see section;
         NORAD/NASA 2-Line Satellite Data, for a full explanation of the
     TRAKSAT  Satellite Tracking Program                           Page 25


         input data.
 
         The Ph is the Phase angle. The phase angle is used for the
         amateur radio satellites. The phase angle is based on the mean-
         anomaly, (the position in the orbital plane from the perigee).
         The mean-anomaly is normaly measured from 0 to 360 degrees,
         however the phase angle is from 0 to 256ths of a circle. The
         conversion of degrees mean-anomaly to phase angle is;
 
                       Phase = (mean anomaly (deg))/(360/256).
           (256ths of circle)
 
         It has become common practice with radio amateur satellites to
         use Mean Anomaly to schedule satellite operations.  Satellites
         commonly change modes or turn on or off at specific places in
         their orbits, specified by Mean Anomaly.  Unfortunately, when
         used this way, it is common to specify the mean anomaly in units
         of 256ths of a circle instead of degrees. The phase angle is
         therefore displayed in units of 256ths of a circle.
 
         The last item displayed is based on if the satellite is visible
         from the tracking station. See main menu Visibility options for a
         complete description of the methods used by TRAKSAT to test for
         visibility.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         To stop the display the user can press any key and the screen
         will "freeze". The user will need to press any key again to
         continue the simulation. If the user presses Esc, escape key, the
         simulation will stop and the user will be returned to the main
         menu.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The ground track will continue until the user stops the
         simulation by pressing Escape (Esc). After 8-9 ground tracks have
         been plotted the screen will be "very busy", the user can re-draw
         the screen by pressing Esc, than pressing main menu option five
         and one again. The world map will be drawn again along with the
         new orbital ground tracks. This will cut down on the screen
         "clutter".
 
         The user can print out the screen output with the ground track
         option. To print the output of the screen press "P" or "p",
         without the quotation marks. The print out may take a minute or
         so depending on the type of printer being used. The print out
         will start with the upper right side of the screen.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
     TRAKSAT  Satellite Tracking Program                           Page 26


         If the user selects any graphic output the program will test for
         a graphics adapter and based on the type of graphics hardware
         will select the "highest" graphics mode supported. An example
         would be;
 
                              VGA mode 640x480 pixels,
                              EGA mode 640x350 pixels,
                              CGA mode 640x200 pixels,
                              HGC mode 720x348 pixels (Monochrome).
 
 
                                 ******************
                                 *  SPECIAL NOTE  *
                                 ******************
 
         The Hercules graphics mode requires running the driver
         MSHERC.COM, this is the driver supplied with several Microsoft
         programing languages, before using the TRAKSAT program. Type
         "MSHERC" and then "TRAKSAT" to start the program. (A TRUE
         Hercules card works with TRAKSAT, some clone cards may NOT.)
 
         Do not use a Microsoft mouse AND the Hercules graphics cards
         together, according to Microsoft, as this may cause some
         "problems". Any mouse drivers that are installed should be
         removed before running TRAKSAT with a Hercules card also.
 
         If the hardware does NOT support graphics an error message will
         be displayed and the program will return to the main menu. All of
         the text modes will still be available to the user however.
 
                 Output Star Background Options
 
         The star background is a view looking from the tracking site
         towards the stars. This plot will be useful for producing a "star
         map" to take outside with you to compare the night sky with the
         satellite path.
 
         If the Star Background option has been chosen the program will
         ask the user for some additional data. The user can display the
         visible star names if so desired. (Only the internal star data
         names will be displayed, not the user defined star data.) The
         user will choose what direction to look, i.e., North, East,
         South, or West. The field of view of the star background is 180
         degrees in azimuth and 0 through 90 degrees in elevation. If the
         user selects North the visible range of the azimuth will be 270
         degrees (west) to 90 degrees (east). If the user selects East the
         visible range of the azimuth will be 0 degrees (north) to 180
         degrees (south) with 90 degrees being the center of the screen
         (due east). The option South will display from 90 degrees (east)
         to 270 degrees (west). The option for West will display from 180
         degrees to 360 degrees with 270 degrees (west) being the center
         of the screen (due west).
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 27


 
         An example could be to see a satellite rise out of the west the
         user would select W, that will display from due south through
         west to the north.
 
 
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³              ³ ßßÛßßßßßßßßßßßßßßßßßßßßß      ³              ³
         ³              ³   Û Ûßß Ûßß Û Ü Ûßß Ûßß ßÛßßß ³              ³
         ³              ³   Û Û   ÛßÛ ÛßÛ ßßÛ ÛßÛ  Û    ³              ³
         ³              ³   Û Û   ÛÜÛ Û Û ÛÜÛ ÛÜÛ  Û    ³              ³
         ³              ³   Û      Version 2.50         ³              ³
         ³              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ              ³
         ³                                                             ³
         ³                                                             ³
         ³   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ M A I N    M E N U ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
         ³   ³   File  System  Time  Output  Visibility  Run  Quit   ³ ³
         ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
         ³                                                             ³
         ³              ÚÄ< Direction To Look >Ä¿                      ³
         ³              ³ North                 ³                      ³
         ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄ³ East                  ³ ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿³
         ³³ Tracking Sta³ South                 ³                     ³³
         ³³ Latitiude (d³ West                  ³ (deg) = -86.5867    ³³
         ³³ Altitiude (mÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ (hrs) = -5.         ³³
         ³³ Current Satellite   = MIR           File: NASA748.TXT     ³³
         ³³ Current Output Mode = Tabular Output Screen   : Single    ³³
         ³³ Current Time Mode   = Delta    Visibility =   LOS         ³³
         ³ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 
 
         The star background option will display visible stars from a
         database of 58 navigational stars, the Sun, the planets, and the
         moon. (Not including any user defined star data.)
 
         The term "star background" will be used in this document to mean
         the 58 navigational stars, the Sun, the planets (not including
         the earth), and the moon.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The star data is internal to TRAKSAT, i.e., there are no
         provisions for the user to MODIFY THE INTERNAL STAR DATA at this
         time. Star positions are for Epoch J2000.0, from USNO Floppy
         Almanac 1988, Version 2.11.88, file STAR1.CAT. HOWEVER THE USER
         CAN SUPPLY ADDITIONAL STAR DATA TO THE PROGRAM, see the section
         on USER DEFINED STAR DATA.
 
         The option to print out this "star map" (or any other graphic
         output) is included in TRAKSAT, as of version 1.80 and up. The
         user will require a Epson FX-80 or compatible printer to use this
         feature. Again this will prove valuable to the user in
         determining where and when to look to "see" the satellite, this
         option will work for LOS or Optical visibility modes. To print
         out a screen copy the user will only have to press a "P" or "p".
         After the output is printed the program will continue with the
     TRAKSAT  Satellite Tracking Program                           Page 28


         plot. The user can interrupt the printer process by pressing any
         key, the printer output will stop and the program will continue.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The printer MUST be connected to parallel printer port number 1,
         LPT1. To stop the printer output the user can press any key. A
         Epson FX-80 or graphics compatible printer must be used for any
         output. The print out routines have been tested on several
         different Epson compatible printers without any problems. Some
         laser printers can emulate the Epson printers and will produce
         good results also.
 
         THE DEFAULT NUMBER OF PRINTER PINS (9 OR 24) IS READ FROM THE
         FILE TRAKSAT.DEF. The user can change the "Printer Pins = 9" to
         "Printer Pins = 24" as required for the printer being used.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         If the user has loaded a User Defined Star file the program will
         plot the internal stars first and then plot the user defined
         stars next.
 
         The user will have the responsibility to check the user defined
         star data for duplicates of the TRAKSAT internal star data. (See
         the section on PROGRAM LIMITATIONS AND ASSUMPTIONS for a list of
         the internal stars used in TRAKSAT.)
 
         By default TRAKSAT will display the star names, including the
         planets and the moon and look west. The user will only need to
         change these options by typing in the correct response.
 
 
         *****************************************************************
         ** REMEMBER TO USE EPOCH J2000 FOR ANY USER DEFINED STAR DATA. **
         *****************************************************************
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 29


 
                     An example of a star background would be;
 
        UTC   14: 2:12.2  Date  3/26/1990  Az   211.3715ø  Rev# 23519
        Local  8: 2:12.2  Date  3/26/1990  El   -43.8641ø  Vis  NOT Visible
         ----------------------------------------------------------------
         |    Satellite: Mir       TRAKSAT 1.85                         |
         |                                                              |
       75-                                                              |
         |                                                              |
         |       O Moon                                                 |
       60-                                                              |
         |                                                              |
         |                           EXAMPLE                            |
       45-                       (NO PLOT SHOWN)                        |
         |                  (This is only an example, the               |
         |                   DATA displayed is NOT correct)             |
         |                                                              |
         |                                                              |
       30-                       o Venus                                |
         |                                                              |
         |                                                              |
       15-                                               . Alpharatz    |
         |                                                              |
         |                            west                              |
         ----------------------------------------------------------------
               210        240         270        300        330
 
         the side axis is the elevation while the bottom axis is the
         azimuth. (Observer coordinates are the only output type at this
         time). In this example star names were displayed and the option
         to look west was selected. The "sky track" of the satellite will
         also be plotted on the screen. The top two lines will display the
         local and UTC time and dates, azimuth, elevation, rev, and if the
         satellite is visible (based on the Visibility option setting LOS
         or Optical). The star map background will remain black even if
         the sun has risen. (The version number may be different in this
         display.)
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         If the delta time mode is selected time steps are marked on the
         screen and labeled for the user. It is recommended that the delta
         time mode be used for star backgrounds so a "time tag" can be
         placed on the screen. The real time mode will not place "time
         tags" on the screen. This approach was used to help reduce screen
         clutter, i.e., to many time tags. This method was chosen because
         few people have laptop computers "out in the field" to use for
         viewing aids. A printed "sky map" generated before the nights
         viewing will be of much greater use to most people.
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         It is noted that the star background will be refreshed EVERY 15
     TRAKSAT  Satellite Tracking Program                           Page 30


         MINUTES, in either delta or real time modes. It is therefore wise
         to select a starting time about 15 minutes PRIOR to the time of
         interest and run the program in the delta mode until PAST the
         time of interest. An example of this would be;
 
                           Time of interest 11:30:00 UTC,
                           Starting time 11:23:00 UTC,
                           Time span 00:14:00.
 
         This will provide the user with the "sky map" from 11:23 to 11:37
         UTC and avoid the screen refresh.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         To stop the display the user can press any key and the screen
         will "freeze". The user will need to press any key again to
         continue the simulation. If the user presses ESC, escape key, the
         simulation will stop and the user will be returned to the main
         menu.
 
 
                 Output Orthrographic View
 
         If the user selects the Orthrographic View main menu a 3-D
         orthographic projection of the earth and the satellite will be
         drawn. The perspective will be centered on the tracking station
         coordinates with the altitude above the earth being set by the
         semi-major axis of the satellite to view. A small "X" will mark
         the tracking station coordinates. The grid lines are drawn 10
         degrees apart with the orthographic projections.
 
         The 3-D graphic will plot the "orbital trace" above the planet,
         i.e., not the ground trace, WHILE HOLDING THE EARTH STILL. The
         earth will be non-rotating with the satellite going around it.
 
         The close earth satellites (1000 Km altitude and less) will
         produce a good quality plot while near geosync satellites will
         display the earth as a small hard to see "ball". The highly
         eccentric orbits (ecc. > .3) will not display the complete
         orbital trace due to some limitations of the methods used in
         TRAKSAT. This should not pose much of a concern to most users.
 
         ****************************************************************
         THE 3-D PROJECTION WILL BE SLOW ON XT TYPE COMPUTERS WITHOUT A
         COPROCESSOR SO IF THE USER DOES NOT WANT TO WAIT FOR THE COMPLETE
         EARTH TO PLOT OUT PRESS ANY KEY AND THE EARTH LAND MASS PLOT WILL
         STOP AND THE SATELLITE VIEW WILL START. (Only the grid lines will
         be displayed.)
         ****************************************************************
 
         The screen can be stopped and started the same way as any other
         graphic modes, i.e., any key to freeze and Esc to stop.
 
         At this time the altitude above the earth is not a user changed
         option. If the user would like a polar (either north or south)
         projection select a new Tracking station from the Main Menu File
         options and select either the north, south or even the equator
     TRAKSAT  Satellite Tracking Program                           Page 31


         tracking station coordinates.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         It is recommended that the user edit the TRAKSAT.CTY file and
         change the first three tracking station coordinates to his or her
         LOCAL LONGITUDE. The user will answer the questions about
         tracking station altitude and time zone information based on the
         local conditions.
 
         Below is an example of the TRAKSAT.CTY file with the first three
         "extra" tracking stations included. The format of the tracking
         station is;
 
          City Name     Long. (deg)   Lat. (deg).
 
          'North Pole ',-86.5867,90.0
          'Equator ',-86.5867,.0
          'South Pole ',-86.5867,-90.0
          'Rancho Palos Verdes CA ',-118.403334,33.767501
          'Calaveras County, CA ',-120.566667,38.15
          'Washington (USNO), DC ',-77.06575,38.920556
          'Auburn, AL ',-85.4833,32.6067
          'Birmingham, AL ',-86.81,33.5169
          'Gadsden, AL ',-86.0114,34.0158
          'Huntsville, AL ',-86.5867,34.7317
 
         The TRAKSAT.CTY file can hold a maximum of 1000 tracking stations
         in it. (The file included with TRAKSAT has 725 "cities" in it)
 
 
 
                 Output Tabular Options
 
         TRAKSAT can also produce a tabular output of the satellite
         tracking data, the output is in a text mode not graphics. If the
         user picks Tabular option, the program will display another menu
         asking to include the right ascention & declination or the
         Latitude and Longitude in the output. The output can go to a
         file or the screen also.
 
         The file option output can be edited and printed out by the user
         if so desired.
 
 
         Below is an example of the screen output without the Ra & Dec;
 
       Tracking Station:  HUNTSVILLE, AL           Satellite:  Mir
      Date    Time (UTC)   Azim      Elev   Range      Lat       Long     Rev   
 V
              HR:MN:Sec    Deg       Deg    Km         Deg       Deg
  Thr 25Jan90 01:27:5.550  268.7678 -43.87 9384.23883  -1.65793 -176.815 22575
  Thr 25Jan90 01:27:5.600  268.7689 -43.87 9384.00198  -1.65535 -176.813 22575
  Thr 25Jan90 01:27:5.660  268.7702 -43.87 9383.72069  -1.65229 -176.811 22575
  Thr 25Jan90 01:27:5.710  268.7712 -43.87 9383.48382  -1.64971 -176.809 22575
 
         this example was run using the real-time mode and the default
         tracking station, Huntsville, Al..
     TRAKSAT  Satellite Tracking Program                           Page 32


         In this case the LONG is the satellites longitude, positive (+)
         means EAST longitude while negative (-) means WEST longitude.
 
         The column "V" is the visibility flag, i.e., if the satellite is
         visible the flag is set to "Y" else it is blank.
 
         If the user had chosen to include the Ra & Dec the output would be
         like;
 
       Tracking Station:  HUNTSVILLE, AL           Satellite:  Mir
      Date    Time (UTC)   Azim      Elev   Range      Ra        Dec      Alt   
 V
              HR:MN:Sec    Deg       Deg    Km         HH:MM:SS  DD:MM:SS Km
  Thr 25Jan90 01:27:15.38  268.9799 -43.57 9337.76175  21:58:19 -01:05:53 388
  Thr 25Jan90 01:27:15.44  268.9811 -43.56 9337.47902  21:58:20 -01:05:42 388
  Thr 25Jan90 01:27:15.55  268.9835 -43.56 9336.95618  21:58:21 -01:05:22 388
 
         the user will notice that the latitude and longitude have been
         replaced by the Ra & Dec.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The Ra & Dec are based on the J2000 epoch, 1,1.5,2000 UTC date,
         and are NOT user selectable, perhaps in the next version of
         TRAKSAT. The J2000 epoch is the "current" epoch on most star
         charts.
 
         The user will notice that the header is stationary just the data
         is scrolling. This option is useful for a quick view of tracking
         data, since no graphics are used.
 
         If the user was in delta-time mode the step between outputs would
         be the delta time step value set in main menu option four.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         To stop the display the user can press any key and the screen
         will "freeze". The user will need to press any key again to
         continue the simulation. Pressing ESC will return the user to the
         main menu.
 
         If the output was directed to a file the tracking data output
         file name will consist of the first 8 characters of the satellite
         name with the extension ".PRT" added to the end. The name of the
         output file will be displayed for the user.
 
         An example could be the satellite Mir, the filename for output
         would be "Mir.PRT".
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The program will produce the file xxxxxxx.PRT, the x being the
         current satellite name, if one is not found, but will OVERWRITE
         an old one if found. The user will have the responsibility to re-
     TRAKSAT  Satellite Tracking Program                           Page 33


         name the file after completing a run if they would like to save
         the output.
 
         The output in the file is very similar to the screen output
         option. Below is an example of the file output mode;
 
                               TRAKSAT  Version 1.90
 
                     Tracking Station:  HUNTSVILLE, AL
                     [ Line Of Sight (LOS) Visibility ]
                     Satellite: Mir
 
                               Satellite Data Set:
      1 16609U 86 17  A 90 91.75081924  .00058269  00000-0  66933-3 0  5052
      2 16609  51.6174 355.6250 0013230 341.6181  18.4560 15.61365027236165
 
 
      Date      Time (UTC)   Azim     Elev     Range    Lat     Long     Rev   V
 
                HR:MN:SEC    Deg      Deg      Km       Deg     Deg
 
 
  Thr  25Jan90  01:26:42.04   268.26  -44.61   9494.42   -2.86  -177.67  22575
  Thr  25Jan90  01:26:42.21   268.26  -44.60   9493.63   -2.86  -177.66  22575
  Thr  25Jan90  01:26:42.32   268.27  -44.60   9493.12   -2.85  -177.66  22575
  Thr  25Jan90  01:26:42.43   268.27  -44.60   9492.60   -2.84  -177.65  22575
 
         again this example used the real-time mode. This output is a
         standard 80 columns, for printers or the 25x80 text screen. In
         this example a line of sight (LOS) mode was chosen. If the
         visibility mode was optical the header, the line under the
         tracking station name, would display; [ Optical visibility ].
 
         If the file mode and the real-time mode are chosen the screen
         will display the number of records that have been written to
         file. The program DOES check the remaining disk space and stops
         the program if the record space exceeds available disk space. The
         data prior to exceeding the disk space is written and an error
         message is displayed, no data will be lost.
 
         It is recommended that the real-time mode NOT be used for file
         output, mainly because of the large files that could be produced.
 
         If the file mode and delta-time mode are chosen the screen will
         display the same record count as above, but also the total number
         of records to calculate. This method produces the smallest file
         size the user requires.
 
         The total number of records to calculate would be;
 
         total_records = (stop_time - start_time)/delta_time.
 
         The size of the file is approximately 81 bytes per record,
         therefore 1440 records, one day at one minute intervals, will
         produce a file size of about 116K. (ALL TIME STEPS DISPLAYED).
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
     TRAKSAT  Satellite Tracking Program                           Page 34


         To stop the display the user can press any key and the screen
         will "freeze". The user will need to press any key again to
         continue the simulation. Pressing ESC will return the user to the
         main menu.
 
         The option has been added to TRAKSAT version 1.5, and up, to
         display only the visible passes, based on the setting of the
         visibility options. The program will default to ALL passes.
 
         The output, in the tabular modes, can display Ra & Dec of the
         satellite also. The coordinate used is based on J2000 epoch, this
         was chosen to be used with "current" star charts. The default is
         to include Ra & Dec in the output.
 
 
 
                 Visibility Options
 
         There are two different methods used by TRAKSAT to determine
         visibility. The first method is simply when the elevation is
         greater than zero degrees the satellite will be visible to the
         tracking station. This method is called line of sight (LOS) in
         the program. This method would be suitable for monitoring
         satellite radio transmissions, interesting RF signals no doubt.
 
         It should be noted that at most tracking sites zero degrees
         elevation is not visible due to ground based obstructions, i.e.
         trees buildings, and other such objects. A rule of thumb is if
         you hold out your arm straight and stick out your thumb
         horizontal to the ground so it appears to touch the horizon the
         upper edge of your thumb is about two degrees elevation, while
         your closed fist is about ten degrees elevation.
 
         The second method, optical visibility, requires the satellite to
         be above zero degrees elevation also, however the satellite must
         be sun-lit while the tracking station is in darkness. This
         method would be used for viewing satellites with the aid of say
         binoculars. It is of interest to note that some satellites are
         NOT visible even if the elevation angle is above the horizon,
         because they are in the earth's shadow. It is difficult to
         observe a satellite "coming out" of the earth's shadow, it is
         easier to see the entrance into the shadow.
 
         If the lighting conditions are favorable a "bright" satellite can
         be seen with the naked eye also. The best time for these
         favorable lighting conditions usually occur an hour before sun
         rise or an hour after sun set, as seen at the tracking site. The
         best type of satellite is low, about 250 - 400 kilometer
         altitude, ones for naked eye observations. (Mir, Hubble, Shuttle
         are a good examples.)
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         TRAKSAT version 1.60 and above use NAUTICAL twilight, i.e. the
         sun is greater than or equal to -12 degrees BELOW the local
         horizon, to determine the lighting conditions. The user can not
         change the type of twilight used in TRAKSAT, i.e., civil,
     TRAKSAT  Satellite Tracking Program                           Page 35


         nautical, or astrodynamic.
 
         The type of visibility is set from the main menu visibility
         option, the default is to use the LOS method. If the user would
         like to change the visibility method, select from the main menu
         the visibility option. The Current Status Box will always print
         the type of visibility test that will be performed by the
         program.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         With either method the visual magnitude is NOT calculated. Such
         a calculation would require knowledge about the emissivity of the
         satellite, and atmospheric conditions, neither of which is readily
         available to the user.
 
 
 
                 Output Multi-Tracking Options
 
         TRAKSAT version 1.7 and above have the capability to track
         several satellites at the same time. The main menu output option
         will ask the user for either a single or multi-track of
         satellites. If the user selects Multi-Track the multi-track
         output menu will appear asking the user to select ground track or
         tabular output modes. The Current Status Box will display the
         output option (ground track or tabular) along with the :(Multi)
         title. This will clue the user that the multi-track options are
         active.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The user can ONLY change the satellite names by editing the
         TRAKSAT.DEF file and changing the default names. The format for
         the satellite names is as follows;
 
                       COLUMN
                       1  - through -   16 CAN BE ANYTHING,
                       COLUMN 16 STARTS THE SATELLITE NAME,
                       THE NEXT 12 CHARACTERS USED ARE THE
                       NAMES OF THE SATELLITES TO TRACK.
 
                       Below is an example, this is the data
                       included in the TRAKSAT.DEF file.
 
                        Satellite # 1: MIR
                        Satellite # 2: SALYUT 7
                        Satellite # 3: IRAS
                        Satellite # 4: SEASAT 1
                        Satellite # 5: EGP
                        Satellite # 6: NOAA 9
 
         It is recommended that the FULL name of the satellite be used,
         the search routine will use the first match found and not look
         for any other matches. If the name of a satellite is not found
     TRAKSAT  Satellite Tracking Program                           Page 36


         the output will display a NO DATA, i.e., no data for the
         requested satellite has been loaded.
 
         Six satellites MAXIMUM can be tracked, if the TRAKSAT.DEF has
         fewer than TWO the program will issue a error and return to the
         main menu. (Use the single tracking mode.)
 
         If the ground track option is chosen the program will proceed to
         plot the tracks on the world map. The plots are very similar to
         the single satellite plots, except that for every satellite a
         different colored line is drawn. The order of the colors are;
 
                               1st satellite = yellow
                               2nd satellite = cyan
                               3rd satellite = green
                               4th satellite = lite red
                               5th satellite = lite magenta
                               6th satellite = lite green.
 
                       (The colors can NOT be changed by the user)
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         Users with monochrome monitors will have trouble identifying the
         ground tracks in the multi-track mode as no difference in the
         colors will be seen. As of TRAKSAT version 1.90 and above a
         number (1 - 6) along with the "starting circle" is plotted to
         help identify the satellite on the monochrome screen.
 
         Below is an example of the multi-track ground tracks. It is noted
         that no actual graphics plot is included due to the limits of
         storing graphics and text together.
 
     -------------------Ý    TRAKSAT   Version 1.80    Þ------------------
    |   UTC   17:17:36.3  Date  2/20/1990  Satellite Name: MULTI-TRACKING  |
    |   Local 11:17:36.3  Date  2/20/1990  Tracking Station: HUNTSVILLE, AL|
    |                                                                      |
    |        (The version number may be different in this display.)        |
    |                (no world map drawn in this example)                  |
    |                                                                      |
    |    Mir         Salyut 7    IRAS        SeaSat 1    EGP         NOAA 9|
    |Azi 32.079      227.66      274.10      220.47      4.9673      2.2960|
    |Ele 14.499      -60.75      -50.48      -57.27      33.954      -15.43|
     ----------------------------------------------------------------------
 
         The output will display the ground tracks, the azimuth as seen
         from the tracking station, and the elevation. The elevation is
         the angle above or below the tracking station horizon. The output
         is in degrees, with the time and date formats being; HH:MM:SS.s
         and MM/DD/YYYY. (The version number may be different in this
         display.)
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         No visibility methods, LOS or optical, are used in the multi-
     TRAKSAT  Satellite Tracking Program                           Page 37


         track GROUND TRACK modes. THE TABULAR OUTPUT MODES WILL DETERMINE
         THE VISIBILITY BASED OF THE SETTING OF THE VISIBILITY OPTION,
         (LOS or Optical). (The user can determine the LOS visibility by
         looking at the elevation angles displayed when using the ground
         track option.)
 
 
         MULTI-TRACKING TABULAR OUTPUT MODE
 
         As of TRAKSAT version 2.30 and above a tabular multi-tracking
         mode has been included. The output is in text rather than a
         graphic display mode. Below is an example of the multi-tracking
         tabular output mode. The different satellites will be displayed
         in different colors also, the colors are the same as the ground
         track options.
 
 
  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ    TRAKSAT  Version 2.30    ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
  º                       Tabular Multi-Tracking Mode                         º
  º  Tracking Station: HUNTSVILLE, AL          Input Data File: NASA707.TXT   º
  º                  UTC   00:10:00.0  Date  6/19/1990                        º
  º                  Local 00:10:00.0  Date  6/18/1990                        º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ Mir           ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude   -12.0376ø  Azimuth    283.3060ø  Range 11839.43 Km       º
  º       Longitude   42.4516ø  Elevation  -63.4864ø  NOT Visible             º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ Salyut 7      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude    -5.4339ø  Azimuth    249.6659ø  Range  7706.61 Km       º
  º       Longitude  209.8406ø  Elevation  -33.6718ø  NOT Visible             º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ HST           ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude    21.5907ø  Azimuth    350.3650ø  Range 11762.57 Km       º
  º       Longitude  102.0782ø  Elevation  -60.0983ø  NOT Visible             º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ SeaSat 1      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude    59.6848ø  Azimuth    328.8212ø  Range  7653.05 Km       º
  º       Longitude   20.8611ø  Elevation  -29.3966ø  NOT Visible             º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ EGP           ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude    -2.4094ø  Azimuth    106.5518ø  Range  8414.05 Km       º
  º       Longitude  338.9396ø  Elevation  -27.4664ø  NOT Visible             º
  ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ IRAS          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
  º       Latitude    57.6857ø  Azimuth    354.3749ø  Range  9450.31 Km       º
  º       Longitude   82.8507ø  Elevation  -39.6712ø  NOT Visible             º
  º                                                                           º
  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
         The output of the multi-tracking mode is similar to the bottom
         two lines of a ground track plot. The output will display only
         satellites found in the element file.
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 38


 
 
 
                 Main Menu Quit Option
 
         This option will stop the TRAKSAT program and return the user to
         DOS. If the tracking station data was changed during the program
         execution, the user will be asked if the new data should replace
         the old default data. That choice is up to the user to decide.
         The old data will be displayed along with the current data to help
         the user with the choice. THE DEFAULT IS NOT TO SAVE THE NEW
         DATA.
 
 
 
         USER DEFINED SATELLITE PLOTTING COLOR
 
         TRAKSAT version 2.40 and above allows the user to choose what
         color to plot the satellite in. The color is changed in the file
         TRAKSAT.DEF. Below is an example of a TRAKSAT.DEF file with the
         default satellite plotting color as light yellow (14). To change
         the color edit the file TRAKSAT.DEF and change the Color = XX to
         any of the colors allowed. (If a incorrect color is chosen the
         light yellow will be used as a default.)
 
                                   COLUMN NUMBER
         123456789012345678901234567890123456789012345678901234567890123456
 
          2447836.50000000  Color =  14 Printer Pins = 9
          HUNTSVILLE, AL         34.7317000  273.4033000    228.60 -5
          NASA678.TXT
             Multi-Track Satellite Names
          Satellite # 1: MIR
          Satellite # 2: SALYUT 7
          Satellite # 3: IRAS
          Satellite # 4: SEASAT 1
          Satellite # 5: EGP
          Satellite # 6: NOAA 9
             User Defined Satellite Names
          IRAS
          SALYUT 7
          COSMOS 1686
          COSMOS 1766
          MIR
 
                   The user can choose from the pallette of;
 
            2 = GREEN                          9 = LIGHT BLUE
            3 = CYAN                          10 = LIGHT GREEN
            4 = RED                           11 = LIGHT CYAN
            5 = MAGENTA                       12 = LIGHT RED (sun term.)
            6 = BROWN                         13 = LIGHT MAGENTA
            7 = WHITE (map land mass color)   14 = LIGHT YELLOW
            8 = GRAY                          15 = BRIGHT WHITE
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 39


 
                       NORAD/NASA 2-LINE SATELLITE DATA
 
 
         NORAD maintains general perturbation element sets on all resident
         space objects.  These element sets are periodically refined so as
         to maintain a reasonable prediction capability on all space
         objects. In turn, these element sets are provided to users.
 
         The input file of current orbital elements can be obtained form
         several BBS around the country. One such BBS is the Celestial BBS
         at (513) 427-0674 in Fairborn, Ohio, the SYSOP is T.S. Kelso.
 
         See section; Obtaining Satellite Data, for more information on
         obtaining satellite data.
 
         I have included a file of the latest elements for over 130
         orbiting satellites. See section; Files Required To Run TRAKSAT.
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
         The following was downloaded from Celestial BBS, T.S. Kelso SYSOP.
 
         Effective January 1986, this system began posting the most recent
         element sets received from NASA/Goddard Space Flight Center for
         several categories of satellites:  Amateur Radio, Earth
         Resources, Manned Spacecraft, Navigation, Weather, and NASA's 30
         Day Specials (which contain objects launched within the last 30
         days and are often easy to spot visually).  More specifically,
         these include the following satellites or satellite series:
         OSCAR, Radio Sputnik, UOSAT, Cosmos, LandSat, SeaSat 1, SPOT,
         Mir, Salyut 7, Soyuz, LDEF, US Space Shuttle, NAVSTAR (GPS),
         GOES, Meteor, and NOAA.
 
         These elements will be maintained in ASCII format in the file.
         Data for each satellite will consist of three lines in the
         following format:
 
         AAAAAAAAAAA
         1 NNNNNU NNNNNAAA NNNNN.NNNNNNNN +.NNNNNNNN +NNNNN-N +NNNNN-N N NNNNN
         2 NNNNN NNN.NNNN NNN.NNNN NNNNNNN NNN.NNNN NNN.NNNN NN.NNNNNNNNNNNNNN
 
         Line 1 is a eleven-character name. Lines 2 and 3 are the standard
         Two-Line Orbital Element Set Format identical to that used by
         NASA and NORAD.  The format description is:
 
         Line 2
         Column     Description
         01-01     Line Number of Element Data
         03-07     Satellite Number
         10-11     International Designator (Last two digits of launch year)
         12-14     International Designator (Launch number of the year)
         15-17     International Designator (Piece of launch)
         19-20     Epoch Year (Last two digits of year)
         21-32     Epoch (Julian Day and fractional portion of the day)
         34-43     First Time Derivative of the Mean Motion (rev/day^2)
                   or Ballistic Coefficient (Depending of ephemeris type)
     TRAKSAT  Satellite Tracking Program                           Page 40


         45-52     Second Time Derivative of Mean Motion (Blank if N/A)
         54-61     BSTAR drag term if GP4 general perturbation theory was used.
                   Otherwise, radiation pressure coefficient.
         63-63     Ephemeris type
         65-68     Element number
         69-69     Check Sum (Modulo 10)
                   (Letters, blanks, periods = 0; minus sign = 1;
                    plus sign = 2)
 
 
         Line 3
         Column     Description
         01-01     Line Number of Element Data
         03-07     Satellite Number
         09-16     Inclination [Degrees]
         18-25     Right Ascension of the Ascending Node [Degrees]
         27-33     Eccentricity (decimal point assumed)
         35-42     Argument of Perigee [Degrees]
         44-51     Mean Anomaly [Degrees]
         53-63     Mean Motion [Revs per day]
         64-68     Revolution number at epoch [Revs]
         69-69     Check Sum (Modulo 10)
 
                   All other columns are blank or fixed.
 
         Example:
 
         NOAA 6
         1 11416U          86 50.28438588 0.00000140           67960-4 0  5293
         2 11416  98.5105  69.3305 0012788  63.2828 296.9658 14.24899292346978
 
         For a description of the mean orbital elements see section; What
         Are The Mean Classical Elements.
 
         Note that the International Designator fields are usually blank,
         as issued in the NASA Prediction Bulletins.  All epochs are UTC.
         Satellites will be ordered by their NASA Catalog Number.  The
         data file will be updated as soon as possible after receipt of
         new element sets or whenever element sets are received for the
         Space Shuttle.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 41


 
 
 
         The following pages contain a brief overview of the methods used
         in TRAKSAT and are included to help the reader understand the
         mechanics of a orbiting satellite about the earth.
 
 
 
                 WHAT ARE THE MEAN CLASSICAL ELEMENTS
 
 
         Five independent quantities called "orbital elements" are
         sufficient to completely describe the size, shape and orientation
         of an orbit. A sixth element is required to pinpoint the position
         of the satellite along the orbit at a particular time. The
         classical set of six orbital elements are defined as:
 
                 1. a, semi-major axis, a constant defining the size of
                    the conic orbit.
 
                 2. e, eccentricity, a constant defining the shape of the
                    conic orbit.
 
                 3. i, inclination, the angle between the Z axis, i.e.
                    like the North Pole, and the angular momentum vector,
                    h = R X V, i.e. the vector R crossed with the vector V.
 
                 4. ê, longitude of the ascending node, the angle, in the
                    fundamental plane, between the direction of the
                    vernal equinox and the point where the satellite
                    crosses the fundamental plane in a northerly
                    direction, (ascending node).  This angle is measured
                    counterclockwise when viewed from the north side of
                    the fundamental plane.
 
                 5. w, argument of periapsis, the angle, in the plane of
                    the satellite's orbit, between the ascending node and
                    the periapsis point, measured in the direction of the
                    satellite's motion.
 
                 6. T, time of periapsis passage, the time when the
                    satellite was at periapsis.
 
                 6a. Sometimes the time of periapsis passage is replaced
                    by the true anomaly, v, the angle, in the plane of
                    the satellite's orbit, between perigee and the
                    position of the satellite at the particular time, t0,
                    called the epoch.
 
                                  * (To convert from T to v)
                                    v = (360 deg) * t0 / T
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 42


 
         The sharp reader will notice that the NORAD elements do NOT
         include the semi-major axis, a. It is possible to calculate the
         semi-major axis with the data in a NORAD elements set. The
         approach would be;
 
                 1. Convert the mean motion into degrees per second.
                    and calculate the time to complete one orbit, this
                    will be called the period.
 
                 2. Using the period and the earth's gravitational
                    constant, mu, the semi-major axis can be calculated.
 
                                  (equations used)
 
                 xn_s = (mean motion * 360)/86400
                 per  =  360/xn_s
                 a    = ((per^2 * mu)/(4*ã^2))^(1/3)
 
                   mu = 3.986012d+14 km^3/sec^2.
 
 
         The starting point for the study of motion of one body orbiting
         another, such as an artificial satellite about the earth, is
         always the two-body problem; i.e., two point masses attracted to
         each other according to Newton's Law of Universal Gravitation,
         the inverse square law. The solution is well-known; the two
         bodies move about each other in conic sections. For bounded
         motions, such as those of an earth satellite, this conic is
         either a circle or an ellipse.
 
         The problem can be formulated in different ways, but is always
         convenient to chose a coordinate system with the origin centered
         at one of the bodies. The position of the second body then can
         be specified, for example, by giving its initial cartesian
         position and velocity coordinates and then integrating the
         equations of motion to find the future positions and velocities.
         The cartesian system is not the most convenient one in which to
         represent the motion because an analytic solution cannot be
         obtained and the integrations must be done numerically.
         By adopting a polar coordinate system, one is able to effect an
         analytic solution referred to above which can be specified in
         terms of six constants of motion; five orbital elements,
         a,e,i,w,ê and the time of pericenter passage T. The last
         constant can be, and usually is, replaced by the mean anomaly M
         which is a linear function of time. This is a very convenient way
         to specify the initial position and velocity of a satellite and
         it also allows an easy visualization of the motion. The position
         and velocity of the satellite at any future time can be
         specified in terms of these six constants, a,e,i,w,ê,M and
         time.
 
         In realistic applications, such as artificial satellites about
         the earth, there are forces acting on the satellite in addition
         to the inverse square force although this is the dominate one.
         Other gravitational forces are due to distant bodies such as the
         moon and sun but the principal additional gravitational forces
         are due to the non-sphericity of the earth. All of the
         gravitational forces are conservative and can be represented by
     TRAKSAT  Satellite Tracking Program                           Page 43


         a potential function. In addition to these extra gravitational
         forces, there are non-conservative forces such as atmospheric
         drag. All of these forces other than the inverse square force
         are called perturbations. The prediction of motion considering
         these additional forces is called Perturbation Theory.
         The orbital elements, constant for pure two-body motion, become
         slowly varying functions of time when the perturbations are
         considered. Differential equations describing the time rates of
         change of the elements are called the Lagrange Planetary
         Equations, LPE and can be found in any standard book on
         celestial mechanics. Considering conservative forces only, which
         can be represented by a potential function, the part of the
         potential other than the two-body part is conventionally called
         the disturbing function, represented by R, and the LPE are:
 
                    .
                    a = 2 / n a * ( ëR / ëM )
 
                    .
                    e = (-(1-eý)^« / naýe)*ëR/ëw+(1-eý/naýe)*ëR/ëM
 
                    .
                    i = cot i/(naý(1-eý)^« * ëR/ëw - ëR/(ëênaý(1-eý)«)
 
                    .
                    w = (1-eý)^« * ëR / naýeëe - cot i * ëR/(naý(1-eý)^«)*ëi)
 
                    .
                    ê = ëR/(naý sin i *(1-eý)^«) * ëi)
 
                    M = n - 2ëR/naëa - 1-eý * ëR/(naýe * ëe).
 
                         * where ë is the partial derivative
 
         starting from the very simple representation of the gravitational
         potential between two point masses of magnitude m0 and mi
         separated by distance r as;
 
                                V = -G * (m0 * mi)/r
 
         one can, by applying this to a satellite of mass m0 and to every
         infinitesimal mass point mi of the earth and integrating over the
         whole earth, arrive at the following potential function for the
         earth;
                  ì                   n ì              n    m
         V=-æ/r(1-ä JnPn (sinë)(re/r)^ +ä ä Jnm (re/r)^  Pn^ (sinë)cos(m(à-à))).
 
                n=2                     n=2m=1                             mn
 
         The first term is the one giving pure two-body motion and the
         additional terms are the perturbing terms. The first sum, zonal
         harmonics, represents the flattening and other distortions
         relative to the equator and the second sum, tesseral harmonics,
         represents the non-uniformity of the earth in longitude. If, as
         is frequently done, one assumes that the earth possesses
         rotational symmetry, then the second sum vanishes. The neglect of
         the second sum usually produces no noticeable effects except in
         the case of geosynchronous satellites. Then one must consider
         those terms which cause slow long-period drifts of the
         geosynchronous position.
 
     TRAKSAT  Satellite Tracking Program                           Page 44


         For close earth satellites one can usually take about three terms
         from the first sum and get very accurate results; even the first
         term alone will produce very satisfactory results in most cases
         for short-time periods.
 
         The Jn are constants which depend on the mass distribution in the
         earth and are deduced from analysis of observed satellite
         motions. The currently accepted values of J2, J3, and J4, which
         are used in TRAKSAT, are;
                                                    -3
                                  J2 = 1.082616 X 10
 
                                                    -6
                                  J3 = -2.53881 X 10
 
                                                    -6
                                  J4 = -1.65597 X 10  .
 
         The Pn (sin ë) are Legendre polynomials of index n and are even
         functions of sin ë for n even and odd functions for n odd. The J2
         term describes the flattening of the earth and the J3 term the
         so-called pear shape. J2, which is three orders of magnitude
         larger than J3, gives rise to secular changes in the elements w,
         ê, and M while J3 gives rise to long_period oscillations in e and w.
         In general, even harmonics cause long-period and secular changes
         in the elements, and odd harmonics cause long-period
         oscillations.
 
         Short-period oscillations can result from all terms; but since J2
         is so much larger than the other coefficients, generally only the
         J2 short-period terms are considered. Secular terms are those
         which monotonically increase or decrease with time. For first
         order solutions this change with time is linear. Long-period
         terms are those which oscillate with a period of typically one to
         two months, and short-period terms are those which oscillate with
         a period of one orbital period or some rational fraction of it.
         To finish formulating the problem, the disturbing function is
         expressed in terms of the orbital elements and then the
         appropriate partial derivatives are taken and substituted into
         the LPE. One then has a coupled set of first order non-linear
         ordinary differential equations. Because they are non-linear, they
         can be solved only by various approximation methods. The usual
         method is to assume that the solutions can be represented in some
         type of power series expansion in a small parameter and arrive at
         sets of approximation equations which can be a close
         representation of the real motion, at least over short-time
         periods.
 
         The complete solution consists of the sum of the secular terms,
         short-period terms, and the long-period terms; i.e.,
 
                 a    = a  + a  + a  .
                  osc    s    sp   lp
 
 
                                 ******************
                                 * IMPORTANT NOTE *
                                 ******************
 
 
     TRAKSAT  Satellite Tracking Program                           Page 45


         I have NOT included the actual equations used in the program in
         this document for obvious reasons, i.e. they are long and hard to
         type in with a text based word processor. If you have an interest
         in these equations they are in several references I have listed.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 46


 
 
 
                 MODELS FOR PROPAGATION OF NORAD ELEMENT SETS
 
        NORAD maintains general perturbation element sets on all
        resident space objects.  These element sets are periodically
        refined so as to maintain a reasonable prediction capability on
        all space objects.  In turn, these element sets are provided to
        users.
 
         The most important point to be noted is that not just any
         prediction model will suffice.  The NORAD element sets are "mean"
         values obtained by removing periodic variations in a particular
         way.  In order to obtain good predictions, these periodic
         variations must be reconstructed (by the prediction model) in
         exactly the same way they were removed by NORAD.  Hence,
         putting NORAD element sets into a different model (even though
         the model may be more accurate or even a numerical integrator)
         will result in degraded predictions.
 
         All space objects are classified by NORAD as near-Earth (period
         less than 225 minutes) or deep-space (period greater than or
         equal 225 minutes). Depending on the period, the NORAD element
         sets are automatically generated with the near-Earth or deep-
         space model.
 
         The PROGRAM will calculate the satellite period and know which
         PREDICTION MODEL TO USE.
 
 
                 THE PROPAGATION MODELS
 
         Two mathematical models for prediction are used by TRAKSAT. The
         first of these, SGP4, was developed by Ken Cranford in 1970 (see
         Lane and Hoots 1979) and is used for near-Earth satellites.  This
         model was obtained by simplification of the more extensive
         analytical theory of Lane and Cranford (1969) which uses the
         solution of Brouwer (1959) for its gravitational model and a
         power density function for its atmospheric model (see Lane, et al
         1962).
 
         The next model, SDP4, is an extension of SGP4 to be used for
         deep-space satellites.  The deep-space equations were developed
         by Hujsak (1979) and model the gravitational effects of the moon
         and sun as well as certain sectoral and tesseral Earth harmonics
         which are of particular importance for half-day and one-day
         period orbits.
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 47


 
                  COMPATIBILITY WITH NORAD ELEMENT SETS
 
         The NORAD element sets are currently generated with either SGP4
         or SDP4 depending on whether the satellite is near-Earth or deep-
         space.
 
         For SGP4 and SDP4 users, the mean motion is first recovered from
         its altered form and the drag effect is obtained from the SGP4
         drag term (B*) with the pseudo-drag term being ignored.  The
         value of the mean motion can be used to determine whether the
         satellite is near-Earth or deep-space (and hence whether SGP4 or
         SDP4 was used to generate the element set).  From this
         information the program will decide whether to use SGP4 or SDP4
         for propagation and hence be assured of agreement with NORAD
         predictions.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 48


 
 
                PROGRAM LIMITATIONS AND ASSUMPTIONS
 
 
 
         The ephemeris equations DO include the zonal harmonics, through
         2nd order, of the gravitational potential.  This implies a
         gravitational field produced by an oblate spheroidal earth
         unsymmetrical with respect to the equator, pear-shaped. In other
         words, the ephemeris equations contain J2, J3, and J4 terms. The
         currently accepted values of J2, J3, and J4, which are used in
         TRAKSAT, are;
                                                    -3
                                  J2 = 1.082616 X 10
 
                                                    -6
                                  J3 = -2.53881 X 10
 
                                                    -6
                                  J4 = -1.65597 X 10  .
 
 
         The earth equatorial radius used by TRAKSAT is; 6378.135 Km,
         while the flattening factor used is 1/298.257 (both are from the
         1972 WGS models).
 
 
         The program TRAKSAT models only ELLIPTICAL orbital motion about
         the earth. That is, the orbital eccentricity MUST BE LESS THAN
         ONE and GREATER THAN ZERO. Very small eccentricities are
         acceptable, i.e., such as 1.0E - 5.
 
 
 
         STARS USED IN TRAKSAT
 
         The star background option will use the following list of stars
         for the display. The star data values are from USNO Floppy
         Almanac 1988, Version 2.11.88, file STAR1.CAT using Epoch J2000
         coordinates.
 
                     Bayer Name            Proper Name
                     ----------            -----------
 
                     Ursae Minoris         Polaris
                     Andromedae            Alpheratz
                     Phoenicis             Ankaa
                     Cassiopeiae           Schedar
                     Ceti                  Diphda/Deneb Kaito
                     Eridani               Achernar
                     Arietis               Hamal
                     Eridani               Acamar
                     Ceti                  Menkar
                     Persei                Mirfak
                     Tauri                 Aldebaran
                     Orionis               Rigel
                     Aurigae               Capella
                     Orionis               Bellatrix
     TRAKSAT  Satellite Tracking Program                           Page 49


                     Tauri                 Elnath
                     Orionis               Alnilam
                     Orionis               Betelgeuse
                     Carinae               Canopus
                     Canis Majoris         Sirius
                     Canis Majoris         Adhara
                     Canis Minoris         Procyon
                     Geminorum             Pollux
                     Carinae               Avior
                     Lambda Velae          Suhail
                     Carinae               Miaplacidus
                     Hydrae                Alphard
                     Leonis                Regulus
                     Ursae Majoris         Dubhe
                     Leonis                Denebola
                     Corvi                 Gienah
                     Crucis                ACrux
                     Crucis                GaCrux
                     Ursae Majoris         Alioth
                     Virginis              Spica
                     Ursae Majoris         Alkaid
                     Centauri              Hadar
                     Centauri              Menkent
                     Bo”tes                Arcturus
                     Centauri A            Rigil Kentaurus
                     Librae                Zubenelgenubi
                     Ursae Minoris         Kochab
                     Coronae Borealis      Alphecca
                     Scorpii A             Antares
                     Triangulii            Atria
                     Ophiuchi              Sabik
                     Lambda Scorpii        Shaula
                     Ophiuchi              Rasalhague
                     Draconis              Eltanin
                     Sagittarii            Kaus Australis
                     Lyrae                 Vega
                     Sagittarii            Nunki
                     Aqilae                Altair
                     Pavonis               Peacock
                     Cygni                 Deneb
                     Pegasi                Enif
                     Gruis                 Al Na ir
                     Piscis Austrini       Fomalhaut
                     Pegasi                Markab
 
 
 
         USER DEFINED STAR DATA
 
         The option of using your own star data in TRAKSAT is
         included. Up to 1500 stars can be included in a data file.
 
 
                ** ALL STAR DATA WILL NEED TO BE FOR EPOCH J2000. **
 
         The following description of the data base format is included
         for the user. All star data files are in standard ASCII code. See
         section; Files Required To Run TRAKSAT for a sample star data
         file.
 
     TRAKSAT  Satellite Tracking Program                           Page 50


                User defined star data has the following format:
 
                           GGGCCC HHMMD+DDMM +M.M +C.CC
                           ----------------------------
                           GAMCAS 00567+6043 +2.4 -0.15
                           GA2AND 02039+4220 +2.3 +1.37
                           39 ARI 02479+2915 +4.5 +1.11
                           HR961  03203+7744 +5.5 +0.19
 
         where GGG is the first three characters of the Greek name of the
         star OR the first two characters and a superscript number OR the
         Flamsteed number of the star. Alpha is ALP, beta is BET, gamma is
         GAM, and so on. Omicron and Omega are abbreviated OI and OE to
         distinguish them. CCC is the standard three-letter abbreviation
         of the constellation name -- ORI for Orion, UMA for Ursa Major,
         CVN for Canes Venatici. If the star has neither Greek letter nor
         Flamsteed number, then GGGCCC becomes is "HR" plus the four-digit
         Yale Bright Star Catalog number.
 
         HHMMD+DDMM is the star's location in right ascension and
         declination coordinates for Epoch J2000. HH is hours, MM is
         minutes, and D is decimal minutes of RA. +DD is declination
         degrees and MM is declination minutes. The coordinates, as given,
         are precise enough for virtually any computer graphics
         application. +M.M is the star's visual magnitude in yellow light,
         essentially how bright the star appears to the eye. The sign is
         necessary because some of the brightest stars, like Sirius, have
         negative magnitudes.
 
         Finally +C.CC is the B-V "color index" of the star. This number
         ranges from -0.25 to +2.5. The "bluest" stars have the lower or
         negative B-V color, while red stars have color indices over 1.6
         or so. The Sun has a B-V of +0.62, and is a yellow-white star.
         TRAKSAT does not use the color data for any calculations. We thus
         decode the examples as: Gamma Cassiopeiae, a medium-bright blue
         star at 0 hours 56.7 minutes right ascension and +60 (degrees)
         43' declination; Gamma-2 Andromedae as a reddish star of
         approximately the same brightness; 39 Arietis doesn't have a
         Greek letter name; and HR 961 is the 961st entry in the Yale
         Bright Star Catalog, barely visible to the naked eye.
 
         The user defined star data option will NOT display the star
         names. (There would not be any room on the screen to see the
         orbital track!) The format used is popular with several star map
         programs and should be available to the user. (A star file is now
         included with TRAKSAT.)
 
 
 
 
         ACCURACY OF TRAKSAT
 
         Several people have asked the question; " How accurate is
         TRAKSAT ?". To answer such a question one must define a set of
         limits. The real "acid test" is to have a prediction from TRAKSAT
         and then go outside and observe that satellite, taking note of
         the time and position of the satellite. A comparison between
         actual observed data and predicted can then be determined.
 
     TRAKSAT  Satellite Tracking Program                           Page 51


         Another approach is to compare the output from TRAKSAT against
         several other satellite tracking programs. Both the public domain
         and the commercial markets have several good tracking programs
         that the user could compare with.
 
         The later approach, that is the comparison between tracking
         programs, has been carried out by several people including
         myself. The output from TRAKSAT compares very well with many of
         the "current" tracking programs (both commercial and public
         domain). It could be concluded from a simple test of TRAKSAT that
         it agrees with several other tracking programs. (Gee we all can't
         be wrong!)
 
         The next step is one of comparing predicted output and observed
         data. The most popular use for TRAKSAT has been in the optical
         sighting options. The optical sighting of a satellite will be the
         "acid test" used for this accuracy test.
 
         First a note about NASA 2-line elements, low earth satellites
         (about 15 rev per day satellites) have larger disturbances from
         the atmosphere than higher satellites. The drag on a satellite
         can cause purtubations greater than the J2 terms therefore the
         drag term is of great importance. The very latest elements for
         the low earth satellite can greatly improve the prediction
         process, while the higher satellites do not require as current of
         elements. (The term low will be in the range of 250 - 375
         kilometers altitude.)
 
         Reports about TRAKSAT (and its predictions) have been made on the
         MIR satellite along with several other low earth satellites. The
         bottom line being LESS THAN 30 SECONDS ERROR (prediction vs.
         actual) for 10 day old satellite element sets. If the satellite
         elements are 20 days old the error is about 60 seconds. If the
         elements a only a day or two old, errors of less than 10 seconds
         are possible (several reports have been made about 2-10 seconds
         of error).
 
         The position data is on the money, it is the time at that
         position that usually drives the accuracy of the observation.
 
         The higher earth satellites generally have less than 30 seconds
         of error for 20 day old elements.
 
         A NOTE MUST BE MADE ABOUT THE ERROR ANALYSIS, THE ASSUMPTION IS
         MADE THAT NO ORBITAL MANEUVERING WAS DONE TO THE SATELLITE DURING
         THE "TEST" PERIOD. (The STS-31, the Hubble launch, was a prime
         example of several orbital maneuvers changing the predicted
         observed times).
 
         In general it can be said that the most current elements are the
         best ones for planning the evenings viewing. (Elements over 30
         days old can have a very large error to them). Element sets 7 -14
         days old will be acceptable for most users.
 
         NORAD/NASA updates the satellite elements for this very reason,
         to keep the prediction process accurate.
 
     TRAKSAT  Satellite Tracking Program                           Page 52


 
 
         A BRIEF EDITORIAL
 
         One of the first decisions to be made when setting out to write a
         program is the choice of a programming language. I'm an Aerospace
         Engineer working for a company in Huntsville, Al. My job title
         is; Trajectory Analysis Engineer. I work with NASA, mostly the
         shuttle program, and design trajectories for several upcoming
         shuttle missions. I have written large trajectory simulations
         programs, for the most part they were written in FORTRAN.
 
         I know FORTRAN is not the best language to use for programs that
         use graphics, but Microsoft has come up with the ideal solution.
         Microsoft FORTRAN, version 4.0 and higher, can call BASIC, C, and
         PASCAL routines. Microsoft FORTRAN version 5.0 also contains graphic
         routines that were used in TRAKSAT, these graphic routines are the
         same as used in QuickC version 2.5.
 
         Most (75%) of the TRAKSAT program is written in FORTRAN to get
         the best speed and high precision mathematics and C, Microsoft C
         version 6.0, for some useful utilities and the menus. I have
         found this combination to be very powerful and useful for program
         development.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 53


 
 
 
         SPECIAL THANKS
 
 
         I would like to take this opportunity to thank the many people
         who helped me either directly or indirectly on this program.
 
         First of all my wife, Anita, who understands why I have a hobbie
         like computers and enjoy working with them. She has not
         complained about the many hours, in excess of 600 hours, I have
         spent working on TRAKSAT.  TRAKSAT version 2.45 has some 21,000
         lines of code and IS STILL GROWING.
 
         Dave Ransom Jr., of Rancho Palos Verdes, CA. has kept me going
         when my interest in the program was slipping away. I did use the
         city data from his excellent program ASTROCLOCK. I also used
         several of the references Dave listed in his program. I would
         highly recommend his program to any person interested in
         astrodynamics.  The documentation supplied with ASTROCLOCK is in
         itself very interesting reading and very well done. I could only
         hope that someday TRAKSAT will have that level of
         professionalism. My thanks to Dave and his wife Vicki.
 
         John Williams and Dr. Jeff Wallach, from the Dallas DataLink BBS,
         have been very helpful in this project also. They have offered
         data and a helping hand with TRAKSAT.  The DataLink BBS has a
         vast amount of satellite information along with other interests.
         I would recommend it to others interested in satellite tracking.
         The DataLink BBS is THE place to learn about obtaining satellite
         images. My thanks to John and his family.
 
         I would also like to thank T.S. Kelso, SYSOP of the Celestial BBS
         where current satellite data can be downloaded. Several satellite
         tracking programs are also available on his BBS along with a vast
         amount of satellite information.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 54


 
 
 
 
         QUESTIONS AND COMMENTS
 
 
                 I would very much like to hear from anyone interested in
         this program and astrodynamics in general. I have not included
         the source code to TRAKSAT mainly because most people do not have
         a Microsoft FORTRAN compiler nor a working knowledge of FORTRAN.
         The high cost ($500.00) of both the FORTRAN and C compilers makes
         the cost of working on a project like TRAKSAT expensive also.
 
         As for the choice of FORTRAN compiliers there are many fine
         products out and I have used many of them. However, the only
         compilier that supports mixed language is Microsoft. For this
         reason alone I would recommend it to others interested in
         programming.
 
         At this time I feel that TRAKSAT is still going through some
         "growing pains"  and I would like the chance to improve it and
         add new features. The only way this can happen is if you, the
         user, takes the time to leave me messages or mail on problems or
         suggestions. I will try to answer your messages in a timely
         manor.
 
         One of the major goals of this project is to make the finest,
         easiest to use, satellite tracking program available. A program
         the average person can use and successfully track satellites.
 
         I would suggest the user to OBTAIN A COPROCESSOR if they do not
         have one already. A coprocessor speeds up math intensive
         programs, such as TRAKSAT, to a level that was only dreamed about
         a few years ago.
 
         Please feel free to contact me to discuss TRAKSAT or other
         computer problems. I can reached through the RPV BBS;
 
                         RPV BBS
                         Rancho Palos Verdes, Ca.
                         213-541-7299
                         24 hours, 2400/1200 baud.
 
         This BBS is owned and operated by Dave Ransom Jr.. I call up the
         BBS three or four times a week to check my mail and do some file
         transfers. This BBS is geared towards Astronomical interests. The
         latest version of ASTROCLOCK can be downloaded from this BBS
         also.
                            Other BBS's I frequent are;
 
             Celestial RCP/M                     DataLink RBBS System
             Fairborn, Ohio                      Dallas, Texas
             513-427-0674                        214-394-7438
             24 hours, 2400/1200 baud,           24 hours, 9600/2400/1200 baud.
 
         I can also be reached at work or home, please no calls after 10
         PM Central Time. Please leave a phone number and the best time to
         call on any messages that require by personal attention. My work
     TRAKSAT  Satellite Tracking Program                           Page 55


         number has an answering machine pick-up if I can not be reached.
         The last, and slowest method to reach me is with the U.S. mail
         service, I will respond with a phone call if at all possible.
 
                         Paul E. Traufler
                         111 Emerald Drive
                         Harvest, Al.  35749
 
                         Phone (work) 205-726-5511
                         Phone (home) 205-830-8450
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 56


 
 
 
 
         FUTURE UPGRADES
 
 
         To obtain the latest version of TRAKSAT, several BBSs around the
         country keep it online. The BBSs listed under section; Questions
         and Comments list several places to obtain the current version.
         Compuserve has TRAKSAT and many other releated files also.
 
         For a small fee ($10.00) I will mail TRAKSAT on a disk, 360K,
         1.2M, if that is the easiest way to obtain the latest version,
         (1.2M is best for me). Please contact the author for more
         information.
 
         ***** FLASH ********** FLASH ********** FLASH ********** FLASH *****
 
                                 SAVE YOUR PRINTER!
 
         Thats right save your printer from printing out the TRAKSAT
         document file (60+ pages). Send $20.00 to the author and receive
         a laser printed copy.
 
 
         ***** FLASH ********** FLASH ********** FLASH ********** FLASH *****
 
 
         TRAKSAT and its companion files is being distributed as
         shareware. YOU ARE ENCOURAGED TO SHARE THIS SOFTWARE WITH OTHERS
         PROVIDED THAT IT IS DISTRIBUTED COMPLETE WITH DOCUMENTATION AND
         IN UNMODIFIED FORM AND THAT NO FEE OR OTHER CONSIDERATION IS
         CHARGED OR ACCEPTED.
 
         *****************************************************************
         *****************************************************************
 
         THERE IS NO CHARGE FOR THIS PROGRAM, but in the spirit of the
         shareware concept, if the end user finds this package useful, and
         would like to help fund development of enhancements to this
         package, any amount that the end user feels is appropriate for
         the value received in using this package will be gladly accepted
         (perhaps $15.00). Please mail any donations to the above address.
 
         ANYONE WHO SENDS A DONATION WILL RECEIVE A PERSONALLY REGISTERED
         COPY OF TRAKSAT AND BE PLACED ON THE UPDATE LIST FOR FUTURE
         UPDATES TO THE PROGRAM. This copy will give the user credit for
         supporting the shareware concept.
 
         *****************************************************************
         *****************************************************************
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 57


                 OBTAINING NORAD SATELLITE DATA SETS
 
         The following BBS's have the current satellite data files;
                         Celestial RCP/M
                         Fairborn, Ohio
                         SYSOP: T.S. Kelso
                         513-427-0674
                         24 hours, 2400/1200 baud,
                         8 bit NO parity 1 stop.
 
                         Datalink RBBS System
                         Dallas, Texas
                         SYSOP: Dr. Jeff Wallach
                         214-394-7438
                         24 hours, 9600/2400/1200 baud,
                         8 bit NO parity 1 stop.
 
                         RPV BBS
                         Rancho Palos Verdes, Ca.
                         SYSOP: Dave Ransom Jr.
                         213-541-7299
                         24 hours, 2400/1200 baud,
                         8 bit NO parity 1 stop.
 
 
         To obtain the elements from the Celestial RCP/M BBS, (with the
         least amount of trouble), just dial up the BBS and login. The
         next step is to type "F" (without the quotes) to go to the Files
         section, then to area #1. The next step is to type "D", for
         download and then type "BULLETIN.ARC" as the file to download,
         open an XMODEM file transfer mode with your telecommunications
         software. This will transfer the NASA 2-line elements to a file
         on the users computer. Log out of the BBS and then unarchive the
         file using several of the unarchiving programs, (PAK, ARC,
         PKZIP, etc.).
 
         The downloaded file will have some characters at the
         top of the file that will need to be removed with a word
         processor (this MUST save the file in pure ASCII, i.e., PC-Write,
         Edlin etc. works very well).
 
         (This method assumes that an account is available to the user).
 
         NASA can provide up to 20 satellite data sets (HARD COPY FORM
         ONLY) if the user writes and requests them. This service is free
         but the user will need to enter the elements into a file for use
         with TRAKSAT. (This is done the old fashion way, you TYPE them!)
 
                         NASA Goddard Space Flight Center
                         Control Center Support Section
                         Code 513
                         Greenbelt, Md.  20771
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 58


 
 
                 FILES REQUIRED TO RUN TRAKSAT
 
         The following files should have been included in the archive
         file;
 
               TRAKSAT.EXE  The program.
               TRAKSAT.DEF  The default data for the tracking station.
               TRAKSAT.CTY  The city file for tracking stations.
               TRAKSAT.DOC  TRAKSAT program documentation.
                 EARTH.DAT  World map data file.
               NASA753.TXT  This is the latest NORAD satellite data set,
                            (as of 26 September, 1990, element set #753).
                  READ.ME   Latest notes about the program.
                MSHERC.COM  This utility is used for Hercules graphics.
                MODERN.FON  This is a font file used for the graphics.
 
 
                 STARS.DAT  This is a star data base that is NOT required
                            to run TRAKSAT, it is optional. This data file
                            can be used in the user defined star data
                            option.
 
                            STARS.DAT is almost identical to the star
                            database used with Richard Berry's (Editor of
                            ASTRONOMY) program STARS.BAS. For
                            compatibility, I have retained the same
                            database format. According to Mr. Berry's
                            documentation file STARS.DOC, his database is
                            essentially the same database used for the
                            StarDome map printed in the center spread of
                            ASTRONOMY every month.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
     TRAKSAT  Satellite Tracking Program                           Page 59


 
         BIBLIOGRAPHY
 
 
                 THe following sources were used to prepare and test the
                 TRAKSAT program.
 
 
         Meeus, Jean, ASTRONOMICAL FORMULAE FOR CALCULATORS, 3rd Edition,
         Willmann-Bell, Inc., Richmond, VA. 1985.
 
         Duffett-Smith, Peter, PRACTICAL ASTRONOMY WITH YOUR PERSONAL
         COMPUTER, Cambridge University Press, New York, NY. 1986.
 
         Danby, John, FUNDAMENTALS OF CELESTIAL MECHANICS, 2nd Edition,
         Willmann-Bell, Inc., Richmond, VA. 1988.
 
         Bate-Mueller-White, FUNDAMENTALS OF ASTRODYNAMICS, Dover
         Publications, Inc. New York, NY. 1971.
 
         Forsythe-Malcolm-Moler, COMPUTER METHODS FOR MATHEMATICAL
         COMPUTATIONS, Prentice-Hall, Inc. Englewood Cliffs, NJ. 1977.
 
         USAF-Ford Aerospace Corporation, ORBITAL MECHANICS, O&M Training
         Section, Sunnyvale, CA. 1982.
 
         Moulton, F. R., CELESTIAL MECHANICS, Macmillan Company, New York,
         NY. 1960.
 
         Brand, L., VECTOR ANALYSIS, John Wiley and Sons, New York, NY.
         1957.
 
         Geyling-Westerman, INTRODUCTION TO ORBITAL MECHANICS, Addison
         Wesley, Whippany, NJ. 1971.
 
         Brouwer, D., "Solution of the Problem of Artificial Satellite
         Theory without Drag", Astronomical Journal 64, 378-397, November
         1959.
 
         Hilton, C.G. and Kuhlman, J.R., "Mathematical Models for the
         Space Defense Center", Philco-Ford Publication No. U-3871, 17-28,
         November 1966.
 
         Hoots, F.R., "A Short, Efficient Analytical Satellite Theory".
         AIAA Paper No. 80-1659, August 1980.
 
         Hoots, F.R., "Theory of the Motion of an Artificial Earth
         Satellite", accepted for publication in Celestial Mechanics.
 
         Hujsak, R.S., "A Restricted Four Body Solution for Resonating
         Satellites with an Oblate Earth", AIAA Paper No. 79-136, June
         1979.
 
         Hujsak, R.S. and Hoots, F.R., "Deep Space Perturbations Ephemeris
         Generation", Aerospace Defense Command Space Computational Center
         Program
         Documentation, DCD 8, Section 3, 82-104, September 1977.
 
 
     TRAKSAT  Satellite Tracking Program                           Page 60


 
         Kozai, Y., "The Motion of a Close Earth Satellite", Astronomical
         Journal 64, 367-377, November 1959.
 
         Lane, M.H. and Cranford, K.H., "An Improved Analytical Drag
         Theory for the Artificial Satellite Problem", AIAA Paper No. 69-
         925, August 1969.
 
         Lane, M.H., Fitzpatrick, P.M., and Murphy, J.J., "On the
         Representation of Air Density in Satellite Deceleration Equations
         by Power Functions with Integral Exponents", Project Space Track
         Technical Report No. APGC-TDR-62-15, March 1962, Air Force
         Systems Command, Eglin AFB, FL.
 
         Lane, M.H. and Hoots, F.R., "General Perturbations Theories
         Derived from the 1965 Lane Drag Theory", Project Space Track
         Report No. 2, December 1979, Aerospace Defense Command, Peterson
         AFB, CO.
 
         Bellman, R. and Kalaba, R.E., "Modern Analytic Computational
         Methods in Science and Mathematics", American Elsevier Publishing
         Company, Inc. 1967.
 
         Escobal, P.R., "Methods of Orbit Determination", John Wiley and
         Sons, New York, NY. 1965.
 
         Craig, C. John, "Microsoft QuickC Programmer's Toolbox",
         Microsoft Press, Redmond Washington 1990.
 
         El'yasberg, P. E., "Theory of Flight of Artificial Earth
         Satellites", Israel Program for Scientific Translations Ltd.,
         1967. (Translated from Russian)
 
         King-Hele, Desmond, "Observing Earth Satellites", Van Nostrand
         Reinhold Co. Inc., 1983.