----------------------------------------------------------------------
------------ FREELIB: The FREE Assembly Language Library -------------
--------------- Copyright (C) April 1996 Tenie Remmel ----------------
----------------------------------------------------------------------

1. Introduction ................................ Line 15
2. Terms of use/Legal disclaimer ............... Line 34
3. Processors, calling conventions ............. Line 55
4. Re-assembling ............................... Line 91
5. Program Syntax .............................. Line 116
6. Procedure Reference ......................... Line 176
7. Future additions, bug reporting ............. Line 1652
    

1.  Introduction.

  FREELIB is a library of 130 procedures that may be useful for
  programming in assembly language.   As the name implies, this
  is public domain, completely free for all non-commercial use.
  If you find this library useful,  you are strongly encouraged
  to contribute some of your own routines for possible addition
  to FREELIB.  Full source code is included, so if you find any
  bugs (!)  or wish to make changes to any of the routines, you
  can.  However, if you do make any improvements, please notify
  the author,  so that FREELIB  can continue to be expanded and
  improved. If you modify any part of this library, you may not
  distribute it, for free or not, without prior permission from
  the author (see below).

  Be sure to read the sections 2, 3 and 5 carefully,  including
  the miscellaneous notes in section 3.


2.  Terms of use/Legal disclaimer.
 
  This software is hereby released into the public domain,  and
  may  therefore  be freely  copied and distributed  within the
  following restrictions: 

      1).  It is distributed in its original,  unmodified form,
           including all source code and documentation.

      2).  No fee is charged for use, copying or distribution.

      3).  The program may not be  included with other goods or
           services supplied for a fee, unless specific written
           permission to do so is obtained  in advance from the
           author.  (E-mail: tjr19@mail.nwlink.com)

  This program is provided AS-IS without any warranty,  express
  or implied, including  but not limited to warranty of fitness
  for a particular purpose.


3.  Processors, calling conventions, string type, etc.

  FREELIB is programmed in 80186 assembly language.  This is to
  ensure compatibility with as many computers as possible,  but
  not sacrificing very much speed.

  FREELIB uses the  Pascal calling convention.   The parameters
  are  pushed on the stack in order,  and the calling procedure
  does not have to worry about stack cleanup.  This seems to be
  the fastest method,  and it also helps in debugging... if the
  wrong number of arguments are pushed to call a procedure, the
  program will crash, which is much more obvious than the weird
  results produced with the 'C' convention, etc.

  Notice that in the source code,  the syntax is given by a 'C'
  style prototype.  Why a 'C' prototype?  Well, Pascal does not
  have prototypes, and the 'C' prototype is useful to concisely
  show the syntax of a procedure on one line.

  Misc. Notes:   Many of the routines assume  DS = CS,  so make
  sure that this is the case.   The program is intended to be a
  .COM file, but .EXE files are possible as long as the DS = CS
  restriction is met.   Do not use uninitialized data,  it will
  confuse the memory manager.  Use dynamically allocated memory
  instead.  The fixed-point numbers are 16:16, and signed.  The
  strings are ASCIIZ (null-terminated) strings, like in C.  The
  long integers can be either signed or unsigned,  depending on
  which multiply, divide and shift you use.  When clock timings
  are given,  they always include the call/return,  and exclude
  the argument pushes.   Even though some  procedures require a
  character argument,  a word-sized value must still be pushed.
  There is no way to push a byte value.   The files TEXT???.INC
  are not to be included in your programs.  They are internally
  used by the High-Res Text Mode routines in FREELIB3.ASX.  The
  colorset in High-Res Text Mode is different, see below.

  Colorset in High-Res Text Mode:

  0 = Black         8 = Dark Gray
  1 = Dark Green    9 = Red
  2 = Green         10 = Orange
  3 = Light Green   11 = Yellow
  4 = True Blue     12 = Sky Blue
  5 = Dark Purple   13 = Dark Blue
  6 = Magenta       14 = Cyan
  7 = Light Gray    15 = White


4.  Re-assembling FREELIB.

  A batch file (REDO.BAT) is provided for this purpose.   These
  source files are .ASX files (ASsembly eXtended) which contain
  multiple modules.  A utility (SPLIT.COM) is included to split
  the .ASX files.  SPLIT.C is the 'C' source to SPLIT.COM.  The
  batch file takes care of splitting the files. However, if you
  wish to add a new .ASX file  (in addition to FREELIB1-3), you
  must modify the batch file, otherwise it will be ignored.

  SPLIT outputs TLIB  command file codes.   SPLIT takes zero or
  one arguments.  When run with no arguments, it produces codes
  that end the command file.   When run with an argument  (what
  it is doesn't matter)  it produces codes that continue to the
  next file.

  In the .ASX files, a line starting with three tildes (~) that
  are followed by a file name without extension will denote the
  beginning of a new module.   Either make sure that all of the
  module names start with 'C_' or modify the REDO.BAT file.  If
  you put any .ASM  files with names starting with  'C_' in the
  FREELIB directory, be warned: they will be deleted along with
  the temporary .ASM files created by SPLIT.


5.  Program syntax for use with FREELIB.

  Your program should do a near call, or jump, to the 'startup'
  procedure at the beginning. The main body of the program must
  be in the procedure 'main', which must be declared public.

  On entry to main, the number of arguments is in CX and a list
  of near pointers to the arguments is at offset DI.  DS and ES
  both equal CS.  AX, BX, DX, SI, and BP are undefined.

  You must declare as  external all procedures  that you intend
  to use.  One way to simplify this is with a macro:
  
;**************************************

Macro       lcall prced             ;; library call

            extrn prced:near        ;; declare as external
            call prced              ;; call procedure

EndM

;**************************************

  and then you would replace  'call' with  'lcall' when calling
  library procedures.

  This is a skeleton program:

;**************************************

Ideal                               ; ideal mode

Public      main                    ; declare main as public
Extrn       startup:near            ; declare startup procedure

Macro       lcall prced             ;; library call

            extrn prced:near        ;; declare as external
            call prced              ;; call procedure

EndM

Model Tiny                          ; tiny model
CodeSeg                             ; code segment
Org 100h                            ; .COM file start

Start:      jmp startup             ; start up program

Proc        main                    ; main procedure

            ret                     ; return

EndP        main

End Start                           ; entry at 'Start'

;**************************************


6.  Reference: Syntax and description of all FREELIB procedures.

  -------------------------------------------------------------
  ------------ Initialization and Exit Procedures -------------
  -------------------------------------------------------------

  ---------- startup            Start program

    jmp startup

    This procedure must be jumped to at the beginning of
    your program.  (See Section 5.)

    This procedure calls 'main'.  It also does internal
    initialization, and sets null Ctrl-C and divide-error
    handlers.

  ---------- exit               Exit program

    push retcode
    call exit

    This procedure exits your program with a return code.
    If exit is not used, the return code is the value of
    AX on return from main.

  -------------------------------------------------------------
  ---------------------- File Procedures ----------------------
  -------------------------------------------------------------

  ---------- fopen              Open file

    push offset filename
    push filemode
    call fopen
    ; AX = handle
    
    This procedure opens a buffered file.  The handle is
    returned in AX.  This handle is NOT a DOS handle.
    If it is used as such, the results are unpredictable.
   
    The file modes are:
    
    0     Open for Read-Only (open if it exists, fail if not)
    1     Modify for Read/Write (open if it exists, create if not)
    2     Open for Read/Write (open if it exists, fail if not)
    3     Create for Read/Write (truncate if it exists, create if not)

  ---------- fclose             Close file

    push handle
    call fclose

    This procedure closes a buffered file.

  ---------- fgetc              Get char from file

    push handle
    call fgetc
    ; AX = char

    This procedure gets a character from a buffered file.
    If the end of file is reached or an error occurs, -1
    is returned.

  ---------- fputc              Put char to file

    push handle
    push char
    call fputc
    ; AX = return code

    This procedure puts a character to a buffered file.
    If the end of file is reached or an error occurs, -1
    is returned, otherwise the character is returned.

  ---------- fread              Read block from file

    push handle
    push size
    push offset buf
    call fread
    ; AX = return code

    This procedure reads a block from a buffered file.  The
    number of characters read is returned.  If this is less
    than the requested size, the end of file was reached or
    an error occured.

  ---------- fwrite             Write block to file

    push handle
    push size
    push offset buf
    call fwrite
    ; AX = return code

    This procedure writes a block to a buffered file.  The
    number of characters written is returned.  If this is
    less than the requested size, an error occured.

  ---------- fseek              Set file pointer

    push handle
    push pos_hi
    push pos_lo
    push mode
    call fseek
    ; AX = return code

    This procedure sets the position of the file pointer.
    The position is a long integer.  If an error occurs, 0
    is returned, otherwise a nonzero value is returned.

    The seek modes are:

    0     Seek from beginning of file
    1     Seek from current position
    2     Seek from end of file

  ---------- ftell              Get file pointer

    push handle
    call ftell
    ; DX:AX = file pointer

    This procedure returns the position of the file pointer.

  ---------- fsetbuf            Set file buffer size

    push size
    call fsetbuf

    This procedure sets the file buffer size.  It does not
    affect currently open files.  It only affects files that
    are opened after this call.  The default size is 512
    bytes, but it may be set to from 128 to 32752 bytes.
    If the size requested is greater than 32768, the high
    bit is simply masked off, f.i. 33024 will produce 256.

  ---------- ftrunc             Truncate file

    push handle
    call ftrunc
    ; AX = return code

    This procedure truncates a buffered file at the current
    position.  If an error occurs, 0 is returned, otherwise
    a nonzero value is returned.

  ---------- fdel               Delete file

    push offset filename
    call fdel
    ; AX = return code

    This procedure deletes a file.  If an error occurs, 0 is
    returned, otherwise a nonzero value is returned.
    
  ---------- fmove              Move/Rename file

    push offset oldname
    push offset newname
    call fmove
    ; AX = return code

    This procedure moves and/or renames a file.  If an error
    occurs, 0 is returned, otherwise a nonzero value is
    returned.

  -------------------------------------------------------------
  --------------- Directory and Disk Procedures ---------------
  -------------------------------------------------------------

  ---------- mkdir              Create Directory

    push offset dirname
    call mkdir
    ; AX = return code

    This procedure creates a directory.  If an error occurs,
    0 is returned, otherwise a nonzero value is returned.
    
  ---------- rmdir              Remove Directory

    push offset dirname
    call rmdir
    ; AX = return code

    This procedure deletes a directory.  If an error occurs,
    0 is returned, otherwise a nonzero value is returned.
    
  ---------- setdir             Set Current Directory

    push offset dirname
    call setdir
    ; AX = return code

    This procedure sets the current directory.  If an error
    occurs, 0 is returned, otherwise a nonzero value is
    returned.
    
  ---------- getdir             Get Current Directory

    push offset buffer
    call getdir

    This procedure returns the current directory.
    The full path is returned in 'buffer'.
    
  ---------- setdrive           Set Current Drive

    push dr_num
    call setdrive

    This procedure sets the current drive.  The numbers are
    the same as the DOS drive numbers.  (0 = default, 1 = A,
    2 = B, 3 = C, etc.)
    
  ---------- getdrive           Get Current Drive

    call getdrive
    ; AX = drive number

    This procedure returns the current drive.  The numbers
    are the same as the DOS drive numbers.  (0 = default,
    1 = A, 2 = B, 3 = C, etc.)
    
  ---------- getdfree           Get Free Disk Space

    push dr_num
    call getdfree
    ; DX:AX = amount of free space

    This procedure returns the amount of free disk space
    on a drive.  The number returned is in bytes.
    

  -------------------------------------------------------------
  ----------------- Memory Manager Procedures -----------------
  -------------------------------------------------------------

  ---------- allocmem           Allocate Memory

    push size
    call allocmem
    ; AX = pointer

    This procedure allocates memory.  If there was not a big
    enough block of memory, -1 is returned, otherwise a
    pointer to the block of memory is returned.

  ---------- freemem            Free Memory

    push ptr
    call freemem

    This procedure frees memory.  If 'ptr' does not point to
    a valid block, nothing happens.  If free blocks abut the
    block to be freed, they are coalesced.

  ---------- getmfree           Get Free Memory

    call getmfree
    ; AX = size of largest free block

    This procedure returns the size of the largest free
    block of memory.  If there are no free blocks, 0 is
    returned.

  ---------- faralloc           Allocate Far Memory

    push size
    call faralloc
    ; AX = segment

    This procedure allocates far memory.  If there was not
    a big enough block of memory, -1 is returned, otherwise
    the segment of the memory block is returned.  The size
    must be specified in paragraphs (16 bytes each).  This
    calls the DOS allocate memory service.

  ---------- farfree            Free Far Memory

    push seg
    call freemem

    This procedure frees far memory.  If 'seg' is not the
    segment of a valid memory block, the results will be
    undefined.  If free blocks abut the block to be freed,
    they are coalesced.  This calls the DOS free memory
    service.

  ---------- getfarfree         Get Free Far Memory

    call getfarfree
    ; AX = size of largest free block

    This procedure returns the size of the largest free
    block of far memory.  If there are no free blocks, 0
    is returned.


  -------------------------------------------------------------
  ----------------- Put/Get String Procedures -----------------
  -------------------------------------------------------------

  ---------- puts               Put String

    push offset string
    call puts

    This procedure writes a string to the screen.  If the
    STDOUT handle is redirected, this still works.  The
    string is output literally, using Int 29h.

  ---------- fputs              Put String to File

    push handle
    push offset string
    call fputs

    This procedure writes a string to a file.  If an error
    occurs, -1 is returned, otherwise a nonzero value is
    returned.  The handle is a FREELIB handle, not a DOS
    handle.

  ---------- xputs              Put String, Generalized

    push offset outfunc
    push offset string
    call xputs

    This procedure outputs a string using a user-defined
    function.  The function must take one word argument,
    the character to output, save all registers, and return
    with a 'Ret 2' to clean up the stack.

  ---------- gets               Get String

    push offset buffer
    push max
    call gets

    This procedure inputs a string from the keyboard.  The
    string of maximum 'max' chars will be put into 'buffer'.
    Any excess characters will be discarded.  This procedure
    allows simple editing using the <BkSp> key.

  ---------- fgets              Get String from File

    push handle
    push offset buffer
    push max
    call fgets

    This procedure reads a line from a file.  The string of
    maximum 'max' chars will be read into 'buffer'.  The
    line must end with a CR/LF pair.  An entire line will be
    input even if it exceeds 'max' characters.  Any excess
    will be discarded.  The handle is a FREELIB handle, not
    a DOS handle.

  ---------- xgets              Get String, Generalized

    push offset outfunc
    push offset buffer
    push max
    push terminator
    call xgets

    This procedure reads a logical line using a user-defined
    function.  The function must take zero arguments and
    return in AL the character input.  No register except
    AX may be changed.  The value 'terminator' must be
    returned on end of logical line.  The string of maximum
    'max' chars will be read into 'buffer'.  An entire
    logical line will be input even if it exceeds 'max'
    characters.  Any excess will be discarded.


  -------------------------------------------------------------
  ------------- Formatted String Print Procedures -------------
  -------------------------------------------------------------

  ---------- printf             Print Formatted String

    push offset fmtstr
    push offset arglist
    call printf

    This procedure prints a formatted string to the screen.
    It is similar to the 'printf()' in 'C'.  In the format
    string, the '%' character is special.  The '%' character
    can be followed by the following characters, which
    indicate what type of argument to print:

      %d        Integer
      %x        Hex integer
      %s        String
      %c        Character
      %ld       Long integer
      %lx       Long hex integer

    The parameter 'arglist' is a list of arguments, in
    order.  Their types are taken from the format string.
    If the wrong type is specified in the format string,
    printf has no way of knowing, so the results will be
    unpredictable.

    Example of using printf:

;**************************************

            ...

FmtStr      db '%d %s %c %lx',0

ArgList     dw 15600
            db 'This is a string',0
            db 'X'
            dd 1A2B3C4Dh

            ...

            push offset FmtStr
            push offset ArgList
            call printf

            ...

;**************************************

    This example will output '15600 This is a string X 1A2B3C4D'.

  ---------- fprintf            Print Formatted String to File

    push handle
    push offset fmtstr
    push offset arglist
    call printf

    This procedure prints a formatted string to a file.  It
    works the same way printf does.  See 'printf' for more
    information.

  ---------- sprintf            Print Formatted String to String

    push offset dest_str
    push offset fmtstr
    push offset arglist
    call printf

    This procedure prints a formatted string to a string.
    The string output will be null terminated.  This
    procedure works the same way printf does.  See 'printf'
    for more information.

  ---------- xprintf            Print Formatted String, Generalized

    push offset outfunc
    push offset fmtstr
    push offset arglist
    call printf

    This procedure prints a formatted string using a user
    defined function.  The function must take one word
    argument, the character to output, save all registers,
    and return with a 'Ret 2' to clean up the stack.  This
    procedure works the same way printf does.  See 'printf'
    for more information.


  -------------------------------------------------------------
  ------------ Alphanumeric Conversion Procedures -------------
  -------------------------------------------------------------

  ---------- atoi               Convert String to Integer

    push offset string
    call atoi
    ; AX = result

    This procedure converts a string to an integer.  It
    recognizes the '-' and '+' signs, but it will stop on
    any other non-digit.  The integer corresponding to the
    string is returned.  If the result overflows, the low
    16 bits of the result are returned.

  ---------- atol               Convert String to Long

    push offset string
    call atol
    ; DX:AX = result

    This procedure converts a string to a long integer.
    It recognizes the '-' and '+' signs, but it will stop on
    any other non-digit.  The long integer corresponding to
    the string is returned.  If the result overflows, the
    low 32 bits of the result are returned.

  ---------- itoa               Convert Integer to String

    push number
    push offset buffer
    call itoa

    This procedure converts an integer to a string.  On
    return, 'buffer' will contain the decimal representation
    of 'number'.  The string will be null terminated.  If
    the number is negative, this will be handled correctly.

  ---------- ltoa               Convert Long to String

    push num_hi
    push num_lo
    push offset buffer
    call ltoa

    This procedure converts a long integer to a string.  On
    return, 'buffer' will contain the decimal representation
    of the number.  The string will be null terminated.  If
    the number is negative, this will be handled correctly.

  ---------- atofix             Convert String to Fixed-Point

    push offset string
    call atofix
    ; DX:AX = result

    This procedure converts a string to a fixed-point
    number.  Itrecognizes the '-' and '+' signs and the
    decimal point, but it will stop on any other non-digit.
    The fixed-point number corresponding to the string is
    returned.  If the result overflows, the value returned
    will have the correct fractional part, and the integer
    part will be the low 16 bits of the true value.

  ---------- fixtoa             Convert Fixed-Point to String

    push num_hi
    push num_lo
    push offset buffer
    call fixtoa

    This procedure converts a fixed-point number to a
    string.  On return, 'buffer' will contain the decimal
    representation of the number.  The string will be null
    terminated.  If the number is negative, this will be
    handled correctly.  Fractions will also be handled
    correctly.


  -------------------------------------------------------------
  ------ Long Integer/Fixed Point Arithmetic Procedures -------
  -------------------------------------------------------------

  ---------- ldiv               Long Divide

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call ldiv
    ; DX:AX = result

    This procedure divides unsigned long integers.
    It divides 'num1' by 'num2'.

  ---------- lidiv              Long Divide, Signed

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call lidiv
    ; DX:AX = result

    This procedure divides signed long integers.
    It divides 'num1' by 'num2'.

  ---------- lmul               Long Multiply

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call lmul
    ; DX:AX = result

    This procedure multiplies unsigned long integers.
    It takes 70 clock ticks on a 486, including the
    call/return but not the argument pushes.

  ---------- limul              Long Multiply, Signed

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call limul
    ; DX:AX = result

    This procedure multiplies signed long integers.
    It takes 89-97 clock ticks on a 486, including the
    call/return but not the argument pushes.

  ---------- lshl               Long Shift Left

    push num_hi
    push num_lo
    push dist
    call lshl
    ; DX:AX = result

    This procedure shifts a long integer to the left.
    It shifts 'num' by 'dist', and takes 37 clock
    ticks on a 486, including the call/return but not
    the argument pushes.

  ---------- lshr               Long Shift Right

    push num_hi
    push num_lo
    push dist
    call lshr
    ; DX:AX = result

    This procedure shifts an unsigned long integer to the
    right.  It shifts 'num' by 'dist', and takes 37 clock
    ticks on a 486, including the call/return but not
    the argument pushes.

  ---------- lsar               Long Shift Right, Signed

    push num_hi
    push num_lo
    push dist
    call lsar
    ; DX:AX = result

    This procedure shifts a signed long integer to the
    right.  It shifts 'num' by 'dist', and takes 39 clock
    ticks on a 486, including the call/return but not
    the argument pushes.

  ---------- fixmul             Fixed-Point Multiply

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call fixmul
    ; DX:AX = result

    This procedure multiplies fixed-point numbers.
    It takes 101-109 clock ticks on a 486, including
    the call/return but not the argument pushes.

  ---------- fixdiv             Fixed-Point Divide

    push num1_hi
    push num1_lo
    push num2_hi
    push num2_lo
    call fixdiv
    ; DX:AX = result

    This procedure divides fixed-point numbers.
    It divides 'num1' by 'num2'.


  -------------------------------------------------------------
  ---------------------- String Procedures --------------------
  -------------------------------------------------------------

  ---------- strlen             String Length

    push offset string
    call strlen
    ; AX = length

    This procedure returns the length of a string, not
    including the null terminator.

  ---------- strcpy             Copy String

    push offset dest_str
    push offset src_str
    call strcpy

    This procedure copies 'src_str' to 'dest_str', including
    the null terminator.  There is no checking to see if the
    string fits, so be careful.

  ---------- strcat             Concatenate Strings

    push offset dest_str
    push offset src_str
    call strcat

    This procedure concatenates 'src_str' onto 'dest_str',
    including the null terminator.  There is no checking to
    see if the string fits, so be careful.

  ---------- strcmp             Compare Strings

    push offset string1
    push offset string2
    call strcmp
    ; AX  = return value

    This procedure compares 'string1' and 'string2'.  If
    'string2' is lexicographically greater, a negative value
    is returned.  If 'string1' is greater, a positive value
    is returned.  If they are equal, zero is returned.

  ---------- stricmp            Compare Strings, Case Insensitive

    push offset string1
    push offset string2
    call stricmp
    ; AX  = return value

    This procedure compares 'string1' and 'string2'.  If
    'string2' is lexicographically greater, a negative value
    is returned.  If 'string1' is greater, a positive value
    is returned.  If they are equal, zero is returned.  This
    procedure differs from strcmp in that the compare is
    case insensitive.

  ---------- strchr             Search String for Char

    push offset string
    push char
    call strchr
    ; AX  = return value

    This procedure searches for 'char' in 'string'.  If the
    character is not found, -1 is returned, otherwise the
    position of the character in the string is returned.

  ---------- strstr             Search String for Substring

    push offset string
    push offset substr
    call strchr
    ; AX  = return value

    This procedure searches for 'substr' in 'string'.  If
    the substring is not found, -1 is returned, otherwise
    the position of the substring in the main string is
    returned.

  ---------- strlwr             Convert String to Lowercase

    push offset string
    call strlwr

    This procedure converts a string to lowercase.  Any
    character in the string that is already lowercase or
    that is not a letter will not be affected.

  ---------- strupr             Convert String to Uppercase

    push offset string
    call strupr

    This procedure converts a string to uppercase.  Any
    character in the string that is already uppercase or
    that is not a letter will not be affected.

  ---------- strltrim           Trim Leading Spaces

    push offset string
    call strltrim

    This procedure trims leading spaces from a string.  If
    there are no leading spaces, nothing happens.

  ---------- strrtrim           Trim Trailing Spaces

    push offset string
    call strrtrim

    This procedure trims trailing spaces from a string.  If
    there are no trailing spaces, nothing happens.


  -------------------------------------------------------------
  ------------------ Memory Block Procedures ------------------
  -------------------------------------------------------------

  ---------- memcpy             Copy Memory Block

    push dest_offset
    push src_offset
    push length
    call memcpy

    This procedure copies a block of memory from
    'src_offset' to 'dest_offset'.  The block is of length
    'length'.  This procedure will work correctly if the
    blocks overlap.

  ---------- memset             Set Memory Block

    push memd_offset
    push length
    push byte
    call memset

    This procedure fills a block of memory of length
    'length' at 'mem_offset' with 'byte'.

  ---------- memcmp             Compare Memory Blocks

    push dest_offset
    push src_offset
    push length
    call memcmp
    ; AX = return code

    This procedure compares two blocks of memory at offsets
    'src_offset' and 'dest_offset'.  The blocks are of
    length 'length'.  If they are equal, 1 is returned,
    otherwise 0 is returned.

  ---------- memchr             Search Memory Block

    push mem_offset
    push length
    push byte
    call memchr

    This procedure searches a block of memory of length
    'length' at 'src_offset' for 'byte'.  If the byte is
    found, its position within the block is returned,
    otherwise -1 is returned.


  -------------------------------------------------------------
  ---------------- Search and Sort Procedures -----------------
  -------------------------------------------------------------

  ---------- isearch            Search Array of Integers

    push offset array
    push size
    push elem
    call isearch
    ; AX = return code

    This procedure searches an array of integers of size
    'size' for 'elem'.  This procedure assumes that the
    array is sorted.  If the element is found, its position
    in the array is returned, otherwise -1 is returned.

  ---------- lsearch            Search Array of Longs

    push offset array
    push size
    push elem_hi
    push elem_lo
    call lsearch
    ; AX = return code

    This procedure searches an array of long integers of
    size 'size' for 'elem'.  This procedure assumes that the
    array is sorted.  If the element is found, its position
    in the array is returned, otherwise -1 is returned.

  ---------- ssearch            Search Array of Strings

    push offset array
    push size
    push offset elem
    call ssearch
    ; AX = return code

    This procedure searches an array of strings of size
    'size' for 'elem'.  This procedure assumes that the
    array is sorted.  If the element is found, its position
    in the array is returned, otherwise -1 is returned.

  ---------- xsearch            Search Array, Generalized

    push offset array
    push size
    push offset elem
    push offset cmpfunc
    call xsearch
    ; AX = return code

    This procedure searches an array of pointers of size
    'size' for 'elem'.  It assumes that the array is sorted.
    If the element is found, its position in the array is
    returned, otherwise -1 is returned.

    This procedure uses a user-defined function.  The
    function must take two word-sized pointer arguments.
    It must return the result of the comparison in AX so
    that a negative value indicates less, a positive value
    indicates greater, and zero indicates equal, and it
    also should preserve all registers except for AX.

  ---------- isort              Sort Array of Integers

    push offset array
    push size
    call isort

    This procedure sorts an array of integers of size
    'size' in ascending order.

  ---------- lsort              Sort Array of Longs

    push offset array
    push size
    call lsort

    This procedure sorts an array of long integers of size
    'size' in ascending order.

  ---------- ssort              Sort Array of Strings

    push offset array
    push size
    call ssort

    This procedure sorts an array of strings of size
    'size' in alphabetical order.

  ---------- xsort              Sort Array, Generalized

    push offset array
    push size
    push offset cmpfunc
    call xsort

    This procedure sorts an array of pointers of size
    'size'.  This is the generalized sort procedure.

    This procedure uses a user-defined function.  The
    function must take two word-sized pointer arguments.
    It must return the result of the comparison in AX so
    that a negative value indicates less, a positive value
    indicates greater, and zero indicates equal, and it
    also should preserve all registers except for AX.


  -------------------------------------------------------------
  ----------------- Miscellaneous Procedures ------------------
  -------------------------------------------------------------

  ---------- cputype            Get CPU Type

    call cputype
    ; AX = CPU type

    This procedure returns the CPU type (0 = 8086, 1 = 186,
    etc.)  It cannot detect SX/DX variations.

  ---------- fputype            Get FPU Type

    call fputype
    ; AX = FPU type

    This procedure returns the FPU type (0 = 8087, 1 = 187,
    etc.)  If there is no FPU, -1 is returned.

  ---------- atexit             Register Exit Function

    push offset func
    call atexit

    This procedure registers a function for calling on exit.
    If an error occurs, 0 is returned, otherwise a nonzero
    value is returned.

  ---------- bitcnt             Count Bits

    push number
    call bitcnt
    ; AX = number of set bits

    This procedure returns the number of set bits in an
    integer.

  ---------- highbit            Find High Bit

    push number
    call highbit
    ; AX = highest bit

    This procedure returns the positon of the highest set
    bit in an integer.  -1 is returned if it is zero.

  ---------- sqrt               Square Root

    push num_hi
    push num_lo
    call sqrt
    ; AX = result

    This procedure returns the square root of a long
    integer.  The result is a normal integer.  This
    procedure treats all values as unsigned.

  ---------- exec               Execute Program

    push offset progname
    push offset cmdline
    call exec
    ; AX = return code

    This procedure executes another program as a child
    process, with arguments in 'cmdline'.  If an error
    occurs, 0 is returned, otherwise a nonzero value
    is returned.

  ---------- rand               Random Number

    push max
    call rand
    ; AX = result

    This procedure returns a random number below 'max'.

  ---------- srand              Seed Random Numbers

    call srand

    This procedure seeds the random number generator with
    the system clock.

  ---------- delay              Delay

    push delaytime
    call delay

    This procedure delays for a specified number of
    milliseconds before returning.

  ---------- sound              Set Speaker

    push freq
    call sound

    This procedure turns on the speaker at a specified
    frequency.

  ---------- nosound            Turn Speaker Off

  call nosound

  This procedure turns the speaker off.


  -------------------------------------------------------------
  ----------- High-Res Text Mode (90x34) Procedures -----------
  -------------------------------------------------------------

  ---------- inittext           Initialize Text System

    call inittext

    This procedure initializes the High-Res Text Mode.

  ---------- closetext          Close Text System

    call closetext

    This procedure closes the High-Res Text system, and
    sets the standard text mode.

  ---------- clrscr             Clear Screen

    call clrscr

    This procedure clears the screen on the current video
    page.

  ---------- setwin             Set Window

    push x1 y1
    push x2 y2
    push rel_flag
    call setwin

    This procedure sets the clipping window.  'rel_flag'
    indicates whether coordinates will be relative to the
    window or not.

  ---------- clrwin             Clear Window

    call clrwin

    This procedure clears the current window.

  ---------- setpage            Set Video Page

    push page_num
    call setpage

    This procedure sets the current video page.  The page
    number must be between 0 and 5 (there are six pages).

  ---------- getpage            Get Video Page

    call getpage
    ; AX = current page

    This procedure returns the current video page.

  ---------- setcolor           Set Color

    push color
    call setcolor

    This procedure sets the current text color.  The color
    is a byte, 0XYh, where X is the background color and Y
    is the foreground color.

  ---------- getcolor           Get Color

    call getcolor
    ; AX = current color

    This procedure returns the current text color.

  ---------- box                Draw Box

    push x1 y1
    push x2 y2
    push char
    call box

    This procedure draws a box with character 'char'.  The
    box is clipped to the current window.

  ---------- sbox               Draw Style Box

    push x1 y1
    push x2 y2
    push style
    call sbox

    This procedure draws a style box.  The box is clipped
    to the current window.  Here is the list of styles:

    0       Blank
    1       Single Line
    2       Double Line
    3       Single/Double
    4       Double/Single

  ---------- fbox               Draw Filled Box

    push x1 y1
    push x2 y2
    push char
    call fbox

    This procedure draws a filled box with character 'char'.
    The box is clipped to the current window.

  ---------- hline              Draw Horizontal Line

    push x1 x2
    push y
    push char
    call hline

    This procedure draws a horizontal line with character
    'char'.  The line is clipped to the current window.

  ---------- vline              Draw Vertical Line

    push y1 y2
    push x
    push char
    call vline

    This procedure draws a vertical line with character
    'char'.  The line is clipped to the current window.

  ---------- hsline             Draw Horizontal Style Line

    push x1 x2
    push y
    push style
    call hsline

    This procedure draws a horizontal style line.  The line
    is clipped to the current window.  See the description
    for 'sbox' for a list of the styles.

  ---------- vsline             Draw Vertical Style Line

    push y1 y2
    push x
    push style
    call vsline

    This procedure draws a horizontal style line.  The line
    is clipped to the current window.  See the description
    for 'sbox' for a list of the styles.

  ---------- gotoxy             Set Cursor Position

    push x y
    call gotoxy

    This procedure sets the position of the cursor.  It is
    clipped to the current window.

  ---------- getx               Get Cursor X

    call getx
    ; AX = current X position

    This procedure returns the X position of the cursor.  If
    the window relative flag is set, the position will be
    relative to the current window.

  ---------- gety               Get Cursor Y

    call gety
    ; AX = current Y position

    This procedure returns the Y position of the cursor.  If
    the window relative flag is set, the position will be
    relative to the current window.

  ---------- setctype           Set Cursor Type

    push cur_type
    call setctype

    This procedure sets the type of the cursor.  The format
    is: 0XXYYh, where XX is the starting line (0-13) and YY
    is the ending line (0-13).

  ---------- getctype           Get Cursor Type

    call getctype
    ; AX = cursor type

    This procedure returns the current cursor type.  The
    format is: 0XXYYh, where XX is the starting line (0-13)
    and YY is the ending line (0-13).

  ---------- setch              Set Character

    push x y
    push char
    call setch

    This procedure sets the character at (x, y) to 'char'.
    The output is clipped to the current window.

  ---------- setat              Set Attribute

    push x y
    push attr
    call setat

    This procedure sets the attribute at (x, y) to 'attr'.
    The output is clipped to the current window.

  ---------- setcha             Set Char & Attr.

    push x y
    push char
    push attr
    call setcha

    This procedure sets the character at (x, y) to 'char',
    and the attribute to 'attr'.  The output is clipped to
    the current window.

  ---------- readcha            Read Char & Attr.

    push x y
    call readcha
    ; AL = char, AH = attr

    This procedure returns the character and attribute
    at (x, y).

  ---------- tputs              Put String at (X, Y)

    push x y
    push offset string
    call tputs

    This procedure prints 'string' at (x, y).  Output is
    clipped to the current window.  Output will not wrap
    around lines.  Control characters will be displayed
    literally.

  ---------- tprintf            Print Formatted String at (X, Y)

    push x y
    push offset fmtstr
    push offset arglist
    call tprintf

    This procedure prints a formatted string at (x, y).
    It is equivalent to a 'sprintf' followed by 'tputs'.
    See 'sprintf' and 'tputs' for more information.

  ---------- getline            Get Line of Text

    push x y
    push offset buffer
    push min
    push max
    call getline

    This procedure inputs a line of text from the user.
    A field is drawn at (x, y) extending for (max - 1)
    characters, and the string is input there.  Full
    editing, i.e. insert/delete, etc., is supported.
    A string of minimum 'min' and maximum (max - 1)
    characters will be put into 'buffer'.

  ---------- setglchar          Set Char for 'getline'

    push char
    call setglchar

    This sets the character used to clear the input field in
    'getline'.  The default value is a space (20h).  Another
    useful value is the small bullet (0FAh).

  ---------- gettext            Get Block of Text

    push offset buffer
    push x1 y1
    push x2 y2
    call gettext

    This procedure captures a rectangular block of text into
    'buffer'.  No clipping is performed.

  ---------- puttext            Put Block of Text

    push offset buffer
    push x1 y1
    call puttext

    This procedure displays a rectangular block of text from
    'buffer' at (x1, y1).  Output is clipped to the current
    window.

  ---------- movetext           Move Block of Text

    push x1 y1
    push x2 y2
    push x y
    call movetext

    This procedure moves a rectangular block of text from
    (x1, y1)-(x2, y2) to (x, y).  If the blocks overlap,
    it will be handled correctly.  No clipping is performed
    and the window relative flag is ignored.

  ---------- delline            Delete Line

    push y
    call delline

    This procedure deletes a line (at 'y') from the current
    window.  All text below the line is scrolled up, and the
    bottom line is cleared.

  ---------- insline            Insert Line

    push y
    call insline

    This procedure inserts a line (at 'y') from the current
    window.  All text below the line is scrolled down, and
    the inserted line is cleared.

  ---------- scroll             Scroll Window

    push dir
    call scroll

    This procedure scrolls the current window.  The values
    for the direction 'dir' are:

    0       Scroll Up
    1       Scroll Down
    2       Scroll Left
    3       Scroll Right


  -------------------------------------------------------------
  -------- High-Res Text Mode (90x34) Mouse Procedures --------
  -------------------------------------------------------------

  ---------- minit              Initialize Mouse System

    call minit
    ; AX = return code

    This procedure initializes the High-Res Text Mode
    Mouse Driver.  If an error occurs or the mouse is
    not found, 0 is returned, otherwise a nonzero value
    is returned.

  ---------- mclose             Close Mouse System

    call mclose

    This procedure closes the mouse system.

  ---------- mshow              Show Mouse Cursor

    call mshow

    This procedure displays the mouse cursor on the screen.

  ---------- mhide              Hide Mouse Cursor

    call mhide

    This procedure hides the mouse cursor.

  ---------- mget               Get Mouse Position

    call mget
    ; AX = button status
    ; BX = mouse X position
    ; CX = mouse Y position

    This procedure returns the position and status of the
    mouse.  The format for the button status is:

    Bit     Meaning

     0     Left button
     1     Right button
     2     Middle button

  ---------- mgetdn             Get Mouse Presses

    push button
    call mgetdn
    ; AX = press count
    ; BX = X position at last press
    ; CX = Y position at last press

    This procedure returns the status of a particular mouse
    button, for presses.  The button values are as follows:

    0       Left button
    1       Right button
    2       Middle button

  ---------- mgetup             Get Mouse Releases

    push button
    call mgetup
    ; AX = release count
    ; BX = X position at last release
    ; CX = Y position at last release

    This procedure returns the status of a particular mouse
    button, for releases.  See 'mgetup' for button values.


7.  Future additions, bug reporting, etc.

  Bugs may be reported to the author at:  tjr19@mail.nwlink.com.

  In the future, a set of wrapper procedures for calling
  some of the FREELIB routines from 'C' may be provided.

  This is a list of the routines wanted for future addition:

  (1) VGA graphics.  (16 AND 256 colors, hopefully integrated,
        i.e. they do both modes)

  (2) EMS/XMS/Disk virtual memory manager.  Should be transparent
        as to which medium is being used.

  (3) Low-level disk routines (read/write sector, format floppy).

  (4) Indefinite long arithmetic, 256 bytes at least.

  (5) Routines to read and write configuration data from the
        program's executable file.

  (6) Inter-procedure jumps, like the 'C' setjmp() and longjmp().

  (7) Sound card interface routines.

  (8) General data compression.

  (9) Process management and multitasking.

  (10) Anything else that might be useful!!!

----------------------------------------------------------------------
----------------------------------------------------------------------