ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ·
      ³                                                                   º Û
      ³                                                                   º Û
      ³                           A M I s e t u p                         º Û
      ³                                                         Shareware º Û
      ³ Documentation                                                     º Û
      ³ AMISETUP.DOC                                                      º Û
      ³                                                                   º Û
      ³ Copyright (c) Robert Muchsel 1992-1993                            º Û
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ Û
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      AMIsetup is an external setup program for 386/486 PCs with modern AMI
      BIOS (AMI Hi-Flex BIOS). AMIsetup can change all setup options (even
      those the BIOS doesn't display) conveniently.

      In this manual, symbols from the extended character set are used (code
      page 437). In the program itself, these can be turned off.


      Important
      ÄÄÄÄÄÄÄÄÄ
       ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                                                                    ³
      ³                         USE AT YOUR OWN RISK!                      ³
      ³  This program is based on undocumented data structures.            ³
      ³  Improper use, program errors or bad luck can cause hardware,      ³
      ³  software and stored data of the computer be irreversibly damaged! ³
      ³  The user is advised always to make adequate Back Ups of all       ³
      ³  valuable files or Data. Because he can have no control over how   ³
      ³  this program is used                                              ³
      ³          THE AUTHOR ACCEPTS NO LIABILITY FOR ANY DAMAGE!           ³
      ³                                                                    ³
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      No part of this documentation may be reproduced, transmitted,
      transcribed, stored in any retrieval system, or translated into any
      other language or computer language in whole or in part, in any form
      or by any means, whether it be electronic, mechanical, magnetic,
      optical, manual or otherwise, without prior written consent of the
      author, Robert Muchsel.

      The author disclaims all warranties as to this software, whether
      express or implied, including without limitation any implied warranties
      of merchantability, fitness for a particular purpose, functionality,
      data integrity or protection, in so far as permitted by applicable
      legislation.

      All trademarks are property of their respective owners and appear for
      identification purposes only.

      What's new: Changes are described in a separate file, AMISETUP.NEW.


      Shareware
      ÄÄÄÄÄÄÄÄÄ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  Writing this program has taken lots of work. If you continue     ³
      ³  using it after a reasonable trial period of 30 days, you have    ³
      ³  to pay a small fee to the author.                                ³
      ³                                                                   ³
      ³  SHAREWARE is NOT FREE SOFTWARE. You can, however, test shareware ³
      ³  before purchasing it.                                            ³
      ³                                                                   ³
      ³  For detailed information, see appendix A.                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      You are encouraged to copy and pass on the unregistered shareware
      version of this program, if
      - the contents of the original archive aren't changed
      - no fee is charged for the distribution,
        especially no disk copying fee, postage, download costs (BTX/
        videotex, BBS) etc.
      The program must not be added to CD ROMs, books, magazines etc., even
      if no additional fee is charged.
      Sale or bundling of this program with hardware or other software is
      not allowed.

      º If you want to offer this program (shareware version or full version)
      º to your customers, please contact the author. In most cases a
      º a distribution license and upgrade information will be sent by fax!

      The information contained in the online reference for registered users
      must not be copied, published or separated from the program. The author
      has taken every care to ensure the technical correctness of the
      information, but cannot accept any liability in case of any error.

      If you have comments or find an error, please send them to the author!


      Highlights
      ÄÄÄÄÄÄÄÄÄÄ

      AMIsetup does what the ROM setup in newer 386 and 486 computers with
      an AMI BIOS lacks. In addition to the capabilities of the ROM setup,
      there are file operations, manual register changes can be made and
      all setup options can be accessed, even those which are turned off in
      the ROM setup.

      þ Menu driven setup with all options and help texts defined by the BIOS
      þ Complete mouse support, high resolution video mode (EGA/VGA)
      þ Comprehensive online help
      þ Standard setup including type 47 hard drives
      þ Manually change certain CMOS registers
      þ Save and restore CMOS RAM contents using a file
      þ Print register contents and current configuration
      þ Display BIOS power-on and standard configuration
      þ Compatible with all memory managers by using "image files"
      þ Reboot directly from the program
      þ Display and change the CMOS password!
      þ Online reference with explanations of many setup options
        (registered users ONLY)
      þ Password protection option against unauthorized use
      þ Analyse BIOS ID string and CMOS error flags
      þ Compare DOS and RTC timing
      þ Measure DMA frequency to avoid possible damage
      þ Supports Soundblaster audio card


                                     Contents
                                     ÄÄÄÄÄÄÄÄ

        1   Caution!
        2   Starting the program
        3   Menus in detail
            3.1 ð (System) menu
            3.2 BIOS menu
            3.3 CMOS menu
            3.4 Setup
                1. Standard setup
                2. Extended/chipset setup
                3. Change register
                4. Password
                5. Load ROM setup defaults, load ROM power-on defaults
                6. Print current setup
                7. Analyse ID string
                8. Save changes and quit
                9. Exit without saving
            3.5 Options dialogue
            3.6 Help menu
        4   Key shortcuts

            Appendix

        A   Registration, addresses
        B   AMIsetup and OS/2 2.0, AMI BIOS and OS/2
        C   Known problems
            1. Is AMIsetup compatible with your BIOS?
            2. Frequent errors with compatible BIOS versions
            3. Stopgap: -OVERRIDE
        D   Glossary
        E   If the machine won't boot...
        F   Switching to the English user interface
        G   Soundblaster

      NB: The program needs write access to the current directory.
      Diskettes must not be write protected if file operations are to be
      used.


      1  Caution!
      ÄÄÄÄÄÄÄÄÄÄÄ

      If you are not familiar with setup options or if you don't know
      what they do, please consider whether changing the setup options
      is really necessary.

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  On many PCs, the DMA clock speed can be changed.                 ³
      ³  This may work at first, but later the DMA chip may be destroyed, ³
      ³  thus making the motherboard useless!                             ³
      ³                                                                   ³
      ³  Another critical point is the password option. Since you cannot  ³
      ³  erase CMOS RAM on some mainboards (see appendix E), it may       ³
      ³  happen that because of - forgetfulness, BIOS errors, different   ³
      ³  keyboard layout etc. - you are irreversibly locked out of your   ³
      ³  computer.                                                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      Before making ANY change, ask yourself:
      - is it necessary?
      - what are the consequences?

      The rule is therefore:

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  N E V E R   C H A N G E   A   R U N N I N G   S Y S T E M  !!!   ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      WHEN DID YOU DO YOUR LAST COMPLETE BACKUP???


      2  Starting the program
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      First of all, please read the manual and the file "AMISETUP.NEW".

      Normally, you start AMIsetup without additional commandline arguments.
      There is an exception though (see appendix C). You should read
      appendix B if you want to use AMIsetup under OS/2.

      If using AMIsetup for the first time, you have to choose the desired
      language:

              ÚÄÄÄÄÄÄÄÄÄÄÄÄ Welcome / Willkommen ! ÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³  This is a bilingual version of AMIsetup.      ³
              ³  For English help texts and user interface,    ³
              ³  press [E].                                    ³
              ³                                                ³
              ³  Dies ist eine zweisprachige Version von       ³
              ³  AMIsetup. Dr�cken Sie [D] f�r deutsche Hilfe- ³
              ³  texte und Benutzeroberfl„che.                 ³
              ³                                                ³
              ³  [E] English version     [D] deutsche Version  ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      Should you decide on the german version, please continue reading in
      the file "AMISETUP.DOK".

      Next you must to accept the warning message with a "Y":

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ C A U T I O N ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³              USE AT YOUR OWN RISK!             ³
              ³                                                ³
              ³  This program is based on undocumented data    ³
              ³  structures. Hard- and software and stored     ³
              ³  data could be damaged irrevocably!            ³
              ³                                                ³
              ³ THE AUTHOR WILL NOT BE LIABLE FOR ANY DAMAGES! ³
              ³                                                ³
              ³ [Y] accept and start program   [N] back to DOS ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      If you have set a password in the "Options" dialogue (3.5), you will
      be prompted to enter it.

                   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                   º                                      º
                   º AMIsetup is password protected.      º
                   º Please enter the current password.   º
                   º                                      º
                   º  Password    ****                    º
                   º                                      º
                   º                                      º
                   º          OK   Ü      Help  Ü         º
                   º        ßßßßßßßß     ßßßßßßßß         º
                   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Next, a dialogue box containing program revision and registration
      number (or "UNREGISTERED") appears. If you haven't yet paid for
      AMIsetup and a registration number appears anyway, you've got an
      (illegal) pirated copy. Please contact the author.

                  ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Information ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º                                         º
                  º             AMIsetup v2.0               º
                  º             External setup              º
                  º         REGISTERED (#XXXXXXXX)          º
                  º   Copyright (c) 1992-93 Robert Muchsel  º
                  º                                         º
                  º                                         º
                  º            OK    Ü      Help  Ü         º
                  º          ßßßßßßßßß    ßßßßßßßßß         º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


      º You can also view this entire file from AMIsetup ("Help|View
      º AMISETUP.DOC").


      Quick start
      ßßßßßßßßßßß

      The most frequent error stems from use of AMIsetup with a memory
      manager (386MAX, QEMM386, EMM386...) loaded. Please note para 3.2
      "BIOS|Write image to file" and appendix C.


      3  Menus in detail
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Using the mouse or pressing <F10>, you get to the main menu bar.
      There, you have the following pull down menus at your disposal:

       ð  BIOS  CMOS  Setup  Options  Help
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Pressing <F1> gets you help. The online help contains nearly all of the
      manual.

      Hint for mouse users: The right button is equivalent to <Esc>.


      3.1 ð (System) menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°°°°°°°°
       ³ About    Shift-F10 ³ °°°°°°°°°°°°°°°°°
       ³ Evaluate DMA clock ³ °°°°°°°°°°°°°°°°°
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°°°°°°
       ³ Video mode   Alt-V ³ °°°°°°°°°°°°°°°°°
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°°°°°°
       ³ Reboot             ³ °°°°°°°°°°°°°°°°°
       ³ Exit         Alt-X ³ °°°°°°°°°°°°°°°°°
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      About
        Shows a dialogue box containing program revision and registration
        number (if any).

      Evaluate DMA clock
        Tries to determine the current DMA clock speed (this operation is
        very hardware dependent and it is possible it won't work - "Error"
        is displayed then).

        The measured clock speed is displayed in
          green  (up to 4.25 MHz): Everything OK
          yellow (up to 5.10 MHz): Caution, possibly decrease DMA clock speed
          red    (from  5.10 MHz): The clock is too fast and can cause damage!

        Conditioned by "DMA waits" it is possible that too low a clock is
        shown. I.e.: If AMIsetup detects a "red" DMA clock, then it is truly
        time to decrease it - the DMA chip can be destroyed by overclocking!

        On many systems, DMA clock is coupled with bus clock (e.g. ETEQ,
        OPTI, SIS, UMC). You only need to double the DMA clock rating to
        obtain the bus clock.

      Video mode
        Toggles the display mode between 25 lines and 43/50 lines and requires
        an EGA/VGA graphics adaptor.
        AMIsetup automatically stores the last used video mode.

      Reboot
        Executes a cold boot. The keyboard controller is programmed to trigger
        a hardware reset.

        The "Reboot" function can be turned off using the "Options" dialogue.

        CAUTION! If you use a hard disk cache (Smartdrive, PC-KWIK, Hyperdisk,
        PC-Cache etc.), you shouldn't use "Reboot" but press <Ctrl><Alt><Del>
        instead.

      Exit
        Exits the program.


      3.2 BIOS menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      °°° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°°°
      °°° ³ Test version        ³ °°°°°°°°°°°°
      °°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°°°
      °°° ³ Write image to file ³ °°°°°°°°°°°°
      °°° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Test version
        Verifies whether the BIOS and AMIsetup are compatible. This check
        is executed automatically whenever you start "Setup". If this test
        fails ("*ERROR*") and you use a memory manager (e.g. QEMM-386,
        EMM386, 386MAX), you may have to create a BIOS image (see below),
        or reboot from a plain vanilla DOS diskette.
        Please read appendix C for more information about compatible BIOS
        versions.

      Write image to file
        Using this function, you can create a "BIOS image" file. This file
        is necessary if you use a memory manager like QEMM-386, EMM386 or
        386MAX. Otherwise you don't need an image file. "BIOS|Test version"
        tells you whether you need an image file.

        To create a "BIOS image" file, do the following:
        1. Reboot the PC WITHOUT memory manager and WITHOUT shadow RAM (if
           possible). It's best to boot from a floppy disk.
        2. Start AMIsetup.
        3. Turn off "Use BIOS image" in the "Options" dialogue.
        4. Select "BIOS|Test version" and verify that everything checks out
           OK.
        5. Select and execute "BIOS|Write image to file" (you can change the
           filename in the "Options" dialogue, if need be. Default is
           "BIOS.DAT").
        6. Finally don't forget to turn on "Use BIOS image" in the "Options"
           dialogue in order to use the newly created BIOS image.


      3.3 CMOS menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      °°°°°°°°° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°
      °°°°°°°°° ³ Test checksums      ³ °°°°°°°
      °°°°°°°°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°
      °°°°°°°°° ³ Print               ³ °°°°°°°
      °°°°°°°°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°
      °°°°°°°°° ³ Write image to file ³ °°°°°°°
      °°°°°°°°° ³ Restore from image  ³ °°°°°°°
      °°°°°°°°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°
      °°°°°°°°° ³ Information         ³ °°°°°°°
      °°°°°°°°° ³ Time compare        ³ °°°°°°°
      °°°°°°°°° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Test checksums
        Verifies the CMOS RAM checksums. There are two areas - the first is
        in all AT computers, the second only in PCs with an AMI BIOS. If
        one of these two tests fails, the program declines to run "Setup".

        If you have written your Setup to a file before this error occurred,
        you can correct the problem through "Restore from image".

      Print
        Prints the CMOS RAM contents and is used for diagnostic and
        reference purposes only. In order to get a readable, plain English
        print, use "Setup|Print current setup".

                 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
                 °ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ Print CMOS ÍÍÍÍÍÍÍÍÍÍÍÍÍ»°
                 °º                                      º°
                 °º ¯Print to file                       º°
                 °º   PRN                                º°
                 °º                                      º°
                 °º                                      º°
                 °º  [  OK  ]    [Cancel ]   [ Help  ]   º°
                 °º                                      º°
                 °ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°
                 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

        If you enter a name different from "PRN", the output will be
        redirected to a file, e.g. "CMOS.TXT". Of course you can also use
        device names (e.g. "LPT2")

        If your printer cannot print graphic characters, you must turn off
        "Extended character set" in the "Options" dialogue.

        Data is written in the following format:

                           Reg ³ Current value
                           ÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                            00 ³ 13  00010011
                            01 ³ 23  00100011
                           ...    ...
                            7E ³ 00  00000000
                            7F ³ 00  00000000

        Opposite to the register number (hexadecimal), the current value is
        printed in hexadecimal and binary format.

        If you don't want a form feed at the end, turn it off in the
        "Options" dialogue.

      Write image to file
        Copies contents of CMOS RAM to a file. You can change the filename
        in the "Options" dialogue (default is "CMOS.SAV").

      Restore from image
        Reads this file back to CMOS RAM and restores the saved state. Time
        and date are not set, however!

      Information
        Shows the date of the RTC, the alarm time and information about
        errors at system boot.

                ÉÍÍÍÍ Information about CMOS RAM contents ÍÍÍÍÍ»
                º                                              º
                º  Date ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
                º  ³ 03/19/1993             ³                  º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
                º                                              º
                º  Alarm ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
                º  ³ 00:00:00           off ³       OK    Ü    º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ßßßßßßßßßß    º
                º                                              º
                º  Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿     Print   Ü    º
                º  ³ Battery:             û ³    ßßßßßßßßßß    º
                º  ³ Power:               û ³                  º
                º  ³ Checksum:            û ³      Help   Ü    º
                º  ³ Configuration:       û ³    ßßßßßßßßßß    º
                º  ³ Memory size:         û ³                  º
                º  ³ Harddisk C:          û ³                  º
                º  ³ Time:                û ³                  º
                º  ³ Cache:               û ³                  º
                º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Date
          The current system date of the real time clock (RTC).

        Alarm
          The RTC supports an "alarm clock" mode. You need an external
          program (TSR), which processes the RTC message and then activates.

        Status
          Shows possible errors from the last system boot. A "û" means
          "no error found".
          - Battery: CMOS battery is discharged and CMOS contents were invalid
          - Power: RTC power supply failed
          - Checksum: CMOS checksums were invalid
          - Configuration: Self test results and CMOS configuration were
            different
          - Memory size: Memory size determined by self test and memory size
            stored in CMOS were different
          - Hard disk C: Hard disk C: (if available) couldn't be initialized
            and couldn't be booted from
          - Time: Time was invalid
          - Cache: Self test revealed cache error

          Most of these errors disappear after a reboot.

      Time compare
        Compares the current DOS time and the RTC time and is used for
        reference purposes only. If the difference is more than approx. 2
        secs, you should check hard- and software.


      3.4 Setup
      ÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Setup ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      ³
      ³05/05/91(C)1990 American Megatrends Inc., All Rights Reserved
      ³ROM BIOS (C)1990 American Megatrends Inc.,
      ³
      ³
      ³                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                      ³        Standard setup         ³
      ³                      ³    Extended/chipset setup     ³
      ³                      ³        Change register        ³
      ³                      ³           Password            ³
      ³ DATE:                ³    Load ROM setup defaults    ³      WARNING:
      ³ 05/05/91             ³  Load ROM power-on defaults   ³      Improper
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´      Setup may
      ³                      ³      Print current setup      ³      severe pr
      ³                      ³       Analyse ID string       ³
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³                      ³     Save changes and quit     ³
      ³                      ³      Exit without saving      ³
      ³                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      ³
      ³ 30-0201-ABCDEF-00101111-050591-OPWB
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If the CMOS RAM checksums and the internal BIOS copyright strings are
      valid, the above Setup screen is displayed.
      If you are a registered user (see appendix A), you can begin with this
      screen automatically at program start. Simply set "Options|Auto start
      setup" to on.

      AMIsetup searches for two specific copyright strings at several
      locations. One of these is displayed at the top. At the left is
      the BIOS date, at the bottom the BIOS ID string (as displayed at
      system boot).


      3.4.1 Standard setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You can change the following settings:

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Standard setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                                  º
      º Base memory:       640K                                          º
      º Extended memory: 16384K                                          º
      º                                                                  º
      º Drive A         Drive B           HDD 0 Ü         HDD 1 Ü        º
      º                                   ßßßßßßß         ßßßßßßß        º
      º  ( ) None        ( ) None          Type:    47    NONE / SCSI    º
      º  ( )  360K 5¬"   ( )  360K 5¬"     Cyl:   1024                   º
      º  ( )  1.2M 5¬"   ()  1.2M 5¬"     Heads:   64                   º
      º  ( )  720K 3«"   ( )  720K 3«"     S/Trk:   26                   º
      º  () 1.44M 3«"   ( ) 1.44M 3«"     Size:  832M                   º
      º  ( ) 2.88M 3«"   ( ) 2.88M 3«"                                   º
      º                                                                  º
      º Display adapter      Options                                     º
      º  ( ) Not installed    [X] Keyboard installed                     º
      º  ( ) Color 40x25      [ ] Enable daylight saving                 º
      º  ( ) Color 80x25                                                 º
      º  ( ) Monochrome                                                  º
      º  () VGA/PGA/EGA                  Ok   Ü    Cancel Ü     Help  Ü º
      º                                 ßßßßßßßß    ßßßßßßßß    ßßßßßßßß º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      At top, the memory size as determined by the BIOS is displayed.

      Drive A
      Drive B
        Allows you to change the type of installed floppy disk drives.
        NB: You can only select "2.88 MB" if your BIOS supports this
        type of drive (06/12/91 or later).

      Display adapter
        With this you set the type of the installed graphics adapter.

             ( ) Not installed
             ( ) Color 40x25
             ( ) Color 80x25   = CGA
             ( ) Monochrome    = MDA, Hercules
             () VGA/PGA/EGA

        Often you have to change a jumper on the mainboard in addition to
        this setting.

      Options - Keyboard installed
        If the keyboard should be checked at system boot, check this box.
        Should the keyboard not be checked or if there is no keyboard
        installed (e.g. LAN server), leave it empty.

      Options - Enable daylight saving
        Activates automatic daylight saving time correction, which is
        hard-wired into the real time clock chip. This only works for
        USA (last Sunday in April and October) and is useless in Europe.
        Some versions of DOS clear this bit when you use the DATE/TIME
        command.

      HDD 0
      HDD 1
        With this you can set the type of installed MFM, RLL or IDE
        hard drives. Using a SCSI controller, you mustn't define a hard disk
        here - please read your controller and hard disk manual to prevent
        momentous wrong settings!

        The current parameters are displayed below the pushbutton - type
        (number) of the disk, cylinders, heads, sectors per track and the
        calculated size. If you push the button, a list of predefined disk
        types appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ Hard disk 0 parameters ÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º Type³ Cyls. ³Heads³ Precomp³ LZone ³S/Trk³  Size º
             ºÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄº
             º  32 ³  1024 ³  15 ³   NONE ³  1024 ³  17 ³  128M >
             º  33 ³  1024 ³   5 ³   1024 ³  1024 ³  17 ³   43M ±
             º  34 ³   816 ³  15 ³   NONE ³   816 ³  32 ³  191M ±
             º  35 ³  1024 ³   9 ³   NONE ³  1024 ³  17 ³   77M ±
             º  36 ³  1024 ³   8 ³    512 ³  1024 ³  17 ³   68M ±
             º  37 ³   615 ³   8 ³    128 ³   615 ³  17 ³   41M ±
             º  38 ³   745 ³   4 ³    512 ³   745 ³  28 ³   41M ±
             º  39 ³   987 ³   7 ³    987 ³   987 ³  17 ³   57M ±
             º  40 ³   820 ³   6 ³    820 ³   820 ³  17 ³   41M ±
             º  41 ³   977 ³   5 ³    977 ³   977 ³  17 ³   41M ±
             º  42 ³   981 ³   5 ³    981 ³   981 ³  17 ³   41M ±
             º  43 ³   755 ³  16 ³   NONE ³   755 ³  17 ³  100M ±
             º  44 ³   887 ³  13 ³   NONE ³   887 ³  34 ³  191M ±
             º  45 ³   968 ³  10 ³   NONE ³   968 ³  34 ³  161M ±
             º  46 ³   751 ³   8 ³      0 ³   751 ³  17 ³   50M þ
             º¯ 47 ³ USER DEFINED³        ³       ³     ³      ®<
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The columns contain type (number) of the disk, number of cylinders,
        heads, the precompensation cylinder (see glossary), landing zone,
        number of sectors per track and the calculated size (rounded) in
        megabytes. Please compare these items with the data sheet of your
        hard disk.

        It's likely you CANNOT find the specifications of the hard disk to
        be installed in this list. In this case, select type 47 (USER
        DEFINED).
        The following dialogue appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍ  Change type 47 parameters  ÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                                    º
             º                                                    º
             º     615 ¯Cylinders                                 º
             º                                                    º
             º       4  Heads                                     º
             º                                                    º
             º     300  Precompensation (65535 for NONE)          º
             º                                     [  Save   ]    º
             º     615  Landing zone                              º
             º                                     [ Cancel  ]    º
             º      17  Sectors/track                             º
             º                                     [  Help   ]    º
             º                                                    º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Here you can set the parameters yourself. Note that the value of
        precompensation has a special meaning: 65535 means DISABLED for the
        whole hard disk. 0 means ENABLED for the whole disk.
        Modern drives ignore precompensation and landing zone. For reasons
        of software compatibility, set precompensation to "NONE" and landing
        zone to the highest available cylinder.


      3.4.2 Extended/chipset setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A list of options and their current settings is displayed:

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Extended setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      º            Option            ³Register³Bits ³ Current setting
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      º¯Typematic Rate Programming   ³ 11  10000000 ³ 10000000  Enabled     ®
      º Typematic Rate Delay (msec)  ³ 11  01100000 ³ 00000000  250
      º Typematic Rate (Chars/Sec)   ³ 11  00011111 ³ 00000011  21.8
      º ¨ Mouse Support Option       ³ 13  10000000 ³ 10000000   <1>
      º Above 1 MB Memory Test       ³ 13  01000000 ³ 00000000  Disabled
      º Memory Test Tick Sound       ³ 13  00100000 ³ 00000000  Disabled
      º Memory Parity Error Check    ³ 13  00010000 ³ 00010000  Enabled
      º Hit <ESC> Message Display    ³ 13  00001000 ³ 00000000  Disabled
      º Hard Disk Type 47 Data Area  ³ 13  00000100 ³ 00000000  0:300
      º Wait For <F1> If Any Error   ³ 13  00000010 ³ 00000010  Enabled
      º System Boot Up Num Lock      ³ 13  00000001 ³ 00000001  On
      º þ Numeric Processor          ³ 14  00000010 ³ 00000010  Present
      º Weitek Processor             ³ 2D  10000000 ³ 00000000  Absent
      º Floppy Drive Seek At Boot    ³ 2D  01000000 ³ 00000000  Disabled
      º System Boot Up Sequence      ³ 2D  00100000 ³ 00000000  C:, A:
      º System Boot Up Speed         ³ 50  00000100 ³ 00000000  High
      º Cache Memory                 ³ 2D  00001000 ³ 00001000  Enabled
      º ¨ Internal Cache Memory      ³ 2D  00000100 ³ 00000100   <1>
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      The four columns have the following meaning:

      Option
        The name of the setting to be changed, peeked from the BIOS.
        The signs "þ" and "¨" denote options which cannot be changed from
        the BIOS and are marked as "disabled" (see explanation under
        "Options|Display ...").
        If you change settings of options marked in this way, be especially
        careful. You can disable the display of these options selectivly
        in the "Options" dialogue.
        By the way, blame the BIOS manufacturer for reversed letters in this
        row, not AMIsetup.

      Register
        Hexadecimal number of the CMOS register which stores the setting.
        This information may help experienced users to change settings
        by hand using "Change register". If a "+"-sign is displayed behind
        the register number, possibly more than one registers are affected.

      Bits
        Bit mask for the setting. Only Bits marked with a "1" are used
        for the specified setting (see also Register).

      Current setting
        Bit mask of the setting stored in the program copy of CMOS RAM
        and the corresponding text in clear. If plain language is not
        available, a decimal value in acute brackets is shown. E.g.: <2>
        denotes the third possible setting, since <0> is valid, too.
        If there is the possibility that more than 8 bits are used for
        the setting, the bit mask is not shown.

      Now you can select an option with the mouse or the enter key, as
      appropriate. A new window is displayed (see below).

      Instead of pressing the enter key, <Ctrl>+<RightArrow> or <Ctrl>+
      <LeftArrow> increase or decrease the current setting respectively by one
      (for the hurried user, not available for options marked with a "+").

      List:                                       Radio buttons:
      ÉÍ[þ]ÍÍÍÍÍÍÍÍ Typematic Rate (Chars/Sec)    ÉÍ[þ]ÍÍÍÍ Typematic Rat
      º                                           º
      º   ¯Options                 Bits           º   ¯Options
      º     30.0             <     00000011       º    ¯() Disabled®
      º     26.7             ±    À00011111Ù      º     ( ) Enabled
      º     24.0             þ                    º
      º    ¯21.8            ®±              [     º
      º     20.0             ±                    º
      º     18.5             ±              [     º
      º     17.1             ±                    º
      º     16.0             ±              [     º
      º     15.0             >                    º
      º                                     [     º
      º                                           º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      Marked below "Options" or "Setting" is the current setting. To change
      the setting, scroll the list or press the appropriate button.

      The "Bits" field shows you which bit mask corresponds to the selected
      setting. Listed below the bit field are once again the bits which can
      be affected by the option.

      "Save" copies the changed setting into the program copy of CMOS RAM
      (use "Save changes and quit" to make the change permanent), "Cancel"
      cancels the operation.

      Caution: Some settings are "Reserved" or "RESERVED". Do consider
      whether you really want to set an option to "Reserved". For safety
      reasons, these changes have to be confirmed.

      "BIOS help": Sometimes, the BIOS ROM has an own (english) help text
      to the respective option. You can view this text using "BIOS help",
      e.g.:

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ BIOS help ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             ºThe base address changes in           º
             ºsteps of 16k and 512k                 º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      "Reference": Registered users can look up explanations to the setup
      options.

      Options which are controlled entirely by the BIOS (these usually change
      more than eight bits and are marked with a "+") display a window
      containing the buttons "® < > ¯"; you can also use (Ctrl+)RightArrow
      and (Ctrl+)LeftArrow. The buttons "® ¯" are intended for fast leafing
      and don't work on all machines. On some machines, a window appears
      after pressing "® < > ¯". Here you can enter data - this input window
      is controlled by the BIOS, so mouse input and function keys are
      disabled.

      Setting controlled by BIOS:
      ÉÍ[þ]ÍÍÍÍÍÍÍÍ Non-Cacheable Block-0 Base ÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                    º
      º                                                    º
      º                                                    º
      º                                      [BIOS help]   º
      º   Setting                                          º
      º   _0 KB_______________________       [Reference]   º
      º                                                    º
      º    [ ® ]  [ < ]  [ > ]  [ ¯ ]        [  Save   ]   º
      º                                                    º
      º                                      [ Cancel  ]   º
      º                                                    º
      º                                      [  Help   ]   º
      º                                                    º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Note that some options affect each other!


      3.4.3 Change register
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You may not be able to set the CMOS the way you want from the
      "Extended/chipset setup" menu. In this case, you can make the change
      manually.

      Caution: Use this function only if you are absolutely, positively sure
      about what you're doing!

             ÉÍ[þ]ÍÍÍÍÍ Change register ÍÍÍÍÍÍÍÍÍ»
             º                                   º
             º  Enter register number:           º
             º   __   Range 10 to 7F (hex)       º
             º                                   º
             º                                   º
             º [ Change ]  [ Cancel ]  [ Help ]  º
             º                                   º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

             ÉÍ[þ]ÍÍÍ Change register 12 ÍÍÍÍÍÍÍÍ»
             º  Current value: 00                º
             º                                   º
             º  Enter new value:                 º
             º   __   Range 00 to FF (hex)       º
             º                                   º
             º [  Set   ]  [ Cancel ]  [ Help ]  º
             º                                   º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      First, you have to enter the register number in hexadecimal and then
      the new value.


      3.4.4 Password
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function enables you to display the current CMOS password and to
      change it.

      This password can be called for at system boot or when entering the
      ROM setup.

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º Current password is "AMISET".        º
             º                                      º
             º                                      º
             º                                      º
             º  [Change]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

             ÉÍ[þ]ÍÍÍÍÍÍ Change password ÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º  New password: FIDO__                º
             º                                      º
             º                                      º
             º                                      º
             º  [  Ok  ]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Caution! If you use a foreign language keyboard (i.e. non-USA),
      note that no foreign keyboard support is loaded at boot time.
      Example: On German keyboards, "Z" and "Y" are reversed.

      Often you can enable the US-american keyboard by pressing <Ctrl><Alt><F1>
      and then test which keys are which. Use <Ctrl><Alt><F2> to reenable the
      foreign keyboard.

      On some machines the password function has to be activated by the
      "Password" option in "Extended/chipset setup" (3.4.2).

      CAUTION! If you set the "Password" option to "Always", you cannot
      boot your machine if you forget the password!

      Hint: Try the setting "Setup" first.


      3.4.5 Load ROM setup defaults, load ROM power-on defaults
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are two tables of predefined CMOS settings in the ROM. One of
      those, the "power-on defaults" is used to eliminate all possible
      hardware problems; thus the processor is switched to low speed, the
      cache is turned off etc. Using "power-on defaults", the machine should
      boot in any case.

      Using this function, you can load a predefined configuration or simply
      view it for reference purposes, since all settings will be written to
      the program copy of CMOS RAM first and only be saved if you use "Save
      changes and quit".


      3.4.6 Print current setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      With this function, you can print the current settings of the program
      copy of CMOS RAM to the printer or to a file.

             ÉÍ[þ]ÍÍÍÍÍÍÍÍ Print current setup ÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                             º
             º ¯Print to file                              º
             º   PRN______________________________         º
             º                                             º
             º  Format                                     º
             º   () Standard (current/possible)    Margin º
             º   ( ) Alternate (current bin&hex)     79_   º
             º                                             º
             º                                             º
             º  [  Ok  ]    [Cancel]    [ Help ]           º
             º                                             º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      First the settings of "Standard setup" will be printed; then, a list:

      Standard
        The list is formatted as follows:

                        Option            ³ Current  ³ Possible settings
             ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
             Typematic Rate Programming   ³ Enabled  ³ Disabled
             Typematic Rate Delay (msec)  ³ 250      ³ 500 750 1000
             Typematic Rate (Chars/Sec)   ³ 24.0     ³ 30.0 26.7 21.8 [...]
             ¨ Mouse Support Option       ³ <1>      ³
             Above 1 MB Memory Test       ³ Disabled ³ Enabled
             ...

        "Margin" (61-254) is the maximum width of the list. "Possible
        settings" will be truncated to "[...]" if exceeding the maximum
        width.

      Alternate
        The list looks like the list displayed in "Extended/chipset setup".
        "Margin" is ignored.

                        Option            ³Register³Bits ³ Current setting
             ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
             Typematic Rate Programming   ³ 13  10000000 ³ 10000000  Enabled
             Typematic Rate Delay (msec)  ³ 13  01100000 ³ 00000000  250
             Typematic Rate (Chars/Sec)   ³ 13  00011100 ³ 00010000  15
             þ Mouse Support Option       ³ 11  10000000 ³ 10000000  Enabled
             ...

      Note: If your printer cannot print extended characters, disable them
      in the "Options" dialogue.

      Hint: If you disable "þ" and "¨" in the "Options" dialogue, you can
      create a list of those settings which can be changed from the ROM
      setup. This list you can distribute e.g. to your customers as a
      reference.


      3.4.7 Analyse ID string
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function explains the meaning of the BIOS ID string displayed
      in the lower left corner.
      Note: The information determined by AMIsetup is not always 100 percent
      correct, since not all manufacturers adhere to the standard.

           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Analyse BIOS ID string ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º                                                      º
           º  30-0201-ABCDEF-00101111-050591-OPWB                 º
           º  23H-0-0000-00-00-0000-00-00-000                     º
           º  23H-1-0000-00-00-0000-00-00-00-2                    º
           º                                                      º
           º  Required processor:   386                           º
           º  BIOS size:            64 KB                         º
           º  Version:              2.01               Ok    Ü    º
           º  Reference number:     ABCDEF          ßßßßßßßßßß    º
           º  Halt on POST error:   no                            º
           º  Clear CMOS on boot:   no               Print   Ü    º
           º  PS/2 mouse support:   no              ßßßßßßßßßß    º
           º  Wait for F1 on error: yes                           º
           º  BIOS date:            05/05/91          Help   Ü    º
           º  Chipset ID:           OPWB            ßßßßßßßßßß    º
           º  Clock switching pin:  23                            º
           º  Cache control pin:    23                            º
           º  BIOS modified flag:   02                            º
           º                                                      º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Use "Print" to print the information or to write it into a file.


      3.4.8 Save changes and quit
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Not until you use this function will changes be made permanent. "Save
      changes and quit" writes all CMOS settings from the program copy of
      CMOS RAM into the real CMOS RAM and exits setup.


      3.4.9 Exit without saving
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Quits setup without changing the CMOS RAM.


      3.5 Options dialogue
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Options ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                              º
      º  Setup                         Display                       º
      º   [ ] Use BIOS image            [X] þ Options                º
      º   [X] Auto start setup          [ ] ¨ Options                º
      º   [ ] Print form feed                                        º
      º   [X] Extended character set    [ ] Soundblaster             º
      º   [ ] Enable reboot command                                  º
      º   [X] Beep on error                                          º
      º   [ ] Reverse mouse buttons      Password  Ü                 º
      º   [ ] German language           ßßßßßßßßßßßß                 º
      º                                                              º
      º  BIOS image file               CMOS image file               º
      º   C:\SETUP\BIOS.DAT             C:\SETUP\CMOS.SAV            º
      º                                                              º
      º  Help file                                                   º
      º   C:\SETUP\ENGLISH.HLP                                       º
      º                                                              º
      º    Save  Ü    Cancel Ü     Help  Ü                           º
      º   ßßßßßßßß    ßßßßßßßß    ßßßßßßßß                           º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Customise the program to your own needs using this dialogue.

      Use BIOS image
        Usage of an image file instead of peeking directly into the ROM. See
        "BIOS|Write image to file" for more information.

      Auto start setup
        Instead of selecting "Setup" manually each time using the menu,
        "Setup" can also be started automatically at program start
        (registered copies only).

      Print form feed
        Do a form feed after printing.

      Extended character set
        This box must be left blank if your printer doesn't print the extended
        character set (code page 437), e.g. characters like "«" or "þ".

      Enable reboot command
        If this box is blank, the "Reboot" function in the "ð" menu is
        disabled (see explanation there).

      Beep on error
        If this option is checked, the program beeps if you enter incorrect
        values in (hexa-) decimal input boxes.

      Reverse mouse buttons
        You can reverse right and left mouse buttons (for lefthanders or
        southpaws).

      German language
        You can disable the English user interface and work with the German
        one instead. In this case the help file must be changed manually.

      Display
      ... þ
      ... ¨
        There are two types of disabled options in the ROM BIOS.
        1. Some options are actually there, but marked as "inadmissible".
           This can be e.g. redundant options. AMIsetup displays a "þ"
           in front of the option. Mostly the "þ" options work perfectly.
        2. Some options are marked as "inadmissible" AND there are no valid
           known settings. AMIsetup then displays a "¨". Often "¨" options
           don't work.
        You can enable and disable both types. If neither "þ" nor "¨" are
        enabled, then AMIsetup shows the same set of options as the ROM
        setup.

      Soundblaster
        See appendix G.

      BIOS image file
      CMOS image file
        You can change both filename and directory of these files, if you
        don't like the default names or if you want to keep more than one
        version of each.

      Help file
        Here you can enter the filename of the online help / online reference
        file. Default setting is "ENGLISH.HLP", but you can use "GERMAN.HLP",
        too.

      Password
        You can define a password, which will be needed at program start.
        Password protection reduces misuse of the AMIsetup.

               ÉÍ[þ]ÍÍÍÍÍÍ Change password ÍÍÍÍÍÍÍÍÍÍÍ»
               º                                      º
               º  New password:  ****                 º
               º                                      º
               º  Confirm:       ****                 º
               º                                      º
               º                                      º
               º                                      º
               º     Ok   Ü    Cancel Ü     Help  Ü   º
               º   ßßßßßßßß    ßßßßßßßß    ßßßßßßßß   º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        For security reasons, you have to enter the same password in both
        lines.
        If you enter an empty password (simply press Enter), the password
        protection will be disabled.

        Changes of the password are written into the file AMISETUP.EXE,
        which must not be write protected for this operation.


      3.6 Help menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        ð  BIOS  CMOS  Setup  Options  Help
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ Contents          ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ View AMISETUP.DOC ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ Print order form  ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ Online reference  ³ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ °°°°°°°°°°
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Contents
        Gives an overview about online help.

      View AMISETUP.DOC
        You can view AMISETUP.DOC without leaving AMIsetup. It is necessary
        that AMISETUP.DOC be installed in the same directory as AMISETUP.EXE.

        You can leave the AMISETUP.DOC window in the background while
        working with AMIsetup.

      Print order form
        To order AMIsetup, you can print an order form to the printer or
        to a file.

      Online reference
        Registered users (read appendix A how to become a registered user)
        can read explanations of approx. 100 of the most widespread setup
        options.

        Select "Online reference", and the index is displayed.

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Online reference ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
        º
        º            Ü Index
        º            ßßßßßßß
        º
        º    General advice
        º    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
        º
        º  Caution!
        º  Beep codes
        º
        º
        º    Tuning tips
        º    ÄÄÄÄÄÄÄÄÄÄÄ
        º
        º
        º    Setup options
        º    ÄÄÄÄÄÄÄÄÄÄÄÄÄ
        º
        º  256KBÿMemoryÿRelocation
        º  256K/384KÿMemoryÿRelocation
        º  7CLK2ÿCASÿPulseÿWidth
        ÈÍþ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±

        You can mark one of the bold terms using <Tab> or the mouse and get
        a closer explanation:

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Online reference ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
        º
        º       Fast Gate A20 Option  [Disabled] [Enabled]
        º       Gate A20 Emulation Option
        º
        º Activates a faster method for enabling and disabling address line
        º needed for accessing extended memory.
        º
        º The address line A20 is normally toggled by the keyboard controlle
        º comparably slow 8042 processor.
        º
        º For reasons of compatibility with PC/XT systems (8086/8088), addre
        º A20 is disabled under DOS in most cases. PCs with the 8088 had onl
        º address lines up to A19. When on the 8088 PC address FFFF:XXXX (se
        º first 64KB was actually addressed.
        º
        º In order to access memory above 1MB (extended memory) on 286 or ne
        º address line A20 must be toggled. This also holds for switching be
        º line A20, allowing the first 63 KB of extended memory to be access
        º mode (and used as "high memory").
        º
        º Control by the keyboard controller can be replaced by a faster tec
        º option became famous as "OS/2 optimization".
        º
        º Modern software uses other methods of switching (triple fault or 3
        ÈÍþ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±


      4 Key shortcuts
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      <F1>         Help
      <Alt><F3>    Close active window
      <F5>         Zoom active window
      <Ctrl><F5>   Move active window (Cursor keys)
                   Change window size (<Shift>+Cursor keys)
      <F9>         Start Setup
      <F10>        Activate main menu
      <Shift><F10> Show program information
      <Alt><X>     Exit Setup or program
      or <Alt><F4>

      NB:  <>            = <Shift>
           <Return>, <Ù> = <Enter>
           <>            = <Tab>


                                   A P P E N D I X
                                   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A  Registration
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If you want to continue using AMIsetup after 30 days, you have to
      register. The program protects itself against illegal usage. And
      in addition the online reference is for registered users only.

      See REGISTER.FRM for the registration fee valid for your
      country (DEM 40.- to DEM 55.- depending on the country).

      º  Inquire for more than 2 licenses or for hardware bundling!   º

      Send DEM Euro-cheques or banknotes to the following address:

                              Robert Muchsel
                              Hegaublick 2
                              W-7750 Konstanz 19
                              Germany

                              FAX +49-7533-3151

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Please use the form "REGISTER.FRM" included with this program.    ³
      ³ You can print it using "Help|Print order form" directly from      ³
      ³ AMIsetup.                                                         ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  Email:                                                           ³
      ³                     2:241/7011.11@FidoNet                         ³
      ³           (mccs BBS, Singen/Germany, +49-7731-69523)              ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      B  AMIsetup and OS/2 2.0
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      The program will not run in a DOS session of OS/2, not even in a DOS
      image (VDM). Write accesses to the CMOS RAM are redirected to a buffer
      by OS/2, which is discarded when exiting the virtual machine (source:
      "Redbooks, Vol. 2: DOS and Windows-Environment, Virtual CMOS Device
      Driver"; IBM Document Number GG24-3731-00).
      In addition, read accesses to the second half of the CMOS (40-7F) are
      not supported. Because of this, the program won't run under OS/2.
      An OS/2 version of AMIsetup is impossible, since AMIsetup directly
      executes code of the real mode BIOS.

      If you make a DOS boot disk and copy AMIsetup as well as a disk editor
      there, then you've got a sort of "emergency disk".


        AMI BIOS and OS/2
        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are NO general problems with OS/2 2.0 and the BIOS versions
      supported by AMIsetup. OS/2 runs with BIOS versions PRIOR to 05/05/91
      and with keyboard controller revision -K8.

      However, problems might arise e.g. when using faulty memory chips,
      too low refresh rates, wrongly installed cache memory or wrong
      bus clock. Because of the protected mode architecture, OS/2 is much
      more sensitive to errors than DOS software, which often ignores
      or doesn't even notice them.


      C  Known problems
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      1. Is AMIsetup compatible with your BIOS?

         For technical reasons, AMIsetup only works with the newer generation
         of the AMI BIOS, the so-called "Hi-Flex BIOS".
         On one hand, the BIOS must be manufactured by "American Megatrends
         Inc." ("AMI") (this you can see when powering on your computer).

         Example of power-on screen:
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ 05/05/91(C)1990 American Megatrends Inc., All Rights Reserved ³
         ³                                                               ³
         ³ (C)1990 American Megatrends Inc.,                             ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³                                                               ³
         ³ 30-0101-ABCDEF-00011001-050591-FORX                           ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         On the other hand, a compatible BIOS has a colo(u)red ROM setup
         (or built-in setup) and normally three levels of setup ("Standard",
         "Advanced" and "Advanced Chipset"), "Password" and "Hard Disk
         Utility".

         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º          BIOS SETUP PROGRAM-AMI BIOS SETUP UTILITIES         º
         º    (C) 1990 American Megatrends Inc., All Rights Reserved    º
         ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
         º                                                              º
         º                     STANDARD CMOS SETUP                      º
         º                     ADVANCED CMOS SETUP                      º
         º                   ADVANCED CHIPSET SETUP                     º
         º            AUTO CONFIGURATION WITH BIOS DEFAULTS             º
         º          AUTO CONFIGURATION WITH POWER-ON DEFAULTS           º
         º                       CHANGE PASSWORD                        º
         º                      HARD DISK UTILITY                       º
         º                    WRITE TO CMOS AND EXIT                    º
         º                DO NOT WRITE TO CMOS AND EXIT                 º
         º                                                              º
         ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
         º                                                              º
         º  Standard CMOS Setup for Changing Time, Date, Hard Disk, etc.º
         º                                                              º
         ÈÍÍÍÍÍµ ESC:Exit |-|-:Sel F2/F3:Color F10:Save & Exit ÆÍÍÍÍÍÍÍÍ¼

         Custom-made BIOS versions are NOT compatible with AMIsetup, even
         though they are from AMI. These have a so-called "XCMOS Setup" (and
         they are black & white).

                              ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿
      2. Frequent errors with ³ compatible ³ BIOS versions
                              ÀÄÄÄÄÄÄÄÄÄÄÄÄÙ

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking 34 .. 3F:              *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Possible causes:
         - A program has overwritten your CMOS. Restart your PC and follow
           the instructions of the ROM BIOS.

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking "AAAAMMMMIIII":        *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking "American Megatrends": *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ CX overflow - BIOS not compatible!      ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Possible causes:
         - You are using a memory manager, which overwrites parts of your
           BIOS. Create a BIOS image following instructions in 3.2.
         - You are using an image file which is faulty (it was created while
           a memory manager was loaded?).
           Repeat the procedure EXACTLY following instructions (part 3.2)
         - Your version of AMIsetup is obsolete

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Checking 16 bit checksum:       *ERROR* ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Normally (if all runs well) you can ignore this error.
         Possible cause:
         - It might be necessary to disable "(Main) BIOS Shadow RAM" before
           creating the BIOS image file.

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ Setup incomplete - may not work!        ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

         Your BIOS seems to be hacked. There could be some options which
         AMIsetup doesn't display. If your image file is OK (see above),
         your BIOS may have been patched by the manufacturer.


      3. Stopgap: -OVERRIDE

         As a last resort you can start the program with the command line
         argument "-OVERRIDE" (CAPITAL letters). This parameter disables
         all error messages; faulty operation or a locked-up computer may
         result, though.


      D  Glossary
      ÄÄÄÄÄÄÄÄÄÄÄ

      Some frequently used abbreviations and terms (explanations for setup
      options only online and only for registered users):

      AMI
        American Megatrends Inc., a BIOS manufacturer

      BIOS
        Basic routines contained in a non-volatile memory (ROM) of the PC
        which e.g. drive the hard disk, but are also needed for system boot
        and system setup.

      BIOS Checksum
        AMIsetup calculates a 16 bit checksum (addition w/ overflow) over
        the BIOS ROM. If this checksum is 0, AMIsetup assumes that the BIOS
        is OK. Else, it is possible that parts of the BIOS have been
        overwritten (e.g. by memory managers). Overwritten parts of the BIOS
        can cause AMIsetup to hang, since it executes BIOS code directly.

      CMOS RAM
        This chip can be read from and written to; unlike normal memory the
        contents are buffered by a battery or an accumulator after turning
        off the PC. CMOS RAM contains data like type of installed floppy
        disk drives, the time etc.

      CMOS RAM Checksum
        A checksum is calculated for parts of the CMOS and stored in CMOS.
        If checksum and CMOS RAM contents differ, either the battery is
        defect or the CMOS RAM contents are invalid. In any case you must
        re-enter the data, possibly replace the battery resp. accumulator,
        too.

      Extended Character Set, Graphic characters
        Characters like „”� or æþ¨. Some printers cannot print these.

      Precompensation
        Precompensation is used with some hard disks to compensate for the
        higher recording density in the inner tracks during write.
        Normally, precompensation and reduced write current begin
        approximately at half the cylinder count. The precompensation
        logic shifts certain bit patterns by +/- 12-15ns.
        Precompensation only affects writing, not reading of data.
        Many hard drives work perfectly with or without precompensation,
        newer hard disks ignore the setting (you should turn it off then).

      ROM
        Read Only Memory - memory which can only be read from and not
        written to.


      E  If the machine won't boot...
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If the setup has been altered so that the PC doesn't even display
      "Press <DEL> for Setup", some models have the following possibilities:

      1. On newer models, you can press <Ins> while powering on. All
         settings will be reset to standard values.

      2. On many machines there is a jumper on the mainboard which you can
         use to erase CMOS RAM. Sometimes this takes several hours.

      3. Often there is the possibility of connecting an external battery
         pack. To install it, you have to remove a jumper residing on a
         4 pinned connector. This jumper does the same as (2).

      4. Only when encountering password errors and only with BIOS from
         12/12/91 on: Pin 32 of the keyboard controller can be grounded
         to erase the password.

      Please note that after these steps all configuration data must be
      re-entered. Make certain that you set the correct hard disk parameters!
      If you are not an hardware expert, you should contact your dealer
      first before destroying your hardware by wrong handling!


      F   Switching to the English user interface
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If you have installed the German version and want to switch,
      do the following:

      Disable "German language" or "Deutsche Oberfl„che" in the "Options"
      dialogue. Replace "GERMAN.HLP" with "ENGLISH.HLP" in the "Help file"
      resp. "Hilfedatei" setting.
      Select OK, exit and restart AMIsetup.


      G  Soundblaster
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      To make the monotonous task of setting up computers a little more
      fun, AMIsetup supports the Soundblaster audio card. The Soundblaster
      support must be explicitly enabled (AMIsetup is, after all, a serious
      program) and works only in registered copies.

      - Turn on "Soundblaster" in the "Options" dialogue (default: OFF)

      - The environment variable "BLASTER" must be set correctly, e.g.:
        SET BLASTER=A220 I5 D1 T4

      - The driver CT-VOICE.DRV must be in the current directory or in the
        subdirectory DRV\ of the "SOUND" directory:
        SET SOUND=D:\SBPRO

        CT-VOICE.DRV is included with every Soundblaster.

      - You must have the VOC files.

        Included are:

        CONFIRM.VOC  - Confirmation (gong)
        COPYRIGH.VOC - About AMIsetup
        ERROR.VOC    - Replaces the error beep
        ERRORBOX.VOC - Error (car horn)
        EXIT.VOC     - Program exit
        WARNING.VOC  - Warning

        Not included:

        HELP.VOC     - Help

        You can delete single files and the corresponding action will be
        "quiet".

        You can replace these files with your own. Not all VOC files work,
        some cause a terrible noise. You can send in your own, better
        collection of files; the included collection sould be acceptable
        though (not overdone).

        The files souldn't be too long (though AMIsetup can play files
        300,000 Bytes long). Playing in the background works only with files
        up to 23,000 Bytes, you can continue working while the sound is
        played. All sounds are turned off immediatly when the corresponding
        action is aborted/finished.


      04/15/1993                               Thank you for your patience...
                                - THE END -