Overview:
---------
LANKEY.ZIP contains a group of functions designed to workaround the printing
slowdown on non-dedicated network servers.  Since Clipper is never really
"idle," the operating system never gets much time to print a spooled print
job.  LANKEY forces Clipper to share time with a C function (in up to half-
second time slices) when waiting for a keystroke.  During the C function, the
operating system gets enough time to print at full speed.  There is no
performance penalty, since both functions (Clipper and C) are interrupted by
the next keystroke.  There is no need to have a special version of the
program for non-dedicated network servers, since there is no performance
penalty for letting the time slicing occur even on single-user machines.


Files contained in LANKEY.ZIP:

LANKEYC.C   : C code, C_INKEY() and C_PEEK() functions
LANKEYC.OBJ : result of compiling LANKEYC.C
LANKEY.PRG  : Clipper code, P_INKEY() function
LANKEY.DOC  : this file


Use of LANKEY:
--------------
The C functions are support functions for the Clipper function P_INKEY(). 
You should use P_INKEY() wherever you have calls to INKEY() now.  Note that
P_INKEY() is a wait state, which means your SETKEYs will work.  It is easy to
take this feature out of it if you don't like it.  You will also probably
want to modify GETSYS.PRG to use P_INKEY() instead of INKEY().  If you leave
the wait state feature in P_INKEY(), then in GETSYS.PRG, in the procedure
GetReader(), find the line that says

                GetApplyKey( oGet, inkey( 0 ) )

and change it to

                GetApplyKey(oGet,P_INKEY(0,.F.))

This is so that P_INKEY() will not try to check for the SETKEYs, because
GetApplyKey does that automatically.

If you use ACHOICE() or MENU TO..., you may want to write your own menu
function which handles waiting for a keystroke using P_INKEY(0).

If you have any questions about the code, feel free to email them to me
(Shawn B. Lipscomb, CIS ID 76247,772).


Technical description:
----------------------
C_INKEY() watches the keyboard buffer's tail to sense when a key has been
hit.  There are other ways to sense a keystroke, but a bug in DOS 3.3
prevents functions like kbhit() from sensing enhanced-keyboard-only key
combinations (like <CTRL><UP>) under certain circumstances.  kbhit() is still
necessary though, because that's where the network gets most of its time.

These functions work with all versions of Clipper from 5.01 to 5.2a.  As of
06/09/93, they have been revised to also work with ExoSpace.  They should
work on all non-dedicated servers, but have only been tested on Novell
Netware and Lantastic.  One user also reports success on CBIS's Network-OS
version 7.26C.  


You may distribute LANKEY.ZIP freely, as long as the original files stay
intact.  You may, however, add your own files to the ZIP.


Instructions:
-------------
To incorporate LANKEY into your application:

    1. Compile LANKEY.PRG with the command:

               CLIPPER LANKEY /N

    2. Change all your calls to INKEY() to call P_INKEY() instead.  The
       syntax is exactly the same.  You may want to use the following
       #xtranslate preprocessor command to automatically make this change at
       compile time:

               #xtranslate INKEY([<v1>]) => P_INKEY([<v1>])

       Do NOT include this preprocessor command when compiling LANKEY.PRG
       since P_INKEY() does actually call INKEY().
    
    3. Recompile GETSYS.PRG after making the changes described earlier.

    4. Link the following files into your application:

               LANKEY.OBJ
               LANKEYC.OBJ 
               GETSYS.OBJ
               LLIBCA.LIB

       LLIBCA.LIB is Microsoft's large library and is available on Compuserve
       if you don't have Microsoft C.

       If you are using a link script, the additional lines would be

               FILE LANKEY, LANKEYC       # Put these lines after your
               FILE GETSYS                # other FILE commands.  All three
                                          # can be overlaid.

               LIB LLIBCA                 # This should be the LAST line in
                                          # the link script (make sure it's
                                          # after CLIPPER.LIB).

    5. Run your application and smile.